!!!!! *YOU* *MUST* read the last paragraph about problems !!!!!

!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!
!!!!! Don`t wonder about the new size of the Updates and that !!!!!
!!!!! the Updater doesn`t print all module versions anymore.  !!!!!
!!!!! This is NO bug. The modules are still there.            !!!!!
!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!!

New Upgrade features:

  o Manual Mount support to allow the controller to search for
    a RDB on units with a CDROM type like DVD Rams.

  o CVPPC 31khz support..this is no real monitor but more a
    copy gfxdata patch so it`s not that fast but still usable.
    The native aga output is still there.
    With older CGFX versions you may experience problems if
    you boot with "echo on" or the shell window pop up.
    Try to avoid anything in the startup-sequence which accidently
    opens a screen before the Workbench.

  o ECS/AA 31khz support
    the Bootmenu now ALWAYS pops up in 31khz mode, so
    people with 15khz monitors have to use <SPACE> to
    switch the resolution to 15khz INTERLACE.
    The resolution is saved too in the flash so the next
    time it uses the resolution you set.
    The resolution switch is disabled if there`s a permedia
    card found.


  o WideTermination check
    A lot people don`t seem to have read the manual correctly
    and use Wide/Narrow bridges without upper Widebus termination
    which leads to not working reselection.
    (Syndrom: 44.2 works perfectly with your devices but only slowly)
    If the check detects such broken SCSI configuration the device
    completely disables reselection for all units.
    (CDROM is reselection by default)

    ATTENTION:
    Correct Termination checks are NOT 100%.


  o New Unit ID standard so it works with WIDE HDs.
    Board * 10*1000*1000
    Lun   * 10*1000
    Unit  * 10
    + 8 (8 in the last digit switches the format)

    so if you wanna access Unit 13 Lun 5 it would look like

    500138

    or Unit 8 Lun 0

    88

    or Unit 1 Lun 0

    18 (NewStyle)

    or

    1 (OldStyle)

    The old Format was

    Board * 100
    Lun * 10
    Unit * 1

    so you could only use 9 Units though Wide provides 15.
    I know the use of Unit=8 as a flag isn`t
    elegant but it`s the only compatible system i found and
    it`s not really that bad.

  o Key "2" disables the processor on an 1200 ONLY.
  o Key "s" pressed during booting disables the SCSI,
            cdrive, bootmenu, bootmenu settings.
  o Key "c" pressed during booting disables 31khz bootmonitor
            and cvppc support
  o Key "m" pressed during booting disables the memory
  o Key "a" pressed during booting disables all

  o BootMenu which can be invoked by holding
    the Key <ESC> key during the system boot.
    (It may not work for weird tower pc-keyboard hacks)


    Then you see a menu with the 3 entries

    o SCSI
      o List with 8 or 16(WideSCSI) Units.
        The entries show the current settings for the UnitID.
        The Controller UnitID entry is marked differently.
        If you click on the UnitID you get into a simular menu
        like Unitcontrol`s Option menu.
        If you click on the controller UnitID entry you get into
        a simular menu like Unitcontrol`s Prefs menu.

        Unit prefs:

          o NO LUN
            1 LUN
            2 LUNs
            3 LUNs
            4 LUNs
            5 LUNs
            6 LUNs
            7 LUNs
            8 LUNs

            -> This Entry can be used to disable the scan for the whole
               unit for more Luns which can speed up booting a lot.

          o Offset
            Here you specify the synchron handshake.

          o Period
            Here you specify the synchron clock.

          o ASynchron/Synchron
            ASynchron
            Synchron
        
            Here you enable the synchron mode, so you
            can change Offset and Period now.
            The ASynchron/Synchron mode means that the
            synchron mode is activated if specified by
            the RDB for example.(The AUTO mode)

          o Auto Buswidth
            8-Bit
            16-Bit

            Here you specify the buswidth for a unit.
            Well..anything more than Auto Mode isn`t really
            needed.

          o Auto Reselection
            No Reselection
            Reselection

            Disabling reselection for units with problems is
            possible here. Auto Mode means that reselection
            is activated if the RDB flag is set or if it has
            no RDB but is a normal unit like a cdrom.
            Scanners and other esotheric units don`t use
            reselection in AUTO mode.


          o Auto Mount
            Mount
            No Mount

            Auto Mount(normal) only searches RDB on random access and optical drives.
            DVD Rams use the CDROM type and if the controller should search for a
            RDB here you have to use "Mount".

          o Auto Removable
            Removable
            No Removable

            Only for completeness..


          o CDBoot Pri
            define the cdrom boot priority. Check the System Bootmenu for
            the boot priority of other devices.


          o CDRom Device Name
            define the device name with which the cdrom should be mounted.

          o No CDRom Bount
            CDRom Mount
            CDRom Boot

            The buildin CDRom filesystem is the old Phase5 CDRive filesystem.
            Its feature set may not be enough for your needs.


        Controller Prefs:

          o BusID
            Controller BusID..normally 7.
            The BusID of the controller. This doesn`t mean you
            can use SCSI Nets as these don`t work in general.

          o SCSIResetDelay
            The seconds the device waits after the first
            SCSI Reset/Init.

          o ErrorDelay
            The seconds the device waits after an Inquiry Error

          o RemovableDelay
            The second intervall for a removable check

          o ErrorDelayRetry
            The retry count for an Inquiry after an Error.

          o ErrorRetry
            The retry count for an SCSI Operation after an SCSI Error.

          o TimeOut
            (not yet used)


    o CDFS

      o No CDFS HD RDB Scan
        CDFS HD RDB Scan

        Update the filesystem.resource with CDFS filesystems when these
        are placed in the RDB of HDs **BEFORE** the CD Drive at the same
        controller. This way you can theoretically use other cdfilesystems.
        *Theoretically* means that i haven`t tested if other cd filesystem
        work with such startup as they may need to find their prefs.

        The CDFS dostype is

        #define ID_CDFS_DISK	(0x43444653L) /* 'CDFS' */
        The new SCSIConfig has an automatic filesystem entry for this.

      o Cache Sets
        How many Cache Sets are allocated.
        CacheSets*CacheSetBlocks*2048 is the memory needed.
        Only useful for CDFS

      o Cache Set Blocks
        The number of of each cache set.
        A cache set is the line of block at Sector & ~(CacheSetBlocks-1) which
        is fetched into the cache.
        Only useful for CDFS

    o RAM
      Read SetMemMode documentation in the 68060 archive.

      o MemorySpeed 70ns
        -> standard waitstates
        MemorySpeed 60ns
        -> for 50Mhz 060 / 66Mhz PowerPC cards this means
           o 68k No Read Waitstate
           o 68k No Write Waitstate
           o PPC No Read Waitstate
           o PPC No Write Waitstate

        Free Config

      o 68k Read Waitstate
        68k No Read Waitstate
        -> possible with at least 70ns rams

      o 68k Write Waitstate
        68k No Write Waitstate
        -> possible with at least 70ns rams

      o 68k PreCharge
        68k No PreCharge
        possible with at least 60ns rams  but not guranteed
        to work with every ram.
        (Enabled only for boards supporting this)

      o PPC Read Waitstate
        PPC No Read Waitstate
        possible with at least 60ns rams

      o PPC Write Waitstate
        PPC No Write Waitstate
        possible with at least 60ns rams

      o PPC PreCharge
        PPC No PreCharge
        possible with at least 60ns rams  but not guranteed
        to work with every ram.
        (Enabled only for boards supporting this)

    o SYSTEM
      Read Cybermap documentation in the 68060 archive.

      o No MapRom
        MapRom
        -> *current* kickstart ROM is mapped.

        o No MacPatch
          MacPatch
        -> the mapped kickstart`s chipram starts at 0x4000
           to avoid shapeshifter/fusion hack tools.
           Only tested with 40.68

        o No SCSIPatch
          SCSIPatch
        -> the mapped kickstart`s scsi.device is disabled.
           This means for the A4000 that IDE is off
           and for A3000 that the on board SCSI is off.

        o No NCR SCSIPatch
          NCR SCSIPatch
        -> the mapped kickstart`s NCR scsi.device is disabled.
           This only works on the A4000T and means that
           the on board SCSI is off.

        o No Checksum Patch
          Checksum Patch
        -> the mapped kickstart`s checksum check is disabled.
           This may speed up booting.

      o No 31Khz Screen
        31Khz Default Screen
        1) No CVPPC Board
           ->Uses the 31khz 640*480 BootMonitor now also for the
             AmigaOS BootMenu and for the initial shell.
             When IPrefs is started the 31Khz Bootmonitor patch
             gets inactive.

            *ATTENTION*

             I set the hardware into best mode, which means
             that it boots into AGA mode, if a Boot31Khz Screen
             is opened. Normally BestMode is set with setpatch,
             so setting it before may have consequences for old
             games or demos.

        2) CVPPC Board
           ->It opens a 640*400 NTSC Interlace screen which is
             also updated on the CVPPC 31khz screen for the
             BootMenu and the initial Shell screen.
             The 31Khz BootVGA monitor isn`t initiated in this
             case.

      o SuperScalar No
        SuperScalar Yes
        ->Enables superscalar mode to speed up booting.
          This mode is activated with the 68060.library later
          anyway.
        
      o BranchCache No
        BranchCache Yes
        ->Enables the branchcache to speed up booting.
          This mode is activated with the 68060.library later
          anyway.

      o WriteBuffer No
        WriteBuffer Yes
        ->Enables the writebuffer to speed up booting.
          This mode is activated with the 68060.library later
          anyway.

    o SAVE | USE | CANCEL

      - SAVE saves the settings into the flashrom which
        means that these settings are used for every coldboot
        or warmboot if not changed or *NEW FLASH UPDATE* is
        done. With the help of the 2nd joystickport`s button
        you can completely disable scsi device and settings
        if you have for some reason a problem to get into the
        new bootmenu after playing around with special settings.
        So you SHOULD HAVE the PPCUpdate/MK3Update on a disk so
        you can quickly reinstall it without a hd which is
        connected to the CyberStorm.

      - USE uses the current changed settings for the current boot.
        The settings aren`t saved and are lost in the next reset.

      - CANCEL doesn`t use the settings.


How to solve Problems ?

 o Weird problems if you have CVPPC and suddenly the output
   of AGA/ECS screens is sort of copied after cgx is started.
   Remove PatchControl and simular tools *BEFORE* cybergfx
   i started

 o Performance drop while running PPC programs and an ISDN
   adapter by VMC, Multiface, HyperCom...Int 6 cards
   Your CyberstormPPC doesn`t sit correctly.
   Try to press the board into the slot again.

 o If you have weird crashes you probably have a power problem.
   Even if you have a bigger power supply the problem can be
   occur because the small power connection to the A1200 board
   by certain towers can`t transport the needed power so the
   ppc board gets unstable. To work around this problem
   you should create a 2nd connection from the A1200 to the
   power supply. Several people used the floppy connectors.

 o If you have problems with 60ns mode your simms need significant
   more power in 60ns mode which is a problem.
   Read the first section how to fix about power problems.
   Unfortunately 60ns printed on a Simm don`t necessary mean
   that it`s a real 60ns Simm. 

 o If you`re using at least 1 Ultra unit on the bus be *very*
   careful with the length of the cable.

 o If you use a 68/50 adapter and use more than one unit on
   this new chain or let the wide chain end here with one unit
   this adapter MUST BE active terminated on the wide lines.

 o At least one unit must provide TERM power.

 o The controller is NOT terminated

 o If you have problems and can`t boot with a certain setup
   try to disable units in the Bootmenu until you`re able to
   boot. Then use Unitcontrol Rescan and you may get device
   error requesters.
   If you get parity errors for example you have a serious
   cable/term problem.
   The device has absolutely nothing to do with that.

 o IBM and (Seagate ?..not mine) drives have problems with
   the device when the SDTR Jumpers are set.
   I can`t see what is exactly happening then because i
   don`t have such drive.

 o You don`t get SYNCHRON in Auto Mode means that your RDB
   hasn`t set the SYNC flag.

**************************************************************************
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
--------------------------------------------------------------------------
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
**************************************************************************
 o You use AmiCDFS or other CDFilesystems and the new BlizzardPPC or
   CyberstormPPC FlashUpdate is installed.
   !! It does NOT matter if it`s a SCSI CDROM or not...it also effects IDE. !!

     Change the 0x43444653 (CDFS) dostype in the (AmiCDFS) mountlist.
     Add a 1 at the last number for example.
     OR
     add the line FORCELOAD = 1

     otherwise it`s using the Phase5 CDFilesystem which may
     not do what you want it to do.
     The CDRive filesystem is always added to the filesystem.resource
     with the 0x43444653 ID

**************************************************************************
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
--------------------------------------------------------------------------
++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++
**************************************************************************

 o SYSIHack Problem...SYSIHack says that iprefs was already
   started which it wasn`t. (Caused by opening gadtools.library
   in the rom)

    Enter the BootMenu GUI, then leave it...SysIHack won`t
    start because it checks if the gadtools.library is already
    used. The gadtools.library can`t be expunged so there`s
    no cure for this problem.

 o Only use the real Setpatch 40.16.
   The last CBM had released.
   ** You don`t need anything after 40.16. It can only get worse **
    

 o Well..Xopa,artm,sysspeed,scout all seem to have a bug in showing
   indirect resident table entries. The good old xoper and the obviously
   the OS itself does it correctly.
   So if you see weird entries in the resident table ask the authors(if
   they`re still alive) to fix their programs:-)
   (They should read exec.library/SumKickData about the special usage
    of Bit 31)

 o Don`t use skick as people reported problems with it.
   Use cybermap instead.