SEE Version 1.7                                   October 9, 1987

                                   COPYRIGHT 1987
                                         by
                               ABACUS Computer Service
                                 Donald J. Jackowski
                                    16 Green Road
                                Mine Hill, NJ  07801
                                   (201) 584-8201
                                 All Rights Reserved

          INTRODUCTION
               SEE is  a utility  program that  allows a  user to display a
          file containing  non-printable  characters  and  to  make limited
          modifications  to  the  input  to  create  a  file that most text
          editors can handle.  An  option  is  provided  to  strip (Ignore)
          printer control  sequences, making it easy to create a pure ASCII
          file from one containing printer control characters.

               Non-printable characters are divided into two classes, those
          in  the  numeric  range  0  through  31  are  considered  CONTROL
          characters except for the four characters that normally  occur in
          text files  namely the  "newline" character (10, ^J, \n, NL), the
          "return" character (13, ^M, \r, CR), the "tab"  character (9, ^I,
          \t,  TAB)  and  the  "formfeed"  character (12, ^L, \f, FF).  The
          second class called GRAPHIC  characters is  comprised of  all the
          characters  in  the  numeric  range  127  through 255.  Some text
          editing programs will not operate correctly on a  file containing
          either class  of non-printable  characters and many programs take
          the control character 26 (^Z) to be an End Of  File marker.   SEE
          offers  a  mechanism  to  allow  the user to visually observe the
          characters contained in  ANY  file  and  then  make  some limited
          substitutions that  will render the output acceptable to any text
          editor.

          USAGE
               The SEE program usage is:
                    SEE [-aipstNwNiho] file ...
               Where:
                    -a  = show ALL characters.
                    -i  = Ignore ALL non-printing characters.
                    -p  = Ignore ALL Printer control sequences.
                    -s  = Substitute a 'space' for each control character.
                    -ss = Substitute a 'space' for each non-printing char.
                    -tN = Set Tab Stop value. (default 8)
                    -wN = Set output column Width. (default 78)
                    -h  = Show Hex values.
                    -o  = Show Octal values.

               When SEE is invoked with no arguments or  if invalid options
          are given,  a short  menu is displayed.  When SEE is invoked with
          one or more file names but no options  the contents  of each file
          is displayed,  all normally non-printing characters are displayed
          as a series of regular printing  characters.   CONTROL characters
          are  displayed  in  the  ^A  style  and  GRAPHIC  characters  are
          displayed as a three digit number surrounded by  the <> character
          pair.




          Copyright 1987 (C) by ABACUS Computer Service         Page 1 of 3


          SEE Version 1.7                                   October 9, 1987

          OPERATION
               The  control  characters  "new  line",  "return", "tab", and
          "form feed" are displayed  as  normal  characters  unless  the -a
          option is  given in  which case they are displayed as ^J, ^M, ^I,
          and ^L.  When the -a option is  given the  length of  each output
          line is  a result of the default column Width setting unless this
          default is changed with the -w option. 

               The -s option can be  used  to  cause  SEE  to  substitute a
          'space'  character  (decimal  32)  for  each  occurrence of a any
          control character, if used in conjunction with the  -a option the
          substitution includes  the "new line", "return", "tab", and "form
          feed" characters.  If the -ss option is given a 'space' character
          is  substituted  for  each  GRAPHIC  character"  as  well as each
          CONTROL character."

               The  -i  option  will   ignore  both   CONTROL  and  GRAPHIC
          characters and will override and disable the -s option.

               The  -p  option  will  ignore  printer control sequences and
          automatically turns on the -i option.  This  option uses  a table
          to determine  the number of bytes to ignore after an ESC (decimal
          27) character.  The default table  contains the  data appropriate
          for an  EPSON FX-85  printer but can be easily modified for other
          printers as outlined under OTHER PRINTERS.

               The SEE output (normally displayed  on  the  screen)  can be
          redirected to a file.  For example the command line:
                    SEE file >temp
          Will place the output in the file named TEMP.

               Since  SEE  does  not  actually  display  on  the screen but
          depends on the DOS to do  the actual  display the  -t option will
          NOT  affect  the  actual  display.   The -t option is intended to
          provide  tab  setting  control  when  SEE   calculates  how  many
          characters to  permit on  a line, and is generally only needed in
          conjunction with the -w option.  SEE expects  both the  -t and -w
          options to  be given with a number, the first digit of the number
          may be given  immediately  after  the  option  letter  or  may be
          separated from  the option  letter by a 'space', thus the command
          lines:
                    SEE -w45 file       and
                    SEE -w 45 file
          Are equivalent, both set the column width to 45.

          NOTE
               An interesting use of SEE is to look for message  strings in
          normally unprintable  executable files (i.e .EXE and .COM files).
          For example the command line:
                    SEE -i SEE.EXE
          Will display some random characters, some  of the  actual machine
          codes, and all of the internal messages.







          Copyright 1987 (C) by ABACUS Computer Service         Page 2 of 3


          SEE Version 1.7                                   October 9, 1987

          USER LICENSE
               If you  find this program useful you are requested to send a
          $10 registration and  license  fee  to  ABACUS  Computer Service.
          This  fee  will  entitle  you  to  continue that use with a clear
          conscience.  Please pass a copy to a friend!  It is NOT necessary
          to be a licensed user to distribute copies.  All registered users
          will receive notice of the first update that is made  after their
          registration. 

          OTHER PRINTERS
               The following information is intended as an aid to those who
          use a printer  requiring  different  control  sequences  than the
          EPSON  FX-85.    All  the  ESCAPE  sequence  byte length data are
          maintained in a single  table to  make modification  easier, this
          internal table,  used by  the -p  option, contains  the number of
          bytes to be taken as part of an ESCAPE (27) sequence is:
               /*          0    1    2    3    4    5    6    7    8    9*/
               /* -------------------------------------------------------*/
               /*  00 */   0,   0,   0,   0,   0,   0,   0,   0,   0,   0,
               /*  10 */   0,   0,   0,   0,   1,   1,   0,   0,   0,   0,
               /*  20 */   0,   0,   0,   0,   0,   2,   0,   0,   0,   0,
               /*  30 */   0,   0,   2,   2,   0,   1,   3,   2,   0,   0,
               /*  40 */   0,   0,   0,   0,   0,   2,   0,   2,   1,   1,
               /*  50 */   1,   2,   1,   1,   1,   1,   1,   1,   0,   0,
               /*  60 */   1,   1,   1,   0,   1,   2,   9,   2,   9,   1,
               /*  70 */   1,   1,   1,   2,   2,   0,   0,   1,   2,   1,
               /*  80 */   1,   2,   2,   2,   1,   2,   0,   2,   0,   0,
               /*  90 */   0,   0,   3,   0,   0,   0,   0,   2,   9,   0,
               /* 100 */   0,   0,   0,   0,   0,   2,   2,   0,   2,   0,
               /* 110 */   0,   0,   2,   0,   0,   2,   0,   0,   0,   0,
               /* 120 */   2,   0,   0,   0,   0,   0,   0,   0

               This table contains an entry for  each of  the 128 character
          values that  could be  the byte  immediately following the ESCAPE
          byte.  This table begins at 2A42H in the SEE.EXE file.   The zero
          values in  this table represent "Unexpected ESCAPE sequences", an
          error message is displayed if any  such ESCAPE  sequence is found
          in the input.  The values 1 through 8 represent the length of the
          ESCAPE sequence, excluding the ESC character.   EXAMPLE:  row 50,
          column 1  represents 51  which is  the decimal value of the ASCII
          character '3' and the printer ESCAPE sequence:
                    27   51   (n)
               The  length  of  this  ESCAPE  sequence,  excluding  the ESC
          character is two.

               The value  9 is interpreted to mean that the next NULL input
          byte marks the end of the  ESCAPE  sequence.    EXAMPLE:  row 60,
          column 8  represents 68  which is  the decimal value of the ASCII
          character 'D' and the printer ESCAPE sequence:
                    27   68   (n1) (n2) ...  0 (NULL)
               The length of this sequence is  signaled by  the terminating
          NULL (zero) byte.

               If you alter this table to accommodate a different printer I
          would appreciate if you  would send  a copy  of your  table along
          with the  printer make  and model  to: ABACUS  Computer Service. 
          Future versions of SEE will include the data we receive  on other
          printers, and/or an "install" program.

          Copyright 1987 (C) by ABACUS Computer Service         Page 3 of 3