TVGA VESA SUPER VGA BIOS EXTENSIONS (Version 1.02)
            ==================================================

        TVGAVESA is designed for TVGA 8800  &  8900, and provides all
 functions  which  follow the Video Electronics Standards Association
 (VESA) Super VGA BIOS Extension standard #VP891001.  These functions
 include:
        Function 00H - Return Super VGA information
                 01H - Return Super VGA mode information
                 02H - Set Super VGA video mode
                 03H - Return current video mode
                 04H - Save/Restore Super VGA video state
                 05H - CPU Video Memory Window Control

        TVGAVESA will  detect  TVGA  board  type  automaticlly.  The
 TVGAVESA BIOS supports different groups of Super VGA modes depending
 on board type. For details please see the following list:

    TVGA Board      Memory Size        Super VGA modes Supported
 ==================================================================
      8800            256K             100H (640x400, 256 colors)
                                       102H (800x600,  16 colors)
                                        6AH (800x600,  16 colors)

      8800            512K             100H (640x400, 256 colors)
                                       101H (640x480, 256 colors)
                                       102H (800x600,  16 colors)
                                       104H (1024x768, 16 colors)
                                        6AH (800x600,  16 colors)

      8900            256K             102H (800x600,  16 colors)
                                        6AH (800x600,  16 colors)

      8900            512K             100H (640x400, 256 colors)
                                       101H (640x480, 256 colors)
                                       102H (800x600,  16 colors)
                                       103H (800x600, 256 colors)
                                       104H (1024x768, 16 colors)
                                        6AH (800x600,  16 colors)

      8900            1024K            100H (640x400, 256 colors)
                                       101H (640x480, 256 colors)
                                       102H (800x600,  16 colors)
                                       103H (800x600, 256 colors)
                                       104H (1024x768, 16 colors)
                                       105H (1024x768,256 colors)
                                        6AH (800x600,  16 colors)