Qmodem - Telecommunications Program Version 1.13  Page 1












                            Qmodem Operations Manual
                                  Version 1.13









                             The Forbin Project Inc.
                               and John Friel III  
                                24 December 1985



























             Copyright (c)  The Forbin Project Inc. and John Friel III
             All rights to Qmodem are reserved by the Forbin Project Inc.   


        Qmodem - Telecommunications Program Version 1.13  Page 2


             Qmodem  is  a  User Supported program.   I am asking  for  a 
        donation   of  $20.00  for its use.    Those that  donate    will 
        receive   published     announcements    for future  updates   to 
        Qmodem   and other  programs written by the Forbin Project  Inc.

             Qmodem    may  be  shared  with   other  people  under   one 
        condition;    that there is  NO CHARGE  for the copy(s).   

             A special note to Corporations:  Site licensing is available 
        by arrangement with the author.   Do NOT make multiple copies for 
        use  inside your corporation until you contact The Forbin Project 
        Inc.


                            The Forbin Project Inc.
                            c/o John Friel III
                            715 Walnut Street
                            Cedar Falls, Iowa  50613


        Qmodem - Telecommunications Program Version 1.13  Page 3


                        T A B L E   O F   C O N T E N T S 

                                                           Page     
             Description ..................................  5 
             System Requirements ..........................  6
             Starting Qmodem ..............................  7
             
             Commands .....................................  8

                  Alt-A     Strip / Replace communication table  9

                  Alt-B     Bells and Beeps toggle ............  9

                  Alt-C     Clear screen ......................  9

                  Alt-D     Dialing directory ................. 10 
                       C)        Clear entry(s) .................. 10
                       D)        Dial an entry ................... 11
                       E)        Revise the Prefix file .......... 12
                       M)        Manual dial a number ............ 13
                       N)        Next page of the directory ...... 13
                       P)        Previous page of the directory .. 13
                       R)        Revise an entry ................. 13
                       X)        Exit back to Qmodem ............. 14

                  Alt-E     Echo toggle ....................... 14

                  Alt-G     Graphic mode toggle ............... 14

                  Alt-H     Hang-up modem ..................... 14

                  Alt-I     Information on Qmodem ............. 15

                  Alt-J     Function key menu ................. 15

                  Alt-L     Log drive ......................... 15

                  Alt-O     Sub directory change .............. 15

                  Alt-P     Communication parameter menu ...... 16

                  Alt-Q     Redial last number ................ 16

                  Alt-R     DOS shell ......................... 17

                  Alt-S     Split screen toggle ............... 17

                  Alt-T     Screen Dump ....................... 17

                  Alt-V     View file ......................... 18

                  Alt-W     Disk directory and Xmit time ...... 18

                  Alt-X     Exit Qmodem ....................... 18


        Qmodem - Telecommunications Program Version 1.13  Page 4


                  Alt-Y     Delete a file ..................... 19

                  Alt-Z     Xon / Xoff toggle ................. 19

                  PgUp      Upload menu ....................... 20

                  PgDn      Download menu ..................... 23

                  Up-Arrow  Scroll back screen ................ 24


             Appendix A

                  QINSTALL - Qmodem Installation Program ...... 25

             Appendix B

                  TURBO Pascal Usage .......................... 26

             Appendix C

                  Dialing Directory description................ 27

             Appendix D

                  A note from the Forbin Project Inc. ......... 28


        Qmodem - Telecommunications Program Version 1.13  Page 5


                              D E S C R I P T I O N

             Qmodem  is  a modem communications program.   It  can  store 
        many phone numbers in a personal directory for later recall.   It 
        will  handle a variety of modems connected to the PC.    Transfer  
        files  to  other  computers using either XON  /  XOFF    or   the   
        ever  popular  XMODEM  protocols.    The  program    was  written   
        using Turbo Pascal from Borland International.


        Qmodem - Telecommunications Program Version 1.13  Page 6


                      S Y S T E M   R E Q U I R E M E N T S


             Qmodem  requires  an IBM PC/XT/AT/PCjr or  close  compatible 
        with 192K, a Color/Graphics or Monochrome card and monitor, and a 
        serial port and modem.   

             It should be noted here, that Qmodem sometimes does not work 
        on a PC when other background software is running.   I have heard 
        a  few  horror stories where a screen clock routine  caused   all  
        sorts of problems with the serial port.   


        Qmodem - Telecommunications Program Version 1.13  Page 7


                          S T A R T I N G   Q M O D E M

             Throughout   the  documentation,   you  may  run  into   the 
        characters [RETURN] and <cr>.   These represent the return key on 
        the keyboard.  If you see these in the text, press the return key 
        rather than typing in the string.

             Qmodem   is started by entering  "Qmodem [RETURN]" from  the 
        DOS prompt like the following.

                  A>Qmodem [RETURN]
          
             Please read the opening screen carefully.   Press any key to 
        continue on into Qmodem.   At the top of the next screen,  Qmodem 
        displays  the version logo and what  type of display card you are 
        using.  Immediately after the logo,  Qmodem looks  for 6 files on 
        the  disk as follows:      

             QMODEM.CNF - the  configuration  file.     
             QMODEM.KEY - the function key file.
             QMODEM.PRE - the dialing prefix file.
             QMODEM.FON - the dialing directory file.
             QMODEM.XLT - the strip / replace table file.
             QMODEM.WND - the window definition file.

             If  you  are just starting and do not have the files  listed 
        above,   Qmodem   will  create  most of them  for  you.   Two  of 
        them:  QMODEM.CNF  and  QMODEM.WND  are created by  the  Qinstall 
        program listed in Appendix A (also on you Qmodem Disk).  For  the  
        dialing  directory,   Qmodem   will   initialize   all   of   the  
        communication parameters by asking you 3 or 4 questions.   


        Qmodem - Telecommunications Program Version 1.13  Page 8


                                 C O M M A N D S

             There are 29 commands in the Help Menu as follows.

                  Alt-A ........ Strip / Replace screen
                  Alt-B ........ Beeps and Bells toggle
                  Alt-C ........ Clear screen 
                  Alt-D ........ Dialing directory 
                  Alt-E ........ Echo toggle
                  Alt-G ........ Graphics mode toggle
                  Alt-H ........ Hang-up modem 
                  Alt-I ........ Information on Qmodem
                  Alt-J ........ Function key menu 
                  Alt-L ........ Log drive
                  Alt-O ........ Sub directory change
                  Alt-P ........ Communication parameter menu 
                  Alt-Q ........ Redial last number 
                  Alt-R ........ DOS shell
                  Alt-S ........ Split screen toggle
                  Alt-T ........ Screen Dump
                  Alt-V ........ View file     
                  Alt-W ........ Disk directory and Xmit time 
                  Alt-X ........ Exit Qmodem
                  Alt-Y ........ Delete a file
                  Alt-Z ........ Xon / Xoff toggle
                  Home ......... Main Menu window
                  PgUp ......... Upload menu 
                  PgDn ......... Download menu 
                  Up-Arrow ..... Scroll back screen 
                  Ctrl-End ..... Sustained BREAK signal
                  Shft-Tab ..... Add Linefeeds toggle
                  Ctrl-PrtSc ... Printer echo toggle
                  Ctrl-Home .... Capture Buffer toggle

             All   are   selected  by  pressing  the  corresponding   key 
        combinations on the keyboard. 


        Qmodem - Telecommunications Program Version 1.13  Page 9


             Alt-A  Strip / Replace table.

             Pressing  the  Alt-A  key  combinations  produces  a  screen 
        containing  the  ASCII values 0 through 127 and  their  translate 
        equivalents.   Above   the  translate  table  is  the   Character 
        representation  of  the  highlighted  entry,  both  received  and 
        translated.  
         
             If,  Qmodem  has  created the file,  all entries  will  have 
        duplicate   translate  values.    This  is  referred  to  as  "No 
        translation performed". 
             
             To  change  (translate)  an  ASCII  value,   you  move   the 
        highlighted  (semi  box  looking thing)  around  the  table  (up,  
        down,  left,  and  right)   to the number you want to   strip  or 
        replace. The number to the left of the dash is the ASCII position  
        in  the  table.    The  number to the right of the dash   is  the 
        character  you  will see when Qmodem receives the number  on  the   
        left. To change the character from the input, press the Space Bar 
        once.  You  will  receive a prompt at the bottom  of  the  screen  
        asking for an integer between 0 and 255.   To strip the character   
        from   the input,  you need only replace the number on the  right 
        with  a 0 (ZERO).  Press [RETURN] to complete the change.   The S 
        key will swap  the table showing the high bit entries 128  - 255.    
        Repeat the procedure to change any of these also.  When you   are 
        finished,  press  the [Esc] key to save the changes (if any)  and 
        return to Qmodem ready.


             Alt-B  Bells and Beeps toggle

             Qmodem can now be made totally silent.   The Bells and Beeps 
        to signal you that something is different can be very distracting 
        in an office environment.   You can set Qmodem's default state in 
        the  installation program Qinstall,  or toggle it on and off with 
        Alt-B.


             Alt-C  Clear screen

             This  will clear  the screen of all data.    If you  are  in 
        split screen mode, this will only clear the bottom portion of the 
        screen.
            
             In addition to clearing the active screen,  if ANSI graphics 
        mode has been enabled [see Alt-G in this document],  Qmodem  will 
        also  send  the  escape sequences necessary to reset  the  screen 
        colors  you have selected.   For those of you who  call  Bulletin 
        Boards that have those neat color screens,  sometimes, the colors 
        end up different than you would like.  Using Alt-C will reset the 
        color on your screen back to your configuration selections.  

             It  should also be noted;  some clone  computers,  like  the 
        Tandy 1000,  use ANSI.SYS for the CLS command from DOS.   You may 
        see  "<-[02J"  when typing CLS.   This means you have  booted  up 


        Qmodem - Telecommunications Program Version 1.13  Page 10


        without  the ANSI.SYS in your CONFIG.SYS file.   You need to  add 
        the following line to your CONFIG.SYS file:

                  Device=ANSI.SYS<CR>        <-- <CR> means RETURN key

        Make  sure  you have this if you want ANSI graphics or your  Al-C 
        puts funny characters on your screen.


             Alt-D Dialing directory.

             The following is an example of the dialing command prompt at 
        on the screen.


         * Dial number(s) [ <cr> for Dialing Directory, <Esc> to exit ]
         * 


             This  is the quick entry prompt.   Here,  you can enter your 
        dialing directory number(s) and skip the dialing directory.   All 
        of  the dialing prefix codes are valid.   For  example,  to  dial 
        directory  number  12,  you would just enter "12<cr>" and  Qmodem 
        will  process the call.  Instructions are given below for dialing 
        up to 10 different numbers in a single command!

             With  the use of the optional prefix  codes,  long  distance 
        services   may  be utilized.   Some services require  the  prefix 
        codes before the actual number,  another needs it just at the end 
        of  the  number,   while still others need two  codes  sent  out.  
        Qmodem  can handle all of the above cases with ease.    Refer  to 
        the  dialing  prefix subcommand below for a full explanation   on 
        how to use the prefix codes.

            The dialing directory can hold up to 200 names,   numbers and 
        communication   parameters.    This  command  is  also  a   small 
        environment in itself.  From here, you can dial or revise any one 
        of  the  200  numbers,  change any one of the  5  prefix  dialing 
        strings,  enter  a  manual  dial mode or just  page  through  the 
        listing.  There are Nine sub-function as follows:

                  C) Clear entry(s)
                  D) Dial an entry
                  E) Revise the Prefix file
                  N) Next page of the directory
                  M) Manual dial a number
                  P) Previous page of the directory
                  R) Revise an entry
                  X) Exit back to Qmodem
                  #) 0 to 9, shows numbered page


             Clear entry(s)

             The  familiar  "Number >" shows up again waiting for you  to 


        Qmodem - Telecommunications Program Version 1.13  Page 11


        enter  a number in the range 1 - 200.   Pressing  [RETURN]  exits 
        back to the dialing option menu.   After entering a number, say 1 
        for  example,  Qmodem  asks "Through >".   Here you can  enter  a 
        larger  number if you want to clear a continuous group  or  press 
        [RETURN] and Qmodem will repeat the first number for you.   Last, 
        Qmodem says "Are you sure ?".  To clear them a 'Y' or 'y' must be 
        entered, anything else and Qmodem aborts the clear command.


             Dialing an entry

             Again,   the  option  side of the screen will clear and  you 
        will see the prompt "Number >".   Now you have two options:  One,  
        you can enter a number in the range 1 - 200 and press enter,   or 
        Two,  you can prefix the number with one of five characters, [ +,  
        -,  !,  @,  and  #].   This will cause  one of the five  optional 
        prefix  strings  to  be tacked on to the phone  number  from  the 
        entry.   The  following  examples show both good and bad  dialing 
        entries:

                  Good ==>       Number >+1
                                 Number >#200
                                 Number >123

                  Bad ===>       Number >a12  (a is not a valid prefix)
                                 Number >201  (number > 200)
                                 Number >$1   ($ is not a valid prefix)

             As I mentioned above,  Qmodem now has the capability to dial 
        up to 10 different numbers at one time!  At either of the dialing 
        prompts  (quick dial or from within the dialing  directory),  you 
        can  specify  up  to 10 different entry  numbers  (complete  with 
        prefix  codes) to be cycled through until a connection  has  been 
        established. 
             
             At  the dial prompt,  you are now allowed to enter up to  70 
        characters that define the entries in the phone book.  An example 
        will be helpful now:

                  [(dial prompt)] +1, +12, +123, +!199- 50 51,52,53<cr>
             
             Whew!   That  is a lot of dialing commands!    Here is  what 
        happens  next.    Qmodem   parses  (takes apart)  the  string  of 
        characters  and  places  each dialing  command  into  a  separate 
        holding  area.    There are only 10 such holding areas so  Qmodem 
        will  ignore any  extras.   The characters that tell Qmodem  that 
        this   is  a  new number are the comma "," and the  space   "  ".    
        Commas  and spaces can  be next  to  each  other for  clarity  if  
        you   so choose.     As  in  the example,   the first area   will 
        contain the string "+1".   The second will contain "+12",   third 
        "+123",   fourth "+!199-",   fifth "50", sixth has "51",  seventh 
        holds "52" and the eighth contains "53".  
             
             As  before,    note  that commas  and  spaces  can  be  used 
        together   and   are  ignored  by Qmodem.   When Qmodem  finds  a 


        Qmodem - Telecommunications Program Version 1.13  Page 12


        holding area that has more  that six characters,   it flags it as 
        invalid and goes on to the next one.    Remember,    the  maximum  
        characters  is six for   any  one  dial string!   

             Now comes the neat part!   If you enter two or more  entries 
        to dial, Qmodem automatically puts you in Re-Dial mode and starts 
        through  the  list,  one at a time until it makes  a  connection.  

             When  Qmodem senses the connection,  it removes  that  entry 
        from the list  so  that when you finish the call,   you can press 
        Alt-Q  to continue with the previously selected numbers.
         

             Revise Prefix entries

             This is much the same as revising a dialing entry.  A window 
        will  open up near the bottom of the screen showing you all 5  of 
        the prefix entries.   Enter the prefix character that corresponds 
        to the string you want to change or press [RETURN].   To clear an 
        entry, press [SPACE] and then [RETURN].  

             As stated earlier in the documentation, the prefix codes can 
        be used in a variety of ways.  Let me set up a couple of examples 
        to  demonstrate the versatility of prefix codes.   I will make  a 
        couple of assumptions: that we are using a Hayes compatible modem 
        and that we use three different long distance services.

             Here are the Prefix code strings currently stored:

             +) ,,,1234567
             -) 1
             !) 123-4567,,,1234567
             @) 9,,
             #) 999-9999,,,1234

             Let's  say we are using the type of service that  needs  the 
        special  codes  at the beginning of the call.   We want  to  call 
        number  12  in  the directory.  The correct  entry  to  the  dial 
        subcommand  would  be "!12".   The resulting command sent to  the 
        modem  would be:      

                  ATDT999-9999,,,1234319 266  8086<cr>.   

             The  commas  used in the prefix codes are assumed to be  the 
        default   2  second delay used by most Hayes  compatible  modems.   
        If  you use a long distance system,   you will have to experiment 
        with how  many commas you need to make a successful call.

             In the second scenario,  the service in use needs a password 
        at  the end of the long distance number.   So,  to dial number 12 
        again,  use  the  command "12+".   This will send  the  following 
        string to the modem:   

                  ATDT319 266 8086,,,1234567<cr>.


        Qmodem - Telecommunications Program Version 1.13  Page 13


             And  last but not least,  a service that uses both types  of 
        passwords.   To make things seem worse,  we are going to make the 
        call at work using the PBX exchange.   This way,  I can make full 
        use of three prefix codes at the same time.   Once again, we will 
        dial  12  from  the  directory.   The dialing  command  would  be 
        "@!12+".   

             The  string  sent to the modem would  be  as  follows:    
                  
                  ATDT9,999-9999,,,1234319 266 8086,,,,1234567

             Of  course,  this  string is 45 characters and  most  modems 
        limit the input  to  40.    Be careful not to exceed the   limit!   
        Take  out unnecessary spaces and commas to fit.


             Manual dial

             With  manual  dial,  any combination of numbers and  letters 
        (like  SmartModem(tm)  commands)  can be used.    Note  too  that  
        the  dialing  prefixes  are valid in manual  dial   mode!   Also,  
        after  using manual dial,   the Alt-Q redial will use the  number  
        entered  for  the last manual dial.   This will most likely  save 
        some  typing time  for  those of you that use   strange   dialing  
        combinations.

             I  did  not put a limit on the number of characters  and  or 
        letters  that could be entered in the manual dial.   It is up  to  
        you  to determine how many characters that can be entered  before 
        your modem will stop accepting data.


             Next page

             Shows  the next page of the dialing directory unless page 10 
        is already displayed.


             Previous page

             Shows the previous page of the dialing directory unless page 
        1 is already displayed.


             Revise an entry

             The options side of the screen will clear and a prompt  will 
        say "Number >".  Enter the number of the directory to be changed.  
        Note  that the number to be changed does not have to be displayed 
        for this to work.   Any number between 1 and 200 including 1  and 
        200  will work fine.   

             A window will open up in the top middle of the screen.  Each 
        part  of the entry number is displayed,  one part at a time,  and 
        waits  for you to enter something.   If,  for  example,  you  are 


        Qmodem - Telecommunications Program Version 1.13  Page 14


        updating  just the number for a bulletin board,  when the name is 
        displayed, just press [RETURN] to skip to the next entry.  A null 
        entry in the form of [RETURN] at any prompt in the revise  window 
        will NOT change the previous data for that entry. In other words, 
        you  won't have to retype all of the data every time you want  to 
        make a small change.  

             When  the  revision is complete,  the window will  disappear  
        and the directory will be updated on disk.  


             Exit dialing directory

             This  will make the dialing directory window  disappear  and 
        bring back the main screen just as it was before.


             Alt-E Echo toggle

             This will turn on and off the Echo feature of Qmodem.   This 
        is  used in case your keyboard strokes are echoed like "HHEELLOO" 
        or not visible at all.


             Alt-F Configuration menu

             The configuration menu has been moved to a separate  program 
        called  QINSTALL.    Refer  to  Appendix  A  for  instruction  on 
        Installations.


             Alt-G  Graphics toggle

             This  is  used to toggle the display of ANSI  graphics.   It 
        also controls  the  music to be heard if there is any.    To  use  
        ANSI  graphics,   you  MUST have the ANSI.SYS in your  CONFIG.SYS 
        file at boot-up time.   For further questions about ANSI,  please 
        consult your DOS manual.


             Alt-H  Hang up the Modem

             This  may  do one of two things depending on what  you  have 
        entered in the configuration.   If you have entered "DTR" for the 
        modem hangup string,  Qmodem will toggle the "DTR" signal and the 
        connection will be dropped.   Otherwise,  it sends  out the Modem 
        HangUp string.


        Qmodem - Telecommunications Program Version 1.13  Page 15


             Alt-I  Information on Qmodem

             This  will  always tell you what version of Qmodem  you  are 
        using,  The day it was compiled, and MY name, John Friel III.  If 
        you  have  any problems with Qmodem,  please send me a card or  a 
        letter and include this information.   This is the only way I can 
        accurately solve the problem.


             Alt-J  Function key menu

             This  will open up a rather large window with 5  parameters.  
        Straight,  Shifted,  Ctrl,  Alt and Return to Qmodem.   Of course 
        this is only good for the 10 function keys.   Select 1-4 to  view 
        the current definitions for the key group.   If you want to alter 
        any  of the keys,  enter the number to the left of the definition 
        at  the  bottom.   

             There  are  Two  special character you  can  use.   The  "{" 
        character will be substituted  by the [RETURN] key,  and the  "~" 
        will cause a one-half second pause.  


             Alt-L  Log new drive

             This  opens a small window and asks for the drive letter  to 
        become  the default drive.   This works in conjunction  with  the 
        Alt-W  and  downloads if no alternate drive was  defined.   Drive 
        letters A through Z  are valid.


             Alt-O  Change Sub-directories

             You  MUST  be  using DOS 2.0 or higher for this  command  to 
        work.  This has to be one of the neater features of Qmodem.  With 
        this command,  not one,  but two windows open up.   The long tall 
        one  on the left of the screen is a listing of valid sub-dirs for 
        the current directory you are in.  if you don't have any sub-dirs 
        or  don't use them,  this would be blank.   the other main window 
        lists  your  current path (if any) and waits for you to  enter  a 
        CHDIR  command.   Any valid CD command can be entered  here,  not 
        just what shows in the left column.  

             Examples:

             The current sub dir is C:\TURBO\QMODEM and I pressed Alt-O.
             The left column would list  .
                                         ..
                                         TESTING
                                         COLOSSUS

             Only 2 optional sub-dirs showed up.   To select TESTING, you 
        only  need enter "testing" in the main window.   No need to  type 
        the whole thing in again.   If you enter something wrong,  Qmodem 
        will  give  you the message "Invalid CHDIR  command.  No  changes 


        Qmodem - Telecommunications Program Version 1.13  Page 16


        made." and the windows will disappear.  On the other hand, Taking 
        the same example as above,  if I wanted to switch to  my optional 
        download  directory,  I could have typed in \COMM\DOWNLOAD to the 
        prompt  and (provided the path was valid) I would then be  at  my 
        download sub-dir.  Then I could do an Alt-W to check things out.

             Note too, that if you include the drive specifier with a new 
        path command,  only the path on that drive is changed.   You will 
        not change your current logged drive to that which was specified.  
        This is important to remember,  The only way to change the logged 
        drive is with the Alt-L command.


             Alt-P  Communications parameters

             You  can  change your communication parameters  "on-the-fly" 
        without  having  you  modem  hang  up.   Just  select  the  right 
        parameters from the list shown. Pressing [RETURN] alone keeps the  
        previous  setting and exits to Qmodem ready.  If one of the  list 
        entries is selected,  the communication parameters   are  altered 
        to reflect the new  choice  before  the window disappears.


             Alt-Q  Redial last number

             The  last number   dialed  through  the  Alt-D  command  can  
        be  repeatedly dialed until connection is made.    You MUST  have  
        used  the   Alt-D first or you will get the message  "Nothing  to 
        Redial".   
             
             Provided  there  is a number to redial,   Qmodem  shows  the 
        current time redial was entered,  the current retry  number,  the 
        time and the statistics about the number (who and what the number 
        is).   Depending on how you have your modem set up,  specifically 
        the S7 register in the Hayes,  the modem can time out and you get 
        a "* Modem timed out or line busy *" message or the  Redial delay 
        was hit and Qmodem cycles the redial itself.  

             Please keep the Redial delay above 45 seconds,  That way you 
        are  assured  of getting at least a busy signal and  not  cycling 
        just  as  the BBS is answering the phone.   

             While the window is open, you have Three commands: 
                  
                  C)ycle    cancels the current call in progress and goes 
                            on to the next number.
                  D)elete   cancels the current call and deletes it  from 
                            the queue.   This means Redial will no longer 
                            try the number.
                  Any  KEY  will cancel the redial window and  bring  you                     
                            back  to Qmodem's  terminal  mode.   Pressing 
                            Alt-Q  again  will restart the dialing  cycle 
                            again.


        Qmodem - Telecommunications Program Version 1.13  Page 17


             Alt-R  DOS shell

             If  there  is  enough memory in your system and  a  copy  of 
        COMMAND.COM is in the current path,   you  can temporarily   drop 
        to DOS and return.   

             All  DOS commands are  then available,  should you  wish  to 
        format a disk for example.  You can NOT  execute any program that 
        attaches itself to DOS.    SideKick is a good example.  To return 
        to Qmodem,  enter the EXIT command at the DOS prompt.   Remember,  
        not  all  programs can be executed  in  this fashion,   Qmodem is 
        not designed to be  a  DOS shell.

             Qmodem  will  try  to position you back to  where  you  were 
        before  execution of Alt-R.   But because of stupid Drive  Letter 
        limitation in DOS,  Qmodem may fail in this task.   Drive letters 
        higher  than O:  are not recognized as valid and return an error, 
        even  though  DOS 3.0 and up allow for drives  up  to  Z.   Turbo 
        Pascal  mimics the error and will not let you log a disk with the 
        ChDir  procedure higher than O:.   

             I have gotten around that to some extent,  but it is iffy at 
        best.   Qmodem will print a "Warning" message on the screen  upon 
        return if you were logged to a drive higher than O:.   If,  while 
        you  were  in the DOS shell,  you changed drives and  the  logged 
        drive previous to the Alt-R was higher than O:, Qmodem will say:
             
             * Warning: previous Drive\Path may be different.

             This  means  you  should check with Alt-O and Alt-L  to  see 
        where you are.


             Alt-S  Split screen mode

             The  screen  is  divided into two  partitions.   The  bottom 
        partition  has  4 lines and the top has  20  lines.    I  thought 
        there  might  be a need for something like this so here   it  is.   
        Alt-S  is a toggle,  so hitting Alt-S again will drop you out  of  
        split   screen   mode.    This is now  true  split  screen   mode 
        complete  with  a  254  character  buffer.    Pressing  the  <CR> 
        transmits  the buffer.   The keystrokes are kept track on on  the 
        dividing  line.   The  character "{" can be used to substitute  a 
        [CR] in the string.


             Alt-T  Screen Dump

             This  copies  the  screen  in  its entirety  to  a  file  as 
        specified in Qinstall.  The screen is APPENDed to the file with a 
        Time and Date stamp.


        Qmodem - Telecommunications Program Version 1.13  Page 18


        2.16      Alt-V  View a file

             This has several nice features wrapped into one.  It will do 
        a  selective  directory  search  if wildcards  are  used  in  the 
        filename.  Any number of these can occur until you either enter a 
        valid  filename  or you press [RETURN] for an  invalid  filename.  
        Both  exit back to Qmodem ready.   

             If  you  enter a valid filename,  you  are then  asked  what 
        method  you  would like to view the  file.   Options  include  1) 
        Qmodem  internal  method,   2) DOS TYPE command,  and   3)   your  
        favorite List or Browse  utility.   The  last  two choices depend 
        on how much free memory you have in your  machine.   Refer to the 
        DOS  Shell command as the last 2 choices use a subset of the  DOS 
        Shell.     If you select 3,  the  window clears and you are given 
        a chance to read the  bottom line which states:   "Press  [SPACE] 
        to pause,  [Esc] to exit.   Bytes queued  = X".    The later part  
        has  to  do  with the amount of  data coming in  while  you   are 
        viewing  a  file.    This will let you  know where  you are  with 
        respect to communications.   


             Alt-W  Disk directory with Xmit time

             This  is just like the DOS version of DIR /p.   Depending on 
        where you are with respect to sub-directories,  all of the normal 
        files are displayed with their respective attributes.  One of the 
        enhancements  I  have made is to add the Transmit times  to  each 
        file.   This Xmit time is is based on your current baud rate  set 
        by  the Alt-P command.   Try changing the baud rate and doing  an 
        Alt-W  and see the Xmit times change.   Don't you wish we all had 
        9600 baud modems??  I do!  

             For those of you who have very lengthy directories,  you can 
        press  the [Esc] key and Qmodem will skip the rest of  the  files 
        and  show you the free space on the drive.   That's something DOS 
        won't do.


             Alt-X  Exiting Qmodem

             Pressing Alt-X will open yet another window (do you get  the 
        feeling  that  I  like the use of the windows??) and ask  if  you 
        really want to exit.   Of course,  this is just a safety valve in 
        case  that  you really didn't intend to press Alt-X.   If you  do 
        exit though,   no matter where you are in your hard disk,  Qmodem 
        will   return you to where you started.   Qmodem will also  close 
        your Capture File if it is open and restore you system to normal.
             
             Another command has been added to the Alt-X, entering an 'X' 
        in response.  This will cause Qmodem to exit to DOS and leave the 
        DTR line active.   If you were online with another computer,  you 
        could  issue the Alt-X command,  enter an 'X',  format a disk  or 
        some such thing, and re-invoke Qmodem and still be online.  


        Qmodem - Telecommunications Program Version 1.13  Page 19


             Alt-Y  Delete a file

             Yes  Virginia,  there  is a file delete routine  in  Qmodem.  
        Like  most file delete methods,  Qmodem asks for a valid filename 
        and  checks to see if that file exist in the  current  directory.  
        If it does, it asks you again if you really really want to delete 
        this  file.   This  will be the last chance before you  might  do 
        something  that can only be regretted later.   Please be  careful 
        with this one!


             Alt-Z  Xon / Xoff toggle

             This  will toggle the Xon / Xoff error checking  built  into 
        Qmodem.   Xon  /  Xoff  is a very simple means  of  flow  control 
        usually used by mini and mainframe computers.  With Xon / Xoff in 
        the OFF mode,  a buffer overrun may occur in Qmodem on long ASCII 
        transmissions.


        Qmodem - Telecommunications Program Version 1.13  Page 20


             PgUp  Upload a file

             The  PgUp  key will open a window and ask you what  type  of 
        transfer protocol you would like to use.  The choices are spelled 
        right  out.    

                            1)  ASCII  
                            2)  Xmodem  
                            3)  Xmodem CRC   
                            4)  Relaxed Xmodem  
                            5)  IMP
                            5)  Exit.   

             I  personally got tired of  adding  '=X' to all of  my  file 
        transfers with  PC-Talk.     How many times have  you been  in  a  
        hurry with an upload or a  download and  forgot  the '=X'?    Did 
        it screw  things up?     Now  you know why I like  to put  things 
        in menus. Let me explain a about the different transfer methods.

             ASCII  Transfer.   When  you select ASCII for  the  transfer 
        method,  be  aware that line noise could make that  nice  looking 
        documentation   look  funny  on the other  end.    Enough   said.   
        The  options  that  immediately show up for the transfer  are  as 
        follows:

                      'Enter  the  filename to Transmit >'  

            Answer this  with  the file you want to send.    Next you get 
        a list of transfer methods.  1)  Prompted   2)  Time delay  3) No 
        delay.    Each  one  has  its advantages and disadvantages  based 
        upon  what kind of computer you are talking to.    Prompted  asks 
        you  for the character to look for before sending a line of data.   
        The prompt character cannot be a [SPACE].    Time delay asks  you 
        to  enter  a  number in Hundredths of a  second  to  wait  before 
        sending a line of data.    No delay is  a 'Blast that data' until 
        it is all sent.  

             When ASCII mode is selected,  XON / XOFF protocol is also in 
        effect.   This was added at a very late date to support the  mini 
        and   mainframe  methods.    At  any time  during  the  transfer,  
        pressing the PgUp key will  terminate the operation and bring you 
        to the Qmodem ready mode.

             XMODEM  Transfer.    There are two methods currently used in 
        public  domain to compute the validity of data sent  via  XMODEM.  
        The first method is called checksum.  In checksum, the data block 
        has  all  of the bytes added together and is then ANDed with  hex 
        'FF'.   While  checksum is a pretty reliable method  of  insuring 
        that  the  file  you sent is correct,  errors can  creep  in.   I 
        believe the rate of error detection is somewhere near 99.6%.  

             The  second   method  of  error  checking  is  called   CRC,  
        short  for Cylindrical  Redundancy  Checking.   This  method  has  
        an  error detection rate of 99.9969%.    Unfortunately,  not  all 
        BBS software has CRC transfer available.    Check with your local 


        Qmodem - Telecommunications Program Version 1.13  Page 21


        board  to  find  out  which method should  be  used.   Qmodem  is 
        intelligent  enough to figure  out  which is being sent when  you  
        download,   so   if  you select the wrong one,  Qmodem will  make 
        sure you get it right.

             First,  enter  a valid filename to  transmit.   Qmodem  will 
        check  it out.   Qmodem will wait approximately 20 seconds for  a 
        NAK to be received to start the transfer.   When the transfer  is 
        started,  much  useful information is displayed.  Total blocks to 
        send,  Transmit  time based on the current baud rate,  The  block 
        being sent,  The current error count, and the time remaining till 
        completion.  The time remaining till completion is based upon the 
        number of blocks remaining at any given time.   

             Lets face it,  You will not be sending your data at the full 
        baud  rate all of the time with XMODEM.   The time delay for  the 
        NAK/ACK response slows this down.  Qmodem is fast though and this 
        will certainly help the phone bills.  Here too, pressing the PgUp 
        will terminate the transfer if so desired.

             Relaxed  Xmodem is nothing more than regular Xmodem,  except 
        the timing has been relaxed by a factor of 10.   In other  words, 
        it  takes  ten  times  longer  for  the  error  condition  to  be 
        generated.   CompuServe users will appreciate this.   In fact, it 
        was  because of the way CompuServe's computers handle (or fail to 
        handle)  Xmodem that this was added.   Only use "Relaxed  Xmodem" 
        when  talking  to  CompuServe  and  even  then  use  it  at  your 
        discretion.   

             The last one is IMP.   This was completely thought up by  me 
        and  should  NOT be confused with any other protocol  out  there.  
        Again,  this  is  Unique to Qmodem v1.11 and up.   IMP  (Internal 
        Modem  Protocol) is just that,  it relies on the availability  of 
        modems  to  do  their own data  transmission  checking.   A  good 
        example  would be the much talked about MNP from  Microcom.   MNP 
        protocol  can be implemented on the hardware level usually inside 
        your modem.  When two modems connect using MNP, the modems do all 
        the  checking and retransmission necessary for a clean  exchange.  
        Several  modem manufacturers like ARK (ARK  24K),  Novations  new 
        2400, MultiTech's new 224 etc. have MNP built in.  

             But how does Qmodem take advantage of the MNP?   

             Simple,  it doesn't do anything!   Actually,  the modems are 
        always verifying the data so there ARE no errors in the transfer.  
        IMP  is a block oriented transfer method that uses no ACK or  NAK 
        in the Xmodem sense.   Every block that goes out is guaranteed to 
        get  there the way it was sent.   So,  IMP does not wait for  the 
        other  computer to say if the block was correct or not,  that  is 
        handled by the modems in REAL time.  

             But why does CTS have to be used?  

             In my experiences with MNP in the modems,  they use the  CTS 
        signal  to  temporarily halt the flow to the modem when an  error 


        Qmodem - Telecommunications Program Version 1.13  Page 22


        does occur.   If they didn't, Qmodem would overflow the modem and 
        lost data would result, and ultimately, a bad file transfer.  

             What are the advantages of IMP?

             In  my  testing  (from Virginia to Iowa,  using  2  ARK  24K 
        modems),  IMP  showed an impressive 115 blocks a minute  at  2400 
        baud.   To put that in perspective, normal Xmodem (or Xmodem CRC) 
        could only get about 88 blocks a minute at 2400 baud.   Remember, 
        to use IMP, the modems MUST have an internal protocol. 


        Qmodem - Telecommunications Program Version 1.13  Page 23


             PgDn  Download a file

             Here  too,  you get the menu asking for the type of transfer 
        you want to use.   Enter the appropriate response.   Let me  jump 
        right into the separate protocols.

             ASCII.   The  screen  will clear and you will be  told  that 
        pressing  the  PgDn key will terminate the transfer and save  the 
        file.   If you start the transfer, but no data has been received, 
        Qmodem will pretend as if no file was ever sent.   I don't  think 
        ASCII need much more explanation.

             XMODEM.   This  is  the new and improved method  of  keeping 
        track  of the transfer.   All types of errors are kept track  of.  
        When  the transfer starts,  the download window clears and a list 
        of  all of the errors are displayed.   Total blocks  received  is 
        displayed at the top.  The last line of the window shows the most 
        recent error message and at which block it occurred. 

             If you receive ten errors in a row,  Qmodem will cancel  the 
        transfer.  As soon as one block of data is received successfully, 
        the error count is set to zero.  Qmodem tries to recover from all 
        data  errors.   You  will note too the speed of which Qmodem  can 
        recover.    If you are having a problem,  give me a call.   I  am 
        willing  to  talk to you about any transfer problem that you  may 
        encounter.
             
             Again,   "Relaxed  Xmodem"  was  designed  for  talking   to 
        CompuServe.   See  the  description  under  File  Upload  in  the 
        previous section.

             For a description of IMP,  see the previous discussion under 
        Upload protocols.

             Now  a brief description of the errors that can be  detected 
        during  an  Xmodem  transfer.   Qmodem keeps track of  each  type 
        separately.  

             1)   Long block error  -  Caused usually by line  noise  
             and this creates extra characters in the transmission. 

             2)   Short  block error  -  if the line is weak or  you  
             are recovering from a previous error,  this can result. 
             It means that Qmodem did not receive enough  characters  
             to complete the data block.  

             3)    SOH error -  The first character of every  Xmodem  
             block  is  the SOH character (01  HEX).  If  the  first 
             character is not an SOH, Qmodem flags the block as bad. 
             Chances are that if the first byte is bad, so are a few 
             others  due  to the fact that line noise  usually  last 
             long enough to corrupt more that one byte.

             4)    Complement error -  The data block had two  bytes  
             in   the   header  to  hold the block  number  that  is   


        Qmodem - Telecommunications Program Version 1.13  Page 24


             being  transmitted/received.    The  second  of   these  
             two   is  the complement of the first (first  byte  XOR 
             255).   This ensures that Qmodem is getting the correct 
             block.

             5)    Block # error  -  This is usually caused by  line  
             noise  too.    The transmitting computer received a NAK 
             in place  of the  ACK Qmodem sent and resends the block 
             you just received successfully.    Essentially,  Qmodem  
             ignores the block  and sends another ACK.

             6)     Checksum/CRC  error -  Every block  of  data  in 
             Xmodem   is followed by either a Checksum byte or by  2 
             CRC  bytes.  CRC  is  a more accurate method  of  error 
             detection,   but  requires one more byte to be sent  in 
             every block.  If the Checksum or CRC is wrong,   Qmodem 
             sends a NAK and discards  the  data.  Again, line noise 
             is usually the culprit.

             This  might be an appropriate place to mention that  if  you 
        have "Call Waiting" with your phone service and someone calls you 
        while  you are doing an Upload/Download,  you stand a  chance  of 
        getting  errors.   This may even terminate the transfer depending 
        on the noise generated.  Be forewarned!


             Up Arrow  Scroll back the screen

             By  pressing the Up arrow,  you can scroll back through  the 
        previous lines of data that have come to the tube.    The   valid 
        keys  in  scroll  back mode are  

                  1) Up arrow    - go up one line  
                  2) Down arrow  - go down one line
                  3) PgUp        - go up one page
                  4) PgDn        - go down one page
                  5) Esc         - exit scroll back

             Pressing the [Esc] will exit scroll back mode.   This should 
        be  pretty much self  explanatory.    When you  reach the top  of 
        the scroll,  you get a message :

                                 * Top of Scroll 

        When you are at the bottom : 

                               * Bottom of Scroll


        Qmodem - Telecommunications Program Version 1.13  Page 25


                               A P P E N D I X   A

                     Qinstall - Qmodem Installation Program
                  
             Qinstall  takes the place of the Alt-F key combination  that 
        previous versions of Qmodem had.   More information was needed to 
        explain  the configuration than Qmodem could hold.   I have taken 
        the Alt-F screens and reworked for ease of setup.

             Qinstall will read any QMODEM.CNF file starting with  Qmodem 
        version  1.06.   You  may see garbage in some of the  data  entry 
        areas depending on how old your CNF file is.   It is important to 
        note; Qmodem v1.13 REQUIRES running Qinstall v1.13!  

             Lets jump right in and execute Qinstall.

             The first thing you will see is the familiar QMODEM logo and 
        a  list  of options.   These options are basically the same  ones 
        that  Qmodem used to have.   I recommend going through all Six so 
        you can make sure the data looks good.

             Select  option number One.   Qinstall will display  the  Six 
        Color  Options of Qmodem,  a Color Chart,  and the sample  Qmodem 
        display near the top.   Depending on the type of monitor card you 
        are  using,  the  edit  fields  are  either  inverse  video  (for 
        Monochrome)  or hi intensity White on Blue (for Color  Graphics).  

             Several  keys need to be explained;  as Qinstall contains  a 
        mini editor.  

                  Tab, Shift-Tab           Goes from field to field.
                  Up and Down Arrows            Same.
                  Left and Right Arrows    Moves by character.
                  Insert and ^V            Toggles INSERT mode.
                  Delete                   Deletes 1 character.
                  Esc                      Exit with no update
                  F10                      Exit and Update.
                  F1                       Context sensitive Help
             
             If you have any questions on any of the fields, press the F1 
        key and Qinstall will show you more information about that field.  
        If  you do not want to keep the changes made,  and would like  to 
        reset  them  to whatever they were when you entered  the  screen, 
        press  Esc.   To tell Qinstall to keep the changes you have made, 
        press F10.  Pressing F10 does Two things... a preliminary Edit on 
        the data,  and if it is good,  saves it.   If you have any  wrong 
        data,  Qinstall  will  warn  you and position the cursor  to  the 
        offending spot.  

             Qinstall has been created with the NEW USER in mind.  If you 
        are having trouble,  I would like to know about it.  Please write 
        me at the address given in Appendix D.


        Qmodem - Telecommunications Program Version 1.13  Page 26


                               A P P E N D I X   B


             TURBO Pascal Usage

             TURBO   Pascal  was  used  to  create  Qmodem  for   several 
        reasons.    The  language  is  easy  to  work  with.   It  allows 
        structured top-down programming and the  ability  to define  your 
        own types of variables.    Just as  a side   note,   Qmodem  does  
        not have a  single  GOTO  statement!  Another  advantage  is  the  
        creation  of  .COM  files  from  the compiler.   No  more  having  
        to load BASIC  and  then  run  your program.
             
             The   program editor is another big plus to the system.   It 
        emulates  the WordStar editor almost completely.    TURBO  Pascal 
        also  lets  you use all of the available memory in  your  system.  
        Programs can be larger than the available memory by the efficient 
        use of overlays.   I could go on and on about TURBO  Pascal.   By 
        the way,  I am not affiliated with Borland International,  just a 
        very happy customer.


        Qmodem - Telecommunications Program Version 1.13  Page 27


                               A P P E N D I X   C


             File structure of the phone directory

             The   following  is a copy from the source code  which shows 
        the file structure.

        Type
           check_bit        = (even, none, oddd);
           phone_type       = record
                                name                   : string[25];
                                number                 : string[14];
                                speed, dbits, sbits    : integer;
                                parity                 : check_bit;
                              end;


        Qmodem - Telecommunications Program Version 1.13  Page 28


                               A P P E N D I X   D


             Please consider the donation of $20.00.   Good software at a  
        good   price  is hard to come by.    We at  the  Forbin   Project 
        Inc.  support    the idea of "Shareware" and "Freeware" and  hope 
        all    of  you  do too.      It's because of you that I am   able  
        to  bring  you helpful programs like Qmodem.  Thanks again.



                             The Forbin Project Inc.
                             c/o John Friel III
                             715 Walnut Street
                             Cedar Falls, Iowa 50613