DACPLAY Version 1.0
     (C) 1993 Kevin Patterson, KHP-UNISystems Co.
      
     Sound Hardware Circuits Document
      
      
     This document is supplied to provide simple universal circuits for use
     with DACPLAY and other programs.  These are inexpensive devices the
     produce sound output that rivals the quality of the original Sound
     Blaster.
      
      
     I.   A Simple Single Chip D/A Converter
      
          The following is a simple circuit hight quality sound, and
     requires only a few components.  This circuit will work with other
     software, such as Mark J. Cox's MODPLAY and MODRES, which play amiga
     sound files on your PC.  It even sounds better than a Sound Blaster
     for digital audio!
      
         You will need:
      
         IC1   ZN426
         C1    10 uF electrolytic capacitor, 10V+
         C2    4.7 uF electrolytic capacitor, 10V+
         R1    330 ohm resistor, 5%, 1/8 watt
         RJ1   Female RCA jack for line-level output to your amplifier
         RJ2   25 pin male D-type (DB-25) connector for your parallel port
      
         A +5v supply
      
                                    ZN426E    +5V
                    RJ2            Ú--------¿  ³
                       (2)  D0  ---´9     14Ã--´
          Pins in ()   (3)  D1  ---´10      ³ ÚÁ¿
          are on the   (4)  D2  ---´11      ³ ³ ³ R1 330 ê
          DB-25 con.   (5)  D3  ---´12      ³ ÀÂÙ
                       (6)  D4  ---´13     5Ã--´
                       (7)  D5  ---´1      6Ã--´       +
                       (8)  D6  ---´2      4Ã--³--------´ ÛÛ----é RJ1
                       (9)  D7  ---´3   7   ³  ³        10æF    ³
                                   À----Â---Ù -Á- +             ³
                                        ³     ÞÛÝ C1 4.7æF      ³
                                        ³      ³                ³
                      (24)  ------------Á------Á----------------Ù
                      (25)  ------------¿
                                        ³
                                       ÍÏÍ
                                        Ñ GND
      
          Depending on your amplifier, if the above circuit sounds poor,
     try removing the 10 uF capacitor.  This circuit automatically shuts
     off when the DB-25 connector is unplugged from the computer.
          The ZN428 is made by Ferranti or Plessey, which are UK
     manufacturers.  It is an excellent chip, but it's hard to get.  I
     obtained one from EasyTech, a mail-order electronics supplier listed
     in most electronics magazines.
      
      
      






     II.  An Alternate DAC
      
     If you can't get the ZN426 you can use a DAC0800, DAC0801, DAC0803
     from National Semiconductors in the circuit below.
      
                                    DAC 080x
                    DB-25          Ú--------¿ 0.01æF   0.1æF
                       (2)  D0  ---´12    16Ã--´ ÛÛ----´ ÛÛ--Â--- GND
                       (3)  D1  ---´11      ³                ³
                       (4)  D2  ---´10    15Ã---------ÛÛÛÛÛÛ-Ù5kê
                       (5)  D3  ---´9       ³
                       (6)  D4  ---´8     14Ã---------ÛÛÛÛÛÛ-¿5kê
                       (7)  D5  ---´7     13Ã----------------´
                       (8)  D6  ---´6      2Ã--´ ÛÛ----------Á-- +5V
                       (9)  D7  ---´5 3 1  4Ã----------´ ÛÛ-----------é RCA
                                   À--Â-Â---Ù  0.1æF  + 10æF          ³ out
                                      À-´                             ³
                                        ³                             ³
                      (24)  ------------Á-----------------------------Ù
                      (25)  ------------¿
                                        ³
                                       ÍÏÍ
                                        Ñ GND
               
      
         The 0.01 uF and 0.1 uF capacitors are ceramic.  Depending on your
     amplifier, if the above circuit sounds poor, try removing the 10 uF
     capacitor.  This circuit automatically shuts off when the DB-25
     connector is unplugged from the computer.
      
      
     This document is (C) 1993 KHP-UNISystems.
      
     Amiga is a registered trademark of Commodore Computer Corporation?