[]---------------------------------------------------------------------[]
| AMM (Audio Manager Module) Format by TechnoMaestro/RDG.  1995.        |
| Technical documentation. Revision 1.1                                 |
[]---------------------------------------------------------------------[]

Below are the file formats supported by AudioManager 3.x and Platinum Play III.
This DOC is meant for programmers only.
Enjoy!

PROS:
	ю It's supports what S3M, MOD, 669, MTM ... can do. Except some
	  formats, like XM! (Argh!)
	ю It's usually smaller, and compresses quite well.
	ю Quite expandable? (Not expandable for XM compatibility)

CONS:
	ю It's proprietary, and thus, there's little support.
	ю Not easy to implement
	ю I myself will be dumping it for a newer no-limit and XM-compatible
	  format!

TERMS USED:
	Track           =       Channel


ІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІ

	F I L E     F O R M A T S

ІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІ

±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±
AUDIO MANAGER MODULE (AMM)±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±
Bytes і Stuff ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
3     і Signature 'AMM' (Audio Manager Module)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
1     і Character 1Ah. (End Of File marker).
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Version of AM tracker used. LO=Minor HI=Major. 0205h = 2.05.
      і Since there ain't any AM tracker yet (maybe will never be one),
      і set this version to 0.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Info
      і         Bit 0   1=Set MOD note range limit. (Octave 1-6) (MOD)
      і                 (S3M uses limit 2-5! But what the hell!)
      і             1   Reserved
      і             2   1=S3M effect bugs emulation
      і             3   1=Force mono playback
      і             4   1=Stereo music
      і          4-13   Reserved. Set to 0.
      і            14  0=Standard packed patterns 1=Extra packed
      і                (Bit 15 must be set for this bit to take effect)
      і            15  0=Unpacked patterns (standard) 1=Packed
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
40    і Song name.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Number of Tracks (Suggested max = 32) (Also PP3 max)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Number of patterns (Suggested max = 128. True max = 255)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Number of samples (Suggested max = 128. True max = 255)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Song length (number of orders) (Suggested max = 255)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Master volume (Affects the note volume.) (S3M's Global vol)
      і The resultant volume = (NoteVolume*MasterVolume)/64
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Amplification/Mixing mode. Controls amount of multiplication on
      і resultant mixed sound wave. (S3M's Master volume)
      і 0-32767 = Amplification. Observe the below chunk of code for signed
      і           samples multiplication. Note: This multiplication is not
      і           done on individual samples, but on the final resultant
      і           waveform to ensure quality and speed!
      і
      і         MOV  AX,TheSignedSoundWaveWord
      і         IMUL AmplificationValue
      і         SAR  AX,8
      і         (CLIP WAVEFORM HERE)
      і
      і           This is not the actual code in AudioManager/PP3. It's
      і           actually some sort more complicated.
      і           I realize that there are better methods other than
      і           this...but I dare not touch my code again!! Hahaha.
      і           For 16-bit waveform output, the amplification is multiplied
      і           by 256. (That means you can throw off the SAR AX,8 there).
      і
      і 32768   = Quality SHIFT mode. Real quality shift value = Value-32768.
      і -32775    0 being the loudest. This is a method faster than using
      і           master volume, but slower than the standard mixing mode.
      і           The final waveform is SHIFTED x-32768 number of bits to
      і           the right. (Div by exponents of 2).
      і
      і 65535   = Standard mixing mode. Lowest quality, but ensures all sound
      і           are played correctly without clippings.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
1     і Startup speed (as in effect 1)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
1     і Startup tempo (as in effect 2)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
1     і Song source
      і 0=Unknown
      і 1=AM Tracker
      і 2=MOD/NST
      і 3=S3M
      і 4=MTM
      і 5=669
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
      і
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і Number of bytes in extra data section (located after samples).
      і
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
13    і Reserved
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
		  UP TO HERE, HEADER IS 80 BYTES LONG
	      AFTER THIS, ALMOST ALL DATA ARE VARIABLE SIZED
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
x     і Track pan flags. Each Track has one byte flag here.
      і These Track flags contains the position of of Track at
      і startup.
      і  0 (Left most)           64 (Middle)            128 (Right)
      і  255=Disabled Track      254=Surround (not supported yet)
      і  129-137=Adlib channel 1-9. (NOT SUPPORTED YET & WILL CAUSE PROBLEMS)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
x     і Pattern sequence. Each element is 2 bytes long.
      і 65534=Skipped order (padding...S3M)
      і 65535=End of song marker.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
x     і Patterns in this format...
      і All notes throughout the song are divided into Tracks.
      і Therefore, patterns for Track 1 comes first, followed by Track 2,
      і etc... There are 64 rows per pattern. Therefore, for one pattern
      і of a one Track song, 5*64 = 320 bytes are required.
      і
      і aaaabbbb cccccccc dddddddd 00yyyyyy zzzzzzzz
      і BYTE 1  (255=No note, 254=Key off (stop sample))
      і         aaaa = Octave (0-7...maybe next time up to 15? :)
      і         bbbb = Note (0=C, 1=C#, etc... B=B)
      і BYTE 2  (0=No sample/instrument)
      і         cccccccc = Instrument number (1=1st instrument, etc...)
      і BYTE 3  dddddddd = Volume (0-64)
      і BYTE 4  xx = Unused. Keep to 0.
      і         yyyyyy = Effect number
      і BYTE 5  zzzzzzzz = Effect data
      і
      і Value 255 is used throughout the patterns as no-data.
      і Note 255   = No note (use previous)
      і Volume 255 = No volume
      і Sample 255 = No sample (use previous)
      і Efx 255    = No efx
      і
      і However, this method wastes alot of space, and thus, I've abandoned
      і it (I still, however, use it in memory) for a new packed format.
      і As before, each tracks are separated into separate blocks...
      і For one Track, the format is as follows...
      і
      і 4       Length of whole block, excluding these 4 bytes.
      і x       Event
      і x       Event
      і x       ..
      і .       ..
      і
      і Each event is as follows...
      і aa [bb] [cc] [dd] [ee & ff]
      і BYTE 1  - Information byte
      і           BIT 0 1=Note & instrument present (Val 255=Use previous)
      і               1 1=Volume present
      і               2 1=Change in effect number
      і               3 1=Change in effect data
      і               7 1=Data present  0=Empty rows RLE encoded .
      і                   If bit set, then Bit 0-6 = Number of empty rows-1.
      і                   We do not have a signal for end of pattern because
      і                   it isn't necessary, as each pattern must be 64-rows
      і                   and if we reach more than 64 rows, it's time to
      і                   increment the pattern count.
      і                   This bit can save up to 128 empty rows with just
      і                   one byte! :-) Now that's COOL! :-)
      і
      і                   In Extended Compression mode (Bit 14 of info word)
      і                   is set, this bit 7 may remain to be 0, but the next
      і                   3 bits after the events (bit 4-6) = number of empty
      і                   rows follows this event, 0-7.
      і aa = Info byte
      і bb = Optional note number
      і cc = Optional instrument number
      і dd = Optional volume number
      і ee = Optional effect number
      і ff = Optional effect data
      і
      і All of them can be present at one time, and after this info byte,
      і it is followed by...
      і 1-BYTE Note & Instrument number (if present)
      і 1-BYTE Volume number (if present)
      і 1-BYTE New effect number (if present)
      і 1-BYTE New effect data (if present)
      і
      і I used change in effect number as opposed to present effect because
      і I notice many songs, particularly S3Ms by Purple Motion/Skaven
      і uses a same effect for more than 1 row. (Esp. Vibrato,etc...)
      і Thus, I took advantage of this to create smaller files.
      і For each track, by startup, the previous effect and effect data are
      і assumed to be 255 (no efx).
      і
      і The RLE, however, *DOES NOT FALL INTO THIS CONTEXT*. It is purely
      і meant for really empty tracks, with all it's values 255 in memory.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
x     і Sample structure x NumberSamples (info for each sample)
      і Each info is 80 bytes long and is identical to the AMS format.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
x     і Sample data
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
x     і Special data (Author name, etc...)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
x     і Any other data that would not be loaded. :)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД


±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±
AUDIO MANAGER SAMPLE (AMS)±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±
Bytes і Stuff ±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±±
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
3     і Signature 'AMS' (Audio Manager Digital Sample)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
1     і Character 1Ah. (End Of File marker).
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і Reserved for internal use. Used to store memory handle.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і Position within the memory block
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і Reserved. TO BE USED IN SAMPLE LIBRARY AS POINTERS TO POS IN FILE.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і Length (NOTE! AMM can use samples much larger than 64k)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і Loop begin offset
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і Loop past offset (the offset right after the last byte in sample)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
4     і C2 Sample rate (8363 is the standard value) (Not C2 actually)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Default playback rate (for SFX in games) ??????????????/
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
1     і Volume (0-64)
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
2     і Info
      і         Bit 0-1 Type. 00=Adlib 01=4 bit 10=8 bit 11=16 bit
      і                 4 bit samples are not linear, but logarithmic
      і                 values based on internal tables.
      і               2 0=Mono 1=Stereo (left right left right)
      і               3 1=Looped (Loop past offset must not be 0)
      і               4 0=Unsigned 1=Signed
      і               5 0=Normal RAW samples 1=Delta-encoded samples
      і            6-14 Reserved
      і              15 0=Not loaded 1=Loaded
      і
      і
      і                 Delta-Encoded samples use difference between two
      і                 sample bytes/words to encode sample. This method,
      і                 while produces the same file size, compresses
      і                 better using a general purpose compressor, as
      і                 their value ranges are usually small, which helps
      і                 considerably the Huffman Coding compression algo.
      і
      і                 RAW TO DELTA-ENCODED:
      і                 The starting 'previous value' for each sample is 0.
      і                 Then, as each sample element is taken, it is subtracted
      і                 by 'PreviousValue'. The new 'previous value' is taken
      і                 as the current sample value (not the delta-encoded val)
      і
      і                 DELTA-ENCODED TO RAW:
      і                 The starting 'previous value' for each sample is 0.
      і                 Then, a delta-encoded sample is taken and added with
      і                 'previous value'. The new 'previous value' is taken
      і                 as the current decoded value.
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
30    і Sample name
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД
13    і Sample file name
ДДДДДДЕДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДДД

80      TOTAL BYTES



ІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІ

	E F F E C T S

ІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІІ

00xx    No effect

01xx    Set speed
	00      Use previous value
	Others  Set speed. Default is 6.

02xx    Set tempo (BPM)
	00      Use previous value
	Others  Set tempo (BPM) to xx. Default is 125.

03xx    Set master volume (global volume in S3M)
	Set master volume. Varies from 0 to 64.
	Internally, it is multiplied by 4 for range of 0-256 used in AM3.

04xx    Jump to order xx (hexadecimal)
	Jump to next order, at row 0 (if Pattern break was not set) or
	the row specified by pattern break if pattern break was set on
	the same line as this command.

05xx    Pattern break to row xx (hexdecimal! Not decimal as in other formats)
	Jump to next order (if jump to order command was not used to set
	the next target order), row xx.

06xy    Volume slide.
	00      Continue previous (fine/slide)
	x0      Volume slide up by x
	0y      Volume slide down by y
	xF      Fine volume slide up by x
	Fy      Fine volume slide down by y
	FF      Fine volume slide up by F (slide up has more priority).

07xy    Slide up
	00      Continue previous (extra/fine/slide)
	Ey      Extra fine slide up with speed y.
	Fy      Fine slide up with speed y.
	Others  Slide up with speed xy (if xy not [extra] fine).

08xy    Slide down
	00      Continue previous (extra/fine/slide)
	Ey      Extra fine slide down with speed y.
	Fy      Fine slide down with speed y.
	Others  Slide down with speed xy (if xy not [extra] fine).

09xx    Slide to note
	00      Continue slide with previous *slide to note* speed.
	xx      Slide to note by with speed xx.

0Axy    Vibrato
	00      Continue previous.
	xy      Vibrate pitch using active waveform with speed x and
		depth y.
	0y      Retains speed. Sets depth to y.

0Bxy    Tremolo
	00      Continue previous.
	Others  Vibrate volume using active waveform with speed x and
		depth y.

0Cxy    Arpeggio
	00      Continue previous.
	Others  Switch between 3 notes, including the current note quickly
		at every tick. Plays in the order... Current Note,
		Current Note+x semitones, Current Note+y semitones.

0Dxy    Continue vibrato and do volume slide
	00      Continue previous volume slide speed.
	Others  Volume slide, with the same parameters as the normal volume
		slide.

0Exy    Continue slide to note and do volume slide
	00      Continue previous volume slide speed.
	Others  Volume slide, with the same parameters as the normal volume
		slide.

0Fxx    Set sample offset
	Sets sample offset to xx*256.

10xy    Retrigger note [+ optional volume slide]
	Retriggers note and optionally do volume slide too.
	x=Volume slide type
		0: 0    (No volumeslide)
		1: -1
		2: -2
		3: -4
		4: -8
		5: -16
		6: 2/3 times the original volume
		7: 1/2 times the original volume
		8: ?
		9: +1
		A: +2
		B: +4
		C: +8
		D: +16
		E: 3/2 times the original volume
		F: 2 times the original volume
		Where the original volume is the CURRENT volume.
	y=Retrigger note at every y ticks.

11xx    Set panning
	00-128  Left(0)   Middle(64)    Right(128)
	254     Surround (Not supported yet)
	255     Disable channel

12xx    Cut note
	00      No cut
	Others  Cut notes after xx ticks.

13xx    Delay note
	00      Note not played.
	Others  Delays note and triggers it only after xx ticks.

14xy    Tremor
	Turns sound on for x+1 ticks and off for y+1 ticks throughout
	the row.

15xx    Pattern loop
	00      Set start of loop
	Others  Set end of loop and number of repetitions.

16xx    Pattern delay
	00      No delay
	Others  Repeats current row x times without triggering the notes again,
		but applyin the effects.

17xx    Set vibrato waveform to
					     xx VALUES
	Waveform   Name                Retriggered  No Retrigger
	---------- ------------------- -----------  ------------
	/\  /\     Sine (default)           0            4
	  \/  \/

	|\ |\      Ramp down                1            5
	  \| \|

	,-, ,-,    Square                   2            6
	  '-' '-'

	?????????  Random                   3            7

	Retrigger means that it will reset the position within the sine
	table everytime a new note is encountered. By default, the
	waveform is 0.

18xx    Set tremolo waveform to xx.
	See 17xx, Set vibrato waveform.

19xx    Set glissando (Slide to note will slide in halfnotes).
	00      Disable glissando
	Others  Enable glissando. Usually, people use value 1 for enabling
		glissando.

1Axx    Set sample fine tune (set C-2's frequency)
	Set sample fine tune, where xx corresponds to the appropriate
	frequency of C-2.
	Values for X:
		0       - 7895 Hz
		1       - 7941 Hz
		2       - 7985 Hz
		3       - 8046 Hz
		4       - 8107 Hz
		5       - 8169 Hz
		6       - 8232 Hz
		7       - 8280 Hz
		8       - 8363 Hz (No finetune)
		9       - 8413 Hz
		A       - 8463 Hz
		B       - 8529 Hz
		C       - 8581 Hz
		D       - 8651 Hz
		E       - 8723 Hz
		F       - 8757 Hz
	To convert old amiga fine tunes to current fine tune value,
	perform [(ADD 8) AND 1111b].

1Bxx    Set filter
	Amiga hardware stuff (plays with Amiga LED or something).
	Not implemented.

1Cxx    Set stereo control.
	An old Scream Tracker command. Not implemented.

1Dxx    Invert loop (aka InvertFunk/FunkRepeat?)
	Plays sample backwards with speed xx. Not implemented.

1Exx    Set event.
	Sets the event flag in AM3 and sets the value of AM.MI_Event to xx.
	Similar command in Scream Tracker is Zxx.

1Fxx    Fine vibrato (S3M)
	Similar to Vibrato, but 4x finer.


SUMMARY:
	MI@EFXnoEffect                  = 000h
	MI@EFXsetSpeed                  = 001h
	MI@EFXsetTempo                  = 002h
	MI@EFXsetMasterVolume           = 003h
	MI@EFXpatternJump               = 004h
	MI@EFXpatternBreak              = 005h
	MI@EFXvolumeSlide               = 006h
	MI@EFXslideUp                   = 007h
	MI@EFXslideDown                 = 008h
	MI@EFXslideToNote               = 009h
	MI@EFXvibrato                   = 00Ah
	MI@EFXtremolo                   = 00Bh
	MI@EFXarpeggio                  = 00Ch
	MI@EFXvibrato_VolumeSlide       = 00Dh
	MI@EFXslidetoNote_VolumeSlide   = 00Eh
	MI@EFXsetSampleOffset           = 00Fh
	MI@EFXretrigger                 = 010h
	MI@EFXsetPan                    = 011h
	MI@EFXcutNote                   = 012h
	MI@EFXdelayNote                 = 013h
	MI@EFXtremor                    = 014h
	MI@EFXpatternLoop               = 015h
	MI@EFXpatternDelay              = 016h
	MI@EFXsetVibratoWaveform        = 017h
	MI@EFXsetTremoloWaveform        = 018h
	MI@EFXsetGlissando              = 019h
	MI@EFXsetFineTune               = 01Ah
	MI@EFXsetFilter                 = 01Bh
	MI@EFXstereoControl             = 01Ch
	MI@EFXinvertLoop                = 01Dh
	MI@EFXevent                     = 01Eh