dprof/dprof							dprof/dprof

			       DPROF.DOC

    DPROF <proffile> [-call]

    The DPROF program generates profiling output from the binary data file
    generated by an executable which was compiled with profiling enabled.

    In order to use DPROF you must compile your program with the -prof
    option. There are three levels of profiling:

    -prof1	profile only your code (same as -prof with no numerical level)
    -prof2	profile your code and the standard C library
    -prof3	profile your code, the C library, and the amiga library tags

    To use -prof2 you must have DLIB:CSP.LIB (small data profiled c.lib)
    or DLIB:CSRP.LIB (small data profiled c.lib for registered arguments).

    To use -prof3 you must have DLIB:AMIGASP20.LIB (small data profiled
    amiga.lib) or DLIB:AMIGASRP20.LIB (small data profiled amiga.lib for
    registerd arguments).

    Other combinations are possible depending on the options you use for
    linking.  These libraries will not necessarily exist on DCC1:, they are
    most likely lharc'd in DCC2:DLIB or DCC3:DLIB depending on how I've
    arranged the distribution.	Registered users can make other library
    combinations directly from the library source.

				USAGE WARNINGS

    The profiling code is accurate to 20 microseconds under 2.0, 1/60
    second under 1.3.  The profiling code itself will slow down a program
    by quite a bit but, in general, the system makes every attempt to
    filter out its profiling overhead in the statistics file (so the grand
    total time will be less then the actual amount of time the program took
    to run).

    Note, however, that the results will be skewed somewhat anyway, not
    only due to the overhead of the profiling code, but also due to task
    switches and other system overhead.  To get accurate results you should
    only run the executable that is to generate a .dprof file on an
    unloaded system (i.e. don't do anything else while the executable is
    running).  Many calls to very short, quick routines will suffer the
    most and numbers should be taken more in a qualitative fashion than a
    quantitative fashion.

    Keep in mind that it is not necessary to profile everything,
    particulary for large projects.  You may want most of the system to run
    at full speed while only profiling a small part of it at a time.


				     EXAMPLE

    EXAMPLE: -------------------------

	void	fubar1(void);
	void	fubar2(void);
	void	loop(long);

	main(ac, av)
	char *av[];
	{
	    short i;

	    for (i = 0; i < 100; ++i) {
		fubar1();
		fubar2();
	    }
	    loop(10);
	    fubar1();
	    fubar2();
	}

	void
	fubar1()
	{
	    short j;
	    for (j = 0; j < 10000; ++j);
	    fubar2();
	}

	void
	fubar2()
	{
	    short j;
	    for (j = 0; j < 100; ++j);
	}

	void
	loop(n)
	{
	    if (n)
		loop(n - 1);
	}

    ----------------------------------

    compile and the run the program, then dump the profile. the DPROF
    program automatically appends the '.dprof' onto the filename you
    specify.

    1> dcc test.c -o test -prof1
    1> test
    1> dprof test


@($)DPROF V2.06.01  Sep 30 1991         test.dprof

GrandTotal:   539.53 mS

**** BY ROUTINE ****

_main	calls=1      total=  539.53 mS (100.00%) local=   10.37 mS (  1.92%)
_fubar1 calls=101    total=  517.45 mS ( 95.90%) local=  507.75 mS ( 94.10%)
_fubar2 calls=202    total=   20.44 mS (  3.79%) local=   20.44 mS (  3.79%)
_loop	calls=11     total=    0.96 mS (  0.17%) local=    0.96 mS (  0.17%)
	\_______/    \_________________________/ \__________________________/
		       total amount of time	    amount of time spent in the routine
      the number of    spent in the routing	    not including profiled subroutine
      calls made to    including all subroutine     calls it may make.
      the routine      calls.
						    The percentage is relative to
			Percentage is relative to   the grand total run time
			the grand total

**** BY PARENT ****

	total number of calls made to fubar2()
	and total running time, same as from
	the first table
	 ____________________________
	/			     \
_fubar2 calls=202    total=   20.44 mS
    From _fubar1 calls=101    total=	9.69 mS ( 47.43%)
    From _main	 calls=101    total=   10.75 mS ( 52.56%)

    \_____________________/	\________________________/

     number of calls made to	    time spent in fubar2() for calls
     fubar2() from fubar1() and     made from fubar1() and main(), adds
     main() respectively            up to the total on the first line.



_loop	calls=11     total=    0.96 mS
    From _main	 calls=1      total=	0.96 mS (100.00%)
    From _loop	 calls=1      total=	0.04 mS (  4.65%)
    From _loop	 calls=1      total=	0.13 mS ( 13.95%)
    From _loop	 calls=1      total=	0.22 mS ( 23.25%)
    From _loop	 calls=1      total=	0.31 mS ( 32.55%)
    From _loop	 calls=1      total=	0.40 mS ( 41.86%)
    From _loop	 calls=1      total=	0.49 mS ( 51.16%)
    From _loop	 calls=1      total=	0.60 mS ( 62.79%)
    From _loop	 calls=1      total=	0.69 mS ( 72.09%)
    From _loop	 calls=1      total=	0.78 mS ( 81.39%)
    From _loop	 calls=1      total=	0.87 mS ( 90.69%)

**** COMBINED CALL TREE ****


	Top line contains the same information from table 1
       ________________________________________________________
      / 						       \
_main	calls=1     tot=  539.53 (100.00)  loc=   10.37 (  1.92)
    _fubar1 calls=101	tot=  517.45 ( 95.90)  loc=  507.75 ( 94.10)
    _fubar2 calls=101	tot=   10.75 (  1.99)  loc=   10.75 (  1.99)
    _loop   calls=1	tot=	0.96 (  0.17)  loc=    0.08 (  0.01)
     \___________________________________________________________/

	main() calls fubar1() 101 times, fubar1() takes 517 mS total
	time over these calls.	main() calls fubar2() directly 101
	times and fubar2() takes 10 mS over these calls.  Note that
	fubar2()'s time is not the same as in table 1 because only
	those calls made from main() are counted here.

	Percentages are relative to main()



	fubar1() calls fubar2() 101 times.  percentages are relative
	to fubar1()'s total time.  Note that if you add fubar2()'s
	number of calls and total time to the fubar2() entry above
	you will get the grand total for fubar2() shown in the first
	table.

	 _____________________________________________________
	/						      \
_fubar1 calls=101   tot=  517.45 (100.00)  loc=  507.75 ( 98.12)
    _fubar2 calls=101	tot=	9.69 (  1.87)  loc=    9.69 (  1.87)

_fubar2 calls=202   tot=   20.44 (100.00)  loc=   20.44 (100.00)

_loop	calls=11    tot=    0.96 (100.00)  loc=    0.96 (100.00)
    <SELF>  calls=10
    \_____________/

	The profiled data includes the entire call tree but for
	simplicity, recursive calls are simply shown as above.


    You can also request DPROF to print out the entire call tree.  This is
    done by adding the -call option to dprof.  Note, however, that this
    option may result in a huge amount of data printed out.  On the
    otherhand, much of the data is quite useful especially when tracing
    subroutine stacking and other things.

    1> dprof test -call

    .....

**** CALL TREE ****

_main	calls=1     tot=  539.53 (100.00)  loc=   10.37 (  1.92) {
    _fubar1 calls=101	tot=  517.45 ( 95.90)  loc=  507.75 ( 94.10) {
	_fubar2 calls=101   tot=    9.69 (  1.79)  loc=    9.69 (  1.79)
    }
    _fubar2 calls=101	tot=   10.75 (  1.99)  loc=   10.75 (  1.99)
    _loop   calls=1	tot=	0.96 (  0.17)  loc=    0.08 (  0.01) {
	_loop	calls=1     tot=    0.87 (  0.16)  loc=    0.08 (  0.01) {
	    _loop   calls=1	tot=	0.78 (  0.14)  loc=    0.08 (  0.01) {
		_loop	calls=1     tot=    0.69 (  0.12)  loc=    0.08 (  0.01) {
		    _loop   calls=1	tot=	0.60 (  0.11)  loc=    0.11 (  0.02) {
			_loop	calls=1     tot=    0.49 (  0.09)  loc=    0.08 (  0.01) {
			    _loop   calls=1	tot=	0.40 (  0.07)  loc=    0.08 (  0.01) {
				_loop	calls=1     tot=    0.31 (  0.05)  loc=    0.08 (  0.01) {
				    _loop   calls=1	tot=	0.22 (  0.04)  loc=    0.08 (  0.01) {
					_loop	calls=1     tot=    0.13 (  0.02)  loc=    0.08 (  0.01) {
					    _loop   calls=1	tot=	0.04 (  0.00)  loc=    0.04 (  0.00)
					}
				    }
				}
			    }
			}
		    }
		}
	    }
	}
    }
}