lbmake/lbmake						    lbmake/lbmake

				  LBMAKE.DOC

		    SECOND GENERATION LINK LIBRARY MANAGER

    The LBMake utility is similar to LibMake but greatly enhances your
    ability to manage the compiling of link libraries from source code. The
    LBMake utility uses a control file called "lib.def" in the directory
    you run lbmake from.  For a good example of a fully working LBMake
    system refer to the LIB.DEF file in the DCC:LIB/ directory (containing
    the full compilable library source to DICE).

    LBMake understands the basics of compiling source files into objects
    and JOINing objects into libraries as well as how to turn .FD files
    into tag libraries.  LBMake is used to generate all of DICE's
    link libraries and object modules.

    The LBMake control file, "lib.def" determines LBMake's operation in
    conjuction with keywords you give it.  The control file may contain
    lines of the following form:

    @Type   <symbol>	<options>

	The @Type command associates a set of compiler options with a
	symbol.  For example:

	@Type	s	    -ms -r -pr

	You normally have several @Type commands denoting various memory
	models you wish to generate libraries for.  When you run LBMake,
	any keywords you specify on the command line which match symbols
	specified in @Type commands will cause the associated options to
	be used when compiling source files.  By specifying several keywords
	on the LBMake command line you can merge options for several
	memory model combinations.

	The @Type symbols are merged together to create a single symbol
	which can be used to modify the name of the generated library
	or object module.

    @Objects <symbol> <filepath>

	The @Objects command defines a symbolic name which will later be
	used to reference individual files that are to be compiled into
	individual object modules.  The <filepath> contains the filename
	template that is to be used to name the object files after
	compilation, where %s denotes the name of the object module.
	For example:

	@Objects startup    dlib:%s

	If, later on, the 'startup' symbol is associated with the files
	fubar/a.c, fubar/b.c, and fubar/c.c LBMake will, when asked to
	compile 'startup', generate the object modules dlib:a.o, dlib:b.o,
	and dlib:c.o from their source files.

	You may specify multiple @Objects commands but should specify at
	most one @Objects reference at a time on the LBMake command line,
	as in the example above.

    @Library <symbol> <filepath>

	The @Library commands is similar to the @Objects command but
	indicates that all files referenced by <symbol> are to be
	JOIN'd together into a single result.  For example:

	@Library    clib    dlib:c%s.lib

	The filename template in this case reflects any @Type commands
	which you have activated via the LBMake command line.  For
	example, if you ran the following LBMake:

	1> LBMake s r clib

	LBMake would commence to compile objects associated with the 'clib'
	symbol, JOIN them together, and name the result 'dlib:csr.lib'.

	You may specify multiple @Library commands but should specify at
	most one @Library reference at a time on the LBMake command line,
	as in the example above.

    @DefTree	<filepath>

	The @DefTree command defines the default DIRECTORY where
	intermediate files are to be stored.  The name of the directory
	can depend on the @Type commands which have been activated
	thereby giving you separate directories for separate memory
	models.

	@DefTree    dtmp:comp3/lib_%s/

	So, for example, if you were to 'LBMake s r clib' LBMake would put
	the associated object modules in 'dtmp:comp3/lib_sr/'.

    @AltTree	<symbol>    <filepath>

	The @AltTree command works like @DefTree but allows you to specify
	a symbol on the LBMake command line which overides the @DefTree.

	@AltTree    pass2   dtmp:comp2/lib_%s/

	You may specify multiple @AltTree commands but should specify at
	most one on the LBMake command line.  This feature is most useful
	in a production system to generate 'experimental' versions of a
	library until one is ready for the next release, then generate a
	'master' version.

			    SPECIFYING FILES

    The remainder of the "lib.def" control file contains file
    specifications.. i.e. a list of files and which libraries they
    apply to.  A file can apply to more then one library.  The general
    format for the file list is:

    <filename>		    +/-<symbol> +/-<symbol> +/-<symbol> ...

    Each file is followed by one or more symbols.  For example:

    amiga/profile.c	+clib +uclib +free -pass2

    Would indicate that the amiga/profile.c module is associated with the
    library defined by the symbol 'clib', the library defined by the symbol
    'uclib', and the library defined by the symbol 'free' (i.e. these three
    symbols are part of @Library commands).  However, the file does not
    exist in any of these libraries of the 'pass2' symbol is specified on
    the Command line, where 'pass2' also refers to an @AltTree command.

    The basic idea is that you list every file for every library in a
    particular project, just as I have done in my "lib.def" file for DICE,
    then use LBMake to generate the actual .lib and .o files.

    LBMake will create a duplicate directory structure in the object tree
    as specified by @DefTree (or an active @AltTree).  It appends the
    FULL PATH of the source file to the destination tree so, for example,
    if you were to:

    1> LBMake s r clib

    The LBMake would compile 'amiga/profile.c' into
    'dtmp:comp3/lib_sr/amiga/profile.o'

    Therefore, you may not specify any absolute file paths in order for
    LBMake to work properly.


				.FD FILES

    LBMake supports the generation of tag libraries from .FD files.  It
    recognizes a .FD file by the .FD extension in the file specification.
    In order to properly support .FD files LBMake requires that the
    file specification be of the following form:

	[directory_path]filename_lib.fd     +/-<symbol> +/-<symbol> ...

    Why the brackets?  Well, remember what I said about not being able to
    use absolute filepaths because they screw up the placement of object
    modules in the object tree?  Brackets provide a solution to this
    problem when you have no choice but to use absolute file paths. The
    part of the path in brackets will be IGNORED when it comes to figuring
    out what the object file name should be.  This is especially important
    for .FD files which are generally put elsewhere.

    To further automate operation LBMake looks for the prototype file
    associated with the .FD file using the same path but munging the
    '_lib.fd' part to '_protos.h' and munging '/fd/' or ':fd/' into
    '/clib/' or ':clib/'.  In otherwords, it munges something like:

	[dinclude:amiga20/fd/]mathieeesingbas_lib.fd	 into
	[dinclude:amiga20/clib/]mathieeesingbas_protos.h

			    AUTOINIT CODE INCLUSION

    For autoinit code inclusion one needs to specify the actual
    name of the library, e.g. 'fubar.library', along with each .FD file
    name using the following format:

	[directory_path]filename_lib.fd,libraryname	+/-<symbol> +/-<symbol> ...

    For example:

	h/fd/myfubar_lib.fd,fubar.library   +mylib