romable/romable 					      romable/romable

			      ROMABLE.DOC

		       GENERATING ROMABLE FIRMWARE

			      REFERENCES

    Please refer to the following DCC options:

	-pi	generate position independant code.  All code references
		forced to PC-relative

	-pr	generate residentable position independant code.  Unless
		-mw is specified A4 relative addressing is used for data
		items.	All code references forced  to PC-relative.

	-ma	specify that initialized data + bss will be hardwired to
		a known address

	-mw	specify that initialized data + bss will be hardwired to
		a known address and all of data + bss occurs somewhere
		within the first 32KBytes of the address space
		(0x0000-0x7FFF).  Also allows DICE to use A4 as a register
		variable.

	-ms	const items go into EPROM in local cases

	-mS	const items go into EPROM in local and external cases

    The following documentation may appear confusing, but only because so
    many possibilities exist when one intends to put code in ROM.  When you
    are in doubt, it is usually a good idea to write a small test source
    file, compile it, link it with symbols, and then look at the resulting
    executable with DOBJ.


			  MAKING ROMABLE PROGRAMS

    DICE has the capability to generate ROMABLE programs.  That is, program
    binaries that you can use to directly burn an EPROM.  When generating
    ROMABLE code you have more data model options available to you.  The
    basic idea of ROMd code is as follows:
		       ________________
FIXED ADDRESS = EPROM | 	       |
		      | 68000 vectors  |	const data objects
		      |----------------|
		      |     CODE       |
		      |----------------|
		      |  const DATA    |	string constants and other
		      | 	       |	const items, stays in eprom.
		      |----------------|
		      | read-only copy |
		      | of initialized |	this is copied to a working
		      | data	       |	RAM copy by the reset code
		      |________________|

		       ________________
FIXED ADDRESS = RAM   | run-time copy  |    (copied from EPROM by startup)
		      | of initialized |
		      | data	       |
		      |----------------|    (cleared by EPROM startup)
		      | run-time BSS   |
		      |________________|


    From the above you have two basic choices in terms of where your
    RUN-TIME DATA is based.  If your RAM exists in low-memory
    (0x0000-0x7FFF) you may choose to compile your code to use the
    ABSOLUTE-WORD addressing mode.  This modes takes the same space as the
    A4-RELATIVE addressing mode yet does not require use of the A4 register
    and, in fact, the A4 register will then be available for use as a
    register variable.

    If you have minimal RAM in low-memory or your DATA+BSS is larger than
    32KBytes (yes, that's 32KBytes people, not 64KBytes), then you will
    have to choose either the formal large-data model or the A4-relative
    small data model.  If you initialized data is over 64KBytes you can
    still use the small-data model for most objects by using the __far
    keyword judiciously.

    NOTE: in all cases you can allocate or generate points for any ram
    location, this just refers to accesses of declared variables!  Pointers
    are always 32 bits.

	model		options 	advantages	      disadvantages

    absolute-word	-mw	-ms	no need for A4	      low 32KBytes only
					A4 available as
					reg variable

    small-data		-ma	-ms	RAM can be anywhere   requires A4
							      must use __geta4

    large-data		-ma -mD -ms	RAM can be anywhere   code is larger
							      libs must all be
							      large-data


				CODE MODEL

    The CODE MODEL is normally left at PC-relative and should not present a
    problem.

				CONST DATA

    You want to use the -ms option or even the -mS option (see DCC.DOC for
    the differences).  This will place all string constants in EPROM and
    IN THE CODE SEGMENT, thus this initialized data will NOT take up space
    in RAM.  Any 'const' initialized data will be placed in the code segment
    and thus in EPROM.	Any non-const initialized data will be copied from
    EPROM into RAM by your reset-startup code.

    Any tables that you declare that you will never modify should be
    declared const so they reside in EPROM and do not take up space in RAM.
    On the otherhand, if your EPROM is running 6 wait states and your RAM
    is running 0 you might consider not using 'const'.... assuming you have
    a lot of RAM.

    When your code is less than 32KBytes big you can use -pi or -pr and
    should definitely use -mS.	When your code is larger than 32KBytes you
    cannot use -mS unless you are absolutely positive pc-relative const
    data references do not exceed the word-relative range.

			  RESET VECTOR, DATA MODEL SETUP

    If your EPROM is mapped into low memory on boot you can declare a vector
    table by declaring a CONST LONG array as the first data object in the
    first object module that you link to create the executable:

	const long ROMVectorTable[] = {
	    InitialSSP,
	    ResetVector,
	      .
	      .
	      .
	};

    Remember, this must be the first data declaration in the first object
    module!!!  If you are using the A4-RELATIVE small-data model you must
    qualify your ResetVector with the __geta4 type qualifier to set up A4.

    In most cases you will want ResetVector to point to some assembly which
    initializes your RAM DATA & BSS before calling C code.  The assembly
    normally looks like this (this would be the second object in the link):

		;   RESET exception, copy initialized data to RAM and clear
		;   BSS area before calling rom_main()
		;
		;   Assumes less than 256KBytes of data and 256KBytes of BSS

		xref	__DATA_BAS	    ; linker generated symbols
		xref	__ABSOLUTE_BAS
		xref	__DATA_LEN
		xref	__BSS_LEN
		xref	_rom_main

_ResetVector
		lea	__DATA_BAS,A0	    ; ROM data
		lea	__ABSOLUTE_BAS,A1   ; RAM data
		move.w	#__DATA_LEN,D0	    ; long words of data
		bra	trentry
trloop		move.l	(A0)+,(A1)+         ; copy EPROM copy to run-time
trentry 	dbf	D0,trloop	    ; RAM copy.

		move.w	#__BSS_LEN,D0	    ; long words of BSS (follows data)
		moveq.l #0,D1
		bra	trbentry
trbloop 	move.l	D1,(A1)+            ; clear run-time RAM
trbentry	dbf	D0,trbloop

		jmp	_rom_main(pc)

    Where rom_main() is your C main routine qualified with __geta4 (if you
    are using the A4-RELATIVE data model).  Any special items, such as
    the EPROM getting mapped at reset, must be dealt with as well, usually
    before the reset code sets up the run-time enviroment.

    If you are using the ABSOLUTE-WORD data model DO NOT USE __GETA4!
    Specifically, the -mw option TELLS DICE THAT A4 IS FREE FOR USE AS A
    NORMAL REGISTER VARIABLE.  This gives you an extra register variable if
    you haven't guessed!

			       EXAMPLE PROGRAM

    Assume the above assembly module has been assembled and is called
    'romc.o'.  The following C program is called 'test.c'.  In all cases
    the code may start anywhere.

    Also, in all cases note that ROMC.O is specified AFTER test in the
    DCC line (that also serves as the link line).  This is because for
    a standalone product we want our CONST data object that is the
    ROM VECTOR TABLE to be first.  Of course, if you put the ROM VECTOR
    TABLE in ROMC.A instead of TEST.C then ROMC.A would go first.  To
    put the ROM VECTOR TABLE in ROMC.A it should be the first data
    object declarations (dc.l's) in the CODE segment.


    (1) SMALL-DATA-MODEL

	extern void TrapReset();
	extern char SSp[512];

	const long RomVectors[] = { (long)SSp, (long)TrapReset };

	char SSp[512];	    /*	our supervisor stack in BSS */

	__geta4 void
	rom_main()
	{
	    short i;

	    for (;;) {
		for (i = 0; i < 10000; ++i) {
		    <do something here with  i>
		}
	    }
	}
				    note, ram can be beyond 64K
				    v

	COMPILE:    dcc test.c romc.o -ma 0x10000 -o t:test -r -v -lrom
		    romable t:test -o t:test.bin -D 0x10000 -C 0x0
		    burn eprom using test.bin


    (2) ABSOLUTE WORD DATA MODEL

	The source code is the same except you do not need __geta4.  Here
	I am assuming RAM starts at, say, 0x2000.

	void
	rom_main()
	{
	    ...
	}

	COMPILE:    dcc test.c romc.o -mw 0x2000 -o t:test -r -lrom
		    romable t:test -o t:test.bin -D 0x2000 -C 0x0
		    burn eprom using test.bin

    (3) ABSOLUTE LONG DATA MODEL

	The source code is the same as for (2).  Here the RAM may start
	anywhere (also true in (1)).

	COMPILE:    dcc test.c romc.o -ma 0x10080 -o t:test -r -lrom
		    romable t:test -o t:test.bin -D 0x10080 -C 0
		    burn eprom using test.bin

    (4) EXAMPLE OF EPROM INITIALLY MAPPED AT 0x0000 BUT REMAPPABLE TO
	SOMEWHERE ELSE

	In this case the assembly, ROMC.A, must relocate the EPROM back
	to where it should be before initializing the data segment.  Here
	your initial CONST data is the EPROM VECTOR TABLE, and your initial
	non-CONST INITIALIZED data (because BSS gets stuck after all
	initialized data) will be your RAM VECTOR TABLE.

	In this example I assume that RAM will be mapped into 0x0000-
	by the time rom_main() gets called.  Compilation depends on the
	data model.  The example below uses the ABSOLUTE WORD data model.

	extern void TrapReset();
	extern char SSp[512];

	const long RomVectors[] = { (long)SSp, (long)TrapReset };
	long RamVectors[] = { (long)SSp, (long)TrapReset, ... };

	char SSp[512];	    /*	our supervisor stack in BSS */

	void
	rom_main()
	{
	    ...
	}

	In this compilation example I am assuming the RAM will be at 0x0000 and
	the ROM, say, at 0x20000 (above the 64KBmark)

	COMPILE:    dcc test.c romc.o -mw 0 -o t:test -r -lrom
		    romable t:test -o t:test.bin -D 0 -C 0x20000
		    burn eprom using test.bin

				USING ROM.LIB

    ROM.LIB is generated from LIB/FILES.ROM3LIB and contains those modules
    from C.LIB that do not declare any variables and are position
    independant.  Modules in the library are entirely position independant.
    If you use library calls instead of macros in <ctype.h> for ctype
    functions those are position independant as well ... they use
    pc-relative to access the lookup tables (which are declared const).

    Nothing in ROM.LIB declares any data variables.  The idea is to link
    your code with ROM.LIB instead of C.LIB to ensure that incompatible
    routines are never included by mistake.

    Warning: If you want position independant code you must compile with
    -pi or -mS, especially when accessing <ctype.h> macros.  Accessing
    <ctype.h> macros and not using either the above options will result in
    absolute-code references to ctype's lookup tables.

    ------------------------------------------------------------------------
				MAKING RAM MODULES

    Generating a binary image for an executable that is meant to run from
    RAM instead EPROM is relatively easy.  In many cases you want only a
    single copy of the data (instead of two copies as in EPROM modules..
    the permanent initialized data in EPROM and the run-time data+bss in
    RAM).  This means that the program is not-reentrant... once an
    initialized data variable is modified it stays modified.  If this is
    not desireable you can use the same methods as were described for
    making EPROM code combined with methods (see LIB/AMIGA/C_PR.A) to
    allocate the data space run-time.

    If you want to generate resident style modules use the small-data model
    version in the previous section 'MAKING ROMABLE PROGRAMS' and simply
    apply the concept of downloading such a module into RAM instead of ROM.
    It is especially easy when the code is completely position independant
    because your firmware does not have to deal with relocation at all.

    This section describes standalone modules with UNsharable code because
    the code is completely position independant and references only one set
    of data.

		       ________________
 ANY ADDRESS IN RAM   |startup	       |
		      |     CODE       |
		      |----------------|
		      | initialized    |
		      |    data        |
		      |----------------|
		      | 	       |
		      |     BSS        |
		      |----------------|

    The code uses a single PC-relative reference to find the start of the
    data, then generates the A4 register to point to the data section.
    NOT A SINGLE 32-BIT REFERENCE EXISTS.

    WARNING:	The module has only one set of data.  Once initialized data
    is modified it stays modified through multiple invocations of the module

    The advantage of using a position independant module is obvious... you
    can copy it to any point in ram as-is and then call it!  For small
    68000 boxes with limited memory this is definite plus as it greatly
    simplifies the loading mechanism.

    To create a 100% relocatable module, the code must be less than 32K
    and the data less than 64K.  You must use the -pi option when compiling
    all source modules, when running dlink, and when running ROMABLE.

    The -pi option, amoung other things, puts the __ABSOLUTE_BAS and
    __DATA_BAS linker symbols in the code section.  Actually, dlink puts
    the entire program into a single CODE hunk!

	dcc -c test.c -pi
	dlink -pi rampi.o test.o -lrom -o test
	romable test -o test.bin -pi

    RAMPI.A is something you have to write, but you do have a template.
    Take a look at LIB/AMIGA/C_PI.A as an example (also note that
    LIB/AMIGA/X.A is also required).  Remember that the autoinit sections
    must be entirely supported though not necessarily the autoexit sections,
    it depends on your application.

				USING ROM.LIB

    ROM.LIB is generates from LIB/FILES.ROM3LIB and contains compiler
    support routines that do not require any RAM.  Modules in the library
    are entirely position independant.	If you use library calls instead
    of macros in <ctype.h> for ctype functions those are position
    independant as well ... they use pc-relative to access the lookup
    tables (which are declared const).

    Nothing in ROM.LIB declares any data variables.  The idea is to link
    your code with ROM.LIB instead of C.LIB to ensure that incompatible
    routines are never included (instead you get an undefined symbol error
    from the linker when you make a mistake).

    Warning: If you want position independant code you must compile with
    -pi or -mS, especially when accessing <ctype.h> macros.



    ------------------------------------------------------------------------

    ROMABLE exeFile -o outFile [-o outFile2] -C addr -D addr -pi

    addr:   decimal, 0octal, or 0xHEX

    Romable generates a binary image for an executable compiled under DICE
    and is normally used to generate a ROMABLE raw binary output file.

	exeFile 	input executable linked with dlink

	-o outFile	output binary (unformatted -- raw).  If TWO -o options
			are specified the two output files will have even bytes
			and odd bytes respectively, which is what you need when
			you must program two eproms (one on the LSB data lines
			and one on the MSB data lines)

	    example: -o out1		result: 01 02 03 04

	    example: -o out1 -o out2	result (out1):  01 03
					result (out2):  02 04


	-C addr 	code start address, 0octal, decimal, or 0xHEX

	-D addr 	data start address, 0octal, decimal, or 0xHEX

	-DC		place actual data+bss just after code (i.e. the
			result is intended to be downloaded into RAM, there
			is no duplicate data in this case).

			'-D addr' is not specified in this case

	-pi		generate a position independant module.  Neither
			-C or -D are specified in this case, and ROMABLE
			will warn you have any absolute references.

    Note that your custom startup code determines how much of __autoinit
    and __autoexit is to be supported.	Note especially that __autoinit0
    MUST BE SUPPORTED because DICE will generate __autoinit0 sections to
    handle 32 bit data relocations run-time.

    ROMABLE generates a raw output file or files with the EPROM code first,
    and initialized data after the main code (still in EPROM) which, as
    has already been described, will be copied to RAM on reset by your
    startup routine.

    This startup-copying of initialized data and clearing of BSS makes it
    extremely easy to use DICE to generate ROMED applications without
    having to deal with major porting considerations.