K4Ed Professional


                              Demo-Version 2.99 



           Copyright (C) 1992 by Martin Stengle and Bernd Jessel




      The K4Ed_Professional is a Sharewareproduct which was designed 
       to edit and transfer sounddatas of the Kawai_K4-Synthesizer.


 -------------------------------------------------------------------------
 NOTICE:  

 K4Ed_Professional_V2.99 is copyrighted by Martin Stengle and Bernd Jessel.
 It may not be freely distributed. In no event will the author be liable 
 for direct or indirect damage or loss resulting from the use of this program.
 -------------------------------------------------------------------------
 The midi.library is Copyright (C) 1987, 1988, Pregnant Badger Music.
 All rights reserved.
 Req.library is Copyright ©1989, 1990 by C.W. Fox and Bruce Dawson.  
 The library is FreeWare.
 ------------------------------------------------------------------------

REQUIREMENTS «««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««

To use K4Ed_Professional you need the midi.library and the req.library.
(further you need the diskfont.library, serial.device and printer.device)
The receive- and the transmit-channel of your K4 must be set to 1.
Further set "Receive_program = Norm" and "Receive_exclusive = On".
Required stacksize is 50000. If you start K4Ed_Professional from Workbench
the stack will be set automatically to 50000 (from the .info-file).


INTRODUCTION «««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««

K4Ed_Professional is a very comfortable soundeditor for the Kawai_K4-
Sythesizer which makes it easy for you to edit the numerous parameters
of Singles, Multis, Effects and Drums.

There are a lot of powerful funktions included in K4Ed_Professional, e.g.:

Editing of the parameters can be done by mouse (drag-and-move) or by keys.
All changes will be send immediatly (autosend) to the K4 if desired.

If you want to hear and test your sound-creations you can simply use your
Amiga-keyboard (with 2.5 octaves) to play notes. Its also possible to
transpose the octaves (from C-1 to G#-6) and to change the velocity and
midichannel.

Another feature is the multipleload_funktion. This is very helpful if
you want to load a lot of Singles or Multis which are not stored in a
bank. You can load up to 64 Singles or Multis at once or if you choose
less you can insert them in a already filled bank.

The environment of the program (colors, font, pathnames, etc...) is 
easy to set and can be stored.


DESCIPTION of the functions ««««««««««««««««««««««««««««««««««««««««««««««««

»» GADGETS «««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««

 » Load  : load sounddatas from any (disk-)device.
           (factory settings of the K4 are included in the dumps directory)

 » Save  : save sounddatas to any (disk-)device.

 » Get   : receive data from K4
           (the gadgets on the bottom determins the type of data)

 » Put   : transmit data to K4
           (the gadgets on the bottom determins the type of data)

 » Edit  : if you are in single, multi, effect or drum mode you can edit 
           all parameters after selecting this gadget.
           to leave the Edit-mode press this gadget again.
           (for further explanations look HOW TO EDIT)

 » Swap  : to swap two singles, multis or effects with each other

 » Quit  : to exit the program

 » All   : |
 » Block : |
 » Single:  \   These gadgets determins the type of data which is displayed.
 » Multi :  /   If the selected buffer is empty the K4 logo is shown.
 » Drum  : |
 » Effect: |


 » Intern/Extern: to switch between the internal memory and an external card
                  please don't try to receive data from a card you dont have


»» MENU »»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»»

 » PROJECT «

 - About
   some copyright notices and other informations

 - Registration
   to print out a registration formular

 - Clear
   to clear the actual buffer or all buffers

 - Open
   to load sounddatas from any (disk-)device 

 - Multiple Load
   to load from one to 64 singles or multis at once
   (a requester will appear asking you which datas you want to load
   and for a position to insert them. Use the gadgets to enter a position.
   "Start" means A-01 and "current" is the position of the last selected
   Single or Multi. To continue select "OK". Now you are requested to
   select the directory containing the Singles or Multis. The requester is
   pre-setup to the directory in the environment for Singles or Multis.
   After this all Singles or Multis of this directory are displayed.
   Make your selection with the mouse and select "OK" when ready.

 - Save
   to save sounddatas to any (disk-)device, the program uses the path and 
   filenames of the environment

 - Save as
   to name and save sounddatas to any (disk-)device 

 - Print
   to print out the data actually displayed

 - Save & Quit
   to save all buffers and exit the program

 - Quit
   to exit the program


 » ENVIRONMENT «

 - Autosend
   if enabled, the editbuffer of K4 will be updated after each parameter
   change caused by mouse. If arrow-keys are used for editing the spacebar 
   must be pressed to update the editbuffer.
   if disabled, the editbuffer of K4 will not be updated.

 - Colours
   Adjust : to adjust colours
   Default: to select the default colours

 - Enable Get/Put
   to enable or disable the Get/Put option

 - Pathnames
   a large requester will appear in which you can enter a specified 
   directory and filename for loading/saving of each different buffer

 - Select Font
   Diskfont: to select a specified font from disk
             proportional fonts and fontsizes < 9 are supported
   Topaz 80: to select the Amiga ROM font (for a faster textoutput)

 - Interlace
   to switch between non-interlace and interlace resolution

 - Load environment
   Default : to load the default preferences
             the program will try to load the file k4editor.setup
             from the s: directory. If the file is not available
             the internal defaults are used.
   Specify : to load a specified preferences
                            
 - Save environment
   to save a specified preferences


 » RECEIVE «

  With these items you can receive all kinds of dumps from K4.
  (same funktions as get-gadget)


 » TRANSMIT « 

  With these items you can transmit all kinds of dumps to K4.
  (same funktions as put-gadget)


 » EDIT «

  With these items you can jump into the editor for a single, multi,
  effect or drum. 


 » SPECIAL «

 - Swap
   Swap two data dumps in respect of the actual block-mode

 - Copy  
   Copy one data dump to another position

 - Switch Int/Ext
   to switch between the internal memory and an external card,
   the actual mode is shown on the gadget on the right bottom.
   intern: all transmissions will be send to/from intern K4 memory.
   extern: all transmissions will be send to/from an extern memory card.

 - Split
   split all_data dump into
                          block_single data dump,
                          block_multi data dump,
                          block_effect data dump,
                          drum data dump.
   If you load or receive an All-dump and you want to work on the Singles,
   Multis, Effects or Drums, you have to split the All-dump first into
   its components. The All-dump is still stored in memory after this and
   is not changed until you use "unsplit" to copy back the several dumps
   to the all_buffer.

 - Unsplit
   opposit of the Split function. Ask what buffers you want to copy back
   to the all_buffer.
   If you want to save or transmit an All-dump containing the changed
   datas, you have to unsplit the All-dump. This funktion collects
   the several dumps into the All-dump.



HOW TO EDIT ««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««

The first thing to do is to receive a data dump from your K4 or to load 
one from disk. If you filled your all_buffer and you would like to edit
any sound data you first have to split the all_buffer into its components.
For this select Split in the menu. After this you should click on 
Single, Multi, Effect or Drum. You will enter now the selected block_buffer.
There you can pick a data dump by clicking on its name. Make shure that 
Autosend in the environment-menu is enabled.
Now select the Edit-Gadget. You have entered the Edit-mode in this moment.
Use the mouse to select and change the parameters.
While changing keep left mousebutton pressed and move the mouse.
Moving the mouse to the top or right margin increases the value of the 
parameter. Moving the mouse to the bottom or left margin decreases the 
value of the parameter. After releasing the left mousebutton the
editbuffer of the K4 will be updated.
If you use the cursor keys to select and change the parameters, the 
spacebar must be pressed to update the editbuffer of K4.

If you want to hear your new sound press any key (see Keys setting)
to play a melody, rhythm, drumpattern or something you like.

I think you will understand the system of editing very soon.
As long as you are in the Edit-mode you can`t select a menu or gadget.
To end the Edit-mode select the Edit-Gadget. Your new data will be copied
immediately to the block_buffer. Use Unsplit in the menu to copy the data
in the all_buffer.


KEYS SETTING «««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««

These keys are only working in the Edit-mode:

left/right arrow : to walk through the parameters

up/down arrow    : to increase/decrease the value of a parameter

spacebar         : to update the editbuffer of the K4
                   make shure that the autosendflag in the menu is set!

A-Z, 1-0         : to play notes from the Amiga-keyboard 

                                    2 3   5 6 7   9 0   ` \
                   higher octave:  q w e r t z u i o p ü +

                                    a s   f g h   k l   ä
                   lower octave :  < y x c v b n m , . -

Del              : to delete midi-drones from a specific channel
                   sometimes it occures that a note didn`t get his note-off
                   message (i.e. if you press keys from the keypad while
                   playing notes). The Del-Key sends a All-Notes-Off-message
                   to the actual channel.

THE KEYPAD:
1-2-3     : to transpose the notes from Amiga-keyboard press 
            "1" to decrease by one octave
            "2" to choose the default value (=2)
            "3" to increase by one octave
                the value 1 means that the lower octave starts by C1,
                the value 2 means that the lower octave starts by C2, etc...

4-5-6     : to increase/decrease the channel of the notes
            in single-edit you should take channel 1,
            in drum-edit you should take channel 10,
            in multi-edit you can make your choice.
            "4" to decrease by one channel
            "5" to choose the default value 
                (single-multi-and effect-edit=1, drum-edit=10)
            "6" to increase by one channel

7-8-9     : to increase/decrease the velocity of the notes.
            Its a kind of volume control; a high value stands for loud
            a low value stands for soft.
            "7" to decrease velocity by 10
            "8" to choose the default value (=50)
            "9" to increase velocity by 10


RESTRICTION ««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««

In this demoversion the Save- and Transmit-option is disabled and 
autosend is only available in Multis and Drums.
 

REGISTRATION «««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««

If you want to support this project and become a registered user please send 
your contribution of $30.- or DM40.-(prefered) (cash or Check) to one of the 
addresses below and you will get the latest full-working version of 
K4Ed Professional.


      Martin Stengle                     Bernd Jessel                   
      Kaspar-Kerll-Str.37                Schleissheimerstr.229b          
      8000 Muenchen 60                   8000 Muenchen 40               
      Germany                            Germany                        


««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««««