TXZM -- ZMODEM PROTOCOL DRIVER

               (c) 1991-94 Mike Dumdei, 6 Holly Lane, Texarkana Texas
                        North East Texas DataLink  1:3819/128
                        BBS (903)838-6713, Voice (903)838-8307

              TXZM (Texas Zmodem :) is a zmodem protocol that was
          developed to demonstrate the speed and capabilities of the
          MCOMM C serial communications library.  The latest version of
          TXZM or MCOMM may be obtained from N.E.T. DataLink by either
          logging in and downloading or by file request of "MCOMM" or
          "TXZM".  The shareware version of MCOMM contains the TXZM
          shell in source form and the low level Zmodem driver in
          library form.  The complete source code comes with the "Libs &
          Source" registered version of MCOMM.  Libraries for all memory
          models except for the BCC/TC huge model come with the "Libs
          Only" registered version of MCOMM. See the MCOMM order form
          for specifics on various options.

                                  TXZM RESTRICTIONS

              TXZM IS NOT PUBLIC DOMAIN however the executable version
          may be distributed and used free of charge for non-commercial
          purposes.  If you intend to use TXZM commercially or in a com-
          mercial environment and the program will be loaded or operated
          on more than 3 systems ANYWHERE within the organization, you
          must obtain a license.

              The complete TXZM source code is provided as part of the
          "Libs & Source" registered version of the MCOMM software
          package. Linkable libraries are provided with the "Libs Only"
          registered version of MCOMM.  None of the source code or
          libraries that are part of the registered version of MCOMM may
          be distributed, neither may they be incorporated in whole or
          in part into a competing software product without a written
          license agreement. Competing software products are products
          that are not end user programs themselves, such as "Your
          Serial Library", and products that directly compete with TXZM
          (fully developed terminal programs, BBS systems, and similar
          products are FUNCTIONALLY DIFFERENT than TXZM and NOT
          considered competing products).

              The license agreement requirement for commercial use of
          the EXECUTABLE VERSION ONLY (TXZM.EXE) does not apply to
          governmental, educational, church, civic, or non-profit
          organizations.  This does not waive restrictions that apply to
          the source code for those organizations.



                         MCOMM ASYNC LIBRARY (Advertisement)

              MCOMM is a serial communications library for Microsoft C,
          Turbo C/C++, Borland C/C++, and Zortech C/C++.  It also will
          work with any other C compiler or language that supports
          Microsoft C calling conventions.  Some of the features of
          MCOMM are:

               -  Fully interrupt driven
               -  16550 FIFO mode support
               -  Baud rates up to 115200 baud
               -  Supports definitions for any comm port that operates on
                  IRQs 2 through 15 at any address
               -  Supports simultaneous operation of 4 ports
               -  Written in assembler for maximum speed and minimum code
                  size
               -  Advanced features such as block transmit and receive,
                  XON/XOFF and hardware flow control, receive buffer look
                  ahead, definable ring buffer sizes and location, ...

                Also included with MCOMM is a set of ANSI capable video
          functions that support windowed output, save/restore screen
          functions, timer functions, and miscellaneous other code.  The
          current shareware version of MCOMM is MCOMM600.ZIP.  It
          includes a complete small model LIB, TXZM (partial source,
          rest as libs), and both a C and C++ demo terminal program.
          The registered version is available as either "Libs only" or
          "Libs & Source". The "Libs Only" version is $25 and includes
          libraries for all memory models. The "Libs & Source" version
          is $45 and comes with both libraries and all source code.  See
          the MCOMM order form.


                                    TXZM OPERATION

              TXZM has 3 modes of operation.  These are command line
          send, command line receive, and terminal mode.  Running TXZM
          with no command line parameters will list available TXZM
          options.

          Specifying the serial port:

              TXZM directly supports COM1 through COM4, however COM3 and
          COM4 on older hardware may not match what is considered
          standard.  The -c switch (described below) may be used for
          non-standard configurations of COM3 and COM4 or to force TXZM
          to recognize a custom port.  For standard versions of COM1-4,
          use "txzm com#" where '#' is 1-4.

          TXZM switches:

              -u  Start in terminal mode.  Terminal mode may be started
                  either before or after a CONNECT is made.  It has a
                  limited set of functions (dial, upload, download).

              -r  Start in receive mode.  This switch must come last on
                  the command line if it is used.  It may be followed by
                  an optional subdirectory if the files are to down-
                  loaded to a specific location.  The -r switch may be
                  used in conjunction with the -u switch to specify a
                  download directory.  When used with the -u switch,
                  TXZM starts in mini-terminal mode.

              -s  Start up in send mode.  This must be the last switch
                  on the command line and be followed by the filename(s)
                  to be sent. The filename list may contain wild cards.
                  The send function will recurs subdirectories if the
                  filename specifications are placed in parenthesis.
                  Placing filenames in parenthesis to recurs
                  subdirectories also works in mini-terminal mode.

              -p  Send or accept complete pathnames.  This option, used
                  in conjunction with the -r option, will cause TXZM to
                  accept complete pathname information in the received
                  filename. Without it, only the root name and extension
                  of the filename are used.  If the received filename
                  specifies a directory that does not exist, it will be
                  created.  If a download directory was specified (-r
                  dlpath), the subdirectories will be created under
                  "dlpath".

                  When used with the -s switch, the -p switch will cause
                  filenames to be sent with complete path information.
                  Per zmodem specifications, only the path is sent (no
                  drive identifiers).  Without the -p switch only the
                  file's root name and extension are sent.  This applies
                  even if recursing subdirectories.


              -b####   Specify the CONNECT baud rate.  The CONNECT baud
                  rate is used to determine estimated file transfer
                  times. TXZM currently will not adjust to a CONNECT
                  rate when initially making the connection.  Unless a
                  locked baud rate is used (-l), you must dial using the
                  baud rate you will CONNECT at.  If the connection is
                  already established, and neither -l or -b is given,
                  TXZM will open the port using the baud rate it is
                  currently operating at.

              -l####   Set a locked baud rate.  Use this option to set a
                  fixed computer to modem baud rate. The -b option may
                  be used with the -l option to specify both the
                  computer to modem rate and the modem to line rate.

              -chhh,#  Specify a non-standard port configuration.  TXZM
                  will work with any port addresfrom 000h to 3f8h and
                  IRQs 2-15.  Replace 'hhh' with the port address in hex
                  and '#'ith the IRQ to be used.  For example, to use a
                  port at I/O address 2E8h that uses IRQ 5, use "txzm
                  -c2E8,5".

              -h  Use hardware flow control (RTS/CTS).  This is required
                  for modems that use a locked baud rate.

              -i  Ignore absence of carrier detect signal.  Use this
                  switch when using TXZM to transfer  files between
                  systems connected with a null modem cable. (TXZM only
                  requires the Rx, Tx, and Gnd wires to be connected).

              -v  Disable serial I/O  during disk writes.  Use this
                  option if errors occur when the received data is
                  written to disk.  This should only be necessary when
                  operating at high baud rates with no 16550 UART or the
                  file is being downloaded to a floppy.  The -v option
                  also expands the disk buffer to 20K bytes to maintain
                  a higher level of efficiency.

              -e# Set duplicate file handling option.  This option
                  determines what happens if an attempt is made to
                  download a file that already exists.  The following
                  choices are available:
                    -e0  Skip the file -- do not download.
                    -e1  Resume the transfer at the end of current file.
                         This is the default.
                    -e2  Create a duplicate file name and download the
                         file as a separate file.
                    -e3  Overwrite the existing file.

              -w####  Sets the maximum bytes that may be in transit at
                  any one time (transmit window size).  This must be a
                  multiple of 128.

              -x  Escape all control characters.  This option causes the
                  characters between 00h and 20h, 80h and A0h, 7Fh, &
                  FFh to be ZDLE escaped. Zmodem automatically escapes
                  XON, XOFF, ZDLE (CAN), DLE, and "<CR>@<CR>" sequences.
                  The -x option is for networks that do not pass other
                  control characters.


              -x# As an option, a specific list of control characters to
                  escape may be given.  For example to only ZDLE escape
                  the ESC character (27 decimal or 1B hex) and
                  ESC+parity (145 decimal or 9B hex) and let all other
                  control characters pass unaltered, use:  -x27,145.

              -6  Force use of 16 bit CRC.  The default is 32 bit CRC.
                  This option does not show up on the help screen (ran
                  out of room).

              -7  Strip high bit from received characters in terminal
                  mode.

              -0  Use BIOS screen writes.  This only works in command
                  line mode.  Mini-terminal still does direct writes.

              -q  Run in DesqView mode.  This option makes TXZM DesqView
                  aware meaning it writes to DesqView's video buffer
                  rather straight into video memory.  It also causes
                  TXZM to release its time slice when it is idle.

              -y  Added in version 2.25.  Allows overriding the received
                  filename on Zmodem receives.  Ex:
                    txzm -y THISNAME.ZIP -r
                  The above line would cause the received file to be
                  called "THISNAME.ZIP"  rather than  the name sent by
                  the sender. This option does not show  on the help
                  screen.

              -$  Added in version 2.30.  Sets "quiet mode" when doing
                  file transfers.  With this option set, the display of
                  the zmodem transfer screen and transfer stats are
                  disabled. This option does not show  on the help
                  screen.

          16550 related switches:

              -d  Do not enable 16550 FIFO mode. Normally TXZM
                  automatically enables FIFO mode.  If you are using a
                  Western Digital 16550 UART at lower baud rates you may
                  need to use this option. The WDC16550 UART doesn't
                  work in FIFO mode at low baud rates.  If you have a
                  16550 and don't know if it is a Western Digital but
                  get Garbled Packet errors when attempting to start a
                  transfer, try this option.  The National Semiconductor
                  16550 (NS16550A) works at all baud rates in FIFO mode.

              -t# Maximum characters to send to 16550 FIFOs per
                  interrupt. This may be between 1 and 16.  The default
                  is 8.  A lower value may be required for modems that
                  used a locked baud rate, hardware flow control, and
                  have a small internal buffer.  8 works fine with USRs.

              -m  Disable modem status register interrupts.  This option
                  is another patch to accommodate Western Digital's
                  version of the 16550.  Some WDC16550s lock up if the
                  modem status lines (CTS, CD, etc.) are not connected
                  to a driving signal.  This could happen if the serial
                  or null modem cable being used does not have all


                  signal lines connected (very possible with a null
                  modem cable).  Using -m prevents this problem.  It
                  also disables hardware flow control and carrier
                  detect, however, so if you require either of these and
                  have a WDC16550 you must use a cable with all
                  appropriate lines connected.

        Examples:

            txzm -p -s (c:\)   // send all files on drive C -- include
                               // complete path information

            txzm -p -r         // accept complete pathnames -- if path
                               // does not exist, create it

            txzm -p -r d:\temp // accept complete pathnames but put files
                               // and created directories under D:\TEMP

            txzm -r            // receive to current directory, if path
                               // information is received it is ignored

            txzm -s (\project\*.c) (\project\*.h)  // Sends all .c and .h
                               // files in the subdir PROJECT and all subs
                               // under project.  Does not send pathnames.

            txzm -u -r \dnlds  // start in mini-terminal mode, received
                               // files are placed in "\dnlds" directory

            txzm com2 -u       // mini-terminal mode, use COM2

            txzm -l38400 -b9600 -h -s file1.zip file2.zip
                               // 38400 baud locked rate, 9600 CONNECT,
                               // hardware handshake, send file list

            txzm -b2400 -u     // 2400 baud, mini-terminal mode

            txzm -c2e0,15 -r   // custom serial port at 2E0h on IRQ15,
                               // use current baud rate, receive

            txzm com2 -b115200 i u  // 115200 baud, ignore carrier detect,
                               // mini-terminal mode

            txzm -e2 -r        // COM1, current baud rate, receive, create
                               // duplicate name if file exists

            txzm -s @filelist  // send all files listed in "filelist"
                               // the name "filelist" is an example only


            Other than the -r and -s switches that must appear last on
        the command line if used, neither case nor switch order are
        significant. Also you may use a '/' instead of a '-' or no
        switch identifier at all.  Ex: "txzm i E2 -u /b2400 r" is legal
        syntax.



                                    GENERAL NOTES

            TXZM is faster than any other zmodem protocol driver I am
        aware of.  It will run at 95% efficiency in both send and
        receive modes at 115200 baud on an 8 MHz 286 with a 16550 UART.
        This translates to an effective throughput of 110 Kbps.  In a PC
        Magazine (Apr 91) article reviewing various communications
        software packages, the BEST zmodem operated at less than 50 Kbps
        when tested at 115200 baud on the same type of equipment (8 Mhz
        286's with 16550 UARTs).  TXZM is over twice as fast.  The
        review covered several well known shareware and commercial
        packages.

            TXZM was also tested on a 4.77 MHz 8088 laptop that
        contained the functional equivalent of a 16450 UART (no FIFOs)
        and a 4.77 MHz IBM XT (true blue IBM) that had 16550 UARTs
        installed.  On the laptop system TXZM could send most
        efficiently at 23040 baud and receive most efficiently at 28800
        baud.  The XT, with 16550 UARTs, could receive at a full 38400
        baud but with the baud rate set to 38400 could only achieve an
        effective throughput rate of around 35000 baud. The tests were
        performed using the systems' hard drives (original slow hard
        drives), not a RAM disk, which also had some impact on speed.
        With 16550 UART's, TXZM could very effectively work a high speed
        modem (HST, V.32, or V.32bis) even on a slow 4.77 MHz computer.

            If you compare the CPS rating stated by TXZM and other
        programs, you may find TXZM reporting slightly lower rates.
        This is due to a difference in the calculation method TXZM uses
        only.  Many other progams appear to fudge a little bit on their
        statistics. At lower speeds or on fast CPUs all Zmodem drivers
        will run about the same. The speed difference shows up when the
        system is under a load such as with extremely high baud rates or
        moderately high baud rates on slow CPUs.


                                     BBS SUPPORT

            TXZM now recognizes the TXZMLOG environment variable and
        will create a log file with the same format as the one created
        by DSZ if DSZLOG is set.  This was added primarily to support
        BBS software that uses DSZLOG format log files to track
        downloads, efficiency, etc.  If all you want is a log file you
        can set TXZMLOG only.  If you are using BBS software that looks
        for a DSZLOG variable, you will have to also set DSZLOG to the
        same value as TXZMLOG.  Ex:

              set TXZMLOG=C:\BBS\ZMODEM.LOG
              set DSZLOG=C:\BBS\ZMODEM.LOG

            I did not use DSZLOG to avoid infringing on any non-public
        domain features of DSZ.  If you want to patch your personal copy
        of TXZM to use DSZLOG directly rather than TXZMLOG, you can use
        a utility such as Norton Utilities or PC Tools to scan TXZM.EXE
        for the string "TXZMLOG" and change it to "DSZLOG".  This is
        only patch you are authorized to make. DO NOT under ANY
        circumstances distribute ANY modified version.


            It is also now possible to specify a file that contains a
        list of the files to be sent.  This is also primarily for BBS
        support.  To use this option precede the file containing the
        list of files with an '@' sign.  The files may be separated by
        any valid whitespace characters including spaces, tabs, carriage
        returns, line feeds, etc.

            The -q option has been added as of version 2.10 for BBS
        operators who run under DesqView.  It causes TXZM to not mess up
        the video and also to release CPU time when it is waiting for
        characters or for the transmit buffer to empty.

            The -0 option will disable direct screen writes if you are
        using command line send or command line receive options.  All
        screen writes will be done through BIOS calls.  Mini-terminal
        mode does direct writes even with the -0 option specified.  -0
        does not appear on the help screen.

            BBS sysops may also use TXZM free (even if you charge for
        access to your system).

                                   REVISION HISTORY

          2.41  Working version of 2.40b below.  IRQs 8-15 now work.  So
                do the fixes for Delphi.

          2.40b Released only as a limited beta version and can cause
                problems.  Added support for IRQs 8-15 (but it didn't
                work).  Some of these are used by the system software so
                make sure to pick a free one. Made two changes to the
                core functions to enable zmodem uploads to the Delphi
                information service to work properly.

          2.31  Some early PCI motherboards (mine, for instance) use a
                chip set that causes the serial port to lock up when
                FIFO mode is enabled.  2.31 detects this problem and
                unlocks the port (transparent to the user).  Also
                changed dial function so it will recognize "CARRIER" as
                a valid connect string.

          2.30  Finalized version of the 2.26b.  Also 1) modified the
                routine that captures the CONNECT rate so that it works
                with the higher speed modems (V.FAST), 2) added a "quiet
                mode" of operation (see -$ flag) that disables the
                zmodem transfer display screen, and 3) added the ability
                to specify a modem init string and the dial prefix
                string via the TXZMDIAL.DIR. See TXZMDIAL.DIR for more
                information.

          2.26b Added an optional dialing directory for miniterm mode.
                The dialing directory is an ASCII text file (you create)
                that TXZM looks for when the program first loads (see
                TXZMDIAL.DIR for an example of how to set up the
                directory).  Also changed the CPS calculation routine to
                make it display correctly when running under DesqView.
                (THIS IS A BETA VERSION).

          2.25  Fixed the "-c" (custom comport switch).  Added -y
                (override received filename) switch.


          2.24  Fixed a problem with the "recurse subdirectories" option
                and also corrected a problem that caused TXZM to not
                work right when running it in a DOS box under OS/2.

          2.22  Recompiled using a different version of the MCOMM
                communications driver.

          2.21  Fixed a divide by zero error that occasionally occurred on
                restarted file transfers.

          2.20  Added support for Doorway mode (ALT = toggles it on and
                off).  Added support for BBSs that autodetect ANSI
                capable programs.  Added -7 switch to enable stripping
                high bit when in terminal mode.

          2.14  Minor changes so code will compile without warnings
                using BC++ 3.0 and so that TXZM would automatically
                trigger a Qmodem download (Qmodem requires an "rz\r" as
                well as the INIT packet -- most programs trip on the
                INIT packet alone). Also modified the -n (BBS support
                option) so that it took the name of a Maximus or Opus
                style LASTUSER.BBS filename rather than a node number.
                Modified FIFO usage so that TXZM set FIFO buffers to 1
                in terminal mode and 8 when sending files (corrects
                jerky display at low baud rates).

          2.10  Changed name to TXZM from ZMP.  The ZMPLOG environment
                variable is now  TXZMLOG.  Found out somebody else
                already had a ZMP in CP/M days.  Added DesqView aware
                option.  Fixed Dial Command so that it looked at the
                connect baud rate and adjusted accordingly. Fixed Redial
                Command to continually dial until a connect was made or
                ESC pressed.  Added F1 for help key.  Added ALT-P so the
                modem parameters could be changed manually, ALT-C so the
                screen could be cleared, and ALT-= for Doorway mode
                operation.

          2.00  First non-beta version.  Added a capture file.  Fixed a
                minor problem with the -0 option.

          1.21  Added support for specifying files to send in a file
                that contains a list of the filenames.  Added -0
                option (disable direct screen writes in command mode).

          1.20  Fixed bug introduced in version 1.19 that caused a
                divide by zero error if the total bytes to be sent was
                between 1 and 18.  Added ZMPLOG environment variable.

          1.19  Corrected bugs in the -w and -x options.  Fixed problem
                with negative CPS rates showing up when more than 11
                megabytes were sent.  Added the -6 switch.

          1.17  Fixed double backslash in pathnames when downloading
                while in the root directory (couldn't DL to root).

          1.16  Added support for send and receive of complete pathnames
                and creation of subdirectories.  This allows duplication
                of entire drives or subdirectories through the serial
                port.


          1.10  16 bit CRC mode now really does work.  TXZM102 was
                supposed to have fixed it but didn't.

          1.02  Fixed bug in 16 bit CRC mode (I thought).  Fixed minor error
                in ZRPOS handler.  The sender now sends a ZCRCW packet when an
                error occurs rather than a ZCRCG. This conforms with Chuck
                Forsberg's Zmodem specification.

          1.01  Fixed bug in ZRPOS handler.  This bug occasionally
                caused TXZM to trash the screen and lock up when a ZRPOS
                was received.
                  Optimized the code. TXZM will now operate at 115200
                baud at 95% efficiency on an 8MHz 286 (approx 11100 cps
                -- 2 meg in 3 mins).  A 16550 UART is required to obtain
                high speed operation.
                  In mini-term mode, PGDN puts TXZM in receive mode in
                case the sender's ZRQINIT was missed.  Previously it
                relied on the incoming ZRQINIT to trigger receive mode.
                It now works either way.
                  Added a '-v' switch.  This switch disables overlaying
                disk and serial I/O.  It also expands the receive file
                buffer to 20K bytes.  The result is 20K of data is
                received, serial I/O pauses, the 20K is written to disk,
                a ZACK is sent, and the sender resumes sending.