page 1
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³ ASTATER.EXE Version 1.0 - AHDL State Machine Generator ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

           (C)Copyright & Support - Amos Zaslavsky @ 972-4-230219.

   Description ........................................................  1
   Command line syntax ................................................  2
   Example 1 : A Mealy machine with fully encoded state assignment ....  3
   Example 2 : A Mealy machine with One-Hot state assignment .......... 11
   Example 3 : A Moore machine with direct outputs .................... 15
   Example 4 : A Moore mixed example .................................. 21
   Errors, Warning & Note Messages .................................... 28
   Limitations & Legal details ........................................ 32

                                 Description
                                -------------

ASTATER.EXE is a utility for generating an ABEL file for state machines.

It will generate a file template that will fit your requirements of:

- number of inputs
- number of outputs
- maximum number of relevant conditions per state
- number of flip flops
- state names

After generation of the state machine file you will have to make a few
changes to the file with your text editor. This utility can save time and let
you concentrate on the logic of the machine an not on the syntax. The program
is simpler to use then some fancy graphical state machine generators that
are on the market (which are also expensive).

The original idea of a stater program came from Ofer Hoffman (A VHDL shark
@ 972-4-230048) how wrote a program like this for VHDL users !


 page 2
                             Command line syntax
                            ---------------------

ASTATER must be followed by eight command line parameters:

 ASTATER <module> <in> <out> <con> <ff> /1|2 <state_name> <state_name>...

  <module>  Is the module name. This will also be the file name and device
            name.

  <in>      Is the number of inputs. At least one input must be defined.

  <out>     Number of indirect outputs. Indirect output is an output that is
            not a direct flip flop output.

  <cond>    Is the maximum number of relevant condition per state. A machine
            can have many inputs (for example 15: I1,I2...I15), but in each
            state only a small number of conditions is relevant. for example:

            condition1 -   I1 & !I2
            condition2 -   I1 &  I2
            condition3 -  !I1

            (in this example only 3 conditions). The maximum number of
            conditions is 2^(inputs). A condition is not only a single input
            signal (literal) but a can be a function of such signals (Like in
            the previous example).

  <ff>      Number of flip-flops. A state machine must have at least one
            flip-flop. If it has no flip-flops it is not a synchronous state
            machine. If you plan to use one of the Flip-Flop outputs as an
            output of the machine (a good way to prevent output spikes), don't
            count it as an output of the machine. Such an output is called in
            this document - "A direct output". Only indirect outputs should be
            counted as outputs of the machine.

  /1|2      Type of machine:

            /1 - Moore machine (outputs depend only of the present state of
                                the machine)
            /2 - Mealy machine (outputs depend both on the present state of
                                the machine and the inputs)
            /3 - Dummy machine (A moore machine that can be compiled with on
                                modifications. The machine is a cyclic counter
                                enabled by the "input1" signal. The number of
                                conditions that you enter as command line is
                                not relevant.)

  <state>   A state name. A list of state names must have at least tow
            members, but can have more.


 page 3

       Example 1 : A Mealy machine with fully encoded state assignment
       ---------------------------------------------------------------

In this example we will describe a Mealy state machine with 3 inputs and 3
outputs.

                                 ÚÄÄÄÄÄÄÄÄÄ¿
                           U ÄÄÄ>´         ÃÄÄ>Ä R
                Inputs     V ÄÄÄ>´    M1   ÃÄÄ>Ä S     Outputs
                           W ÄÄÄ>´         ÃÄÄ>Ä T
                                 ÀÄÄÄÄÂÄÄÄÄÙ
                                      ³
                              Cp ÄÄ>ÄÄÙ


This is a state-table of the machine:

            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÂÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
            ³ Present State ³  Input  ³³  Next State   ³ Output  ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       AA      ³   !U    ³³      AA       ³    R    ³
            ³               ³    U    ³³      BB       ³    R    ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       BB      ³   !V    ³³      CC       ³   S,T   ³
            ³               ³    V    ³³      DD       ³   S     ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       CC      ³ !V & W  ³³      CC       ³    -    ³
            ³               ³  V & W  ³³      DD       ³    -    ³
            ³               ³     !W  ³³      AA       ³    -    ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       DD      ³    1    ³³      AA       ³   R,S   ³
            ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÙ


It is easy to see from the table that the maximum number of transition
conditions per state is three. The behavior of this machine is a Mealy
behavior only when the machine is in state BB (and it's enough to make it a
Mealy machine). When the machine is in state DD it makes an un-conditional
transition (Autonomous) to the AA state.

In This example we will use a full binary encoding of state assignments. For
this kind of encoding we need only tow flip-flops. In the next example we will
use a One-Hot decoded state assignments. In the next example four flip-flops
will be needed.


 page 4

For this example ASTATER.EXE will be used with The following command line
parameters:

               3 - inputs
               3 - outputs
               3 - conditions
               2 - flip-flops
              /2 - Mealy machine
              AA - first state
              BB - second state
              CC - third state
              DD - forth state

Here is the command line you have to type:

ASTATER M1 3 3 3 2 /2 AA BB CC DD

Here is the file that will be created by ASTATER.EXE :


                                    M1.ABL
ÚÄ
³MODULE M1
³TITLE 'M1.ABL created by ASTATER.EXE Version 1.0
³       Time of creation is Sat Aug 20 17:07:13 1994
³      '
³DECLARATIONS
³
³   M1 DEVICE ;
³   input1 PIN ;
³   input2 PIN ;
³   input3 PIN ;
³   CP PIN ; "CLOCK INPUT"
³   MR PIN ; "MASTER RESET (ASYN) INPUT"
³   output1 PIN ISTYPE 'COM' ;
³   output2 PIN ISTYPE 'COM' ;
³   output3 PIN ISTYPE 'COM' ;
³   Q1 NODE ISTYPE 'REG,BUFFER' ;
³   Q0 NODE ISTYPE 'REG,BUFFER' ;
³
³   PS = [Q1,Q0] ; "STATE ASSIGNMENT"
³   AA = [ 0, 0] ;
³   BB = [ 0, 0] ;
³   CC = [ 0, 0] ;
³   DD = [ 0, 0] ;
³
³   C , X , P , Z = .C. , .X. , .P. , .Z. ;
³
 page 5

³EQUATIONS
³
³PS.AR = !MR ;
³   PS.CLK = CP ;
³
³STATE_DIAGRAM PS
³
³   STATE AA :
³      [output1,output2,output3]=[0,0,0] ;
³      CASE
³         condition11 : next_state11
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition12 : next_state12
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition13 : next_state13
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³      ENDCASE ;
³   STATE BB :
³      [output1,output2,output3]=[0,0,0] ;
³      CASE
³         condition21 : next_state21
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition22 : next_state22
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition23 : next_state23
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³      ENDCASE ;
³   STATE CC :

 pgage 6

³      [output1,output2,output3]=[0,0,0] ;
³      CASE
³         condition31 : next_state31
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition32 : next_state32
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition33 : next_state33
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³      ENDCASE ;
³   STATE DD :
³      [output1,output2,output3]=[0,0,0] ;
³      CASE
³         condition41 : next_state41
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition42 : next_state42
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³         condition43 : next_state43
³            WITH
³               [output1,output2,output3]=[0,0,0] ;
³            ENDWITH ;
³      ENDCASE ;
³
³DECLARATIONS
³
³   NS = [Q1,Q0] ; "NEXT STATE"
³
³TEST_VECTORS
³
³   ([MR,CP,input1,input2,input3] -> [NS,output1,output2,output3])
³
³END
ÀÄ

All the place holders were generated by ASTATER.EXE in lowercase letters.
Using the replace function of your editor (a global replace) do the folowing
replacements:


 page 7

- Replace input1 with U

- Replace input2 with V

- Replace input3 with W

- Replace output1 with R

- Replace output2 with S

- Replace output3 with T

Now do the folowing changes:

- Make state assignments.

  for example:

                AA = [0,0], BB = [0,1], CC = [1,0], DD = [1,1]

  The assignment of combination [0,0] to state AA and the declarations of
  attributes 'REG,BUFFER' that were chosen for Q1 and Q0, make the AA state
  the reset state of the machine. It is not hard to change it.

- Delete the WITH..ENDWITH blocks from first, third and last state blocks.
  These blocks desribe Mealy type behavior, and these blocks are Moore type
  blocks (only the second block describes a Mealy behavior).

- Replace dummy conditions (condition1,condition2...) and next_states
  (next_state1, next_state2...) , with real conditions and real next_states
  and delete lines that are not needed.

  It is possible to describe an unconditional transition with ABEL's CASE
  statements in the following way:

    STATE DD :
       [R,S,T]=[1,1,0] ;
       CASE
          1 : AA                   <- this is the unconditional transition
       ENDCASE ;

  it is equivalent to the folowing statements:

    STATE DD :
       [R,S,T]=[1,1,0] ;
       GOTO AA

 page 8

- Replace zero output assignments (Mealy and Moore type) with real (0 or 1)
  output assignments and delete output assignments that are not needed.

- Add test vector values.

Now the file will look like this:

                                    M1.ABL
ÚÄ
³MODULE M1
³TITLE 'M1.ABL created by ASTATER.EXE Version 1.0
³       Time of creation is Sat Aug 20 17:07:13 1994
³      '
³DECLARATIONS
³
³   M1 DEVICE ;
³   U PIN ;
³   V PIN ;
³   W PIN ;
³   CP PIN ; "CLOCK INPUT"
³   MR PIN ; "MASTER RESET (ASYN) INPUT"
³   R PIN ISTYPE 'COM' ;
³   S PIN ISTYPE 'COM' ;
³   T PIN ISTYPE 'COM' ;
³   Q1 NODE ISTYPE 'REG,BUFFER' ;
³   Q0 NODE ISTYPE 'REG,BUFFER' ;
³
³   PS = [Q1,Q0] ; "STATE ASSIGNMENT"
³   AA = [ 0, 0] ;
³   BB = [ 0, 1] ;
³   CC = [ 1, 0] ;
³   DD = [ 1, 1] ;
³
³   C , X , P , Z = .C. , .X. , .P. , .Z. ;
³
³EQUATIONS
³
³   PS.AR = !MR ;
³   PS.CLK = CP ;
³
 page 9
³STATE_DIAGRAM PS
³
³   STATE AA :
³      [R,S,T]=[1,0,0] ;
³      CASE
³         !U : AA
³          U : BB
³      ENDCASE ;
³   STATE BB :
³      [R,S]=[0,1] ;
³      CASE
³         !V : CC
³            WITH
³               T = 1 ;
³            ENDWITH ;
³          V : DD
³            WITH
³               T = 0 ;
³            ENDWITH ;
³      ENDCASE ;
³   STATE CC :
³      [R,S,T]=[0,0,0] ;
³      CASE
³         !V & W : CC
³          V & W : DD
³             !W : AA
³      ENDCASE ;
³   STATE DD :
³      [R,S,T]=[1,1,0] ;
³      CASE
³         1 : AA
³      ENDCASE ;
³
³DECLARATIONS
³
³   NS = [Q1,Q0] ; "NEXT STATE"
³
 page 10
³TEST_VECTORS
³
³  ([MR,CP,U,V,W] -> [PS,R,S,T])
³   [ 0, X,X,X,X] -> [AA,1,0,0]; "RESET"
³   [ 1, C,0,X,X] -> [AA,1,0,0]; "AA->AA"
³   [ 1, C,1,X,X] -> [BB,0,1,X]; "AA->BB (T IS X)"
³   [ 1, 0,X,0,X] -> [BB,0,1,1]; "BB/T"
³   [ 1, 0,X,1,X] -> [BB,0,1,0]; "BB/!T"
³   [ 1, C,X,0,X] -> [CC,0,0,0]; "BB->CC"
³   [ 1, C,X,0,1] -> [CC,0,0,0]; "CC->CC"
³   [ 1, C,X,X,0] -> [AA,1,0,0]; "CC->AA"
³   [ 1, C,1,X,X] -> [BB,0,1,X]; "AA->BB (T IS X)"
³   [ 1, C,X,1,X] -> [DD,1,1,0]; "BB->DD"
³   [ 1, C,X,X,X] -> [AA,1,0,0]; "DD->AA"
³   [ 1, C,1,X,X] -> [BB,0,1,X]; "AA->BB (T IS X)"
³   [ 1, C,X,0,X] -> [CC,0,0,0]; "BB->CC"
³   [ 1, C,X,1,1] -> [DD,1,1,0]; "CC->DD"
³   [ 1, C,X,X,X] -> [AA,1,0,0]; "DD->AA"
³
³END
ÀÄ

Now compile, simulate and generate a JEDEC file using ABEL.


 page 11

          Example 2 : A Mealy machine with One-Hot state assignment
          ---------------------------------------------------------

In this example we will design the same state machine that we designed before,
but we will use the One-Hot state assignment. for this kind of assignment
we need 4 flip-flops. This time we will run ASTATER.EXE using the same command
line parameters except the number of flip-flops that is 4 and the name of the
machine that will be changed to M2. Here is how the command line looks:

ASTATER M2 3 3 3 2 /2 AA BB CC DD

The file that will be generated looks like the file we got earlier but with
more flip-flops. All the replacements we did before will be done here too:

- Replace input1 with U

- Replace input2 with V

- Replace input3 with W

- Replace output1 with R

- Replace output2 with S

- Replace output3 with T

The main difference between this example and the previous example, is in the
state assignments. Write the following one-hot state assignments:

        AA = [1,0,0,0], BB = [0,1,0,0], CC = [0,0,1,0] DD = [0,0,0,1]

Other important change that must be done (that differ from the previous
example) is to change the declaration of node Q0 from ISTYPE 'REG,BUFFER' to
ISTYPE 'REG,INVERT'. This change is done because we want the reset state to
be AA [1,0,0,0]. When MR is invoked (MR is active-low) we want the machine to
be in the AA state. In this state Q0 (the flip-flop of state AA) must be in a
High (1) state.

All the other changes we had to make in this example to the original ASTATER
generated source file, are the same changes we had to do in the previous
example. Here are all the changes that need to be done:

- Delete WITH..ENDWITH blocks from first, third and last state blocks. These
  blocks describe Moore type behavior.

- Replace dummy conditions (condition1,condition2...) and next_states
  (next_state1, next_state2...) with real conditions and real next_states and
  delete lines that are not needed.


 page 12

- Replace zero output assignments (Mealy and Moore type) with real output
  assignments and delete output assignments that are not needed.

- Add test vector values.

Now the file will look like this:

                                    M2.ABL
ÚÄ
³MODULE M2
³TITLE 'M2.ABL created by ASTATER.EXE Version 1.0
³       Time of creation is Sat Aug 20 17:07:13 1994
³      '
³DECLARATIONS
³
³   M2 DEVICE ;
³   U PIN ;
³   V PIN ;
³   W PIN ;
³   CP PIN ; "CLOCK INPUT"
³   MR PIN ; "MASTER RESET (ASYN) INPUT"
³   R PIN ISTYPE 'COM' ;
³   S PIN ISTYPE 'COM' ;
³   T PIN ISTYPE 'COM' ;
³   Q3 NODE ISTYPE 'REG,BUFFER' ;
³   Q2 NODE ISTYPE 'REG,BUFFER' ;
³   Q1 NODE ISTYPE 'REG,BUFFER' ;
³   Q0 NODE ISTYPE 'REG,INVERT' ;
³
³   PS = [Q3,Q2,Q1,Q0] ; "STATE ASSIGNMENT"
³   AA = [ 0, 0, 0, 1] ;
³   BB = [ 0, 0, 1, 0] ;
³   CC = [ 0, 1, 0, 0] ;
³   DD = [ 1, 0, 0, 0] ;
³
³   C , X , P , Z = .C. , .X. , .P. , .Z. ;
³
³EQUATIONS
³
³   PS.AR = !MR ;
³   PS.CLK = CP ;
³
 page 13
³STATE_DIAGRAM PS
³
³   STATE AA :
³      [R,S,T]=[1,0,0] ;
³      CASE
³         !U : AA
³          U : BB
³      ENDCASE ;
³   STATE BB :
³      [R,S]=[0,1] ;
³      CASE
³         !V : CC
³            WITH
³               T = 1 ;
³            ENDWITH ;
³          V : DD
³            WITH
³               T = 0 ;
³            ENDWITH ;
³      ENDCASE ;
³   STATE CC :
³      [R,S,T]=[0,0,0] ;
³      CASE
³         !V & W : CC
³          V & W : DD
³             !W : AA
³      ENDCASE ;
³   STATE DD :
³      [R,S,T]=[1,1,0] ;
³      CASE
³         1 : AA
³      ENDCASE ;
³
³DECLARATIONS
³
³   NS = [Q1,Q0] ; "NEXT STATE"
³
 page 14
³TEST_VECTORS
³
³  ([MR,CP,U,V,W] -> [PS,R,S,T])
³   [ 0, X,X,X,X] -> [AA,1,0,0]; "RESET"
³   [ 1, C,0,X,X] -> [AA,1,0,0]; "AA->AA"
³   [ 1, C,1,X,X] -> [BB,0,1,X]; "AA->BB (T IS X)"
³   [ 1, 0,X,0,X] -> [BB,0,1,1]; "BB/T"
³   [ 1, 0,X,1,X] -> [BB,0,1,0]; "BB/!T"
³   [ 1, C,X,0,X] -> [CC,0,0,0]; "BB->CC"
³   [ 1, C,X,0,1] -> [CC,0,0,0]; "CC->CC"
³   [ 1, C,X,X,0] -> [AA,1,0,0]; "CC->AA"
³   [ 1, C,1,X,X] -> [BB,0,1,X]; "AA->BB (T IS X)"
³   [ 1, C,X,1,X] -> [DD,1,1,0]; "BB->DD"
³   [ 1, C,X,X,X] -> [AA,1,0,0]; "DD->AA"
³   [ 1, C,1,X,X] -> [BB,0,1,X]; "AA->BB (T IS X)"
³   [ 1, C,X,0,X] -> [CC,0,0,0]; "BB->CC"
³   [ 1, C,X,1,1] -> [DD,1,1,0]; "CC->DD"
³   [ 1, C,X,X,X] -> [AA,1,0,0]; "DD->AA"
³
³END
ÀÄ

Now compile, simulate and generate a JEDEC file using ABEL.


 page 15
               Example 3 : A Moore machine with direct outputs
               -----------------------------------------------

In this example we will be designing the following Moore machine:


            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÂÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
            ³ Present State ³  Input  ³³  Next State   ³ Output  ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       AA      ³   !U    ³³      AA       ³    R    ³
            ³               ³    U    ³³      BB       ³    R    ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       BB      ³   !V    ³³      CC       ³   S,T   ³
            ³               ³    V    ³³      DD       ³   S,T   ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       CC      ³ !V & W  ³³      CC       ³    -    ³
            ³               ³  V & W  ³³      DD       ³    -    ³
            ³               ³     !W  ³³      AA       ³    -    ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       DD      ³    1    ³³      AA       ³   R,S   ³
            ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÙ

This machine has 3 inputs an 3 outputs and behaves almost exactly like the
machine from the previous examples. The only difference is that the T output
dose not change as a function of V, when the machine is in the BB state (it
used to change on the first and second examples).

In the previous examples the outputs of the machine were not directly the
outputs of the flip-flops. Combinatorial logic was used to decode the
flip-flop outputs combinations to machine output combinations (a waste of
hardware resources).


                                  CP Ä>Ä¿
                     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³  ÚÄÄÄÄÄÄ¿
                     ³  Cmbinational  ÃÄÅÄ>´D1    ÃÄÂÄ Q1
                     ³                ³ ÃÄÄ´> FF  ³ ³
                     ³ Sum of product ³ ³  ÀÄÄÄÄÄÄÙ ³
                     ³                ÃÄÅÄÄÄÄÄ<ÄÄÄÄÄÙ foldback
            U ÄÄÄÄÄÄ>´     Matrix     ³ ³  ÚÄÄÄÄÄÄ¿
                     ³                ÃÄÅÄ>´D1    ÃÄÂÄ Q0
            V ÄÄÄÄÄÄ>´                ³ ÀÄÄ´> FF  ³ ³
                     ³                ³    ÀÄÄÄÄÄÄÙ ³
            W ÄÄÄÄÄÄ>´                ÃÄÄÄÄÄÄÄ<ÄÄÄÄÄÙ foldback
                     ³              d ³
                     ³              e ÃÄÄÄÄÄÄÄ>ÄÄÄÄÄÄÄ R
                     ³              c ³
                     ³              o ÃÄÄÄÄÄÄÄ>ÄÄÄÄÄÄÄ S
                     ³              d ³
                     ³              e ÃÄÄÄÄÄÄÄ>ÄÄÄÄÄÄÄ T
                     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

 page 16

When a design of this type is implemented with a flip-flop that has no buried
registers, it wastes pins (ABEL will automatically exchange NODEs to PINs if
the device has no nodes).

When designing a Moore machine, one can assign flip-flops so the outputs of
machine will be directly the outputs of filp-flops.



                                  CP Ä>Ä¿
                     ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ ³  ÚÄÄÄÄÄÄ¿
                     ³  Cmbinational  ÃÄÅÄ>´DR    ÃÄÂÄ R
                     ³                ³ ÃÄÄ´> FF  ³ ³
                     ³ Sum of product ³ ³  ÀÄÄÄÄÄÄÙ ³
                     ³                ÃÄÅÄÄÄÄÄ<ÄÄÄÄÄÙ
            U ÄÄÄÄÄÄ>´     Matrix     ³ ³  ÚÄÄÄÄÄÄ¿
                     ³                ÃÄÅÄ>´DS    ÃÄÂÄ S
            V ÄÄÄÄÄÄ>´                ³ ÃÄÄ´> FF  ³ ³
                     ³                ³ ³  ÀÄÄÄÄÄÄÙ ³
            W ÄÄÄÄÄÄ>´                ÃÄÅÄÄÄÄÄ<ÄÄÄÄÄÙ
                     ³                ³ ³  ÚÄÄÄÄÄÄ¿
                     ³                ÃÄÅÄ>´DT    ÃÄÂÄ T
                     ³                ³ ÀÄÄ´> FF  ³ ³
                     ³                ³    ÀÄÄÄÄÄÄÙ ³
                     ³                ÃÄÄÄÄÄÄÄ<ÄÄÄÄÄÙ
                     ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

This will save pins of the PAL, reduce tpd (from the clock signal to the
outputs), and produce clean outputs with no spikes. Not all outputs have to be
produced this way. Some times a mixture of direct and indirect outputs is also
chosen.

In this example we want all outputs to come directly from flip-flop outputs.
To do this we choose to define zero outputs in the command line of ASTATER.
The number of outputs defined for ASTATER is the number of indirect outputs !
We also chose three flip-flops (a flip-flop for every output). This is the
command and command line parameters used:

ASTATER M3 3 0 3 3 /1 AA BB CC DD


 page 17

Here is the file that will be created by ASTATER.EXE :


                                    M3.ABL
ÚÄ
³MODULE M3
³TITLE 'M3.ABL created by ASTATER.EXE Version 1.0
³       Time of creation is Sat Aug 20 17:07:13 1994
³      '
³DECLARATIONS
³
³   M3 DEVICE ;
³   input1 PIN ;
³   input2 PIN ;
³   input3 PIN ;
³   CP PIN ; "CLOCK INPUT"
³   MR PIN ; "MASTER RESET (ASYN) INPUT"
³   Q2 NODE ISTYPE 'REG,BUFFER' ;
³   Q1 NODE ISTYPE 'REG,BUFFER' ;
³   Q0 NODE ISTYPE 'REG,BUFFER' ;
³
³   PS = [Q2,Q1,Q0] ; "STATE ASSIGNMENT"
³   AA = [ 0, 0, 0] ;
³   BB = [ 0, 0, 0] ;
³   CC = [ 0, 0, 0] ;
³   DD = [ 0, 0, 0] ;
³
³   C , X , P , Z = .C. , .X. , .P. , .Z. ;
³
³EQUATIONS
³
³   PS.AR = !MR ;
³   PS.CLK = CP ;
³
 page 18
³STATE_DIAGRAM PS
³
³   STATE AA :
³      CASE
³         condition11 : next_state11
³         condition12 : next_state12
³         condition13 : next_state13
³      ENDCASE ;
³   STATE BB :
³      CASE
³         condition21 : next_state21
³         condition22 : next_state22
³         condition23 : next_state23
³      ENDCASE ;
³   STATE CC :
³      CASE
³         condition31 : next_state31
³         condition32 : next_state32
³         condition33 : next_state33
³      ENDCASE ;
³   STATE DD :
³      CASE
³         condition41 : next_state41
³         condition42 : next_state42
³         condition43 : next_state43
³      ENDCASE ;
³
³DECLARATIONS
³
³   NS = [Q2,Q1,Q0] ; "NEXT STATE"
³
³TEST_VECTORS
³
³   ([MR,CP,input1,input2,input3] -> NS ;
³
³END
ÀÄ

Notice that the Mealy output assignments are missing now from the file.


 page 19

All the replacements we did in previous examples are done here in the same
way:

- Replace input1 with U

- Replace input2 with V

- Replace input3 with W

- There are no replacements for output1/2/3 because they were not generated in
  file

The main difference between this implementation and the previous ones is in
the state assignments. Write the following state assignments:

            AA = [1,0,0], BB = [0,1,1], CC = [0,0,0], DD = [1,1,0]

In case a unique assignment for each state could not be found more flip-flops
could be appended to the state register (we do not need to add flip-flops in
this example).

Other important change that must be made is to change node Q0 from ISTYPE
'REG,BUFFER'to ISTYPE 'REG,INVERT'. This is because we want the reset state to
be AA. When MR is invoked (low) we want the machine to be in the AA state. In
this state Q0 (the flip-flop that is a direct output implementing the R output
of the machine) must be in a High (1) state.

All the other changes we have to make to the original ASTATER generated file
are the same changes we did in the previous examples. Here are all the changes
that need to be done:

- Replace dummy conditions (condition1, condition2...) and next_states
  (next_state1, next_state2...) with real conditions and next_states and
  delete lines that are not needed.

- Add test vector values.


 page 20

Now the file will look like this:

                                    M3.ABL
ÚÄ
³MODULE M3
³TITLE 'M3.ABL created by ASTATER.EXE Version 1.0
³       Time of creation is Sat Aug 20 17:07:13 1994
³      '
³DECLARATIONS
³
³   M3 DEVICE ;
³   U PIN ;
³   V PIN ;
³   W PIN ;
³   CP PIN ; "CLOCK INPUT"
³   MR PIN ; "MASTER RESET (ASYN) INPUT"
³   Q2 NODE ISTYPE 'REG,INVERT' ;
³   Q1 NODE ISTYPE 'REG,BUFFER' ;
³   Q0 NODE ISTYPE 'REG,BUFFER' ;
³
³   PS = [Q2,Q1,Q0] ; "STATE ASSIGNMENT"
³   AA = [ 1, 0, 0] ;
³   BB = [ 0, 1, 1] ;
³   CC = [ 0, 0, 0] ;
³   DD = [ 1, 1, 0] ;
³
³   C , X , P , Z = .C. , .X. , .P. , .Z. ;
³
³EQUATIONS
³
³   PS.AR = !MR ;
³   PS.CLK = CP ;
³
³STATE_DIAGRAM PS
³
 page 21
³   STATE AA :
³      CASE
³         !U : AA
³          U : BB
³      ENDCASE ;
³   STATE BB :
³      CASE
³         !V : CC
³          V : DD
³      ENDCASE ;
³   STATE CC :
³      CASE
³         !V & W : CC
³          V & W : DD
³             !W : AA
³      ENDCASE ;
³   STATE DD :
³      CASE
³         1 : AA
³      ENDCASE ;
³
³DECLARATIONS
³
³   NS = [Q2,Q1,Q0] ; "NEXT STATE"
³
³TEST_VECTORS
³
³   ([MR,CP,U,V,W] -> NS)
³    [ 0, X,X,X,X] -> AA; "RESET"
³    [ 1, C,0,X,X] -> AA; "AA->AA"
³    [ 1, C,1,X,X] -> BB; "AA->BB"
³    [ 1, C,X,0,X] -> CC; "BB->CC"
³    [ 1, C,X,0,1] -> CC; "CC->CC"
³    [ 1, C,X,X,0] -> AA; "CC->AA"
³    [ 1, C,1,X,X] -> BB; "AA->BB"
³    [ 1, C,X,1,X] -> DD; "BB->DD"
³    [ 1, C,X,X,X] -> AA; "DD->AA"
³    [ 1, C,1,X,X] -> BB; "AA->BB"
³    [ 1, C,X,0,X] -> CC; "BB->CC"
³    [ 1, C,X,1,1] -> DD; "CC->DD"
³    [ 1, C,X,X,X] -> AA; "DD->AA"
³
³END
ÀÄ
Now compile, simulate and generate a JEDEC file using ABEL.


 page 21
               Example 4 : A Moore mixed example
               ---------------------------------

In this example we will be designing the following Moore machine:

                                 ÚÄÄÄÄÄÄÄÄÄ¿
                           I ÄÄÄ>´         ÃÄÄ>Ä P
                           J ÄÄÄ>´         ÃÄÄ>Ä Q
                Inputs     K ÄÄÄ>´    M4   ÃÄÄ>Ä R     Outputs
                           L ÄÄÄ>´         ÃÄÄ>Ä S
                           M ÄÄÄ>´         ÃÄÄ>Ä T
                                 ÀÄÄÄÄÂÄÄÄÄÙ
                                      ³
                              Cp ÄÄ>ÄÄÙ


            ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÂÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¿
            ³ Present State ³  Input  ³³  Next State   ³ Output  ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       AA      ³   !I    ³³      AA       ³    P    ³
            ³               ³    I    ³³      BB       ³    P    ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       BB      ³   !J    ³³      BB       ³    Q    ³
            ³               ³    J    ³³      CC       ³    Q    ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       CC      ³  I $ J  ³³      DD       ³    -    ³
            ³               ³  I!$ J  ³³      CC       ³    -    ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       DD      ³  K # L  ³³      EE       ³   R,T   ³
            ³               ³ !K & !L ³³      DD       ³   R,T   ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       EE      ³   !M    ³³      EE       ³   S,T   ³
            ³               ³    M    ³³      FF       ³   S,T   ³
            ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ´
            ³       FF      ³    1    ³³      AA       ³  R,S,T  ³
            ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÙ

 page 22

This machine has 5 inputs an 5 outputs and behaves as a moore machine.

Suppose we need that the outputs P,Q and T be clean outputs that do not
produce decoding spikes (because they drive for example an asynchronous reset
of a flip-flop or a write-enable input of a RAM) It is recommended to use a
One-Hot state assignment for state A and B because the P and Q outputs are
active only on state AA and BB. We will assign state AA to flip-flop Q2 and
state BB to flip flop Q3. The outputs of the flip-flops Q2 and Q3 will be P
and Q outputs respectively. The T output is not unique to only one state, so
we will not be able to use a one hot assignment in order to produce it. We
will just add a special flip-flop that will produce this output directly. This
will be flip-flop Q4. The output of Q4 is the output T (T is a direct output).

Suppose that the other outputs are allowed to have decoding spikes (because
they drive for example other synchronous devices that share the same clock).
Also suppose for example, that target device has unused buried nodes. We will
want to use the buried nodes and not waste any more output macrocells of the
device. We can choose to fully encode the other state combinations and assign
them to a pair of flip-flops called Q1 and Q0. We will assign CC to
[Q1,Q0] = [0,0], DD to [Q1,Q0] = [0,1], EE to [Q1,Q0] = [1,0] and FF to
[Q1,Q0] = [1,1]

When we use ASTATER.EXE we need only to declare to outputs (R and S), which
are indirect outputs. All other outputs (P,Q and T) are direct flip-flop
outputs. The total number of flip-flops will be 1 + 1 + 1 + 2 = 5. The number
of states is 6 and number of transitions is 2. The number of inputs is 5.

The command and command line parameters used in this example are:

ASTATER M4 5 2 2 5 /1 AA BB CC DD EE FF


 page 23

Here is the file that will be created by ASTATER.EXE :


                                    M4.ABL
ÚÄ
³MODULE M4
³TITLE 'M4.ABL created by ASTATER.EXE Version 1.0
³       Time of creation is Sat Aug 20 17:07:13 1994
³      '
³DECLARATIONS
³
³   M4 DEVICE ;
³   input1 PIN ;
³   input2 PIN ;
³   input3 PIN ;
³   input4 PIN ;
³   input5 PIN ;
³   CP PIN ; "CLOCK INPUT"
³   MR PIN ; "MASTER RESET (ASYN) INPUT"
³   output1 PIN ISTYPE 'COM' ;
³   output2 PIN ISTYPE 'COM' ;
³   Q4 NODE ISTYPE 'REG,BUFFER' ;
³   Q3 NODE ISTYPE 'REG,BUFFER' ;
³   Q2 NODE ISTYPE 'REG,BUFFER' ;
³   Q1 NODE ISTYPE 'REG,BUFFER' ;
³   Q0 NODE ISTYPE 'REG,BUFFER' ;
³
³   PS = [Q4,Q3,Q2,Q1,Q0] ; "STATE ASSIGNMENT"
³   AA = [ 0, 0, 0, 0, 0] ;
³   BB = [ 0, 0, 0, 0, 0] ;
³   CC = [ 0, 0, 0, 0, 0] ;
³   DD = [ 0, 0, 0, 0, 0] ;
³   EE = [ 0, 0, 0, 0, 0] ;
³   FF = [ 0, 0, 0, 0, 0] ;
³
³   C , X , P , Z = .C. , .X. , .P. , .Z. ;
³
³EQUATIONS
³
³   PS.AR = !MR ;
³   PS.CLK = CP ;
³

 page 24

³STATE_DIAGRAM PS
³
³   STATE AA :
³      [output1,output2] = [0,0] ;
³      CASE
³         condition11 : next_state11
³         condition12 : next_state12
³      ENDCASE ;
³   STATE BB :
³      [output1,output2] = [0,0] ;
³      CASE
³         condition21 : next_state21
³         condition22 : next_state22
³      ENDCASE ;
³   STATE CC :
³      [output1,output2] = [0,0] ;
³      CASE
³         condition31 : next_state31
³         condition32 : next_state32
³      ENDCASE ;
³   STATE DD :
³      [output1,output2] = [0,0] ;
³      CASE
³         condition41 : next_state41
³         condition42 : next_state42
³      ENDCASE ;
³   STATE EE :
³      [output1,output2] = [0,0] ;
³      CASE
³         condition51 : next_state51
³         condition52 : next_state52
³      ENDCASE ;
³   STATE FF :
³      [output1,output2] = [0,0] ;
³      CASE
³         condition61 : next_state61
³         condition62 : next_state62
³      ENDCASE ;
³
³DECLARATIONS
³
³   NS = [Q4,Q3,Q2,Q1,Q0] ; "NEXT STATE"
³
³TEST_VECTORS
³
³   ([MR,CP,input1,input2,input3,input4,input5] -> [NS,output1,output2])
³
³END
ÀÄ

 page 25

Here is the file after making changes with an editor:

                                    M4.ABL
ÚÄ
³MODULE M4
³TITLE 'M4.ABL created by ASTATER.EXE Version 1.0
³       Time of creation is Sat Aug 20 17:07:13 1994
³      '
³DECLARATIONS
³
³   M4 DEVICE ;
³   I PIN ;
³   J PIN ;
³   K PIN ;
³   L PIN ;
³   M PIN ;
³   CP PIN ; "CLOCK INPUT"
³   MR PIN ; "MASTER RESET (ASYN) INPUT"
³   R PIN ISTYPE 'COM' ;
³   S PIN ISTYPE 'COM' ;
³   Q4 PIN  ISTYPE 'REG,BUFFER' ;
³   Q3 PIN ISTYPE 'REG,BUFFER' ;
³   Q2 PIN ISTYPE 'REG,INVERT' ;
³   Q1 NODE ISTYPE 'REG,BUFFER' ;
³   Q0 NODE ISTYPE 'REG,BUFFER' ;
³
³   PS = [Q4,Q3,Q2,Q1,Q0] ; "STATE ASSIGNMENT"
³   AA = [ 0, 0, 1, 0, 0] ;
³   BB = [ 0, 1, 0, 0, 0] ;
³   CC = [ 0, 0, 0, 0, 0] ;
³   DD = [ 1, 0, 0, 0, 1] ;
³   EE = [ 1, 0, 0, 1, 0] ;
³   FF = [ 1, 0, 0, 1, 1] ;
³
³   C , X , P , Z = .C. , .X. , .P. , .Z. ;
³
³EQUATIONS
³
³   PS.AR = !MR ;
³   PS.CLK = CP ;
³


 page 26

³STATE_DIAGRAM PS
³
³   STATE AA :
³      [R,S] = [0,0] ;
³      CASE
³         !I : AA
³          I : BB
³      ENDCASE ;
³   STATE BB :
³      [R,S] = [0,0] ;
³      CASE
³         !J : BB
³          J : CC
³      ENDCASE ;
³   STATE CC :
³      [R,S] = [0,0] ;
³      CASE
³         I $ J  : DD
³         I !$ J : CC
³      ENDCASE ;
³   STATE DD :
³      [R,S] = [1,0] ;
³      CASE
³          K #  L : EE
³         !K & !L : DD
³      ENDCASE ;
³    STATE EE :
³       [R,S] = [0,1] ;
³       CASE
³         !M : EE
³          M : FF
³      ENDCASE ;
³   STATE FF :
³      [R,S] = [1,1] ;
³      CASE
³         1 : AA
³      ENDCASE ;
³
³DECLARATIONS
³
³   NS = [Q4,Q3,Q2,Q1,Q0] ; "NEXT STATE"
³


 page 27

³TEST_VECTORS
³
³   ([MR,CP,I,J,K,L,M] -> [NS,R,S])
³    [ 0, X,X,X,X,X,X] -> [AA,0,0]; "P IS 1"
³    [ 1, C,0,X,X,X,X] -> [AA,0,0]; "P IS 1"
³    [ 1, C,1,X,X,X,X] -> [BB,0,0]; "Q IS 1"
³    [ 1, C,X,0,X,X,X] -> [BB,0,0]; "Q IS 1"
³    [ 1, C,X,1,X,X,X] -> [CC,0,0];
³    [ 1, C,0,0,X,X,X] -> [CC,0,0];
³    [ 1, C,1,1,X,X,X] -> [CC,0,0];
³    [ 1, C,0,1,X,X,X] -> [DD,1,0];
³    [ 1, C,X,X,0,0,X] -> [DD,1,0]; "T IS 1"
³    [ 1, C,X,X,1,1,X] -> [EE,0,1]; "T IS 1"
³    [ 1, C,X,X,0,0,0] -> [EE,0,1]; "T IS 1"
³    [ 1, C,X,X,0,0,1] -> [FF,1,1]; "T IS 1"
³    [ 1, C,X,X,X,X,X] -> [AA,0,0]; "P IS 1"
³END
ÀÄ

The following changes were made:

input1 -> I
input2 -> J
input3 -> K
input4 -> L
input5 -> M

output1 -> R
output2 -> S

State Assignment:
   AA = [ 0, 0, 1, 0, 0] ;
   BB = [ 0, 1, 0, 0, 0] ;
   CC = [ 0, 0, 0, 0, 0] ; 
   DD = [ 1, 0, 0, 0, 1] ;
   EE = [ 1, 0, 0, 1, 0] ;
   FF = [ 1, 0, 0, 1, 1] ;

Inserting the true outputs of R & S

Inserting transition conditions

Changing attribute of Q2 from 'REG,BUFFER' to 'REG,INVERT'

Changing signal type of Q4,Q3 and Q2 from NODE to PIN

Adding test vector values


 page 28
                       Errors, Warning & Note Messages
                       -------------------------------

If any error occurs the program will abort execution. Some errors will
generate a help screen. this is the help screen:

------------------------------------usage-------------------------------------
  ASTATER <module> <in> <out> <con> <ff> /1|2 <state_name> <state_name>...
---------------------------------parameters-----------------------------------
  <module>.........................Module name \(file_name = module_name.ABL
  <in>...............................................Number of input signals
  <out>..............Number of output signals that are not flip-flop outputs
  <cond>......................Maximum number of relevant condition per state
  <ff>..................................................Number of flip-flops
  /1|2|3...................Machine type : /1 - Moore , /2 - Mealy , /3 Dummy
  <state><state>.........................A list of state names (two or more)
------------------------------------------------------------------------------

Here is a the list of errors that the program can report:

Error (1) : Define number of inputs.

            The number of inputs parameter is not defined correctly. It has to
            be an integer.


Error (2) : Define number of outputs.

            The number of outputs parameter is not defined correctly. It has
            to be an integer.


Error (3) : Define maximum number of transition conditions.

            The maximum number of outputs parameter is not defined correctly.
            It has to be an integer.


Error (4) : Define number of flip flops.

            The number of flip-flops parameter is not defined correctly. It
            has to be an integer.


Error (5) : Define machine type - moore (/1) or Mealy.

            The type of the machine is not defined correctly. It
            has to be a foreslash (/) followed by an integer.


 page 29

Error (6) : Machine type 'n' is an unknown machine_type.

            The type of the machine number is not defined correctly. It
            has to be a /1 (Moore) or /2 (Mealy).


Error (7) : Can't create file 'file_name' for writing.


Error (8) : Autonomous state machine is not supported.

            Autonomous transitions are supported, but only if they are not
            global. Read on previous text how to describe Autonomous
            transitions using the CASE..ENDCASE syntax.


Error (9) : Too many inputs.

            The maximum number of allowed inputs is 30.


Error (10) : Too many outputs.

             The maximum number of allowed outputs is 30.


Error (11) : Calculated number of transition conditions is too big.

             Defined number of transition conditions by user was zero. In a
             situation like this the software normally chooses a number
             that is equal to (2)^(number_of_inputs). In this case the
             calculated number is too big.


Error (12) : Too many transition conditions.

             The maximum number of allowed conditions is 4096.


Error (13) : No flip-flops in machine.

             A state machine with no Flip-Flops is not a state machine. It is
             a combinatorial system.


Error (14) : Too many flip-flops.

             A maximum of 30 flip-flops is allowed.


 page 30

Error (15) : 'n' states can not be assigned to only 'm' flip-flop(s).

             If for example you tried to declare tow flip-flops and six states
             it will not be possible to assign all six states to only four
             possible flip-flop combinations. This is because tow flip flops
             can decode only four states.


Error (16): Missing command line parameter(s).

            The minimum number of command line parameters must be at least 7:

            - number of inputs
            - number of outputs
            - maximum number of input conditions
            - number of flip-flops
            - machine type
            - a first state name
            - a second state name

Error (17): A Mealy type machine with no indirect outputs.

            Declaration of a mealy machine with no outputs is impossible
            because a mealy machine must have at least one output that depends
            on an input and not only on flip-flops.

Here is a list of Errorlevel that are set when exiting the program:

                     0 - Successful execution
                     1 - Bad numeric values of parameters
                     2 - Bad definition of parameters
                     3 - File Overwrite not allowed
                     4 - File write problems

Warnings & Notes will not be followed by aborting of execution. Warnings are
for making you pay attention because some thing bad might be going on. Notes
are only for informing you.


 page 31

Here is a list of Warnings that the program can report:


Warning (1) : Output file 'file_name' already exists.

              The user has an option to Overwrite it (by hitting the <Y> key)
              or to abort (hitting any other key)


Warning (2) : Zero outputs.

              Zero outputs is possible because all outputs of the machine can
              come directly from flip-flop outputs. In these cases it is
              possible for the designer to enter zero as the number of outputs
              (using the 0 command line parameter).

Warning (3) : The number of transition conditions was changed
              from 'm' to 'n'.

              If the number that defined transition conditions was zero, and
              the user defined a number of inputs that is greater then zero,
              the software will generate a canonical number of transition
              conditions = (2)^(number_of_inputs). This can be a large number.

              Other cases when this warning is reported are when the maximum
              number of defined state transitions is higher than it is
              possible with the defined number of inputs. For example if the
              the user defined tow inputs and five conditions a warning
              will be reported. It will tell you that the maximum number of
              conditions was decreased, to four conditions (the maximum
              possible number of conditions when the machine has tow inputs).


Here is a list of Notes that the program can report:

Note (1) : Machine type is Moore.

Note (2) : Machine type is Mealy.

Note (3) : Number of un-used states is: 'n'.

           The program calculates the difference between the largest number
           off possible flip-flop combinations and the actual number of states
           that was defined. The designer has to pay attention to these
           Hang-Up states. The machine can enter a Hang-Up state during
           power-up or as a result of noise.


 page 32

                         Limitations & Legal details
                         ---------------------------

The software is written by and Copyrighted to - Amos Zaslavsky. ASTATER is a
shareware. This means that you are allowed to copy it freely, and give copies to
other users.

       You are encouraged to do so, but with the following limitations:

- You must distribute ASTATER.EXE and ASTATER.DOC together and unmodified.

- You may not charge more than a minimal distribution fee (maximum $5.00)
  for covering disk price & postage of a diskette containing the files.

- You may not distribute ASTATER with or as part of other commercially sold
  software without written permission of the author.

- You are not permitted to sell this program for profit in any way, shape or
  form.

- If you like this program and use it regularly, the author would appreciate a
  contribution of $25.00, sent to the address below.

- As with all shareware, these contributions are the incentives for the
  author to continue developing this utility and other utilities.

- Contributors suggestions for enhancements will be considered in future
  versions.

- The author would appreciate being informed of any bugs !

- Future enhancements may include improovments like ABEL Symbolic-state style,
  entering input & output names, an interactive version, and other HDL's like
  PALASM and CUPUL or even C.


My address is:
                           Amos Zaslavsky
                           28 Berel Katzenelson st.
                           Haifa
                           Israel 32768

Telephone (voice):
                           972-4-230219



                                  Thank you.