PrintGL 1.54 HP-GL, HP-GL/2, and ADI Commands

                    (c) Copyright Ravitz Software Inc. 1990,1995


       Ravitz Software Inc.                              BBS/FAX 606-268-0577
       P.O. Box 25068
       Lexington, KY  40524-5068
       USA                                  Compuserve Cary Ravitz [70431,32]



       ------------------------------ Contents ------------------------------

       PrintGL Initial Information File ......................... PRINTGL.TXT
       PrintGL Documentation File                                 PRINTGL.DOC
       Introduction ....................................................... 3
       HP-GL Commands                                                       3
       HP-GL/2 Commands .................................................. 11
       ADI Commands                                                        13
       HP-GL Character Sets .............................................. 14


                                                                          p-3
       Introduction ---------------------------------------------------------

         This   document  is   a   description   of   the  subset   of  HP-GL
         (Hewlett-Packard  Graphics  Language), HP-GL/2,  and  ADI  (Autodesk
         Device  Interface) that is supported by  PrintGL.  If you  are using
         PrintGL to work with commercial  graphics software,  then  you  will
         probably not need this manual.  If you are writing graphics software
         you  will  find  here  the information  needed  to  make your output
         compatible with PrintGL.

       HP-GL Commands -------------------------------------------------------

         PrintGL's HP-GL specification is taken from the  programming manuals
         for the HP 7475A, ColorPro (7440/17440), and 7550A.  The 7550 manual
         is  the  best reference for HP-GL - HP  manual 07550-90001.  PrintGL
         supports  the 7475, and 7440/17440 command sets except for character
         set 8 (Katakana), digitize commands, output commands, the error mask
         command, and some device control  commands.  Supported commands  are
         listed below.  Commands that are not applicable to printing, such as
         pen velocity, are  considered supported  but are completely ignored.
         Commands that are not supported are flagged and then ignored.

         In addition, PG,  AF, ES, LO, the enhanced IW command, character set
         5, and proportional spaced fonts, from the 7550, are supported.  And
         forty pens are allowed instead of eight.

         In reading a plotfile, PrintGL ignores carriage returns, line feeds,
         and nulls  except where  they may be valid characters (LB,  SM,  DT,
         esc.), and ASCII EOF (026) is interpreted as an end of file mark.

         AA x_center , y_center , arc_angle [, chord_angle]

           Arc absolute - AA moves  the pen through  an arc,  starting at the
           current position, with the pen in the current up/down state.

         AF

           Advance full page -  AF  starts  a new plot.  PrintGL starts every
           page with the pen up at 0,0.

         AP

           Automatic pen pickup - IGNORED

         AR x_center_delta , y_center_delta , arc_angle [, chord_angle]

           Arc  relative  - AR moves the pen through an arc, starting at  the
           current position, with the pen in the current up/down state.

         AS

           Acceleration select - IGNORED                                     


                                                                          p-4
         CA character_set

           Designate alternate character set - See HP-GL Character Sets for a
           list of character sets.

         CI radius [, chord_angle]

           Circle - CI draws a circle centered at the  current position.  The
           current up/down state and position are unchanged by a CI command.

         CP [spaces , lines]

           Character plot  - CP moves the pen by character spaces (+ is along
           the text)  and lines  (+ is up), using  the current up/down state.
           Using no parameters is the same as a carriage return/line feed.

         CS character_set

           Designate standard character set - See HP-GL Character Sets for  a
           list of character sets.

         CV

           Curved line generator - IGNORED

         DF

           Default values -  This  sets  default  values  for  the  following
           commands: CA, CS,  DR, DT, ES, FT, IW, LO, LT, PA, PT, SC, SM, SL,
           SR, SS, TL.

         DI [run , rise]

           Absolute  character direction - DI sets the baseline direction for
           labels. The default is 1,0.

         DR [run , rise]

           Relative character direction - DR sets the  baseline direction for
           labels. Run and rise are a percentage of P2X-P1X and P2Y-P1Y.  The
           default is 1,0.

         DTt

           Define label terminator - The label terminator ends an LB command.
           The default is ASCII 003.

         EA x_opposite_corner , y_opposite_corner

           Edge  rectangle  absolute  - EA draws a rectangle  defined by  the
           current position and the parameters.  The pen position and up/down
           state are unchanged.

         EC

           Enable cutter - IGNORED                                           


                                                                          p-5
         EP

           Edge polygon - EP draws the current polygon edge.  Any pen up/down
           used in creating the polygon is respected in drawing the edge.

         ER x_opposite_corner_delta , y_opposite_corner_delta

           Edge  rectangle relative  -  ER  draws  a rectangle  with  corners
           defined by  the current position  and the command parameters.  The
           current pen position and up/down state are unchanged.

         ES [ space [, line]]

           Extra space  - ES adds to the  space between characters and lines.
           The  units  are in  character  cells  (1.5*width,  2*height).  The
           allowed range is -1 to 1. -.3333 causes characters to touch.

         EW radius , start_angle , sweep_angle [, chord_angle]

           Edge  wedge - EW draws a wedge centered  at the  current position.
           The current pen position and up/down state are unchanged.

         FP

           Fill polygon - FP fills the current polygon.  Pen up/down commands
           used in creating the polygon are ignored.

           There is a limit of 4000 fill line segments per polygon.

         FS

           Force select - IGNORED

         FT [type [, spacing [, angle]]]

           Fill type - These are the fill types.  Type 2 is identical to type
           1 for PrintGL.

             1  solid lines spaced at half the pen thickness (see PT command)
             2  unidirectional solid lines spaced at half the pen thickness
             3  lines at the specified spacing
             4  cross hatched lines at the specified spacing
             5  type ignored

           A spacing  parameter  of 0 sets  the  spacing  to 1%  of the P1-P2
           diagonal. Spacing is in x axis units (this is only relevant if the
           axes have different scaling).  PrintGL supports any  integer angle
           for fill. Cross hatched lines are at angle + 90.

         IN

           Initialize                                                        


                                                                          p-6
         IP [p1x , p1y [, p2x , p2y]]

           Sets scaling points P1 and P2 - IP sets the scaling points (P1 and
           P2) in plotter units.  P1  and P2 are used by several commands  to
           help with size independent plots.

         IW [x_lower_left , y_lower_left , x_upper_right , y_upper_right]

           Input window - IW sets a clipping window in plotter units. With no
           parameters, the clipping window is turned off.

           If  PrintGL's  /YE switch is  set and user  scaling  is on then IW
           parameters are in user units.  In this case the window is rescaled
           with an IP command, but any SC command locks the current window.

         LB..text..terminator

           Label - Labels use the current character set, based on CA, CS, SA,
           and SS commands. See HP-GL Character Sets for font specifics.

         LO [ position_number ]

           Label origin -  LO  sets  the  label  origins,  shown  below.  For
           positions 4..9  and  14..19  the  label buffer is  limited  to 150
           characters. The default is 1.

           13                     16                      19
              3......  .......  ...6...  .......  ......9
              .     .  .     .  .     .  .     .  .     .
           12 2     .  .     .  .  5  .  .     .  .     8 18
              .     .  .     .  .     .  .     .  .     .
              1......  .......  ...4...  .......  ......7
           11                     14                      17

         LT [pattern_number [, pattern_length]]

           Line  type  - PrintGL's line type patterns are close  to, but  not
           identical  to HP's.  Pattern  length is a  percentage of the P1-P2
           diagonal with a default of 4%  and a minimum of 4 dots for types 1
           and 2 and 16 dots for other types.  Negative (adaptive) line types
           from the HP 7550 are supported.

           no parameter  solid            1  .               .
                                          2  ________        ________
           0             dots at          3  ____________    ____________
                         endpoints        4  ____________  . ____________  .
                         only             5  __________  __  __________  __
                                          6  ______  __  __  ______  __  __
                                          7  __________  . . __________  . .
                                          8  ______  . __  . ______  . __  .

         PA [x , y] [, x , y] ...

           Plot absolute - PA sets absolute mode and optionally moves the pen
           in the current up/down state.                                     


                                                                          p-7
         PD [x , y] [, x , y] ...

           Pen down - PD sets the pen  down and optionally moves it with  the
           current absolute/relative mode.

         PG [i]

           New page - PG starts a new plot. The parameter is ignored. PrintGL
           starts every page with the pen up at 0,0.

         PM i

           Polygon mode - PM  0 starts polygon mode.  The current position is
           the first point in the polygon.

           PM 1 starts  a new  subpolygon.  The  position after the next  pen
           movement is the first point in the subpolygon.  The first pen move
           of a subpolygon is done with the pen up, regardless of the current
           up/down status.

           PM 2 ends polygon mode.

           PM  1 and PM 2 close  the current subpolygon with  the current pen
           up/down state. If used without first starting polygon mode (PM 0),
           PrintGL adds an implied PM 0 before processing the PM 1 or PM 2.

           The following  commands are accepted in polygon  mode: PM, PA, PR,
           PU, PD,  AA,  AR,  CI  (circles  are  automatically  prefixed  and
           suffixed by PM 1), and IN.

           The polygon buffer is limited to 1000 data points.

         PR [x_delta , y_delta] [, x_delta , y_delta] ...

           Plot relative - PR sets relative mode and optionally moves the pen
           in the current up/down state.

         PS

           Paper size - IGNORED

           PrintGL ignores PS. The paper size must be set with the /L option.

         PT [thickness]

           Pen  thickness - PT specifies twice the line spacing used in solid
           fills and may be from 0 to 5.0 mm.  It is reset to .3 mm with each
           SP command.

         PU [x,y] [,x,y] ...

           Pen  up  - PU  raises  the pen and optionally  moves  it with  the
           current absolute/relative mode.                                   


                                                                          p-8
         RA x_opposite_corner , y_opposite_corner

           Shade  rectangle  absolute  -  RA  fills  a rectangle with corners
           defined  by the current position and the  command parameters.  The
           current  pen  position  and  up/down  state  are  unchanged.   The
           rectangle edge is not drawn.

         RO [angle]

           Rotate coordinate  system - RO or RO0  sets up a normal coordinate
           system.  RO90, the only other allowed value, sets up a system that
           is rotated 90 degrees.  The type of rotation depends on  the paper
           size.  This command  does  not change the scaling points, so an IP
           command is useful after an RO.

           The HP 7475 specifies two different meanings for RO90 depending on
           the  paper  size (A/A4 or B/A3).  PrintGL  decides  which  type of
           rotation to do based on the sum of  the  print  window  width  and
           height.  If this sum  is  greater than 24 inches  then large paper
           rotation is used. Otherwise, small paper rotation is used.

           Small paper rotation:              Large paper rotation:

           RO 0             RO 90             RO 0             RO 90

             y --------    0,0 -------- y     0,0 -------- y    y --------
              |        |      |        |         |        |      |        |
              |        |      |        |         |        |      |        |
           0,0 -------- x    x --------          |        |      |        |
                                                 |        |      |        |
                                                 |        |      |        |
                                                 |        |      |        |
                                                x --------    0,0 -------- x

         RR x_opposite_corner_delta , y_opposite_corner_delta

           Shade  rectangle  relative -  RR fills  a rectangle  with  corners
           defined by  the current position and the  command parameters.  The
           current  pen  position  and  up/down  state  are  unchanged.   The
           rectangle edge is not drawn.

         SA

           Select alternate  character  set  -  SA  specifies  the  alternate
           character set as current.  The alternate character set  is  chosen
           with CA.

         SC [xmin , xmax , ymin , ymax]  or  SC xmin,xrto,ymin,yrto,2

           Scaling - SC sets user units. The units are defined by user values
           for  P1 (xmin,ymin)  and P2 (xmax,ymax)  or P1 and  the  ratio  of
           plotter to user units.  Using no parameters turns scaling off, and
           subsequent drawing is done in plotter units (1/1016 inch).        


                                                                          p-9
         SI [width , height]

           Character size absolute - SI sets the capital letter box width and
           height in centimeters.  Letter  spacing  is 1.5 *  width  and line
           spacing  is 2 * height.  Using no parameters with B or A3 paper is
           the same as  SI.285,.375  and  any  other  paper is  the  same  as
           SI.187,.269.

         SL [tan_angle]

           Character slant - SL sets  the character  slant.  The parameter is
           interpreted as the tangent  of  the angle from vertical.  Using no
           parameter sets the slant to 0 degrees.

         SM[c]

           Symbol mode  -  SM sets symbol mode, which centers the symbol mode
           character  at  any plotted point.  Any character from ASCII 033 to
           127 except ";" sets symbol mode.  Any other character turns symbol
           mode off.

         SP pen_number

           Select pen - SP selects a pen.  Using 0 or no parameter stores the
           pen  without selecting a new pen.  This is usually done at the end
           of a plot. PrintGL ignores any drawing with pen 0.

         SR [width , height]

           Character size relative - SR sets the capital letter box width and
           height as a percentage of  P2X-P1X and P2Y-P1Y.  Letter spacing is
           1.5 * width and line spacing is 2 * height. Using no parameters is
           the same as SR.75,1.5.

         SS

           Select  standard  character  set  -  SS   specifies  the  standard
           character  set as  current.  The standard character set  is chosen
           with CS.

         TL [positive_length [, negative length]]

           Tick length -  TL  sets the  tick lengths used by XT and  YT.  The
           parameters are lengths above  and  below the current position as a
           percentage of P2Y-P1Y for x-axis ticks and a percentage of P2X-P1X
           for y-axis ticks.

         UC [[pen_control ,] x_delta , y_delta] ...

           User character - UC specifies a  user defined character.  The  pen
           control number is 99 for pen down or -99 for pen up. Pen movements
           are relative, with x_delta in units of 1/4 the character width and
           y_delta in units of 1/8 the character height.

         VA

           Adaptive velocity - IGNORED                                       


                                                                         p-10
         VN

           Normal velocity - IGNORED

         VS

           Pen velocity - IGNORED

         WG radius , start_angle , sweep_angle [, chord_angle]

           Shade  wedge - WG fills a  wedge centered at the current position.
           The current  pen  position and up/down  state are  unchanged.  The
           wedge edge is not drawn.

         XT

           X-axis tick - XT draws a  vertical line, with  length specified by
           the  TL  command, at the current  position.  The  pen position and
           up/down state are unchanged.

         YT

           Y-axis tick - YT draws a horizontal line, with length specified by
           the TL  command, at  the  current position.  The  pen position and
           up/down state are unchanged.

         esc.(
         esc.Y

           Plotter on  - Esc.( and esc.Y turn the plotter  on.  This is  only
           relevant with the /YY option.

         esc.)
         esc.Z

           Plotter off - Esc.)  and esc.Z turn the plotter off. They are only
           effective with the /YY option. The plotter on and off commands let
           you  include comments or data to pass through to another device in
           the plotfile.  These are flagged as unsupported commands if /YD is
           set, as an indication that you should set /YY.

         esc.@, esc.H, esc.I, esc.M, esc.N, esc.R

           RS-232 device control commands - IGNORED                          


                                                                         p-11
       HP-GL/2 Commands -----------------------------------------------------

         PrintGL's HP-GL/2 commands include a subset of HP-GL/2 that lets you
         take  advantage  of  HP-GL/2's  pen  control  and  data compression.
         PrintGL's HP-GL/2 interpreter reads all of the HP-GL commands above,
         except  as noted below.  PrintGL acts like  an  HP-GL/2 plotter, not
         printer,  so  form feeds are done with the PG command  not the  form
         feed character.

         The  LA command  is not supported  - all  lines are drawn with round
         ends and round joints. And all clipping is done to the line center.

         When the  output format is  HP-GL  all of the  HP-GL/2 extended  pen
         control commands are  ignored.  The PT command  is needed to  ensure
         solid fills look good.

         AC [x , y]

           Anchor corner - AC  specifies the origin of  stroked fills.  It is
           handled even with HP-GL/2 off.

         BP

           Begin plot - BP is interpreted as PG;IN;.  It is handled even with
           HP-GL/2 off.

         CO "comment"

           Comment - This is handled even with HP-GL/2 off.

         CR [black_ref_red , green , blue , white_ref_red , green , blue]

           Color range - Sets the color ranges used by the PC command.

         FT [type [, spacing or shading [, angle]]]

           Fill type - When reading HP-GL/2, PrintGL accepts type 10 (shading
           percentage is the additional parameter) and 11 (raster fill number
           is the additional parameter).  Type 11 fills are converted to type
           10 with the shade level taken from the RF command.

           For solid  and  shaded fill types, to guarantee  good results, you
           must use the PW command to set the pen width  and  this width must
           magnify to no  more than 24 dots in the final image.  If either of
           these rules is broken, the fill may be striped rather than solid.

         IR [p1x , p1y [, p2x , p2y]]

           Set  scaling points relative - This is handled even if  HP-GL/2 is
           turned off.

         LT [pattern_number [, pattern_length, [mode]]]

           Line  type -  HP-GL/2 allows the  additional  parameter to  select
           relative (default)  or absolute  (in mm) pattern lengths.  This is
           handled even with HP-GL/2 off.                                    


                                                                         p-12
         NP [number]

           Number  of  pens  -  Sets  the number of pens.  This is ignored by
           PrintGL, which can handle up to 256 pens.

         PC [pen [, red , green , blue]]

           Pen color - Sets the pen color.

         PE

           Polyline encoded  - This  starts PE mode.  It is handled even with
           HP-GL/2 off.

         PT [thickness]

           Pen  thickness  -  The  command is  not  part  of  HP-GL/2 and  is
           generally ignored.  If the  output format is HP-GL  or if  you are
           using /Y1 (HP-GL/2 without pen  control) then PT is interpreted as
           it is in HP-GL.

         PW [width [, pen]]

           Pen width - Sets the  pen width.  After magnification, the maximum
           width is 24 dots. PW is ignored if the output format is HP-GL.

         QL

           Quality level - IGNORED for HP-GL or HP-GL/2

         RF [index [,width, height, pen [.. pen]]

           Raster fill - RF is not fully implemented.  Instead it is read and
           the  pattern is  converted to  a shade level.  Pen numbers and the
           specific  pattern are ignored.  The shade level  is saved for  use
           with fill type 11.

         RO [angle]

           Rotate coordinate system  -  When  reading HP-GL/2,  this  command
           accepts 0, 90, 180, and 270 and always rotates counter-clockwise.

         SV [type [, option1 [, option2]]]

           Screened vectors - Sets the shade level used  to draw lines.  Only
           modes 0 and 1 are supported.

         TR [mode]

           Transparency mode - Sets opaque or translucent mode.

         UL [index [,gap1, .., gapn]]

           User  line type - UL is not fully implemented.  Instead it is read
           and the pattern is converted  to one  of PrintGL's eight  standard
           line types. The gaps must be less that 256.                       


                                                                         p-13
         WU [type]

           Width units - Sets the units used by the PW command.

         esc% .. A

           Enter PCL or RTL mode -  This command is treated  like esc.).  All
           commands are ignored until the next esc% .. B.

         esc% .. B

           Enter  HP-GL/2 mode - This command  is treated like esc.(.  It  is
           required before any commands are interpreted.

       ADI Commands ---------------------------------------------------------

         With the /YA option PrintGL can read Autodesk ADI 4.0 vector plotter
         binary commands intermixed in the HP-GL. 1016 dpi coordinates or the
         current HP-GL user coordinates are assumed. The table shows each ADI
         command  and  the  equivalent  HP-GL  command   (as  interpreted  by
         PrintGL).  In  the ADI code column, the  code  number  and  "b"s are
         bytes,  and  "x" and  "y"  are words.  Eight line  types (other than
         solid) are supported.

           ADI command     ADI code     equivalent HP-GL

           begin plot      1 b          ignored
           end plot        2            PG;
           move            3 x y        PUx,y;
           draw            4 x y        PDx,y;
           pen             5 b          SPb;
           speed           6 b          ignored
           line type       7 b          if b=0 then LT; else LTb,2;
           raise pen       8            ignored
           abort           9            ignored                              


                                                                         p-14
       HP-GL Character Sets -------------------------------------------------

         PrintGL  supports all of the character sets that  are included  with
         the HP 7475 and 7440/17440 except Katakana, and adds character set 5
         and  the  proportional  spaced  fonts   from  the  7550.   PrintGL's
         characters are similar to but not identical to HP's.

            0  ANSI ASCII                           30  ISO Swedish
            1  9825 character set                   31  ISO Swedish For Names
            2  French/German                        32  ISO Norway Version 1
            3  Scandinavian                         33  ISO German
            4  Spanish/Latin American               34  ISO French
            5  Special Symbols (7550 extension)     35  ISO United Kingdom
            6  JIS ASCII                            36  ISO Italian
            7  Roman Extensions                     37  ISO Spanish
            8  Katakana - NOT SUPPORTED             38  ISO Portuguese
            9  ISO IRV                              39  ISO Norway Version 2

         The character sets specify a font for codes 033..127. Codes 000..032
         and 128..255 are independent of the character set and are all no ops
         except these.

           003  default label terminator
           008  backspace                 013  carriage return
           009  half backspace            014  select alternate character set
           010  line feed                 015  select standard character set
           011  reverse line feed         032  space

         Each of  the  character sets  is available as a proportional font by
         adding 10 to the set number.  The proportional  fonts  are kerned to
         improve  appearance (the character spacing is adjusted to compensate
         for  character shape).  Use the LO  command to simplify working with
         proportional fonts. To improve the appearance of large text, use the
         ES command to reduce the character spacing.

         Codes 65 to 81 in character set 5 are symbols designed to be used in
         symbol mode (SM command) or as one character labels.  When used in a
         label (LB command) these characters  are centered at the current pen
         position and leave the pen position unchanged.                      


                                                                         p-15
         The  HP-GL  characters  cannot  be  printed  with the standard ASCII
         character set.  The file PRINTGL2.CHR is  an HP-GL file that  can be
         used  to print  a  replacement for this page, showing  the character
         sets. Set up PrintGL with "magnification" "magnify: 1.0", "position"
         "plot:  0.0,0.0  at print origin", and "window/margins" "default" to
         print this plotfile.