MIDICARD.CFG - Info file

    Both SEND.EXE and ASK.EXE use MIDICARD.CFG file as their configuration
    file. File can be configured with Libra's 'Settings' option.
    The file contents are:

        1     MIDI Card type: 0=dumb MPU UART, 1=smart MPU, 2=GUS
        330   MIDI Base address in Hex. 330 should be the default for MPU.
              For GUS, if card base address is 220, the midi address
              would be 320.
        5     IRQ Number for GUS MIDI Port (MPU routines doesn't use IRQ)
        0     Count for delay loop in MPU send routines.

    Command lines: ([] must contain something, while <> can be left out)

        SEND.EXE [SysEx file name] <-q>
         ASK.EXE [midi channel (0..15)] [RAM bank (0..11)] [SysEx filename]

    RAM Banks are:
      0 RAM1
      1 RAM2
      2 ROM (same as ROM11)
      3 CARD
      4 RAM3
      5 ROM4
      6 ROM5
      7 ROM6
      8 ROM7
      9 ROM8
     10 ROM9
     11 ROM10