========================== Formatter 2.7 =============================
======================================================================
A  floppy  disk formatting program, written by Olaf 'Olsen' Barthel of
MXM.   Copyright,  © 1990 by MXM.  Shareware, all rights reserved.  No
guarantee  of  any  kind is made that the program(s) described in this
document are 100% reliable.  You use this material on your own risk.

============================== Purpose ===============================
======================================================================
The  standard  'format'  command surely does a brilliant job, since it
gets  around  with  any device driver and partitions of any size.  But
which  data media is formatted most oftenly?  Floppy disks (3½" format
hardwired  to  the  Amiga  computer)  of  course.  'Formatter 2.7' was
written  to fit the niche for fast(er) and user friendlier floppy disk
formatting  programs.   It  also  shows  how to format file systems in
general and how to get AmigaDOS to accept them.

=============================== Usage ================================
======================================================================
'Formatter  2.7'  can  be  called both from  Shell and Workbench. Note
that arp.library is required to run the program (Yuck!).

         The following command line parameters are supported:

Drive..........	This can be any disk drive from DF0:  through DF3:  as
		long  as it's really connected.  You will get an error
		message  if  the  disk  drive  cannot  be found in the
		current DOS mountlist.

NAME/K.........	The  name you wish the formatted disk to receive.  Any
		name longer than 31 characters will be truncated.

FAST/S.........	No  secret  fast formatting tricks yet, this option is
		similar to the 'QUICK' switch of the standard 'format'
		command:   if enabled only the root block and the boot
		block  of  the  disk  will  be rewritten (clearing all
		relevant  data).   If  your  disks  have  already been
		formatted clearing those blocks can save much time.

INSTALL/S......	If  you  want  to use the formatted disk as a bootable
		AmigaDOS disk,'Formatter 2.7' will install  it just as
		if you had used the AmigaDOS 'Install' command on it.

VERIFY/S.......	If   enabled,  each  write  access  to  disk  will  be
		verified,  i.e.  the disk blocks being written will be
		reread and compared with the source data.  Needless to
		say,  verification  slows  down  the  disk  formatting
		process  but  helps  to  tell  the good disks from the
		corrupt ones.

AUTOSTART/S....	If enabled, any disk inserted into the specified drive
		will be formatted automatically.  This saves some time
		if  lots  of  disks have to be formatted one after the
		other.

FFS/S..........	In  behalf of the new Kickstart release, the fast file
		system  is  supported  as well.  The disk receives the
		FFS IDs where the standard format program places them.

A  small  window  will pop up on the Workbench screen (right under the
mouse  pointer  if  possible).   The window will look like this (well,
roughly, I never claimed being a graphic artist, did I?):

      #X#Formatter2.6======================##|##
      |..   ..   ..   ..   ..   ..   ..   ..   | <- Track numbers
      ||    |    |    |    |    |    |    |    |
      |----------------------------------------|
      |                                        | <- Process indicator
      |------------+--+-------------+----------|
      | Auto start |  | Fast format |          | <- Some gadgets
      |------------+  +-------------+   Start  |
      |Verify write|  |Install disk |          | <- Some more gadgets
      |--------+-+-+------+-+-------++ +-------|
      |  DF0:  | |  DF1:  | |  DF2:  | |  DF3: | <- Drive selection
      |--------+ +--------+ +--------+ +-------|
      |         +------------------------------|
      | Name:   | Blank                        | <- Name string gadget
      |         +------------------------------|
      +----------------------------------------+

Control  should  be  intuitively  (why  shouldn't  it,  you're running
Intuition  anyway, aren't you?), if you've understood the command line
options  (to  which  the gadgets somehow correspond to) you should get
along with the rest of the program easily.

========================= Keyboard shortcuts =========================
======================================================================
To  make  life  easier,  each  gadget  in  the  control  window can be
enabled/toggled  via  keyboard.  These shortcuts are supported through
the Intuition menu attached to the 'Formatter 2.7' window.

About... 		(-> ?)	Display a short program info.
Auto start		(-> A)	Toggle auto-start option
Fast format		(-> F)	Toggle fast formatting
Verify write		(-> V)	Toggle write verification
Install disk		(-> I)	Toggle disk installation
Use FFS			(-> U)	Toggle FastFileSystem support

Drive DFx:		(1..4)	Select a disk drive to be formatted
Modify stepdelay	(-> M)	Modify the drive step delay rates
Start formatting	(-> S)	This should speak for itself
Quit			(-> Q)	Close the window and leave the program

====================== Formatter 2.7 vs. format ======================
======================================================================
'Formatter  2.7' is  limited to the 3½" drives  hardwired to the Amiga
computer, no other filesystems will be formatted (I haven't tried yet,
but  I  suppose that 5¼" drives won't be formatted either).  The disks
will  be  formatted  using  either the old standard file system or the
FastFileSystem.
	Formatting  time  is  well  below  the  time  'format'  needs;
formatting  a  disk without verify takes between 47 and 50 seconds, if
verify  is enabled formatting will take between 1:34 and 1:40 minutes.
	You  are  daring  and  adventurous?  Why not try to modify the
step  delay  rate  of your disk drives?  A little change can provide a
welcome  speedup.  The step delay rate usually is about 3000 ms.  Most
drives  will  feel  happy with about 2000 ms, some will even work with
step  rates below 1800 ms.  'Formatter 2.7' will bring up a small menu
allowing  you  to  adjust  the  step delay rate for all connected disk
drives.  These settings may be saved to/restored from disk.
	Caution:   You  are  doing quite dangerous things in modifying
the default values!

============================== Credits ===============================
======================================================================
Credits  go  to  Mark Rinfret for the very, very basic disk formatting
routines  employed  by his harddisk backup program.  It took some time
to  spy out the default disk format information.  The block types were
picked  up  both  from  Ralph Babel's 'Amiga Guru' book and the Bantam
AmigaDOS Programmers' manual.

=============================== Author ===============================
======================================================================
This  program was written by Olaf Barthel of MXM.  All files have been
placed in the public domain.  You may freely distribute this material,
even  a  small  copy  fee  is  okay  but  everything  which looks like
commercial distribution is forbidden.  Still you may use this material
for software development without giving credit to the original author.

The  program  and the accompanying files are distributed as Shareware.
If  you  like  'Formatter 2.7'  and use it frequently, please send at
least  7  US$  or  DM 15,- to cover our media costs.  If you enclose a
self  adressed  (and  stamped)  envelope (note:  Germany only, for all
other  countries  enclose  postage  separately)  you  will receive new
material and updates from MXM.

Send   new   program  revisions,  comments,  bug  reports,  donations,
unmarried   sisters,   non-poisoned   candy,  home-grown  palm  trees,
horoscopes, promising capital investments, etc.  to:

                          Olaf Barthel, MXM
                          Brabeckstrasse 35
                          D-3000 Hannover 71

                     Federal Republic of Germany

============ Revision history (most recent change first) =============
======================================================================
V2.7	The  name  of  the  disk inserted is displayed if autostart is
	enabled.   The  program  will  wait three seconds in which the
	'Stop'-button can be pressed to cancel the formatting process.

V2.6	The  data  verification  is  handled by the blitter.  Added an
	option  to  modify  the  step delay rate of all connected disk
	drives.

V2.5	This  version  will  also  format the sector label information
	available  for each disk track.  The additional 352 bytes will
	be  set to zero.  Window height and gadgets will be adapted to
	reflect the current system font settings.  Unfortunately, this
	does not affect the string gadget border.

V2.4a	Very  much  the same as Formatter 2.4, different only in parts
	of  the  user  interface.   The  older  release did not handle
	menus/gadgets correctly.

V2.4	The  bootblock  installation  process  obviously never worked,
	this  has  been  fixed.   Funny  enough,  if  several disk I/O
	requests   were   queued,  the  root  track  was  not  written
	correctly.  This occured particularly often on Turbo-Amigas or
	A3000  computers.   Holger  Lubitz  suggested  that  the disks
	should  be  validated  after  the  formatting process.  If two
	Formatters  were  run simultaneously, the disk validator could
	accidentally  modify the contents of the rootblock.  All known
	other errors have been fixed.

V2.3	The disk formatting and verification process have been sped up
	greatly.  The  disk  root  block  is written during formatting
	rather than after it.  The data on disk will be verified after
	the  disk  has been formatted and will start at track 79 going
	down to track 0.

	There   is   a  debug  switch  available  from  Shell.   If  a
	verification  error occurs, both track buffers will be written
	to RAM:.

V2.2	Added  a  menu  and  FastFileSystem  support.   Applied  small
	changes to the code to make the program work smoother.

V2.1	Removed  a  bunch of suspicious code passages which caused the
	various  gadgets  to  get  mixed  up  by the message broadcast
	system.

V2.0	A complete rewrite  of  the  original  program,  first  public
	release.

V1.0	A very limited disk formatting program.

                                  *

             Do only its possibilities make it an Amiga?

                        WHERE IS THE MAGIC ???