ZIP.DOC
                                   -------
                           Instructions for ZIP.COM
                   IBM PC Fast Serial File Transfer Utility
                             Version 1.21 (05/88)

                               (c)1988 E. Meyer

      Requires:  100% IBM PC compatible computers;  MS/PCDOS 2.x or 3.x


     ZIP is a tiny, fast utility to transfer files between two IBM compatible 
computers over an ordinary serial cable connection.  This is most useful when 
the computers don't share a common disk format, as in the case of a desktop PC 
with 5" drives and a laptop (or PS/2) with only a 3" drive.  ZIP is easier to 
use, and over 6 times faster, than any ordinary telcom program.

              Telcom programs: modem       2400 bps      0.3 K/sec
              Telcom programs: cable      19200 bps      2.3 K/sec
        --->  ZIP: cable                 115200 bps     14.1 K/sec

     Most computer manufacturers offer additional disk drives or other 
hardware accessories to provide access to data on both 3" and 5" disks; but 
these can cost hundreds of dollars.  They can also make a laptop computer a 
lot less than portable.  Direct serial connection isn't quite as fast, but it 
does allow a data rate of 115200 baud -- that's over 14K per second.

     There are commercial programs for this purpose (of which LapLink may be 
the best known).  I'm sure they work very well, and have many extra 
conveniences that ZIP lacks.  But even they are priced at $100 and up, which 
is far more than I was willing to pay.  ZIP transfers files just as well, and 
is free.


                                  BASIC USE

     Obviously, you will need a copy of ZIP.COM on both computers.  (You can 
accomplish this at 19200 bps using your serial cable, if both machines have 
telcom software with XMODEM protocol transfers.)

     ZIP makes transferring a file as easy as copying it from one disk to 
another.  To transfer any MSDOS file, once the cable is properly connected to 
the COM ports of the two computers, from any DOS prompt:

     (1) On the sending machine, type:        C>zip FILENAME
     (2) On the receiving machine, type:      C>zip
                                          or  C>zip DIRECTORY

(Don't try to hit RETURN at exactly the same time on both ends; this actually 
makes an initial handshaking error more likely.)

     The "FILENAME" you give can be a single file, or a GROUP specified by 
wildcards and/or commas (see examples below).  Each name may include a 
directory.  Each file will appear with the same name on the receiving end.  
As data is transferred you should see a blinking asterisk.  When you see the 
message "Verified", you know that the received copy exactly matches the 
original.

     The "DIRECTORY" may optionally be specified on the receiving end; 
otherwise, files are received in the current directory.  Note: the directory 
MUST end with either a colon ":" or a backslash "\", otherwise ZIP will think 
it's a FILE to SEND!  See examples below.

     ZIP can be aborted by pressing any key:
              (1) on either end, during initial handshaking
              (2) on sending end, during file transfer
                    (will abort once current file is finished)


                             SELECTING THE SPEED

     By default ZIP works at 115200 bps.  In case you should have trouble at 
this speed, ZIP has two command line options that request a slower speed:

              /M   = Use the moderate speed (57600 bps).
              /S   = Use the slow speed (38400 bps).

Naturally these must be specified on BOTH ends, if used.  You will see an 
additional note in the ZIP signon message, "Speed=_", indicating a slower 
speed has been selected.


                          SELECTING THE SERIAL PORT

     Most IBM computers have anywhere from one to four serial (RS232) ports.  
The first two, COM1 and COM2, are implemented at standard addresses (03F8, 
02F8); COM3 and COM4, if present, can vary from one computer to another.  To 
use them you will have to install the appropriate address in ZIP.COM (see 
below).

     ZIP has two command line options that you can specify (once, after any 
filename(s) present) on either end, to determine which of the two standard 
serial ports is used:

              /1   = Use the COM1 port.  (This is normally the default.)
              /2   = Use the COM2 port.

You will see a note in the ZIP signon message, "Port=____", giving the port 
address in use.


                                USAGE EXAMPLES

     C>zip \work\my         sends file C:\WORK\MY over COM1

     C>zip gort,klaatu /s   sends C:GORT, C:KLAATU over COM1 at slow speed

     C>zip my.* /2          sends all files C:MY.* over COM2

     C>zip                  receives files over COM1 into current directory

     C>zip \work\           receives files over COM1 into directory C:\WORK\

     C>zip d: /2            receives files over COM2 into directory D:



                              TECHNICAL DETAILS

     ZIP does full CRC (Cyclic Redundancy Checksum) verification on the 
received file.  Being designed for direct serial transfer at maximum hardware 
speed, ZIP is not compatible with other software, including ordinary telcom 
programs.  Do not disturb the cable when ZIP is running, as this may cause the 
program to stall, requiring a reboot of your computer(s).

     Be sure to use the SAME version of ZIP on both ends: the transfer 
protocol may have changed.  Otherwise, if you can't get ZIP to transfer files, 
your computer(s) or your cable are incompatible.  ZIP is written entirely in 
assembly language; it will only work on fully IBM compatible computers.  I 
have tested it myself on 8088 PC clones with clock speeds of 4.77 to 8 MHz; I 
rely on users' reports that it works well on more sophisticated systems.

     Serial cables can be wired in many different ways.  The one I use was 
labeled as an "IBM AT adapter", and had female connectors on both ends (one 
DB9, one DB25).  Any cable that doesn't work by itself should with a null 
modem adapter.  If you find that you need to build a cable, don't ask me for 
advice: I don't know any more about this than you do!


                            MODIFYING THE DEFAULTS

     If no command-line option is given, ZIP will use its built-in "defaults" 
for the serial port address and speed.  These values appear in ASCII form at 
the start of ZIP.COM, and can be modified to customize your copy of ZIP.  To 
get a quick look at the current settings, just enter:

                      A>type zip.com
                      __[Defaults: Port=03F8. Speed=F.]

     For the Port, you can use "03F8" (COM1), "02F8" (COM2), or whatever (see 
your computer manual for COM3 or COM4 port addresses).  The possible values 
for Speed are "F", "M", or "S".  Changes can be made with any patching 
utility, such as DEBUG.  Just change the data under "Defaults:" to whatever 
you require.  After modifying the defaults, you can still use any command-line 
options above to override them.
     Here is how the DEBUG session might look; we Display the default data, 
Enter 0"2"F8 in place of the 03F8 to change to a default of COM2, Display 
again to see the new value, Write the change to the file, and then Quit:

C:\WORK>debug zip.com
-d100,12f
xxxx:0100  EB 20 5B 44 65 66 61 75-6C 74 73 3A 20 50 6F 72   . [Defaults: Por
xxxx:0110  74 3D 30 33 46 38 2E 20-53 70 65 65 64 3D 46 2E   t=03F8. Speed=F.
xxxx:0120  5D 1A E8 A8 06 0D 0A 5A-49 50 20 31 2E 32 31 20   ]......ZIP 1.21
-e113 32
-d100,12f
xxxx:0100  EB 20 5B 44 65 66 61 75-6C 74 73 3A 20 50 6F 72   . [Defaults: Por
xxxx:0110  74 3D 30 32 46 38 2E 20-53 70 65 65 64 3D 46 2E   t=02F8. Speed=F.
xxxx:0120  5D 1A E8 A8 06 0D 0A 5A-49 50 20 31 2E 32 31 20   ]......ZIP 1.21
-w
Writing 0896 bytes
-q

     For further information on DEBUG see your MSDOS manual.  Please DO NOT 
distribute modified copies of ZIP.COM; this could confuse other users.  They 
are for your personal use only.


                          ZIP 1.2 TRANSFER PROTOCOL

     This information is provided for programmers interested in writing 
applications compatible with ZIP on other computer systems.  The version 1.2 
protocol may need to be modified with future development of ZIP.  All transfer 
takes place at 115200 bps (unless a slower speed is selected); be aware that 
very tight polling loops, minimal handshaking, and fixed packet size are 
needed to avoid loss of data at 115200 bps.

     The initial handshaking involves the receiver sending a version code byte 
(120 decimal, for 1.20) at intervals until it is acknowledged (ACK, 6 decimal) 
by the sender.  From this point on all data transfer is in fixed-size packets.
     The receiver, when ready, requests each packet by sending an ENQ (5 
decimal), and acknowledges correct receipt with an ACK.  Each packet has a 3- 
byte header, consisting of an SOH (1 decimal) and a 16-bit count to indicate 
the number of significant bytes in the packet; then 512 bytes of data; then a 
concluding ETX (3 decimal).
     The first packet contains the file name; an empty name packet signifies 
the end of the transmission.  Subsequent packets contain the file data; a 
packet that is less than full (count less than 512) signifies the end of the 
file.  One final packet contains the 16-bit CCITT CRC value for the entire 
file, the DOS time stamp word, and the DOS date stamp word, in that order.
     The receiver looks for the SOH and ETX bounding each packet, but does no 
further checking.  There are no timeouts.  No attempt is made to resend 
packets; under normal circumstances, transmission errors should not occur.  
Upon any serious error, a NAK (21 decimal) is sent to the other end before 
exiting to DOS.  Upon receipt of this signal, the other end also terminates.


                                ERROR MESSAGES

            <ERROR>  invalid command (probably illegal option).
    <OUT OF MEMORY>  less than 64K free RAM available.
         <TOO MANY>  global filespec includes too many files.
       <FILE ERROR>  trouble reading or writing a disk file.
     <COMM FAILURE>  transmission error; or, aborted at the other end.
        <CRC ERROR>  received file CRC did not match, bad transfer.
          <ABORTED>  you pressed a key.


                                   HISTORY

ZIP 1.0 (04/88) - trial release.  Worked on many systems.
    1.1 (04/88) - improved transmission algorithm; batch transfers allowed 
                 using wildcards and/or commas; receive directory option; 
                 original file time/date preserved.
    1.2 (05/88) - improved error handling; patchable default port also 
                 allows use of COM3,4; small bug fixes.
   1.21 (05/88) - slower speed options; fixed bug in initializing ports.


     ZIP and its documentation are (c)1988 E. Meyer, all rights reserved.  
They may be freely distributed, but not modified or sold for profit without 
my written consent.  The user takes full responsibility for any damages 
resulting from the use (or misuse) of this program.  Please report any 
problems encountered.

                 Eric Meyer
            427 N. Washington #4             CompuServe [74415,1305]
           Bloomington, IN  47401


         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  The P(s)L cannot de-
         bug programs over the telephone.

         Disks in the P(s)L are updated monthly, so if you did not get
         this disk  directly from the P(s)L,  you should be aware that
         the files in this set may no  longer be the current versions.

         For a copy of the latest monthly software library newsletter
         and a list of the 1,000+ disks in the library, call or write

                        The Public (Software) Library
                              P.O.Box 35705 - F
                           Houston, TX 77235-5705
                               (713) 665-7017