YPTF034.TXT
July 8, 1996
 
 
Fix Name:
---------
YPTF$034.SYS
 
 
Affected Machines:
------------------
760C,CD,L,LD,E,ED,EL,ELD
 
 
Applicable Operating Systems:
-----------------------------
This fix applies to the following Operating Systems:
 
  - DOS (with or without Windows 3.1 or 3.11)
  - Windows 95
 
 
Symptom:
--------
External trackpoint keyboard reset can occur while typing
on the external keyboard in the following configuration:
 
  - TP760 (all)
  - External Trackpoint keyboard attached through Y-cable or through 
    Dock.
  - Internal Trackpoint device enabled
 
When the reset occurs, the keyboard LEDs flash and some keystrokes are
lost.
 
 
Fix:
----
During boot, the YPTF$034.SYS driver checks for the presence of an 
external trackpoint device. If one is detected, it automatically disables
the internal trackpoint device.
 
 
Installation:
-------------
1. Copy YPTF$034.SYS to the directory of your choice on your hard
   disk drive.
2. Add the following line to the beginning of your CONFIG.SYS file:
 
         DEVICE=C:\path\YPTF$034.SYS
 
   where path indicates the directory where installed.
3. Ensure that the internal trackpoint is enabled using ThinkPad
   Features.
4. Shutdown and reboot for the change to take effect.