MIDI LIBRARY
                                ==== =======

WHAT IS THE MIDI LIBRARY?
---- -- --- ---- --------

The MIDI library is a standard Amiga disk-based library that provides 
multitasking access to MIDI resources such as the serial port.  The 
library is based around a "copying" message system so that a single 
message sent in can cause several messages to be sent back out.  Included 
as part of the library are tasks that convert serial I/O to MIDI messages 
which can be sent to any task that cares to listen.  This provides for 
unlimited sharing of the serial port by MIDI applications.

The need for such a service seems obvious in a multitasking environment.  
Without this sort of interface, two tasks trying to receive MIDI data 
from the serial port at the same time will exclude each other from 
working correctly.  Neither of them will get all the data they seek.  By 
using the MIDI library this problem is eliminated because there is only 
one task actually receiving data from the serial port.  Data is then 
distributed to all who are waiting for it.

A similar problem occurs with transmitting.  MIDI is based around a 
message system.  Each message contains a certain number of bytes and must 
be received intact to make sense to the receiver.  If two tasks try to 
transmit data to the serial port at the same time it is likely that the 
partial messages from each stream will merge producing disastrous 
results.  The MIDI library handles this by keeping messages intact, and 
again only one task is actually sending data to the serial port.

The MIDI library is intended for developers writing MIDI applications to 
use with their products.  The library takes care of all the grunginess of 
transferring MIDI data between your applications and the serial port.  
Instead of getting an unformatted stream of bytes your programs receive 
complete messages as asynchronous events.


Features
--------

     *  Unlimited MIDI message merging.

     *  Provides an interface for multiple MIDI applications to access 
        the serial port without conflict.

     *  Versatile MIDI filtering including message, channel, controller, 
        and SysEx ID number filtering.

     *  Exists as a standard disk-based Amiga library less than 10K in 
        size.

     *  Supports the full MIDI message specification including system 
        exclusive, 3 byte SysEx ID's, and MTC.

     *  Transfers MIDI packets using the Amiga Executive message system.

     *  Entirely written in Assembly.



OVERVIEW
--------

Tasks wishing to perform MIDI I/O create "source" and "destination" 
nodes.  These nodes are where messages are sent to and received from.  
Sources and destinations are then "routed" together.  Once connected in 
this manner, MIDI messages that are placed at the source node are 
distributed to destination nodes connected to that source.  Any number of 
source and destination nodes may exist at one time and any number of 
routes can be connected to a source or destination.

In addition to piping information along, a route processes MIDI data.  
The following operations can be performed by a route in any combination:

     Message filtering
     Channel filtering
     Channel offset
     Note offset
     Controller number filtering
     Sys/Ex id number filtering

In addition to nodes that the applications create there are "resident" 
nodes that launch built-in tasks.  Currently the only built-in tasks are 
for transmitting and receiving MIDI messages to and from the Amiga's 
serial port.

Covered in this remainder of this document are in depth descriptions of 
each of the major sections and concepts within the MIDI Library.  In 
general, there are a few rules you should keep in mind when using the 
MIDI Library (and all other Amiga resources):

     1. You must free any resource that you allocate (such as an MSource, 
        MDest, MRoute, MidiPacket, etc) when you are done with it.

     2. Only those fields within a structure that are explicitly 
        documented as writable should be treated as such.

     3. Any shared lists must be locked prior to examination (there are 
        various list locking functions described in the Inner Workings 
        section).

More detailed information about each MIDI Library function can be found 
in midi.doc.  Examine midi/midi.h (or midi/midi.i) for more information 
on the structures used within the MIDI Library and some handy constants 
not described in this document.

This document assumes that you have access to and are familiar with MIDI 
1.0 Spec v4.0 from the IMA.  Also, familiarity with C and the Amiga Rom 
Kernel are assumed.


LIBRARY
-------

Before using the MIDI library it must be opened like any other Amiga 
library.  The global symbol for the library base is "MidiBase".

          MidiBase = OpenLibrary (MIDINAME,MIDIVERSION);


The constants MIDINAME and MIDIVERSION are defined in the include file 
midi/midi.h.  MIDINAME is "midi.library" and as of this writing 
MIDIVERSION is 7.

When done using the library you should close it:

          CloseLibrary (MidiBase);


SOURCE AND DESTINATION NODES
------ --- ----------- -----

The MIDI source and destination nodes are the terminals for MIDI 
communication.  Messages are placed at a source to be distributed to 
destinations through whatever routes are connected to the source.

Nodes can be either public or private.  Private nodes can only be 
accessed by the task that created them.  Public nodes are available to 
everyone.  This way an application can perform it's own private 
communications or can be made available for routing in a patch bay.

The MIDI source is defined in "midi/midi.h" is follows:

          struct MSource {
               struct Node Node;
               struct Image *Image;
               struct MinList RPList;
               APTR UserData;
               UWORD RouteMsgFlags;
               UWORD RouteChanFlags;
          };

     Node
          An instance of an Exec Node used for linking public nodes into 
          the library's source list.  The ln_Name field is set for public 
          nodes to the name supplied by the caller.  ln_Type is set to 
          NT_MSOURCE for user MSource's or NT_RESMSOURCE for resident 
          MSource's.

     Image
          Points to an Intuition Image structure.  The image may be used 
          by graphics-based patch bay applications.  It is only used for 
          public nodes.  A NULL here indicates that the creator of this 
          node does not have an Image for it; patch bay programs may deal 
          with that as they see fit.

     RPList
          A linked list of MRoutePtr structures.  Each member of the list 
          is attached to an MRoute structure.  Scanning this list allows 
          you to determine what other nodes are connected to this one.

     UserData
          A generic pointer to any user extension data.  For resident 
          nodes this points to an instance of an MTaskInfo structure.

     RouteMsgFlags
     RouteChanFlags
          The sum of MsgFlags and ChanFlags, respectively, in all routes 
          attached to the MSource.  This is used internally by the 
          message distributor as a pre-check for which message classes 
          actually need to be transmitted.


In general you will only be concerned with a pointer to an MSource, not 
its contents.  It is not safe to touch anything in the MSource structure 
except UserData and then only if you created the MSource.  You are free 
to examine anything in the MSource structure such as RPList to determine 
the sort of route connections to the MSource.  If you plan to do this, be 
sure to read the section on the Inner Workings so that you will 
understand all the necessary precautions.

There are three functions dealing with MSource's:

     CreateMSource (name,image)
          Allocates, initializes, and returns a pointer to a new MSource 
          structure.  If name is non-NULL the MSource will be considered 
          public and will be linked into the library's source list.  
          Otherwise it will be considered private and won't be linked 
          into the library's source list.

     DeleteMSource (source)
          Removes and frees a source created by CreateMSource().

     FindMSource (name)
          Looks for a public MSource with the specified name.  If it is 
          found a pointer to it is returned.

See "midi.doc" for more thorough information on these and other MIDI 
Library functions.

The MIDI destination is defined in "midi/midi.h" is follows:

          struct MDest {
               struct Node Node;
               struct Image *Image;
               struct MinList RPList;
               struct MsgPort *DestPort;
               APTR UserData;
               struct MRouteInfo DefaultRouteInfo;
          };

These fields differ from an MSource

     Node
          The same as in an MSource except ln_Type is set to NT_MDEST for 
          user MDest's or NT_RESMDEST for resident MDest's.

     DestPort
          Points to an Exec MsgPort that is automatically created.  This 
          is where MIDI messages will arrive.  The port flags are set to 
          PA_SIGNAL so you can Wait() for something to arrive.  You don't 
          GetMsg() from this port, however.  See the messages section for 
          the proper way to read messages.

     DefaultRouteInfo
          Used as storage for the default connection options for this 
          MDest.  There is more on this subject in the Routing section.

The only field in this structure that you are likely to ever need to 
access is the DestPort since you will need to Wait() for messages to 
arrive there.  Otherwise, the same guidelines that apply to MSource's 
apply to MDest's:  don't tamper with anything other than UserData and 
only if you created the MDest.


As with MSource there are three functions dealing with MDest's that have 
essentially the same functions as those for MSource's:

     CreateMDest (name,image)
          Allocates, initializes, and returns a pointer to a new MDest 
          structure.  If name is non-NULL the MDest will be considered 
          public and will be linked into the library's destination list.  
          Otherwise it will be considered private.

     DeleteMDest (source)
          Removes and frees a source created by CreateMDest().  Also any 
          unread messages will be freed.

     FindMDest (name)
          Looks for a public MDest with the specified name.  If it is 
          found a pointer to it is returned.

     FlushMDest (dest)
          Disposes of any MidiPackets pending at the specified MDest.

At this point it is worth discussing the Resident Nodes currently 
available.  Resident nodes are public nodes that are always present in 
the public node lists and are physically part of the MIDI Library.  They 
can be routed to just like any other public node as will be described in 
the next section.  There are currently two resident nodes.

     name     type    description
     ----     ----    -----------
     MidiIn   source  Converts incoming data from the Amiga's serial port 
                      to MIDI Messages.  Any MDest's that you route to 
                      MidiIn will be able to receive messages from any 
                      MIDI devices connected to the serial port.

     MidiOut  dest    Converts MidiPackets to data sent out the Amiga's 
                      serial port.  Any MSource's that you route to 
                      MidiOut will then be able to transmit MIDI messages 
                      to devices connected to the serial port.  Any 
                      number of MSource's can be routed to it without 
                      fear of mangled data; messages are merged 
                      properly.  Each message sent to it will be 
                      transmitted to the serial port in the order 
                      received.


ROUTES
------

Routes are the "cables" that connect sources to destinations.  Nodes can 
have any number of routes connected to them and routes may be connected 
in parallel.  Additionally routes process MIDI messages as they are 
transferred along them.

The route structure and related structures are defined in "midi/midi.h" 
is follows:

The MRoute structure is the actual route structure managed by the 
library.  You probably need not be concerned with it's contents.


              struct MRoute {
                      struct MSource *Source;
                      struct MDest *Dest;
                      struct MRoutePtr SRoutePtr, DRoutePtr;
                      struct MRouteInfo RouteInfo;
              };

     Source
              Points to the source end or input to this route.  If is 
              NULL, then the source no longer exists.

     Dest
              Points to the destination end or output of this route.  If 
              is NULL, then the destination no longer exists.

     SRoutePtr
     DRoutePtr
              Instances of the MRoutePtr structure.  These are linked 
              into the source and destination RPLists respectively.  See 
              midi/midi.h for the actual MRoutePtr structure definition.

     RouteInfo
              An instance of an MRouteInfo structure.  This is a copy of 
              data supplied by the user.

When creating a route you have the option of using the default MRouteInfo 
structure within the target MDest or supplying your own.  This structure 
is what determines the behavior of a route:  filtering, event processing, 
etc.  There is a great deal of flexibility offered by this system.

          struct MRouteInfo {
               UWORD MsgFlags;
               UWORD ChanFlags;
               BYTE  ChanOffset;
               BYTE  NoteOffset;
               struct RIMatch SysExMatch;
               struct RIMatch CtrlMatch;
          };

     MsgFlags
          Flag bits indicating which messages are to be supported by this 
          route.  "midi/midi.h" contains MMF_ constants which may be ORed 
          together.  A value of MMF_ALL indicates all message types.

     ChanFlags
          Flag bits indicating which channels for channel messages are to 
          be supported by this route.  The least significant bit 
          corresponds to MIDI channel 1, the most significant bit 
          corresponds to MIDI channel 16.  A value of 0xffff indicates 
          all channels.

     ChanOffset
          A signed offset to be applied to all channel messages passed 
          through this route.  If the resulting channel is out of range 
          the message is not sent.

     NoteOffset
          A signed transposition offset to be applied to note on and off 
          messages in half steps.  If the resulting note number is out of 
          range the message is not sent.


     SysExMatch
          An instance of an RIMatch structure.  It allows you to specify 
          up to three one-byte System Exclusive ID numbers or one 
          three-byte ID to pass or block through this route.  If left 
          unset, all will be passed.  To use this the MMF_SYSEX bit must 
          be set in MsgFlags.  See below for more on this.

     CtrlMatch
          An instance of an RIMatch structure.  It allows you to specify 
          up to three controller numbers to pass or block through this 
          route.  If left unset, all will be passed.  To use this the 
          MMF_CTRL bit must be set in MsgFlags.

The RIMatch structure is used to specify up to three values to match.

          struct RIMatch {
               UBYTE Flags;
               UBYTE Match[RIM_MAXCOUNT];
          };

     Flags
          Indicates how the value(s) in Match should be treated.  A value 
          of 0 causes Match to be ignored.  A value of 1 to 3 is used to 
          specify how many one-byte values are contained in Match.  
          Without any other flags set, this indicates that only the 
          value(s) in Match will pass through this route.

          If the RIMF_EXCLUDE bit is set (OR with value of 1-3), the 
          logic is reversed such that all except those values in Match 
          are passed.

          SysExMatch only:  If the RIMF_EXTID bit is set, Match is 
          assumed to contain exactly one three-byte System Exclusive ID.  
          This may be combined with RIMF_EXCLUDE.

     Match
          Value(s) to match packed left to right.

In order to create a route you need to have a source pointer, a 
destination pointer, and optionally a properly filled out MRouteInfo 
structure.  The contents of your MRouteInfo is copied to the created 
route so you do not need to preserve it after creation.

There are several functions dealing with route management.  First a note 
about public nodes.  Since public nodes are available to other tasks 
besides the creator there needs to be a way to insure the validity of a 
given node between the time that someone finds it and the time that 
someone attempts to route to it.  There is a pair of functions to lock 
the node lists to prevent a node from being removed while you are dealing 
with it.  Additionally there are some special routing functions for 
dealing with public nodes that lock the lists for you.  Thus, there is 
route creation function for every permutation of public and private nodes.

          source    dest      function
          ------    ----      --------
          private   private   CreateMRoute
          private   public    MRouteSource
          public    private   MRouteDest
          public    public    MRoutePublic


     CreateMRoute (source,dest,routeinfo)
          Allocates and links a route into the specified source and 
          destination nodes.  The data pointed to by routeinfo, if 
          supplied, is copied to the new route structure.  This is 
          primarily used when both source and destination are private.

     MRouteSource (source,destname,routeinfo)
          Routes a source to a named public destination.

     MRouteDest (sourcename,dest,routeinfo)
          Routes a named public source to a destination.

     MRoutePublic (sourcename,destname,routeinfo)
          Routes a named public source to a named public destination.

In all cases above, you may supply your own MRouteInfo by passing a 
pointer to it or use the DefaultMRouteInfo within the target MDest by 
passing NULL instead.

The remaining functions deal with modifying and deleting routes:

     ModifyMRoute (route,newrouteinfo)
          Copies the contents of the new MRouteInfo structure to the 
          specified route.

     DeleteMRoute (route)
          Unlinks and frees a route.

     SetDefaultMRouteInfo (dest,newrouteinfo)
          Copies the contents of the supplied to MRouteInfo to 
          DefaultMRouteInfo in the supplied MDest.  This does not affect 
          any routes already connected to the MDest, only the template 
          for creating new routes.  You should only call this routine on 
          MDest's that you created.

You are responsible for deleting any routes you create even if the nodes 
it connected have been deleted.  You should not delete or modify anyone 
else's routes.


MESSAGES AND PACKETS
-------- --- -------

From the point of view of the MIDI Library, a MIDI Message is simply an 
array of UBYTEs containing a status byte as its first byte and any data 
bytes associated with that message.  With the exception of system 
exclusive, all messages are from 1 to 3 bytes in length.  A given status 
byte always has the same number of data bytes.  Messages never contain 
embedded Real Time status bytes as these are sent as separate messages.  
Messages never rely on running status so there will always be a status 
byte at the beginning of every message and there will never be more than 
one message worth of data bytes within that message.

System exclusive messages can be any length.  Also, the last byte in a 
system exclusive message is the EOX status byte used as a terminator 
(like '\0' in a C string).

The MidiPacket structure is built around the above MIDI Message concept.  
This structure is what arrives at the DestPort within an MDest.


          struct MidiPacket {
               struct Message ExecMsg;
               UWORD Type;
               UWORD Length;
               ULONG reserved;
               UBYTE MidiMsg[4];
          };

     ExecMsg
          The standard Exec Message node used to send to MsgPorts.

     Type
          An MMF_ message type value for the message contained in this 
          packet as returned by MidiMsgType().

     Length
          The length of this message in bytes as returned by 
          MidiMsgLength().

     MidiMsg
          The actual message as described above.  There always at least 4 
          bytes here, but the actual length that you should use is found 
          in Length.  Specifically, system exclusive packets more often 
          than not have more than 4 bytes here.

MIDI Messages (just the UBYTE array) are used for transmitting messages 
to an MSource.  MidiPackets are used for receiving messages at an MDest.  
MidiPackets are always created by the MIDI Library, never by you.  
Consider them entirely read-only.

These functions deal with receiving MidiPackets:

     GetMidiPacket (dest)
          Gets the first MidiPacket available at a destination and 
          returns a pointer to it.  If none are available NULL is 
          returned.  Any MidiPacket that you receive from GetMidiPacket() 
          should be freed with FreeMidiPacket().  See below for an 
          example packet reader.

     FreeMidiPacket (packet)
          Frees a MidiPacket received from GetMidiPacket().

     These functions deal with sending MIDI Messages:

     PutMidiMsg (source,msg)
          Places a single MIDI Message at a source for distribution.  
          Upon return you may recycle your msg buffer since its contents 
          has been copied to any MidiPackets that have been sent.  This 
          function assumes that you have constructed a valid MIDI message 
          as described above.  Invalid or undefined messages are ignored, 
          however an unterminated system exclusive message cannot be 
          detected and runs the risk of crashing the machine.

     PutMidiStream (source,fillbuffer,buf,bufsize,cursize)
          Converts an unformatted data stream into MIDI messages which 
          are then sent by calling PutMidiMsg().  See midi.doc for proper 
          usage.

These functions give you information about specific MIDI Messages:


     MidiMsgType (msg)
          Returns an MMF_ flag indicating the type message.  It returns 0 
          for invalid or undefined messages.

     MidiMsgLength (msg)
          Returns the number of bytes in a message.  For non-exclusive 
          messages this is the status byte + data bytes.  For system 
          exclusive messages it is status byte + data bytes + EOX.  0 is 
          returned for invalid or undefined messages.

These functions deal with receiving MIDI Messages w/o the packets and are 
primarily here for backwards compatibility.  They do little more than 
apply an offset from the beginning of the MidiPacket to the MidiMsg field 
and call the corresponding MidiPacket function.  It is not recommended 
that these be used in new code since they are less efficient from the 
point of the Library and the caller:

     GetMidiMsg (dest)
          Gets the first MIDI message available at a destination and 
          returns a pointer to it.  If none are available NULL is 
          returned.  Any message that you receive from GetMidiMsg() 
          should be freed with FreeMidiMsg().  See below for an example 
          message reader.

     FreeMidiMsg (msg)
          Frees a message received from GetMidiMsg().

Some additional notes about messages:

     1. Invalid or undefined status bytes are ignored.

     2. EOX is not considered a valid status byte on its own.  It is only 
        used to terminate system exclusive messages and will be ignored 
        if sent by itself using PutMidiMsg().

     3. Incomplete messages (such as system exclusive messages without a 
        manufacturer ID) are ignored.

     4. Note On messages with velocity == 0 are considered Note Off 
        messages.  MidiMsgType() will return MMF_NOTEOFF rather than 
        MMF_NOTEON for these.

     5. Controller numbers 121-127 are reserved for MIDI Mode Messages 
        and are treated as such.  MidiMsgType() will return MMF_MODE 
        rather than MMF_CTRL for these.


Here is a code fragment showing the recommended MidiPacket receive 
technique:

     domidi(dest)
     struct Dest *dest;
     {
          struct MidiPacket *packet;


          while (!done) {
               Wait (1L << dest->DestPort->mp_SigBit);
               while (packet = GetMidiPacket (dest)) {
                    /* process the packet: */
                    /*   perhaps examine packet->Type */
                    /*   or packet->Length */
                    /*   or the actual Message in packet->MidiMsg */
                         .
                         .
                    /* then free it */
                    FreeMidiPacket (packet);
               }
          }
     }


It's important to understand a little about how MidiPackets are 
allocated.  For all message types other than System Exclusive, 
MidiPackets are allocated from a pre-allocated pool of MidiPackets.  This 
is considerably quicker than having to call AllocMem() each time a 
MidiPacket needs to be allocated.  The pool gets initialized the first 
time you create a route.  If the pool becomes full, it gets extended but 
will not be pruned until someone calls FlushMDest() or DeleteMDest().  It 
gets totally expunged when the last user of the library calls 
CloseLibrary().

If you cache MidiPackets for any length of time, your memory may vanish 
to increase the size of the packet pool.  In order to get it back you 
will have to call FlushMDest().

System Exclusive packets are allocated using AllocMem() which explains 
why they are marginally slower to route than non-exclusive messages.


INNER WORKINGS
----- --------

This section is for the more adventurous MIDI programmer.  The 
information here is necessary for authors of patch bay or other route 
managing applications.

MidiBase
--------

The structure of the library base is defined in "midi/midibase.h".  This 
structure is strictly READ-ONLY.  You may examine fields with care as 
noted below.

          struct MidiBase {
               struct Library libnode;
               struct List SourceList, DestList;
               struct SignalSemaphore ListSemaphore;
               struct SignalSemaphore RouteSemaphore;
               BPTR SegList;
               APTR SysBase, DosBase;
               struct MinList SignalList;
          };

     libnode
          Standard Amiga library node.


     SourceList
          An Exec linked list containing all public MSource nodes.

     DestList
          An Exec linked list containing all public MDest nodes.

     ListSemaphore
          A SignalSemaphore for locking the source and destination 
          lists.  This is the semaphore used when you call LockMidiBase() 
          or UnlockMidiBase().  Exclusive access to lists is required 
          when managing or scanning either the source or destination 
          list.  It is not required for message propagation.  It is 
          required for route management only when a public node is 
          involved.

     RouteSemaphore
          A SignalSemaphore for locking the route system.  The routines 
          LockMRoutes() and UnlockMRoutes() use this semaphore.  
          Exclusive access to the routing system is required for message 
          propagation and route management.  It is not needed for 
          managing or scanning the node lists.  Use this with care since 
          it blocks message propagation.

     SegList
          A BPTR to the segment list for the library.

     SysBase & DosBase
          The library's pointers to Exec and Dos.

     SignalList
          The list of MListSignal nodes.

Only SourceList and DestList are likely to be of any interest to patch 
bay programmers.  The rest can be ignored.

These routines are useful for examining the base:

     LockMidiBase()
          Gains exclusive access to the source and destination lists.  
          Use of this will block anyone else from managing nodes or 
          scanning the lists.  Messages propagation is not blocked, 
          however.  Calls may be nested but each call must be matched 
          with a call to UnlockMidiBase().

     UnlockMidiBase()
          Relinquishes exclusive access to the source and destination 
          lists.

These routines are useful for examining the routes attached to a specific 
source or destination:

     LockMRoutes()
          Gains exclusive access to the route system.  Use of this will 
          block message propagation and route management.  Calls may be 
          nested but each call must be matched with a call to 
          UnlockMRoutes().

     UnlockMidiBase()
          Relinquishes exclusive access to the route system.


You shouldn't be very likely to need to lock the route system, however, 
and if you do it should only be to read the route lists not to modify 
anything.  A patch bay application should not use this approach to keep 
track of its routes.  Instead it must maintain its own list of routes.  
As long as everyone observes the rule of modifying only their own 
structures there shouldn't be any trouble.

Signals
-------

There is a system by which your task can be signaled when either of the 
public node lists changes.  This permits a patch bay system to be 
notified when it needs to redraw its display of available nodes.

          struct MListSignal {
               struct MinNode Node;
               struct Task *SigTask;
               UBYTE SigBit;
               UBYTE Flags;
          };

     Node
          Standard Exec MinNode used to link this MListSignal into 
          SignalList.

     SigTask
          Pointer to the task owning this MListSignal.

     SigBit
          Signal bit for this MListSignal.  Used to Signal() SigTask on 
          public node list change.

     Flags
          Flag bits describing which lists to watch for this signal.

This entire structure should be considered READ-ONLY.  The only field you 
should be concerned with examining is SigBit since you'll need to Wait() 
for that in order to find out when a list changes.  The signals do not 
accumulate and you don't know what changed when you receive one, just 
that something you were looking for has changed since you last received a 
signal.

These functions manage MListSignals:

     CreateMListSignal (flags)
          Adds your task to the list of those to be signaled when the 
          public node lists change.  Flags contains either MLSF_SOURCE, 
          MLSF_DEST or both depending on which list(s) you want to 
          monitor.  The function returns a pointer to an MListSignal 
          which you must keep and pass to DeleteMListSignal() when you 
          are done with it.  A signal bit is allocated for you when you 
          call this and is placed in SigBit.

     DeleteMListSignal (signal)
          Removes and frees an MListSignal allocated by CreateMListSignal.



Resident Nodes
-------- -----

As noted before there are some nodes that are always present.  They are 
created by the library when it is first loaded.  These nodes are attached 
to built-in tasks (actually AmigaDOS Processes) that are launched when 
the nodes are routed to.  There are currently only two resident nodes:  
one for receiving from the serial port and one for transmitting to the 
serial port.

     MidiIn   source  Launches a task called MidiIn running at +30 
                      priority when it is first routed to.  It receives 
                      data from the serial port and converts it to MIDI 
                      messages which are posted to its MSource node.  
                      Anyone with destinations routed to this node will 
                      receive MIDI messages from it.

     MidiOut  dest    Launches a task called MidiOut which also runs at 
                      +30 priority.  It is responsible for receiving 
                      messages from it's MDest node and sending them to 
                      the serial port.

Resident nodes can be identified by a node type value (in ln_Type) of 
NT_RESMSOURCE or NT_RESMDEST.  Resident nodes have an additional 
MTaskInfo structure attached to them that is pointed to by the UserData 
field in the MSource or MDest structure.

This rest of the information about resident nodes is provided merely for 
the curious and is not terribly useful.  Consider ALL of this stuff to be 
READ ONLY.  And be forewarned that it may change if necessary.  The 
MTaskInfo structure is defined in "midi/midibase.h".

          struct MTaskInfo {
               char *Name;
               WORD Pri;
               void (*Entry)();
               UWORD Stack;
               UWORD Sources;
               struct MNodeInfo *SourceList;
               struct Dests;
               struct MNodeInfo *DestList;
               struct SignalSemaphore Semaphore;
               UWORD UsageCount;
               struct MsgPort *TaskPort;
               BPTR Segment;
          };

These fields are defined within each task's module:

     Name
          Points to the name of the task.

     Pri
          The task's priority.

     Entry
          The start of the task's code.

     Stack
          The size of stack to allocate for the task.


     Sources
          The the number of MSource nodes defined for this task.

     SourceList
          Points to an array of MNodeInfo structures containing the 
          definition of this task's MSource nodes.

     Dests
          Is the the number of MDest nodes defined for this task.

     DestList
          Points to an array of MNodeInfo structures containing the 
          definition of this task's MDest nodes.

     These fields are managed by the library:

     Semaphore
          A signal semaphore for locking this MTaskInfo structure.  This 
          is only used when launching or shutting down this task.

     UsageCount
          The number of accessors to this task.  If it is non-zero the 
          task is running otherwise it is dormant.

     TaskPort
          Points to the message port used to communicate with the task.

     Segment
          A BPTR to a fake segment list necessary for CreateProc().  The 
          segment contains a jump instruction to the startup code for the 
          task.  The task's code is actually part of the library's 
          segment list.  This might be considered making use of 
          undocumented features, but as long as no one tries to 
          UnloadSeg() this segment (and no one should) there shouldn't be 
          any trouble.

The MNodeInfo structure referred to above is used to define the resident 
source or destination nodes attached to this task.  Tasks are not 
restricted to just one resident node, but that is the current usage.  
This structure is also defined in "midi/midibase.h".

          struct MNodeInfo {
               char *Name;
               struct Image *Image;
               APTR Node;
          };

     Name
          Points to the name of the node.  This shouldn't ever be NULL.

     Image
          Points to an Intuition Image structure for this node.  This may 
          be NULL (and currently is in all cases).

     Node
          Points to the node allocated for this MNodeInfo structure so 
          that the task can find it easily.



SERIAL I/O CONSIDERATIONS
------ --- --------------

The resident nodes that access the serial port do so by using 
serial.device - the standard device driver for the serial port.  
serial.device does however have a hard time receiving MIDI data at full 
speed, even with the SERF_RAD_BOOGIE flag set.  It occasionally loses a 
byte or two on larger transfers such as long system exclusive messages.  
I have heard that there are also similar problems when running at 19200 
baud, so it seems likely that some attention will be given to improving 
serial.device in future releases of the operating system (like v1.4).

In the meantime, it is strongly recommended that you make sure that you 
get what you expect when reading system exclusive messages from MidiIn.  
Use whatever error detection methods are appropriate for the data being 
transferred (like dump sizes or checksums).

Some sequencers use interrupt driven serial I/O for speed reasons.  
These, from what I've seen, do not suffer from the lost data problems 
that serial.device does.  I have given the matter of using my own serial 
interrupt handler some thought and these are my reasons for not doing so 
at this time.

     1. serial.device is the polite way of accessing the serial hardware 
        and it should be used whenever possible as it does provide a nice 
        interface to the hardware and is presumably compatible with any 
        future serial hardware that comes along.

     2. Serial interrupt handlers are exclusive:  only one task can own 
        the serial interrupts at a time.  Right now there are a few MIDI 
        applications that use serial.device directly for MIDI.  These do 
        not directly conflict with the MIDI Library so long as both are 
        not attempting to read or write data to the serial port at 
        exactly the same time.  If MIDI Library were to use its own 
        interrupt system, these types of applications will not be able to 
        access MIDI at all while someone is using MIDI Library.

     3. The problem does not appear bad enough (at least in my own 
        applications) to warrant it.

     4. Commodore will presumably fix the problem eventually.

     5. MIDI Library uses memory allocations occasionally during message 
        routing.  Interrupt code cannot call the memory allocator.  (This 
        can be worked around by implement the interrupt handler as simply 
        a queue that is read by a task which in turn calls MIDI Library)


CONCLUSION
----------

Hopefully this document has provided you with an understanding of the 
MIDI library and will enable you to make use of its features in your own 
MIDI applications.

Good luck.



COPYRIGHT AND DISTRIBUTIONS
--------- --- -------------

The MIDI Library is Copyright (c) 1987, 1988, Pregnant Badger Music.  All 
rights reserved.  The MIDI Library may be used in and included with 
commercial products with the following provisos:

     1. Pregnant Badger Music should be kept informed of your intent to 
        release products that make use of the MIDI Library so that we may 
        keep you informed of changes, updates, etc.

     2. The above copyright notice should be included somewhere in the 
        documentation accompanying any such commercial products.

Bill Barton
Pregnant Badger Music
1111 El Sur Way
Sacramento, CA  95864
(916) 487-9472

    Bix:  peabody
  PLink:  peabody