MCX11
                                          
                             MicroController eXecutive
                                      for the
                                 Motorola MC68HC11
                                          
                                    Version 1.3
            
            
            
            
                                         by
            
                             A.T. Barrett & Associates
                                 11501 Chimney Rock
                                Houston, Texas 77035
                                   (713)728-9688
            
            
                                    April 1990
            
            
                                  Support Contact:
                                          
                                     Mike Wood
                                     M/S OE319
                                   Motorola, Inc.
                           6501 William Cannon Drive West
                                Austin, Texas 78735
                                   (512)891-2717
            
            
            
            Neither Motorola,  Inc. nor  A.T. Barrett & Associates makes
            any warranty,  expressed or  implied, with  regard  to  this
            material including  but not  limited to  merchantability  or
            fitness for  a given  purpose.    The  information  in  this
            document is  subject to  change without  notice and  neither
            Motorola, Inc.  or A.T.  Barrett &  Associates  assumes  any
            responsibility for  any errors which may appear herein.  Nor
            shall Motorola,  Inc. or  A.T. Barrett & Associates bear any
            liability  for   use   of   this   material   with   respect
            compensatory,   special,   incidental,   consequential,   or
            exemplary damages.











                  MCX11 - MicroController eXecutive for the 68HC11
                                          
                                          
                                  TABLE OF CONTENTS
                                                      
            Section 1  Introduction                               Page
            
            1.1  Background and Features........................... 1-1
            1.2  MCX11 as a Software Component..................... 1-1
            1.3  Target Environment................................ 1-2
            1.4  Development Environment........................... 1-2
            1.5  Manual Format..................................... 1-2
            
            Section 2  MCX11 Functional Overview
            
            2.1  What Is MCX11..................................... 2-1
            2.2  Tasks............................................. 2-2
            2.3  Multitasking...................................... 2-2
            2.4  Priority and Scheduling........................... 2-2
            2.5  Intertask Communication and Synchronization....... 2-3
            2.6  Time based Functions.............................. 2-4
            2.7  Interrupt Service................................. 2-4
            
            Section 3  MCX11 Control & Data Structures
            
            3.1 Tasks.............................................. 3-1
            3.1.1 Task Identifier & Priority....................... 3-1
            3.1.2 Task State Table................................. 3-2
            3.1.3 Stack............................................ 3-3
            3.2  Semaphores........................................ 3-3
            3.3  Messages and Mailboxes............................ 3-5
            3.4  Queues............................................ 3-7
            3.5 Timers............................................. 3-8
            
            Section 4  Executive Service Requests (ESRs)
            
            4.1  Purpose........................................... 4-1
            4.2  Semaphore ESRs.................................... 4-1
            4.3  Message ESRs...................................... 4-2
            4.4  Queue ESRs........................................ 4-2
            4.5  Task Control ESRs................................. 4-2
            4.6  Time Based ESRs................................... 4-2
            
            Section 5  Alphabetical Listing of ESRs
            
            5.1  .delay.  -  Delay a Task for a Period of Time..... 5-2
            5.2  .dequeue.  -  Get an Entry from a FIFO Queue...... 5-4
            5.3  .enqueue.  -  Insert Data into FIFO Queue......... 5-6
            5.4  .execute.  -  Execute a Task...................... 5-9
            5.5  .pend.  -  Force a Semaphore to a PENDING State.. 5-11
            5.6  .purge.  -  Purge a Task's Timers................ 5-12
            5.7  .receive.  -  Receive a Message.................. 5-14
            5.8  .resume.  -  Resume a Task....................... 5-16
            5.9  .send.  -  Send a Message to a Task.............. 5-17
            5.10  .sendw.  -  Send a Message and Wait............. 5-19
            5.11  .signal.  -  Signal a Semaphore................. 5-20



                                        Page i






                  MCX11 - MicroController eXecutive for the 68HC11
                                          
                                          
                                  TABLE OF CONTENTS
                                                      5.12  .suspend.  -  Suspend a Task.................... 5-22
            5.13  .terminate.  -  Terminate a Task................ 5-23
            5.14  .timer.  -  Start a Timer....................... 5-24
            5.15  .wait.  -  Wait on Semaphore.................... 5-26
            
            Section 6  System Configuration
            
            6.1  System Configuration Concepts..................... 6-1
            6.2  MCX11 System Table Memory Requirements............ 6-1
            
            Section 7  Device Driver & Interrupts
            
            7.1  Driver Concepts................................... 7-1
            7.2  Interrupt Service................................. 7-1
            7.2.1 Interrupt Processing Variables................... 7-2
            7.2.2 Interrupt Processing Code........................ 7-4
            
            Section 8  Advanced Topics
            
            8.1  Other topics...................................... 8-1
            
            Appendix A  MCX11 Distributed Source Files............. A-1

































                                       Page ii






                  MCX11 - MicroController eXecutive for the 68HC11



                                     SECTION 1
                                          
                                    INTRODUCTION
                                          
                                          
            1.1  BACKGROUND AND FEATURES
            
            MCX11, the MicroController eXecutive for the MC68HC11, is an
            efficient  software   framework   for   embedded   real-time
            applications using  the Motorola  MC68HC11  microcontroller.
            Motorola, Inc.  makes MCX11 available free of charge via the
            Freeware Bulletin  Board System.   MCX11  is written  in the
            AS11 assembly  language  which  is  also  available  on  the
            Motorola Freeware BBS (512/891-3733).
            
            MCX11 provides  many features  which are designed to support
            real-time applications.  These features include:
            
                -     Multitasking for up to 126 tasks
                -     Pre-emptive task scheduling by priority
                -     Intertask communication and synchronization via
                       semaphores, messages, and queues.
                -     Support for timed operations
                -     Fast context switch
                -     Very small RAM and ROM requirements
                -     Fifteen Executive Service Request functions
            
            
            1.2  MCX11 AS A SOFTWARE COMPONENT
            
            MCX11 is  furnished in  AS11 source form and is downloadable
            via  a   modem  connection  to  the  Freeware  BBS.  In  its
            distribution  form,  it  is  not  executable.    It  may  be
            assembled separately  or with  the application  programs and
            any device  drivers peculiar  to the application.  MCX11 may
            be treated as any other software library.  The user need not
            know how  MCX11 performs  its functions internally.  Rather,
            the user  need only  know what  functions of MCX11 to use to
            achieve a  desired result.   Thus, MCX11 becomes much like a
            large scale  integrated circuit  component in  the hardware.
            Knowledge of what inputs produce what outputs is all that is
            needed to  use  the  "chip"  successfully.  Unlike  a  chip,
            however, MCX11  users are  provided with  the source code to
            the kernel  so that  they can exercise complete control over
            their applications.  With the  source code,  users may  even
            wish to extend the functionality of MCX11 by the addition of
            new services.
            
            This manual  is not meant as a tutorial on real-time kernels
            in general.  It is  intended to  explain  the  "inputs"  and
            "outputs" of  MCX11 as  a software  component of  the user's
            application.  In  an  effort  to  assist  the  user  in  the



            Copyright (c) 1989         Page 1 - 1          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            successful employment  of MCX11,  this manual will cover the
            following subjects:
            
                -     basic concepts of MCX11 design
                -     interfaces to the MCX11 services
                -     system generation procedure
                -     assembly procedure for MCX11 and application
                       source files
                -     procedure for merging MCX11 with the application
                       object files
            
            1.3  TARGET ENVIRONMENT
            
            MCX11 is  designed to operate in an embedded processor, that
            is, one whose functions are fixed within the application. No
            assumptions are  made about  the configuration of the target
            system.   It is the responsibility of the user to define the
            target environment  and to insure that all necessary devices
            have program support. No distinction is made between Single-
            Chip Operating  mode or  Expanded Multiplexed Operating mode
            in the design of MCX11. If there are special requirements in
            the application for functions related to a certain operating
            mode, it will be the responsibility of the user to add them.
            
            
            1.4  DEVELOPMENT ENVIRONMENT
            
            MCX11 development  requires a  computer compatible  with the
            IBM PC and having at least 256K bytes of RAM, 1 floppy disk,
            a keyboard, and a video monitor, an RS-232 compatible serial
            I/O port, a Centronics compatible parallel printer port, and
            a printer (preferably one which is Epson compatible). A hard
            disk  is   very  desirable   for  development   work.   This
            configuration is  needed to run the AS11 cross assembler and
            serve as a debug terminal to the target assuming MC68HC11EVM
            Evaluation Module is being used. Consult the EVM User Manual
            for specifics  on connection tp PC. Recommended software for
            the  development  environment  besides  MS-DOS  includes  an
            editor,  and   the  Kermit  communications  program  (public
            domain).
            
            
            1.5  MANUAL FORMAT
            
            Section 1 of this manual is simply an overview of MCX11.
            
            Section 2 gives the functional overview of MCX11.
            
            Section 3  details  the  organization  and  content  of  the
            various MCX11 control and data structures.
            




            Copyright (c) 1989         Page 1 - 2          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            Section 4  gives a  description  of  the  Executive  Service
            Requests (ESRs)  provided by  MCX11, subdivided  into  their
            classes.
            
            Section 5  gives an  alphabetical presentation  of all MCX11
            Executive Service Requests.
            
            Section 6  deals with  the configuration  and generation  of
            MCX11 systems.
            
            Section 7  discusses device  drivers and  interuupt  service
            routines.
            
            Section 8  presents technical information on advanced topics
            related to the use of MCX11.
            
            Appendices  round   out  the  specifics  of  necessary  user
            knowledge.
            




































            Copyright (c) 1989         Page 1 - 3          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                                     SECTION 2
                                          
                             MCX11 FUNCTIONAL OVERVIEW
                                          
            
            2.1  WHAT IS MCX11
            
            A real-time  executive provides  a software framework within
            which different  processes can  operate and  gain access  to
            various system resources.  Real-time systems usually consist
            of several  processes, or  tasks, which need to have control
            of  the  system  resources  at  varying  times  due  to  the
            occurrence of  external events.  These tasks  are at various
            times  competing   for  system  resources  such  as  memory,
            execution time, or peripheral devices. They range from being
            compute bound  to I/O  bound. Tasks which are I/O or compute
            bound   cannot be allowed to monopolize a system resource if
            a more important function requires the same resource.  There
            must be  a way  of interrupting the operation of the task of
            lesser importance  and granting  the needed  resource to the
            more important task.
            
            A multitasking   real-time  executive  promotes  an  orderly
            transfer of  control from  one task  to  another  such  that
            efficient usage  of the  computer's resources  is  achieved.
            Orderly transfers  require that  the executive keep track of
            the needed resources and the execution state of each task so
            that they  can be  granted to  each task in a timely manner.
            The key  word there is timely. A real-time system which does
            not perform  a required  operation at  the correct  time has
            failed. That  failure can have consequences which range from
            the benign  to the catastrophic. Response time to a need for
            executive services  and the  execution time of such services
            must be  sufficiently fast  enough  so  that  no  need  goes
            undetected.
            
            One way  to  achieve  timeliness  is  the  assignment  of  a
            priority to  each task.  The priority of a task is then used
            to determine  its place  within the sequence of execution of
            all tasks.  Tasks of  low priority  may have their execution
            pre-empted by  a task  of higher priority so that the latter
            can perform some time critical function.
            
            An event  can be any stimulus which requires a reaction from
            the executive  or a task. Examples of an event would include
            a timer  interrupt, an alarm condition, or a keyboard input.
            Events  may   originate  externally   to  the  processor  or
            internally from  within the  software.  An  executive  which
            responds to  these events  as  the  stimuli  for  allocating
            resources is  said to  be event  driven. If response time to
            any event   occurs  within a  period of  time which  can  be




            Copyright (c) 1989         Page 2 - 1          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            accurately defined and guaranteed, the executive can be said
            to be deterministic.
            
            By  these  definitions,  MCX11  is  a  deterministic,  event
            driven, multitasking, real-time executive.
            
            
            2.2  TASKS
            
            In MCX11, a task is a program module which exists to perform
            a  defined  function  or  set  of  functions.    A  task  is
            independent of  other tasks  but may establish relationships
            with other tasks.  These relationships may exist in the form
            of data  structures, input/output,  or other  constructs.  A
            task executes when the MCX11 task dispatcher determines that
            the resources  required by  the task are available.  Once it
            begins running,  the task has control of all of the system's
            resources.   But as  there are  other tasks in the system, a
            running task  cannot  be  allowed  to  control  all  of  the
            resources all  of the time.  Thus, MCX11 employs the concept
            of multitasking.
            
            
            2.3  MULTITASKING
            
            Multitasking appears  to  give  the  computer  the  apparent
            ability to  be performing  multiple operations concurrently.
            Obviously, the  computer cannot  be doing two or more things
            at once  as it  is a  sequential machine.  However, with the
            functions of the system segregated into different tasks, the
            effect of  concurrency can  be achieved.   In  multitasking,
            each task  once  given  operating  control  either  runs  to
            completion, or to a point where it must wait for an event to
            occur, for  a needed  resource to become available, or until
            it is  interrupted.   Efficient use  of the  computer can be
            obtained by  using the  time a task might otherwise wait for
            an event to occur to run another task.
            
            This switching  from one  task to another forms the basis of
            multitasking.  The result is the appearance of several tasks
            being executed simultaneously.
            
            
            2.4  PRIORITY AND SCHEDULING
            
            When several  tasks can  be competing  for the  resource  of
            execution time,  the problem is to determine how to grant it
            so that  each gets  access to  the system in time to perform
            its function.  The solution  is to assign a priority to each
            task indicative of its relative importance to other tasks in
            the system.   MCX11 uses a fixed priority scheme in which up
            to 126  tasks may  be defined.   Tasks  which have a need to



            Copyright (c) 1989         Page 2 - 2          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            respond rapidly  to events  are  assigned  high  priorities.
            Those which perform functions that are not time critical are
            assigned lower priorities.
            
            It is  the priority of each task that determines where it is
            to run  in the  hierarchy of  tasks.   When a  task may  run
            depends  on  what  is  happening  to  the  tasks  of  higher
            priority.   Tasks are  granted execution  time in  a  strict
            descending order  of priority.   While executing, a task may
            be interrupted  by an  event which  causes a  task of higher
            priority to be runnable.  The lower  priority task is placed
            into a  temporary state  of suspension and execution control
            is granted to the higher priority task.  Eventually, control
            is returned to the interrupted task and it is resumed at the
            point of  its interruption.   Thus,  when any  task is given
            execution control,  no higher  priority task  can  be  in  a
            runnable state.  This is a most important point to remember.
            When all  tasks are  in  an  unrunnable  state,  control  is
            granted to the null task.
            
            The null  task is  a do-nothing task which allows the system
            to run in an idle mode while waiting for an event which will
            resume or  start a  higher priority  task.  The null task is
            always the  lowest priority task in the system and is always
            runnable. It is an integral part of the kernel.
            
            
            2.5  INTERTASK COMMUNICATION AND SYNCHRONIZATION
            
            MCX11 provides  an environment whereby two or more tasks can
            communicate with one another.  The three major ways in which
            this  is  done  are  through  the  mechanisms  of  semaphore
            signalling, message  transmission, and  queues.  A semaphore
            is actually  a flag  which contains  information  about  the
            state of  the associated event.  Any event which is used for
            task synchronization  will be  associated with  a particular
            semaphore.   The occurrence  of  a  specific  event  can  be
            signalled by manipulating the semaphore associated with that
            event.
            
            Message transmission  involves the  logical transfer of data
            packets from  one task  to another.   These data packets are
            called "messages".   Messages  are sent  from one  task  and
            placed in  the "mailbox"  of the receiving task in the order
            of the  priorities of  the senders.   Messages may be of any
            format recognizable  by the sender and receiver and data may
            be passed  in either direction.  That is, it is possible for
            two tasks to alternate the roles of sender and receiver.
            
            A third  technique whereby  two tasks  can  communicate  and
            synchronize is  via  a  first-in-first-out  (FIFO)  queueing
            mechanism.   The queueing  techniques used  by MCX11 involve



            Copyright (c) 1989         Page 2 - 3          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            the physical  transfer (copying)  of data  packets from  one
            task to  another.   Task  synchronization  due  to  queueing
            operations is automatically performed by MCX11.
            
            
            2.6  TIME BASED FUNCTIONS
            
            An MCX11  system is  configured with an interval timer using
            the Real  Time Interrupt (RTI) clock as a peripheral device.
            The timer  permits  task  control  on  a  timed  basis.    A
            generalized scheme  using  one-shot  and  cyclic  timers  in
            conjunction with  semaphores is provided.  MCX11 efficiently
            manages multiple  timers using  an ordered  linked  list  of
            pending timer  events. A timer for an event is inserted into
            the  linked   list  in   accordance  with  its  duration.  A
            differential technique  is employed  so that  the timer with
            the shortest  time to expiration is at the head of the list.
            Timed  events  may  even  be  co-terminous.  Directives  for
            scheduling and  cancelling timed events are an integral part
            of the executive.
            
            
            2.7  INTERRUPT SERVICE
            
            Support  for  a  generalized  interrupt  service  scheme  is
            provided within  the MCX11  kernel. The   Interrupt  Service
            Routine (ISR)  code, however,  is provided  by the User. The
            rules for  writing interrupt  service routines that function
            with  MCX11   are  quite   simple  and  require  only  minor
            housekeeping  chores.   MCX11  also   provides  the   common
            Interrupt Service  Exit function.  This logic is used by all
            interrupts to  determine if  a context switch is in order as
            the result  of the interrupt. If no task switch is required,
            the  interrupted  task  is  resumed  at  the  point  of  the
            interrupt. If,  however, a  task switch  is  in  order,  the
            interrupted task's  context is saved, the new task's context
            is loaded and control is given to it.
            
            
















            Copyright (c) 1989         Page 2 - 4          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                                     SECTION 3
                                          
                          MCX11 CONTROL & DATA STRUCTURES
                                          
            
            In order  to understand  how MCX11  works and  how to  build
            real-time application  systems around it, it is necessary to
            understand how its various control and data structures work.
            This  section   describes   these   structures   and   their
            interrelationships. The descriptions will include:
            
                 -    tasks
                 -    semaphores
                 -    messages and mailboxes
                 -    queues
                 -    timers
            
            The MCX11  executive services  which deal with these classes
            of control  and data  structures  will  be  presented  in  a
            subsequent section.
            
            
            3.1 TASKS
            
            In a real-time application using MCX11, the functions of the
            system are  assigned to  various tasks. MCX11 supports up to
            126 tasks in a single system. The nature of each task is, of
            course, application dependent and left to the imagination of
            the system designer. However, there are attributes which all
            tasks share. These include:
            
                 -    a task identifier
                 -    a priority
                 -    a task state table
                 -    a stack
                 -    a mailbox
                 -    an entry point
            
            3.1.1 Task Identifier & Priority
            
            Each task is identified by a numerical identifier which is a
            number from  1 - 126. The task identifier, or number, serves
            as a  reference  during  executive  operations.  Task  1  is
            executed before task 2 which is executed prior to task 3 and
            so on.  Thus, the  task number  is inversely  related to the
            task's execution  priority. The  lower the  task number, the
            higher the  priority. MCX11  uses this  fixed task numbering
            scheme because  it is low in overhead and quite adequate for
            most applications.  The task  number permits a direct access
            to the  task's state table without the need for linked lists
            or other commonly used technique.
            



           Copyright (c) 1989          Page 3 - 1          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            3.1.2 Task State Table
            
            The state  table is  commonly referred  to as a Task Control
            Block (TCB).  A TCB  in MCX11  is contained  in two separate
            sections in  order to  minimize the  use of system RAM. Only
            those data about the execution state of the task are kept in
            RAM. Static  information about the task is kept in ROM. Both
            sets of  this TCB information are kept in arrays which allow
            direct access  to the  data based  on the  task number. This
            makes for very quick access without the commonly wasted time
            of searching a linked list.
            
            The RAM portion of the TCB contains only volatile data about
            the task and includes the following:
            
                 -    the execution state
                 -    the stack pointer
                 -    the first link in the task's mailbox
            
            Whenever the  MCX11 dispatcher  is looking  for  a  task  to
            execute, it  examines the execution state variable to see if
            the  task  is  runnable  or  not.  The  execution  state  is
            contained in a single byte and a value of $00 indicates that
            the task  is runnable.  Any other  content in the task state
            and the task is blocked from running.
            
            The stack  pointer contains  the address of the current top-
            of-stack.
            
            The first link in the task's mailbox contains the address of
            the highest  priority message  waiting to be received by the
            task. If no message is waiting, the pointer contains zero.
            
            The ROM part of the TCB contains:
            
                 -    the initial execution state
                 -    the entry point
                 -    the base address of the stack
                 -    the address of the RAM part of the TCB
            
            The initial  execution state  is  specified  by  the  system
            designer at  the time  of system configuration. This becomes
            the initial  content of the execution state. By specifying a
            value of  zero, the  task will be executed immediately after
            initialization   in    accordance   with    its    priority.
            Specification of a non-zero value will prevent the task from
            automatically starting execution after initialization.
            
            The entry  point is  the address  where the task is to begin
            execution.
            




           Copyright (c) 1989          Page 3 - 2          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            The base  address of  the stack  identifies that location in
            RAM where the task's stack begins.
            
            The address of the RAM part of the TCB table is included for
            completeness and  is sometimes  used to save time in setting
            up the address of the RAM TCB area.
            
            3.1.3 Stack
            
            Each task must have a stack on which the context of the task
            is saved  during those periods when the task is not actually
            executing. The  base address  of the  stack is stored in the
            ROM portion  of the  TCB. The  stack extends  from the  base
            address downward  in memory, i.e. towards address $0000, for
            a number  of bytes specified by the given stack size for the
            task. The  size of  each task's  stack is  dependent on many
            things such  as the  maximum  depth  of  nested  subroutines
            calls, the  maximum  amount  of  working  space  needed  for
            temporary variables,  and the  size of any stack frames used
            by the  task. At  minimum, the  size of the stack must allow
            for the  storage of  a complete  context which requires nine
            (9) bytes.  If XIRQ  is to  be used  in the design, an extra
            nine (9) bytes must be allocated to each task's stack due to
            the possibility of stacking an IRQ followed by an XIRQ. This
            is possible  because the  XIRQ  cannot  be  masked  and  can
            interrupt an IRQ interrupt service routine at any point.
            
            In addition to the stacks needed by the tasks, there is also
            the need  for a stack for MCX11. This system stack must have
            sufficient space  to handle the maximum number of interrupts
            possible  at  any  given  time,  less  one  interrupt.  Each
            interrupt requires  nine bytes. MCX11 functions have a worst
            case stack  requirement of  seven (7)  bytes  not  including
            those bytes required for the system stack.
            
            The sum  of all  of the  stack requirements  should  not  be
            allowed to exceed available RAM or there will be trouble.
            
            
            3.2  SEMAPHORES
            
            Semaphores (event  flags) are  used to synchronize two tasks
            to the  occurrence of  an asynchronous  event.  One task may
            need to  wait for  the other to reach a certain point before
            it can  continue.  Input/output operations are an example of
            this type  of synchronization.   For instance, when an input
            from an  external device  is desired by a task, it must wait
            for the  input event  to occur.  When the input operation is
            completed, the  device driver  signals that  the  event  has
            occurred  which  indicates  the  data  is  available.    The
            signalling  process  causes  the  waiting  task  to  resume,




           Copyright (c) 1989          Page 3 - 3          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            presumably to process the input data. The synchronization of
            the task with the event is done with the use of a semaphore.
            
            There are  several forms  that a  semaphore may  take in the
            design of  a real-time kernel.  MCX11 uses a basic semaphore
            construct that  is known to handle most events and is low in
            overhead.  A   semaphore  is   referenced  by   a  numerical
            identifier limited  to  a  value  from  1-255.  A  semaphore
            identifier of  zero has  a special  meaning. There are three
            different classes of semaphores used by MCX11 as follows:
            
                -     Named semaphores
                -     Task semaphores
                -     Queue semaphores
            
            Named semaphores  are those  normally referenced by the user
            in the  application code. Task and queue semaphores are used
            by MCX11  internally for  the purpose  of orthogonality with
            the semaphore  service functions. Task semaphores are always
            referenced by the identifier of zero (0) which is translated
            by MCX11  into the  proper number  for the  task  semaphore.
            Queue semaphores should never be referenced by the user lest
            undesirable results should occur.
            
            An MCX11  semaphore is a single byte (8 bits) which contains
            a value  representing one  of the  three possible  states in
            which it can exist.  These states are:
            
                -     PENDING
                -     WAITING
                -     DONE
            
            A PENDING state indicates that the event associated with the
            semaphore has  not yet  occurred and  is therefore  pending.
            The WAITING  state shows that not only has the event not yet
            occurred but  a task  is waiting for it to happen.  The DONE
            state tells  that the  event has occurred.  MCX11 semaphores
            have a  very  strict  state  transition  protocol  which  is
            automatically managed  by  MCX11.    The  permissible  state
            changes are shown below in Figure 3-1.
            
            
                            +------- PENDING------- +
                            |           ^           |
                            |   |------ |           |
                            v   |                   v
                            DONE<--------------- WAITING
            
                                     Figure 3.1
            
            




           Copyright (c) 1989          Page 3 - 4          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            If a  task attempts  to wait  on a semaphore which is in the
            DONE state,  the  wait  does  not  occur  and  the  task  is
            immediately resumed  (since the  desired event  has  already
            happened)  and  the  semaphore  state  is  changed  back  to
            PENDING.   If a  task attempts to wait on a semaphore in the
            PENDING state,  the state  of the  semaphore is  changed  to
            WAITING and  the task's  execution is  suspended  until  the
            event occurs.  An attempt  to wait  on a  semaphore which is
            already in the WAITING state can cause unpredictable results
            and should  not be  attempted. It  should  be  considered  a
            design error.
            
            If an  attempt is  made to  signal a semaphore which is in a
            PENDING state,  the semaphore is placed into the DONE state.
            As this  action does not concern any task, no further action
            is taken.   However,  if a  signal is sent to a semaphore in
            the WAITING state, the semaphore transitions to a DONE state
            and the  task waiting  on the  event is made runnable again.
            The semaphore  is then  automatically set  back to a PENDING
            state by MCX11.
            
            
            3.3  MESSAGES AND MAILBOXES
            
            Messages are  one of  the means by which data is transmitted
            from a  sender to  a receiver task. Every task running under
            MCX11  is  capable  of  being  both  a  message  sender  and
            receiver. Each  task is  assigned a "mailbox" into which are
            placed all  messages sent  to it. When a sender task sends a
            message, it is put into the mailbox of the receiver task. If
            two or more tasks are sending messages to a single receiver,
            their messages  are put  into the mailbox in strict sequence
            of their priorities, highest priority first.
            
            The content  of the  message is  not actually moved from the
            sender to  the receiver  when it  is sent. Instead, messages
            are linked  into a threaded list according to the priorities
            of their  senders. When the receiver requests receipt of the
            next  message,  its  address  is  returned.  This  technique
            guarantees the receiver that the highest priority message is
            received first.  It is  possible,  however,  to  temporarily
            suspend this  order by requesting only those messages from a
            particular sender.  This is  useful when it is desirable not
            to mix  messages  on  a  shared  resource,  for  example,  a
            printer.
            
            The mailbox  of a  task is  a threaded  (linked) list of all
            messages sent  to but  not yet  received by  that task.  The
            mailbox consists  of a pointer (link) to the message sent by
            the highest  priority sender.  That message is linked to the
            next highest  priority message  and it  in turn is linked to
            the third  highest priority message, and so on until the end



           Copyright (c) 1989          Page 3 - 5          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            of the  thread. The  last message  in a  task's mailbox will
            contain a NULL (value of zero) link.
            
            Messages may  be sent with or without waiting for a response
            from the  receiver. When  a task wants to send a message and
            wait until  the receiver  has processed the message, it will
            include a  semaphore number  as one  of the arguments in the
            MCX11   send  message  directive.  That  semaphore  is  then
            associated with  the event  of completed  processing of  the
            message. Once  the message is linked into the mailbox of the
            receiver task,  the sender  is put  into a WAIT state on the
            message processing complete event.
            
            The receiver  removes  the  message  from  the  mailbox  and
            processes it  according to  the content of the message body.
            When the  receiver no  longer needs  the data in the body of
            the message,  it signals  the semaphore  associated with the
            completion of  message processing   making  the sender  task
            runnable again  and, thereby,  allowing it  to continue  its
            operation.
            
            It should  be remembered  that the  body of  the message can
            also be  used by the receiver to send a response back to the
            sender. This  is a  very efficient  way of  passing data bi-
            directionally between two tasks with little overhead.
            
            If the  sending task  does not wish to wait on the action of
            the receiver  or if there is no response required, a message
            can be  sent without  waiting for  completion of processing.
            This makes  it  possible  for  a  sender  to  send  multiple
            messages to  a receiver,  or, simply do something else while
            the receiver  processes the  message. However, even though a
            message is  sent without  waiting for  the response,  it  is
            still possible   at  a later time for the sender to wait for
            the completion of processing event.
            
            If the  receiver has completed the use of the message by the
            time the  sender waits  for that  event,  the  sending  task
            continues operation  without interruption.  If the  receiver
            has not  yet completed processing of the message, the sender
            must wait  for the  event to  occur. When it does occur, the
            sender's operation is resumed.
            
            A message is a four-element structure set up in a contiguous
            area of  RAM. The  first three  elements of  the message are
            used by  MCX11 to  control the  transmission. The  user need
            only set up the content of the message body. The format of a
            MCX11 message is as follows:
            
                 -    Mailbox link (supplied by MCX11)
                 -    Task number of sender (supplied by                 
                      MCX11)



           Copyright (c) 1989          Page 3 - 6          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 -    Message semaphore number (optional)
                 -    Message body (supplied by User)
            
            The first  element in  the message  provides the link to the
            next message, if any, in the mailbox.
            
            The second  element is  the task  number of the sender. This
            field is  included so that the receiver task can selectively
            receive only those messages from a specified task.
            
            The third  element  of  the  message  contains  an  optional
            message semaphore  number.   Typically, when  a sending task
            wants to  send a  message and  wait until  the receiver  has
            processed the  message, it will include a non-zero semaphore
            number as  one  of  the  calling  arguments  for  the  MCX11
            directive. The  sending task  will  then  suspend  execution
            until the  receiver task  completes the  processing  of  the
            message content.  When the receiver no longer needs the data
            in the body of the message, it signals the message semaphore
            to notify the sender that it may continue processing.
            .
            The last  element, the  body, of  the  message  may  contain
            whatever data  is required  by  the  receiver  task  and  in
            whatever format.  It may  be fixed  or variable in length as
            required.
            
            
            3.4  QUEUES
            
            MCX11  supports   first-in-first-out  (FIFO)  queues  having
            single or  multiple bytes per entry.  The queues can support
            multiple producer/single  consumer service  but are  usually
            employed in  only a  single producer/single  consumer  mode.
            Queues are  referenced via  a numerical  identifier which is
            unique to  each queue.   Queue  numbers are  assigned in the
            system generation  procedure.    MCX11  queues  differ  from
            messages in  that the  actual entry  data  rather  than  its
            address is  entered into or removed from the queue.  Another
            difference  is   that  the   queue  entries   represent  the
            chronological order  of processing.  Also, the priorities of
            the sender  or receiver are not considered as with messages.
            Queues are  usually used  to handle  data such  as character
            stream input/output or other data buffering.  Queues require
            more overhead  as they  move the data from the source to the
            queue  or   vice  versa  but  they  also  provide  automatic
            synchronization  between   the  queue's   producer  and  its
            consumer.   It is  recommended that  they not  be used where
            high throughput rates are required.
            
            A queue  consists of  two parts:   the  queue header and the
            queue body.   The  queue header  contains  that  information
            needed by the MCX11 internal routines to enable them to move



           Copyright (c) 1989          Page 3 - 7          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            data into  and out of the queues properly.  The organization
            of the queue header consists of the following elements:
            
                -     Width, queue entry size (in bytes)
                -     Depth, maximum length (in entries)
                -     Current size of the queue (in entries)
                -     Put index (in bytes; MCX11 internal use)
                -     Address of queue body
                -     Queue not empty semaphore number
                -     Active semaphore number
            
            The first  three elements  are  defined  during  the  system
            generation process.   The  Current Size  and the  Put  Index
            fields are initialized to zero (empty). Both of these fields
            are  maintained  internally  by  the  MCX11  queue  handling
            routines. They should never be manipulated by a user task.
            
            Semaphores are used to signal internal events such as queue-
            not- empty  or   queue-not-full. The  semaphores  for  these
            events are allocated as a consecutive pair during the system
            initialization process.  The queue-not-full semaphore number
            is equal to the number of the queue-not-empty semaphore plus
            one. A  queue can have a semaphore active only for those two
            mutually exclusive  events. Consequently only the queue-not-
            empty semaphore  number requires  definition  in  the  queue
            header.
            
            The active  semaphore number  field in  the queue  header is
            used to  contain the number of the semaphore associated with
            one of  the two possible events. If the queue is empty and a
            task attempts to remove an entry, the active semaphore field
            in the  queue header  is set  to contain  the number  of the
            queue-not-empty semaphore. Conversely, if a task attempts to
            put an  entry into a queue which is already full, the active
            semaphore field  is set  to contain the number of the queue-
            not-full semaphore.
            
            By use  of these  semaphores, it  is possible  to send  data
            between tasks  asynchronously but without the worry of over-
            running the queue.
            
            
            3.5 TIMERS
            
            In the descriptions of time based functions to follow in the
            succeeding sections,  it will be important to understand the
            conventions used  by MCX11.  All timers in MCX11 are 16-bits
            long. The  two time units used internally by MCX11 are ticks
            and tocks.   A  tick gives  the amount of time between clock
            generated system  interrupts, or  equivalently,  the  period
            between clock interrupt service requests.
            



           Copyright (c) 1989          Page 3 - 8          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            A tock  is an  integral number of ticks and is the time unit
            used by  all of  the time dependent functions in MCX11.  The
            tick frequency  of the  RTI clock  is set  during the system
            initialization process but was determined, as was the number
            of ticks  per tock,  by the  system  designer  during  MCX11
            system configuration.
            
            As an  example, suppose  the hardware clock is configured to
            cause interrupts every 25 milliseconds and that 0.25 seconds
            (250 milliseconds)  is the time most convenient interval for
            timing events  in the application. In order to determine the
            number of ticks per tock, simply divide the desired duration
            of the  tock (250  ms) by  the duration  of a  tick (25 ms).
            Thus, in this case, 1 tock = 10 ticks.
            
            Timer values  are defined  as  the  number  of  clock  tocks
            required to  form the  needed amount  of time.   If  a timer
            value is  positive, it  is used  only once (one-shot timer).
            However, if  the value  is negative,  it is used as a cyclic
            timer having  a period  equal to  the 2's  complement value.
            For example,  if a  clock tock  equals 250  milliseconds,  a
            timer value  of 20  would produce  a once-only  period of  5
            seconds.   If the  timer were  -20, the  period is  still  5
            seconds but the timer is cyclic.
            
            All timed  event operations  and data structures are handled
            by MCX11. A task should not attempt to manipulate any of the
            timer related control or data structures.
            


























           Copyright (c) 1989          Page 3 - 9          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                                     SECTION 4
                                          
                         EXECUTIVE SERVICE REQUESTS (ESRS)
                                          
            
            4.1  PURPOSE
            
            Executive Service  Requests (ESRs)  are the functions that a
            real-time kernel  performs and  serve to give it its flavor.
            This  section   will  describe  the  classes  of  the  MCX11
            directives.  The directives are divided into five classes as
            follows:
            
                -     Semaphores
                -     Messages
                -     Queues
                -     Task control
                -     Time based
            
            A brief  functional description of each ESR within the class
            is given  along with their respective calling arguments. The
            calling arguments  needed  for  each  ESR  appear  below  in
            parentheses. Where  two or more arguments are required, they
            are separated  by commas.  These are  not the actual calling
            sequences but  are for  purposes of explanation only. Actual
            calling sequences are given in Section 5.
            
            In the  paragraphs below,  the ESR function name is enclosed
            within two  periods. This  will be  the convention  used for
            MCX11 to denote an ESR. The following abbreviations are used
            below for the arguments:
            
                -     SEMA      Semaphore number
                -     TASK      Task number
                -     QUEUE     Queue number
                -     TOCK      Timer value
                -     PNTR      Address pointer or data value
                -     MSG       Message address
            
            4.2  SEMAPHORE ESRS
            
            A complete  set of  directives for  managing  semaphores  is
            provided by MCX11.
            
            
            .wait. (SEMA)       wait for a specific sema to be signalled
            .signal. (SEMA)     signal semaphore
            .pend. (SEMA)       reset semaphore state to PENDing
            
            





            Copyright (c) 1989         Page 4 - 1          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            4.3  MESSAGE ESRS
            
            The message directives provide a means of transferring large
            amounts of  data between  tasks with  minimal overhead since
            only pointers  (addresses)  are  passed.    Message  receipt
            acknowledgement is  also provided  for task synchronization.
            The format  of a  MCX11 message  and function prototypes are
            noted.
            
            .send. (MSG,TASK)        send message to a task
            .sendw. (MSG,TASK,SEMA)  send & wait acknowledgement
            .receive. (TASK)         receive message
            
            
            4.4  QUEUE ESRS
            
            Queue directives  provide a  means of  passing multiple byte
            packets of  information between  tasks with  automatic  task
            synchronization of queue full and empty conditions.
            
            .dequeue. (QUEUE,PNTR)  remove entry from queue
            .enqueue. (QUEUE,PNTR)  insert entry into queue
            
            
            4.5  TASK CONTROL ESRS
            
            The task  control directives provided by MCX11 allow for low
            level  complete   control  of  tasks  and  their  respective
            interactions.
            
            .resume. (TASK)         resume specific task
            .suspend. (TASK)        suspend specific task
            .terminate. (TASK)      terminate specific task
            .execute. (TASK)        execute task from starting point
            
            
            4.6  TIME BASED ESRS
            
            The time based directives provide for the synchronization of
            tasks with  timed events.   In  addition, a generalized time
            based  semaphore   scheme  for   more  advanced  time  based
            requirements is provided.
            
            .delay. (TASK,SEMA,TOCK)  delay task
            .timer. (TASK,SEMA,TOCK)  schedule timer for task/sema
            .purge. (TASK,SEMA,PNTR)  purge timer for task/sema
            








            Copyright (c) 1989         Page 4 - 2          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                                     SECTION 5
                                          
                            ALPHABETICAL LISTING OF ESRs
                                          
            
            In  the   pages  to  follow,  each  ESR  will  be  shown  in
            alphabetical order.   Each  ESR will  be given in a standard
            format:
            
            Name - brief functional description
            
            CLASS
            
                 One of the five ESR classes of which it is a member.
                 
            SYNOPSIS
            
                 The prototype  declaration including  argument  typing.
                 The decimal  value of  the function code is enclosed in
                 brackets [xx].
            
            DESCRIPTION
            
                 A description  of what  the ESR  does, data types used,
                 etc.
                 
            CALLING SEQUENCE
            
                 The formal  AS11 calling  sequence  for  the  ESR.  The
                 following notations will be used:
                 
                      ACCA = Accumulator A, 8 bits
                      ACCB = Accumulator B, 8 bits
                      IX = Index register X, 16 bits
                 
            RETURN VALUE
            
                 A description of the return values from the ESR.
                 
            EXAMPLE
            
                 One or  more typical ESR uses.  The examples assume the
                 syntax of AS11 cross assembler.
                 
            SEE ALSO
            
                 List  of   related  ESRs  that  could  be  examined  in
                 conjunction with the current ESR.







            Copyright (c) 1989         Page 5 - 1          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.1  .delay.  -  DELAY A TASK FOR A PERIOD OF TIME
            
            CLASS
            
                 Timer
            
            SYNOPSIS
            
                 .delay. (TASK,SEMA,TOCK)       [13]
            
            DESCRIPTION
            
                 The delay  directive places  the specified  task into a
                 Wait state  for the  period defined  by the TOCK value.
                 TASK is  a task  number in the range of 1-126. Or, TASK
                 may be 0 if the reference is to SELF. Thus, a task need
                 not know  its own  task number  to schedule a delay for
                 itself. SEMA  is the  semaphore number  associated with
                 the  expiration  of  the  timer.  It  may  be  a  named
                 semaphore if  its number  > 0.  Or, it  may be the task
                 semaphore of  the calling task if it is specified as 0.
                 TOCK is  a 16-bit timer. If TOCK is > 0, the timer is a
                 one-shot. If  TOCK <  0, the  timer is  cyclic. Caution
                 should be  exercised when  scheduling delays  for other
                 tasks.
            
            CALLING SEQUENCE
            
                 ACCA = Task number (0 if SELF)
                 ACCB = Semaphore number (0 if Task's semaphore)
                 IX = Number of clock tocks to delay
                 swi
                  FCB  .delay.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 Assume that  the RTI  is used  as the time base using a
                 2**23 crystal  and the  clock TICK  is  defined  to  be
                 15.625 msec.  Further assume that there are 8 TICKS per
                 TOCK so  that a TOCK is 125 msec. If a 2.5 sec delay is
                 desired for  the calling  task using a named semaphore,
                 TIMEOUT, the request would appear as:








            Copyright (c) 1989         Page 5 - 2          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 
                 TOCK      equ   8
                 TOCKTIME  equ   1000/8         TOCKTIME = 125 msec
                 TIMEOUT   equ   3              Named semaphore #3
                           .
                           :
                           clra                 Task is self (ACCA=0)
                           ldab  #TIMEOUT       Semaphore = TIMEOUT
                           ldx  #2500/TOCKTIME  Timer = 20 TOCKS
                           swi
                            FCB  .delay.
                           .                    Point of continuation
                 
                 The requesting  task would  be put into a WAIT state on
                 semaphore TIMEOUT  while the  2.5 sec  clock runs down.
                 When it  expires, TIMEOUT  would be  signalled and  the
                 task would  continue at  the instruction  following the
                 FCB declaration.
            
            SEE ALSO
            
                 .timer., .purge.

































            Copyright (c) 1989         Page 5 - 3          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.2  .dequeue.  -  GET AN ENTRY FROM A FIFO QUEUE
            
            CLASS
            
                 Queue
            
            SYNOPSIS
            
                 .dequeue. (QUEUE,PNTR)       [7]
            
            DESCRIPTION
            
                 Dequeue is  used to get an entry from a FIFO queue. The
                 number of bytes in the entry is determined by the Width
                 entry in  the Queue  Header. If the queue is empty, the
                 calling task  is placed into an EVENT WAIT state on the
                 queue-not-empty semaphore.   If the queue is not empty,
                 the oldest  entry in  the queue is removed and returned
                 to the  calling task. If the size of the queue entry is
                 greater than two bytes, the returned data is in the RAM
                 area beginning at the address specified by PNTR. If the
                 queue entry  is one  or two  bytes, PNTR is ignored and
                 the entry is returned in one or two registers.
            
            CALLING SEQUENCE
            
                 ACCA= Queue number
                 IX = Destination address of queue entry if size > 2
                 swi
                  FCB .dequeue.
                 return
            
            RETURN VALUE
            
                 If queue entry size = 1, ACCA= queue entry
                 If queue  entry size = 2, ACCA = byte 1 of queue entry,
                                      and ACCB = byte 2 of queue entry
                 Other registers unchanged
            
            EXAMPLE
            
                 Example #1:
                 
                 There  exists   a  FIFO  queue,  DBLQ,  containing  two
                 character entries.  The queue  currently contains  four
                 entries as follows:
                 
                           ab
                           DE
                           Mc
                           xY
                 



            Copyright (c) 1989         Page 5 - 4          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 A task  is programmed to remove the oldest entry in the
                 queue and  return it  for  subsequent  processing.  The
                 entry is dequeued by:
                 
                 DBLQ      equ  4              Queue #4
                           .
                           :
                           ldaa  #DBLQ         ACCA = queue # 4
                           swi
                            FCB  .dequeue.
                           .                   Point of continuation
                 
                 At the  instruction following the FCB declaration, ACCA
                 and ACCB will contain the two characters, ab. The queue
                 will now contain the three entries:
                 
                           DE
                           Mc
                           xY
                 
                 Example #2:
                 
                 Another queue  exists, QUADQ,  which contains four byte
                 entries and  is currently  empty. The request to get an
                 entry from the queue would appear as:
                 
                 QUADQ     equ   5             Queue #5
                           .
                           :
                           ldaa  #QUADQ        ACCA = queue # 5
                           ldx   #destn        IX = destination address
                           swi
                            FCB  .dequeue.
                           .                   Point of continuation
                           :
                 destn     ZMB   4             Where the entry is placed
                           :
                 
                 Since there  are no entries available to dequeue, MCX11
                 puts the  task into  a  WAIT  state  on  the  NOT_EMPTY
                 semaphore associated  with  queue  #5.  The  task  will
                 remain in  that state  until another task puts a 4-byte
                 entry into  QUADQ. When  that happens, the waiting task
                 is put  into the RUN state. The entry is removed and is
                 stored at the specified destination address, destn, and
                 the task continues at the instruction following the FCB
                 declaration.
            
            SEE ALSO
            
                 .enqueue.




            Copyright (c) 1989         Page 5 - 5          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.3  .enqueue.  -  INSERT DATA INTO FIFO QUEUE
            
            CLASS
            
                 Queue
            
            SYNOPSIS
            
                 .enqueue. (QUEUE,PNTR)     [8]
            
            DESCRIPTION
            
                 Enqueue inserts  an entry  into a  FIFO queue.   If the
                 queue is  full, the calling task is set to a WAIT state
                 on the queue NOT FULL condition.  When the queue is not
                 full, the  entry is  inserted into  the queue.  If  the
                 width of  the queue  entry is greater than 2 bytes, the
                 data to  be put  into the queue is found at the address
                 specified by  the contents of register IX. If the width
                 is 1  byte, the  actual data to be enqueued is found in
                 bits 8-15 of IX. If the width is equal to 2 bytes, then
                 byte 1  of the  entry is  found in bits 8-15 of IX, and
                 byte 2 is in bits 0-7 of IX.
            
            CALLING SEQUENCE
            
                 ACCA= Queue number
                 IX = Source address of entry to be enqueued if size > 2
                      Or, IX8-15 = byte to be enqueued if size = 1
                      Or, IX8-15 = byte 1 and IX0-7 = byte 2 if size = 2
                 swi
                  FCB .enqueue.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 Example #1:
                 
                 Using the  2-byte queue,  DBLQ, defined  above, a  task
                 wants to  put an  entry into  it. Assume that the queue
                 contents are the three entries:
                 
                           DE
                           Mc
                           xY
                 
                 The queue  entry size  is two  bytes which  permits the
                 entry to  be passed  to the  queue routine  in ACCA and



            Copyright (c) 1989         Page 5 - 6          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 ACCB. The  request to  put a  two-byte entry,  LW, into
                 DBLQ is:
                 
                           ldaa  #DBLQ         ACCA = queue # 4
                           ldx   #"LW"         IX = "LW"
                           swi
                            FCB  .enqueue.
                           .                   Point of continuation
                 
                 Since the  queue has content, no task is waiting for an
                 entry to  dequeue; therefore, the entry is put into the
                 queue following  the "xY"  entry and the task continues
                 at the  instruction following  the FCB. The new content
                 of DBLQ is:
                 
                           DE
                           Mc
                           xY
                           LW
                 
                 
                 Example #2:
                 
                 Using the  queue, QUADQ,  previously  defined  but  now
                 containing three entries:
                 
                           abcd
                           EFGH
                           iJkL
                 
                 A request  to put  a new entry into the queue, MnOp, is
                 given by:
                 
                           ldaa  #QUADQ        ACCA = queue # 5
                           ldx   #srcadr       IX = source address
                           swi
                            FCB  .enqueue.
                           .                   Point of continuation
                           :
                 srcadr    FCC   "MnOp"
                           :
                 
                 Since the entry size is four bytes, IX must contain the
                 address of  the entry  to be enqueued. After continuing
                 at the instruction following the FCB declaration, QUADQ
                 contains:
                 
                           abcd
                           EFGH
                           IjKl
                           MnOp
            



            Copyright (c) 1989         Page 5 - 7          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            SEE ALSO
            
                 .dequeue.




















































            Copyright (c) 1989         Page 5 - 8          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.4  .execute.  -  EXECUTE A TASK
            
            CLASS
            
                 Task control
            
            SYNOPSIS
            
                 .execute. (TASK)     [12]
            
            DESCRIPTION
            
                 The execute  task directive is used to start or restart
                 a task from its beginning. The program counter (PC) and
                 stack pointer  (SP) are  initialized to  their starting
                 values and the specified task is made runnable.  If the
                 new task is of higher priority than the current task, a
                 context switch is performed and the new task runs, else
                 control is  returned to  the  caller.  The  task  being
                 started cannot be SELF (task number argument = 0).
            
            CALLING SEQUENCE
            
                 ACCA= Task number
                 swi
                  FCB .execute.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 The current task wishes to cause task number 6 to begin
                 execution at  its starting  point.  Task  number  6  is
                 currently IDLE. The request appears as:
                 
                 TASK6     equ   6             Task #6
                           .
                           :
                           ldaa  #TASK6        ACCA = task # 6
                           swi
                            FCB  .execute.
                           .                   Point of continuation
                 
                 If TASK6  is of  higher priority, then the current task
                 is interrupted,  but still  runnable, and TASK6 is made
                 the current task. The task which scheduled TASK6 is not
                 given control  again until  all other  higher  priority
                 tasks, including  TASK6, are not runnable. When it does
                 continue, it will do so following the FCB declaration.



            Copyright (c) 1989         Page 5 - 9          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 
                 If TASK6 is of lower priority that the current task, no
                 context switch occurs and the current task continues at
                 the instruction following the FCB declaration.
            
            SEE ALSO
            
                 .terminate.















































            Copyright (c) 1989         Page 5 - 10          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.5  .pend.  -  FORCE A SEMAPHORE TO A PENDING STATE
            
            CLASS
            
                 Semaphore
            
            SYNOPSIS
            
                 .pend. (SEMA)       [3]
            
            DESCRIPTION
            
                 To understand  the use  of the  pend directive,  recall
                 that the  WAIT directive  will return  control  to  the
                 calling task  immediately if  the task requests to wait
                 on a semaphore found to already be in a DONE state.  In
                 this  sense,   semaphores  keep   a  history  of  their
                 associated events,  even if  no task  is waiting at the
                 time  of   the  signal.     If   a  task  needs  to  go
                 unconditionally into a Event Wait state on a semaphore,
                 a call should first be made to PEND followed closely by
                 a WAIT directive.
            
            CALLING SEQUENCE
            
                 ACCB = Semaphore number
                 swi
                  FCB .pend.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 The current  task is  going to  make use of a semaphore
                 and wants  to be  certain of its state prior to use. It
                 forces the  semaphore into  a PENDing  condition by the
                 following request:
                 
                 NEWSEMA   equ   14            Semaphore #14
                           .
                           :
                           ldab  #NEWSEMA      ACCB = semaphore # 14
                           swi
                            FCB  .pend.
                           .                   Point of continuation
            
            SEE ALSO
            
                 .wait.



            Copyright (c) 1989         Page 5 - 11          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.6  .purge.  -  PURGE A TASK'S TIMERS
            
            CLASS
            
                 Timer
            
            SYNOPSIS
            
                 .purge. (TASK,SEMA,PNTR)      [15]
            
            DESCRIPTION
            
                 The purge  timer directive is used to remove all active
                 timers for  the specified  task or semaphore number.  A
                 specification of a zero semaphore number will purge all
                 semaphore timers for the given task.  When the purge is
                 completed, the current task is resumed.
            
            CALLING SEQUENCE
            
                 ACCA = Task number (0 if SELF)
                 ACCB = Semaphore number (0 if task semaphore)
                 IX0-7 = Switch: 0 = purge all timers for given task
                                >0 = purge time for given task & sema
                 swi
                  FCB .purge.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 The most common use of this ESR is for the current task
                 to get  rid of  one or  all of its active timers. Since
                 timers are  associated with semaphores, the combination
                 of task  number and  semaphore number  is sufficient to
                 identify a  timer uniquely.  The request  to purge  the
                 current task's timer associated with the task semaphore
                 appears as:
                 
                           clra                ACCA = 0 means SELF
                           clrb                ACCB = 0 means task sema
                           ldx   #1            Only purge one timer
                           swi
                            FCB  .purge.
                           .                   Point of continuation
                 






            Copyright (c) 1989         Page 5 - 12          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 If all  timers for a task are to be purged, the request
                 appears as:
                 
                           clra                ACCA = 0 means SELF
                           ldx   #0            Purge all timers
                           swi
                            FCB  .purge.
                           .                   Point of continuation
            
            SEE ALSO
            
                 .timer., .terminate.
            










































            Copyright (c) 1989         Page 5 - 13          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.7  .receive.  -  RECEIVE A MESSAGE
            
            CLASS
            
                 Message
            
            SYNOPSIS
            
                 .receive. (TASK)       [6]
            
            DESCRIPTION
            
                 The receive message directive is used to fetch messages
                 from a  calling task's  mailbox.   Because the messages
                 are placed  in the mailbox in the order of the sender's
                 priority, they  are processed in the same sequence.  If
                 the receiving  task specifies  a non-zero  task number,
                 the first  message from  that task  will  be  returned.
                 With a  zero task  number, the  first  message  in  the
                 mailbox is  returned.   If there are no messages in the
                 mailbox, the  task's context  is saved, and the task is
                 put into  a Message  WAIT state.  When the next message
                 is sent  to the task it will be resumed and the attempt
                 to receive a message will be reissued.
            
            CALLING SEQUENCE
            
                 ACCA =  Task number  if messages from specific task are
                        wanted. Or, ACCA = 0 if highest priority message
                        is wanted.
                 swi
                  FCB .receive.
                 return
            
            RETURN VALUE
            
                 Register  IX  contains  the  address  of  the  received
                 message. Other registers unchanged.
            
            EXAMPLE
            
                 Example #1:
                 
                 The current  task is  a server which operates only when
                 another task  sends it  a  message  instructing  it  to
                 perform  some   function.  The   server  task  receives
                 messages by making a request such as:
                 
                           clra                0 = next message
                           swi
                            FCB  .receive.
                           .                   Point of continuation



            Copyright (c) 1989         Page 5 - 14          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 
                 The server  task will  not continue  unless there  is a
                 message waiting  in its  mailbox. It will be put into a
                 WAIT state  until such  time as another task sends it a
                 message. No  waiting occurs  if a message is already in
                 the mailbox  at the  time  of  the  request.  When  the
                 message is available, its address is returned in the IX
                 register.
                 
                 Example #2:
                 
                 If the server wants to receive only those messages from
                 a specific  task, and  the task's number is to be found
                 in a variable named 'attach', the request is:
                 
                           ldaa  attach        variable contains task #
                           swi
                            FCB  .receive.
                           .                   Point of continuation
                           :
                 attach    ZMB   1
                 
                 The server  task will now only listen for messages from
                 the task  whose number is in the variable 'attach'. All
                 other messages  will  remain  in  the  mailbox  of  the
                 server. The  server will  continue  only  when  it  has
                 received a message from the specific task.
            
            SEE ALSO
            
                 .send., .sendw.
            























            Copyright (c) 1989         Page 5 - 15          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.8  .resume.  -  RESUME A TASK
            
            CLASS
            
                 Task control
            
            SYNOPSIS
            
                 .resume. (TASK)       [9]
            
            DESCRIPTION
            
                 The resume  directive clears  the suspended  state of a
                 task caused  by a  suspend directive.   If  the resumed
                 task is  made runnable  and is  higher priority, a task
                 switch is performed.  Otherwise, control is returned to
                 the calling task.
            
            CALLING SEQUENCE
            
                 ACCA = Task number
                 swi
                  FCB .resume.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 A task  which has  been  previously  suspended  may  be
                 resumed from the point of suspension only by a .resume.
                 request from another task. The request appears as:
                 
                 TASK6     equ   6             Task #6
                           .
                           :
                           ldaa  #TASK6        ACCA = task # 6
                           swi
                            FCB  .resume.
                           .                   Point of continuation
                 
                 Upon resuming  the given  task, a  context  switch  may
                 occur if  the resumed  task is  of higher priority than
                 the task  making the request. If not, no context switch
                 occurs.  The   requesting   task   continues   at   the
                 instruction following the FCB.
            
            SEE ALSO
            
                 .suspend.



            Copyright (c) 1989         Page 5 - 16          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.9  .send.  -  SEND A MESSAGE TO A TASK
            
            CLASS
            
                 Message
            
            SYNOPSIS
            
                 .send. (MSG,TASK)       [4]
            
            DESCRIPTION
            
                 The send  message directive  inserts a message into the
                 target task's  mailbox in  the  order  of  the  sending
                 task's priority.   If  the receiving task is waiting to
                 receive a  message and  is of  higher priority than the
                 sender, a  task switch  is performed.  If the receiving
                 task is  of lower  priority and  waiting on  a message,
                 then the  receiving task is marked runnable but control
                 is  returned  on  a  message,  the  message  is  simply
                 inserted to his mailbox for later receipt.
            
            CALLING SEQUENCE
            
                 ACCA = Task number of the receiver
                 ACCB = Semaphore number (task semaphore number = 0)
                 IX = Message address
                 swi
                  FCB .send.
                 return
            
            RETURN VALUE
            
                 None.  ACCB   will  contain  the  number  of  the  task
                 semaphore if  ACCB was  = 0  at time  of swi. All other
                 registers unchanged.
            
            EXAMPLE
            
                 A task wishing to send a message to a receiver task can
                 do so by the following code:
                 













            Copyright (c) 1989         Page 5 - 17          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 RCVRTSK   equ   12            Receiving task = task #12
                 MSGSEMA   equ   7             Use sema #7 for Message
                           .
                           :
                           ldaa  #RCVRTSK      ACCA = receiver task #
                           ldab  #MSGSEMA      ACCB = Message semaphore
                           ldx   #msgadr       IX = Address of message
                           swi
                            FCB  .send.
                           .                   Point of continuation
                           :
                 msgadr    ZMB   4             Message overhead
                           FCC   "THIS IS THE MESSAGE BODY"
                 
                 The message  located at  'msgadr' will  be put into the
                 mailbox of RCVRTSK. Processing in the sending task will
                 resume   at   the   instruction   following   the   FCB
                 declaration.
            
            SEE ALSO
            
                 .receive., .sendw.

































            Copyright (c) 1989         Page 5 - 18          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.10  .sendw.  -  SEND A MESSAGE AND WAIT
            
            CLASS
            
                 Message
            
            SYNOPSIS
            
                 .sendw. (MSG,TASK,SEMA)       [5]
            
            DESCRIPTION
            
                 The send  message and  wait directive is similar to the
                 send message directive described above, except that the
                 sending task  is always  put into a Event Wait state on
                 the message  semaphore.  This allows the receiving task
                 to signal  the sender  when the  message processing  is
                 complete and/or  that there  is data  returned  in  the
                 message area.
            
            CALLING SEQUENCE
            
                 ACCA = Task number of the receiver
                 ACCB = Semaphore number (task semaphore number = 0)
                 IX = Message address
                 swi
                  FCB .sendw.
                 return
            
            RETURN VALUE
            
                 None.  ACCB   will  contain  the  number  of  the  task
                 semaphore if  ACCB was  = 0  at time  of swi. All other
                 registers unchanged.
            
            EXAMPLE
            
                 The example  is the  same as for .send. except that the
                 ESR request  will be  .sendw. Another difference is the
                 WAIT state  into which the sending task is placed until
                 the receiving task signals the message semaphore. Until
                 that signal  is received,  the sending task proceeds no
                 further.  When   the  receiver   signals  the   message
                 semaphore,  the  sending  task  will  continue  at  the
                 instruction following the FCB.
            
            SEE ALSO
            
                 .send., .receive.
            





            Copyright (c) 1989         Page 5 - 19          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.11  .signal.  -  SIGNAL A SEMAPHORE
            
            CLASS
            
                 Semaphore
            
            SYNOPSIS
            
                 .signal. (SEMA)       [2]
            
            DESCRIPTION
            
                 The signal  semaphore directive  sets the  state  of  a
                 specified semaphore  to DONE.    If  the  semaphore  is
                 currently in  a WAIT state, the Event Wait state of the
                 waiting task  is removed,  and  the  semaphore  is  set
                 PENDing.   If the  waiting task becomes runnable and is
                 of  higher  priority  than  the  signalling  task,  the
                 context of  the current  task is  saved, and  a context
                 switch is performed.
                 
                 If the  state of  the semaphore  was either  PENDing or
                 DONE, the semaphore is placed in the DONE state and the
                 current task is resumed following the signal ESR.
            
            CALLING SEQUENCE
            
                 ACCB = Semaphore number
                 swi
                  FCB .signal.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 Assume that  the current  task  wishes  to  signal  the
                 occurrence  of   a  particular   event.  The  event  is
                 associated with  a named  semaphore, EVNTSEMA. The task
                 signals the semaphore by the following procedure:
                 
                 EVNTSEMA  equ   15            Named semaphore #15
                           .
                           :
                           ldab  #EVNTSEMA     ACCB = semaphore # 15
                           swi
                            FCB  .signal.
                           .                   Point of continuation
                 




            Copyright (c) 1989         Page 5 - 20          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 Depending on  the  state  of  semaphore  EVNTSEMA,  the
                 signal may  or may  not cause  a  context  switch.  The
                 signalling  task   will  continue   processing  at  the
                 instruction following the FCB declaration.
            
            SEE ALSO
            
                 .pend., .wait.
            














































            Copyright (c) 1989         Page 5 - 21          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.12  .suspend.  -  SUSPEND A TASK
            
            CLASS
            
                 Task control
            
            SYNOPSIS
            
                 .suspend. (TASK)       [10]
            
            DESCRIPTION
            
                 The suspend  directive causes  the specified task to be
                 placed into  a suspended  state.   The suspended  state
                 will remain  in force  until it is removed by a resume,
                 execute, or  reset  directive.    A  task  may  suspend
                 itself.  Task 0 indicates the SELF task.
            
            CALLING SEQUENCE
            
                 ACCA = Task number (this may be SELF [0])
                 swi
                  FCB .suspend.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 The current  task wants  to suspend  itself until  some
                 indeterminate point  in the  future. To do so, it makes
                 the following request:
                 
                           clra                ACCA = 0 means SELF
                           swi
                            FCB .suspend.
                           .                   Point of continuation
                 
                 The task  remains in a suspended state until resumed by
                 a .resume.  ESR issued from another task. At that time,
                 the resumed  task  will  continue  at  the  instruction
                 following the FCB declaration.
            
            SEE ALSO
            
                 .resume.







            Copyright (c) 1989         Page 5 - 22          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.13  .terminate.  -  TERMINATE A TASK
            
            CLASS
            
                 Task control
            
            SYNOPSIS
            
                 .terminate. (TASK)       [11]
            
            DESCRIPTION
            
                 The terminate  directive is  used to terminate a task's
                 operation.   During termination,  the task's  state  is
                 cleared and  the task  state is set to Terminated.  The
                 timer queue  is searched  and all active timers for the
                 task are  purged.   Also, all  messages pending for the
                 task are  removed.   A task  number of 0 indicates self
                 termination.   In all  cases, the highest priority task
                 will execute next.
            
            CALLING SEQUENCE
            
                 ACCA = Task number (may be = 0 if terminating SELF)
                 swi
                  .terminate.
                 return
            
            RETURN VALUE
            
                 None.  Registers   unchanged.  Returns   only  if   not
                 terminating SELF.
            
            EXAMPLE
            
                 The current  task commits suicide by terminating itself
                 with the following procedure:
                 
                           clra                ACCA = 0 means SELF
                           swi
                            FCB .terminate.
                 
                 There is  no point of continuation following a suicide.
                 If another  task is terminated by the current task, the
                 current  task   will   continue   processing   at   the
                 instruction following the FCB declaration.
            
            SEE ALSO
            
                 .purge.





            Copyright (c) 1989         Page 5 - 23          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.14  .timer.  -  START A TIMER
            
            CLASS
            
                 Timer
            
            SYNOPSIS
            
                 .timer. (TASK,SEMA,TOCK)       [14]
            
            DESCRIPTION
            
                 The timer  directive inserts  an entry of the specified
                 time duration  into the  timer queue.  The timer can be
                 cyclic or  one-shot.   Cyclic timers are indicated by a
                 negative  duration  while  one-shots  are  of  positive
                 duration.   Further  options  allow  the  timer  to  be
                 associated either  with a  specified task  number (0  =
                 SELF) or  a semaphore  number.    After  the  timer  is
                 inserted,  the  current  task  is  resumed.    See  the
                 Advanced Topic  section for task versus semaphore-based
                 timers.
            
            CALLING SEQUENCE
            
                 ACCA = Task number (0 if SELF)
                 ACCB = Semaphore number (0 if task's semaphore)
                 IX = Number of clock tocks in timer. If > 0, timer is a
                      one-shot. If < 0, timer is cyclic.
                 swi
                  FCB .timer.
                 return
            
            RETURN VALUE
            
                 None. ACCA will contain the current task number if ACCA
                 was = 0 at swi. Other registers unchanged.
            
            EXAMPLE
            
                 Example #1:
                 
                 Assume that the current task wants to set up a one-shot
                 timer of 5 seconds. Also assume that the RTI is used as
                 the time  base using a 2**23 crystal and the clock TICK
                 is defined  to be 15.625 msec. Furthermore, there are 8
                 TICKS per TOCK so that a TOCK is 125 msec. The setup of
                 a 5  second timer  associated with  a named  semaphore,
                 TIMEOUT, would appear as:
                 





            Copyright (c) 1989         Page 5 - 24          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 TOCK      equ   8
                 TOCKTIME  equ   1000/8         TOCKTIME = 125 msec
                 TIMEOUT   equ   3              Named semaphore #3
                           .
                           :
                           clra                 Task is self (ACCA=0)
                           ldab  #TIMEOUT       Semaphore = TIMEOUT
                           ldx  #5000/TOCKTIME  Timer = 40 TOCKS
                           swi
                            FCB  .timer.
                           .                    Point of continuation
                 
                 The current  task would continue processing immediately
                 after the  ESR is finished because the .timer. ESR does
                 not cause the requestor to be put into a WAIT state nor
                 is there  a  context  switch  possible.  The  task  may
                 attempt to  wait on  the timer  semaphore at some later
                 time.
            
            SEE ALSO
            
                 .purge.

































            Copyright (c) 1989         Page 5 - 25          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



            5.15  .wait.  -  WAIT ON SEMAPHORE
            
            CLASS
            
                 Semaphore
            
            SYNOPSIS
            
                 .wait. (SEMA)       [1]
            
            DESCRIPTION
            
                 The wait  directive is a fundamental function in MCX11.
                 It is used to make a task wait for a specified event to
                 occur.   The event  must be  associated with  the given
                 semaphore.   If the  semaphore is  found  to  be  in  a
                 PENDing state,  the task  is placed  into an Event Wait
                 state and  the semaphore is changed to WAITing, and the
                 context of the current task is saved.  If the semaphore
                 is in a DONE state, no wait occurs and the task resumes
                 immediately.   Upon task resumption, the wait directive
                 returns  the   semaphore  number  of  the  event  which
                 occurred.
            
            CALLING SEQUENCE
            
                 ACCB = Semaphore number
                 swi
                  FCB .wait.
                 return
            
            RETURN VALUE
            
                 None. Registers unchanged.
            
            EXAMPLE
            
                 The current task wants to wait on a timer semaphore set
                 up by  a previous  .timer. request.  The semaphore is a
                 named semaphore, TIMEOUT. The procedure would appear as
                 follows:
                 
                 TIMEOUT   equ   3             Semaphore #3
                           .
                           :
                           ldab  #TIMEOUT      ACCB = semaphore # 3
                           swi
                            FCB  .wait.
                           .                   Point of continuation
                 
                 The current  task is put into a WAIT state on semaphore
                 TIMEOUT as  a result of this request. It will remain in



            Copyright (c) 1989         Page 5 - 26          Motorola, Inc.






                  MCX11 - MicroController eXecutive for the 68HC11



                 this state  until another task, in this case, the clock
                 driver, signals  TIMEOUT  that  the  timer  period  has
                 elapsed.  The   task  would   then  continue   at   the
                 instruction following the FCB.
            
            SEE ALSO
            
                 .pend., .signal.















































            Copyright (c) 1989         Page 5 - 27          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



                                     SECTION 6
                                          
                                SYSTEM CONFIGURATION
                                          
            
            6.1  SYSTEM CONFIGURATION CONCEPTS
            
            Another configuration  concept central  to the  operation of
            MCX11 is  that of  pre-definition.   Most real  time systems
            used  in   embedded  operations   have   a   fairly   static
            configuration.   That is to say, the equipment configuration
            is not  subject to  frequent changes nor is the basic system
            functionality.  Consequently, the system designer can define
            the operating  environment  so  that  the  operating  system
            dynamics are  avoided to  the greatest  degree possible.  In
            other words,  the number of tasks concurrently executing may
            change but  the relative  priorities of  tasks remain fixed.
            Thus task  priorities can  be pre-assigned.   The  amount of
            free memory  can be  computed  and  established,  number  of
            queues and  their  sizes,  and  the  number  of  timers  and
            semaphores are  all defined prior to runtime.  The result is
            that MCX11  works in an established environment which yields
            the effect   of  less system  overhead,  smaller  code,  and
            faster execution;  all three being  desirable in a real time
            system.
            
            In order  to define  a  MCX11  system  configuration  it  is
            necessary to  configure those  data and  control  structures
            with  the   application  specific  information  which  MCX11
            requires. The  configuration is done by creating AS11 source
            code files  which define the necessary information needed to
            assemble with  MCX11 source  code  to  define  a  particular
            configuration.  The   following  paragraphs   describe   the
            techniques.
            
            
            6.2  MCX11 SYSTEM TABLE MEMORY REQUIREMENTS
            
            MCX11 system  tables must  necessarily reside  in an area of
            RAM.  This section is included to assist the system designer
            in determining  the amount of ROM and RAM required for MCX11
            tables. The  amount of  RAM and ROM may be computed from the
            equations below  given the  following  system  configuration
            information:
            
                 NTASKS    The number of tasks
                 NNAMSEM   The number of named semaphores
                 NQUEUES   The number of queues
                 NTIMERS   The number of timers
            





            Copyright (c) 1989         Page 6 - 1          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



            The symbols above are used by MCX11 and should be considered
            reserved symbols.  These numbers  are obviously exclusive of
            any RAM and ROM requirements of the application tasks.
            
            Tasks
            
                 A Task  Control Block  occupies 5  bytes of  RAM and  7
                 bytes of ROM.
                 
                      TASK bytes (RAM) = NTASKS * 5 + 5
                      TASK bytes (ROM) = NTASKS * 7
            
            Semaphores
            
                 Each semaphore  requires 1  byte of  RAM.  Total system
                 area required  for semaphore  control is  the number of
                 named semaphores  + the  number of  tasks + 2 times the
                 number of queues.
                 
                      SEMA bytes (RAM) = NNAMSEM + NTASKS + 2 * NQUEUES
            
            
            Queues
            
                 Each queue  consists of  a queue  header and  the queue
                 body.   Each queue header requires 3 bytes of RAM and 6
                 bytes of ROM.  Each defined queue body requires an area
                 of RAM  defined by the product of its Width (W) and its
                 Depth (D).
                 
                      QUEUE bytes (RAM) = NQUEUES * 3 + Sum(Wi * Di),
                                          where Wi is the width and Di
                                          is the depth of the ith queue,
                                          and i ranges from 1 - NQUEUES.
                 
                      QUEUE bytes (ROM) = NQUEUES * 6
            
            
            Clock
            
                 Timers require  8 bytes  of RAM  each.   The total area
                 required for  timer control  and storage is the product
                 of 8 and the number of defined timers.
                 
                      TIMER bytes (RAM) = NTIMERS * 8
            









            Copyright (c) 1989         Page 6 - 2          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



                                     SECTION 7
                                          
                             DEVICE DRIVER & INTERRUPTS
                                          
            
            7.1  DRIVER CONCEPTS
            
            Device  drivers   are  program   modules  which  provide  an
            organized software  interface between  a physical device and
            the application programs using the device.  The intent is to
            mask the  specifics of  the device's  hardware peculiarities
            from the application software.  By doing so, the application
            code need  only conform  to the  protocol which  the  device
            driver expects  in order to perform a function.  Each device
            driver may  have a  protocol unique to its function, i.e., a
            disk driver  has different  functional requirements  from an
            analog-to-digital converter.
            
            In order  to accommodate the wide range of devices which are
            found in  real-time systems, the device drivers in MCX11 are
            structured as  tasks.   As a  task, a  device driver has the
            most flexible  environment with  complete access  to  system
            resources via  the Executive  Service Requests.  Actually, a
            device driver  usually consists  of two  parts:   the driver
            task, and  the interrupt  service routine (ISR).  The latter
            is used when the device can cause an interrupt to signal the
            completion of a function or the availability of the device.
            
            An ISR  exists to  handle an exception in the normal flow of
            processing.   The general  philosophy of MCX11 drivers is to
            minimize the time spent in the interrupt service routine and
            let the  task portion  handle the  real work  of the driver.
            This design  concept places  no restrictions on the designer
            for either  the ISR or the task functionality. The structure
            of the  ISR is  explained more  completely in  the following
            section.
            
            
            7.2  INTERRUPT SERVICE
            
            The  classic   interrupt   processing   philosophy   is   to
            acknowledge the  interrupt and  save the  current  processor
            context.   Then a branch is made to a software routine where
            the code  services the  specific interrupt  and performs any
            required operations.  When the  interrupt service routine is
            complete, control  of the  main program  is resumed  at  the
            point of  interruption.   MCX11 uses  a modified  version of
            that sequence.
            
            The  MC68HC11  microcontroller  always  pushes  the  current
            processor context of nine (9) bytes on the active stack when
            an interrupt  occurs. That having been done, it acknowledges



            Copyright (c) 1989         Page 7 - 1          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



            the interrupt  and vectors automatically to the specific ISR
            written for  that event.  The user must initialize each two-
            byte interrupt  vector location  specific to his application
            as part of the initialization code.
            
            MCX11  presets   the  vector  locations  for  the  following
            interrupts. All  others not  specifically  reserved  by  the
            MC68HC11 are available to the user.
            
                    Event               Address
                 
                 Clock (RTI)          $FFF0-$FFF1
                 MCX11 ESR request    $FFF6-$FFF7
                 Power On/Reset       $FFFE-$FFFF
            
            MCX11 uses a modified version of the classical ISR approach.
            The sequence is the same until the return to the interrupted
            program is  made at  the  end  of  the  ISR.  In  MCX11,  an
            interrupt may  be the  event for which a task is waiting. If
            so, a  notification of  the event's occurrence must be given
            to the  task. But  the possibility  exists that  the waiting
            task has  a  higher  priority  than  the  interrupted  task.
            Notification of  the event should remove the wait state from
            the higher  priority task  thus making it runnable, assuming
            it is not otherwise blocked.
            
            At that  point, a  decision has  to be  made as  to  how  to
            continue. Whichever  task is  of higher  priority,  the  one
            interrupted or the one which was waiting, it will be the one
            to resume  processing. If  it is  the interrupted  task,  it
            resumes at  the point  of interruption  as  in  the  classic
            sequence. If  the latter  task  is  of  higher  priority,  a
            context switch  is performed in which it is made the current
            task. Its  processor context  is restored from its stack and
            the task  resumes at  the location  following the  ESR which
            caused it to wait. The interrupted task remains runnable and
            will continue at the point of its interruption at some later
            time when it becomes the highest priority runnable task.
            
            MCX11 provides  a common  exit routine  to  which  all  ISRs
            should branch  if there  is the  possibility  of  a  context
            switch as  the  result  of  the  interrupt.  The  function's
            primary responsibility is to signal a specified semaphore of
            the occurrence  of an  event and  to dispatch control to the
            highest priority  task which is runnable after the interrupt
            has been serviced.
            
            
            7.2.1 Interrupt Processing Variables
            
            In order  for MCX11 interrupt servicing to operate properly,
            it is  necessary to  observe a  few rules of the road. There



            Copyright (c) 1989         Page 7 - 2          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



            are some  system variables  which are  used during interrupt
            processing in  the ISR  and in  the common ISR exit routine.
            These variables  must be used only in the ISR and should not
            be used  elsewhere. A  listing of  the variables and a brief
            description of  them follows. Their addresses are also given
            as a  displacement from the base address of the MCX11 system
            variables, MCXVAR.  MCXVAR may be located at any RAM address
            but must  be predefined  and assembled with the MCX11 kernel
            code.
            
            intlvl   (address MCXVAR+11)
            
                 This byte  variable is  a  counter  of  the  number  of
                 interrupts stacked  but not  yet processed  completely.
                 When an  interrupt occurs in a task, intlvl will always
                 contain a value of zero. The ISR code must increment it
                 by 1  to indicate  that an ISR is in process. If a task
                 calls the  MCX11 kernel,  intlvl is  incremented  to  a
                 value of 1. If an interrupt were to occur while control
                 is in  the MCX11 kernel, intlvl would be incremented to
                 2 by the ISR, etc.
                 
                 MCX11  allows  the  existence  of  interruptible  ISRs;
                 therefore, intlvl can assume any value up to the number
                 of possible interrupts in the system. As interrupts are
                 processed by  the common  ISR  exit  logic,  intlvl  is
                 decremented. A  resumption of  processing at  the  task
                 level can  only occur  when the  decremented  value  of
                 intlvl becomes  zero.  Otherwise,  the  non-zero  value
                 indicates the  existence of an interrupt which has been
                 incompletely serviced.  In that  case, the  common  ISR
                 exit logic  returns control  to the interrupted ISR and
                 resumes  processing   at  that   point.  Thus,   nested
                 interrupts and  re-entrant ISRs  are  handled  cleanly,
                 quickly, and automatically by MCX11.
                 
            curtsk  (address MCXVAR+5)
                 
                 This byte  variable contains  the number of the current
                 task. It  is to be considered a READ-ONLY variable. The
                 user should  NEVER write to this variable. It is needed
                 during  ISR   processing  to  determine  if  the  MCX11
                 Dispatcher was interrupted.
                 
            curtcb  (address MCXVAR+6)
                 
                 This  2-byte  variable  contains  the  address  of  the
                 current  task's  Task  Control  Block  (TCB).  The  TCB
                 contains an  entry for  the task's stack pointer. MCX11
                 interrupt  processing   requires  that  the  ISR  which
                 increments intlvl  to a  value of  1 must also save the




            Copyright (c) 1989         Page 7 - 3          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



                 current task's  stack pointer in its TCB. The variable,
                 curtcb, is READ-ONLY.
            
            
            7.2.2 Interrupt Processing Code
            
            All ISRs  which have  the capability  of causing  a  context
            switch should  incorporate the  following routine as in-line
            code in  the ISR.  If the  ISR is  to be  allowed to  enable
            interrupts, this code should precede the CLI instruction. As
            a rule  it should  occur early  in the  ISR  but  there  are
            exceptions. (Refer  to the  MCX11 clock  driver's ISR, whose
            entry address  has the  symbol rtiisr, for a good example of
            an exception to the rule.)
            
            Note that the label, notlvl0, used in the code segment below
            will need  to be changed for each ISR. The symbols ACTSP and
            SYSTACK are  not variables  and should not be changed. ACTSP
            is equated to the value of 1 and represents the displacement
            into the  TCB where  the task's  stack  pointer  is  stored.
            SYSTACK is the location of the base of the System Stack area
            and is defined in the System Configuration source code file,
            SYSTEM.AS.
            
            
                           tst   intlvl    Test for task level interrupt
                           bne   notlvl0   Branch if not task level int
                           tst   curtsk    See if Dispatcher interrupted
                           beq   notlvl0   Branch if so
                           ldx   curtcb    Get task's TCB address
                           sts   ACTSP,x   Save task's stack pointer
                           lds   #SYSTACK  Change to System Stack
                 notlvl0   inc   intlvl    Increment the interrupt level
                 
                 After this  point, the  CLI instruction may be inserted
                 if desired.
            
            
            The interrupt  service code  follows. An important factor in
            interrupt  processing  throughput  is  the  length  of  time
            interrupts are  disabled during  the  ISR.    In  all  ISRs,
            interrupts must  be disabled long enough to perform the code
            segment above and only then should interrupts be re-enabled.
            Ideally,  interrupt   routines  should   be  performed  with
            interrupts enabled to allow other interrupts to be serviced.
            
            The exit  from the  ISR routine is via a branch to the MCX11
            common Interrupt Service Routine Exit routine located at the
            address having  the symbol,  isrrtn. This routine allows for
            optionally signalling  a semaphore  during the exit process.
            The ISR  may wish  to signal  a  semaphore  that  the  event
            associated with  the interrupt  has occurred.  To do so, the



            Copyright (c) 1989         Page 7 - 4          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



            ISR simply  puts the number of the semaphore to be signalled
            into the  B-Accumulator and the executes a branch to isrrtn.
            From there  on, the  further processing  of the interrupt is
            performed automatically  by MCX11. As an example, assume the
            ISR wants  to signal a semaphore and that the label used for
            the semaphore  is EVNTSEMA. Then the concluding code segment
            in the ISR is
            
            
                           ldab  #EVNTSEMA   Load ACCB with semaphore #
                           jmp   isrrtn      Jump to exit logic.
            
            
            If no  semaphore is to be signalled during the exit routine,
            the ISR  should make  sure that the B-Accumulator is cleared
            before branching to isrrtn.







































            Copyright (c) 1989         Page 7 - 5          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



                                     SECTION 8
                                          
                                  ADVANCED TOPICS
                                          
            
            8.1  OTHER TOPICS
            
            Other topics  of interest  will be  added to this section as
            they are researched and documented.














































            Copyright (c) 1989         Page 8 - 1          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



                                     APPENDIX A
                                          
                           MCX11 DISTRIBUTED SOURCE FILES
                                          
            
            MCX11 is  distributed as  a collection of files. Those files
            and their purposes are briefly described below.
            
            CLKDRVR.AS
            
            The AS11  source code  of  the  RTI  clock  driver  and  RTI
            Interrupt Service Routine.
            
            ESREQU.AS
            
            These are  just the  equates for  MCX11  ESRs  included  for
            completeness.
            
            MCX.AS
            
            This is the AS11 source code of the MCX11 kernel. Unless you
            are expanding  the functions  of  the  kernel  or  fixing  a
            reported bug, this file probably won't change too much.
            
            SYSTEM.AS
            
            This AS11 source code file contains the application specific
            information and  should be  studied very  closely.  It  also
            contains initialization  code  which  may  be  necessary  to
            change to meet the needs of a given application. The file is
            pre-configured  with   the  specifications  needed  for  the
            demonstration programs in file TEST.AS.
            
            TEST.AS
            
            This is  an AS11  source code  file containing 4 tasks which
            demonstrate the  use of all of the MCX11 ESRs. It doesn't do
            anything practical except to give the user a limited look at
            how to accomplish certain operations.
            
            VECTORS.AS
            
            AS11 source  code containing  all of  the  vectors  used  by
            MCX11.  This  file  may  need  to  be  edited  for  a  given
            application.
            
            ASSEMBLE.BAT
            
            A MS-DOS  Batch file  used to  assemble MCX11  and the  TEST
            programs. It also produces a listing file.
            
            MANUAL.DOC



            Copyright (c) 1989         Page A - 1          Motorola, Inc.






                 MCX11 - MicroController eXecutive for the MC68HC11



            
            The MCX11 User's Manual is contained in this file. It can be
            printed out directly to any ASCII compatible printer.
            
            README.DOC
            
            Some notes about getting started with MCX11.
            















































            Copyright (c) 1989         Page A - 2          Motorola, Inc.