[42m[33m                      [4m AskTask Documentation [0m[42m                              [0m

    [32mUSAGE:[31m asktask [<-opt>]
        where opt = c    - use my default colors (the intended ones for
                           this program). The previous colors are restored
                           when asktask is terminated.
                    p{n} - start with priority n. Asktask sets its own
                           priority to a default of 15. This option will
                           replace 15 with n. Note that the CLI launching
                           asktask will get this priority too, and retains
                           it even after asktask has terminated. I tend to
                           use 'run asktask -p0'.
        NOTE: [] = optional, <> = 1 or more, {} = mandatory.

    [32mDISCLAIMER:[31m this program accesses important system data structures. It
    should never be used along with programs containing important, unsaved
    data, execpt in emergencies.

    [32mPURPOSE:[31m
        Asktask is intended to allow the user to examine various bits of
    the task structures of all the tasks in the system (except itself).
    These are accessed from the 'ready' and 'waiting' lists attached to
    ExecBase. The information displayed is:
            [32mpriority[31m    (task->tc_Node.ln_Pri)
            [32mstate[31m       (task->tc_State)
            [32mflags[31m       (task->tc_Flags)
            [32mstack[31m       (task->tc_SPReg, tc_SPLower, tc_SPUpper)
                    Rg = register pointer.
                    Up = upper address + 2.
                    Lw = lower address.
                    Sz = Size.
                    Rm = Remaining space.
                (Note: if Rg doesn't lie between Up and Lw, then the task
                 is no doubt a CLI process, where the Rg address is the
                 command's stack pointer, not the CLI's.)
            [32msignals[31m     (tc_SigAlloc, tc_SigWait, tc_SigRecvd, tc_Except)
                    A = allocated signals.
                    W = waiting signals.
                    R = recieved signals.
                    E = exception signals accepted.
    [33mSome facilities for altering this data are also provided, but for the
    purpose of experimenting only!.[0m

    [32mOPERATION NOTES:[31m
        -) You can select a task by clicking on its name.
        -) Asktask's internal task pointer array is not updated unless
           you use the refresh operation.
        -) Be aware that the CLI asktask is launched from gets asktask's
           priority of 15. So any other programs launched from that CLI
           will inherit this unusually large priority, perhaps interfering
           with asktask itself.
        -) A task may be paused by allocating a signal, and setting the
           corresponding wait signal bit, clearing the others. Starting it
           again is a problem though!
        -) RemTask() may be used to remove the current task. This unloads
           the task. This should not be used to kill tasks that are CLI
           commands, since the CLI is removed as well. (A CLI command
           doesn't seem to be a seperate task from its CLI; ie: the CLI
           does not fork off a new task to run commands, unless you use
           'run' (or use WShell or some other shells background task option)
           to start the command).
        -) Exit() may be used to remove the current task. A context switch
           results in the task's pc address being stored on its stack.
           Asktask redirects this address to a piece of data within asktask
           that results in the task calling the DOS function Exit(). This
           should only be used to terminate CLI tasks that are currently
           running a command.
        -) The ABORT (CTRL-C) signal can be sent to the current task by
           setting the appropriate tc_SigRecvd bit (bit # 12 counting from
           zero). This is the preferred method for zapping CLI tasks, but
           only works if the task recognizes the signal. This is
           accomplished for Lattice C users during chkabort(), or level 2(?)
           IO routines. I recommend using the chkabort() and onbreak()
           functions.
        -) [33mWARNING:[31m try not to kill a task that owns some essential system
           resource, particularly the blitter. The removal may well happen
           before the task frees the resource, in which case deadlock city.
           Try reducing its priority instead.
        -) [33mWARNING:[31m try not to kill a task that waits for many messages from
           somebody else. For example, killing the clock program causes a
           'Finish all disk activity - Task held' type requester to appear.
           While other programs will be unaffected, the CLI used to run
           the held task will be frozen.
        -) Note that asktask deals with tasks. Not processes. For those
           who don't know, a process is a task that has been launched by
           AmigaDOS (the CLI or Workbench), and hence has a process data
           structure associated with it as well as a task structure. Asktask
           does not care about this process structure, since tasks are the
           lowest level of multitasking, and while all processes have tasks,
           not all tasks have processes. A similar program could be written
           to get at processes through the DOSBase pointer.
        -) If you set a task's priority (using asktask) to something
           greater than asktask's, asktask will boost its own priority to
           the task's new priority plus 5. Hence the maximum priority you
           can set is 122 (127 - 5). This can be useful if some task has a
           priority that interferes with the system tasks. For instance,
           if you start test from the same CLI as asktask, and it thus
           inherits a priority of 15, because test does no waiting it will
           lock out the trackdisk.device and FileSystem tasks. In addition,
           it will not appear on asktask's task list. Why not I don't know,
           but it needs to have its priority reduced. To do this, you need
           to increase asktask's priority to something greater than 15. So
           selecting say the input.device, and changing its priority to 21
           will boost asktask's priority to 26, thus allowing you to control
           test with asktask. Because asktask spends most of its time
           waiting for your input, it is safe to set asktask's priority as
           high as you like.
        -) Questions can be sent to me at:
                            J.Bickers,
                            214 Rata St,
                            Naenae.
           Complaints can jump in the nearest lake.

    [33m            o/          o__
                |          /          __o            _
                [4m>[0m[33m          [4m>[0m[33m         [4m>[0m[33m  \             \
    [31m         ­­­­       ­­­­      ­­­­          ­­­­   [33m\o[32m¸[31m
             [42m        [0m   [42m        [0m  [42m            [0m  [42m      »»[33m\[31m««    [0m

    [32mEXAMPLE:[31m
        1) run asktask.
        2) make [33mPopCLI III[0m the current task by clicking on it.
        3) select the SIGNAL operation, then press r for the Recvd signal
           bits. Set the 3 bits to the right of the leftmost two, and press
           return.
        4) a newcli should appear (you have simulated the PopCLI hotkey).
        5) start the 'test' program from the newcli. This program is an
           infinite loop:
                    while (1) j++;
        6) refresh the task list a few times to get the newcli task on the
           list, then select it as the current task.
        7) select the Exit() operation, and press y.
        8) the newcli prompt should reappear, test having been forced to
           terminate.
        NOTE: for some reason, endcli doesn't close down the new CLI
           console. Presumably because test has some files still open, such
           as its stdout, which is of course, the console!

    [32mDISTRIBUTION:[31m
        -) this program can be distributed freely, or for a maximum cost of
           copying + postage.
        -) this program cannot be ported to other, ridiculous, single-task
           machines, so there's no problem with that.
        -) feel free to alter or copy the code as you wish.

    [32mSOURCE:[31m The following files make up the source code -
                    asktask.h           at_input.c
                    asktask.c           at_kill.c
                    at_gadg.c           at_putdata.c
                    at_help.c           trans.c
            blink with asktask.lnk

            The following files are also included:
                    asktask.doc
                    test.c/test

    IMPORTANT NOTE: Discovered the task structure is actually contained
        WITHIN (at the start of) a process structure if that task is also
        a process. That is how Exit() knows which process... A pointer to
        a task structure is also a pointer to its process structure:
                        see libraries/dosextens