Table VI C-1

The byte by byte description of the contents of the header record of a SEM incremental file.

| Byte | Contents | Comments |
| --- | --- | --- |
| 001-003 | 3-character code for incremental file creation site | EBCDIC, normally NSS, ASCII |
| 004 | ASCII blank character | ASCII 032 decimal |
| 005-006 | Level 1b data format version number | currently 001 |
| 007-008 | Year of level 1b data format creation | currently 1998 |
| 009-010 | Day of level 1b data format creation | currently 051 |
| 011-012 | Number of bytes in logical record | currently 512 |
| 013-014 | Record block size | currently 512 |
| 015-016 | Number of header records in this incremental file | normally 001 |
| 017-018 | not used |  |
| 019-060 | 42-character name of this incremental data file | EBCDIC, ASCII as of 2005 |
| 061-068 | 8-character processing block ID | EBCDIC, ASCII as of 2005 |
| 069-070 | Spacecraft ID | note (1) |
| 071-072 | Instrument ID | normally 000 |
| 073-074 | Data type code | is 009 for SEM |
| 075-076 | TIP source code | normally 000 |
| 077-080 | Day number from 1 Jan. 1950 at start of this data set | 19546 for July 8, 2003 |
| 081-082 | Year at start of this data set | 4-digit year |
| 083-084 | Day of year at start of this data set | 3-digit day of year |
| 085-088 | UT time in milliseconds at start of this data set | all 4 bytes used |
| 089-092 | Day number from 1 Jan. 1950 at end of this data set | 19546 for July 8, 2003 |
| 093-094 | Year at end of this data set | 4-digit year |
| 095-096 | Day of year at end of this data set | 3-digit day of year |
| 097-100 | UT time in milliseconds at end of this data set | all 4 bytes used |
| 101-102 | Year of last CPIDS update | note (2) |
| 103-104 | Day of year of last CPIDS update | note (2) |
| 105-112 | Not used |  |
| 113-116 | TIP word 08, status 1 and 2 at start of this data set | note (3) |
| 117-118 | Not used |  |
| 119-120 | Data record number of any status change in TIP 08 | note (4) |
| 121-124 | TIP word 08, status 1 and 2 after a status change | note (4) |
| 125-126 | Number of 2-second data records in this data set | note (5) |
| 127-128 | Number of data gaps in this data set |  |
| 129-130 | Number of TIP minor frames without sync errors | note (5) |
| 131-132 | Number of TIP parity errors detected by PACS |  |
| 133-134 | Sum of all sync errors detected in this data set |  |
| 135-136 | Time sequence error flag | note (6) |
| 137-138 | Time sequence error code | note (7) |
| 139-140 | SOCC clock update indicator | note (8) |
| 141-142 | Earth location error indicator | note (9) |
| 143-144 | Earth location error code | note (10) |
| 145-146 | PACS status bit field | note (11) |
| 147-148 | PACS data source | 1 is Fairbanks, 2 is Wallops |
| 149-176 | Not used |  |
| 177-184 | 8-character code for reference ellipsoid model ID | EBCDIC |
| 185-186 | Nadir earth location tolerance | units are tenths of km |

| Byte | Contents | Comments |
| --- | --- | --- |
| 187-188 | Earth location bit field | note (12) |
| 189-190 | Not used |  |
| 191-192 | Spacecraft roll attitude error | units are .001 degrees |
| 193-194 | Spacecraft pitch attitude error | units are .001 degrees |
| 195-196 | Space craft yaw attitude error | units are .001 degrees |
| 197-198 | Epoch year for satellite orbit vector | 4-digit year |
| 199-200 | Epoch day of year for satellite orbit vector | 3-digit day, near byte 083-084 |
| 201-204 | Epoch UT time in milliseconds for orbit vector | all 4 bytes used |
| 205-208 | Semi-major axis of orbit | note (13) |
| 209-212 | Orbit eccentricity | note (14) |
| 213-216 | Orbit inclination | note (15) |
| 217-220 | Argument of perigee | note (16) |
| 221-224 | Right ascension of the ascending node | note (16) |
| 225-228 | Mean anomaly | note (16) |
| 229-232 | Satellite location, x coordinate | note (17) |
| 233-236 | Satellite location, y coordinate | note (17) |
| 237-240 | Satellite location, z coordinate | note (17) |
| 241-244 | Satellite velocity vector, x component | note (18) |
| 245-248 | Satellite velocity vector, y component | note (18) |
| 249-252 | Satellite velocity vector, z component | note (18) |
| 253-256 | Earth/sun distance ratio | note (19) |
| 257-512 | Not used |  |

Notes for Table VI C-1

The bit numbering convention used below is the least significant bit within a byte is bit 01 and the most significant bit is bit 08.  In the case of multiple bytes, the bit count increments from bit 01 of the highest numbered byte to bit 08 of the lowest numbered byte.

- Satellite ID is 2 for NOAA-15, 4 for NOAA-16 and 6 for NOAA-17

- CPIDS refers to a comprehensive calibration data set and these bytes provides the year

and day-of-year of the latest data set update.

- These bytes contain the contents of status1 and status2 from TIP word 08 at the

beginning time of this data set.  The bit assignments are

bytes 113 and 114		not used

bit 8, MSB of byte 115		microprocessor system identifier

bit 7				TED IFC flag

bit 6				MEPED IFC Flag

bit 5				MSB of the TED electron pulse discriminator level

setting

bit 4				LSB of the TED electron pulse discriminator level

setting

bit 3				not used

bit 2				not used

bit  1, LSB of byte 115				not used

bit 8, MSB of byte 116		microprocessor A watchdog error

bit 7				microprocessor B watchdog error

bit 6				MSB of the TED proton pulse discriminator level

setting

bit 5				LSB of the TED proton pulse discriminator level

setting

bits 4-1				not used

See also the Notes for Table VI B-2

- If the contents of status1 or status2 change during the course of this data set, bytes 119-

120 contain the data record number of that change.  Bytes 121-124 contain the contents

of status1 and status2 after that change with the bit assignments in note (3).  Normally a

change in the contents of status1 or status2 is associated with an in-flight calibration.

- Bytes 125-126 contain the number of 2-second SEM data records in this incremental file.

Bytes 129-130 contain the number of TIP minor frames within this incremental file that

did not have sync errors.  If there were no sync errors records, the integer number in

bytes 129-130 should be exactly 20 times the integer number in bytes 125-126 because

there are 20 TIP minor frames in each 2-second data record.  If sync errors are present,

the value of bytes 129-130 will be less than 20 times the integer value of bytes 125-126.

(6)	0 = no time error; otherwise the record number of the first occurrence of an error

(7)	If there is a time error, the following provides details of that error.

if a bit is set to 1, then the statement is true.

byte 137		not used

bit 8, MSB of byte 138	time field is bad but can probably be inferred from the

previous good time.

bit 7			time field is bad and can’t be inferred from the previous good

time.

bit 6			this record starts a sequence that is inconsistent with previous

times (i.e., there is a time discontinuity). This may or may not be associated with a spacecraft clock update.

bit 5			start of a sequence that apparently repeats scan times that

have been previously accepted.

bit 4 to 1		not used

(8)	=0 if no clock update during this orbit; otherwise the record number of the first

occurrence of a clock update.  Typically there is a spacecraft clock update of a few milliseconds each day.

(9)	=0 if no error during this orbit; otherwise the record number of the first error in

earth location.

(10)	If there is an earth location error, the following provides details of that error.

if a bit is set to 1, then the statement is true.

byte 143		not used

bit 8, MSB of byte 144	not earth located because of bad time; earth location fields zero filled.

bit 7	earth location questionable because of questionable time code  (See time problem flags.)

bit 6	earth location questionable—only marginal agreement with reasonableness check.

bit 5	earth location questionable—fails reasonableness check

bit s 4 to 1	not used

(11)	These bytes not used in SEM data processing.  For the record,

byte 145,		not used

bit 8 MSB of byte 146	not used

bits 7-4			not used

bit 3			0 if data stream is normal, 1 if data is pseudo noise

bit 2			0 if tape playback was in reverse, 1 if forward

bit 1, LSB of byte 146	0 if data stream is test, 1 if data stream is flight data

Normally, the value of byte 146 is decimal 3, bits 1 and 2 set to 1

(12)	This is not used in SEM processing

(13)	The integer number in bytes 205-208 is divided by decimal 100000. to obtain the semi-

major axis in kilometers.

(14)	The integer number in bytes 209-212 is divided by 100000000. to obtain the orbit

eccentricity.  Note that a survey of header files shows the eccentricity (and the semi-major axis) varies a great deal day to day.  The orbit eccentricity given in the 2-line NORAD orbit elements obtained from http://celestrak.com/NORAD/elements/noaa.txt

do not show nearly that variation and the NORAD eccentricities generally do not agree with those obtained from this header record.  There is no explanation for this.

(15)	The orbit inclination in degrees is obtained from the integer number in bytes 213-216 by

dividing by decimal 100000.  The orbital inclination is used in SEM data processing.

(16)	The integer values of these parameters are divided by decimal 100000. to obtain the

physical parameters in degrees.

(17)	The integer values of these 4-byte signed integers are divided by decimal 100000. to

obtain the satellite location in kilometers at the epoch time given in bytes 197-204  in earth-centered inertial coordinates.  That is, the Z axis directed north parallel to earth’s axis of rotation, X axis directed toward the vernal equinox, and the Y axis completing the right handed Cartesian coordinate system.

(18)	The integer values of these 4-byte signed integers are divided by decimal 100000000. to

obtain the satellite velocity vector in kilometers per second at the epoch time given in bytes 197-204.  The coordinate system is earth-centered inertial.

(19)	The earth/sun distance ratio is obtained by dividing the integer value of bytes 253-256 by

decimal 1000000.  The definition of the earth/sun distance ratio is not known although the numerical value of this ratio is close to 1.0

Table VI C-2

A sequence of data records follow the header record in an incremental file.  Usually an incremental file contains about one orbit’s data or about 6000 seconds.  A single physical 512 byte data record in the file contains 2-seconds of data so that each incremental file contains about 3000 physical data records.  Each 2-second data record contains 20 TIP minor frames of data, parsed so that the first minor frame is always mod 020.  That is, the first TIP minor frame in each data record is either 000, 020, 040, 060, 080, 100, 120, 140, 160, 180, 200, 220, 240, 260, 280, or 300.  The following is a byte by byte description of the contents of an incremental file data record.

| Byte | Contents | Comments |
| --- | --- | --- |
| 001-002 | TIP major frame number 0 to 7 |  |
| 003-004 | TIP minor frame number at start of this 2-second data record |  |
| 005-006 | 4-digit year at start of this 2-second data record |  |
| 007-008 | 3 digit day of year at start of this 2-second data record |  |
| 009-010 | Not used |  |
| 011-012 | Satellite clock drift relative to UTC in milliseconds | nominally near zero |
| 013-016 | Time in milliseconds the day at start of this 2-second record |  |
| 017-018 | Satellite travel direction indicator, north or south | note (1) |
| 019-028 | Not used |  |
| 029-032 | Quality indicator flags | note (2) |
| 033-036 | Time quality and satellite location quality flags | note (3) |
| 037-048 | Not used |  |
| 049-052 | Satellite orbital navigation/attitude status flags | note (4) |
| 053-056 | Time associated with TIP Euler angles | note (5) |
| 057-058 | Roll Euler angle | note (5) |
| 059-060 | Pitch Euler angle | note (5) |
| 061-062 | Yaw Euler angle | note (5) |
| 063-064 | Satellite altitude above reference geoid in tenths km |  |
| 065-068 | Geodetic sub-satellite latitude | note (6) |
| 069-072 | Geodetic sub-satellite longitude | note (6) |
| 073-080 | Not used |  |
| 081-088 | Missing data flags, 20 entries each for TIP word 20 and 21 | note (7) |
| 089 | TIP word 20, start TIP minor frame plus 00 |  |
| 090 | TIP word 21, start TIP minor frame plus 00 |  |
| 091 | TIP word 20, start TIP minor frame plus 01 |  |
| 092 | TIP word 21, start TIP minor frame plus 01 |  |
| 093 | TIP word 20, start TIP minor frame plus 02 |  |
| 094 | TIP word 21, start TIP minor frame plus 02 |  |
| 095 | TIP word 20, start TIP minor frame plus 03 |  |
| 096 | TIP word 21, start TIP minor frame plus 03 |  |
| 097 | TIP word 20, start TIP minor frame plus 04 |  |
| 098 | TIP word 21, start TIP minor frame plus 04 |  |
| 099 | TIP word 20, start TIP minor frame plus 05 |  |
| 100 | TIP word 21, start TIP minor frame plus 05 |  |
| 101 | TIP word 20, start TIP minor frame plus 06 |  |
| 102 | TIP word 21, start TIP minor frame plus 06 |  |
| 103 | TIP word 20, start TIP minor frame plus 07 |  |

| Byte | Contents | Comments |
| --- | --- | --- |
| 104 | TIP word 21, start TIP minor frame plus 07 |  |
| 105 | TIP word 20, start TIP minor frame plus 08 |  |
| 106 | TIP word 21, start TIP minor frame plus 08 |  |
| 107 | TIP word 20, start TIP minor frame plus 09 |  |
| 108 | TIP word 21, start TIP minor frame plus 09 |  |
| 109 | TIP word 20, start TIP minor frame plus 10 |  |
| 110 | TIP word 21, start TIP minor frame plus 10 |  |
| 111 | TIP word 20, start TIP minor frame plus 11 |  |
| 112 | TIP word 21, start TIP minor frame plus 11 |  |
| 113 | TIP word 20, start TIP minor frame plus 12 |  |
| 114 | TIP word 21, start TIP minor frame plus 12 |  |
| 115 | TIP word 20, start TIP minor frame plus 13 |  |
| 116 | TIP word 21, start TIP minor frame plus 13 |  |
| 117 | TIP word 20, start TIP minor frame plus 14 |  |
| 118 | TIP word 21, start TIP minor frame plus 14 |  |
| 119 | TIP word 20, start TIP minor frame plus 15 |  |
| 120 | TIP word 21, start TIP minor frame plus 15 |  |
| 121 | TIP word 20, start TIP minor frame plus 16 |  |
| 122 | TIP word 21, start TIP minor frame plus 16 |  |
| 123 | TIP word 20, start TIP minor frame plus 17 |  |
| 124 | TIP word 21, start TIP minor frame plus 17 |  |
| 125 | TIP word 20, start TIP minor frame plus 18 |  |
| 126 | TIP word 21, start TIP minor frame plus 18 |  |
| 127 | TIP word 20, start TIP minor frame plus 19 |  |
| 128 | TIP word 21, start TIP minor frame plus 19 |  |
| 129-132 | Not used |  |
| 133-134 | TIP word 08 status1 and status2 availability flags | note (8) |
| 135-136 | TIP word 08 status1 and status2 contents | note (9) |
| 137-140 | Not used |  |
| 141-144 | TIP word 09 and word 10 housekeeping availability flags | note (10) |
| 145-166 | TIP word 09 and word 10 housekeeping values | note (11) |
| 167-512 | Not used |  |

Notes for Table VI C-1

This documentation is obtained from Table 8.3.1.8.3-1 of the NOAA KLM Users Guide available from URL http://www2.ncdc.noaa.gov/docs/klm/index.htm.  As noted below, it appears some of this documentation is in error.

- The direction of satellite travel is required for calculation of sensor look angles with

respect to the geomagnetic field

- These bytes key various timing and earth location problems according to the following

bit assignments.  If the bit is set to 1, the statement is true.

bit 8, MSB of byte 29	this 2-second frame is not valid

bit 7			time sequence error in this 2-second frame

bit 6			a data gap precedes this 2-second frame

bit 5			not used

bit 4			earth location data not available (bytes 65-72 set to zero)

bit 3			first good time following a s/c clock update

bit 2			SEM instrument status changed beginning this frame

bit 1, LSB of byte 29	not used

bytes 30-32		not used

- These bytes provide details of the problems flagged in bytes 29-32.  If the bit is set to 1	the statement is true.

byte 33			not used

bit 8, MSB of byte 34	time is bad but probably can be inferred from previous time

bit 7			time is bad and cannot be inferred from previous time

bit 6			there is a time discontinuity, including a clock update

bit 5			this time starts a sequence that duplicates previous times

bits 4-1			not used

byte 35			not used

bit 8, MSB of byte 36	no earth location because of bad time.  (bytes 65-72 set to zero)

bit 7			earth location questionable because of questionable time

bit 6	earth location questionable – marginal agreement with ‘reasonableness check’

bit 5	earth location questionable – fails ‘reasonableness check’

bits 04-01	not used.

(4)	These bytes key satellite location and attitude problems.  Detailed documentation of the

contents of these bytes is given in the NOAA KLM Users Guide.  However, a survey of

the data in the incremental files shows that bytes 49-52 are always zero and it seems that

satellite attitude quality flags are not introduced in the SEM-2 incremental data file

(5)	These bytes contain information about the actual satellite attitude. Detailed

documentation of the contents of these bytes is given in the NOAA KLM Users Guide.  However, a survey of data in the incremental files shows that bytes 53-62 are always zero and it seems that satellite attitude status data are not introduced in the SEM-2 incremental data file

- The signed integer values bytes 65-68 and 69-72 are divided by decimal 10000. to obtain the sub-satellite latitude and longitude respectively.  Latitudes are negative in the southern hemisphere and the longitude is negative in the western hemisphere.

- The incremental data file flags those instances when data from TIP words 20 and 21 could not be recovered because of bit sync loss and the data padded with value 000.  This information is important to the further processing of SEM-2 data.  The bit assignments in bytes 81-88 are as follows

bits 8-1, byte 81		not used

bits 8-1, byte 82		not used

bits 8-2, byte 83		not used

bit 1 LSB of  byte 83	if 1, TIP word 21, minor frame +19 is padded

bit 8, MSB of byte 84	if 1, TIP word 20, minor frame +19 is padded

bit 7			if 1, TIP word 21, minor frame +18 is padded

bit 6			if 1, TIP word 20, minor frame +18 is padded

bit 5			if 1, TIP word 21, minor frame +17 is padded

bit 4			if 1, TIP word 20, minor frame +17 is padded

bit 3			if 1, TIP word 21, minor frame +16 is padded

bit 2			if 1, TIP word 20, minor frame +16 is padded

bit 1, LSB of byte 84	if 1, TIP word 21, minor frame +15 is padded

bit 8, MSB of byte 85	if 1, TIP word 20, minor frame +15 is padded

bit 7			if 1, TIP word 21, minor frame +14 is padded

bit 6			if 1, TIP word 20, minor frame +14 is padded

bit 5			if 1, TIP word 21, minor frame +13 is padded

bit 4			if 1, TIP word 20, minor frame +13 is padded

bit 3			if 1, TIP word 21, minor frame +12 is padded

bit 2			if 1, TIP word 20, minor frame +12 is padded

bit 1, LSB of byte 85	if 1, TIP word 21, minor frame +11 is padded

bit 8, MSB of byte 86	if 1, TIP word 20, minor frame +11 is padded

bit 7			if 1, TIP word 21, minor frame +10 is padded

bit 6			if 1, TIP word 20, minor frame +10 is padded

bit 5			if 1, TIP word 21, minor frame +09 is padded

bit 4			if 1, TIP word 20, minor frame +09 is padded

bit 3			if 1, TIP word 21, minor frame +08 is padded

bit 2			if 1, TIP word 20, minor frame +08 is padded

bit 1, LSB of byte 86	if 1, TIP word 21, minor frame +07 is padded

bit 8, MSB of byte 87	if 1, TIP word 20, minor frame +07 is padded

bit 7			if 1, TIP word 21, minor frame +06 is padded

bit 6			if 1, TIP word 20, minor frame +06 is padded

bit 5			if 1, TIP word 21, minor frame +05 is padded

bit 4			if 1, TIP word 20, minor frame +05 is padded

bit 3			if 1, TIP word 21, minor frame +04 is padded

bit 2			if 1, TIP word 20, minor frame +04 is padded

bit 1, LSB of byte 87	if 1, TIP word 21, minor frame +03 is padded

bit 8, MSB of byte 88	if 1, TIP word 20, minor frame +03 is padded

bit 7			if 1, TIP word 21, minor frame +02 is padded

bit 6			if 1, TIP word 20, minor frame +02 is padded

bit 5			if 1, TIP word 21, minor frame +01 is padded

bit 4			if 1, TIP word 20, minor frame +01 is padded

bit 3			if 1, TIP word 21, minor frame +00 is padded

bit 2			if 1, TIP word 20, minor frame +00 is padded

bit 1, LSB of byte 88	not used

- Bytes 133 to 134 key whether updated instrument status data from TIP word 08 is in this minor frame.  The bit assignments are as follows

bit 8, MSB of byte 133	if 0, update of microprocessor system ID occurred

bit 7			if 0, update of TED IFC status occurred

bit 6			if 0, update of MEPED IFC status occurred

bit 5			if 0, update of TED electron PHD level occurred, MSB

bit 4			if 0, update of TED electron PHD level occurred, LSB

bits 3-1			not used

bit 8, MSB of byte 134	if 0, update of microprocessor A watchdog occurred

bit 7			if 0, update of microprocessor B watchdog occurred

bit 6			if 0, update of TED proton PHD level occurred, MSB

bit 5			if 0, update of TED proton PHD level occurred, LSB

bits 4-1			not used

(9)	Bytes 135-136 contain the actual instrument status bits according to the following assignments

bit 8, MSB of byte 135	microprocessor system ID, 0 for processor A

bit 7			TED IFC, 0=off, 1=on

bit 6			MEPED IFC, 0=off, 1=on

bit 5			TED electron PHD level, MSB

bit 4			TED electron PHD level, LSB

bits 3-1			not used

bit 8, MSB of byte 136	microprocessor A watchdog, 0=normal

bit 7			microprocessor B watchdog, 0=normal

bit 6			TED proton PHD level, MSB

bit 5			TED proton PHD level, LSB

bits 4-1			not used

(10)	Bytes 141-144 key whether updated instrument analog housekeeping data from TIP words 09 and 10 are in this minor frame.  The bit assignments are as follows

byte 141		not used

bit 8, MSB of byte 142	not used

bit 7			if 0, update of primary bus voltage monitor

bit 6			if 0, update of backup pitch coil driver monitor (attitude control)

bit 5			if 0, update of primary pitch coil driver monitor (attitude control)

bit 4			if 0, update of backup roll/yaw coil driver

bit 3			if 0, update of primary roll/yaw coil driver

bit 2			if 0, update of Z axis gyro torque current monitor

bit 1, LSB of byte 142	if 0, update of Y axis gyro torque current monitor

bit 8, MSB of byte 143	if 0, update of X axis gyro torque current monitor

bit 7			if 0, update of S gyro torque current monitor

bit 6			if 0, update of DPU temperature monitor

bit 5			if 0, update of TED temperature monitor

bit 4			if 0, update MEPED proton telescope temperature monitor

bit 3			if 0, update of MEPED circuit temperature monitor

bit 2			if 0, update of Omni detector bias voltage monitor

bit=1, LSB of byte 143	if 0, update of TED proton CEM high voltage monitor

bit 8, MSB of byte 144	if 0, update of TED electron CEM high voltage monitor

bit 7			if 0, update of TED sweep voltage monitor

bit 6			if 0, update of TED +5V monitor

bit 5			if 0, update of MEPED +5V monitor

bit 4			if 0, update of DPU +5V monitor

bit 3			if 0, update of microprocessor B +5V monitor

bit 2			if 0, update of microprocessor A +5V monitor

bit 1, LSB of byte 144	not used

(11)	Actual values of TIP analog housekeeping words 09 and 10 refreshed only when the corresponding bit in bytes 142-144 is set to 0.

byte 145		microprocessor A +5V monitor

byte 146		microprocessor B +5V monitor

byte 147		DPU +5V monitor

byte 148		MEPED +5V monitor

byte 149		TED +5V monitor

byte 150		TED sweep voltage monitor

byte 151		TED electron CEM high voltage monitor

byte 152		TED proton CEM high voltage monitor

byte 153		MEPED Omni detector bias voltage monitor

byte 154		MEPED electronics circuit temperature monitor

byte 155		MEPED proton telescope temperature monitor

byte 156		TED temperature monitor

byte 157		DPU temperature monitor

byte 158		S gyro torque current monitor

byte 159		X gyro torque current monitor

byte 160		Y gyro torque current monitor

byte 161		Z gyro torque current monitor

byte 162		Primary roll/yaw coil driver current monitor

byte 163		Backup roll/yaw coil driver current monitor

byte 164		Primary pitch coil driver current monitor

byte 165		Backup pitch coil driver current monitor

byte 166		Primary bus voltage monitor

An extensive survey of SEM incremental data files was done to verify this documentation.  Of the bytes between 29 and 62 inclusive, that include navigation error flags and information about the Euler angles, only bytes 29, 34, and 36 ever show values other than 000.  The conclusion is that, the documentation notwithstanding, navigation/attitude status flags (bytes 49-52) and Euler angle information (bytes 53-62) are not provided.

Moreover, certain bits in bytes 29, 34, and 36, that are defined as providing status, never seem to be used.  Specifically: bit 3 in byte 29 (first good time following a s/c clock update) is never set to 1; bit 8 in byte 34 (time is bad but probably can be inferred from previous time) nor bit 5 in byte 34 (this time starts a sequence that duplicates previous times) are never set to 1;  bit 6 in byte 36 (earth location questionable – marginal agreement with ‘reasonableness check’) nor bit 5 in byte 36 (earth location questionable – fails ‘reasonableness check’) are never set to 1.

The study did confirm that bit 2 in byte 29 (SEM instrument status changed beginning this frame) is a reliable indicator of when the TED or MEPED are undergoing IFC.  The combination of bit 8 in byte 29 (this 2-second frame is not valid) set to 1, bit 7 in byte 29 (time sequence error in this 2-second frame) set to 1, bit 4 in byte 29 (earth location data not available) set to 1, AND bit 8 in byte 36 (no earth location because of bad time) set to 1 proves to be a reliable indicator of zero fill in the earth location field (bytes 65 to 72.)

Information about when the magnetic torque coils were energized, a procedure required to maintain S/C attitude control, was introduced into the SEM data record.  This was done because of concern that when the coils were energized the measurement of low energy particles by the TED would be compromised.  The analysis to determine whether or not the TED observations are influenced by the torque coils has not been done.  However, it was verified that data in bytes 162 to 165 do reflect those times when the roll/yaw and pitch coils are energized and so that analysis of any impact on TED can be done.