# TABLE OF CONTENTS

TABLE OF CONTENTS	1

1. Features	2

1.1S3 Trio3D2X (362) and Trio3D2X+(368) Features	2

1.2 S3 MX (260) Features:	3

1.3 S3 Savage 3D(391) Features:	4

2. Hardware Installation	5

2.1 Package Contents	5

2.2 Installing the Card	5

2.3 Resolutions and colors supported:	6

2.3.1 S3 MX (260)	6

2.3.2 S3 Savage 3D (391)	7

2.3.3 S3 Trio3D/2X (362/368)	8

3. Smart Installation	9

4. Windows 95 & Windows 98 Setup	11

4.1 Installation and Setup	11

4.1.1 Windows 95	11

4.1.2 Windows 98	14

4.2 How to Change Color Depth and Resolution	19

4.3 Change Refresh Rate	20

5. Windows NT 3.51, 4.0	21

6. OS/2 Driver Setup	21

6.1 Installation Instructions	21

6.2 To Change Refresh Rate	22

APPENDIX A - Specifications	23

A.1 Bus Type	23

A.2 Video Connector	23

A.3 Graphics Accelerator	23

A.4 Display Memory	23

APPENDIX B - FCC Statement	24

# 1. Features

This manual is for S3 best quality AGP bus VGA card. The functions and specifications describe as below.

## S3 Trio3D2X (362) and Trio3D2X+(368) Features

# High Performance Integrated 2D/3D Graphics and Video Accelerator

64-bit 2D/3D graphics engine

4MB SGRAM or 8M SDRAM (368 only) on board

Integrated 230MHz RAMDAC with gamma correction

Integrated clock synthesizers

66MHz AGP pipelined DMA mode

133 MHz AGP support

S3d Graphics Engine

High performance 2D acceleration

Flat and Gouraud shading for 3D

High quality 3D texture mapping

Perspective correction

Bi-linear and tri-linear texture filtering.

MIP-Mapping.

Depth cueing, fogging, alpha blending.

Video texture mapping.

Z-buffering.

# Glueless 133MHz AGP

Support AGP DMA mode for highest performance 3D rendering

Bus mastering for high performance video capture and display list processing

PCI Power Management

# Glueless Video Digitizer Interface

Support industry standard video digitizers decoders

Odd/even field detection

# S3 Streams processor Technology

Supports on-the-fly stretching and blending of primary RGB stream and RGB or

YUV(video) secondary stream.

Each stream can have different color depths.

High-quality video playback with horizontal and vertical interpolation.

Green PC/Monitor Plug and Play Support

DPMS monitor power savings modes support

DDC monitor communications

## 1.2 S3 MX (260) Features:

S3 MX 2D/3D Accelerator with LCD Panel controller and PanelLink Sil150 Digital interface using MDR20 Standard Connector

- High performance Integrated 2D/3D Graphics and Multimedia Accelerator

- Integrated 64-bit graphics accelerator/24-bit RAMDAC 135MHz-synthesizer core

- Support resolution up to 1280x1024 for CRT, SXGA for TFT LCD Monitor

- 66MHz Baseline AGP

- Supports SGRAM up to 4MB display memory configurations

- 3rd Generation of S3dTMGraphics Engine

- Flat and Gouraud shading for 3D

- High quality 3D texture mapping

- Perspective correction

- Bi-linear and Tri-linear texture filtering

- MIP-Mapping

- Depth cueing, fogging, alpha blending

- Video texture mapping

- 16-bit hardware Z-buffering

- Improved Multimedia Acceleration

- Integrated S3 Streams Processor supports arbitrary stretching with horizontal and   vertical interpolation

- Brightness, hue, saturation controls

- Color key/ Chroma key control of graphics/video overlay placement

- Low Cost, High Quality, Low Power TV-Out Solution

- Integrated 3.3V NTSC/PAL Compatible TV Encoder

- Composite or S-Video output

- 3-Tap Adaptive Flicker Filtering or TV output for high quality

- Direct Interface to Broad Range of LCD

- VESA P&DTM and VESA FPDI-2TM standard compliant

- Adjustable TMDSTM low-voltage swing signaling for long distance support.

- Support for VGA, SVGA, XGA and SXGA TFT color panel Monitor.

- Advanced frame rate control and dithering algorithms provide up to 16.7million colors

- Panel data polarity switching for EMI reduction

- Auto-expansion and centering for VGA text and graphics modes on SVGA and XGA panels

- Universal transmitter, operates with SiI151, SiI141, SiI101, SiI201 receivers

- MDR20 PanelLinkTM Digital standard connector.

- Comprehensive Power Management

- DPMS and DDC Monitor communication for Green PC and CRT Plug and Play support

S3 Dynamic Power Management

SP260AL SWITCH SETTING

| Panel ID | Panel Type | Resolution | SW[4:1] |
| --- | --- | --- | --- |
| A | TFT | 640X480 | 1110 |
| B | TFT | 800X600 | 1100 |
| C | TFT | 1024X768 | 1010 |
| D | TFT | 1280X1024 | 1000 |

NOTE:  1: ON

0: OFF

## 1.3 S3 Savage 3D(391) Features:

# BUS TYPE: 64bit AGP 2X Side bands 133MHz BUS

CHIP SET: S3 Savage 3D

Memory Size: 8MB SGRAM / SDRAM

2D / 3D Graphics Accelerator

- Enhanced 128 bit Graphics Engine.

- Integrated 250MHZ RAMDAC , supports resolutions and refresh rates up to

1600 x 1200 (85HZ)

- Leading 3D Performance with the highest image quality.

Triangle setup engine delivers 5M triangles / sec

Peak performance rates of 125M pixels / sec with all features enabled

- Complete 3D feature set

Triangle Setup Engine.		Palletized Textures

Single pass Tri-linear Filtering	8KB Texture Cache

S3 Texture Compression		Edge Anti-Alisaing

True Color Rendering			Perspective Correction

Void & Cluster Dithering		Alpha Test

Spectlar & Diffuse Shading		Multiple Textures

Alpha Blending				Procedural Morphing

16/24 bit Z buffering			Texture Morphing

Vertex and Table Fog			Reflection Mapping

MPEG-2 Video Textures		Shadows

- Optimized SW DVD Solution(Optional)

Mpeg-2 acceleration features reduce CPU utilization and provide high frame rates.

Motion Compensation

Sub-picture blending and highlights

Planar to Packed Conversion

Support image quality

Filtered down scaling of host data

- Complete Video Feature Set

YUV Planar to Packed Format Conversion

HW Sub-picture Blending and Highlights

Motion Compensation

Front-end Scalar with high quality Downscaling

Advanced Pixel Formatter for Multiple Video Windows

Advanced Streams Processor with Enhanced Scaling Algorithm

Bus Mastering of IDCT Data for SW DVD Playback

De-Interlacing Filter for Bob & Weave.

Independent Color Adjustment

3-tap Programmable Flicker Filter & Vertical Overscan Compensation

Integrated NTSC/PAL Encoder with S-Video, AV connector Support

- S3 391 TV OUT SELECT

If you want to select TV OUT, you must set the resolution at 640X480 mode.

(NTSC/PAL are same)

# 2. Hardware Installation

## 2.1 Package Contents

- S3 Accelerator card.

- CD title or Software diskettes

- This manual (optional).

## 2.2 Installing the Card

- Turn off your computer.

- Remove the cover of the computer per the owner’s manual.

- Install the card in one of the PCI bus slots.

- Replace the cover.

# 2.3 Resolutions and colors supported:

All S3 Family PCI/AGP bus VGA cards are fully compatible VGA with the addition of Hi-Color and True Color modes depending on the amount of video memory stalled. The amount of memory needed to display various resolutions is shown below (Table 1,2,3)

#### 2.3.1 S3 MX (260)

| Resolution & Colors | BPP | Refresh Rate (HZ) | 1MB | 2MB | 4MB |
| --- | --- | --- | --- | --- | --- |
| 640x480-256c | 8 | 60/72/75/85 | ( | ( | ( |
| 640x480-32Kc | 15 | 60/75/85 | ( | ( | ( |
| 640x480-64Kc | 16 | 60/75/85 | ( | ( | ( |
| 640x480-16Mc | 24 | 60/75/85 |  | ( | ( |
| 800x600-256c | 8 | 56/60/72/75/85 | ( | ( | ( |
| 800x600-32Kc | 15 | 60/75/85 | ( | ( | ( |
| 800x600-64Kc | 16 | 60/75/85 | ( | ( | ( |
| 800x600-16Mc | 24 | 60//75/85 |  | ( | ( |
| 1024x768-256c | 8 | 43(I)/60/70/75/85 | ( | ( | ( |
| 1024x768-32Kc | 15 | 43(i)/60/75 |  | ( | ( |
| 1024x768-64Kc | 16 | 43(i)/60/75 |  | ( | ( |
| 1024x768-16Mc | 24 | 43(i)60/75 |  |  | ( |
| 1152x864-256c | 8 | 60 | ( | ( | ( |
| 1280x1024-256c | 8 | 43(i)/60/75 |  | ( | ( |
| 1280x1024-32Kc | 15 | 43(i)/60 |  |  | ( |
| 1280x1024-64Kc | 16 | 43(i)/60 |  |  | ( |

( (I):interlaced  (:Support  x: Not Support )

Table 1

#### 2.3.2 S3 Savage 3D (391)

| Resolution & Colors | BPP | Refresh Rate (HZ) | 1MB | 2MB | 4MB | 8MB |
| --- | --- | --- | --- | --- | --- | --- |
| 640x480-256c | 8 | 60/72/75/85 | ( | ( | ( | ( |
| 640x480-64Kc | 16 | 60/72/75/85 | ( | ( | ( | ( |
| 640x480- True | 32 | 60/72/75/85 |  | ( | ( | ( |
| 720x576-256c | 8 | 60/72/75 |  | ( | ( | ( |
| 720x576-64Kc | 16 | 60/72/75 |  | ( | ( | ( |
| 720x576- True | 32 | 60/72/75 |  |  | ( | ( |
| 800x600-256c | 8 | 56/60/72/75/85 | ( | ( | ( | ( |
| 800x600-64Kc | 16 | 56/60/72/75/85 | ( | ( | ( | ( |
| 800x600- True | 32 | 56/60//72/75/85 |  | ( | ( | ( |
| 1024x768-256c | 8 | 60/70/75/85 | ( | ( | ( | ( |
| 1024x768-64Kc | 16 | 60/70/75/85 |  | ( | ( | ( |
| 1024x768- True | 32 | 60/70/75/85 |  |  | ( | ( |
| 1280x1024-256c | 8 | 60 |  | ( | ( | ( |
| 1280x1024-64Kc | 16 | 60 |  |  |  | ( |
| 1280x1024-True | 32 | 60 |  |  |  | ( |

( (I):interlaced  (:Support  x: Not Support )

Table 2

#### 2.3.3 S3 Trio3D/2X (362/368)

| Resolution & Colors | BPP | Refresh Rate (HZ) | 4MB | 8MB |
| --- | --- | --- | --- | --- |
| 640x480-256c | 8 | 60/72/75/85 | ( | ( |
| 640x480-64Kc | 16 | 60/75/75/85 | ( | ( |
| 640x480-16Mc | 24 | 60/72/75/85 | ( | ( |
| 800x600-256c | 8 | 56/60/72/75/85 | ( | ( |
| 800x600-64Kc | 16 | 56/60/72/75/85 | ( | ( |
| 800x600-16Mc | 24 | 56/60//72/75/85 | ( | ( |
| 1024x768-256c | 8 | 43(I)/60/70/75/85 | ( | ( |
| 1024x768-64Kc | 16 | 43(i)/60/70/75/85 | ( | ( |
| 1024x768-16Mc | 24 | 43(i)60/70/75/85 | ( | ( |
| 1152x864-256c | 8 | 60/70/75/85 | ( | ( |
| 1152x864-64Kc | 16 | 60/70/75/85 | ( | ( |
| 1152x864-16Mc | 24 | 60/70/75/85 | ( | ( |
| 1280x1024-256c | 8 | 43(i)/60/75/85 | ( | ( |
| 1280x1024-64Kc | 16 | 43(i)/60/75/85 | ( | ( |
| 1280x1024-16Mc | 24 | 43(i)/60/75/85 | ( | ( |
| 1600x1200-256c | 8 | 48(i)/60/75/85 | ( | ( |

( (I):interlaced  (:Support  x: Not Support )

#### Table 3

# 3. Smart Installation

3.1 Put the Smart Installation CD in your CD-ROM

If your CDROM drive do not support Auto-insertion

Please run “D:\Sinstall\Sinstall.exe”

(D means the letter of your CDROM drive)

3.2 Click the FLAG or the country name to choose the language you preferred.

Then Click the Driver installation button

3.3 Comes up the Confirm Installation window.

If the information and drivers location is correct

Then Click OK, If you want to change drivers location,

Click Browse and give the new drivers location now

Then Click OK.

3.4 Now comes up the Driver Confirmation window

Click Install for installation

3.5 Installation already done, the default resolution has been set. you can change resolution under “display property” after system restarted.

# 4. Windows 95 & Windows 98 Setup

## 4.1 Installation and Setup

### 4.1.1 Windows 95

The Windows setup program installs and modifies all of the necessary files. Follow these steps to install the Windows 95 driver.

- Insert the “Window 95 Driver” Installation Diskette or DISC (CD Title Driver).

- Double click Control Panel icon under My Computer group.

- Double-click Display icon under Control Panel folder. You can also click the right mouse button anywhere on the desktop and select the Properties option form the pop-out menu.

.

- Choose Settings and Click Change Display Type button.

- Click Change Adapter Type button.

- Click the Have Disk button.

- Change directories and Select ******.INF. Then click OK.

# Diskette is A: or B:\ WIN95 , Disc (CD Title) is D:\drivers\S3\362\WIN95

(“A:” or “B:”( Diskette Drive  “D:”(CD Drive  “362”(VGA type)

- Select S3 Inc. Trio3D/2X (for SP362/SP368)

or S3 Inc. ViRGE/MX (for SP260)

or S3 Inc. Savage3D (for SP391)

- driver form the models list and click OK button. If a message stating that one or more driver files is older than the files on the system respond YES to overwrite the files.

- Click the Close button and Apply button, and restart your computer.

### 4.1.2 Windows 98

- Double Click Control Panel icon under My Computer group.

- Double-click Display icon under Control Panel folder. You can also click the right mouse button anywhere on the desktop and select the Properties option form the pop-out menu.

- Choose Settings and Click Advanced….

- Select Adapter from Properties window and click Change

- Then show Update Device …. window

Click Next

- Then show another Update Device …. window

Check Search for a better……

Then click Next.

- Then comes up another Update Device …. window

Check Specify a location and click Browse

- Then comes up the Browse for Folder window

Select D:\Drivers\S3\362\Win98

Then select OK

(“D:”(CD Drive  “362”(VGA type)

- Then come back the previous Update Device Driver Wizard window

Click Next

- Then comes up another Update Device Driver Wizard window

Select Next

- Then comes up the last Update Device Driver Wizard window

Select Finish

- Now comes up System Settings Change window

Click YES to restart the system.

## 4.2 How to Change Color Depth and Resolution

- Make sure that you have installed the Windows95/98 Driver.

- Click on the Start box in the lower left corner and proceed to Control Panel.

- Inside the Control panel group , click on Display icon to open the Display Properties folder and select the Setting table

- Click on the pull-down arrow from the Color palette area to select color depth or adjust the sliding bar to either Less or More from the Desktop area

- Select OK to restart system and new color depth or the new resolution takes effect.

## 4.3 Change Refresh Rate

- Make sure that you have installed the Windows95 Driver. Click on the Start box in the lower left corner and proceed to Setting, Control Panel

- Inside the Control panel group , click on Display icon to open the Display Properties folder and select the S3 Refresh table

- Click on the Change Configuration to change refresh rate

- Select OK and new refresh rate takes effect

- Refresh Rate default is Optimal .

- If you change Refresh Rate from Optimal to another , you must be to restart Windows95

# 5. Windows NT 3.51, 4.0

# The following steps describe how to install WIN NT 3.51 and 4.0 display drivers

- Select Control Panel from the Main group.

- Select the Display icon.

- Select Change Display Type.

- Select Change from the Adapter Type area.

- Select Other.

- Place the Windows NT Installation Disk or Disc (CD Title) into Driver. Click OK.

- Select Install and click “YES” when the Installing Driver dialog box appears.

- When the WINDOWS NT Setup dialog box appears select driver A or CD- ROM, and click ”Continue”.

A message appears stating that drivers were successfully installed. Click OK. Another message appears stating that the driver could not be restarted dynamically. Restart Windows NT to run the new driver. Click OK.

# 6. OS/2 Driver Setup

## 6.1 Installation Instructions

- Open an OS/2 command prompt (windowed or full screen).

- Insert the OS/2 Installation Diskette into the floppy drive or Disc into to CD- ROM.

- Change to the floppy drive (A: or B:) or Disc (CD- ROM) into which you have inserted the driver diskette or CD ROM. Verify that the diskette (Disc) is labeled “S3 DRVS”. If it is not so labeled , then type label “S3 DRVS”.

- Type “S3INST A: C:” or “S3INST E: C:” and press “Enter”(“A” is the floppy driver, “E” is the CD ROM Driver, “C” is the HDD driver on which OS/2. 2.1 or OS/2 3.0 WARP is installed).

- When prompted, exit the OS/2 command prompt, remove the floppy disk, and shut down and reboot the system.

- Make sure you have all open data files saved before continuing the S3 driver installation.

- Make sure Win-OS/2 session and all Seamless Windows applications are closed (Seamless applications as Windows applications that run on top of the PM Desktop).

- Double click on the “OS/2 System” icon.

- Double click on the “System Setup” icon.

- Double click on the “Display Driver Install” icon.

- When prompted by the Display Driver install dialog, select Primary Display and then click the OK button.

- Select the “32 Bit S3 Display Driver” option form the Primary Display and then click the OK button.

- Select the appropriate option form the Monitor Configuration/Selection Utility dialing, and click the OK button.

- The Source Directory dialog will be displayed. Make sure the source directory is set to the location form which you are installing and select install.

- The installation Program may pause and display prompts to overwrite certain files. Please answer YES for each file.

- You will be given a message stating that you Must shut down and restart your system for the changes to take effect ”Click” the OK button.

- Remove the driver diskette form the floppy drive and Shut down and reboot.

## 6.2 To Change Refresh Rate

- Load and start OS/2 and Insert the “OS/2 drive Installation” diskette (Disc) into your diskette (CD- ROM) drive.

- Go to DOS full screen.

- Copy the “Refresh.exe” program in the \util directory on the “OS/2 drive installation” diskette to your hard disk.

- Start the refresh program and, using the mouse, specify the refresh rate desired for each resolution you may want to run. Note that you must have your mouse driver loaded.

- Changes are not saved when OS/2 is restarted. Therefore, you will have to return the refresh for each new OS/2 session.

# APPENDIX A - Specifications

## A.1 Bus Type

64-bit AGP 1X bus SP260

64-bit AGP 2X bus SP391/SP362/SP368

## A.2 Video Connector

# VGA standard 15 pin analog RGB

S-Video or AV connector for output to TV (SP260/SP391 only)

MDR20 for LCD PANNEL Monitor connector (SP260 only)

## A.3 Graphics Accelerator

- S3 MX or name as SP260

- S3 Trio3D 2X or name as SP362

- S3 Trio3D 2X+ or name as SP368

- S3 Savage 3D or name as SP391

## A.4 Display Memory

- S3 M5			: 4 M byte SGRAM (Standard)

- S3 Trio3D 2X		: 4 M byte SGRAM (Standard)

- S3 Trio3D 2X+	: 8 M byte SDRAM (Standard)

- S3 Savage 3D	: 8 M byte SGRAM/SDRAM (Standard)

# APPENDIX B - FCC Statement

# Federal Communications Commission (FCC) Statement

# RADIO FREQUENCY INTERFERENCE STATEMENT

This equipment has been tested and found to comply with the limits for a class B digital device, pursuant to Part 15 of the FCC rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses and can radiate radio frequency energy and if not install and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

- Reorient the receiving antenna.

- Increase the separation between the equipment and receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

- Consult the dealer or and experienced Radio/TV technician for help.

Any special accessories needed for compliance must be specified in the instruction manual.

Warning: A wielded-Type power cord in required in order to meet FCC emission limits and also to prevent interference to the nearby Radio and Television reception. It is essential that only the supplied power cord be used.

# Use only shielded cables to connect I/O devices to this equipment.

You are cautioned that changes or modifications not expressly approved by the party responsible for compliance could void you authority to operate the equipment.

# Trademark Acknowledgments

# All brand names and trademarks are the property of their owners.