Users
-----

For someone to be able to use the modem port, you MUST have given them a
password.  Do an EU and use W to set the password.  The user can change
it using the NP command over the modem port.

Modem Settings
--------------

The default settings are:  'T E0 V1 X1 Q0 S7=60 S0=0'

Do not change E0, Q0, V1, X1, or S0.  All other settings are fair game.
You can make any changes automatic by putting them in the
INITIALIZE_FILE (see PARMS.DOC)

Modem switches
--------------

You should set your modem to hangup and enter command mode when DTR goes
low.  On older modems, this is a hardware switch.  On newer modems, it
is a software switch (ATSxx=y type).

Some users have reported intermittent crashes during initialization with
certain modems.  A suggested fix is to

    ECHO AT&C1&D2 > COMx

before bringing up the BBS.  The above line can be put in a BAT file.
Substitute a real com number for the "x" above.  This fix will only work
with COM1 and COM2.

User settings
-------------

Recommended user setting for their terminal programs are:

     - Half duplex or Echo on -- Program must supply echo of what is being
       typed.

Forwarding
----------

A typical forwarding script might be:


PATH AA6 B AA4RE
CT*70,8483865
R*call sign*
SAA4RE
R*password
SMYPASS

Note that this represents a change from previous versions.  The CONNECT
message is now taken care of by the code.  The system will also change
speed based on the connect message.