.PL
        WHATS-UP.DOC Release 1.20 Page 1


                             _______

                        ____|__     |                  (tm)
                          --|       |    |-------------------
                            |   ____|__  |  Association of
                            |  |       |_|  Shareware
                            |__|   o   |    Professionals
                          -----|   |   |---------------------
                               |___|___|    MEMBER



                    WHATS-UP (c) Joe Kasser, G3ZCZ, 1990-1991

                               Joe Kasser G3ZCZ/W3
                                    POB 3419
                            Silver Spring, Md. 20918

                              Voice (301) 593 6136
                           Data BBS (301) 593 9067
                           Compuserve (CIS) 70531,1405

        WHATS-UP  is a tool which allows you to capture, decode,  display 
        and  extract for analysis telemetry from the  following  Orbiting 
        Satellites Carrying Amateur Radio (OSCAR). 

        UoSAT-OSCAR 11  1200 baud ASCII Telemetry,
        AMSAT-OSCAR 13  50 baud RTTY Z blocks Telemetry,
        AMSAT-OSCAR 16, WEBER-OSCAR  18 and LUSAT-OSCAR 19  Binary  Tele-
                        metry,
        DOVE-OSCAR 17   ASCII TLM packet Telemetry, 
        Fuji-OSCAR 20   Status and Telemetry. 

        WHATS-UP  will  also allow you to automatically  capture-to  disk 
        morse code telemetry data from AMSAT-OSCAR 21 or any other  morse 
        code telemetry source. 

        WHATS-UP  will also allow you to process any telemetry  data  you 
        have  from  the now re-entered UoSAT-OSCAR 9  and  Fuji-OSCAR  12 
        spacecraft.

        WHATS-UP is a table driven program which uses configuration files 
        to  allow  maximum  flexibility.  If you have  a  Kenwood  Radio, 
        WHATS-UP will monitor a default frequency, the when a  spacecraft 
        comes  up over the horizon, WHATS-UP will tune the Radio's VFO  A 
        to  the spacecraft beacon frequency (plus a presettable   offset) 
        and  set the receive mode for the satellite of interest.  If  the 
        Radio  responds correctly, WHATS-UP will allow you to  read  back 
        the   VFO  A frequency during the pass and capture the data to  a 
        Doppler  measurement file for later import to a spreadsheet.   At 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 2


        the  end  of  the pass, WHATS-UP will return  the  radio  to  the 
        default frequency and communications mode.

        This version of the program is configured for a TNC-1, TNC-2, PK-
        88,  KAM  and PK-232. Note, it will not enable you  to  copy  non 
        packet telemetry if you don't have a multi-mode terminal unit. It 
        will intercept the Microsat Binary telemetry from AMSAT-OSCAR  16 
        (PACSAT),  WEBER-OSCAR 18 (WEBERSAT) and LUSAT-OSCAR  19  (LUSAT) 
        and display and process them as if they were DOVE-OSCAR 17  ASCII 
        telemetry. NOTE: AMSAT have STILL NOT FINALIZED or PUBLISHED  the 
        Binary Telemetry Format for the Microsats.

        The program is distributed as a Shareware product. You may freely 
        copy  and  share the product for non commercial  use,  with  your 
        friends, classmates, associates and radio hams. If you decide  to 
        use  the  product, you are asked to become a registered  user  by 
        completing  the  registration  form and sending  it,  and  $35.00 
        (drawn on a US Bank please) or equivalent in foreign currency  to 
        the author.

        Upon  receipt  of your registration, you will  receive  one  free 
        update disk, telephone and mail (electronic and regular) support. 

        Please  do not use packet radio mail for commercial messages,  or 
        even  those  that may be construed as such by  individual  SYSOPS 
        through whose BBSs the messages may pass.

        This product may not be sold or distributed with another  product 
        without the express written permission of Joe Kasser, G3ZCZ.  Joe 
        Kasser,  G3ZCZ  will  only  support  unmodified  copies  of  this 
        software.  Your comments and suggestions for changes are  however 
        welcome. If you are the first to suggest a change that is  imple-
        mented,  you will be sent a complimentary copy of the  disk  with 
        the change incorporated.

        European Radio Amateur users may register (24.00 Pounds Sterling, 
        includes VAT) and obtain support from Terry Dansey at  ReadyCrest 
        Ltd.,  PO  Box 75, Chatham, Kent, ME5 9DL,  England.   ReadyCrest 
        Ltd.   accepts  credit  cards  (Access,  Visa,   MasterCard   and 
        Eurocard).  Telephones:  Voice 44 (0)634-687168, FAX  44  (0)634-
        687178, Data (BBS) 44 (0)634-200931.

        Potential  Commercial  and Educational Institution  Users  please 
        contact  Joe Kasser directly for modifications and/or details  of 
        Site licensing.







        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 3


                                Table of Contents

        1.0 Introduction
             1.1 Capabilities of WHATS-UP
             1.2 Program Requirements
             1.3 Packet Link Quality Measurements
             1.4 Copying Non-packet Telemetry
             1.5 Obtaining Updates
             1.6 Limit Checking
             1.7 Radio Control
             1.8 Using Diferent Terminal Units and TNCs.

        2.0 Customization
             2.1 Bringing WHATS-UP up for the First Time.
             2.2 Editing the Configuration File.
             2.3 Starting the program.
             2.4 Screen Areas.
             2.5 Setting Up Customized Display Pages.

        3.0 Modes
             3.1 Standby Mode
             3.2 Interactive Mode
             3.3 Real Time Mode
             3.4 Orbital Dynamics Mode
             3.5 Playback Mode
             3.6 (Data) Extraction Mode
             3.7 Audio Warnings and Orbit Data Displays
             3.8 Autotrack

        4.0 Menus
             4.1 Function Keys
                  4.1.1 FK 1 capture to disk Toggle
                  4.1.2 FK 2 type  of display Engineering Units/Raw  Byte 
                             Toggle
                  4.1.3 FK 3 select display page
                  4.1.4 FK 4 Change Doppler frequency display
                  4.1.5 Alt-B send a 'Break' to the TNC 
                  4.1.6 Alt-C connect to another packet station
                  4.1.7 Alt-D disconnect from another packet station
                  4.1.8 Alt-F flush receiver buffer
                  4.1.9 Alt-I autotrack toggle
                  4.1.10 Alt-J jump to DOS (shell)
                  4.1.11 Alt-P Printer on/off toggle
                  4.1.12 Alt-S Sound on/off toggle
                  4.1.13 Alt-X Quit Mode
                  4.1.14 Alt += debug toggle
                  4.1.15 left arrow decreases playback speed
                  4.1.16 right arrow increases playback speed.




        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 4


             4.2 Modes menu
                  4.2.1 Extract From Playback File
                  4.2.2 Interactive Mode
                  4.2.3 Orbital Parameters
                  4.2.4 Playback Mode
                  4.2.5 Real Time Mode
                  4.2.6 Selections Menu
                  4.2.7 Exit to Dos

             4.3 Selections Menu
                  4.3.1 Change Display Page
                  4.3.2 Edit Menu
                  4.3.3 Files Menu
                  4.3.4 Help Menu
                  4.3.5 Jump to DOS
                  4.3.6 Modes Menu
                  4.3.7 Orbits Menu
                  4.3.8 Radio Menu
                  4.3.9 Spacecraft Menu
                  4.3.10 PK232 Menu
                  4.3.11 Utilities Menu
                  4.3.12 Exit to DOS

             4.4 Edit menu
                  4.4.1 Edit Spacecraft Doppler File
                  4.4.2 Edit Any File
                  4.4.3 Edit Orbital Data File
                  4.4.4 Edit Spacecraft Configuration File
                  4.4.5 Pick Capture-to-disk File
                  4.4.6 Edit Capture-to-disk File
                  4.4.7 Edit WHATS-UP.SYS
                  4.4.8 Edit Two Files
                  4.4.9 Edit Doppler Channel File
                  4.4.10 Edit Doppler Data File
                  4.4.11 Pick Spacecraft Configuration .SYS File

             4.5 Files Menu
                  4.5.1 Change Directory Path
                  4.5.2 Change Playback File
                  4.5.3 View Playback File
                  4.5.4 Show Capture-to-disk Files
                  4.5.5 Show Data Files
                  4.5.6 Show Files for 1 Spacecraft

             4.6 Orbits Menu
                  4.6.1 Pick AMSAT Format Element Set
                  4.6.2 Edit WHATS-UP.2LN
                  4.6.3 Load Element File
                  4.6.4 Pick NASA 2 Line Element Set
                  4.6.5 View Spacecraft Orbit Elements


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 5



             4.7 Radio Menu
                  4.7.1 Turn Doppler Tracking On/Off
                  4.7.2 Set New Frequency
                  4.7.3 Change Doppler Interval
                  4.7.4 Read VFO A Frequency
                  4.7.5 Set Default Frequency
                  4.7.6 Select VFO A/B

             4.8 Spacecraft Menu
                  4.8.1 show Spacecraft Configuration file
                  4.8.2 picK Spacecraft
                  4.8.3 Change Spacecraft
                  4.8.4 Pick Ops. Schedule
                  4.8.5 Show Ops. Schedule

             4.9 TNC Menu
                  4.9.1 UoSAT ASCII Beacon
                  4.9.2 Phase 3 RTTY Beacon
                  4.9.3 Set Morse Code (CW)
                  4.9.4 Fuji/MicroSat ASCII Packet
                  4.9.5 Configure TNC
                  4.9.6 FM Packet
                  4.9.7 SARA ASCII Beacon
                  4.9.8 Set TNC Radio Port

              4.10 Utilities Menu
                  4.10.1 Change Directory Path
                  4.10.2 Show Space on Disk
                  4.10.3 Reset Header Counters
                  4.10.4 Show Defaults
                  4.10.6 Show Color Chart
                  4.10.7 Reconfigure WHATS-UP
                  4.10.8 Enable/Disable TNC Port
              
             4.11 Debug Menu
                  4.11.1 Sound CW String
                  4.11.2 Turn Debug OFF
                  4.11.3 Set Frequency
                  4.11.4 Interrogate Radio
                  4.11.5 Show Defaults
                  4.11.6 Talk to Radio
                  4.11.7 Speak Frequency
                  4.11.8 Identify Radio

        5.0 Orbital Elements
             5.1 Basics
             5.2 Orbital Trajectories
             5.3 Types of orbits
             5.4 Orbital Elements


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 6


             5.5 Angle of Inclination.
             5.6 Right Ascension of Ascending Node (RAAN).
             5.7 Eccentricity and Semimajor Axis
             5.8 Decay Rate
             5.9 Argument of Perigee.
             5.10 Epoch Time (of Ascending Node) and Revolution Number.
             5.11 The Mean Motion.
             5.12 The Catalog Number 
             5.13 Mean Anomaly
             5.14 Anticipated Spacecraft Lifetimes

        6.0 The Spacecraft 
             6.1 Receiving system components
                  6.1.1 Antennas
                  6.1.2 Receivers
                  6.1.3 Terminal Units or Modems
             6.2 Receiving Signals from DOVE
             6.3 Receiving Signals from UoSAT-OSCAR 11
             6.4 Receiving Signals from AMSAT-OSCAR 13
             6.5 Receiving PSK Modulated Signals in the 70 cm Band
             6.6 Receiving Signals from SARA-OSCAR 23.

        7.0 Decoding Active Spacecraft Telemetry
             7.1 DOVE-OSCAR 17
             7.2 UoSAT-OSCAR 11
             7.3 AMSAT-OSCAR 13
             7.4 AMSAT-OSCAR 16, WEBER-OSCAR 18 and LUSAT-OSCAR 19 
             7.5 Fuji-OSCAR 20
             7.6 AMSAT-OSCAR 21
             7.7 SARA-OSCAR 23

        8.0 Spacecraft No Longer Active
             8.1 Fuji-OSCAR 12

        9.0 File formats

             9.1 Configuration File
                  9.1.1 Your callsign
                  9.1.2 Default spacecraft Name
                  9.1.3 Station Latitude 
                  9.1.4 Station longitude 
                  9.1.5 Station Altitude 
                  9.1.6 Station minimum antenna elevation for acquisition
                  9.1.7 Station minimum usable pass time 
                  9.1.8 Early warning time
                  9.1.9 Default Kepler file
                  9.1.10 UTC offset 
                  9.1.11 Default directory path (e.g. C:)
                  9.1.12 Default extracted data file
                  9.1.13 Default   file  name  with  list  of   telemetry 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 7


                        parameters to extract file
                  9.1.14 TNC Type
                  9.1.15 Serial port to TNC
                  9.1.16 PC TNC Serial baud rate
                  9.1.17 PC TNC port data bits
                  9.1.18 PC TNC port Stop bits
                  9.1.19 PC TNC Port parity bits
                  9.1.20 PC serial port to Radio
                  9.1.22 PC Radio port data bits
                  9.1.23 PC TNC port Stop bits
                  9.1.24 PC Radio Port parity bits
                  9.1.25 Post pass delay 
                  9.1.26 status (top) window color (e.g. 79)
                  9.1.27 incoming window color (e.g. 14)
                  9.1.28 outgoing window color (e.g. 30)
                  9.1.29 prompt window color (e.g. 15)
                  9.1.30 Alarm window color (e.g. 15)
                  9.1.31 Bottom window color (e.g. 79)
                  9.1.32 Emphasis color (e.g. 14)
                  9.1.33 Option color (e.g. 78)
                  9.1.34 Parameter changed color (e.g. 95)
                  9.1.35 Parameter limit exceeded color (e.g. 14)
                  9.1.36 Orbit element window color
                  9.1.37 Orbit element window In range color
                  9.1.38 Orbit element window early warning color
                  9.1.39 Orbit element window next one up color
                  9.1.39 Orbit alert dit time
                  9.1.40 Orbit alert note
                  9.1.41 Flag Sound
                  9.1.42 Doppler display Flag 
                  9.1.43 Spacecraft Configuration File Linkages
                  9.1.44 * Comment line
                  9.1.45 The  remaining  lines are commands sent  to  the 
                        TNC.

             9.2 Spacecraft Parameter Files
                  9.2.1 Spacecraft ID.
                  9.2.2 Spacecraft Suffix
                  9.2.3 Beacon Frequency
                  9.2.4 Doppler Measurement File
                  9.2.5 Spacecraft  Identification in  Keplerian  Element 
                        File
                  9.2.6 Doppler Measurement Sample Interval
                  9.2.7 Initial Frequency Offset
                  9.2.8 Autotrack flag 
                  9.2.9 Modulation
                  9.2.10 Data Type
                  9.2.11 Receiver Type
                  9.2.12 Receiver Address
                  9.2.13 Selected or default display page number


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 8


                  9.2.14 Selected or default display page number
                  9.2.15 Page Definitions
                  9.2.16 Telemetry Parameter Configuration
                         9.2.16.1 TLM_Channel
                         9.2.16.2 TLM_Segment_ID
                         9.2.16.3 TLM_Description
                         9.2.16.4 TLM_Eqn_Type
                         9.2.16.5 TLM_Ceof_C
                         9.2.16.6 TLM_Ceof_B
                         9.2.16.7 TLM_Ceof_A
                         9.2.16.8 TLM_Units
                         9.2.16.9 TLM_Page
                         9.2.16.10 TLM_Row
                         9.2.16.11 TLM_Col
                         9.2.16.12 TLM_Width
                         9.2.16.13 TLM_Dec
                         9.2.16.14 TLM_Limit_Check
                         9.2.16.15 TLM_Limit_Low
                         9.2.16.17 TLM_Limit_High
                         9.2.16.18 TLM_Negative_Blank
                         9.2.16.99 The Telemetry Identifier Line
                               9.2.16.99.1 The Line Identifier
                               9.2.16.99.2 The Segment Identifier
                               9.2.16.99.3 Spare/Not Used
                               9.2.16.99.4 Location of Segment Identifier 
                                           in Line
                               9.2.16.99.5 Spare/Not Used
                               9.2.16.99.6 Spare/Not Used
                               9.2.16.99.7 Spare/Not Used
                               9.2.16.99.8 Segment Identifier String
                                     9.2.16.99.8.1 Fuji
                                     9.2.16.99.8.2 DOVE
                               9.2.16.99.9 Spare
                               9.2.16.99.10 Number of Lines
                               9.2.16.99.11 First Line
                               9.2.16.99.12 Last Line
                               9.2.16.99.13 Header Lines
                               9.2.16.99.14 Character Count 
             9.2.17 Digital Telemetry Status Channels
                  9.2.17.1 Status_Channel
                  9.2.17.2 Status_Display_Page
                  9.2.17.3 Status_Text
                  9.2.17.4 Status_Bit_Mask
                  9.2.17.5 Status_Row
                  9.2.17.6 Status_Col
                  9.2.17.7 Status_ON_Text
                  9.2.17.8 Status_OFF_Text
                  9.2.17.9 Status_ON_Color
                  9.2.17.10 Status_OFF_Color
             9.2.18 Packet/Link Parameters


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 9


                  9.2.18.1 Packet_title
                  9.2.18.2 Packet_Type
                  9.2.18.3 Packet_Lines
                  9.2.18.4 Packet_Page
                  9.2.18.5 Packet_Color
                  9.2.18.6 Packet_Row
                  9.2.18.7 Packet_Col
                  9.2.18.8 Link_Page
                  9.2.18.9 Link_Row
                  9.2.18.10 Link_Col
                  9.2.18.11 Binary_Byte_Count

             9.3 Telemetry Channel Extraction File
             9.4 Extracted Telemetry Data File

             9.5 Doppler Data File
                  9.5.1 The Time 
                  9.5.2 The Doppler Mark 
                  9.5.3 The Frequency 
                  9.5.4 The Doppler Shift 
                  9.5.5 The Measured Shift 

             9.6 Kepler Element Files (*.2LN)
             9.7 AMSAT Format Element File (*.AMS)
             9.8 Spacecraft Operations File

        10.0 Glossary

        11.0 References and Further Reading

        12.0 Change History

        APPENDIX



















        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 10


        1.0 Introduction

        WHATS-UP  is a tool which provides you the Radio Amateur, or  the 
        Educator,   with  the  capability  to  perform   experiments   in 
        spacecraft orbital dynamics as well as monitoring the environment 
        onboard several of the Orbiting Satellites Carrying Amateur Radio 
        (OSCAR) during individual passes or over long periods of time.  

        Spacecraft  in  the OSCAR series send back volumes  of  Telemetry 
        daily  and apart from the odd Command station, few if  any  Radio 
        Amateurs  or Educators seem to be doing anything with  it.  Radio 
        Amateurs  tend to concentrate on the communications  capabilities 
        of the spacecraft and ignore their telemetry completely. If  they 
        do  listen  to  a beacon, it's usually just  to  check  that  the 
        transponder is on, heaven forbid - to actually copy any data.

        The  telemetry  can  tell  us a story. It can  tell  us  what  is 
        happening to both the spacecraft and its environment. As such  it 
        has  a tremendous educational potential which has  remained  just 
        that - a potential for at least the last six years.

        Before  every satellite launch the equations and format  for  the 
        spacecraft telemetry are published by AMSAT. The telemetry  tells 
        us  about  the health and welfare of the spacecraft  itself,  and 
        something  about  the  payload.  Spacecraft  health  and  welfare 
        information tells us about the battery, solar cells and on  board 
        computer  status. Payload information can range from  information 
        about  transponder loading/utilization to data  from  instruments 
        that  measure  the  environment of the space in  and  around  the 
        satellite.  Battery Telemetry is used by the command stations  to 
        determine  when  the  spacecraft  can  be  used,  and  when   the 
        transponders  should be shut down. The number of individuals  not 
        associated  with  command stations who  have  decoded  spacecraft 
        telemetry  and published their findings can be counted using  the 
        fingers  of one hand. There's a lot of computing power out  there 
        that  has  the  potential  to  process  telemetry  and   discover 
        something new, but does not have the access to the data. WHATS-UP 
        is  an attempt to provide that data to the average Radio  Amateur 
        and Educator.

        Capturing,  decoding  and  displaying  telemetry  from   orbiting 
        spacecraft in real time, in the classroom, is an excellent way of 
        introducing  space  science  to  students.   Signals  from  these 
        spacecraft are downlinked on frequencies that can be received  on 
        regular vhf/uhf scanner radio receivers.   
         
        WHATS-UP  provides  an introduction as to how this  can  be  done 
        using  readily  available  low cost  equipment.   General  topics 
        discussed    cover   telemetry,   the   spacecraft    themselves. 
        Groundstation  hardware topics include receiving antennas,  radio 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 11


        receivers  and  modems.  Software topics  discussed  include  the 
        software  used to track the spacecraft and the software  used  to 
        both decode and display the data in real time as well as that for 
        post  pass analysis.  Excluding the Personal Computer,  a  simple 
        telemetry  capturing  groundstation can be set up for  less  than 
        $500.00 in equipment costs.

        There is no substitute from the excitement of hands-on experience 
        in  awakening  an interest in space.  While OSCARs in  the  main, 
        transmit  down to the ground (downlink) telemetry in morse  code, 
        several  of them also utilize standard computer literate  digital  
        data  schemes  such  as BAUDOT or ASCII  codes.   The  thrill  of 
        receiving  a  signal from space soon fades however  if  the  data 
        cannot  be  understood.  Even after the data  has  been  decoded, 
        watching  the  temperatures on-board a spacecraft  as  it  passes 
        overhead  is  also  of little interest, but,  what  can  be  made 
        interesting is receiving and capturing the data over many days or 
        even months and looking for trends and relationships.  

        You  can capture telemetry just by listening to a spacecraft  and 
        copying  morse  code by ear writing it down with a  pencil  on  a 
        piece  of  paper.  All you need to do is listen  on  the  correct 
        frequency  at  the  right time and you will  hear  some  signals.  
        Write  down  what you hear.  Apart from the thrill of  copying  a 
        signal  from  a satellite, there's not much else to do  with  the 
        data.  While you can look up the conversion equations and  get  a 
        snapshot  of what is happening, it soon becomes tedious and  only 
        dedicated souls do it regularly.

        When  AMSAT  were  building the  Phase  3A  spacecraft,  personal 
        computing was in its infancy.  That was before the Apple 2 or the 
        TRS-80; that was the day of the home built S-100 machine, and the 
        AMSAT-GOLEM-80  Project.  At that time, Karl Meinzer, DJ4ZC,  had 
        written a native German high level computer language called  IPS. 
        This  language was very similar to Forth, but contained a  multi-
        tasking kernel. This language was programmed into the  spacecraft 
        flight  computer  and also used in the ground  command  stations.  
        Using  a  computer  on the spacecraft allowed  AMSAT  to  provide 
        telemetry  that  could  be captured by computer  on  the  ground.  
        While  Phase  3A  never made it into orbit  (the  launch  vehicle 
        malfunctioned),  subsequent spacecraft continued to  provide  the 
        same facility.  Today UoSAT-OSCAR 11 (UO-11), AMSAT-OSCAR 13 (AO-
        13),  UoSAT-OSCAR 14 (UO-14), AMSAT-OSCAR 16 (AO-16),  DOVE-OSCAR 
        17  (DO-17), WEBER-OSCAR 19 (WO-18), LUSAT-OSCAR 19  (LO-19)  and 
        Fuji-OSCAR 20 (FO-20) are all sending back telemetry that you can 
        capture  with your PC and amateur radio equipment.  As  most  non 
        radio   amateurs   do  not  understand   morse   code,   WHATS-UP 
        concentrates   on  those  spacecraft  which   downlink   computer 
        compatible  telemetry and can be received with relatively  simple 
        equipment.  


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 12



             1.2 Capabilities of WHATS-UP

             WHATS-UP contains the following features:

             * Display of spacecraft orbital elements and tracking data.

             * Will automatically set your Kenwood receiver to spacecraft 
               beacon  frequency  when the spacecraft  comes  above  your 
               horizon  and return it to the default frequency  when  the 
               pass is over.

             * Audio  warning of spacecraft acquisition of  signal  (AOS) 
               and loss of signal (LOS).

             * Real-time, Interactive and Playback modes.

             * Automatic Capture-to-disk of raw telemetry.

             * Extracts   telemetry  channel  data  to  a   database   or 
               spreadsheet readable file for further analysis.

             * Link quality measurement.

             * Capability to display and print the raw telemetry as it is 
               received.

             * Up  to 16 user configurable display pages  (screens).  You 
               set  the position on the page (width of  engineering  unit 
               field,  and number of decimal places) that a parameter  is 
               displayed at.

             * Wild card page (parameter shows up on all pages).

             * Selectable  display of Engineering units or Hex  byte  for 
               each display page.

             * Display of raw packets (i.e. STATUS)

             * Color  changes  if  a  parameter  value  changed   between 
               successive frames.

             * Audio  and  visual alarms if a  telemetry  value  exceeds, 
               falls below or falls outside a preset limit value(s).

             * Dumb  split  screen  terminal mode  with  user  selectable 
               number of window rows.

             * Customizable colors, PC to TNC baud rate, data parity  and 
               stop bits.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 13



             * Default spacecraft configuration files.

             * UTC Time of day clock display (in HH:MM:SS format)

             1.2 Program Requirements

             IBM PC or clone with at least 256k memory.

             A Radio receiver and a TNC with an RS-232 interface is  only 
             required for real time data capture. 

             The  program DOES require that the packetized  telemetry  be 
             received,  and captured-to-disk with the packet header on  a 
             different  line  to the contents of the  packet  (HEADERLINE 
             ON). I also suggest that you turn the date/time stamp on  so 
             that  you  will be able to playback your  data  and  extract 
             selected  values and their corresponding time codes  into  a 
             file  that  can be read into your  spreadsheet  program  for 
             further trend analysis.
              
             This version (the default) is set up to display all  packets 
             as  wild  cards (i.e. will show up on all pages),  and  then 
             display several temperatures and solar cell array currents.

             By  putting  the correct parameters  in  the  SPACECRAFT.SYS 
             file, you can set up any of the pages to display any of  the 
             telemetry channel data in any row and column in that page.

             1.3 Packet Link Quality Measurements

             The  packet  link quality part allows the  following  to  be 
             done.  You  can  define which of the  packets  you  want  to 
             display/count  (If  you  just want to  count  them  and  not 
             display  them, set the page value to 99). You can then  view 
             an incrementing count counter each time a selected packet is 
             received.  For  example, using DOVE-OSCAR 17, you  can  also 
             display  the contents of the STATUS, WASH or BCRXMT  packets 
             in any display page. This feature allows you to get an  idea 
             of how good your receiving system is.

             1.4 Copying Non-packet Telemetry

             Packet  telemetry,  by definition is error  free.  The  RTTY 
             blocks from AMSAT-OSCAR 13 on the other hand may be received 
             with  errors.  These errors may take the form of garbled  or 
             missing  characters. If your link is bad, and such  hits  do 
             occur,  you should edit the capture-to-disk file before  you 
             playback the telemetry and decode/display the data.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 14


             If you get bad data in real time, look at the raw data.  You 
             will be able to see the quality of the link.

             1.5 Obtaining Updates

             It  is  anticipated  that  WHATS-UP is  going  to  grow  and 
             incorporate  features for decoding and displaying data  from 
             other  spacecraft. Better Microsat binary  telemetry  decode 
             and  display  capability will be added when  AMSAT  announce 
             that  the format has stabilized, and  sufficient  registered 
             users express interest in having it. To stay on the  mailing 
             list and receive an update as it is released, register  your 
             copy,  then send in a disk containing at least  1  Megabytes 
             (zipped)  of  captured  data from  the  spacecraft  of  your 
             choice.  If  you  would like to  exchange  data  with  other 
             educational  institutions  or  users so as  to  be  able  to 
             analyze  more  data  than  you can get  on  a  single  pass, 
             indicate  that  fact and we will try and put you  in  direct 
             touch with others who are similarly inclined.

             1.6 Limit Checking

             Limits  are only checked for parameters being displayed  (in 
             Engineering  units).  With  this approach, you  can  set  up 
             different  pages for different on-board subsystems, you  can 
             also  set up different display pages of the same  parameters 
             for daylight, darkness and terminator crossing passes,  with 
             different limit values to draw your attention to changes.

             1.7 Radio Control

             When you first bring up WHATS-UP, it sets the radio VFO A to 
             the beacon frequency of the default spacecraft configuration 
             file  (*.SYS).  When a selected spacecraft is  scheduled  to 
             come above your horizon WHATS-UP will tune the radio to  the 
             spacecraft's beacon frequency. When the pass is over, WHATS-
             UP  will return the radio to the default frequency. You  can 
             thus  set  up a "dummy" configuration file  for  your  local 
             Packetcluster or voice repeater and monitor that channel  as 
             long as the selected spacecraft are below your horizon.  

             If a pass is taking place, and a second selected  spacecraft 
             comes over your horizon, WHATS-UP will tune to its frequency 
             UNLESS  the  autotrack is disabled. See Section  ***  for  a 
             description of the autotrack feature.

             1.8 Using Different Terminal Units and TNCs.

             This section briefly covers some of the differences  between 
             the  various TNCs on the market.  To copy PSK  signals  from 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 15


             Fuji-OSCAR  20 and the microsats, you will need a PSK  modem 
             adapter  for your TNC. WHATS-UP has no way of checking  that 
             it is present.
             
             1.8.1 PK-232

             The  PK-232  does not have a software selectable  TNC  radio 
             port.  You have to use the switch on the panel.  The  PK-232 
             will  receive  signals  from UO-11  properly,  only  if  the 
             hardware   modification  described  in  this   document   is 
             performed.  

             1.8.2 KAM

             The KAM cannot demodulate SARA's 300 baud ASCII or 1200 baud 
             ASCII, so signals from SARA and UO-11 cannot be copied.  The 
             KAM  2.85  firmware  used to develop  WHATS-UP  assumes  vhf 
             packet  on the vhf port, and the non packet modes on the  hf 
             port.  WHATS-UP  1.20 does not let you switch ports  on  the 
             KAM.

             1.8.3 MFJ-1278

             The  MFJ-1278 cannot copy SARA's 300 baud ASCII  or  UO-11's 
             1200  baud ASCII. WHATS-UP does not change the  radio  port. 
             You  set the radio command in the WHATS-UP.SYS file. If  you 
             wish to change the radio port, an option is provided in  the 
             Configure TNC Menu.

             1.8.4 TNC1, TNC2 and PK-88

             These TNCs only copy packet. The other modes will not work.

        2.0 Customization

             2.1 Bringing WHATS-UP up for the First Time.

             WHATS-UP  comes  configured  to use Com1 in the  PC  as  the 
             serial  port  between the PC and the PK-232,  and  with  the 
             serial  port between the PC and the Kenwood  Radio  DISABLED 
             (Set  to 0).  WHATS-UP is also configured to assume DOVE  as 
             the default spacecraft.

             If  you  type 'WHATS-UP' followed by the  'Enter'  key,  the 
             program  will load and start to do things.  If  the  default 
             serial  ports  are  correct for your  system,  you  need  do 
             nothing further, other than change the colors of the windows 
             to your preference.

             IF  YOU  ARE NOT USING A PK-232 YOU MUST  DO  THE  FOLLOWING 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 16


             STEPS  in DOS BEFORE, BEFORE you run WHATS-UP for the  first 
             time.

             1    Rename WHATS-UP.SYS to WPK232.SYS.
             2    If you are using a KAM, then rename WKAM.SYS to  WHATS-
                  UP.SYS.
             3    If  you are using an MFJ-1278, then rename WMFJ.SYS  to 
                  WHATS-UP.SYS.
             4    If  you are using a packet only TNC (TNC1, TNC2 or  PK-
                  88), then rename WTNC.SYS to WHATS-UP.SYS.

             2.2 Editing the Configuration File.

             The configuration file is called WHATS-UP.SYS. You must edit 
             it  using option 'S' in the Edit Menu or with an ASCII  word 
             processor  (in the non document mode) to set up the  correct 
             parameters on the RS-232 link between your TNC and your  PC. 
             See  Section  10 for details of what parameter is  on  which 
             line of the WHATS-UP.SYS file.  If you wish to activate  the 
             Radio features, you must select a Radio Port.

             Before  you make any changes, make sure that you do not  try 
             and edit your original, always work from a copy.

             These  are the minimum set up items to change in the  WHATS-
             UP.SYS file.  Refer to Section 9 for fuller details of  what 
             items are on which lines.  Bring up the Selections menu, the 
             access  the  Edit Menu. choose the option  for  editing  the 
             WHATS-UP.SYS  file. As you enter items on the  lines  listed 
             below, delete the entries currently in place.

             Line 1:  Enter your callsign instead of the default one. Use 
                      Capital letters (Upper case). If you do not have  a 
                      callsign,  pick  a mnemonic  that  represents  your 
                      school  or  organization.  You may  use  up  to  10 
                      characters.   The  callsign entered here,  will  be 
                      shown  at the top of the status window,  next  time 
                      you  load WHATS-UP, and will also (more  important) 
                      be  appended  to  your  capture-to-disk  files   to 
                      identify  the  ground station  which  received  the 
                      data.

             Line 3:  Enter  the  latitude  of  your  location.  In   the 
                      southern hemisphere, use a negative number.

             Line 4:  Enter the longitude of your station in degrees West 
                      of Greenwich in the range 0 to 359.9.

             Line 5:  Enter  the  station  altitude above  sea  level  in 
                      meters. If you don't know, don't change anything.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 17



             Line 10: Enter the difference between local time in your  PC 
                      and UTC. For example, eastern standard time is 5.

             Line 15: If  you  are  not using Com1  as  the  serial  port 
                      between  the PC and the TNC, enter the port  number 
                      on this line.

             Line 16: If  you are not using 1200 baud between the PC  and 
                      the TNC enter the actual value on this line.

             Line 20: If you have a compatible radio with RS-232  control 
                      capability,  enter  the port number  on  this  line 
                      (usually Port 2).

             Read  Section 9.1 to see what else to change to make the  PC 
             communicate with the TNC and the radio.

             Save  the file at this time. WHATS-UP will now work for  you 
             in  its  minimal mode. Read the manual to  learn  about  its 
             capabilities and use section 9 when you customize it to suit 
             yourself.

             2.3 Starting the program.

             You may start the program in three ways as follows.

                  2.3.1 Default

                  Type 'whats-up' and return (without the '  characters). 
                  This brings the program up in the default mode. It will 
                  read the whats-up.sys file to determine the  spacecraft 
                  being monitored, and then prompt you for the mode.

                  2.3.2 User Chosen spacecraft
                   
                  Type  'whats-up spacecraft' and return (without  the  ' 
                  characters). The program reads the spacecraft.sys  file 
                  to load the parameters for the Microsat of choice,  and 
                  then prompts you for the mode.

                  Examples of the command are :

                   'WHATS-UP DOVE' or 'WHATS-UP Fuji20'

                  2.3.3 Custom Mode

                  Type 'whats-up spacecraft mode' and return (without the 
                  ' characters). This brings the program up in the custom 
                  mode.  It will read the whats-up.sys file to  determine 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 18


                  the  spacecraft being monitored, and then start  up  in 
                  the  mode  you set. Valid modes are 'p', 'i',  'o'  and 
                  'r'.

                  Examples of the command are :

                   'WHATS-UP DOVE R' or 'WHATS-UP Fuji20 R'

                  If  you  place  a  command  line  like  this  in   your 
                  autoexec.bat  file, should you be copying telemetry  in 
                  an  unattended manner and a power failure  take  place, 
                  the system will boot up into the correct WHATS-UP  mode 
                  when power is restored.

                  When the program loads, the first thing it does is load 
                  the  Keplerian  data  from the default  data  file  and 
                  compute the current position of all the spacecraft. The 
                  following  typical  messages will be send  during  this 
                  activity.

                  MIR Loaded
                  RS-10/11 Loaded
                  AO-13 Loaded
                  UO-14 Loaded
                  AO-16 Loaded
                  DO-17 Loaded
                  Computing Next Pass for AO-10
                  Computing Next Pass for UO-11
                  Computing Next Pass for MIR
                  Computing Next Pass for RS-10/11
                  Computing Next Pass for AO-13
                  Computing Next Pass for UO-14
                  Computing Next Pass for AO-16
                  Computing Next Pass for DO-17

                  If  the default Keplerian data file is not  present  on 
                  the  disk,  the orbital mode will be disabled.  If  the 
                  default  Keplerian  data file is empty,  WHATS-UP  will 
                  abort with a Run-Time Error.

             2.4 Screen Areas

             The  screen is divided into four window areas.   The  Status 
             window occupies the top line. The prompt window occupies the 
             bottom  line.  Raw data are always shown in the  lower  data 
             area. This window also shows any outgoing text that you  may 
             type  at the keyboard or any commands WHATS-UP sends to  the 
             TNC.   The data area in the top half of the screen  contains 
             the  processed data (real time and playback), the  raw  data 
             (interactive) and the orbital data display.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 19



             2.5 Setting Up Customized Display Pages

             The  ability  to customize a display page is a  unique  tool 
             provided  by  WHATS-UP.  This  tool  allows  you  to   group 
             telemetry information so you can see how the monitor  points 
             you are interested in behave, and visually see the  changes.  
             You can locate information in any position on the screen and 
             in  any color you wish. You can also perform limit  checking 
             on  the  data,  and  have  the  "out-of-limit"  show  up  in 
             different colors and generate audible alarms.

             Setting  up display pages is an orderly procedure using  the 
             information  contained  in  Section 9.   When  you  want  to 
             customize  the  displays,  make  a  copy  of  the   supplied 
             spacecraft configuration file and work with it. Look at  the 
             format  of  the  file, read Section 9.2  to  sure  that  you 
             understand what is in the file. Use the editor to adjust the 
             items  in the spacecraft configuration file.  After  editing 
             the  file, reload the file to enter the  changed  parameters 
             into  WHATS-UP  to see the effects of your  changes.  Repeat 
             this procedure until you are satisfied.

             First,  from the utilities menu, view the colors and  decide 
             on the color scheme for the window and data.

             Lay out the display page on graph paper for a screen  window 
             of 13 rows by 78 columns.

             Decide  on the name of the page. If it is a new  page  enter 
             the  name on a new line after the existing pages before  the 
             line  that  ends in an '*' character. Do not delete  the  '* 
             character.   After you have entered the page name, insert  a 
             comma character ',' and a number for the default page color. 
             An example from the DOVE.SYS file for such an entry is shown 
             below.

             PAYLOAD TRANSMITTER/RECEIVERS, 30

                  2.5.1 Customizing Analog Telemetry Channel Displays.

                  The  next  few  lines  contain  the  analog   telemetry 
                  decoding  display information.  Review Section  9.2  to 
                  see  what has to be inserted in each of  the  elements. 
                  The  analog  telemetry lines are  terminated  with  the 
                  following  line, which must be present even if no  data 
                  lines are present.

                  '* end of telemetry'



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 20


                  2.5.2 Customizing Status Telemetry Channel Displays.

                  Section 9.2.14 describes the meaning of each item.  The 
                  status   telemetry  lines  are  terminated   with   the 
                  following  line, which must be present even if no  data 
                  lines are present. 

                  '* end of status bytes'

                  2.5.3 Customizing Packet Header Displays.

                  The  packet  header  configuration  lines  contain  the 
                  analog telemetry decoding display information.  Details 
                  of  the  meaning  of each item  are  given  in  section 
                  9.2.15. The packet header lines are terminated with the 
                  following  line, which must be present even if no  data 
                  lines are present.

                  '*  end of packet types'

             If you want to change the colors that channels out of limit, 
             or  channels  in which the data  changed  between  telemetry 
             frames are displayed in, you must change the entries in  the 
             WHATS-UP.SYS file.  207 is a respectable value for the color 
             to  display  data  for which the  limit  has  been  exceeded 
             (flashing white on red background).

        3.0 Modes

        WHATS-UP  is designed to operate in a number of modes  as  listed 
        below.  Each mode has its own type of window display.  To  change 
        things  or select features, touch the 'Esc' key to bring  up  the 
        top level menu.  Menus in WHATS-UP are organized as a  hierarchy, 
        each  option  will  take you as deep as necessary  to  make  your 
        selection.

             3.1 Standby Mode

             The  standby  Mode  presents  you with  the  Modes  Menu  as 
             described in Section 4.  This mode is activated if you bring 
             up WHATS-UP without specifying a mode in the command line.

             3.2 Interactive Mode

             The  Interactive mode is a dumb terminal. You can use it  to 
             give commands to the TNC. You should also use it to set  the 
             'HEADERLINE ON'. In this mode, you will see the raw  packets 
             on the channel. You can also use this mode as a regular  TNC 
             program  (If  you do, you ought to get your  head  examined, 
             because LAN-LINK will do the job much better). The  capture-


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 21


             to-disk  will turn on when the first packet is  copied,  and 
             will turn off two minutes after the last.

             3.3 Real Time Mode

             The  Real-time mode converts and displays engineering  data. 
             You  can  display  up to 16 (configured  by  you)  pages  of 
             information.  Information  that changes  between  successive 
             frames, is shown in a different color. Information that  has 
             exceeded a preset (by you) limit is shown in an alarm  color 
             (default:  blinking red). The capture-to-disk will  turn  on 
             when  the  first  packet is copied, and will  turn  off  two 
             minutes after the last.

             3.4 Orbital Dynamics Mode

             The  orbital  dynamics  mode  gives you  a  display  of  the 
             positions  of the spacecraft with respect to your  location.  
             If  the  spacecraft  are out of range,  then  you  see  time 
             related information. If the spacecraft are in range then you 
             also  see position related information.  The time  that  the 
             spacecraft  comes  above your horizon is  when  you  acquire 
             signals. This time is known as Acquisition of Signals  (AOS) 
             time. You lose signals when the spacecraft drops below  your 
             horizon.  This  time  is known as  Loss  of  Signals  (LOS).  
             WHATS-UP  allows you to define an early warning  time  (EWT) 
             (in minutes) before AOS.  The period of time between AOS and 
             LOS is known as the pass.

             Orbit positional information is only as accurate as your  PC 
             clock and the reference Keplerian data supplied by AMSAT and 
             other sources. You can expect an accuracy of within a minute 
             or  two if your PC clock is correct. WHATS-UP only  provides 
             time  displays accurate to within a minute or two.  Its  not 
             worth going for greater accuracy in most cases.

             The information displayed in the orbital mode window are  as 
             listed below.

             WNDOW     Time  till AOS (if out of range, or time till  LOS 
                       if in range.
             AOS       Time  of  AOS. This item is not displayed  if  the 
                       spacecraft is in range.
             LOS       Time of LOS.
             PASS      The  amount of time that the pass will  last.   If 
                       the  spacecraft  is  in  range,  then  this   item 
                       displays the minutes remaining till LOS.
             MA        Mean Anomaly, or position of the spacecraft in its 
                       orbit (see Section 5).
             ALT       The altitude of the spacecraft above sea level. An 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 22


                       Up arrow next to it indicates that the altitude is 
                       increasing, a down arrow, that it is decreasing.

             The  following information is only displayed for  spacecraft 
             in range.

             AZ        Azimuth  -  Pointing  angle  to  spacecraft  along 
                       horizon (0 = North, 90 = East).
             EL        Elevation  -  Pointing angle  to  spacecraft  from 
                       horizon to zenith.
             RANGE     Distance between your station and the  spacecraft. 
                       An Up arrow next to it indicates that the altitude 
                       is   increasing,   a  down  arrow,  that   it   is 
                       decreasing.
             DPLR      Doppler shift on spacecraft's beacon signal.

             A typical example of part of the display is shown below.

        ÍÍS/CÍÍÍÍÍWNDOWÍÍAOSÍÍÍLOSÍÍPASSÍÍÍÍMAÍÍÍÍÍALTÍÍÍÍAZÍÍÍÍÍÍELÍÍÍRANGE
         UO-11    02:05 00:08 00:19 00:11  143     681
         AO-13    04:51       02:54 08:01  122   37723  47.92  24.91  
        =DO-17    03:32 01:35 01:45 00:10  206     792

             The  first column provides information about  the  automatic 
             sequencer.

             A  check mark indicates that the spacecraft is the  selected 
             one for data to be captured.

             An  equals  sign indicates that WHATS-UP  is  configured  to 
             configure  itself to tune to its beacon signal  and  capture 
             data at AOS for that spacecraft.

             A  "less  than  equals"  sign  indicates  that  WHATS-UP  is 
             configured to configure itself to tune to its beacon  signal 
             and capture data at EWT for that spacecraft.

             The display is color coded as follows.

             Spacecraft out of range are displayed in the default  window 
             color.  Spacecraft in range are displayed in the 'in  range' 
             color. Spacecraft within EWT are is displayed up in the  EXT 
             color. The spacecraft designator for the next spacecraft  to 
             come in range is displayed in the 'next one up' color.  

             These  colors  may be configured to your preference  in  the 
             WHATS-UP.SYS file.





        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 23


             3.5 Playback Mode

             The Playback mode allows you to play back captured telemetry 
             with 4 speeds (speedy, slow, slower and snail's pace). 

             3.6 (Data) Extraction Mode

             In this mode, data is extracted from a playback file into  a 
             file that can be read into a spreadsheet. If you answer  the 
             prompt  for the default file with a  non-existent  filename, 
             WHATS-UP will prompt you for individual channel numbers.  To 
             terminate the sequence and begin the extract mode, touch the 
             'Enter' key without entering a channel number. 

             Note: Start and stop times are text string matches.

             3.7 Audio Warnings and Orbit Data Displays

             WHATS-UP provides audible warnings in morse code of AOS, LOS 
             and  EWT. Each warning consists of a letter followed by  the 
             spacecraft designator. An 'A' prefixes AOS, an 'L'  prefixes 
             LOS and a 'Q' prefixes EWT.

             WHATS-UP also shows orbit data associated with the  selected 
             spacecraft in the bottom window. This data which  duplicates 
             the  line shown in the orbital mode, is there to be used  in 
             the real-time and interactive modes.

             3.8 Autotrack

             An   autotrack   flag   is  present   in   each   spacecraft 
             configuration  file.  The  autotrack  flag  allows  you   to 
             customize  the way WHATS-UP switches radio  frequencies  and 
             TNC modes.  If the autotrack is disabled, WHATS-UP will  not 
             switch until after LOS of the satellite currently  tracking. 
             If the autotrack flag is enabled, WHATS-UP will switch radio 
             frequency and TNC mode when a new spacecraft is present even 
             if it is currently tracking one.  You use the autotrack flag 
             to stop WHATS-UP from switching away from a satellite in the 
             middle of a pass if a new one comes up over the horizon.

             If the autotrack flag a disabled, a flashing indicator  will 
             be seen next to the spacecraft name in the status window. 

             WARNING,  if you disable the autotrack flag in  the  default 
             configuration   file,   or  manually   load   a   spacecraft 
             configuration  file  with the autotrack  disabled,  WHATS-UP 
             will  not  change radio frequencies or TNC modes  until  the 
             next LOS.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 24


        4.0 Menus

        WHATS-UP  provides various features organized in a  hierarchy  of 
        menus. To bring up the top menu, touch the 'Esc' key.

             4.1 Function Keys

             The  following function keys are active in  the  operational 
             modes described in Section 3:

                  FK 1 capture to disk Toggle
                  FK 2 type of display Engineering Units/Raw Byte Toggle
                  FK 3 select display page
                  FK 4 Change Doppler frequency display
                  Alt-B send a 'Break' to the TNC 
                  Alt-C connect to another packet station
                  Alt-D disconnect from another packet station
                  Alt-F flush receiver buffer
                  Alt-I autotrack toggle
                  Alt-J jump to DOS (shell)
                  Alt-P Printer on/off toggle
                  Alt-S Sound on/off toggle
                  Alt-X Quit Mode
                  Alt += debug toggle
                  left arrow decreases playback speed
                  right arrow increases playback speed.

             4.1.1 FK 1 Capture to disk Toggle

             This function key turns the capture-to-disk ON if it is off, 
             and turns it OFF if it is on.

             4.1.2 FK 2 Type of display Engineering Units/Raw Byte Toggle

             This function key changes the real-time, playback  telemetry 
             display between raw data and decoded engineering units.

             4.1.3 FK 3 select display page

             This   function  key  allows  you  to  select  a   different 
             customized data display page.

             4.1.4 FK 4 Change Doppler frequency display

             This function key allows you to change the Doppler frequency 
             display  between  the  computed receive  frequency  and  the 
             difference  between the satellite beacon frequency  and  the 
             computed receive frequency.
                  



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 25


             4.1.5 Alt-B send a 'Break' to the TNC 

             This function key allows you to send a "break" character  to 
             the  TNC. You use it if you accidentally put the TNC in  the 
             transparent mode.

             4.1.6 Alt-C connect to another packet station

             This function key prompts you to enter a callsign, then,  if 
             you  are  in  the packet communications  mode,  attempts  to 
             connect you to that station.

             4.1.7 Alt-D disconnect from another packet station

             This  function  key allows you to disconnect a  packet  mode 
             connection.

             4.1.8 Alt-F flush receiver buffer

             This function key allows you to flush the receive buffer.

             4.1.9 Alt-I autotrack toggle

             This  function  key  allows you to  enable  or  disable  the 
             autotrack feature. You use this key to override the  default 
             value in the spacecraft configuration file.

             4.1.10 Alt-J jump to DOS (shell)

             This function key lets you jump into DOS for a while without 
             exiting from WHATS-UP.

             4.1.11 Alt-P Printer on/off toggle

             This  function key lets you turn the printer on and off.  If 
             the  printer  is turned on, any incoming raw  data  will  be 
             echoed to the printer as well as to the screen.

             4.1.12 Alt-S Sound on/off toggle

             This  function key lets you turn the sound on and off.

             4.1.13 Alt-X Quit

             This function key quits the mode and allows you to terminate 
             WHATS-UP and return to DOS. 

             4.1.14 Alt += debug toggle

             This  function  key lets you enable and  disable  the  Debug 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 26


             Menu. If the debug menu is enabled, an '*' will be displayed 
             on the left hand side of the status window.

             4.1.15 left arrow decreases playback speed

             This  function key decreases playback speed in the  Playback 
             mode.

             4.1.16 right arrow increases playback speed.

             This  function key increases playback speed in the  Playback 
             mode.

             4.2 Modes menu

             When  you bring up the Modes menu you will be prompted  with 
             the following options.

                            E Extract From Playback File
                            I Interactive Mode
                            O Orbital Parameters
                            P Playback Mode
                            R Real Time Mode
                            S Selections Menu
                            X Exit to Dos

                  Type  the letter associated with the option to  perform 
                  it.

                  Each of the options are described below.

                  4.2.1 Extract From Playback File

                  This option activates the Extraction mode.

                  4.2.2 Interactive Mode

                  This option activates the Interactive mode.

                  4.2.3 Orbital Parameters

                  This option activates the Orbital mode.  This option is 
                  only active if Keplerian data files are in the  defined 
                  directory path.

                  4.2.4 Playback Mode

                  This option activates the Playback mode.




        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 27


                  4.2.5 Real Time Mode

                  This option activates the Real-time mode.

                  4.2.6 Selections Menu

                  This option brings up the Selections Menu.

                  4.2.7 Exit to Dos

                  This option allows you to terminate WHATS-UP and return 
                  to DOS. 

             4.3 Selections Menu

             This menu presents you with the following typical options.

                           C Change Display Page
                           E Edit Menu
                           F Files Menu
                           H Help Menu
                           J Jump to DOS
                           M Modes Menu
                           O Orbits Menu
                           R Radio Menu
                           S Spacecraft Menu
                           T PK232 Menu
                           U Utilities Menu
                           X Exit to DOS

                  4.3.1 Change Display Page

                  This  option allows you to change the display page  for 
                  the  Real-time,  Playback  and  Extraction  Modes.   It 
                  performs the same operation as Function key 3 (F3) when 
                  those modes are active.

                  4.3.2 Edit Menu

                  This option brings up the Edit Menu.

                  4.3.3 Files Menu

                  This option brings up the Files Menu.

                  4.3.4 Help Menu

                  This option displays help information for the  function 
                  keys.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 28


                  4.3.5 Jump to DOS

                  This  option allows you to jump into a DOS  Shell.  You 
                  return to WHATS-UP by typing the DOS command 'EXIT'.

                  4.3.6 Modes Menu

                  This option brings up the Modes Menu.

                  4.3.7 Orbits Menu

                  This  option brings up the Orbits Menu. This option  is 
                  only  available  if  an orbit element  file  (*.AMS  or 
                  *.2LN) is present.

                  4.3.8 Radio Menu

                  This option brings up the Radio Menu if a Kenwood Radio 
                  is present and the interface is operational.

                  4.3.9 Spacecraft Menu

                  This option brings up the Spacecraft Menu.

                  4.3.10 TNC or PK232 Menu

                  This option brings up the TNC Menu.

                  4.3.11 Utilities Menu

                  This option brings up the Utilities Menu.

                  4.3.12 Exit to DOS

                  This option allows you to terminate WHATS-UP and return 
                  to DOS. 

             4.4 Edit Menu

             WHATS-UP  contains an ASCII text editor suitable  for  files 
             less than 64k in size. It is built based on Borland's  Turbo 
             Pascal  Editor Toolbox and the commands are compatible  with 
             Sidekick  and Wordstar. A summary of the editor commands  is 
             shown below. 

                 F10 Switch Windows (if more than one window open)

                  Backspace Delete left char
                  Del Delete Char
                  Enter New line


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 29


                  Ins Toggle insert mode
                  PgUp Move cursor up one page
                  PgDn Move cursor down one page

                  ^A Move cursor left one word
                  ^C Move cursor down one page
                  ^D Move cursor right one character
                  ^E Move cursor up one line
                  ^F Move cursor right one word
                  ^G Delete one character
                  ^H Delete left one character
                  ^I Tab
                  ^L Find/replace next occurrence
                  ^P Insert a control character into the text
                  ^M New line
                  ^N Insert line
                  ^R Move cursor up one page
                  ^S Move cursor left one character
                  ^T Delete one word after cursor 
                  ^V Toggle insert mode
                  ^W Scroll up
                  ^X Move cursor down one line
                  ^Y Delete line at cursor
                  ^Z Scroll down
                  ^K^B Mark beginning of block
                  ^K^C Copy block to position of cursor
                  ^K^D Save file and exit edit 
                  ^K^H Hide block marker
                  ^K^K Mark end of block
                  ^K^Q Abandon file and exit edit
                  ^K^R Read file into screen
                  ^K^T Mark single word as block
                  ^K^V Move block to position of cursor
                  ^K^W Write block to disk file
                  ^K^Y Delete block
                  ^K 1..9 Set marker 1 .. 9
                  ^Q^A Find text and replace
                  ^Q^B Move to beginning of block
                  ^Q^C Move to end of file
                  ^Q^D Move to right of line
                  ^Q^E Move to top of window
                  ^Q^F Find text
                  ^Q^I Toggle autoindent mode
                  ^Q^K Move to end of block
                  ^Q^R Move to top of file
                  ^Q^S Move to left of line
                  ^Q^X Move to bottom of window
                  ^Q^Y Delete to end of line
                  ^Q 1..9 Jump to marker 1..9



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 30


                 The  following options can be set in the  Find/Find  and 
                 Replace (^Qf and ^Qa) operations.

                  # locates #th occurrence
                  G global replace
                  N replace without Y/N question
                  U ignore upper case/lower case
                  W match whole words only

                 Notes
             1    The  ^  key  in front of  a  character  identifies  the 
                  character  as  a 'control' character. To  activate  it, 
                  hold down the Control key AND the character key. 

             2    Some of the commands require two keystrokes.

             3    Use  ^P to embed a control character in the  text.  For 
                  example, if you are creating a file containing commands 
                  to  be sent to the TNC, to enter a control-C  character 
                  into the file, use the ^P^C sequence of keystrokes.

             WHILE  USING THE EDITOR, WHATS-UP can't receive and  process 
             characters from the TNC. All other features ARE INHIBITED OR 
             LOCKED OUT. 

             The  Edit menu allows you to call up the various  files  for 
             editing as shown by this typical display.

                           D DOVE.DOP
                           F Any File
                           K WHATS-UP.2LN
                           M c:dove.SYS
                           P Pick ***.D17 File
                           R c:910313.D17
                           S WHATS-UP.SYS
                           T Two Files
                           W Arrays
                           X whats-up.txt
                           Y Pick ***.SYS File

                  Type the letter corresponding to your choice.

                  4.4.1 Edit Doppler File

                  This  option lets you edit the file containing  Doppler 
                  measurements.

                  4.4.2 Any File

                  This option lets you edit any file.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 31



                  4.4.3 Edit Keplerian Element File

                  This  option lets you edit the default file  containing 
                  Keplerian data.

                  4.4.4 Edit Spacecraft Configuration File

                  This  option  lets  you edit the  file  containing  the 
                  spacecraft  configuration data, such as display  pages, 
                  and automatic radio tuning options.

                  4.4.5 Pick Capture-to-disk File

                  This option lets you pick a capture-to-disk file to  be 
                  edited.  When  you implement this option  you  will  be 
                  presented  with  a list of available files.   Move  the 
                  cursor  down to the desired file and push  the  'Enter' 
                  key.

                  4.4.6 Edit Capture-to-disk File

                  This  option  lets you edit the  file  containing  data 
                  captured during the last pass.

                  4.4.7 Edit WHATS-UP.SYS

                  This option lets you edit the WHATS-UP.SYS file.

                  4.4.8 Two Files

                  This  option lets you edit any two files.

                  4.4.9 Edit Doppler Channel File

                  This  option  lets  you edit the  file  containing  the 
                  channel  numbers of the data to be extracted  from  the 
                  raw telemetry, processed and written to disk.

                  4.4.10 Edit Doppler Data File

                  This option lets you edit the file containing extracted 
                  data.

                  4.4.11 Pick Spacecraft Configuration File

                  This  option lets you pick a  spacecraft  configuration 
                  file  to be edited. When you implement this option  you 
                  will be presented with a list of available files.  Move 
                  the  cursor  down  to the desired  file  and  push  the 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 32


                  'Enter' key.

             4.5 Files Menu

             This menu presents you with the following typical options.

                           A Change Directory Path
                           F Change Playback File
                           S Show Data Files
                           V View Playback File
                           Z Show *.D17 Files
                           1 Show Files for 1 Spacecraft

                  4.5.1 Change Directory Path

                  This  option  allows  you  to  temporarily  change  the 
                  directory path to the capture-to-disk files.

                  4.5.2 Change Playback File

                  This option allows you to change the playback file.  To 
                  select a file, move the cursor down to the desired file 
                  and  push the 'Enter' key. If you have more files  than 
                  fit  in  the window, touch the 'PgDn'  key  to  display 
                  another window full.

                  4.5.3 View Playback File

                  This  option  allows you to view the  contents  of  the 
                  playback file. 

                  4.5.4 Show Spacecraft Capture-to-disk Files

                  This option shows you the names of the capture-to- disk 
                  files   for  the  chosen  spacecraft  in  the   default 
                  directory path.

                  4.5.5 Show Data Files

                  This option shows you the names of ALL the  capture-to- 
                  disk files in the default directory path.

                  4.5.6 Show Files for 1 Spacecraft

                  This option shows you the names of the capture-to- disk 
                  files for a particular chosen spacecraft in the default 
                  directory  path. It will prompt ypou for  the  filetype 
                  associated with the spacecraft (e.g. O23, D17).




        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 33


             4.6 Orbits Menu

             This menu presents you with the following typical options.

                            A Pick AMSAT Format Element Set
                            E Edit WHATS-UP.2LN
                            L Load Element File
                            N Pick NASA 2 Line Element Set
                            V View Spacecraft Orbit Elements

                  4.6.1 Pick AMSAT Format Element Set

                  This  option  allows  you to change  the  AMSAT  Format 
                  Keplerian  Element  file. To select a  file,  move  the 
                  cursor  down to the desired file and push  the  'Enter' 
                  key.  If  you have more files than fit in  the  window, 
                  touch the 'PgDn' key to display another window full.

                  4.6.2 Edit Default Keplerian Element File

                  This  option lets you edit the default file  containing 
                  Keplerian data.

                  4.6.3 Load Element File

                  This  option  loads the data in the element  file  into 
                  WHATS-UP.   When  you activate the option you  will  be 
                  prompted as follows.

                  Which Element File ? WHATS-UP.2LN

                  WHATS-UP   will  supply  the  default  name,  you   may 
                  overwrite  it to supply the name of another  file.  You 
                  use  this option to load a file that is not located  in 
                  the default directory.

                  4.6.4 Pick NASA 2 Line Element Set

                  This  option  allows you to change the  2  Line  Format 
                  Keplerian  Element  file. To select a  file,  move  the 
                  cursor  down to the desired file and push  the  'Enter' 
                  key.  If  you have more files than fit in  the  window, 
                  touch the 'PgDn' key to display another window full.

                  4.6.5 View Spacecraft Orbit Elements

                  This option lets you view the data associated with  the 
                  spacecraft. When you activate this option, you will  be 
                  presented  with  a  menu window containing  a  list  of 
                  spacecraft  designators.  Move the cursor to the  one  of 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 34


                  interest and touch the 'Enter' key to select it.

                  If the default element file is in AMSAT format  (*.AMS) 
                  the two line display is not shown.

                  A typical display is shown below :-

        1 20440U 90  5  E 91059.65616971  .00001077  00000-0  44042-3 0  2017
        2 20440  98.6806 140.0431 0012003 123.1299 237.1040 14.29083383 57498

        Catalog ID:               20440   Apogee:                 803.312
        Element Set:                201   Perigee:                786.093
        Epoch Year:                1991   Period:                  100.76
        Epoch Day:           59.6561697   Semi Major Axis:       7172.862
        Drag:                0.00001070
        Inclination:            98.6806   Epoch Age:               22.263
        RAAN:                  140.0431   Current Date:            81.919
        Eccentricity:         0.0012003   Current Orbit #:           6067
        Argument of Perigee:   123.1299
        Mean Anomaly:          237.1040
        Mean Motion:         14.2908338
        Epoch Orbit #:             5749

             4.7 Radio Menu

             This  menu  is  only present if you  have  a  Kenwood  Radio 
             defined as your Radio Receiver for the spacecraft.  The menu 
             presents you with the following typical options.

                           D Turn Doppler Tracking ON
                           F Set New Frequency
                           I Change Doppler Interval
                           R Read VFO A Frequency
                           S Set Default Frequency
                           V Select VFO A/B

                  4.7.1 Turn Doppler Tracking ON/OFF

                  This  option lets you turn the Doppler tracking on  and 
                  off.

                  4.7.2 Set New Frequency

                  This option lets you set a new (default) frequency into 
                  the radio and tune to it.

                  4.7.3 Change Doppler Interval

                  This  option  lets  you change the  time  interval  (in 
                  minutes)  between successive samples of the  radio  VFO 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 35


                  frequency.

                  4.7.4 Read VFO A Frequency

                  This option lets you read back the frequency that VFO A 
                  is tuned to, and displays it in the status window.

                  4.7.5 Set Default Frequency

                  This option lets you set the radio back to the  default 
                  frequency and tune to it.

                  4.7.6 Select VFO A/B

                  This option lets you select between the two VFOs in the 
                  radio and tune to it.

             4.8 Spacecraft Menu

             This menu presents you with the following options.

                           C Show DOVE.SYS
                           K picK Spacecraft
                           M Change Spacecraft
                           P Pick Ops. Schedule
                           S Show Ops. Schedule

                  4.8.1 Show Spacecraft Configuration File

                  This  option  allows  you  to  display  the  spacecraft 
                  configuration file default settings.

                  4.8.2 picK Spacecraft

                  This  option  allows you to choose  another  spacecraft 
                  from a list. To select one, move the cursor down to the 
                  desired  one  and touch the 'Enter' key.  For  example, 
                  amongst  the  default files supplied are  DOVE.SYS  and 
                  FUJI.SYS. To select the DOVE or the Fuji-20 spacecraft, 
                  move  the cursor down to the 'DOVE.SYS'  or  'Fuji.SYS' 
                  line and touch the 'Enter' key.

                  4.8.3 Change Spacecraft

                  This option allows you to choose another spacecraft. To 
                  select   a   another  one,  enter  the  name   of   the 
                  spacecraft.sys  file. For example, amongst the  default 
                  files supplied are DOVE.SYS and FUJI.SYS. To select the 
                  DOVE or the Fuji-20 spacecraft, type 'DOVE' or 'Fuji'



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 36


                  4.8.4 Pick Ops. Schedule

                  This option allows you to pick an operations  schedule. 
                  (A file with the default extension of "OPS".) You would 
                  use  it to look at the schedule for a spacecraft  other 
                  than the one currently selected.

                  4.8.5 Show Ops. Schedule

                  This  option  allows you to look at  the  schedule  the 
                  spacecraft currently selected.

             4.9 TNC Menu

             This menu presents you with the following typical options.

                           A UoSAT ASCII Beacon
                           B Phase 3 RTTY Beacon
                           C Set Morse Code (CW)
                           M Fuji/MicroSat ASCII Packet
                           P FM Packet
                           R Select MFJ 1278 Radio Port
                           S SARA ASCII Beacon
                           T Configure PK232


                  If  you select an option that your TNC cannot  perform, 
                  you will get an error message.

                  4.9.1 UoSAT ASCII Beacon

                  This  option  will  configure the PK-232  to  copy  the 
                  UoSAT-OSCAR 11 telemetry. Note: you require a  hardware 
                  change  in  the PK-232 to make sense  of  the  received 
                  data.

                  4.9.2 Phase 3 RTTY Beacon

                  This  option will configure the Multi mode TNC to  copy 
                  the UoSAT-OSCAR 13 Baudot Beacon.

                  4.9.3 Set Morse Code (CW)

                  This  option will configure the Multi mode TNC to  copy 
                  morse code. You use this if you want to copy morse code 
                  telemetry.  Note the decoding formats are not  provided 
                  in  this  program,  so  you will  have  to  decode  the 
                  telemetry  in  some other way, such as by  hand  or  by 
                  means of a spreadsheet. 



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 37


                  4.9.4 Fuji/MicroSat ASCII Packet

                  This  option will configure the Multi mode TNC to  copy 
                  the Fuji ASCII format PACKET telemetry. You should  not 
                  use  WHATS-UP to capture AMSAT/UoSAT  binary  telemetry 
                  because WHATS-UP filters the ^J and ^M (carriage return 
                  and line feed characters) from the incoming datastream.

                  4.9.4 Configure TNC

                  This  option configures the TNC to copy the UI  packets 
                  transmitted  by  the  Packet spacecraft  or  any  other 
                  configuration  defined by the parameters at the end  of 
                  the *.SYS file.

                  4.9.5 FM Packet

                  This  option will configure the Multi mode TNC to  copy 
                  the DOVE ASCII format PACKET telemetry. You should  not 
                  use  WHATS-UP to capture AMSAT/UoSAT  binary  telemetry 
                  because WHATS-UP filters the ^J and ^M (carriage return 
                  and line feed characters) from the incoming datastream.

                  4.9.6 SARA ASCII Beacon

                  This option will configure the PK-232 to copy the  SARA 
                  ASCII format 300 baud binary telemetry. You should  not 
                  use  WHATS-UP to capture AMSAT/UoSAT  binary  telemetry 
                  because WHATS-UP filters the ^J and ^M (carriage return 
                  and line feed characters) from the incoming datastream.  
                  At this time no data has been published about  decoding 
                  the telemetry from SARA-OSCAR 23.

                  4.9.6 Select MFJ-1278 Radio Port

                  This option lets you change the MFJ Radio port.  WHATS-
                  UP does nto change it at any other time.

             4.10 Utilities Menu

             This menu presents you with the following typical options.

                           A Change Directory Path
                           D Show Space on Disk
                           R Reset Header Counters
                           S Show Defaults
                           Z Show Files
                           * Show Color Chart
                           ! Reconfigure WHATS-UP



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 38


                  4.10.1 Change Directory Path

                  This  option  allows  you  to  temporarily  change  the 
                  directory  path  to  the  spacecraft   capture-to-disk, 
                  configuration and schedule files. 

                  4.10.2 Show Space on Disk

                  This option allows you to see how much space is left on 
                  a disk with exiting from the program.

                  4.10.3 Reset Header Counters

                  This   option   applies  to   spacecraft   transmitting 
                  packetized telemetry. When activated, the option resets 
                  the packet counters to zero. Use this before a pass  to 
                  see  how many packets of each type are received  during 
                  the pass.

                  4.10.4 Show Defaults

                  This option allows you to display the WHATS-UP  default 
                  settings.

                  4.10.5 Show Files

                  This  option lets you display the files in the  default 
                  directory  path. Use this if WHATS-UP tells you that  a 
                  file does not exist and you are sure that it does.

                  4.10.6 Show Color Chart

                  This   option   allows  you  to   display   the   color 
                  combinations.  Use this to see what how  the  different 
                  color  combinations  appear on your  screen,  note  the 
                  numbers associated with each color, then exit from  the 
                  program  and  edit  the WHATS-UP.SYS  file  using  your 
                  editor  in its ASCII (non document)mode to  change  the 
                  colors to those you desire. 

                  4.10.7 Reconfigure WHATS-UP

                  This option reloads the configurations from the  WHATS-
                  UP.SYS  file. Use it after editing the file to see  the 
                  effect of your changes.

                  4.10.8 Enable/Disable TNC Port

                  This  option lets you enable and disable the PC  serial 
                  port to the TNC. Use it to stop WHATS-UP taking control 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 39


                  of  the port in multi-tasking environments, so you  can 
                  run  LAN-LINK  in one window, and  the  Orbit  Dynamics 
                  display of WHATS-UP in another.

             4.11 Debug Menu

             This menu is only active when the debug flag is enabled. The 
             menu presents you with the following typical options.

                           @ Sound CW String
                           D Turn Debug OFF
                           F Set Frequency
                           I Interrogate Radio
                           S Show Defaults
                           T Talk to Radio
                           V Speak Frequency
                           W Identify Radio

                  4.11.1 Sound CW String

                  This  option asks you to enter some characters  at  the 
                  keyboard.  When you do so, it then sounds them  off  in 
                  morse code. You use this option to adjust the speed  of 
                  the morse code used in the AOS, LOS and EWT signals.

                  4.11.2 Turn Debug OFF

                  This option lets you turn the debug flag off. 

                  4.11.3 Set Frequency

                  This  option  lets  you  enter  a  frequency  into  the 
                  selected VFO.

                  4.11.4 Interrogate Radio
                   
                  This  option lets you enter a manual command  into  the 
                  radio and see the reply returned by the radio.

                  4.11.5 Show Defaults

                  This option allows you to display the WHATS-UP  default 
                  settings.

                  4.11.6 Talk to Radio

                  This  option lets you enter a manual command  into  the 
                  radio.




        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 40


                  4.11.7 Speak Frequency

                  This  option commands the voice module in the radio  to 
                  announce the frequency it is tuned to.

                  4.11.8 Identify Radio

                  This option lets you enter the 'identify' command  into 
                  the radio and see the reply returned by the radio.

        5.0 Orbital Elements

             5.1 Basics

             As  an object moves in space it is subject to gravity.   The 
             object itself has mass and attracts other objects and is  at 
             the  same time attracted by the mass in the  other  objects.  
             Sir Isaac Newton formulated the law of gravity, which can be 
             described in the following manner.

             All   bodies  attract  each  other  with  a   force   called 
             gravitational  attraction.   The  strength  of  the   mutual 
             attraction between two bodies is dependent on their  masses, 
             and  the  distance between the bodies. In  fact  the  closer 
             together that the two bodies are, the greater is the  mutual 
             attraction.   Mathematically  this can be expressed  as  the 
             gravitational  attraction  between two  bodies  is  directly 
             proportional  to their masses and is inversely  proportional 
             to the square of the distance between them.

             Planet  Earth  is  an object moving in space  and  exerts  a 
             gravitational force.  It pulls anything close to it  towards 
             the  center  of  the  Earth  at  an  increasing  speed.   An 
             increasing speed is known as acceleration.  The acceleration 
             due  to  gravity at the surface of the Earth  is  given  the 
             value of 1 Gravity (G).

             5.2 Orbital Trajectories

             If  the Planet pulls everything towards itself,  what  keeps 
             things in orbit around it?  For example, if you throw a rock 
             up  into the air, gravity and air resistance (drag) slow  it 
             down  and  it falls back to Earth.  If you  shoot  a  bullet 
             towards  the  horizon it will travel much further  than  the 
             stone  did,  but will still fall to Earth  (unless  it  hits 
             something first).  

             If you launch a rocket towards the horizon, the rocket  will 
             accelerate as long as the fuel lasts.  When the rocket  fuel 
             is  exhausted,  the  rocket will continue  to  travel  in  a 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 41


             straight  line  until other forces alter its path.   If  the 
             rocket   is  low  enough,  the  molecules  of  air  or   the 
             atmospheric  drag  tends to slow it down. At any  height  it 
             will still be pulled back by gravity.  The force of  gravity 
             always acts towards the center of the Earth.  On its own the 
             rocket  will  travel  in a straight  line.   Gravity  acting 
             downwards  will  curve  the path of the  rocket  around  the 
             Earth.  

             The  force  of gravity will pull the rocket  away  from  its 
             horizontal  path  and  cause  it  to  fall  in  a  downwards 
             direction.  Now the surface of the Earth is also curved  and 
             also curves away in a downwards direction.  If speed of  the 
             rocket  is  such  that  the rate  of  descent  (due  to  the 
             gravitational  attraction  of  the Earth) is  equal  to  the 
             curvature of the Earth, the rocket will always remain at the 
             same  height , namely, it will be in a circular  orbit.   If 
             the rocket does not have enough speed it will gradually fall 
             back  to  Earth, and if it has more speed, it will  tend  to 
             rise above the Earth. 

             If the rocket continues to burn fuel the speed of the rocket 
             increases and the path it takes rises away from the  surface 
             of the Earth.  When the fuel is exhausted, gravity is  still 
             there and still slows down the rocket.  As it slows down its 
             path  curves  more  sharply  until  at  its  furthest  point 
             (apogee)  it  is traveling parallel to the  surface  of  the 
             Earth.   It  is  however traveling  slower  than  the  speed 
             necessary to maintain a circular orbit at that altitude  and 
             starts  to  curve  back towards the  Earth.   The  force  of 
             gravity  now  acts  in a  downward  and  (slightly)  forward 
             direction and speeds up the rocket until at its lowest point 
             (perigee) it once again is traveling parallel to the surface 
             of  the  Earth  but now has enough speed to  rise  away  the 
             surface.  This process repeats each time around and produces 
             an elliptical orbit.(In this orbit, the center of the  Earth 
             is one focus of the ellipse.

             To  place  a satellite into an orbit, it must be  given  the 
             right  amount of speed for the desired orbital  altitude  so 
             that  the  orbital velocity at apogee is such that  it  just 
             balances  the  gravitational pull of the Earth.   Since  the 
             force  of  gravity  decreases  with  altitude,  the  orbital 
             velocity  is  also different at  different  altitudes.   Any 
             rocket can lift a small mass to a much higher altitude  than 
             it can lift a large mass.  How much and how high will depend 
             on the rocket itself.





        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 42


             5.3 Types of orbits

             Different orbits are used for different purposes.   Circular 
             and elliptical orbits come in various forms depending on the 
             angle that the plane of the orbit makes with the equator  of 
             the Earth.  This angle is known as the angle of  inclination 
             of  the orbit (with respect to the equator).  A polar  orbit 
             has an angle of inclination such that the spacecraft in that 
             orbit   can  see  the  polar  regions  of  the   Earth.    A 
             geostationary orbit is one which has an angle of inclination 
             parallel  to  the equator and an altitude  of  22,240  miles 
             (35,790  km)  and the spacecraft moves in its orbit  at  the 
             same speed as a point on the surface of the Earth below  it.  
             The spacecraft thus appears to be stationary with respect to 
             the Earth below it.  

             The direction in which the satellite moves around the  Earth 
             determines  the type of orbit.  One which travels along  its 
             orbit  in  the same direction as the rotation of  the  Earth 
             (eastwards)  is  said to be in a direct or  prograde  orbit.  
             One  which  travels  against  the  rotation  of  the   Earth 
             (westwards) is said to be in a retrograde orbit.  

             The  movement  of  an  object  in  space  can  be  described 
             mathematically.  In the early 17th century, the  only  known 
             objects in space were the Sun, the Moon, the Planets, a  few 
             comets  and  the stars.  It was then  that  Johannes  Kepler 
             formulated  three laws that first described the movement  of 
             the Planets about the Sun.  

             Kepler's Laws are stated in the following paragraphs.

             1.   Each  Planet  revolves about the Sun in an  orbit  that 
                  forms a circumference of an ellipse with the Sun at one 
                  focus of the ellipse. 

             2.   The  line from the center of the Sun to the  center  of 
                  the Planet (called the radius vector) sweeps out  equal 
                  areas  in equal periods of time as the  Planet  travels 
                  along the circumference of the ellipse.

             3.   The  square  of the time taken for a Planet  to  travel 
                  around  the  circumference of the  ellipse  (period  of 
                  revolution of the orbit of a Planet) is proportional to 
                  the  cube of the mean distance of the Planet  from  the 
                  Sun.

             In  the first law, the focus within the Sun is  actually  at 
             the  center of mass of the Earth-Sun system and not  at  the 
             center of the Sun.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 43



             5.4 Orbital Elements

             The position of an object in space can be expressed in terms 
             of  its relationship with other bodies.  Each orbit  can  be 
             described  in terms of a number of parameters  which  supply 
             enough information to accurately locate the satellite.   Six 
             basic  parameters  are used to describe the  position  of  a 
             satellite  in  an  elliptical orbit  are  described  in  the 
             following paragraphs.  They are Angle of inclination,  Right 
             Ascension of Ascending Node (RAAN), Eccentricity,  Semimajor 
             Axis, Argument of Perigee and Epoch time of Ascending  Node.  
             Consider each one in turn.

             5.5 Angle of Inclination.

             The  angle of inclination of an orbit is the  angle  between 
             the  plane  of the orbit and the equator of  the  Earth.   A 
             satellite  moving  in  a  direct  orbit  has  an  angle   of 
             inclination  between  0  and 90 degrees,  one  moving  in  a 
             retrograde  orbit has an angle of inclination of between  90 
             and 180 degrees.

             The  maximum  northern and southern latitudes reached  by  a 
             satellite  are  equal  to the angle of  inclination  of  its 
             orbit. 

             5.6 Right Ascension of Ascending Node (RAAN).

             While  the spacecraft is moving around the Earth, the  Earth 
             is at the same time rotating on its own axis, and is  itself 
             traveling in an orbit about the Sun.  The Right Ascension of 
             Node is needed as a fixed reference point in the sky. 

             Astronomers  use the term celestial sphere to  describe  the 
             sky  for two reasons. First, from where we are  standing  on 
             the surface of the Earth, the sky seems to be painted on the 
             inside  surface  of  a  sphere  (with  the  stars  in  fixed 
             positions  on  the  sphere). Second,  have  you  ever  known 
             scientists  to use a short commonly used word when they  can 
             use long ones?

             The orbital plane of a spacecraft intersects the  equatorial 
             plane  of  the Earth in two places (one on each side of  the 
             globe).  A line drawn between these two points and continued 
             out  to  the celestial sphere is called the line  of  nodes.  
             The  two  points  on  the line of  nodes  where  the  planes 
             intersect  are called the point of nodes.  Most globes  (and 
             maps)  show  the  north pole upwards.  When  the  spacecraft 
             crosses  the  equatorial plane (passes  above  the  equator) 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 44


             going northward it is ascending from south to north and that 
             node point is known as the ascending node.  Conversely  when 
             the  satellite  continues on its way and  travels  half  way 
             around the world it crosses the other node on the equatorial 
             plane  descending to the southern hemisphere.   This  second 
             node is called the descending node.

             The Earth is in an inclined orbit around the Sun, just  like 
             a satellite is in orbit around the Earth.  The Earth has  an 
             ascending  and descending node around the Sun, in a  similar 
             manner  to  a  spacecraft in orbit around  the  Earth.   The 
             orbital  plane of the Earth is known as the  Ecliptic.   The 
             direction in space from the center of the Earth through  the 
             intersection  of  the ecliptic and  the  Earth's  equatorial 
             plane  out  to  the celestial sphere is  called  the  vernal 
             equinox or the First Point of Aries because it points to the 
             constellation  of Aries (which is so far away that (for  all 
             practical purposes) it is in fixed direction).

             The  angle between the line of nodes for the ascending  node 
             of  the  orbit  of  the  spacecraft  continued  out  to  the 
             celestial sphere and the vernal equinox when measured in  an 
             easterly (right as opposed to westerly/left) direction along 
             the earth's equator is defined as the Right Ascension of the 
             Ascending Node (RAAN).

             5.7 Eccentricity and Semimajor Axis

             In  a circle, the radius of the circumference  is  constant.  
             This means that an object traveling along the  circumference 
             is always at a constant distance from the center or focus of 
             the  circle.  The general shape of an orbit is  an  ellipse.  
             Unlike  a  circle,  an ellipse has two  focal  points.   The 
             distance between each of the focal points of the ellipse and 
             an object on the circumference is constant.  A line  through 
             the  two  focal points and the circumference is  called  the 
             Semimajor  Axis.   The  longest line  perpendicular  (at  90 
             degrees   to)  the  semimajor  axis  passing   through   the 
             circumference of the ellipse is called the Semiminor Axis.  

             The  mathematical  term describing the overall shape  of  an 
             ellipse is called Eccentricity.  When the eccentricity of an 
             ellipse  is 0 the length of the semimajor axis is  equal  to 
             the  length  of  the  semiminor axis  and  the  shape  being 
             described is a circle.  A value of eccentricity greater than 
             0  means that there is a difference between the  lengths  of 
             the  axes  and  the  shape  of  the  ellipse  flattens  out.  
             Eccentricity describes the shape of the orbit and the length 
             of  the semimajor axis describes the size of the orbit.   If 
             these  two  parameters  are known, the  apogee  and  perigee 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 45


             values for the orbit can be calculated.

             5.8 Decay Rate

             The  Earth has an atmosphere.  It is dense at  ground  level 
             and thins out with increasing altitude.  The Earth's gravity 
             attracts  the molecules of gas in the atmosphere  and  stops 
             them  from  escaping.  As the satellite  travels  along  its 
             elliptical  orbit  around the Earth, its  altitude  changes.  
             When it is close to perigee, it bumps into molecules of air. 
             The  lower  it gets the greater the drag on it by  the  air. 
             When  the orbital radius decreases as a result of drag,  the 
             potential  energy  of the spacecraft also  decreases  as  it 
             comes closer to the earth. This decrease in potential energy 
             reappears  in  the  form  of heat  energy  imparted  to  the 
             atmosphere  and  to the skin of the spacecraft,  and  in  an 
             increase of the kinetic energy of the spacecraft. It is this 
             latter  that causes the velocity of the spacecraft to  speed 
             up.

             The  rate of change of speed through the atmosphere  at  the 
             perigee  pass  will depend on the type of orbit and  on  the 
             altitude of the perigee point.  In general, satellites  with 
             low  perigee  points will be more affected  than  satellites 
             with  higher perigee points.   The effect of this  over  the 
             long term is to lower the apogee point. Over the long  term, 
             the  satellite tends to spend more time in the denser  parts 
             of the atmosphere which then tends to circularize the  orbit 
             (at   the  perigee)  at  which  point  the  air  drag   acts 
             continuously on the spacecraft and the orbit  disintegrates.  
             The  rate  of change of the orbit measured at  a  particular 
             epoch is called the decay rate.

             5.9 Argument of Perigee.

             A line drawn between the perigee of an elliptical orbit  and 
             the center of the Earth is called the line of perigee.  This 
             line  also  passes through the apogee and is  the  semimajor 
             axis  of the orbit.  The angle between the line  of  perigee 
             and the line of nodes is called the argument of perigee.  It 
             is a measurement of the angular distance between them and is 
             measured in the ascending direction from the line of  nodes.  
             The argument of perigee thus establishes the position of the 
             ellipse itself within the orbital plane.

             5.10 Epoch Time (of Ascending Node) and Revolution Number.

             The  Epoch  time is a time when the  satellite  crosses  its 
             perigee point.  This time is given as a Julian date, and  is 
             the reference time for when the orbital elements are  valid.   


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 46


             The  Epoch  Revolution or orbit number is the  orbit  number 
             (since first perigee crossing) for which the element set  is 
             valid.

             5.11 The Mean Motion.

             The  mean motion a satellite is a measurement of the  number 
             of  orbits  completed in a day.  It is equal  to  twice  the 
             value of PI divided by the time that the spacecraft takes to 
             complete one revolution of its orbit (orbital period).  

             5.12 The Catalog Number 

             The catalog number is the number given to the object. 

             5.13 Mean Anomaly

             As  the  satellite  travels along its  orbit,  its  position 
             changes.   The angle (measured in the direction  of  forward 
             rotation)  between  the position of the spacecraft  and  the 
             line  of perigee is called the true anomaly.  The  speed  of 
             the spacecraft is different at different parts of the orbit.  
             Calculations  are simpler if the speed is considered  to  be 
             constant.   The constant value is the average speed  of  the 
             spacecraft   in  its  orbit.   The  mean  anomaly   is   the 
             hypothetical  position of the satellite in its orbit  (along 
             the ellipse) if it is assumed to be traveling at its average 
             speed.

             5.14 Anticipated Spacecraft Lifetimes

             There  is not much point in setting up equipment to  receive 
             data  from  these  spacecraft if they are not  going  to  be 
             around  for  a reasonable amount of  time.  Past  experience 
             points  to three main factors limiting the operational  life 
             of  an OSCAR, namely orbital decay, battery life, and  total 
             radiation dosage.

             5.14.1 Orbital Decay

             The  last OSCAR to plunge back into the  earth's  atmosphere 
             while still active was UoSAT-OSCAR 9. It was launched into a 
             500km  orbit,  and  lasted  eight  years.  A  chart  in  the 
             Satellite Experimenter's Handbook shows a lifetime of 40000-
             50000 days for spacecraft at the Microsat altitude, or some-
             where  around  120 years; so orbital decay is not  our  main 
             worry.  There has been some concern about  AMSAT-OSCAR  13's 
             orbit, which is expected to decay somewhere between 1992 and 
             1995.  AMSAT  however are currently planning  a  replacement 
             spacecraft so the investment in receiving equipment will not 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 47


             be in vain.

             5.14.2 Battery lifetime. 

             Battery  breakdown  has  caused the demise  of  all  amateur 
             spacecraft  except  UoSAT-OSCAR 9. OSCARs 1, 2  and  3  were 
             limited to whatever charge was in the batteries when launch-
             ed.  Once  Solar  cells and  nickel-cadmium  batteries  were 
             flown,  the limiting factor became the number of  times  the 
             battery cells could be charged and discharged.

             The  batteries in OSCAR spacecraft in low earth  orbit  have 
             lasted between five and eight years. UO 9 was still  looking 
             good  when  it  re-entered the earth's  atmosphere  after  8 
             years.   UoSAT-OSCAR  11,  launched  in  March,  1984,   has 
             batteries  with  the same part number as those used  in  the 
             Microsats. These latter batteries were procured in much  the 
             same  manner, and were matched and tested by the same  group 
             of VITA volunteers in Canada that performed the function for 
             UoSAT-OSCAR  11. The batteries on UoSAT-OSCAR 11 have  shown 
             no  signs of weakening after almost six years in  orbit,  so 
             the  prognosis  for UoSAT-OSCAR 11 and the  Microsats  looks 
             good.

             5.14.3 Radiation Damage.

             Anything above the protection of the atmosphere is subjected 
             to exposure to the radiation due to the direct and secondary 
             effects   of  high  energy  particles,  from  the  sun   and 
             elsewhere.  The part of the spacecraft most  susceptible  to 
             such  damage is the memory in the  on-board-computer  (OBC). 
             Such damage manifests itself as a bit flipping from a 0 to a 
             1 or from a 1 to a 0, which is correctable. Since the memory 
             chips used are byte-wide, many types of single-chip failures 
             can  be  avoided in a manner analogous to  locking  out  bad 
             sectors on a hard disk.  UoSAT-OSCAR 11, which uses somewhat 
             similar  technology  chips, has survived  almost  six  years 
             despite  a  failure of one small section of  memory  several 
             years ago.

             Another  part of the OBC is the controller itself  which  is 
             susceptible to a particle hitting it in a place that  causes 
             uncorrectable errors, such as a wrong operation internal  to 
             the microprocessor, or a CMOS latchup which can result in  a 
             high  current  being  drawn which  overheats  the  part  and 
             destroys it.

             The spacecraft are more likely to fail due to the cumulative 
             effects  of  this constant bombardment, which  is  known  as 
             total dose. Once the total dose reaches a certain point, the 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 48


             gates  in the transistors that make up the computer and  its 
             memories will no longer switch. This situation has  occurred 
             in  AMSAT-OSCAR  10.  Predicting when this  might  occur  is 
             difficult  because  of  lack  of  knowledge  concerning  two 
             things;  the  total  radiation dose in this  orbit  and  the 
             tolerance limits for the parts used. 

             The  MicroSats are in a much more benign orbit  than  AMSAT-
             OSCAR 10 which with its 4000 km perigee, spends more time in 
             the Van Allen radiation belts than was planned.  AMSAT-OSCAR 
             10's  memories therefore failed sooner than hoped,  but  the 
             other  electronics, the transponders, batteries,  and  solar 
             arrays   live  on.  Through  no-longer   actively   attitude 
             controlled, its transponders are still usable many weeks  of 
             the year when its batteries are being charged by the sun.

             AMSAT-OSCAR  13 is in a better orbit with a  lower  perigee, 
             and  should  not suffer radiation degradation  before  other 
             effects shorted its lifespan.

        6.0 The Spacecraft 

        OSCAR spacecraft downlink signals in the amateur 145 MHz and  430 
        MHz  bands  modulated by means of Frequency Shift  Keying  (FSK), 
        Frequency  Modulation (FM) or Phase Shift Keying (PSK).  Some  of 
        the characteristics of the downlinks of suitable OSCARs currently 
        operational  are shown in Table 6-1.  UoSAT-OSCAR 11  and  AMSAT-
        OSCAR  13  send back BAUDOT or ASCII data while  AMSAT-OSCAR  16, 
        DOVE-OSCAR-17,  WEBER-OSCAR 18, LUSAT-OSCAR 19 and Fuji-OSCAR  20 
        downlink packetized telemetry.

        Table 6-1 Some of the Characteristics of OSCAR Downlinks.

        Spacecraft  Beacon     Modulation      Data    Note
                    Frequency  Type            Rate
                      (MHz)          
        UO-11       145.825     FM    ASCII  1200 Baud   1
                    435.025     FM    ASCII  1200 Baud   1
        AO-13       145.812    FSK    BAUDOT   50 Baud   2
                               PSK    ASCII   400 Baud   2
                    435.651    FSK    BAUDOT   50 Baud   2
                               PSK    ASCII   400 Baud   2
        AO-16       437.025    PSK    AX.25  1200 Baud   3
                    437.025    PSK    AX.25  1200 Baud   3
        DO-17       145.825    FM     ASCII  1200 Baud
        WO-18       437.100    PSK    AX.25  1200 Baud   3
                    437.075    PSK    AX.25  1200 Baud   3
        LO-19       437.150    PSK    AX.25  1200 Baud   3
                    437.125    PSK    AX.25  1200 Baud   3
        FO-20       435.912    PSK    AX.25  1200 Baud


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 49


        SO-23       145.955    FM     ASCII   300 Baud   4
        Notes 

        1.   Spacecraft  also broadcasts bulletins and Various  Telemetry 
             formats.

        2.   Spacecraft  downlink  modulation is changed according  to  a 
             pre-published schedule.

        3.   Alternate  (back  up)  beacon  frequency,  may  be  used  on 
             Wednesdays.

        4.   Binary telemetry with ASCII identification.

        Before  discussing the equipment needed to receive  signals  from 
        the  spacecraft, a brief word about the spacecraft themselves  is 
        in  order.   Since  these OSCARs rode  into  space  as  secondary 
        payloads,  the orbits that they are in are close to those of  the 
        primary   payload  and  are  not  optimized  for  amateur   radio 
        communications.  The exception is AMSAT-OSCAR 13 which  contained 
        a motor which was used by radio amateurs to boost the  spacecraft 
        from  the  orbit  the rocket placed it in  into  its  operational 
        orbit.   The  ones that are in low earth orbits can  be  received 
        with  simple  equipment, but are in range for  short  periods  of 
        time, AMSAT-OSCAR 13 in an elliptical orbit is in range for  many 
        hours each day, but needs more sophisticated receiving equipment.  
        The  orbital parameters of the OSCARs under discussion are  shown 
        in Table 6-2.  

        Table 6-21 Orbital Parameters of the OSCARs

        Spacecraft       Apogee   Perigee Inclination  Period
                          (km)     (km)    (Degrees)   (Minutes)  
        UoSAT-OSCAR 11     699     670     98.0          98.3
        AMSAT-OSCAR 13  39,000   2,500     26.1         686.65  [1] 
        AMSAT-OSCAR 16     804     780     98.7         100.8
        DOVE-OSCAR 17      804     780     98.7         100.8
        WEBER-OSCAR 18     804     780     98.7         100.8
        LUSAT-OSCAR 19     804     780     98.7         100.8
        FUJI-OSCAR 20    1,745     912     99.05        112.0
        SARA-OSCAR 23      774     768     98.5         100.3

        Notes 

        1  686.65 minutes is 11 hrs, 26 min.

             6.1 Receiving system components

             Consider  the different components or building  blocks  that 
             are used in the different receiving configurations.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 50



             6.1.1 Antennas

             Antennas receive signals, and each kind of antenna has  some 
             degree  of directive and polarization.  When the  spacecraft 
             rises   above   the  local  horizon,  the   ground   station 
             experiences acquisition of signals (AOS).  At this time  the 
             groundstation is receiving signals coming from a  particular 
             direction (azimuth). As the spacecraft rises in the sky, the 
             elevation  angle of the received signals changes, until  the 
             spacecraft drops below the observer's horizon and the ground 
             station experiences loss of signals (LOS). As seen from  the 
             ground,   the  spacecraft  rises  from  a  horizon  in   one 
             direction,  travels in an arc across the sky and sets  at  a 
             different  horizon in a different direction.  Each pass  for 
             each  spacecraft  is  different.   Antennas  for   receiving 
             signals from spacecraft must thus be able to receive signals 
             coming in from almost any angle.

             Antennas   in  this  context,  fall  into  two   categories, 
             omnidirectional and rotatable.  The simple turnstile antenna 
             is horizontally polarized and has a good response to signals 
             arriving from high angles and can be built for about  $2.00.  
             The  ground  plane  and  J  Pole  antennas  are   vertically 
             polarized and have a good response to signals arriving  from 
             low  angles.  These antennas however do not have much  gain. 
             Yagi  Beam  Antennas however have gain with respect  to  the 
             turnstile or ground plane, but only in specific  directions. 
             You can think of the gain in some directions as being  moved 
             into the direction that the antenna is pointed at.  The gain 
             of  the  antenna depends on the number of  elements  in  the 
             antenna,  and the higher the gain, the narrower the area  of 
             the gain (lobe) is.  Consequently, these beam antennas  must 
             be  moved  to keep the spacecraft in the main  lobe  of  the 
             antenna.  Since the need for keeping the antenna pointed  at 
             the spacecraft depends on the beam width of the antenna, the 
             lower the gain of the antenna the less accurate the tracking 
             need  be.   Luckily  the orbits help out  in  this  respect. 
             UoSAT-OSCAR  11 in low earth orbit, which means it  is  fast 
             moving,  needs  only  a small amount of gain,  so  TV  style 
             rotators  can be employed to point antennas with  between  2 
             and  4  elements,  while  AMSAT-OSCAR  13  which  is  in  an 
             elliptical  orbit,  moves so slowly for nearly 8 of  its  11 
             hour  orbit,  that again, TV style rotators can be  used  to 
             point higher gain antennas with between 8 and 11 elements.  

             Building  your  own  antennas  is  an  easy  and  worthwhile 
             project.  Antennas for these OSCARS are simple and not  very 
             critical  with respect to the materials used.  They  can  in 
             fact be built from recycled junk.  


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 51



             6.1.2 Receivers

             There  are two kinds of Receivers, namely FM and linear.  FM 
             receivers are used for reception of the FM signals from DOVE 
             and  UoSAT-OSCAR 11, while linear receivers are  needed  for 
             reception  of  the  FSK  and  PSK  signals  from  the  other 
             spacecraft.  All  vhf/uhf scanner radios are  FM  receivers.  
             The linear receivers need single side band (SSB) capability, 
             something   normally  found  in  short  wave   communication 
             receivers.  As a result of the growing popularity of amateur 
             satellite  communications,  suitable  vhf/uhf   transmitter-
             receivers (transceivers) have been on the market for several 
             years,  however these transceivers are expensive listing  in 
             the  $800  to  $1200  range.   An  alternative  approach  to 
             reception  is  to use a short wave  communications  receiver 
             listing around $500 together with a front end  downconverter 
             which lists at under $100.  The short wave radio can also be 
             used  to tune in, not only the world of amateur  radio,  but 
             news  broadcasts from overseas; a totally different  are  of 
             classroom activity.

             "Expensive"  is  a relative term. These  days,  many  people 
             think  nothing  of spending $1000 on a stereo system  or  on 
             equipment for photography or other hobbies.

             6.1.3 Terminal Units or Modems

             Digital  radio  links work much in the same way  as  digital 
             signals are transferred over the telephone line. However  in 
             this  case, instead of a phone wire, a radio link  is  used. 
             Both  links  use modems to convert the  serial  input/output 
             digital  RS-232 signals of the computer to the  audio  tones 
             used on the communications link.

             Packet radio signals are demodulated by a radio modem  known 
             as a Terminal Node Controller (TNC). The device is connected 
             in between the radio and the computer and provides hams with 
             two way digital communications. A packet only TNC lists  for 
             between $120 and $200. For reception of the PSK signals from 
             AMSAT-OSCAR  16,  WEBER-OSCAR 18, LUSAT-OSCAR 19  and  Fuji-
             OSCAR  20, PSK Modems are available either as add-ons  to  a 
             regular  TNC or as stand alone units, listing  between  $150 
             and $700.

             The  BAUDOT Radio Teletypewriter (RTTY) signals from  AMSAT-
             OSCAR 13 can be demodulated by an RTTY Terminal Unit.  These 
             devices  are listed at between $100 and $300. On  the  other 
             hand a multi- mode communications controller listing between 
             $250 and $700 can be used for AMSAT-OSCAR 13 as well as DOVE 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 52


             and  the other spacecraft.  AMSAT-OSCAR 13 downlinks  BAUDOT 
             because   that   is   the   most   commonly   used   digital 
             communications   mode  used  by  radio  amateurs   at   high 
             frequencies (short waves)

             The modem for UoSAT-OSCAR 11 is a little more difficult,  as 
             its  ASCII encoding is the reverse of the standard  used  in 
             the  U.S.A. This is because the spacecraft was built in  the 
             UK  and  its  use of tones to represent  data  reflects  the 
             encoding used in a popular tape interface (in the UK) at the 
             time the spacecraft was built (1982- 1984).  Still a  do-it-
             yourself circuit needs a few integrated circuits, is  simple 
             to build, easy to test, and very low cost (under $50). 

             Summarizing the costs of the items mentioned above, the list 
             prices  fall  between a low and high cost depending  on  the 
             amount you wish to pay.  The summary is shown in Table  6-3.  
             It  should  be noted that the high price items  may  not  be 
             better   than   the  cheaper  ones,  particularly   in   the 
             educational  environment.   This table is of course  only  a 
             guide,  since  you will probably end up  with  something  in 
             between.

             Table 6-3 Range of Equipment List Prices

             Item                     Low Price       High Price

             Antenna                       $2.00        $100.00
             Receiver                    $100.00       $1200.00
             Radio Modem (TU/TNC)        $150.00        $700.00
             Tracking Software            $25.00        $350.00
             Telemetry Decoding Software  $35.00         $35.00
             ---------------------------------------------------
             TOTAL                       $312.00       $2385.00
                                                                                                                                                                                                                                                                                                                                                                                                                                                      THE 

             Consider  the equipment needed to receive signals from  each 
             of the spacecraft in turn.

             6.2 Receiving Signals from DOVE

             DOVE  (DO-17) which transmits on a frequency 145.825 MHz  is 
             the easiest spacecraft to receive usable signals from.  This 
             frequency  is  available  on most hand  held  scanners,  and 
             signals  are strong enough to be heard on nothing more  than 
             the simple antenna provided with the scanning radio when  it 
             is  purchased.  However, the thrill of  receiving  satellite 
             signals  wears  off very quickly without any means  to  know 
             what those signals mean.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 53


             A  somewhat  better system is needed  for  reliable  regular 
             reception  of usable signals. A basic receiving  system  for 
             DOVE  is  shown in Figure 6.1.  DOVE's  signals  are  strong 
             enough  that  the ground station does not  need  a  tracking 
             antenna;  an  omnidirectional antenna  is  sufficient.   The 
             antenna  can  be  a ground plane, a turnstile  or  a  J-pole 
             design. A preamplifier should be used to compensate for  any 
             losses in the cable between the antenna and the receiver, or 
             any  fades  in the strength of the  received  signals.   Any 
             scanning radio which receives narrow band FM can be used  as 
             the  receiver.  This is the same type of modulation used  on 
             the  public service channels.  If the scanner can  hear  the 
             police and other services and can tune to 145.825 MHz,  then 
             it  is capable of receiving signals from DOVE.  The  digital 
             signals  from  DOVE are encoded as audio tones  and  need  a 
             modem to convert them to the RS-232 digital signals that can 
             be  interfaced  to the serial port of a PC.   This  type  of 
             modem  is known in Radio Amateur circles as a Terminal  Unit 
             (TU).

             Figure 6.1 Basic Receiving System for DOVE-OSCAR 17.

             OMNIDIRECTIONAL
                ANTENNA
                   |
                   |
                  \|/
                 SCANNER
                 RECEIVER ---------> TNC ---------> COMPUTER

             The signals are sent as packets using a modified version  of 
             the  X.25  protocol called AX.25.  Radio Amateurs  use  this 
             protocol  for  communications,  and  DOVE  employs  it   for 
             telemetry  transmission purposes so that any  Radio  Amateur 
             equipped  for packet radio communications is  also  equipped 
             for receiving signals from DOVE.

             6.3 Receiving Signals from UoSAT-OSCAR 11

             The  same  basic  radio receiving  system  used  to  receive 
             signals  from  DOVE can be used to copy the  telemetry  from 
             UoSAT-OSCAR 11. This spacecraft however has a lower  powered 
             transmitter than that of DOVE and consequently has a  weaker 
             signal  strength  on the ground. This  lower  signal  level, 
             coupled  with  the fact that the modulation is  plain  ASCII 
             data means that errors will be seen in the received data due 
             to  signal fades.  Better antennas are needed  for  reliable 
             reception, and antennas that track or move and always  point 
             at the spacecraft are desirable.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 54


             The TU used for UoSAT-OSCAR 11 is different to that used for 
             DOVE  due to the different data encoding (ASCII  instead  of 
             AX.25).

             6.4 Receiving Signals from AMSAT-OSCAR 13

             So  far  all the spacecraft considered have been  low  earth 
             orbits.   AMSAT-OSCAR 13 however is in an  elliptical  orbit 
             with  a high apogee.  It also downlinks telemetry as  BAUDOT 
             and  ASCII data. While signals from this spacecraft  can  be 
             heard  on  the simple DOVE type of  receiving  configuration 
             with  an omnidirectional receiving antenna, the signals  are 
             weak  and  barely audible, i.e. they are in  the  noise  and 
             cannot  be  received  in  usable  form  without  a  tracking 
             antenna. 

             6.5 Receiving PSK Modulated Signals in the 70 cm Band

             Receiving  signals from AMSAT-OSCAR 16, WEBER-OSCAR  18  and 
             LUSAT-OSCAR  19   as  well as from  Fuji-OSCAR  20  requires 
             somewhat  more complex equipment. These spacecraft  transmit 
             on  downlink frequencies in the 70 cm or 430 MHz  band.   As 
             they  use  PSK,  the  receiver  has  to  be  a  conventional 
             communications receiver. This can be either a communications 
             receiver   designed   for  that  frequency   range,   or   a 
             conventional  short  wave  receiver with a  front  end  down 
             converter.  A PSK modem attached to the TU is also required.  
             Typical  receiving configurations for these  satellites  are 
             shown in Figures 6-2 and 6-3.

             Figure 6-2 Basic Receiving System for PSK Modulation.

             OMNIDIRECTIONAL
                 ANTENNA
                   |
                   |
                   |
                  \|/                    PSK MODEM
                VHF/UHF                    | |
             COMMUNICATIONS                | | 
                RECEIVER ----------------> TNC -------->  COMPUTER


             The difference between the two approaches is that the  first 
             uses a communications receiver designed for the 70 cm  band; 
             the second approach uses a general short wave receiver and a 
             front end down converter.





        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 55


             Figure  6-3  Alternate   Basic  Receiving  System  for   PSK 
             Modulation.


             OMNIDIRECTIONAL
                ANTENNA
                   |
                   |
             DOWNCONVERTER                  
                   |
                   |
               SHORT WAVE                 PSK MODEM
             COMMUNICATIONS                  | |
                RECEIVER                     | |                 
                   |                         | |
                   |-----------------------> TNC --------------> COMPUTER


             6.6 Receiving Signals from SARA-OSCAR 23.

             To receive signals from SARA all you need is a 2 m FM radio. 
             SARA  downlinks  on 145.955 MHz. Its signal is  weaker  than 
             both  UO-2 and DO-17. SARA's telemetry uses 300  baud  ASCII 
             wide  shift.  The  tones it uses comply with  the  old  Byte 
             Magazine audio cassette data storage format. The  modulation 
             sense (1's and 0's) are compatible to UO-1 and are  inverted 
             with respect to UO-2. SARA's data can thus be demodulated on 
             an  unmodified PK-232 as well as a UoSAT Modem, or  even  an 
             old  Byte  audio  tape  interface.  SARA  transmits   binary 
             telemetry  in a cycle that takes 2 minutes and  48  seconds. 
             The  sequence starts with an ASCII identification (as  shown 
             in  the  received example below) followed by many  lines  of 
             binary data. 

                      93162 NOISY LE GRAND CEDEX FRANCE
                      SATELLITE AMATEUR DE RADIOASTRONOMIE
                      ECOUTE DE L'ACTIVITE DECAMETRIQUE DE JUPITER
                      FX0SAT FX0SAT FX0SAT
                      CYCLE nxhw

             All the telemetry relates to the Radio Astronomy  Experiment 
             and voltages and temperatures. The information for  decoding 
             and processing the telemetry should be published shortly.

             Once  the telemetry decoding information is  published,  you 
             will  have  an  opportunity to  analyze  and  correlate  the 
             downlink  data  and perhaps discover  something  new.  SARA, 
             albeit a simple satellite, may have provided amateurs with a 
             tool to make new discoveries in radio astronomy in the 2  to 
             15 MHz range of the spectrum.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 56



             Reception  Reports of SARA are welcome and will be QSL'd  as 
             soon as possible. Send reports via the bureau to ON1KHP  who 
             is  serving  as SARA's QSL Manager, or  direct  to  BELAMSAT 
             (AMSAT-Belgium), c/o Patrick Hamptaux, Thier Des  Critchions 
             2, B-4600-Chenee, Belgium.

        7.0 Decoding Spacecraft Telemetry

        Apart from UoSAT-OSCAR 11, WEBER-OSCAR 18 and SARA-OSCAR 23, none 
        of  the  OSCAR spacecraft are designed  for  "Science"  purposes.  
        Their  telemetry consists of spacecraft housekeeping  parameters, 
        monitoring  on-board temperatures, voltages and currents.   While 
        much use can be made of these data, there isn't much real science 
        data available.   Even the scientific spacecraft are in the  main 
        unusable  by the average listener because information  about  the 
        scientific payload is not readily available.  Let's make a  start 
        with  these  spacecraft, then look to a follow  on  activity.  An 
        OSCAR does not have to be a separate spacecraft. The Soviet Union 
        has  provided  their amateurs with payload space  aboard  two  of 
        their  weather  satellites  [8]. NASA could do the  same  for  an 
        amateur scientific spacecraft which would monitor radiation,  the 
        earth's magnetic field and solar activity; such data being of use 
        to  radio  amateurs  for  predicting  propagation  and  providing 
        schools  with  data about the earth's environment.   NASA  has  a 
        'Mission to Planet Earth' project to provide an Earth Observation 
        Platform in 1997. An attached secondary payload to that platform, 
        transmitting  packetized  scientific telemetry  data  (with  well 
        publicized formats) in the 145 MHz amateur band or in the 136 MHz 
        scientific  band could really bring not only the  space  program, 
        but  the  educational  and scientific use of  space,  into  every 
        educational  institution in the country.  In the mean time,  this 
        section discusses the usable OSCAR spacecraft and their telemetry 
        and the corresponding decoding equations.

        The  satellites  have been built by  different  organizations  at 
        different times and each uses different data formats.  SARA  uses 
        a  300 baud ASCII format. DOVE and Fuji-OSCAR 20 transmit  in  an 
        ASCII  Packet  format,  yet  while DOVE  transmits  the  data  in 
        Hexadecimal  format,  Fuji-OSCAR 20 uses Decimal  Format.  AMSAT-
        OSCAR  16,  WEBER-OSCAR  18 and  LUSAT-OSCAR  19  transmit  their 
        telemetry  in  pure binary format.  By using  packetization,  the 
        data  quality is checked in the link itself and bad  packets  are 
        not normally passed to the computer from the TNC. AMSAT-OSCAR  13 
        does  not  have  any error checking at all, so it is  up  to  the 
        receiving  station to visually inspect the data before trying  to 
        convert  it to engineering units. UoSAT-OSCAR 11  also  transmits 
        its telemetry as ASCII text, but the designers of the  spacecraft 
        recognized that the downlink was prone to error and  incorporated 
        a checksum in its data format.  


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 57



        This  section discusses the data formats and  decoding  equations 
        associated with several of the OSCAR spacecraft.

        7.1 DOVE (DOVE-OSCAR 17)

        DOVE-OSCAR 17 was launched January 22, 1990. Its prime mission is 
        to  provide  an easily received Digital  Orbiting  Voice  Encoded 
        beacon  for educational and scientific use.  Dr. Torres  'Junior' 
        de Castro, PY2BJO sponsored the DOVE experiment. DOVE-OSCAR 17 is 
        licensed  in Brazil with the callsign PT2PAZ.  DOVE-OSCAR 17  was 
        built by AMSAT, occupies less than a cubic foot of space,  masses 
        8.5 kg and contains a V40 microprocessor and 8 Megabytes of  RAM. 
        Essentially  it is a loaded PC Clone in orbit.   AMSAT-OSCAR  16, 
        DOVE-OSCAR  17, WEBER-OSCAR  18 and LUSAT-OSCAR 19  are  commonly 
        known as Microsats and were constructed as a set by AMSAT  during 
        1989.   Each  of the Microsats contains bar magnets  which  align 
        them  along  the earth's magnetic field and is spun  around  that 
        axis by photon pressure from the sun acting on the  communication 
        antennas  which  are painted white on one side and black  on  the 
        other.

        Unfortunately a combination of two on-board hardware failures and 
        lack of available manpower in AMSAT (a volunteer organization for 
        all  practical purposes) have kept DOVE's voice off the air.   At 
        this  time DOVE only transmits packet telemetry.   DOVE-OSCAR  17 
        transmits  telemetry  in several different  transfer  packets  as 
        shown in Figure 7-1.

        Figure 7-1 A typical example of a DOVE-OSCAR 17 Telemetry Frame.

        23-Jan-91  02:49:23  DOVE-1*>TIME-1:
        PHT: uptime is 173/00:36:26.  Time is Wed Jan 23 02:47:30 1991

        23-Jan-91  02:49:26  DOVE-1*>TLM:
        00:59 01:59 02:87 03:31 04:59 05:5A 06:6E 07:52 08:6D 09:72 0A:A2
        0B:DC 0C:E9 0D:D8 0E:02 0F:26 10:CC 11:A8 12:01 13:04 14:AD 15:94
        16:98 17:94 18:96 19:98 1A:94 1B:91 1C:9B 1D:98 1E:25 1F:5F 20:BA

        23-Jan-91  02:49:27  DOVE-1*>TLM:
        21:95 22:82 23:24 24:1E 25:2A 26:01 27:02 28:02 29:01 2A:02 2B:02
        2C:01 2D:29 2E:02 2F:9E 30:CA 31:9E 32:11 33:CE 34:C4 35:9A 36:A8
        37:A6 38:B6

        23-Jan-91  02:49:28  DOVE-1*>STATUS:
         80 00 00 8F 00 18 CC 02 00 B0 00 00 0C 0E 3C 05 0B 00 04 04

        23-Jan-91  02:49:28  DOVE-1*>LSTAT:
        I P:0x3000 o:0 l:13081 f:13081, d:0



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 58


        23-Jan-91  02:49:28  DOVE-1*>WASH:
        wash addr:0680:0000, edac=0xd6

        Telemetry  data are transmitted in 57 (3A hex)  channels  in  two 
        segments  in the TLM packets. The format is AA:BB where  'AA'  is 
        the hexadecimal channel number and 'BB' the hexadecimal value  of 
        the telemetry at the time it was sampled.

        The telemetry decoding equations for DOVE are shown in Table 7.1-
        1. The Equations are in the form of a quadratic equation, 

        Y = A*N^2 + B*N + C
                                     
        where:    N = Telemetry Count (00 - FF);
                  A, B, C = Equation Coefficients;
                  Y = Result (In Specified Units).

        Note N must be converted from hexadecimal to decimal units before 
        performing  the calculation.  A sample decoded page is  shown  in 
        Table 7.1-2.


        Table 7.1-1 DOVE Telemetry Decoding Equations

        Spacecraft:  DOVE-1:                              Rev: 1
                                                          Date: 1/7/90  

        HEX   Description:      C:           B:           A:      Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx E/F Audio(W)+0.000       +0.0246      0.000       V(p-p)
         1    Rx E/F Audio(N)+0.000       +0.0246      0.000       V(p-p)
         2    Mixer Bias V:  +0.000       +0.0102      0.000       Volts
         3    Osc. Bias V:   +0.000       +0.0102      0.000       Volts 
         4    Rx A Audio (W):+0.000       +0.0246      0.000       V(p-p)
         5    Rx A Audio (N):+0.000       +0.0246      0.000       V(p-p)
         6    Rx A DISC:     +10.427      -0.09274     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +9.6234      -0.09911     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.0305      0.000       Volts
         B    +5V Rx Current:+0.000       +0.000100    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0108      0.000       Volts
         D    8.5V BUS:      +0.000       +0.0391      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000037    0.000       Amps
        10    +10V Bus:      +0.000       +0.05075     0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 59


        14    Rx Temp:       +101.05      -0.6051      0.000       Deg. C
        15    +X (RX) temp:  +101.05      -0.6051      0.000       Deg. C
        16    Bat 1 V:       +1.7932      -0.0034084   0.000       Volts
        17    Bat 2 V:       +1.7978      -0.0035316   0.000       Volts
        18    Bat 3 V:       +1.8046      -0.0035723   0.000       Volts
        19    Bat 4 V:       +1.7782      -0.0034590   0.000       Volts
        1A    Bat 5 V:       +1.8410      -0.0038355   0.000       Volts
        1B    Bat 6 V:       +1.8381      -0.0038450   0.000       Volts
        1C    Bat 7 V:       +1.8568      -0.0037757   0.000       Volts
        1D    Bat 8 V:       +1.7868      -0.0034068   0.000       Volts
        1E    Array V:       +7.205       +0.07200     0.000       Volts
        1F    +5V Bus:       +1.932       +0.0312      0.000       Volts
        20    +8.5V Bus:     +5.265       +0.0173      0.000       Volts
        21    +10V Bus:      +7.469       +0.021765    0.000       Volts
        22    BCR Set Point: -8.762       +1.1590      0.000       Counts
        23    BCR Load Cur:  -0.0871      +0.00698     0.000       Amps
        24    +8.5V Bus Cur: -0.00920     +0.001899    0.000       Amps
        25    +5V Bus Cur:   +0.00502     +0.00431     0.000       Amps
        26    -X Array Cur:  -0.01075     +0.00215     0.000       Amps
        27    +X Array Cur:  -0.01349     +0.00270     0.000       Amps
        28    -Y Array Cur:  -0.01196     +0.00239     0.000       Amps
        29    +Y Array Cur:  -0.01141     +0.00228     0.000       Amps
        2A    -Z Array Cur:  -0.01653     +0.00245     0.000       Amps
        2B    +Z Array Cur:  -0.01137     +0.00228     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D    BCR Input Cur: +0.06122     +0.00317     0.000       Amps
        2E    BCR Output Cur:-0.01724     +0.00345     0.000       Amps
        2F    Bat 1 Temp:    +101.05      -0.6051      0.000       Deg. C
        30    Bat 2 Temp:    +101.05      -0.6051      0.000       Deg. C
        31    Baseplt Temp:  +101.05      -0.6051      0.000       Deg. C
        32    FM TX#1 RF OUT:+0.0256      -0.000884    +0.0000836  Watts
        33    FM TX#2 RF OUT:-0.0027      +0.001257    +0.0000730  Watts
        34    PSK TX HPA Temp+101.05      -0.6051      0.000       Deg. C
        35    +Y Array Temp: +101.05      -0.6051      0.000       Deg. C
        36    RC PSK HPA Temp+101.05      -0.6051      0.000       Deg. C
        37    RC PSK BP Temp:+101.05      -0.6051      0.000       Deg. C
        38    +Z Array Temp: +101.05      -0.6051      0.000       Deg. C 
        39    S band TX Out: -0.0451      +0.00403     0.000       Watts
        3A    S band HPA Temp+101.05      -0.6051      0.000       Deg. C













        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 60


        Table  7.1-2 Sample Decoded (General Housekeeping) Page  of  DOVE            
        Telemetry

        PHT: uptime is 177/12:34:12.  Time is Sun Jan 27 14:45:16 1991

        -X Array Cur   : 0.174 A             Array V        :22.829 V  
        +X Array Cur   : 0.000 A             +Z Array V     :23.836 V 
        -Y Array Cur   : 0.000 A             Ext Power Cur  : 0.000 A 
        +Y Array Cur   : 0.000 A             BCR Input Cur  : 0.480 A 
        -Z Array Cur   : 0.000 A             BCR Output Cur : 0.314 A 
        +Z Array Cur   : 0.251 A             BCR Set Point  :   119   
        IR Detector    :    56               BCR Load Cur   : 0.241 A 
        +Z Array Temp  :   3.0 C                                      
        +Y Array Temp  :   4.8 C              Battery 1 V  : 1.330 V             
                                              Battery 2 V  : 1.346 V             
        +2.5V  VREF    : 2.506 V              Battery 3 V  : 1.337 V             
        Ground REF     : 0.020 V              Battery 4 V  : 1.325 V  
                                              Battery 5 V  : 1.350 V
         Bat 1 Temp   :   3.0 C               Battery 6 V  : 1.431 V
         Bat 2 Temp   : -24.8 C               Battery 7 V  : 1.343 V
         TX#1 RF OUT  :   0.0 W               Battery 8 V  : 1.344 V
         TX#2 RF OUT  :   3.7 W                                       

        The  TIME-1  packets  identify  the  time  that  the  data   were 
        downlinked.   The Uptime value in the time packet tells  you  how 
        long the software has been running (since last upload).

        The STATUS packets contain information about spacecraft  on-board 
        status.  These  bytes, have in the past, been  changed  by  AMSAT 
        without   prior  or  post  notification  to  the  radio   amateur 
        community.   The   LSTAT  packet  contains   engineering   status 
        information which has not been published other than that the last 
        value "d:0" means the spacecraft is not set up as a digipeater.

        The  WASH packets provide engineering information about  the  on-
        board RAM memory.
                                             
        7.2 UoSAT-OSCAR 11

        UoSAT-OSCAR  11 which was launched March 1, 1984, is  similar  to 
        and  is a follow on to the now re-entered UoSAT-OSCAR 9.  It  was 
        designed and built at the Department of Electronic and Electrical 
        Engineering  at the University of Surrey, England.  It was  built 
        to develop scientific experimentation and space education.  While 
        much invaluable experience has been received by the UoSAT people, 
        not much has been published in the general educational and  radio 
        amateur  press about its on-board experiments and telemetry  data 
        formats.   As such, apart from a small group of dedicated  users, 
        UoSAT-OSCAR  11  seems to have been ignored by  the  majority  of 
        radio amateurs and educational institutions.  


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 61



        UoSAT-OSCAR 11 carries four on-board experiments:- a Digital Com-
        munications Experiment, a Space Dust Experiment, a Charge Coupled 
        Device (CCD) Video Camera Experiment and a Digitalker Experiment.

        The Digital Communications Experiment demonstrated the concept of 
        store-and-forward digital communications using spacecraft in  low 
        earth  orbit.  The Space Dust Experiment measures the  impact  of 
        dust particles, and calculates the momentum of the particles. The 
        CCD  Video  Camera Experiment takes pictures of the  earth  at  a 
        resolution of 384 x 256 pixels with 128 gray levels.  This exper-
        iment  does not seem to have returned any usable  pictures.   The 
        Digitalker  Experiment  provides clear digitized  voice  using  a 
        fixed vocabulary and is switched on from time to time.

        UoSAT-OSCAR   11  transmits  a  number  of  different  types   of 
        telemetry.  WHATS-UP  can only decode and display  the  real-time 
        telemetry.  Should you tune in signals from UoSAT-OSCAR  11,  you 
        may get anything. Hang in there, sooner or later it will transmit 
        real-time  telemetry, if not on one pass, then on the  next.  The 
        real-time telemetry is transmitted as 1200 baud ASCII data  using 
        FSK.  The  sense of the modulation is inverted  with  respect  to 
        convention  due  to the wide popularity of a  BBC  computer  tape 
        interface (which used the inverted modulation) in England at  the 
        time the spacecraft was built.  This means that either a  special 
        modem has to be built to receive the data or the PK-232 has to be 
        modified  before it will copy signals from UoSAT-OSCAR  11.  This 
        modification is needed because the PK-232 RXR parameter does  not 
        work   above  300  baud  due  to  a  hardware  limitation.   This 
        modification  performs  the equivalent of the  RXR  operation  in 
        hardware by taking advantage of an unused inverter inside the PK-
        232.

        What  has to be done is to wire U15 pins 1 and 2 to a  switch  in 
        series  with  the output to JP4. Adding a green LED to  show  the 
        state  of the switch (at a glance) is optional. The steps are  as 
        follows:

        1. Drill  a 1/4 inch hole in the front panel of the PK-232  above 
           the red DCD LED.

        2. Mount  a Double Pole Double Throw (SPDT) switch on  the  front 
           panel  of  the PK-232 where it will not interfere  with  other 
           components  (near the upper left corner by the AEA logo  above 
           the threshold control).

        3. Carefully  cut the circuit board trace connecting U15's pin  6 
           to the inside pin of JP4.  This trace is easiest to cut  where 
           it comes out from under R20 on the top (component side) of the 
           PC  board.  Be sure to double check that this is  the  correct 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 62


           trace  with an ohm meter.  Cut with care (with a sharp  X-acto 
           knife) so adjacent traces are not touched.

        4. Solder a jumper wire between U15's pins 1 and 6.

        5. Connect the center of one pole on this switch to the inner pin 
           of  JP4  or  the  trace that goes to  it  (which  was  cut  to 
           disconnect it from U15 pin 6).

        6. Connect  the  corresponding  switch  contact  which  will   be 
           hardware "RXR OFF" to U15 pin 6.

        7. Connect  the  corresponding  switch  contact  which  will   be 
           hardware "RXR ON" to U15 pin 2.

        8. Mount  a green LED on the front panel of the PK-232 above  the 
           red DCD LED.

        9. Wire  one leg of the LED to the other pole of the switch,  the 
           other end to a 1K ohm resistance (test the LED first to  make 
           sure you wire it the correct way). 

        10. Wire the other end of the resistance to +12V near the voltage 
           regulator.  Do not wire it to the battery back up voltage  (if 
           the  LED stays lit when you turn the PK-232 off, you wired  it 
           wrongly).

        11. Wire one side of the switch to ground so the green LED lights 
           when the REVERSE position is selected.

        To copy the UoSAT-OSCAR 11 FM AFSK ASCII Telemetry on 145.825 Mhz 
        set  the  new hardware RXR switch in the "reverse"  position.  Be 
        sure  to  return  your RXR switch to "normal" when  you  want  to 
        return to regular operation, as this switch is in the signal path 
        in all modes when the PK-232's internal modem is used.

        A  typical  telemetry  frame starts with a  non  printing   ASCII 
        character  (1E  hexadecimal) followed by the  identification  and 
        date.  The  date  code  can be  deciphered  using  the  following 
        YYMMDDWHHMMSS format where YY is the last two digits of the year, 
        MM,  the month, DD, the day of the month, W, the day of the  week 
        (Sunday = 0), the remainder being hours,minutes and seconds.  All 
        times  are given in UTC. A blank line follows, then follow  seven 
        lines worth of ten channels per line. The format of each line  is 
        as shown below.

        NNDDDCNNDDDCNNDDDCNNDDDCNNDDDCNNDDDCNNDDDCNNDDDCNNDDDCNNDDDC

        where NN is the channel number, DDD the data and C a checksum  to 
        validate  the data.  The checksum is needed because there  is  no 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 63


        error  checking built into the link. Each channel thus  comprises 
        six  digits.  The  checksum  is  computed  for  each  channel  by 
        'exclusive  or'ing  (XOR) each nibble (4 bits) of each of  the  6 
        characters in that channel. A zero result means that the data was 
        received  correctly,  a  non-zero  result  means  the  data   was 
        corrupted.  Figure  7.2-1 contains an example of the  raw  UoSAT-
        OSCAR  11  data showing some of the errors due to  noise  on  the 
        downlink.

        Figure 7.2-1 Example  of a Received Raw UoSAT-OSCAR 11  Telemetry 
                     Data Frame

        00519D0141370267650361400404660503;4 6019E07045608040C08036C
        10519C11298312000313056114069A15529A!6188;175452185905195058
        20519F21220322662223000124001725000726093E27541528564D294681
        30519E31041732287C33568B34007035217236276637393D38426B39455E
        40649F41117242647343061044162545000146000247444748454949422x
        50456251108D52634653284p54663215000056p00357451258447A59460E
        60826A615FC1625F4A63334164440265160466174267700668000E69000F
        UOSAT-2           9101281004625

        7.3 AMSAT-OSCAR 13

        AMSAT-OSCAR  13 which was launched June 15, 1988 was built  as  a 
        joint venture between radio amateurs in the U.S.A. and in Germany 
        organized  as  the Radio Amateur Satellite  Corporation  (AMSAT).  
        AMSAT-OSCAR  13 is a spin stabilized long life long  range  radio 
        amateur    communications   satellite   which   provides    daily 
        intercontinental communications  capability for hours at a  time.  
        It  contains  a number of analog and  digital  transponders  with 
        communications links on several frequencies. An on-board computer 
        based on the RCA 1802 microprocessor controls the spacecraft  and 
        generates the downlink telemetry.  Schedules are published in the 
        amateur  radio  press  which  provide  information  as  to  which 
        transponder is active at any time during the orbit.   AMSAT-OSCAR 
        13  also  contains a motor which was used by  radio  amateurs  to 
        boost the spacecraft from the orbit the rocket placed it in  into 
        its operational orbit.  

        AMSAT-OSCAR  13  transmits telemetry in a number of ways  on  two 
        beacons.  The two meter beacon is on a frequency of  145.812  MHz 
        and  carries  CW,  50  baud RTTY,  and  400  baud  PSK  telemetry 
        according to a published schedule.  WHATS-UP can only decode  and 
        display  the 50 baud RTTY telemetry which is transmitted  in  the 
        form  of Z blocks shown in Table 7.3-1.  The block is  identified 
        as  a 'Z' block by the letter 'Z' before the words "HI.  THIS  IS 
        AMSAT OSCAR 13" which identify the spacecraft.
           
        The block starts with the letter 'Z' in the first line.  Time and 
        status  information  follows, then the  first  telemetry  channel 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 64


        begins several lines down and is shown with the value of 193. Six 
        lines   of  telemetry,  each  line  containing  ten  values   are 
        transmitted,  with  a  blank  line  separating  the  two  halves.  
        Following the telemetry lines, the spacecraft may transmit  plain 
        text information of general interest.  Although the Z block  only 
        contains  60 channels, the equations for decoding all 128 of  the 
        telemetry  channels  are presented in Table 7-3.2  in  which  the 
        Channel Numbers are shown in Hexadecimal. 

        The Bytes in the block are identified in the followings ways:

             C  - unsigned count (0 to +255)
             Cs - signed count (-128 to +127, 2s complement)
             Cx - signed count (+63 to -192, #3F=+63, #FF=-1, #80=-128,
                             #7F=-129, #40=-192, modified 2s complement)

        All  temperature  channels  are  decoded  identically  using  the 
        equation T = (C-120)/1.71  (in Degrees Centigrade).  All channels 
        measuring   currents  use  a  linear  equation   with   different 
        calibrations  constants.  Three  equations  are  used   providing 
        maximum current values of 1A, 2.5A and 5A, as follows:

               1A:  I = (C-15)*4.854 mA
             2.5A:  I = (C-15)*12.135mA
               5A:  I = (C-15)*24.27 mA

        Table 7.3-1 AMSAT-OSCAR 13 RTTY Telemetry Block

             Z  HI. THIS IS AMSAT OSCAR 13
                  05.02.54  8661
             .0086   .0000   .07B9                   
                                
             64  6   0   1   16  218 1               
                                
             
             193 170 158 143 181 144 147 140 200 7   
             147 7   7   7   165 29  100 7   149 7   
             10  7   145 115 34  7   153 129 122 180 
             
             152 73  7   145 137 55  7   183 136 151 
             7   154 137 169 211 142 127 100 9   140 
             161 7   173 149 150 154 14  131 127 210 
             HI THIS IS AMSAT OSCAR 13 08SEP90
             NEW AO13 SCHEDULE FROM 17OCT90 AFTER MOVE TO LON 180  LAT 0
             MODE B  MA 000 TO 095
             MODE JL MA 095 TO 125
             MODE LS MA 125 TO 130
             MODE S MA 130 TO 135
             MODE BS MA 135 TO MA 140
             MODE B  MA 140 TO 256


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 65



        Table 7.3-2 AMSAT-OSCAR 13 Telemetry Decoding Equations

        #    Label          Equation             Remarks

        00   Uin-BCR        U=(C-10)*167mV   U-Panel: +0.6V @ 0.35A
                                                      +0.7V @ 1A
        01   Tx-PWRout-L    Average power=(261-C)^2 / 724 Watts
                                             rectified envelope voltage.
        02   T-Rx-U         Temp             Mode-B receiver temperature.
        03   ---
        04   Uout-BCR       U=(C-10)*79.5mV  BCR output voltage.
        05   ---
        06   T-TX-U         Temp             Mode-B transmitter 
                                             temperature.
        07   I-14V-ST       5A               Transponder separation bus.
        08   U-10V-C        U=(C-10)*53.2mV  Computer supply
        09   Press He-Hi    off              Helium tank pressure.
        0A   T-IHU          Temp             Integrated Housekeeping Unit
        0B   I-14V-S        1A               Separation bus, 14V that 
                                             supplies
                                             torquer and LIU.
        0C   BCR-Oscill1    >~6=OK           BCR status. No count = not
                                             working. Typically C=80.
        0D   Press He-Lo    off              Helium regulator output.
        0E   T-BCR          Temp             Battery Charge Regulator.
        0F   I-10V-C        1A               10V continuous power supply.
        10   BCR-Oscill2    As channel 0C
        11   Press Tank     off              N2O4 tank pressure.
        12   T-SEU          Temp             Sensor Electronics Unit
        13   IbatCharge     2.5A             Positive Current to battery.
        14   L-Sensor (A)   U=(C-10)*8.53mV  Light-Sensor Antenna Side.
        15   Motor Valve    off
        16   T-ABAT1        Temp             Auxiliary battery 1
        17   I-BCR-OUT      5A               14V line to battery and 
                                             other consumers.
        18   L-Sensor (M)   U=(C-10)*8.53mV  Light-Sensor Motor Side.
        19   ---
        1A   T-ABAT2        Temp             Auxiliary battery 2
        1B   I-BCR-IN       Equivalent to total current of all panels,
                            not available due to sensor failure.
        1C   Spin rate      C>131,  Spin rate=479/(C-109)-2 rpm
                            C<=131, Spin rate=(131-C)*0.85+20 rpm
                                             Sensor angular position
                                             oscillator. Lock indication
                                             channel #47.
        1D   Rx-L-AGC       Gain reduction=(C-75)^2 / 1125 dB
        1E   T-MBAT         Temp             Mean battery (normally in  
                                             use)
        1F   I-Panel6       1A               Solar panel 6


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 66


        20   Tx-PWRout-U    Average power=(287-C)^2 / 1796 Watts
                                             As channel 01.
        21   T-He-Tank      Temp
        22   T-Panel1       Temp
        23   I-Panel5       1A
        24   Rx-U-AGC       Gain reduction=(C-71)^2 / 2465 dB
        25   T-Tx-L         Temp             Mode-JL transmitter.
        26   T-Panel3       Temp
        27   I-Panel4       1A
        28   ---
        29   T-Rx-L         Temp             Mode-L receiver.
        2A   T-Panel5       Temp
        2B   I-Panel3       1A
        2C   U-14V-ST       U=(C-10)*66.8mV  Transponder separation bus.
        2D   T-RUDAK        Temp             RUDAK temperature.
        2E   T-top          Temp             Arm 1, Antenna side.
        2F   I-Panel2       1A
        30   U-9V-U         U=(C-10)*54mV    Internal 9 volt bus from
                                             Mode-B transponder.
        31   T-wall-arm2    Temp
        32   T-bottom       Temp             Arm 1, Motor side.
        33   I-Panel1       1A
        34   ---
        35   T-wall-arm1    Temp
        36   T-N2O4         Temp
        37   ---
        38   U-ABAT         U=(C-10)*78.5mV  Auxiliary battery.
        39   T-S-xpnder     Temp             Mode-S transponder.
        3A   T-L-Sensor     Temp             Light sensor antenna side.
        3B   ---
        3C   U-9V-L         U=(C-10)*45.4mV  As channel 30, Mode-L
        3D   T-AZ50-Tank    Temp
        3E   T-nutation damper  Temp         Arm 3.
        3F   ---
        40   ES-Sensitivity 2MUX0            Earth Sensor sensitivity
                                             threshold.
                            bit   significance
                            0 LSB  20mV
                            1      37mV      Hysteresis 200mV
                            2      75mV      Threshold  600mV
                            3     150mV
                            4     300mV
                            5     600mV
                            6     1.2V
                            7 MSB 2.4V

        41   Antenna/SERI   2MUX1            Antenna relays and SERI 
                                             resistors.
                            bit   significance
                            0 LSB Hi-gain  2m  to U


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 67


                            1     Hi-gain 70cm to L
                            2     --+ SERI-1  load resistor for
                            3     -+! SERI-2  both Light-Sensors
                                   !! resistance
                                   00  7.5 Ohm
                                   01  3.9 Ohm
                                   10  2.3 Ohm
                                   11  5.9 Ohm

        42   RUDAK-Status   2MUX2            IN-B (ex Motor-PWR).
                            C=82, Standard-ROS  (S)
                            C=78, Emergency-ROS (N, Not-ROS)
                            C=80, Primitive-ROS (P)

        43   S&RUDAK-CNTL   2MUX3            Mode-S and RUDAK interface.
                            bit   significance
                            0 LSB RUDAK OFF
                            1       "   NMI/
                            2       "   Byte Clock
                            3       "   Byte count reset
                            4      ---
                            5     Mode-S Beacon ON
                            6       "    Squelch defeated
                            7 MSB   "    Squelch Hi Sensitivity

        44   BCR-Sin        2MUX4            Array voltage offset.
                            U=29.1+(Cs*100)mV  (16.3V...41.8V)
        45   BCR-Sout       2MUX5            Battery knee voltage offset.
                            U=14.98+(Cx*20)mV  (11.14...16.2V = 192...63)

        46   BCR-relays     2MUX6
                            bit   significance
                            0 LSB BCR-2 ON
                            1     Auxiliary battery charging
                            2     Auxiliary battery connected,
                                  Main battery disconnected.

        47   SS-1           C=255 or C=0, PLL locked
                                             Sun-Sensor angular position
                                             oscillator, Slit antenna 
                                             side.
        48   SS-2           Time offset from SS-1
        49   Flag-SS        C=1, SS-1        Sun sensor data.
                            C=2, SS-2
        4A   SPIN-RAW                        Raw spin count (1/256).

        4B   Sensor-control bit   significance  (OUT4)
                            0 LSB --+ MUX-CTRL for sensor elec. module
                            1     -+!
                                   !!


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 68


                                   00 - Sun data
                                   01 - spin ref./spin counter
                                   10 - ES lower beam
                                   11 - ES upper beam
                            2     Earth sensor positive edge select.
                                  (Strobes value of spin count at 
                                  transition.)
                            3     Motor Instrumentation ON.
                                  (Pressure sensors, motor valve 
                                  indicator.)
                            4     0.3V Sun Sensor Sensitivity
                            5     0.6V  "    "         "
                            6     1.2V  "    "         "
                            7 MSB 2.4V  "    "         "
                                  (Max. threshold #F = 1 solar constant)
        4C   SS-correction
        4D   Last ES-A      Z                last ES-pulse Antenna side.
        4E     "            O#               (Orbit number and MA value)
        4F   Last ES-M      Z                last ES-pulse Motor side.
        50     "            O#               (Orbit number and MA value)
        51   Lockoutrange   Within +- C counts from sun sensor pip, earth
                            sensor handler ignores data (Spin count 1 
                            circle = 256 counts.)
        52   ES-A           Strobed spin count at edge selected,
                                              Antenna Side beam.
        53   Update Flag1   Indicates update, Antenna Side beam.
        54   ES-M           As channel 52     Motor Side beam.
        55   Update Flag2   As channel 53      "    "    "
        56   S/C STATUS     bit   significance
                            0 LSB LIU power ON
                            1     S/A plug status 0=Safe, 1=Arm
                            2     RUDAK-out (lock)
                            3     Mode-S Squelch open
                            4     ---
                            5     Memory Soft error Counter
                            6       "         "      "
                            7 MSB   "         "      "
        57   ---
        58   ---
        59   ---
        5A   ---
        5B   N              no of 20ms per dot, morse speed.
        5C   n              running count of units for morse.
        5D   ---
        5E   TRANSPONDER    bit   significance  (OUT7)
                            0 LSB GB OFF
                            1     GB FSK (1=+170Hz)
                            2     DPSK OFF
                            3     EB ON
                            4     --+ PSK source


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 69


                            5     -+! for GB (EB: don't care)
                                   !!
                                   00 - no PSK
                                   01 - ranging
                                   10 - EB source
                            6     Low power transponder ON
                            7 MSB Passband OFF (Beacons and Mode-J +3dB)
        5F   ---
        60   MODUS          bit   significance  (magnet control)
                            0     magnet system ON
                            1     underspin magnet
        61   M-Soll         magnet vector desired angle to the despun sun
                            (clockwise as seen from top, 1 circle = 256)
        62   M-Out          bit significance (OUT3, also L,S,J control)
                            0 LSB polarity Arm 1
                            1     polarity Arm 2
                            2     polarity Arm 3
                            3     Magnet power ON
                            4     Mode-J ON
                            5     ---
                            6     Mode-S ON
                            7 MSB Mode-L ON
        63   O-FRAC-lo      Fractional Z increment in 20ms
        64   O-FRAC-hi                       Counts down to 0 from preset
                                             value. 255th Z has different
                                             value of O-FRAC. ~7000 
                                             counts/Z.
        65   O/256          Z from perigee
        66   O#-lo          Orbit number
        67   O#-hi
        68   UHR            10ms             UTC
        69                  sec
        6A                  min
        6B                  hour
        6C                  day              1st  January  1978 = AMSAT 
                                             day 0.
        6D                  256day
        6E   SU0            10ms             IPS stopwatch 0.
        6F                  sec
        70                  min
        71                  min*256
        72   SU1            10ms             IPS stopwatch 1.
        73                  sec
        74                  min
        75                  min*256
        76   SU2            10ms             IPS stopwatch 2.
        77                  sec
        78                  min
        79                  min*256
        7A   SU3            10ms             IPS stopwatch 3.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 70


        7B                  sec
        7C                  min
        7D                  min*256
        7E   Event-Lo                        Used as event ID word in
        7F   Event-Hi                        intermediate buffer.


        7.4 AMSAT-OSCAR 16, WEBER-OSCAR 18 and LUSAT-OSCAR 19 

        AMSAT-OSCAR  16, WEBER-OSCAR 18 and LUSAT-OSCAR 19 were  launched 
        January 22, 1990 together with DOVE-OSCAR 17.  AMSAT-OSCAR 16 and 
        LUSAT-OSCAR 19 are designed to provide a platform for experiments 
        with  digital  store-and-forward communications techniques  as  a 
        follow-on to the Digital Communications Experiment of UoSAT-OSCAR 
        11.   LUSAT-OSCAR 19 is sponsored by AMSAT in  Argentina.  WEBER-
        OSCAR  18 is an engineering project of the Center  for  Aerospace 
        Studies at Weber State University in Utah.  It has the capability 
        for  digital communications but is not used as such. It  contains 
        an on-board video camera which has returned pictures of the earth 
        using  a non standard format picture transmission format.  WEBER-
        OSCAR  18 also carries a number of experiments. The  Spectrometer 
        experiment  is  designed  to observe  the  spectrum  of  sunlight 
        reflected  off the earth's atmosphere and surface.  The  Particle 
        Impact Detector is a piezoelectrical crystal mounted on the  side 
        of  the spacecraft which produces an output voltage each  time  a 
        microparticle   impact  occurs.   The   Magnetometer   Experiment 
        contains two orthogonal flux gate magnetometers. As they were not 
        calibrated  they  can  only provide  information  about  relative 
        changes in the magnetic environment of the spacecraft. As in  the 
        case  of  UoSAT-OSCAR 11, data about the  experiments  and  their 
        telemetry  calibrations is lacking in the general  amateur  radio 
        press.

        These spacecraft downlink telemetry in the 437MHz band similar to 
        that  of  DOVE but using a BINARY format in  an  unpublished  and 
        apparently  "changeable  at any time  without  notice"  sequence. 
        WHATS-UP  intercepts  the binary telemetry and converts it  to  a 
        pseudo  DOVE format as shown in Table 7.4-1 before  decoding  and 
        displaying   the  information.   The  decoding  equations   first 
        published by AMSAT in The AMSAT Journal are given in Tables  7.4-
        2, 7.4-3 and 7.4-4.  











        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 71


        Table 7.4-1 Example of Pseudo DOVE Display of Intercepted  Binary 
                    Telemetry and other intercepted Microsat Packets

        27-Jan-91  17:04:22  LUSAT-1*>AMARG:
        Jan 23, 1600Z.

        AART driver loaded.
        Reload will continue in a short time

        73, LU7XAC
        AMARG Control Team

        27-Jan-91  16:41:50  PACSAT-1*>TIME-1:
        PHT: uptime is 004/10:14:01.  Time is Sun Jan 27 16:40:51 1991
         
        27-Jan-91  16:41:54  PACSAT-1*>AMSAT:
        Jan 22, 8:03 UTC - Reload in progress.  Digi on.  No BBS till the 
        weekend.
        NK6K

        27-Jan-91  16:41:54  PACSAT-1*>LSTAT:
        I P:0x3000 o:0 l:13884 f:13884, d:1 st:0
        27-Jan-91  16:42:48  N8ITP>PACSAT-1*>N8ITP [C]
        27-Jan-91  16:42:50  N8ITP>PACSAT-1*>N8ITP (UA)
        27-Jan-91  16:42:55  N8ITP>PACSAT-1*>N8ITP:
        test1122334455

        27-Jan-91  17:04:22  LUSAT-1*>BCRXMT:
        vmax=762169 battop=766771 temp=218292

        27-Jan-91  17:06:31  LUSAT-1*>LSTAT:
        I P:0x3000 o:0 l:13417 f:13417, d:0 st:2

        27-Jan-91  17:06:38  LUSAT-1*>TIME-1:
        PHT: uptime is 005/14:48:41.  Time is Sun Jan 27 17:05:33 1991
         
        27-Jan-91  17:06:41  LUSAT-1*>TLM:
        00:DC 01:0E 02:30 03:0F 04:3A 05:10 06:DE 07:11 08:84 09:12 
        0A:00 0B:13 0C:E4 0D:14 0E:A9 0F:15 10:A8 11:16 12:6C 13:17 
        14:64 15:18 16:69 17:19 18:69 19:1A 1A:66 1B:1B 1C:6D 1D:1C 
        1E:5F 1F:1D 20:62 21:1E 22:D9 23:1F 24:62 25:20 26:BA 27:21 
        28:B0 29:22 2A:79 2B:23 2C:2C 2D:24 2E:24 2F:25 30:28 31:00 

        14-Feb-91  03:02:48  N4HY>LUSAT-1*>N4HY [D]
        14-Feb-91  03:02:49  N4HY>LUSAT-1*>N4HY (UA)
        14-Feb-91  03:03:09  LUSAT-1*>COMLUS:
        COMMAND 9 ACK

        14-Feb-91  03:06:51  LUSAT-1*>STATUS:
        31 34 2D 46 65 62 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 72


        Table 7.4.2 AMSAT-OSCAR 16 Telemetry Decoding Equations

        Spacecraft:  PACSAT-1:                            Rev: 
                                                          Date: 7/25/91  

        Equations are in the form: Y = A*N^2 + B*N + C
                                     
                                   where: 

                                      N = Telemetry Count (00 - FF) 
                                      A, B, C = Equation Coefficients
                                      Y = Result (In Specified Units)

        HEX   Description:        C:           B:        A:      Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx D DISC:     +9.202       -0.08990     0.000       kHz
         1    Rx D S meter:  +0.000       +1.000       0.000       Counts
         2    Rx C DISC:     +9.179       -0.09277     0.000       kHz
         3    Rx C S meter:  +0.000       +1.000       0.000       Counts
         4    Rx B DISC:     +9.837       -0.08838     0.000       kHz
         5    Rx B S meter:  +0.000       +1.000       0.000       Counts
         6    Rx A DISC:     +9.779       -0.09144     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +10.817      -0.09911     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.0305      0.000       Volts
         B    +5V Rx Current:+0.000       +0.000250    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0108      0.000       Volts
         D    +8.5V Bus:     +0.000       +0.0391      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000037    0.000       Amps
        10    +10V Bus:      +0.000       +0.0500      0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts
        14    Rx Temp:       +101.05      -0.6051      0.000       Deg. C
        15    +X (RX) temp:  +101.05      -0.6051      0.000       Deg. C
        16    Bat 1 V:       +1.8225      -0.0038046   0.000       Volts
        17    Bat 2 V:       +1.9418      -0.0046890   0.000       Volts
        18    Bat 3 V:       +1.8699      -0.0041641   0.000       Volts
        19    Bat 4 V:       +1.7403      -0.0032880   0.000       Volts
        1A    Bat 5 V:       +1.8792      -0.0042492   0.000       Volts
        1B    Bat 6 V:       +2.0499      -0.0054532   0.000       Volts
        1C    Bat 7 V:       +1.9062      -0.0045331   0.000       Volts
        1D    Bat 8 V:       +1.7536      -0.0033192   0.000       Volts
        1E    Array V:       +8.055       +0.06790     0.000       Volts
        1F*   +5V Bus:       +2.864583    4.090715E-2 -1.930042E-4 Volts
        20*   +8.5V Bus:     +7.720951    +8.25979E-3 -1.76254E-5  Volts
        21*   +10V Bus:      +8.882535    +1.39771E-2  0.000       Volts


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 73


        22    BCR Set Point: -6.1130      +1.1270      0.000       Counts
        23    BCR Load Cur:  -0.0477      +0.00767     0.000       Amps
        24    +8.5V Bus Cur: -0.00179     +0.000894    0.000       Amps
        25    +5V Bus Cur:   -0.00104     +0.00406     0.000       Amps
        26    -X Array Cur:  -0.00995     +0.00243     0.000       Amps
        27    +X Array Cur:  -0.02370     +0.00254     0.000       Amps
        28    -Y Array Cur:  -0.02220     +0.00273     0.000       Amps
        29    +Y Array Cur:  -0.01810     +0.00259     0.000       Amps
        2A    -Z Array Cur:  -0.02230     +0.00221     0.000       Amps
        2B    +Z Array Cur:  -0.02000     +0.00232     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D*   BCR Input Cur: -2.103334E-2 +3.382738E-3 0.000       Amps
        2E*   BCR Output Cur:-7.146611E-3 -5.247935E-5 4.878499E-5 Amps
        2F    Bat 1 Temp:    +101.05      -0.6051      0.000       Deg. C
        30    Bat 2 Temp:    +101.05      -0.6051      0.000       Deg. C
        31    Baseplt Temp:  +101.05      -0.6051      0.000       Deg. C
        32    PSK TX RF Out: -0.0291      +0.00361     +0.0000869  Watts
        33    RC PSK TX Out: +0.0055      +0.00172     +0.0001180  Watts
        34    PSK TX HPA Temp+101.05      -0.6051      0.000       Deg. C
        35    +Y Array Temp: +101.05      -0.6051      0.000       Deg. C
        36    RC PSK HPA Temp+101.05      -0.6051      0.000       Deg. C
        37    RC PSK BP Temp:+101.05      -0.6051      0.000       Deg. C
        38    +Z Array Temp: +101.05      -0.6051      0.000       Deg. C 
        39    S band HPA Temp:  0.00       1.0000      0.000       Counts
        3A    S band TX Out: -0.0088      +0.00435     0.000       Watts
         
        * Revised in this release 
         
























        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 74


        Table 7.4.3 WEBER-OSCAR 18 Telemetry Decoding Equations

        Spacecraft:  WEBER-1:                            Rev: 1
                                                         Date: 1/7/90  

        Equations are in the form: Y = A*N^2 + B*N + C
                                     
                                   where: 
                                      N = Telemetry Count (00 - FF) 
                                      A, B, C = Equation Coefficients
                                      Y = Result (In Specified Units)


        HEX   Description:        C:           B:          A:      Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx D DISC:     +11.087      -0.08949     0.000       kHz
         1    Rx D S meter:  +0.000       +1.000       0.000       Counts
         2    Rx C DISC:     +10.322      -0.09448     0.000       kHz
         3    Rx C S meter:  +0.000       +1.000       0.000       Counts
         4    Rx B DISC:     +10.348      -0.09004     0.000       kHz
         5    Rx B S meter:  +0.000       +1.000       0.000       Counts
         6    Rx A DISC:     +11.387      -0.09535     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +10.746      -0.09348     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.03523     0.000       Volts
         B    +5V Rx Current:+0.000       +0.000234    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0133      0.000       Volts
         D    8.5V BUS:      +0.000       +0.0524      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000033    0.000       Amps
        10    +10V Bus:      +0.000       +0.0767      0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts
        14    Rx Temp:       +100.01      -0.5980      0.000       Deg. C
        15    +X (RX) Temp:  +100.01      -0.5980      0.000       Deg. C
        16    Bat 1 V:       +1.8292      -0.0037196   0.000       Volts
        17    Bat 2 V:       +1.8202      -0.0036943   0.000       Volts
        18    Bat 3 V:       +1.8050      -0.0036721   0.000       Volts
        19    Bat 4 V:       +1.8576      -0.0038979   0.000       Volts
        1A    Bat 5 V:       +1.8095      -0.0037439   0.000       Volts
        1B    Bat 6 V:       +1.8979      -0.0041754   0.000       Volts
        1C    Bat 7 V:       +1.8246      -0.0038126   0.000       Volts
        1D    Bat 8 V:       +1.7486      -0.0030475   0.000       Volts
        1E    Array V:       +7.800       +0.06790     0.000       Volts
        1F    +5V Bus:       +1.838       +0.0312      0.000       Volts
        20    +8.5V Bus:     +5.793       +0.0184      0.000       Volts
        21    +10V Bus:      +7.650       +0.0250      0.000       Volts


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 75


        22    BCR Set Point: -6.1963      +1.1277      0.000       Counts
        23    BCR Load Cur:  -0.0405      +0.00620     0.000       Amps
        24    +8.5V Bus Cur: +0.00384     +0.000830    0.000       Amps
        25    +5V Bus Cur:   -0.00763     +0.00394     0.000       Amps
        26    -X Array Cur:  -0.00140     +0.00210     0.000       Amps
        27    +X Array Cur:  +0.00946     +0.00226     0.000       Amps
        28    -Y Array Cur:  -0.01018     +0.00224     0.000       Amps
        29    +Y Array Cur:  -0.01168     +0.00239     0.000       Amps
        2A    -Z Array Cur:  -0.01516     +0.00237     0.000       Amps
        2B    +Z Array Cur:  -0.02111     +0.00239     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D    BCR Input Cur: -0.02189     +0.00332     0.000       Amps
        2E    BCR Output Cur:-0.03019     +0.00327     0.000       Amps
        2F    Bat 1 Temp:    +100.01      -0.5980      0.000       Deg. C
        30    Bat 2 Temp:    +100.01      -0.5980      0.000       Deg. C
        31    Baseplate Temp:+100.01      -0.5980      0.000       Deg. C
        32    PSK TX RF Out: +0.2104      -0.01203     +0.0001786  Watts
        33    RC PSK TX Out: +0.0340      -0.00969     +0.0002198  Watts
        34    PSK TX HPA Temp+100.01      -0.5980      0.000       Deg. C
        35    +Y Array Temp: +100.01      -0.5980      0.000       Deg. C
        36    RC PSK HPA Temp+100.01      -0.5980      0.000       Deg. C
        37    RC PSK BP Temp:+100.01      -0.5980      0.000       Deg. C
        38    +Z Array Temp: +0.0000      +1.0000      0.000       Counts 





























        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 76


        Table 7.4.5 LUSAT-OSCAR 19 Packet Telemetry Decoding Equations

        Spacecraft:  LUSAT-1:                             Rev: 1
                                                          Date: 1/7/90  

        Equations are in the form: Y = A*N^2 + B*N + C
                                   where: 
                                      N = Telemetry Count (00 - FF) 
                                      A, B, C = Equation Coefficients
                                      Y = Result (In Specified Units)

        HEX   Description:        C:           B:         A:       Units:        
                             cccccccccc   bbbbbbbbbb   aaaaaaaaaa  uuuuuu
                          
         0    Rx D DISC:     +9.802       -0.08779     0.000       kHz
         1    Rx D S meter:  +0.000       +1.000       0.000       Counts
         2    Rx C DISC:     +8.429       -0.09102     0.000       kHz
         3    Rx C S meter:  +0.000       +1.000       0.000       Counts
         4    Rx B DISC:     +9.291       -0.08317     0.000       kHz
         5    Rx B S meter:  +0.000       +1.000       0.000       Counts
         6    Rx A DISC:     +9.752       -0.08310     0.000       kHz
         7    Rx A S meter:  +0.000       +1.000       0.000       Counts
         8    Rx E/F DISC:   +10.110      -0.08610     0.000       kHz
         9    Rx E/F S meter:+0.000       +1.000       0.000       Counts
         A    +5 Volt Bus:   +0.000       +0.0305      0.000       Volts
         B    +5V Rx Current:+0.000       +0.000250    0.000       Amps
         C    +2.5V  VREF:   +0.000       +0.0108      0.000       Volts
         D    8.5V BUS:      +0.000       +0.0391      0.000       Volts
         E    IR Detector:   +0.000       +1.000       0.000       Counts
         F    LO Monitor I:  +0.000       +0.000037    0.000       Amps
        10    +10V Bus:      +0.000       +0.0508      0.000       Volts
        11    GASFET Bias I: +0.000       +0.000026    0.000       Amps
        12    Ground REF:    +0.000       +0.0100      0.000       Volts
        13    +Z Array V:    +0.000       +0.1023      0.000       Volts
        14    Rx Temp:       +93.24       -0.5609      0.000       Deg. C
        15    +X (RX) Temp:  +93.24       -0.5609      0.000       Deg. C
        16    Bat 1 V:       +1.7343      -0.0029740   0.000       Volts
        17    Bat 2 V:       +1.7512      -0.0032113   0.000       Volts
        18    Bat 3 V:       +1.7790      -0.0034038   0.000       Volts
        19    Bat 4 V:       +1.7286      -0.0030036   0.000       Volts
        1A    Bat 5 V:       +1.8114      -0.0036960   0.000       Volts
        1B    Bat 6 V:       +1.7547      -0.0032712   0.000       Volts
        1C    Bat 7 V:       +1.7151      -0.0030739   0.000       Volts
        1D    Bat 8 V:       +1.6846      -0.0028534   0.000       Volts
        1E    Array V:       +8.100       +0.06790     0.000       Volts
        1F    +5V Bus:       +2.035       +0.0312      0.000       Volts
        20    +8.5V Bus:     +5.614       +0.0184      0.000       Volts
        21    +10V Bus:      +7.650       +0.0250      0.000       Volts
        22    BCR Set Point: +3.7928      +1.0616      0.000       Counts
        23    BCR Load Cur:  -0.0244      +0.00628     0.000       Amps


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 77


        24    +8.5V Bus Cur: +0.00412     +0.000773    0.000       Amps
        25    +5V Bus Cur:   +0.02461     +0.00438     0.000       Amps
        26    +X Array Cur:  -0.01614     +0.00232     0.000       Amps
        27    -X Array Cur:  -0.01158     +0.00238     0.000       Amps
        28    -Y Array Cur:  +0.00278     +0.00206     0.000       Amps
        29    +Y Array Cur:  +0.00136     +0.00218     0.000       Amps
        2A    -Z Array Cur:  +0.00370     +0.00209     0.000       Amps
        2B    +Z Array Cur:  -0.00793     +0.00216     0.000       Amps
        2C    Ext Power Cur: -0.02000     +0.00250     0.000       Amps
        2D    BCR Input Cur: -0.00901     +0.00283     0.000       Amps
        2E    BCR Output Cur:+0.00663     +0.00344     0.000       Amps
        2F    Bat 1 Temp:    +93.24       -0.5609      0.000       Deg. C
        30    Bat 2 Temp:    +93.24       -0.5609      0.000       Deg. C
        31    Baseplt Temp:  +93.24       -0.5609      0.000       Deg. C
        32    PSK TX RF Out: +0.1059      +0.00095     +0.0000834  Watts
        33    RC PSK TX Out: +0.0178      +0.00135     +0.0000833  Watts
        34    PSK TX HPA Temp+93.24       -0.5609      0.000       Deg. C
        35    +Y Array Temp: +93.24       -0.5609      0.000       Deg. C
        36    RC PSK HPA Temp+93.24       -0.5609      0.000       Deg. C
        37    RC PSK BP Temp:+93.24       -0.5609      0.000       Deg. C
        38    +Z Array Temp: +93.24       -0.5609      0.000       Deg. C 
        39    LU Bcn Temp A: +93.24       -0.5609      0.000    *  Deg. C
        3A    LU Bcn Temp D: +93.24       -0.5609      0.000    ** Deg. C
        3B    Coax Rly Stat: +0.000       +1.0000      0.000       Counts
        3C    Coax Rly Stat: +0.000       +1.0000      0.000       Counts  

          * Note 1:  Thermistor located near box center adjacent to LU
                     thermistor channel no. 5.  

        **  Note  2:   Thermistor  located  near -X face of  box  on  the 
                       experiment baseplate.

        LUSAT-OSCAR  19 also transmits 8 channels of CW telemetry, at  12 
        W.P.M.  with  reduced morse code (to save about 44%  power).  The 
        format of the telemetry is:

        E LUSAT HI HI NL 111 222 333 444 555 666 777 888

        where:
             E is a calibration point to measure the output power.

             NL:N is the EPROM version number. There are 7 copies of  the 
             program in the EPROM, to prevent crashes or hang ups due  to 
             degradation  effects.  The on board  computer  automatically 
             loads  a  valid version, and N indicates which  version  was 
             loaded.

             L  is the result of an internal RAM memory test by the  6805 
             microprocessor.   If L=0, the RAM is "OK". If L=E, an  Error 
             was detected.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 78



        The  telemetry decoding equations for the LUSAT-OSCAR 19  CW  are 
        shown in Table 7.4.6.

        Table 7.4.6 LUSAT-OSCAR 19 CW Telemetry Decoding Equations

        CH# 1 = N1 +5 Reg Volts  :     636/N1         (Volts)
        CH# 2 = N2 +10 Volts Battery   0.064*N2       (Volts
        CH# 3 = N3 CW TX Temperature   0.354(134.7-N3) (Deg. C)
        CH# 4 = N4 CW TX Power Output  (10.9+N)^2/40.1 (Watts)
        CH# 5 = N5 Temp. BOX No. 4     0.356(136-N5)  (Deg. C)
        CH# 6 = N6 +10 V Current       0.7*N6         (mAmps.)
        CH# 7 = N7 Panel +Z Volts      0.15*N7        (Volts)
        CH# 8 = N8 Reg. +8.5 Volts     0.056*N8       (Volts)

        A typical example of a CW telemetry frame is shown below.

        E LUSAT HI HI 1O 128 167 042 162 040 148 045 156

        decoding it, We have: E LUSAT HI HI 

        NL = 1O :  N=1 (first version) ; L=O (Memory 6805 RAM  "OK")

        N1=128: 636/128          = + 4.97  V. REG.
        N2=167: 0.064*167        = +10.69  V. BATTERY
        N3=042: 0.354(134.7-042) =  32.81  Deg. C
        N4=162: (10.9+162)^2/40.1= 745.5   mW.
        N5=040: 0.356(136-040)   =  34.17  Deg. C
        N6=148: 0.7*148          = 103.6   mA. (over 10 V)
        N7=045: 0.15*045         = + 6.75  V. +Z
        N8=156: 0.056*156        = + 8.736 V. REG.

        NOTE: the reduced cw code is USED ONLY for the numeric data,  and 
        AFTER the "HI HI" as in the following example.

         L     U     S     A      T       H    I     H   I      1   O

        1: .-      (A)       6: -....  (6)
        2: ..-     (U)       7: -...   (B)
        3: ...-    (V)       8: -..    (D)
        4: ....-   (4)       9: -.     (N)
        5: .       (E)       0: -      (T)

        7.5 Fuji-OSCAR 20

        Fuji-OSCAR  20  which  was  launched on February  7,  1990  is  a 
        communications   satellite   in   low   earth   orbit   providing 
        simultaneous analog and digital communications capability.  Fuji-
        OSCAR  20 was built in Japan for Japanese radio amateurs  and  is 
        the second Japanese built OSCAR.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 79


         
        On  February  7 1990, the National Space  Development  Agency  of 
        Japan (NASDA) put the Marine Observation Satellite (MOS) 1b  into 
        orbit.  The launch vehicle also carried two secondary   payloads, 
        Fuji-OSCAR 20 and the Deployable Boom and Umbrella Test   (DEBUT) 
        spacecraft which is similar in shape and weight to Fuji-OSCAR 20. 
         
        MOS-1b  was  placed into a circular polar orbit, then  DEBUT  and 
        Fuji-OSCAR 20 separated from the launch vehicle at  0233,   above 
        Santiago, Chile. First signals from the spacecraft were  received 
        in Tokyo around 0309 UTC. 

        Fuji-OSCAR  20  is similar in construction to Fuji-OSCAR  12.  In 
        fact, much of it was originally constructed as a backup to  Fuji-
        OSCAR 12 and designated as JAS-1B. It has since been modified and 
        improved as a result of the lessons learned during the flight  of  
        Fuji-OSCAR  12.  Fuji-OSCAR 12 was known as Fuji-1 in  Japan,  so 
        this  spacecraft is known by the Japanese as Fuji-2 and as  Fuji-
        OSCAR 20 by the rest of the world.  

        Fuji-OSCAR 20's  planned service life is 5 years.  It  is  in   a 
        sunsynchronous elliptical polar orbit, having a perigee of  about 
        900  km  and  an apogee of about 1740 at  an  inclination  of  99 
        degrees.  The  Period of the orbit is about  105  minutes.   This 
        orbit  is  optimal  for MOS-1b which is  to  study  oceanographic 
        resources and observe agricultural environmental conditions.   In 
        this  orbit, the spacecraft passes over a given line of  latitude 
        at  approximately  the same time each day.  In  this  orbit,  the 
        spacecraft is shielded from the sun by the earth for about 33% of 
        the  time.  This  eclipse means that the  solar  cells  can  only 
        provide power for about 70 minutes in each orbit and that the on-
        board  nickel  cadmium  storage  batteries  have  to  power   the 
        spacecraft for the remaining 35 minutes.

        Fuji-OSCAR 20  weighs about 50 kg. and is  a  polyhedron   shaped 
        spacecraft  440mm  in  diameter and 470mm in  height  covered  by 
        approximately  1500  gallium arsenide solar cells  which  provide 
        about  11  Watts of power to keep the 11  series-connected  NiCad 
        cells  (rectangular) with a capacity of 6 AH charged.  There  are 
        26  sides to the polyhedron which almost makes it  spherical  for 
        all  practical  purposes other than sticking solar cells  to  it. 
        Fuji-OSCAR  12  was  the same shape but only  carried  about  600 
        cells.  This larger number of cells means that Fuji-OSCAR 20  has 
        a positive power budget and should not need to be switched off to 
        recharge. 

        The  Power  supply converts the raw bus voltage of +11 to  +18  V 
        (+14 V average) to the three regulated voltages (+10 V, +5 V,  -5 
        V)  used by the rest of the satellite with an efficiency  greater 
        than 70%.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 80



        The  attitude of the satellite is maintained by using the  torque 
        generated  by the interaction of two permanent magnets  with  the 
        earth's  magnetic field. This is a fairly conventional  technique 
        used  in the OSCAR series. Temperature stability is  achieved  by 
        using thermal insulation.

        Fuji-OSCAR 20 carries two Mode J transponders, both of which  may 
        be operational at the same time.  One transponder is analog (Mode 
        JA), the other is digital (Mode JD).

        The  frequencies and capabilities of the analog  transponder  are 
        similar  to those of Fuji-OSCAR 12.  It consists of  an  inverted 
        heterodyne   linear   translator   with  a   passband   100   kHz  
        wide, operating  with a mode J Uplink passband of 145.9 to 146.00  
        MHz, and a corresponding Downlink Passband of 435.9 to 435.8 MHz.  
        The spacecraft  has a Transmitter Output of approximately 1 watt.   
        A  ground  station  needs  an  Uplink EIRP  of  about  100  W  to 
        communicate through  the  transponder.  The JA telemetry   beacon  
        is  on  the nominal frequency of 435.795 MHz with a power  output 
        of about 100 mW and can use CW or PSK modulation.  Fuji-OSCAR  20 
        is using  the callsign  8J1JBS and the beacons transmit telemetry 
        in  the  same manner as Fuji-OSCAR 12.   

        The   digital  transponder  provides   store-and-forward   packet 
        communication  using  AX.25  link  level  protocol,  version   2. 
        Stations   who  used Fuji-OSCAR 12 are able to use Fuji-OSCAR  20 
        without making any modifications to their equipment.  The  uplink 
        requires Bi-phased Manchester code on an FM signal, at a bit rate 
        of   1200  bps. There are four Uplink  Frequencies:  145.85  MHz,  
        145.87 MHz, 145.89 MHz, 145.91 MHz.  The necessary ground station 
        Uplink  EIRP is also about 100 W.  The transponder has an  output 
        power of about 1 W on a downlink frequency of 435.91 MHz and uses 
        NRZI PSK at 1200 bps. The same PSK modem used to copy  Fuji-OSCAR 
        12  or  the  Microsats is needed to  copy  Fuji-OSCAR  20.    The  
        downlink channel also carries packet telemetry.

        The 144 MHz receiving antenna is a ring turnstile mounted at  the 
        bottom of the side panels. The 435 MHz transmitting antenna is  a 
        turnstile antenna mounted at the top of satellite.  Both antennas 
        are  circularly  polarized.   Ground tests have  shown  that  the 
        transmitting  antenna is more omnidirectional than that of  Fuji-
        OSCAR 12, however due to the structure of the  hybrid   circuitry 
        which  allow  both transponders to share the  same  antenna,  the 
        sense  of the circular polarization on the downlink is  different 
        for  each  mode.   As  the  apparent  polarization  is  different 
        depending  on  the  geometry  between  the  spacecraft  and   the 
        groundstation, you will probably have to change between left hand 
        and   right  hand  circular  polarization  during  a  pass.   The 
        spacecraft  is designed so that you can usually keep  the  uplink 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 81


        and downlink polarization the same.

        Mode  JA has provided strong transatlantic signals and  many   CW 
        and  SSB QSOs. Mode-JD was switched on for the first time  during 
        Orbit #95.  To Digipeat via Fuji-OSCAR 20 you don't need to use a 
        digipeater  call.  With the present version of the software,  all 
        AX.25  frames  with a valid CRC heard by the spacecraft  will  be 
        digipeated.

        The  spacecraft also carries a BBS which is accessed by means  of 
        the same commands used to access a terrestrial WA7MBL/W0RLI/AA4RE 
        type  of BBS.  You access the BBS by connecting to 8J1JBS on  any 
        of the four uplink channels. When you do connect to it, make sure 
        that you disconnect before LOS because Fuji-OSCAR 20 only  allows 
        16  simultaneous connections. Stations that hang in  there  after 
        the  satellite  drops below their local horizon block  access  by 
        other  stations  and  have been  christened  'Zombies'.  The  BBS 
        program  is  a modified version of the BBS  program  written  for 
        Fuji-OSCAR 12 and allows the use of 4 banks (1Mbyte) of memory. A 
        typical list of messages copied by KI6QE is shown in Figure  7.5-
        1.

        Figure 7.5-1 Typical Message Listing from the BBS
                        (copied by KI6QE)

        Fuji-OSCAR 20/JAS1b Mailbox ver. 2.00  
        commands [B/F/H/M/R/U/W]
        Use H command for Help
        JAS>JAS>NO.  DATE   UTC    FROM    TO      SUBJECT
        0086 04/13 05:15  WB6GFJ  W6SHP   Welcome
        0085 04/13 05:14  WB6LLO  KI6QE   SOFTWARE
        0084 04/13 05:14  WB6GFJ  W9FMW   Our Chat
        0082 04/13 03:38  W9FMW   WA4EJR  MESSAGE ON CIS
        0080 04/13 03:36  KG6EX   N1GCR   From Ashley
        0078 04/13 03:32  KG6EX   KD8SI   From Ashley
        0077 04/13 03:31  KG6EX   N8AM    From Ashley
        0076 04/13 03:30  KG6EX   DD4YR   From Ashley
        0075 04/13 03:27  KG6EX   DL1CR   From Ashley
        0074 04/13 03:25  KG6EX   G3RUH   From Ashley
        ---------------------------------------------------------

        The  spacecraft telemetry is transmitted either as CW or as  PSK. 
        The  CW  telemetry monitors 12 analog data points and  33  status 
        points, the PSK telemetry monitors 29 analog data points and   33 
        status points.  Telemetry data from Fuji-OSCAR 20 is  transmitted 
        on both the mode JA  and JD beacons. Mode JA sends data by  Morse 
        code  on the beacon signal of  435.795  MHz, repeating one  frame 
        every  one  minute.  Mode  JD sends a telemetry  packet  every  2 
        seconds on the digital  downlink channel of 435.91  MHz when  the 
        telemetry  mode is operating, otherwise, one frame is  downlinked 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 82


        every one minute. The spacecraft  can downlink up to 30 items  of 
        data  and  31  items  of status in the telemetry.   The  Mode  JA 
        beacon  however only carries 12 data elements and most of  status 
        bytes. 
         
        Mode JA Telemetry Data 
         
        The  Mode  JA beacon transmits the telemetry data in  the  format  
        shown below. These data are sent by Morse code with a "HI HI"  at 
        the  beginning  of  each  frame,  with  a  speed  of  about   100 
        characters every minute,  and always in this format repeatedly.  

         HI  HI  1A  1B  1C  1D 
                 2A  2B  2C  2D 
                 3A  3B  3C  3D 
                 4A  4B  4C  4D 
                 5A  5B  5C  5D 
         
        The  number  identifies the group, the letters A  through  D  are 
        decimal values expressed in two digits. Let this two-digit be  N, 
        for  each item, true value or engineering  value is  obtained  by 
        decoding  N as shown below.  For example, a value of 123  for  1A 
        means   group 1 and 23 is the measured value of the  solar  array  
        current.   Groups  4 and 5 contain status information  about  the 
        bird,   where  A,  B,  C  and  D  represent    octal    two-digit 
        combinations of 00 through 37. This corresponds to a  combination 
        of five binary  digits. Each bit shows status of each  designated 
        item  in the order from MSB (Most Significant Bit) to LSB  (Least 
        Significant  Bit).   The decoding equations for the  CW  Mode  JA 
        telemetry are shown in Figure 7.5.2.

        Figure 7.5-2 Fuji-OSCAR 20 Mode JA Telemetry Conversion Equations 
         
        CH  DESCRIPTION                       CALIBRATION   UNITS

        1A  total solar array current          19x(N+0.4)   mA 
        1B  battery charge/discharge current  -38x(N-50)    mA 
        1C  battery voltage                   (N+4)x0.22    V 
        1D  center tap voltage of battery     (N+4)x0.1     V 
        2A  bus voltage                       (N+4)x0.2     V 
        2B  +5 V regulator voltage            (N+4)x0.062   V 
        2C  JTA output power                  2.0x(N+4)^1.618mW 
        2D  calibration voltage               (N+4)/50      V 
        3A  battery temperature               1.4x(67-N)  deg. C 
        3B  baseplate temperature #1          1.4x(67-N)  deg. C 
        3C  baseplate temperature #2          1.4x(67-N)  deg. C 
        3D  baseplate temperature #3          1.4x(67-N)  deg. C 

        The   status  byte conversions are shown in Figure  7.5-3.   This 
        method  is used because all items whose status is represented  in 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 83


        this  manner  only  have  two possible situations, either  ON  or 
        OFF, or  binary values 0 or 1. For example, if the first item  of 
        status 4A  were 423, the 4 identifies group 4, and the 23  should 
        be  thought   of as its equivalent binary   code  (10011).   This 
        shows the status in the  order of MSB to LSB, or bit 4 to bit  0. 
        Using  the  decoding data 423 can be decoded as follows.

        1: Beacon is PSK, 
        0: Engineering data #2 is blank, 
        0: Engineering  data  #1 is blank, 
        1: JTD power is ON, 
        1: JTA power is ON.  


        Figure 7.5-3 Fuji-OSCAR 20 Mode JA System Status Bytes
         
        CH BIT  DESCRIPTION     STATE  
                                1     0 

        4A  0   JTA power       ON    OFF 
        4A  1   JTD power       ON    OFF 
        4A  2   Eng. data #1    ---   --- 
        4A  3   Eng. data #3    ---   --- 
        4A  4   Beacon          PSK   CW 
         
        4B  0   UVC             ON    OFF 
        4B  1   UVC level       1     2 
        4B  2   Battery         tric  full 
        4B  3   Battery logic   tric  full 
        4B  4   Main relay      ON    OFF 
         
        4C  0   PCU             bit 1 (LSB) 
        4C  1   PCU             bit 2 (LSB) 
        4C  2   PCU             manual  auto 
        4C  3   Eng. data #3    ---   --- 
        4C  4   Eng. data #4    ---   --- 
         
        4D  0   Memory bank #0  ON    OFF 
        4D  1   Memory bank #1  ON    OFF 
        4D  2   Memory bank #2  ON    OFF 
        4D  3   Memory bank #3  ON    OFF 
        4D  4   Computer power  ON    OFF 
         
        5A  0   Memory select   bit 1 (LSB) 
        5A  1   Memory select   bit 2 (MSB) 
        5A  2   Eng. data #5    ---   --- 
        5A  3   Eng. data #6    ---   --- 
        5A  4   Eng. data #7    ---   --- 
        5B  0   Solar panel #1  lit   dark 
        5B  1   Solar panel #2  lit   dark 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 84


        5B  2   Solar panel #3  lit   dark 
        5B  3   Solar panel #4  lit   dark 
        5B  4   Solar panel #5  lit   dark 
         
        5C  0   JTA CW beacon   CPU   TLM 
        5C  1   Eng. data #8    ---   --- 
        5C  2   Eng. data #9    ---   --- 
        5C  3   Eng. data #10   ---   --- 
        5C  4   Eng. data #11   ---   --- 
         
        5D  0   Eng. data #12   ---   --- 
        5D  1   Eng. data #13   ---   --- 
        5D  2   Eng. data #14   ---   --- 
        5D  3   Eng. data #15   ---   --- 
        5D  4   Eng. data #16   ---   --- 
         
        Telemetry  data  are downlinked on Mode JD by means  of  packets. 
        These data are transmitted the ASCII format shown in Figure  7.5-
        4.   In  the  ASCII telemetry  (RA and RB) XXX   is  a  3   digit 
        decimal   number  with a range between 000 to 999.  This   number 
        represents  the value of N in Table 5 for channels denoted #00  - 
        #26.

        Figure  7.5-5 contains the equations for converting the  received  
        data  into   engineering   values.   The  YYY  bytes  are   three  
        hexadecimal  bytes  of  system  status data, denoted #27a -  #29c  
        and can be decoded as shown in Figure 7.5-6. The SSS byte in  the 
        last  row  are binary  status data, denoted #30a - #39c.   Figure 
        7.5-7 provides  the information needed to decode them in a manner 
        similar to the Mode JA status points shown in Figure 7.5-3.

        Figure 7.5-4.  Fuji-OSCAR 20 Mode JD PSK telemetry data format
         
         JAS-1b FF YY/MM/DD HH:MM:SS 
         XXX XXX XXX XXX XXX XXX XXX XXX XXX XXX 
         XXX XXX XXX XXX XXX XXX XXX XXX XXX XXX 
         XXX XXX XXX XXX XXX XXX XXX YYY YYY YYY 
         SSS SSS SSS SSS SSS SSS SSS SSS SSS SSS 
         
        where,   FF  is  the  Frame Identifier,  which  may  contain  the 
        following types:
                                            
         RA: Realtime telemetry, - ASCII    
         RB: Realtime telemetry, - Binary   
         SA: Stored telemetry, - ASCII      
         SB: Stored telemetry, - Binary     
         M0: Message #0                     
         M1: Message #1                     
           ...........                      
         M9: Message #9                     


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 85


         
        YY/MM/DD is year/month/day, and HH:MM:SS is hour/minute/second, 
        all in UTC. 

        Figure 7.5-5.  Fuji-OSCAR 20 Mode JD Telemetry Decoding Equations 
         
        CH   DESCRIPTION                  CALIBRATION/UNITS

        #00  total solar array current     1.91x(N-4)mA 
        #01  battery charge/discharge     -3.81x(N-508)mA 
        #02  battery voltage              Nx0.022V 
        #03  battery center voltage       Nx0.009961V 
        #04  bus voltage                  Nx0.02021 V 
        #05  +5 V regulator voltage       Nx0.00620 V 
        #06  -5 V regulator voltage      -Nx0.00620 V 
        #07  + 10 V regulator voltage     Nx0.0126  V 
        #08  JTA output power             5.1x(N-158)mW 
        #09  JTD output power             5.4x(N-116)mW 
        #10  calibration voltage #2       N/500 V 
        #11  offset voltage #1            N/500 V 
        #12  battery temperature          0.139x(669-N)deg. C
        #13  JTD temperature              0.139x(669-N)deg. C
        #14  Baseplate Temperature #1     0.139x(669-N)deg. C
        #15  Baseplate Temperature #2     0.139x(669-N)deg. C
        #16  Baseplate Temperature #3     0.139x(669-N)deg. C
        #17  Baseplate Temperature #4     0.139x(669-N)deg. C
        #18  temperature calibration #1   N/500 V 
        #19  offset voltage #2            N/500 V 
        #20  Solar Cell Panel Temp   #1   0.38x(N-685)deg. C 
        #21  Solar Cell Panel Temp   #2   0.38x(N-643) 
        #22  Solar Cell Panel Temp   #3   0.38x(N-646) 
        #23  Solar Cell Panel Temp   #4   0.38x(N-647) 
        #24  ------------------------- 
        #25  temperature calibration #2   N/500 V 
        #26  temperature calibration #3   N/500 V 
        ---------------------------------------------------------

        Figure 7.5-6.  Fuji-OSCAR 20 Mode JD HEX System Status Bytes
         
        CH   DESCRIPTION
        #27a  Spare (TBD) 
        #27b  Spare (TBD) 
        #27c  Spare (TBD) 
        #28a  Spare (TBD) 
        #28b  Spare (TBD) 
         
        #28c  error count of memory unit #0 
        #29a  error count of memory unit #1 
        #29b  error count of memory unit #2 
        #29c  error count of memory unit #3 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 86


         
        Figure 7.5-7.  Fuji-OSCAR 20 Mode JD BINARY System Status Bytes.
         
        CH    DESCRIPTION             STATE
                                    1      0 

        #30a  JTA power             on     off 
        #30b  JTD power             on     off 
        #30c  JTA beacon            PSK    CW 
        #31a  UVC status            on     off 
        #31b  UVC level             1      2 
        #31c  main relay            on     off 
        #32a  engineering data #1     ----- 
        #32b  battery status        tric   full
        #32c  battery logic         tric   full
        #33a  engineering data #2     ----- 
        #33b  PCU status            bit 1 (LSB)
        #33c  PCU status            bit 2 (MSB)
        #34a  memory unit  #0       on    off 
        #34b  memory unit  #1       on    off 
        #34c  memory unit  #2       on    off 
        #35a  memory unit           on     off 
        #35b  memory select         bit 1 (LSB)
        #35c  memory select         bit 2 (MSB)
        #36a  engineering data #3     ------ 
        #36b  engineering data #4     ------ 
        #36c  computer power        on    off 
        #37a  engineering data #5     ------ 
        #37b  solar panel #1        lit  dark 
        #37c  solar panel #2        lit  dark 
        #38a  solar panel #3        lit  dark 
        #38b  solar panel #4        lit  dark 
        #38c  solar panel #5        lit  dark 
        #39a  engineering data #6     ------ 
        #39b  CW beacon source      CPU   TLM 
        #39c  engineering data #7     ------ 
         

        A typical set of raw PSK telemetry packets are those captured  by 
        KI6QE  and shown in Figure 7.5-8.  A typical decoded and  display 
        page  from WHATS-UP is shown in Figure 7.5-9 for a different  set 
        of raw data.










        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 87


        Figure 7.5-8 Fuji-OSCAR 20 PSK telemetry (as copied by KI6QE)

                      03-Apr-90  17:40:32  8J1JBS*>BEACON:
                      JAS1b RA 90/04/03 17:45:18
                      554 433 700 686 757 837 841 823 398 666
                      617 001 503 516 526 523 526 523 654 000
                      683 675 685 684 999 643 875 316 002 000
                      110 111 000 000 100 000 001 011 111 000

                      03-Apr-90  17:40:34  8J1JBS*>BEACON:
                      JAS1b RA 90/04/03 17:45:20
                      566 427 699 705 746 837 841 824 541 659
                      617 001 503 516 526 523 526 523 654 000
                      683 675 686 683 999 642 874 316 002 000
                      110 111 000 000 100 000 001 011 111 000

         
        Figure  7.5-9 Sample Decoded Display (General Housekeeping)  Page            
        from Fuji-OSCAR 20.

                                JAS1b RA 91/01/13 00:40:58

        Solar Panel Temp #1:  15.20 Deg.C Total Array Current:1105.89 mA
        Solar Panel Temp #2:  31.92 Deg.C Battery Charge     : 102.87 mA
        Solar Panel Temp #3:  32.68 Deg.C Battery Voltage    : 14.806 V
        Solar Panel Temp #4:  29.64 Deg.C Battery Center     :  6.744 V
        Baseplate Temp. #1 :  40.73 Deg.C Bus Voltage        : 17.259 V
        Baseplate Temp. #2 :  41.42 Deg.C   +5 V Regulator   :  5.214 V
        Baseplate Temp. #3 :  40.87 Deg.C   -5 V Regulator   :  0.000 V
        Baseplate Temp. #4 :  41.14 Deg.C  +10 V Regulator   : 10.471 V
        Temperature Cal. #1:   1.30 V     Offset Voltage #1  :  0.000 V
        Temperature Cal. #2:   1.29 V     Offset Voltage #2  :  0.000 V
        Temperature Cal. #3:   1.75 V     Calibration Volt #2:  1.230 V
        Battery Temp.      :  45.04 Deg.C JTA TX Output Power:   0.46 W
        JTD Temperature    :  42.12 Deg.C JTD TX Output Power:   3.52 W

        7.6 AMSAT-OSCAR 21 (RM-1) 

        AMSAT-OSCAR  21  (AO-21) was launched in  February  January  1991 
        from  the North Cosmodrome at Plesetsk.  The orbit is a  slightly 
        elliptical  polar  orbit  with  an  apogee  of  1000  km  at   an 
        inclination  of 83 degrees. The period of the orbit will  be  105 
        minutes.
             
        AMSAT-OSCAR  21 is the first international OSCAR in  which  radio 
        amateurs from the Soviet Union took part.  RM1 stands for  "RADIO 
        M-1",  which  is the official prelaunch name of  AMSAT-OSCAR  21, 
        emphasizes  that  the  spacecraft was built by,  and  for,  Radio 
        Amateurs around the world.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 88


        The  idea  of a joint effort between the two groups, one  in  the 
        USSR  and  the second, in Germany first appeared  in  the  spring 
        1989.  The discussions about what and how things had to  be  done 
        lasted till the meeting of the representatives of the two  groups 
        in  Surrey in July 1989 when the preliminary agreement about  the 
        cooperation  was  signed. The final version  of  the  cooperation 
        agreement  was later signed in the autumn of 1989 after  much  of 
        the work had been completed.

        According  to the mutual agreement, Amsat-U-Orbita developed  and 
        made  the  linear  transponder,  command  radio  link,  telemetry 
        system, power supply system and decided all the problems with the 
        official and other government organizations about the location of 
        the equipment and launching.

        The RUDAK group of AMSAT-DL developed and built the digital part, 
        called RUDAK-2 which contains a digipeater and an AX.25  mailbox. 
        It   also  provides  other  possibilities  for   experiments   in 
        transmitting  of  information using modern digital  methods.   It 
        also contains its own RF input and output circuits.  

        The  ground command station was developed by  the  Amsat-U-Orbita 
        and Amsat-U-Sputnik groups. The Rudak group however provided some 
        special digital part for it.

        During  the  launch and orbital test period ground,  the  command 
        stations  will  be  UC1CWA situated in Molodechno  and  RK3KP  in 
        Moscow.  The  ground command stations for Rudak-2  only  will  be 
        situated  near Munich at DK1YQ and near Hanover, at  DB2OS.   The 
        final  agreement  was signed on behalf of Amsat-U-Orbita  by  the 
        technical director of project "RADIO-M1" - V.Chepyzhenko,  RC2CA; 
        and on behalf of AMSAT-DL, by their president, K. Meinzer, DJ4ZC.  
        The  Project Manager for the RUDAK-2 is Hanspeter Kuhlen,  DK1YQ. 
        The  coordinators  for  the project are  P.  Guelzow,  DB2OS  and 
        L. Labutin, UA3CR.

        AMSAT-OSCAR  21  is an attached  secondary  payload  (Piggy-back) 
        aboard a USSR geological research satellite which provides a Mode 
        B  communications  transponder in low earth orbit as well  as  an 
        orbiting experimental digital communications capacity.
                          
        The AMSAT-OSCAR 21 Specifications are as listed below. 

             Dimension  and shape: Cylinder of height about 4 meters  and 
             diameter 1.8 meters
                  
             System   configuration:  Professional  geological   research 
             equipment,   telemetry  system,  command   link   equipment, 
             transponders  and  power supply,  thermal  control.  Amateur 
             linear  and digital transponders, telemetry system,  command 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 89


             link equipment, power supply.
                  
             Attitude  control:  Satellite attitude  will  be  maintained 
             using  a  gravity gradient approach in the form of a  rod  9 
             meters long pointing away from the earth.
                  
             Planned service life: 3 years.
                  
        Two  sets  of the equipment are installed aboard  the  satellite: 
        Linear  transponder  #1 is Mode B and contains  the  RUDAK-2  and 
        other  subsystems,  while  Linear  transponder  #2  mode  B  with 
        subsystems The Primary transponder is Linear Transponder #1,  the 
        second  one  is a spare which can be put into  operation  in  the 
        event  of  a failure of the primary system. Mode B in  low  earth 
        orbit  provides  a very good communications link  as  anyone  who 
        worked AMSAT-OSCAR 7 Mode B will testify.
             
        The Transponder RF Frequency Assignments and Beacon Data for  the 
        Primary  Payloads  are shown in Table 7-6.1, and  those  for  the 
        Backup  payload in Table 7.6-2.  The 1100 bps is not a  misprint, 
        it  is  real. Apparently this data rate is used by a  popular  PC 
        tape  cassette interface in the Soviet Union. Because this PC  is 
        simple  and  cheap for the Hams in the USSR,  the  AMSAT-U-Orbita 
        team  decided  to use it on this spacecraft, much  in  a  similar 
        manner to the use of reversed AFSK tones in UoSAT-OSCAR 11 due to 
        the  wide availability of a popular interface for those tones  in 
        the  United  Kingdom.  It is unclear as of the  time  of  writing 
        this,  if the telemetry is HDLC or some  proprietary  synchronous 
        PSK such as the 400 baud AMSAT-OSCAR 13 downlink. As such you may 
        not be able to copy this telemetry. 

        Table 7.6-1 Primary Payload 

        Beacons and telemetry #1

        CW telemetry 8 channels  145.822 MHz 0.2 Watts
        Digital telemetry        30 channels 145.952 MHz 0.4 Watts
                                 1100 bps,BPSK/FM, deviation 2kHz
        Digital telemetry 
        Rudak-2                  145.983 MHz 3.0 Watts
                                 BPSK 1200 bps AX.25 (like F-O 20) 
        Transponders #1
            
        Linear transponder:      inversely heterodyned translator
        Uplink passband          435.102 to 435.022 MHz
        Downlink passband        145.852 to 145.932 MHz
        Transmitter output max.  10 Watts
        Bandwith (3db)           80 kHz
        Uplink EIRP required about 100 Watts
             


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 90


        Digital transponder Rudak-2: digipeater and store&forward  packet 
        communication (AX.25), telecommunications experiment with digital 
        signal  processing  up to nearly 20 kHz, 1 MByte RAM  disc,  four 
        separate uplink channels.
                
        Uplink frequencies: 

             RX-1  435.016 MHz 1200bps,FSK,NRZIC/Biphase-M
             RX-2  435.155 MHz (AFC) 2400 bps,BPSK, Biphase-S
             RX-3a 435.193 MHz (AFC) 4800 bps,RSM
             RX-3b 435.193 MHz (AFC) 9600 bps,RSM
             RX-4  435.041 MHz (digital AFC) RX for RTX-DSP
                
        Downlink frequency: 145.983 MHz 3 Watts
                
        The downlink can be switched to the following operating modes:

        Mode 1: 1200 bps, BPSK, NRZI,(NRZ-S) (like FO-20)
        Mode 2: 400 bps, BPSK, Biphase-S (Like AO-13 beacon)
        Mode 3: 2400 bps, BPSK, Biphase-S
        Mode 4: 4800 bps, RSM, NRZIC (Biphase-M) (like 4800 bps uplink)
        Mode 5: 9600  bps,  RSM, NRZI (NRZ-S) +Scrambler (like  9600  bps 
                uplink)
        Mode 6: CW keying (only for special events)
        Mode 7: FSK  (F1 or F2B),e.g. RTTY, SSTV, FAX,  etc.(for  special 
                events)
        Mode 8: FM  modulated  by  D/A signals  from  DSP-RISC  processor 
                (speech) 

        Table 7.6-2 Secondary Payload

        Beacons and Telemetry #2 

        CW telemetry 8 channels          145.948 MHz 0.2 Watts
        Digital telemetry 30 channels    145.838 MHz 0.4 Watts 1100  bps, 
                BPSK/FM, deviation 2kHz
        Digital telemetry  30 channels   145.800 MHz 2.0 Watts 1100  bps 
                BPSK/FM, deviation 2kHz
             
        Transponder #2 
             
        Linear transponder:      inversely heterodyned translator
        Uplink passband          435.123 to 435.043 MHz
        Downlink frequencies     145.866 to 145.946 MHz
        Transmitter output max.  10 Watt max.
        Bandwith (3db)           80 kHz
        Uplink EIRP required about 100 Watts                

        The spacecraft uses two antennas.  The 435 MHz receiving  antenna 
        which  is shared by the analog and digital modes is a Helix  with 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 91


        up to +3 db gain using Right Hand circular Polarization.  The 145 
        MHz  transmitting antenna is a Half wave dipole.  AMSAT-OSCAR  21 
        draws  up  to 100 Watts from the main spacecraft's  power  supply 
        system.  The Primary RM-1 payload including the RUDAK draw up  to 
        47 Watts, the secondary payload draws up to 40 Watts. The Primary 
        AMSAT-OSCAR  21 payload including the RUDAK weighs  approximately 
        28  kg, the secondary payload weighs approximately 22  kg.   Both 
        payloads are about 480x400x300 mm^3. 

        The  CW telemetry started up as soon as the  combined  spacecraft 
        separated  from  the  launch  vehicle and  was  powered  by  main 
        satellite power system. A CW Morse-Code telemetry frame  consists 
        of  the call RS14 and 8 channels of four digits in the  following 
        format: 

              RS14 S0AB=S1AB=S2AB=S3AB=S4AB=S5AB=S6AB=S7AB 

        Channels 0 to 6 contain analog telemetry data. Channel 7 contains 
        engineering calibration parameters. 

        The  first  digit (S) identifies which system  the  telemetry  is 
        from.  A prefix of 7 identifies a general status, a prefix  of  5 
        identifies  a command status. The second digit (0 to 7)  are  the 
        numbers  of the line (channel).  The remaining digits (A  and  B) 
        are  the analog telemetry data which can be decoded according  to 
        the equations shown in Table 7.6-3.

        Table 7.6-3 AMSAT-OSCAR 21 CW Telemetry decoding parameters

        Channel        Parameter                Formula   Unit 

         0        Transponder power output      0.05*N    Watts
         1        Transponder PA Temperature    N         Deg. C
         2         +24 V Regulated              N         Volt
         3         +16 V Regulated              N         Volt
         4         +9  V Regulated              N         Volt
         5         +24 V Regulated              N         Volt
         6        Inside Temperature            N         Deg. C
         7        Engineering Value             N         * 


        A typical frame such as
        "RS14=7080=7137=7224=7316=7409=5524=5032=57PPRS14" may be decoded 
        as shown below.








        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 92


                 RS14
                 7080 - 4 Watts   - general
                 7137 - 37 Deg. C - general
                 7224 - 24 Volts  - general
                 7316 - 16 Volts  - general
                 7409 - 9 Volts   - general
                 5524 - 24 Volts  - command
                 5032 - 32 Deg. C - command
                 57PP             - command (transponder #1)

        Examples of other frames copied and edited by G3ZCZ/W3 are


        28-Feb-91 01:40 RS14=7032=7121=7224=7316=7410=7500=7600=77PP
        01-Mar-91 02:19 RS14=7028=7121=7224=7316=7410=7500=7600=77PP

        The  "PP"  at the end of the frame identifies  the  telemetry  as 
        having  come from transponder #1. Transponder #2  identifies  its 
        telemetry with the "PPPP" sequence.

        The  AMSAT-OSCAR 21 Digital telemetry consists of  30  parameters 
        monitoring  on-board  conditions and 2  calibration  verification 
        points. If you intend to receive, decode and display the  digital 
        telemetry you will need an FM receiver, a TNC, a PSK modem, and a 
        computer  or terminal.  Even then you may not be able  to  decode 
        the  data  since  it may not be downlinked in  HDLC  format.  The 
        decoding  equations for the digital telemetry are shown in  Table 
        7.6-4.  The raw digital telemetry is expected to show up on  your 
        screen in the format shown in Table 7.6-5.

        Table 7.6-4 Decoding   Equations  for  AMSAT-OSCAR   21   Digital 
                    Telemetry (Version 26-Dec-90) 
         
        Line Parameter                  Formula     Unit  Hex-Format-Line 

         1   "Zero" of the comparator      0C         N/A      0000
         2   Reference voltage             6D         N/A      0010
         3   Transponder #1 HF output pwr  0.2N^2    Watt      0020
         4   Transponder #1 PA temperature 0.8*N     Deg. C    0030
         5   DC/DC converter temperature   0.8*N     Deg. C    0040
         6   +14 V Regulated               10*N      Volt      0050
         7   +24 V Regulated               10*N      Volt      0060
         8   +16 V Regulated               10*N      Volt      0070
         9   +12 V Regulated               10*N      Volt      0080
         10  +9 V Regulated                10*N      Volt      0090
         11  +7.5 V Regulated              10*N      Volt      00A0
         12  +5 V Regulated                10*N      Volt      00B0
         13  +9 V Regulated (linear)       10*N      Volt      00C0
         14  +9 V Regulated (digital)      10*N      Volt      00D0
         15  Service                          N      *         00E0


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 93


         16  Service                          N      *         00F0
         17  Transponder #2 HF output pwr  0.2*N^2   Watt      0100
         18  Transponder #2 PA temperature 0.8*N     Deg. C    0110
         19  +24 V Regulated               10*N      Volt      0120
         20  +16 V Regulated               10*N      Volt      0130
         21  +10 V Regulated               10*N      Volt      0140
         22  +9 V Regulated                10*N      Volt      0150
         23  +7.5 V Regulated              10*N      Volt      0160
         24  Status command link           1         *         0170
         25  Status command link           2         *         0180
         26  Status command link                     *         0190
         27  Status command link                     *         01A0
         28  RPC +5V for Rudak-1           2.47*N    Volt      01B0
         29  RPC +5V for Rudak-RTX         2.47*N    Volt      01C0
         30  RPC +5V for Ramdisk           2.47*N    Volt      01D0
         31  RPC +14V total supply current 627-289*N mA        01E0
         32  RPC module temperature        56.7*N-49.5 Deg. C  01F0 

        Note:  RPC  - Rudak Power Conditioner.  The Service  and  command 
        link channels are reserved for use by the ground control team.


        Table 7.6-5 Expected Format of Raw AMSAT-OSCAR 21 PSK Telemetry

         0000 0C E6 0C E6 0C E6 0C E6 0C E6 0C E6 0C E6 0C E6
         0010 6D E6 6D E6 6D E6 6D E6 6D E6 6D E6 6D E6 6D E6
         0020 i E6 i E6 i E6 i E6 i E6 i E6 i E6 i E6
         .................................................... 
         01F0 j E6 j E6 j E6 j E6 j E6 j E6 j E6 j E6 
         
         i...j - the value of the parameter in the hex format, repeated 8 
        times  E6 - separation 

        The  RUDAK  system is a message  store-and-forward  package.  Its 
        downlink is not expected to contain any telemetry. An example  of 
        some RUDAK signals copied by W3/G3ZCZ a few days after launch  is 
        shown in Table 7.6-6.  















        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 94


        Table 7.6-6 Example of AMSAT-OSCAR 21 RUDAK Signals.

        26-Feb-91  02:31:36  RUDAK*>BEACON:
        * RUDAK-II / AMSAT OSCAR 21/RM1
        * Up: 435.016MHz (1200)
        *     435.155MHz (2400)
        * Mailbox=RUDAK Mheard=RUDAK-1
        26-Feb-91  02:32:37  RUDAK*>BEACON:
        RUDAK-Telemetry (91-02-25 23:03:00):
        Used stack entries: 0
        Uplink Carrier Detect (during last minute): 0%
        26-Feb-91  02:33:36  RUDAK*>BEACON:
        * RUDAK-II / AMSAT OSCAR 21/RM1
        * Up: 435.016MHz (1200)
        *     435.155MHz (2400)
        * Mailbox=RUDAK Mheard=RUDAK-1
        26-Feb-91  02:34:37  RUDAK*>BEACON:
        RUDAK-Telemetry (91-02-25 23:05:00):
        Used stack entries: 0
        Uplink Carrier Detect (during last minute): 0%
        26-Feb-91  02:35:09  RUDAK,*>WB5BZE (UA)
        26-Feb-91  02:35:11  RUDAK*>WB5BZE:
        +-------------------------------------------------------+
        +  Welcome to the RUDAK II Bulletin Board System V0.04  +
        +-----------
        26-Feb-91  02:35:13  RUDAK*>WB5BZE:
        --------------------------------------------+
        Logged in at 91-02-25 23:05:33,  1 User
        This is a preliminary release.
        Please rep
        26-Feb-91  02:35:15  RUDAK*>WB5BZE:
        ort deficiencies to DL2MDL.
        73 de AMSAT-UA/AMSAT-DL/RUDAK-Group.
        Enter H for help.
        WB5BZE de RUDAK>
        26-Feb-91  02:35:36  RUDAK*>BEACON:
        * RUDAK-II / AMSAT OSCAR 21/RM1
        * Up: 435.016MHz (1200)
        *     435.155MHz (2400)
        * Mailbox=RUDAK Mheard=RUDAK-1
        26-Feb-91  02:35:51  RUDAK*>WB5BZE [D]
        26-Feb-91  02:35:56  RUDAK*>WB5BZE [D]
        26-Feb-91  02:36:32  KF4WQ>RUDAK*>KF4WQ [C]
        26-Feb-91  02:36:37  RUDAK*>BEACON:
        RUDAK-Telemetry (91-02-25 23:07:00):
        Used stack entries: 0
        Uplink Carrier Detect (during last minute): 0%
        26-Feb-91  02:37:35  RUDAK*>WB5BZE (UA)




        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 95


        7.7 SARA-OSCAR 23

        On  17 July 1991, the attention of AMSAT and the rest of  world's 
        amateur  radio  satellite communicators was focused  on  UoSAT-F. 
        UoSAT-F  became UoSAT 5 when it separated from the  launcher  and 
        another  OSCAR carrying a packet amateur  communications  payload 
        was in ORBIT. The University of Surrey calls the spacecraft UO-5, 
        AMSAT and radio amateurs call it OSCAR 22 or UO-22. UO-5/UO-22 is 
        a scientific satellite similar to UO-4, launched in 1990.

        Hardly anyone noticed that the same Ariane launch vehicle carried 
        the  SARA spacecraft, which became OSCAR 23 a few  seconds  after 
        UoSAT-F  became  UoSAT-5.  SARA-OSCAR 23  (SO-23)  was  built  at 
        ESIEESPACE,   an   aerospace  club  at   the   Ecole   Superieure 
        d'Ingenieurs  en  Electrotechnique et  Electronique  (ESIEE),  in 
        France. SARA is the culmination of six years of development  work 
        which  included  building payloads for balloon  and  sub  orbital 
        rocket launches.

        SARA  is not an amateur radio communications satellite.  Although 
        not  as  complex,  it is also  an  educational  and  experimental 
        satellite  similar to the spacecraft built at the  University  of 
        Surrey  in England, (UO-1, UO-2, UO-3, UO-4 and UO-5).  It  holds 
        (and  identifies  using)  the callsign FX0SAT.  SARA  stands  for 
        "Satellite for Amateur Radio Astronomy". 

        Radio  astronomy  was  born in 1932 with the  discovery  by  Karl 
        Jansky  at  the Bell Telephone Laboratories in  New  Jersey  that 
        radio  waves  were coming from a source in the sky. SARA  is  not 
        amateur  radio's first connection with radio astronomy. In  1937, 
        Grote  Reber,  W9GFZ, designed and built the  world's  the  first 
        radio telescope, a 31ft. (9.4m) dish antenna, in his own backyard 
        in  Wheaton,  IL.  Using this antenna, he  discovered  the  first 
        discrete radio sources in the sky and mapped the distribution  of 
        radio emissions in the Milky Way. Grote Reber was the only person 
        doing research in Radio Astronomy before World War II and single-
        handedly brought radio astronomy to the attention of professional 
        astronomers.  Like  Grote Reber, SARA is also a  pioneer,  albeit 
        with a two fold mission.

        7.7.1 The Primary Mission: - a Radio Astronomy Experiment 

        SARA's primary mission is a Radio Astronomy Experiment to  listen 
        for hf radio signals from Jupiter's radio-electric activities  in 
        the decametric wavelengths. Jupiter is known to be emitting radio 
        noise  in  the  hf  frequency bands. This  Jovian  DX  cannot  be 
        investigated  by  a terrestrial station because for much  of  the 
        time,  either the Earth or its atmosphere blocks the signals.  In 
        the  past,  a  few  other satellites  have  measured  the  Jovian 
        emissions,  but not for a long enough period of time  to  achieve 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 96


        meaningful results.

        Jupiter's  radio  emissions in the decametric  band  is  powerful 
        enough  to  wipe out all other natural extra  terrestrial  signal 
        sources  under normal conditions. In the vicinity of  the  earth, 
        the  flux received from Jupiter ranges from 10.E-20 to  5.10.E-19 
        W.m^-2.Hz^-1 which is much stronger than the galactic  background 
        noise.  During the Sun's calm period, the flux received from  the 
        sun  is about 10.E-24 W.m^-2.Hz^-1. During periods of high  solar 
        activity   it  increases  to  10.E-17  W.m^-2.Hz^-1.  The   solar 
        eruptions  can be distinguished from the Jovian signals by  their 
        signal strength, length of time, and by correlation with  signals 
        received  on other wavelengths. Jupiter's radio activity  in  the 
        decametric  band is partially known: above 15 MHz the  ionosphere 
        sometimes  becomes transparent and makes it possible to  do  some 
        measurements,  which can then be extrapolated to the 2 to 15  MHz 
        band. 

        The  Jovian  decametric emission is irregular. It  occurs  mostly 
        during  storms that last from periods ranging from one minute  to 
        an hour. Depending on the type of storm, radio-electrical  energy 
        is  concentrated  into  peaks  of 1 to 50 mS or 1  to  10  S,  in 
        frequency  bands about 50 KHz wide sweeping across the  spectrum. 
        These  storms  are closely related to the rotation  of  Jupiter's 
        satellite  Io and to Jupiter's own rotation. Solar eruptions  may 
        also influence them. 

        Voyager 1 carried out reception tests in the vicinity of Jupiter, 
        but   because  of  electromagnetic  interference  from  its   own 
        instruments  in  the decametric band, it could  only  detect  the 
        strongest peaks of the Jovian emissions. To date, no measurements 
        have  yet  been made in the 2 to 15 MHz band during a  period  of 
        high solar activity. SARA is a pioneer following a voyager.

        The  radio-electrical waves are received by means of three  pairs 
        of   aerials   placed  perpendicularly  to   each   other.   This 
        configuration  allows computation of the intensity of  the  field 
        regardless of its direction and polarization.

        As  the  received electromagnetic field is  quite  strong,  three 
        pairs  of  short aerials, five meters long are used. One  of  the 
        pairs is also used to downlink telemetry data to earth in the 2 m 
        band.  The aerials are made of 100 mm wide steel tape. They  were 
        rolled up for the launch and unrolled themselves as soon as  they 
        were freed in orbit. 

        The  Jovian emissions between 2 and 15 MHz are measured on  eight 
        channels,  each  of  them 100 KHz wide. The  on  board  equipment 
        averages  their  amplitude  over a time interval of  150  S.  The 
        average  amplitude produces the envelope of the storms but  hides 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 97


        the peaks, which represent the internal structure of the  storms. 
        A  single receiver is switched between the channels  and  between 
        the three pairs of aerials. The receiver thus gets in  succession 
        the three polarizations of each of the eight channels. This cycle 
        is  executed  several  times  during the 150  S  to  prevent  the 
        measurements  on the different channels from being  separated  in 
        time. 

        The  receiver  has a 40 dB dynamic range in order to  detect  the 
        Jovian peaks as well as certain solar ones without saturating the 
        receiver.  This  allows  for enough  sensitivity  to  detect  the 
        galactic background noise which is constant at a known level, and 
        which will serve as a reference standard when Jupiter and the sun 
        are silent. 

        7.7.2 The Secondary Mission: - a Reliability Experiment. 

        Consider  the  reliability  of the  electronic  components  in  a 
        spacecraft.  SARA  uses  consumer-made  components,  rather  than 
        military  or  space  qualified parts, for  reasons  of  cost  and 
        availability.  Why  do  professional  satellites  use  the   most 
        expensive  components, and why did SARA do otherwise? The  launch 
        causes  vibrations amounting to 10 g. Once the payload gets  into 
        orbit,  outer  space is a favorable  environment  for  electronic 
        equipment.  As a result, SARA is made from components  that  have 
        been tested and burnt in.

        Commercial  mass  produced  components are just  as  reliable  as 
        conventional  space qualified parts. For instance, a TV set  that 
        can  work for 10 years or more without needing repairs has to  be 
        built  out  of very reliable components. While SARA  doesn't  use 
        hardened  components,  it doesn't use  risky  components  either. 
        Chemical capacitors are banished, the Power Amplifier transistors 
        are  oversized  and  well cooled, the PROMs  are  debugged  after 
        programming, as advised by the manufacturer. SARA's equipment  is 
        simple   and   conservatively   designed   and   that   is   why, 
        statistically, a long operational life can be anticipated for the 
        satellite. 

        7.7.3 The Downlink

        The  satellite circles the earth in 100 minutes on its  low,  sun 
        synchronous,  quasi-polar  orbit at an altitude of about  770  km 
        downlinking  its data continuously. One telemetry transfer  frame 
        cycle  takes 2 minutes 48 seconds. An uplink  command  capability 
        can shut the beacon down if it causes QRM. 

        The  downlink transmitter power of the satellite is about 1 W  at 
        145.955  MHz. The carrier wave is modulated in amplitude  with  a 
        +/- 3400 Hz spectrum using AFSK coding at frequencies of 1200 and 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 98


        2200  Hz  at a speed of 300 bits/s. The  aerial  polarization  is 
        linear. 

        7.7.4 The Onboard Electronics

        The  electronics  are  controlled by  a  sequencer  because  data 
        acquisition  and  transmission are made at  different  rates  and 
        times.  All the logic state machines required for the  experiment 
        are  built on a single printed circuit card, the remaining  cards 
        being analog or combinational logic. This approach simplified the 
        design of the equipment and testing.

        The  sequencing card manages the measurements: it  specifies  the 
        frequency  and  the pair of aerials to be used by  the  receiver, 
        digitizes and stores the data, interprets received commands,  and 
        prepares the telemetry. Data stored during a 24 hour time  period 
        is  time-tagged and downlinked in telemetry cycles lasting a  few 
        minutes.

        The functions described above are performed by a microcontroller. 
        As  the program must operate over a period of years in  spite  of 
        errors   that  could  occur  due  to  interference  or   ionizing 
        particles, it will be reset regularly.

        7.7.5 The Power System

        The power system supplies power to the electronics equipment, and 
        also  started the satellite up after the launch, having  detected 
        the separation from the launcher. After a proper time delay,  the 
        energy  system freed the aerials and started supplying  power  to 
        the  equipment.  The equipment needs about 3 W and  uses  a  non-
        regulated voltage bus that is locally regulated to 5 V.

        During  certain times of the year, the satellite is  eclipsed  by 
        the  earth for up to a third of each orbit. A storage battery  is 
        thus  used  as a permanent power supply. The battery  is  charged 
        when  sun  shines  on  the photovoltaic  cells.  The  battery  is 
        protected against overloading.

        Because  the satellite does not have an attitude control  system, 
        sunlight  can hit it from any direction. Solar cells were  placed 
        on each side of the space craft, which is in the form of a  cube. 
        Its size was calculated so that each side is able to supply power 
        for  the whole experiment. This means 60% of the surface  of  the 
        470 mm cube was covered with high quality cells.

        Separation  from the launcher was detected by a push button  that 
        directly controlled the power supply for the on-board  experiment 
        and the cutter to free the aerials. In addition, the power supply 
        is controlled by a security circuit.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 99



        7.7.6 Mechanical integration

        Integration is based on a single plate 400 mm by 400 mm, on which 
        everything  else  is  mounted;  the  electronic  equipment,   the 
        aerials, the solar cells, the interface with the launcher and the 
        manual controls.

        The  solar cells are placed on two half shells made  of  aluminum 
        sheets  that constitute the case when they are brought  together. 
        The integration plate is easily accessible when they are removed. 
        Each  piece  of  equipment  is a box.  The  cables  are  directly 
        connected  to  the  pieces they  connect.  The  whole  mechanical 
        structure  is made of aluminum pieces. The junctions  that  carry 
        strains  are  soldered. The spacecraft when assembled is  a  cube 
        measuring about 470 mm each side.

        7.7.7 Thermal Control 

        To  accomplish  their mission, the electronic equipment  and  the 
        batteries  need moderate temperatures. These temperatures can  be 
        achieved  using passive controls. The internal  temperature  only 
        depend  on  exterior  conditions  (Sun  and  Earth)  and  on  the 
        satellite's characteristics.

        The  target  temperature is an average of + 20 C,  which  can  be 
        achieved  by  choosing  appropriate  coatings  for  the  external 
        surfaces  of  the  satellite. About 40% of the  surface  was  not 
        covered  with solar cells and was thermally coated. The shape  of 
        the box was chosen so as to have a quasi-constant section in  all 
        directions,   temperature   being  then  independent   from   the 
        orientation  of the satellite relative to the sun. The  equipment 
        dissipates  3  W and does not modify the thermal balance  of  the 
        structure.

        The  heat must be able to pass easily from the lighted  sides  to 
        the  dark ones so that temperatures remain close to the  average. 
        The problem is simplified by the small size of the satellite, and 
        by  the  use of aluminum shells 2 mm thick which  are  enough  to 
        limit the thermal gap to 30 degrees. The satellite then does  not 
        need to be spun to maintain thermal control.

        7.7.8 Educational Opportunities

        SARA  provides  a  unique  educational  opportunity  in   orbital 
        dynamics. The radio signals SARA are monitoring are generated  by 
        the interaction between Jupiter and and one of its moons (Io)  as 
        a beam of radio energy. Why? How? The signals are synchronized to 
        sidereal time and appear roughly four minutes earlier  successive 
        day.  Why? It takes about two hours for the beam to swing  across 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 100


        the earth. Why? 

        Ideally  SARA  should have been placed in an orbit in  which  the 
        earth never gets between the spacecraft and Jupiter. SARA however 
        took the orbit the Ariane rocket gave it, an orbit optimized  for 
        the primary payload, the Earth Resources Satellite (ERA-1).  When 
        the  earth gets between SARA and Jupiter there will be breaks  in 
        reception of Jovian signals for up to 40 minutes each orbit. 

        Plot the current positions of Jupiter and the Earth in the  solar 
        system. Look at the angles between Jupiter and the orbital  plane 
        of SARA around the Earth. Does the Earth eclipse SARA? If so, how 
        long before the geometry is such that SARA will get uninterrupted 
        viewing  of Jupiter? If SARA has uninterrupted viewing, how  long 
        will  this  condition last? If SARA receives signals when  it  is 
        eclipsed  by the earth, what are they and where are  they  coming 
        from?

        Educators,  just answering these questions can  provide  material 
        for a semester or more. Additionally why not bring space into the 
        classroom. Set up a receiving station to acquire and capture  the 
        telemetry.  Send in a reception report for a QSL? Write  to  NASA 
        for some pictures of Jupiter.

        8.0 Spacecraft No Longer Active

        This  section  is provided for post mission analysis  of  digital 
        data from spacecraft that are  no longer active in case you  have 
        access  to  data from those satellites and wish to the  tools  in  
        WHATS-UP to view and analyze the data.

        8.1 Fuji-OSCAR 12 

        The  Fuji-OSCAR 12 PSK Telemetry Data Format. It  is  practically  
        identical  to the Fuji-OSCAR 20 format.  The format is  shown  in 
        Table  8.1-1, the decoding equations are presented in Table  8.1-
        2.

        Table 8.1-1 Fuji-OSCAR 12 PSK Telemetry Frame Format

        JAS-1 FF YY/MM/DD HH:MM:SS
        xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
        xxx xxx xxx xxx xxx xxx xxx xxx xxx xxx
        xxx xxx xxx xxx xxx xxx xxx xxx yyy yyy
        sss sss sss sss sss sss sss sss sss sss
         
        FF := Frame Identifier   RA: Realtime Telemetry - ASCII 
                                 RB: Realtime Telemetry - Binary 
                                 SA: Stored Telemetry - ASCII 
                                 SB: Stored Telemetry - Binary 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 101


                                 M0: Message #0
                                 M1: Message #1
                                 .......
                                 M9: Message #9

        YY/MM/DD  =  Date 

        HH:MM:SS  =  Time (The command station attempts to keep the clock 
                     as close as possible to UTC)
         
        [ Following is valid only for RA and SA frames ]
         
        xxx =  000 - 999  Format:  3  digit  decimal  (Analog  Data)   28  
                     samples  in  row 0 column 0 through row 2  column  7 
                     (denoted #00 - #27 below)
         
          y =  0 - F one byte Hex (System Status Data)
                     9 samples in row 2 column 8  through  row 2 column 9 
                     (denoted #28a - #29c below)
         
          s =  0 or 1  Binary Status Data
                       30 samples in row 3  through  row 3 column 9
                       (denoted #30a - #39c below) 

        Table 8.1-2 Fuji-OSCAR 12 Telemetry Calibration Equations  
         
        Ch.     Item                          Equation    Units

        #00     Total Solar Array Current     1.91 * ( N - 4 )    mA
        #01     Battery Charge/Discharge      3.81 * ( N - 528 )  mA
        #02     Battery Voltage               N * 0.0210    V
        #03     Half-Battery Voltage          N * 0.00937   V
        #04     Bus Voltage                   N * 0.0192    V
        #05     + 5 V. Regulator Voltage      N * 0.00572   V
        #06     - 5 V. Regulator Voltage      N * -0.00572  V
        #07     +10 V. Regulator Voltage      N * 0.0116    V 
        #08     JTA Power Output              5.1 * ( N  - 158 )  mW
        #09     JTD Power Output              5.4 * ( N - 116 )   mW
        #10     Calibration Voltage #2        N / 500  V
        #11     Offset Voltage #1             N / 500  V
        #12     Battery Temperature           0.139 * ( 689 - N )  Deg. C
        #13     JTD Temperature               0.139 * ( 689 - N )  Deg. C
        #14     Baseplate Temperature #1      0.139 * ( 689 - N )  Deg. C
        #15     Baseplate Temperature #2      0.139 * ( 689 - N )  Deg. C
        #16     Baseplate Temperature #3      0.139 * ( 689 - N )  Deg. C
        #17     Baseplate Temperature #4      0.139 * ( 689 - N )  Deg. C
        #18     Temperature Calibration #1    N / 500  V
        #19     Offset Voltage #2             N / 500  V
        #20     Facet Temperature #1          0.38 * ( N - 684 )  Deg. C 
        #21     Facet Temperature #2          0.38 * ( N - 684 )  Deg. C


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 102


        #22     Facet Temperature #3          0.38 * ( N - 690 )  Deg. C
        #23     Facet Temperature #4          0.38 * ( N - 683 )  Deg. C
        #24     Facet Temperature #5          0.38 * ( N - 689 )  Deg. C
        #25     Temperature Calibration #2    N / 500  V
        #26     Temperature Calibration #3    N / 500  V
        #27     Depth of Battery discharge    ( N - 500 ) / 189   AH
         
        Fuji-OSCAR 12 System Status Telemetry Bytes
         
        Ch.     Item
         
        #28a    Spare (TBD)
        #28b    Spare (TBD)
        #28c    Memory Unit #0 error count
         
        #29a    Memory Unit #1 error count
        #29b    Memory Unit #2 error count
        #29c    Memory Unit #3 error count

        Fuji-OSCAR 12 Binary Status Data Points 
         
        Ch.    Item                     1         0

        #30a   JTA Power                On        Off
        #30b   JTD Power                On        Off
        #30c   JTA Beacon               PSK       CW
         
        #31a   UVC Status               On        Off
        #31b   UVC Level                1         2
        #31c   Main Relay               On        Off
         
        #32a   Engineering Data #1      ----      ----
        #32b   Battery Status           Tric      Full
        #32c   Battery Logic            Tric      Full
         
        #33a   Engineering Data #2      ----      ----
        #33b   PCU Status                Bit 1 (LSB)
        #33c   PCU Status                Bit 2 (MSB)
         
        #34a   Memory Unit #0           On        Off
        #34b   Memory Unit #1           On        Off
        #34c   Memory Unit #2           On        Off
         
        #35a   Memory Unit #3           On        Off
        #35b   Memory Select             Bit 1 (LSB)
        #35c   Memory Select             Bit 2 (MSB)
         
        #36a   Engineering Data #3      ----      ----
        #36b   Engineering Data #4      ----      ----
        #36c   Computer Power           On        Off


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 103


         
        #37a   Engineering Data #5      ----      ----
        #37b   Solar panel #1           Lit       Dark
        #37c   Solar panel #2           Lit       Dark
         
        #38a   Solar panel #3           Lit       Dark
        #38b   Solar panel #4           Lit       Dark
        #38c   Solar panel #5           Lit       Dark
         
        #39a   Engineering Data #6      ----      ----
        #39b   CW beacon source         CPU       TLM
        #39c   Engineering Data #7      ----      ----
         
        9.0  File formats

        This section contains details of the contents of the different 
        files used by WHATS-UP.

             9.1 Configuration File

             The contents of the Configuration file (WHATS-UP.SYS) are as 
             follows:

             1    Your callsign (e.g. G3ZCZ)
             2    Default spacecraft configuration file (e.g. Dove)
             3    station latitude (e.g. 35.00)
             4    station longitude (e.g. 74.00)
             5    station altitude (e.g. 100)
             6    station minimum antenna elevation for acquisition  (e.g. 
                  0)
             7    station minimum usable pass time (e.g. 5) 
             8    early warning time (e.g. 5)
             9    default Kepler file (e.g. whats-up.2ln)
             10   UTC offset (e.g. EST = 5)
             11   default directory path (e.g. C:)
             12   default extracted data file (e.g. whats-up.txt)
             13   default file name with list of telemetry parameters  to 
                  extract file (e.g. ARRAYS)
             14   TNC Type (e.g. PK-232)
             15   PC serial port to TNC (e.g. 1)
             16   PC serial TNC port baud rate (e.g. 1200)
             17   PC Serial TNC port data bits (e.g. 8)
             18   PC Serial TNC port Stop bits (e.g. 1)
             19   PC Serial TNC port parity (e.g. N)
             20   PC serial port to Radio (e.g. 2)
             21   PC serial Radio port baud rate (e.g. 1200)
             22   PC Serial Radio port data bits (e.g. 8)
             23   PC Serial Radio port Stop bits (e.g. 1)
             24   PC Serial Radio port parity (e.g. N)
             25   Post pass delay (e.g. 2)


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 104


             26   status (top) window color (e.g. 79)
             27   Incoming window color (e.g. 14)
             28   outgoing window color (e.g. 30)
             29   prompt window color (e.g. 15)
             30   alarm window color (e.g. 15)
             31   bottom window color (e.g. 79)
             32   Emphasis color (e.g. 14)
             33   option color (e.g. 78)
             34   parameter changed color (e.g. 95)
             35   parameter limit exceeded color (e.g. 14)
             36   Orbit element window color
             37   Orbit  element  window Orbit element  window  In  range 
                  color
             38   Orbit element window early warning color
             39   Orbit element window next one up color
             40   Orbit alert dit time
             41   Orbit alert note
             42   Flag Sound 
             43   Doppler display Flag 
             44   The  next few lines link the  spacecraft  configuration 
                  files  and  contain:- SC ID,  Spacecraft  configuration 
                  file name, autotune parameter.

             The * that follows denotes the last line of SC ID data.

             You  must  configure WHATS-UP before you try any  Real  Time 
             activity.  

             The items in the configuration file are described below.

             9.1.1 Your callsign

             This item is the callsign displayed at the top of the screen 
             and  appended to the capture files when  capture-to-disk  is 
             turned on. 

             9.1.2 Default spacecraft Name

             This item is the default spacecraft name (e.g. Dove). WHATS-
             UP  adds the ".SYS" to the end of the name  (e.g.  DOVE.SYS) 
             and loads that configuration file at start up.

             9.1.3 Station Latitude 

             This  item  is your station latitude (e.g.  35.00).  In  the 
             southern hemisphere, enter a negative number.

             9.1.4 Station longitude 

             This  item  is  your station longitude in  degrees  WEST  of 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 105


             Greenwich. (e.g. 74.00)

             9.1.5 Station Altitude 

             This item is the altitude of your station antenna above  sea 
             level in Meters. (e.g. 100)

             9.1.6 Station minimum antenna elevation for acquisition

             This item is the minimum angle of elevation of your antennas 
             at  which you can acquire a signal. If you are on top  of  a 
             hill  or tall building the angle my be less than 0,  if  you 
             are in a valley, it may be greater, such as 5 degrees.

             9.1.7 Station minimum usable pass time 

             This  item is the minimum time in minutes for a usable  pass 
             for collecting data (e.g. 5).

             9.1.8 Early warning time

             This item is the early warning time in minutes you want  for 
             notice  that  a spacecraft is about to come  up  above  your 
             local horizon (e.g. 5).

             9.1.9 Default Kepler file

             This  item is the default file name that contains the  orbit 
             element data used when the program is first turned on  (e.g. 
             whats-up.2ln).

             9.1.10 UTC offset 

             This  item  is the time difference (in  hours)  between  the 
             local time in your PC and GMT or Universal Coordinated  Time 
             (UTC).  WHATS-UP always displays UTC time. (e.g. EST = 5)

             9.1.11  Default directory path (e.g. C:)

             This item is the directory path for the spacecraft  capture-
             to-disk  (YYMMDD.S/C), spacecraft configuration (*.SYS)  and 
             spacecraft operations schedule files (*.OPS).

             9.1.12  Default extracted data file

             This  item  is the name of the file to which data  which  is 
             extracted from a playback file will be written to in a comma 
             delimited  format  so that the data can be imported  into  a 
             spreadsheet  package  for  further  analysis  (e.g.   whats-
             up.txt).


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 106



             9.1.13  Default file name with list of telemetry  parameters 
             to extract file

             This  item  is the name of the file containing  the  channel 
             numbers to extract from a playback file for further analysis 
             (e.g. ARRAYS)

             9.1.14 TNC Type

             This  item is the type of TNC or Multi-mode  controller  you 
             are using. WHATS-UP currently supports the PK-232.

             9.1.15 Serial port to TNC

             This item is the Communications port number between the  TNC 
             and  the  PC (e.g. 1).  If you set it to  0,  WHATS-UP  will 
             never try to access the TNC.

             9.1.16 PC TNC Serial baud rate

             This  item is the baud rate used between the TNC and the  PC  
             (e.g. 1200).

             9.1.17 PC TNC port data bits

             This  item is the number of data bits used between  the  TNC 
             and the PC (e.g. 8).

             9.1.18 PC TNC port Stop bits

             This  item is the number of stop bits used between  the  TNC 
             and the PC (e.g. 1).

             9.1.19 PC TNC Port parity bits

             This item is the parity setting used between the TNC and the 
             PC. The letters to use are defined as 

                  N No parity, 
                  O Odd, 
                  E Even, 
                  M Mark, 
                  S Space.

             9.1.20 PC serial port to Radio

             This  item is the Communications port number between the  PC 
             and  the Radio (e.g. 2).  If you set it to 0, WHATS-UP  will 
             never try to access the radio. 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 107



             9.1.21 PC Radio port Serial baud rate

             This item is the baud rate used between the PC and the Radio 
             (e.g. 4800).

             9.1.22 PC Radio port data bits

             This item is the number of data bits used between the  Radio 
             and the PC (e.g. 8).

             9.1.23 PC TNC port Stop bits

             This item is the number of stop bits used between the  Radio 
             and the PC (e.g. 2).

             9.1.24 PC Radio Port parity bits

             This  item is the parity setting used between the Radio  and 
             the PC. The letters to use are defined as 

                  N No parity, 
                  O Odd, 
                  E Even, 
                  M Mark, 
                  S Space.

             9.1.25 Post pass delay 

             This  item is the time (in minutes) that WHATS-UP after  the 
             computed LOS time before returning the radio to the  default 
             frequency  (e.g. 2). This delay is to be used in  the  event 
             that  the elements do not quite predict the exact times  for 
             your system.

             The following items are the color values used for  different 
             windows or messages.

             9.1.26 status (top) window color (e.g. 79)
             9.1.27 incoming window color (e.g. 14)
             9.1.28 outgoing window color (e.g. 30)
             9.1.29 prompt window color (e.g. 15)
             9.1.30 Alarm window color (e.g. 15)
             9.1.31 Bottom window color (e.g. 79)
             9.1.32 Emphasis color (e.g. 14)
             9.1.33 Option color (e.g. 78)
             9.1.34 Parameter changed color (e.g. 95)
             9.1.35 Parameter limit exceeded color (e.g. 14)
             9.1.36 Orbit element window color
             9.1.37 Orbit element window In range color


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 108


             9.1.38 Orbit element window early warning color
             9.1.39 Orbit element window next one up color

             9.1.39 Orbit alert dit time

             This item is the speed of the morse code annunciator used to 
             alert you of satellite AOS, EWT and LOS.

             9.1.40 Orbit alert note

             This item is the tone of the morse code annunciator used  to 
             alert you of satellite AOS, EWT and LOS.

             9.1.41 Flag Sound

             This  item controls the sounds coming from the PC.  A  1  is 
             on, 0 is off.

             9.1.42 Doppler display Flag 

             This  item  determines  the  type  of  Doppler  display   as 
             follows:-

             0 display beacon frequency, 
             1 display Doppler shift.

             9.1.43 Spacecraft Configuration File Linkages

             The  next few lines contain the information  which  WHATS-UP 
             uses  to  link  the spacecraft configuration  files  to  the 
             Keplerian  elements  for orbit determination  and  automatic 
             selection  of  spacecraft at AOS time.  There should  be  NO 
             SPACE characters before or between the commas, in the  first 
             two data elements. The lines contain data as shown below.

                           UO-11,UOSAT11.SYS, 0
                           AO-13,OSCAR13Z.SYS,0
                           AO-16,PACSAT.SYS,  0
                           DO-17,DOVE.SYS,    1
                           WO-18,WEBER.SYS,   0
                           LO-19,LUSAT.SYS,   2
                           FO-20,FUJI.SYS,    0

             The  first item is the Keplerian element identifier for  the 
             spacecraft as used in the orbit element files.

             The second item is the FULL configuration file name for  the 
             spacecraft.

             The  third  item  is the automatic  AOS  selection  flag  as 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 109


             itemized below.  

             '0', automatic selection is inhibited. 

             '1', WHATS-UP selects that spacecraft configuration file  at 
                  EWT  time  (if it is not selected at  that  time),  and 
                  tunes  the  radio  to the  beacon  frequency  +  offset 
                  defined in that file. 

             '2', WHATS-UP selects that spacecraft configuration file  at 
                  AOS  time  (if it is not selected at  that  time),  and 
                  tunes  the  radio  to the  beacon  frequency  +  offset 
                  defined in that file. 

             9.1.44  * Comment line

             This  line  must be present and signals  WHATS-UP  that  the 
             default  parameters  have been read and that  the  following 
             lines contain commands to be sent to the TNC on starting  up 
             the program.

             9.1.45  The remaining lines are commands sent to  the  PK232 
             when you configure the TNC. Note to avoid lock ups FLOW  and 
             XFLOW MUST be OFF. Typical commands are as follows:-

                           HEAD ON
                           ECHO OFF
                           DAYSTAMP ON
                           MONITOR 6
                           MSTAMP ON
                           FLOW OFF
                           XFLOW OFF
                           MFILTER None

             9.2 Spacecraft Parameter Files

             You  need  a Different spacecraft parameter  file  for  each 
             spacecraft.  Spacecraft  parameter files are  named  by  the 
             spacecraft  and  given the extension  '.SYS'.  Examples  are 
             'DOVE.SYS'  and 'Fuji20.SYS'. These files determine how  the 
             individual channels are decoded, and where, in which  screen 
             page,  and  in which color the decoded data  are  displayed. 
             Some  of  the items are unique to WHATS-UP and some  to  the 
             particular spacecraft.

             The  contents  of the SPACECRAFT.SYS file are  as  described 
             below.





        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 110


             9.2.1 Spacecraft ID.

             This is the call sign of the spacecraft. For example, 

                           Spacecraft      ID

                            DOVE-OSCAR 17  DOVE-1
                            Fuji-OSCAR 12  8J1JAS
                            Fuji-OSCAR 20  8J1JBS

             In  the case of the Microsats and Fuji-OSCAR 12/20, and  any 
             other  using packet telemetry, WHATS-UP searches the  packet 
             headers to detect the spacecraft by this callsign.

             9.2.2 Spacecraft Suffix

             This becomes the filetype for the capture-to-disk files. The 
             default suggestions are as shown below.

                            Spacecraft          Suffix

                            UoSAT-OSCAR 11      U11
                            Fuji-OSCAR 12       F12
                            AMSAT-OSCAR 13      O13
                            AMSAT-OSCAR 16      O16
                            DOVE-OSCAR 17       D17
                            WEBER-OSCAR 18      W18
                            LUSAT-OSCAR 19      L19
                            Fuji-OSCAR 20       F20
                            AMSAT-OSCAR 21      O21

             9.2.3 Beacon Frequency

             This is the frequency of the spacecraft beacon (in MHz) that 
             you  are  monitoring.  It will be displayed  in  the  status 
             window.

             9.2.4 Doppler Measurement File

             This  is  the  default name of the file used  to  store  the 
             Doppler frequency measurements.

             9.2.5  Spacecraft Identification in Keplerian Element  File, 
             examples are as follows.

                           UO-11      AO-13          AO-16      DO-17
                           WO-18      LO-19          FO-20





        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 111


             9.2.6 Doppler Measurement Sample Interval
             
             This  is  the  default sample  interval  (in  seconds)  used 
             between Doppler frequency measurements.

             9.2.7 Initial Frequency Offset

             This  is  the  default value (in kHz) added  to  the  beacon 
             frequency,   and  output  to  the  Radio  Receiver  when   a 
             particular spacecraft is selected. The default value is 5 to 
             tune  the radio 5 kHz above the beacon. This will allow  the      
             signal  to slide into lock, whereby the TAPR PSK Modem  will      
             lock on and follow the frequency for the rest of the pass.

             9.2.8 Autotrack flag 

             This  item tells WHATS-UP if it should allow another AOS  to 
             interrupt data collection from this spacecraft.

                  0    Don't let another AOS to interrupt collection.
                  1    Allow   another   spacecraft  AOS   to   interrupt 
                       collection, namely, tune to that spacecraft at its 
                       AOS.

             9.2.9 Modulation

             This  is the type of modulation to set the Radio to to  copy 
             data from the spacecraft. Current options are :-

             C CW
             F FM 
             L LSB
             P PSK
             U USB.

             9.2.10 Data Type

             This is the type of data downlinked by the spacecraft.

             A ASCII as used by UoSAT-OSCAR 11.
             B BAUDOT as used by AMSAT-OSCAR 13.
             C CW as used by AMSAT-OSCAR 21.
             P Packet  as  used by DOVE-OSCAR 17, Fuji-OSCAR 20  and  the 
               Microsats.

             9.2.11 Receiver Type

             This  is  the  manufacturer of the radio  receiver  you  are 
             using.   This version of WHATS-UP only supports the  Kenwood 
             series.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 112



             9.2.12 Receiver Address

             This is a spare for use with future radios such as Icom.

             9.2.13 Selected or default display page number

             This  is  the  default display page for  the  Real-time  and 
             Playback modes, when WHATS-UP is first loaded.

             9.2.14 Page Definitions

             These are the page definitions, with two items on the  line. 
             The  format  is PAGE_TITLE, Page_Color, as  in  the  example 
             below.

             SPACECRAFT HOUSEKEEPING, 30

             9.2.15 Telemetry Parameter Configuration

             The   next  set  of  items  are  the   Telemetry   parameter 
             configurations (maximum = 99). You must have at least one of 
             these  lines in the file. If you want a value to show up  in 
             more  than one page (other than the wild card [0]) you  must 
             enter it twice (once per page). Typically each row  contains 
             17 items in the format shown below.

             TLM_Channel, TLM_Segment_ID, TLM_Description,  TLM_Eqn_Type, 
             TLM_Ceof_C,  TLM_Ceof_B,  TLM_Ceof_A,  TLM_Units,  TLM_Page, 
             TLM_Row,   TLM_Col,  TLM_Width,  TLM_Dec,   TLM_Limit_Check, 
             TLM_Limit_Low, TLM_Limit_High, TLM_Negative_Blank.

             Each item is described in the following sections.

                  9.2.15.1 TLM_Channel

                  This is the channel number of the telemetry data in the 
                  frame.  The  DOVE channel number is  hexadecimal  (e.g. 
                  '0F'), Fuji is decimal. Each entry must be two digits.

                  A special identifying TLM_Channel is defined in  WHATS- 
                  UP. If the value is '99 then the segment identifier and 
                  position  of the segment identifier is defined  in  tow 
                  positions in the line. This special channel  identifies 
                  the type of telemetry frame.

                  9.2.15.2 TLM_Segment_ID

                  This is the segment identifier as described in  Section 
                  9.2.15.99 below. 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 113



                  9.2.15.3 TLM_Description

                  This  item  is the text string or  description  of  the 
                  telemetry channel that will be displayed on the  screen 
                  page. (e.g. '+Z Array Temp.')

                  9.2.15.4 TLM_Eqn_Type

                  This item tells WHATS-UP the type of equation to use to 
                  decode the telemetry. 

                  Type 1 is the general purpose equation used by AMSAT-NA 
                  in the Microsats.

                  Fuji uses two other types of equations (2 and 3).  They 
                  are in the formats of

                  Y = D*(N+E), and Y = F*(G-N). If you know some  algebra 
                  you can convert both of Fuji's equations to the  Format 
                  used  by AMSAT, but since a computer is  involved,  why 
                  not  let it do the job. You do however have to  convert 
                  an equation of the form Y=(N+a)/b.

                  AMSAT-OSCAR 13 also needs three more types (4 5 and  6) 
                  of equations to decode the RTTY Z blocks.

                  A  type  1 equation in WHATS-UP is a quadratic  of  the 
                  form 
                   Y = A*N^2 + B*N + C,
                   where: N = raw telemetry data value
                   A,  B,  C = Equation Coefficients; Y,  N  are  decimal 
                  values.

                  A  type  2 equation in WHATS-UP has the format  in  the 
                  form of
                   Y = B*(A+N) + C
                  where  C,  B,  A are coefficients;  Y,  N  are  decimal 
                  values.

                  A  type  3 equation in WHATS-UP has the format  in  the 
                  form of
                   Y = B*(A-N) + C
                   where  C,  B,  A are coefficients; Y,  N  are  decimal 
                  values.

                  A  type  4 equation in WHATS-UP has the format  in  the 
                  form of
                   Y = B*(N+A)^2 +C
                   where  C,B,  A  are coefficients;  Y,  N  are  decimal 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 114


                  values.

                  A  type  5 equation in WHATS-UP has the format  in  the 
                  form of
                   Y = B*(A-N)^2 + C
                   where  C,  B,  A are coefficients; Y,  N  are  decimal 
                  values.
                   
                  A type 6 equation in WHATS-UP is a special case. It  is 
                  the  AMSAT-OSCAR 13 (Channel 1C) Spin Rate equation  as 
                  specified below.

                  if N > 131
                   then Y := 479/(N - 109) - 2
                   else Y := (131 - N) * 0.85 + 20;

                  where  N is the raw decimal number in Channel 1C and  Y 
                  is the spin rate.

                  9.2.15.5 TLM_Ceof_C
                   
                  This item is the equation Coefficient C.

                  9.2.15.6 TLM_Ceof_B

                  This item is the equation Coefficient B.

                  9.2.15.7 TLM_Ceof_A

                  This item is the equation Coefficient A.

                  9.2.15.8 TLM_Units

                  This  item is the Units text string (e.g. '.C') in  the 
                  screen display. However if the Tlm_Channel is '99' then 
                  this item is the segment identifier string.

                  9.2.15.9 TLM_Page

                  This  item is the Display page number. A 0 is  a  'wild 
                  card' which will be displayed on every page.

                  9.2.15.10 TLM_Row

                  This item is the Display page row. It identifies  which 
                  row in the screen the data element will be displayed.

                  9.2.15.11 TLM_Col

                  This  item  is the Display page column.  It  identifies 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 115


                  which  column  in  the screen the  data  item  will  be 
                  displayed.

                  9.2.15.12 TLM_Width

                  This  item is the Display width for Engineering  Units. 
                  It tells WHATS-UP how many characters wide the  display 
                  is  to  be. You can set it to any value you  want.  For 
                  example,  you  can  display  a  voltage  as  '1.3'   or 
                  '1.28567'.  Before  you  widen the  display  too  much, 
                  remember the sampling accuracy of the analog-to-digital 
                  converter in the spacecraft.

                  9.2.15.13 TLM_Dec

                  This  item  defines  the number  of  digits  after  the 
                  decimal point in the display.

                  9.2.15.14 TLM_Limit_Check

                  This  item tells WHATS-UP to perform limit checking  on 
                  the  telemetry channel. It may have several  values  as 
                  described below.

                   0 = do nothing, 
                   1 = check below low limit,
                   2 = check above high limit, 
                   3 = check for EITHER [below low limit] or [above  high 
                       limit]).

                  9.2.15.15 TLM_Limit_Low

                  This item is the Low limit value (e.g. -4.00).

                  9.2.15.17 TLM_Limit_High

                  This item is the High limit value (e.g. +10.6).

                  9.2.15.18 TLM_Negative_Blank

                  This  item is a 1 if you want computed negative  values 
                  to  be  displayed as a zero. Use this for  example,  in 
                  Solar  Cell Voltage computations, when negative  values 
                  are  produced by the equation supplied even though  the 
                  negative  values are not real. The negative values  are 
                  produced because the equation used to convert the  data 
                  is not valid at low or zero values of light.

             A  line with an '*' as the first character  terminates  this 
             section.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 116



             9.2.15.99 The Telemetry Identifier Line

             The  Telemetry  identifier  line has the same  format  as  a 
             regular line, but contains different parameters as follows:

                   9.2.15.99.1 The Line Identifier

                   This  item  has to be '99' to identify  the  telemetry 
                   identifier line.

                   9.2.15.99.2 The Segment Identifier

                   This  is used when the spacecraft transmits  telemetry 
                   in  more  than one segment. It  contains  the  segment 
                   identifier showing which segment the channel is  down 
                   linked in. 

                   9.2.15.99.3 Spare/Not Used

                   9.2.15.99.4 Location of Segment Identifier in Line

                   This  item  contains  the  location  of  the   segment 
                   identifier in the first line of the telemetry data.

                   9.2.15.99.5 Spare/Not Used
                    
                   9.2.15.99.6 Spare/Not Used

                   9.2.15.99.7 Spare/Not Used

                   9.2.15.99.8 Segment Identifier String

                   This item is the segment identifier string as follows.

                           9.2.15.99.82.1 Fuji

                           The Fuji frame contains one real time  segment 
                           (Segment   1)   in  a   frame   addressed   as 
                           8J1JBS>BEACON. A typical frame is shown below.

                            19-Apr-90 17:14:34 8J1JBS*>BEACON:
                            JAS1b RA 90/04/19 17:13:58
                            609 430 687 676 744 837 845 829 498 681
                            617 001 505 516 526 524 526 523 654 000
                            683 675 686 695 999 643 875 471 099 000
                            110 111 000 000 111 100 001 111 111 000

                           The  segment identifier is in the seventh  and 
                           eighth  characters  of the first line  of  the 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 117


                           data.  A segment identifier of  that  position 
                           identifies  the  second segment.  The  segment 
                           identifier  is the 'RA' located on  the  first 
                           line  of the data just after the  JAS1b  where 
                           the  'R' in 'RA' is the seventh  character  in 
                           the line. 

                           Any   telemetry  frame  addressed  to   BEACON 
                           received  without that segment  identifier  is 
                           assumed by WHATS-UP to be Segment 2.

                           9.2.15.99.8.2 DOVE

                           DOVE  transmits telemetry in two  frames  each 
                           addressed  as DOVE-1>TLM. The  Microsat  ASCII 
                           frame thus contains two segments. Two  typical 
                           segments of DOVE telemetry are shown below.

        DOVE-1>TLM [01/29/90 22:08:46]:
        00:59 01:59 02:86 03:30 04:58 05:58 06:6D 07:45 08:6C 09:66 0A:A1
        0B:D9 0C:E8 0D:D8 0E:01 0F:23 10:CC 11:A8 12:00 13:01 14:A8 15:94
        16:96 17:94 18:95 19:96 1A:93 1B:90 1C:9A 1D:98 1E:23 1F:5E 20:BC

        DOVE-1>TLM [01/29/90 22:08:47]:
        21:98 22:7B 23:24 24:21 25:2E 26:00 27:00 28:00 29:00 2A:00 2B:00
        2C:00 2D:29 2E:00 2F:9B 30:C8 31:9C 32:11 33:DA 34:C0 35:95 36:A4
        37:A4 38:B2 39:96 3A:00


                           The default segment identifier used by  WHATS- 
                           UP  is in the first and second  characters  of 
                           the   first  line  of  the  data.  A   segment 
                           identifier   of  '00'  identifies  the   first 
                           segment,  and anything else in  that  position 
                           identifies the second segment.

                           AMSAT-OSCAR  13 RTTY Telemetry is  transmitted 
                           in  the form of Z blocks shown below  (several 
                           blank lines have been deleted to same space in 
                           this document).












        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 118


                       Z  HI. THIS IS AMSAT OSCAR 13
                            05.02.44  4661
                       .0086   .0000   .07B9                   
                                          
                       64  6   0   1   16  218 1               
                       
                       193 170 158 143 181 144 147 140 200 7   
                       147 7   7   7   165 29  100 7   149 7   
                       10  7   145 115 34  7   153 129 122 180 
                       
                       152 73  7   145 137 55  7   183 136 151 
                       7   154 137 169 211 142 127 100 9   140 
                       161 7   173 149 150 154 14  131 127 210 
                       HI THIS IS AMSAT OSCAR 13 08SEP90
                       NEW AO13  SCHEDULE FROM 17OCT90 AFTER MOVE TO  LON 
                           180  LAT 0
                       MODE B  MA 000 TO 095
                       MODE JL MA 095 TO 125
                       MODE LS MA 125 TO 130
                       MODE S MA 130 TO 135
                       MODE BS MA 135 TO MA 140
                       MODE B  MA 140 TO 256

                           Note the non telemetry information at the  end 
                           of the block. UoSAT-OSCAR 11's ASCII telemetry 
                           looks different, so WHATS-UP is told where  to 
                           look for the telemetry by the following items.

                           9.2.15.99.9 Spare

                           9.2.15.99.10 Number of Lines

                           This  item is used in non packet telemetry  to 
                           tell WHATS-UP how many lines of data are in  a 
                           frame.

                           9.2.15.99.11 First Line

                           This  item is used in non packet telemetry  to 
                           tell WHATS-UP which line in the frame contains 
                           the first line of data.

                           9.2.15.99.12 Last Line

                           This  item is used in non packet telemetry  to 
                           tell WHATS-UP which line in the frame contains 
                           the last line of data.





        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 119


                           9.2.15.99.13 Header Lines

                           This  item is used in non packet telemetry  to 
                           tell WHATS-UP how many lines there are in  the 
                           header.

                           9.2.15.99.14 Character Count 

                           In non packet telemetry this item tells WHATS-
                           UP the maximum number of characters on a line. 
                           Use  it  in BAUDOT,ASCII and CW  telemetry  to 
                           stop  the display overrunning the page and  to 
                           force  recognition of the identifier and  turn 
                           the automatic capture-to-disk on.

             9.2.16 Digital Telemetry Status Channels

             The  next  set  of lines instruct WHATS-UP  how  to  display 
             digital telemetry status in the Fuji-OSCAR 20 frame. Digital 
             status  channels  contain a number of status  points.  Fuji-
             OSCAR  12  and 20 have three data elements in  each  digital 
             status  channel.  Typically, each line in  the  WHATS-UP.SYS 
             file contains ten items in the following format.

             Status_Channel,      Status_Display_Page,       Status_Text, 
             Status_Bit_Mask,  Status_Row,  Status_Col,   Status_ON_Text, 
             Status_OFF_Text, Status_ON_Color, Status_OFF_Color.

             Each item is described in the following sections.

                  9.2.16.1 Status_Channel

                  This  is  the  channel number  of  the  digital  status 
                  telemetry  data  in the frame. Each entry must  be  two 
                  digits.

                  9.2.16.2 Status_Display_Page

                  This  item is the Display page number. A 0 is  a  'wild 
                  card' which will be displayed on every page.

                  9.2.16.3 Status_Text

                  This is the text that is displayed in the page.

                  9.2.16.4 Status_Bit_Mask

                  This  is the bit mask to mask out the position  of  the 
                  desired  bit. The masks are in decimal. i.e. 1, 10  and 
                  100.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 120



                  9.2.16.5 Status_Row

                  This item is the Display page row. It identifies  which 
                  row in the screen the data element will be displayed.

                  9.2.16.6 Status_Col

                  This  item  is the Display page column.  It  identifies 
                  which  column  in  the screen the  data  item  will  be 
                  displayed.

                  9.2.16.7 Status_ON_Text

                  This  item  is  the text that  is  displayed  when  the 
                  spacecraft telemetry contains a 1 value.

                  9.2.16.8 Status_OFF_Text

                  This  item  is  the text that  is  displayed  when  the 
                  spacecraft telemetry contains a 1 value.

                  9.2.16.9 Status_ON_Color

                  This  item is the color the text is displayed  in  when 
                  the spacecraft telemetry contains a 1 value.

                  9.2.16.10 Status_OFF_Color

                  This  item is the color the text is displayed  in  when 
                  the spacecraft telemetry contains a 0 value.

             These  lines  also terminate with an '*' character.   A  few 
             typical lines from a Fuji.SYS file are shown below.

             30,3,JTA Power    :,100, 4, 1, ON  , OFF ,11,10
             30,3,JTD Power    :, 10, 4,25, ON  , OFF ,11,10
             30,3,JTA Beacon   :,  1, 4,45, PSK , CW  ,11,10
             38,3,Solar Panel 3:,100,12, 1, LIT , DARK,11,10
             38,3,Solar Panel 4:, 10,12,25, LIT , DARK,11,10
             38,3,Solar Panel 5:,  1,12,45, LIT , DARK,11,10

             Note the blanks in the Text ON and OFF positions. The blanks 
             are used to ensure that a word such as "LIT" which  contains 
             three  letters fully overwrites a word which  contains  four 
             characters such as "DARK".

             9.2.17 Packet/Link Parameters

             The  next  set  of  items  are  the  Packet/Link  Parameters 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 121


             configurations  (maximum = 16). If you want a value to  show 
             up in more than one page (other than the wild card [0])  you 
             must  enter  it twice (once per page).  Typically  each  row 
             contains 10 items in the sequence shown below.

             Packet_title,  Packet_Type,   Packet_Lines,  
             Packet_Page,   Packet_Color,  Packet_Row,
             Packet_Col,    Link_Page,     Link_Row,
             Link_Col,      Binary_Byte_Count.

             Each item is described in the following sections.

                  9.2.17.1 Packet_title

                  This  item is the name of UNP address  (e.g.  TLM,WASH, 
                  BCXRT).

                  9.2.17.2 Packet_Type

                  This  item  is used by WHATS-UP to define the  type  of 
                  telemetry   .  The  following  assignments  have   been 
                  allocated but are not necessarily used in this  release 
                  of WHATS-UP.

                  0    AMSAT-OSCAR 13 Non Packet Decimal telemetry.

                  1    AMSAT  Microsat  Packet Telemetry (TLM)  with  the 
                       format  CC:DD where CC is the hexadecimal  channel 
                       number and DD the hexadecimal data.

                  2    AMSAT Microsat Packet Telemetry, hexadecimal ASCII 
                       STATUS telemetry.

                  3    Fuji  Packet Telemetry format of decimal  data  in 
                       which  the  line  and the  position  on  the  line 
                       identify the channel. WHATS-UP allows for up to 60 
                       channels.

                  4    AMSAT Microsat Packet Telemetry hexadecimal Binary 
                       STATUS telemetry.

                  5    AMSAT Microsat Binary TLM Packet Telemetry.

                  6    UoSAT-OSCAR 9/11 ASCII Telemetry.

                  9.2.17.3 Packet_Lines

                  This item is the number of lines of text in the packet. 
                  for example, the AMSAT TLM packets contain three lines, 
                  the WASH packets contain only one.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 122



                  9.2.17.4 Packet_Page

                  This  item  is the page that the raw  contents  of  the 
                  packet will be displayed on. A '0' is a wild card which 
                  will make WHATS-UP display it on every page. By careful 
                  use of this item, you can display both raw and  decoded 
                  packet data on the same page.

                  9.2.17.5 Packet_Color

                  This item is the color that the raw packet data will be 
                  displayed in.

                  9.2.17.6 Packet_Row

                  This item is the row position that the raw packet  will 
                  be displayed in, on the selected page.

                  9.2.17.7 Packet_Col

                  This  item is the column position that the  raw  packet 
                  will be displayed in, on the selected page.

                  9.2.17.8 Link_Page

                  This item is the Display page for the cumulative  count 
                  of the packet type. The wild card '0' applies.

                  9.2.17.9 Link_Row

                  This  item is the row position that the  packet  header 
                  will be displayed in, on the selected page.

                  9.2.17.10 Link_Col

                  This item is the column position that the packet header 
                  will be displayed in, on the selected page.

                  9.2.17.11 Binary_Byte_Count

                  This item is the number of bytes in a binary packet. As 
                  no  standard  currently  exists, we have  to  tell  the 
                  computer how many bytes to expect.

             These lines also terminate with an '*' character.

        9.3 Telemetry Channel Extraction File

        The  contents of this file are the defaults for  extracting  data 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 123


        from  the playback file. A typical set are shown below.  WHATS-UP 
        does  a  string  match,  and looks for  the  first  time  that  a 
        particular string occurs. You may thus use the contents of a time 
        packet, or the time mark in a header.

                  ZCZC (default start time string) {start of file}
                  NNNN (default stop time string) {end of file}
                  2F
                  35
                  38

        The  first line contains the start string. 'ZCZC' tells  WHATS-UP 
        to start extracting at the beginning of the file. The second line 
        contains   the  stop  string.  'NNNN'  tells  WHATS-UP  to   stop 
        extracting  at the end of the file. The remaining lines  are  the 
        individual channels (uppercase letters), one channel per line.

        9.4 Extracted Telemetry Data File

        This an ASCII string, comma delimited file which can be  imported 
        into your spreadsheet.  The format of the file is such that  each 
        line starts with a date code or packet header. Then each  channel 
        and  the  datum  associated  with that  channel  follow  for  all 
        channels  in the packet segment or non packet frame for each  and 
        every  channel displayed in the selected page on the screen.   If 
        the data from that channel is not displayed on the screen in  the 
        extract mode, the data will not be extracted.

        A typical example of three lines from this file is shown below.

        "01-Mar-91  03:39:46  DOVE-1*>TLM:","35",    6.7,"38",   -9.7
        "01-Mar-91  03:39:56  DOVE-1*>TLM:","35",    6.7,"38",  -10.3
        "01-Mar-91  03:40:06  DOVE-1*>TLM:","35",    6.7,"38",  -10.3

        9.5 Doppler File

        Doppler data are stored in this file. If the file does not exist, 
        it is created when needed. IF it does exist, data are appended to 
        the  file. The first line of data identifies the time, place  and 
        spacecraft as shown below.

        "*** 22-Feb-91 02:57  Doppler Track STARTED for WEBER @ G3ZCZ"

        The  next  line  provides the headings for the  five  columns  as 
        follows.

        "Time","Doppler    Mark","Frequency","Doppler    Shift","Measured 
        Shift"




        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 124


             9.5.1 The Time 

             The Time is obtained from the PC clock. 

             9.5.2 The Doppler Mark 

             The Doppler Mark is a sequential count incrementing at  each 
             sample.  It can be used to provide an 'X' axis in  a  graph.  
             Elapsed  time  will be the Doppler mark  multiplied  by  the 
             Doppler sampling interval in seconds. 

             9.5.3 The Frequency 

             The Frequency is the measured radio frequency. 

             9.5.4 The Doppler Shift 

             The Doppler Shift is the calculated/predicted Doppler  Shift 
             in kHz.

             9.5.5 The Measured Shift 

             The  Measured Shift is the difference (in kHz)  between  the 
             measured  radio  frequency and the beacon frequency  in  the 
             configuration file.

        These  parameters  should allow you to plot  Doppler  curves  and 
        determine  orbit  parameters using the time of  closest  approach 
        technique.

        Typical entries in the file are shown in the following lines.

        "02:57:32", 2, 437110740, 8.1494,10.740
        "02:57:37", 3, 437110740, 8.1354,10.740
        "02:57:42", 4, 437110740, 8.1202,10.740
        "02:57:47", 5, 437109860, 8.1045,9.860
        "02:57:52", 6, 437110670, 8.0880,10.670
        "02:57:57", 7, 437110620, 8.0709,10.620
        "02:58:13", 8, 437110620, 8.0525,10.620
        "02:58:18", 9, 437109780, 7.9868,9.780
         .
         .
        "03:07:17", 115, 437092570, -7.7884,-7.430
        "03:07:22", 116, 437092570, -7.8204,-7.430
        "03:07:27", 117, 437092570, -7.8511,-7.430
        "03:07:32", 118, 437092570, -7.8802,-7.430
        "*** 22-Feb-91 03:07  Auto End"

        The lines of data end with a termination statement.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 125


        All  text items are enclosed in double quotation marks  (").  All 
        elements are delimited by comma characters (,).

        If you plan to do Doppler measurements on the Microsats, then you 
        may be interested in the following information.

        The  following  frequencies were taken after the  completion  and 
        final  tuning  of  the  completed  transmitter  assemblies.   The 
        measurements  were  made at a temperature of 23 deg.  C.  As  the 
        frequency does change with temperature the current frequency will 
        be slightly different.

                 PACSAT:   Normal PSK TX:        437.02625 MHz
                           Raised Cosine TX:     437.05130 MHz
                           S-Band TX:           2401.14280 MHz

                 DOVE:     FM TX No. 1:          145.82516 MHz
                           FM TX No. 2:          145.82438 MHz
                           S-Band TX:           2401.22050 MHz

                 WEBERSAT: Normal PSK TX:        437.07510 MHz
                           Raised Cosine TX:     437.10200 MHz

                 LUSAT:    Normal PSK TX:        437.15355 MHz
                           Raised Cosine TX:     437.12580 MHz

        9.6 Kepler Element Files (*.2LN)
         
        The following outlines the "NASA Two-Line" Keplerian data format.
        Data for each satellite consists of three lines in the  following 
        format:

        Example:
         
        Mir
        1 16609U          91 36.87776287 0.00038608           39705-3 0  2481
        2 16609  51.6077 232.9299 0024950 205.6681 154.3223 15.64092124284608
             Line 1 contains an eleven-character name.
              
             Lines 2 and 3 are the standard Two-Line Orbital Element  Set 
                        used  by NASA and NORAD.  The format  description 
                        is:
              
             Line 2
             Column     Description
              01-01     Line Number of Element Data
              03-07     Satellite Number
              10-11     International  Designator  (Last  two  digits  of 
                        launch year)
              12-14     International  Designator (Launch number  of  the 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 126


                        year)
              15-17     International Designator (Piece of launch)
              19-20     Epoch Year (Last two digits of year)
              21-32     Epoch  (Julian Day and fractional portion of  the 
                        day)
              34-43     First  Time  Derivative  of the  Mean  Motion  or 
                        Ballistic  Coefficient  (Depending  on  ephemeris 
                        type)
              45-52     Second  Time Derivative of Mean  Motion  (decimal 
                        point assumed; blank if N/A)
              54-61     Radiation  pressure coefficient.  (Decimal  point 
                        assumed)
              63-63     Ephemeris type
              65-68     Element number
              69-69     Check Sum (Modulo 10)
                        (Letters,  blanks, periods = 0; minus sign  =  1; 
                        plus sign = 2)
              
             Line 3
             Column     Description
              01-01     Line Number of Element Data
              03-07     Satellite Number
              09-16     Inclination (Degrees)
              18-25     Right Ascension of the Ascending Node (Degrees)
              27-33     Eccentricity (decimal point assumed)
              35-42     Argument of Perigee (Degrees)
              44-51     Mean Anomaly (Degrees)
              53-63     Mean Motion (Revs per day)
              64-68     Revolution number at epoch (Revs)
              69-69     Check Sum (Modulo 10)
              
             All other columns are blank or fixed.

        9.7 AMSAT Format Element File (*.AMS)

        The  AMSAT format file is the AMSAT file as received by means  of 
        packet radio. WHATS-UP scans the text for the word  "Satellite:". 
        When  it finds it, it assumes that the next few lines  carry  the 
        data in the fixed order.  You thus, do not need to edit the file, 
        just  capture it to disk, and save with a filetype of 'AMS'.  For 
        example the following file could be saved as ORBS-19.AMS.

        If you need to enter data in by hand, edit an AMSAT format file.









        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 127


             4116] B   BID: ORBS-019.D  
             Date: 20 Jan 91 02:58:24 Z
             From: N4QQ@N4QQ
             To: ALL@AMSAT
             Subject: Orbital Elements   019.MICROS
              
             R:910120/0258z 18616@N4QQ.MD.USA [Silver Spring,Md]  Z:20901
             From: N4QQ@N4QQ.MD.USA
             To: ALL@AMSAT
              
              
             HR AMSAT ORBITAL ELEMENTS FOR THE MICROSATS
             FROM N3FKV HEWITT, TX      JANUARY 19, 1991
             TO ALL RADIO AMATEURS BT
              
              
             Satellite: AO-16
             Catalog number: 20439
             Epoch time:      91014.08680572
             Element set:     188
             Inclination:       98.6853 deg
             RA of node:        94.6412 deg
             Eccentricity:    0.0010690
             Arg of perigee:   259.0593 deg
             Mean anomaly:     100.9381 deg
             Mean motion:   14.28942714 rev/day
             Decay rate:       3.95e-06 rev/day^2
             Epoch rev:            5098

             Satellite: DO-17
             Catalog number: 20440
             Epoch time:      91014.07510019
             Element set:     187
             Inclination:       98.6867 deg
             RA of node:        94.6574 deg
             Eccentricity:    0.0010787
             Arg of perigee:   258.7019 deg
             Mean anomaly:     101.2949 deg
             Mean motion:   14.29004143 rev/day
             Decay rate:       4.60e-06 rev/day^2
             Epoch rev:            5098

        9.8 Spacecraft Operations File

        This  is a text file which can usually be obtained from a  packet 
        radio bulletin. You may create one with the editor, if you  can't 
        find one on a packet radio BBS. A Typical file is shown below.





        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 128


            AO-13 TRANSPONDER SCHEDULE
             
              Mode-B : MA 060 to MA 165 :
              Mode-JL: MA 165 to MA 190 :
              Mode-LS: MA 190 to MA 195 :
              Mode-S : MA 195 to MA 200 : <= Mode B is Off - no swishing!
              Mode-BS: MA 200 to MA 205 : <= QRP on BS please.
              Mode-B : MA 205 to MA 256 :
              Omnis  : MA 240 to MA 060 :
             
            This schedule is expected to continue through 27 March 91
             

        10.0 Glossary

        AMSAT     The Radio Amateur Satellite Corporation
        AO        AMSAT-OSCAR 
        AOS       Acquisition of Signals
        ARRL      American Radio Relay League
        CCD       Charge Coupled Device
        DO        DOVE-OSCAR 
        DOVE      Digital    Orbiting    Voice   Encoder,    also    used 
                  interchangeably with DOVE-OSCAR or DO 
        EWT       Early Warning Time
        FM        Frequency Modulation
        FO        Fuji-OSCAR 
        FSK       Frequency Shift Keying
        LO        LUSAT-OSCAR 
        LOS       Loss of Signals
        OSCAR     Orbiting Satellite Carrying Amateur Radio
        AO        AMSAT-OSCAR 
        PSK       Phase Shift Keying
        RTTY      Radio Teletypewriter
        SSB       Single Side Band
        TNC       Terminal Node Controller
        TU        Terminal Unit (Radio Modem)
        UO        UoSAT-OSCAR 
        WO        WEBER-OSCAR 

        11.0 References and Further Reading

        The  best  book is "The Space Radio Handbook" by  John  Branegan, 
        GM4IHJ.  It is published by the Radio Society of  Great  Britain. 
        The book is available from the RSGB, Lambda House, Cranborne  Rd, 
        Potters  Bar, Herts., England EN6 3JE. The price is 13.34  pounds 
        sterling. John has also written several booklets on MIR, DOVE and 
        UOSAT-OSCAR 14 specifically for the educator and beginner. He can 
        be reached at 8 Whitehills, Saline, Fife, Scotland KY12 9UJ.

        Other books and articles of interest are listed below.


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP.DOC Release 1.20 Page 129



             Space  Radio Handbook, John Branegan, GM4IHJ, Radio  Society 
             of Great Britain.

             Satellite  Experimenter's Handbook, Martin Davidoff,  K2UBC, 
             ARRL 1990, 2nd Edition. 

             A  Turnstile Antenna for Two Meters, Joe Kasser,  G3ZCZ,  73 
             Magazine, June 1978.

             Antennas for Microsat Ground Stations, Dick Jansson, WD4FAB, 
             The AMSAT Journal, Volume 13, Number 1, March 1990.

             Satellite Antennas from Recycled Junk, Howard Sodja,  W6SHP, 
             Proceedings  of the OSCAR Seminar, September 29 & 30,  1990. 
             Available from Project OSCAR Inc.

             Microcomputer Processing of UoSat-OSCAR 9 Telemetry,  Robert 
             J.  Diersing, N5AHD,  The Satellite Anthology, Pages  46-51, 
             ARRL, 1988.

             The  First Flock of Microsats, Tom Clark, W3IWI,  Jan  King,   
             W3GEY,  Bob  McGwier,  N4HY and the AMSAT  team,  The  AMSAT   
             Journal, Volume 12 Number 1, May 1989.

             Ariane  Launch  Vehicle Malfunctions - Phase  3A  Spacecraft   
             Lost!, Tom Clark, W3IWI, Joe Kasser, G3ZCZ, Orbit  Magazine,   
             Volume 1 Number 2, June/July 1980.

        12.0 Change History

        1.00 (4/01/91) Initial Release.

        1.10 (7/15/91) Converted to TP 6.0. Break procedure added on  TNC 
             port.    Radio  port  parameters  added   to   WHATS-UP.SYS. 
             Autotrack  added.  Default radio freq/mode added.   TNC  and 
             Radio Serial Port values 0 added to allow WHATS-UP to run in 
             a  multi-tasking  environment without interfering  with  the 
             serial  ports.  Directory  path changed  to  apply  only  to 
             capture-to-disk   files.   Debug  Menu  added.  Radio   Menu 
             changed.  CW telemetry automatic capture-to-disk added  (for 
             A-O 21).

        1.20 (11/08/91) SARA, TNC1, TNC2, PK-88, KAM and MFJ-1278 added.








        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        APPENDIX 1 Obtaining Further Information Page 130 


        For   further  information  about  any of the spacecraft and  the  
        Radio   Amateur    Satellite  program,  photocopy  and  mail  the 
        following form together  with  a self addressed stamped  envelope 
        (SASE) to :-

         To: 
        [ ]       Project OSCAR Inc. POB 1136, Los Altos, CA. 94023-1136.

        [ ]       AMSAT-UK, 94 Herongate Road, Wanstead Park, London  E12           
                  5EQ.  Telephone (081) 989 6741.

        I  read about the Radio  Amateur Satellite   program in  WHATS-UP 
        and  am interested in it.  Please  send  me  further  information  
        about  the  program,   and   details  of   membership   in   your 
        organization.

         CALL ________________ TODAY'S DATE _____________

         NAME ______________________________________________

         ADDRESS ___________________________________________

         ___________________________________________

         CITY ___________________________________________

         STATE _________ POSTCODE ______________________

        Comments and questions ...


















        From WHATS-UP (c) G3ZCZ




        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        APPENDIX 2 Amateur Radio Software by Joe Kasser G3ZCZ


        PC-HAM 3.52

        PC-HAM contains a number of programs some of which are  described 
        below. 

                                     LOGBOOK

        Full  blown  logging package. With automatic check  of  logs  for 
        awards such as DXCC. Allows you to recall any entry by call  sign 
        within  seconds.  Indexed displays, QSLing, Contest  mode  QSLing 
        (prints the lot) and lots more written in dBASE3, but a  compiled 
        LOGBOOK.EXE file is supplied together with the source code. 

                                     CONTEST

        Keeps Dupes in memory, logs QSO's to disk in format which can be 
        processed by the LOGBOOK package. 

                                      CQSS

        Sweepstakes  game.  Work  the ARRL Sweepstakes  contest  on  your 
        computer.   You  are  located  just  outside  Washington  DC.   A  
        propagation   model is built in to the program. This  program  is  
        REQUIRED  training   for all sweepstakes  operators.  Program  is 
        based  on  the one  described in detail in 'Software for  Amateur 
        Radio'   by   Joe Kasser  G3ZCZ,  published by  TAB  Books,  Blue  
        Ridge  Summit,  PA. 17214.

                                     WHATSON

        Predict HF Propagation. Contest mode with printout to whole world 
        at hourly intervals. Needs BASIC


        LAN-LINK 1.59

            LAN-LINK  will  capture AMSAT related bulletins  from  packet 
            radio BBSs automatically.  Amongst its many features are :-

            Zmodem binary file transfer capability.  

            Function  key  and  Menu driven. 

            Automatic  logbook  entries  for Packet  and   Mailbox/Beacon 
            Mode   AMTOR   Connects,  semiautomatic logbook  entries  for 
            other modes. Log file can be processed by the Logbook Package 
            of  PC-HAM.   Contest  operation,  sends   standard   message  
            and  automatically increments  QSO count. Automatic optimized 
            configuration  of  the TNC  for each communications mode. 



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        APPENDIX 2 Amateur Radio Software by Joe Kasser G3ZCZ


            All  mode Function  key  'OVER' feature (End). There  are  10 
            files with fixed names (LAN-LINK.001  through   LAN-LINK.010)  
            which  may  be viewed and transmitted by means  of   function 
            keys. They may also be edited from the Edit Menu.  

            Time   display  and  event  scheduler.  ASCII  Text   Editor. 
            Customizable  Colors.   Access  to the TNC  Command  Mode  is 
            provided in  case  the user wishes to override any defaults. 

            Automatic  capture  to  disk of all  packet  radio  connects. 
            Automatic indication  of the number of Packet connects. Local 
            Area   Network  (LAN) message store and  Forward  capability.  
            Capable   of  automatic connect attempts to download  a   QTC  
            from another station in the LAN. Capable of automatic connect 
            attempts  to   a   packet  BBS  to  download  your   incoming 
            messages,   when   your  callsign  appears on  the  BBS  mail 
            beacon annunciator. 

            Capable   of automatically requesting Bulletins  on  subjects 
            that  interest   you  from your local  packet  BBS.  Digipeat  
            monitoring  and capture. Alert signal to let  you  know  when  
            a   predetermined  call  shows up  in  a  packet  header   on 
            frequency. 

            Conference  Mode  in  multiconnect  situations.  Bridge  Mode  
            in  multiconnect   situations.   Path  determination  to   DX  
            station   via  :QMH:.  Indicator  that  a  specific   station  
            designated   as   the 'target'  call   connected   in  Packet 
            Mode,   or  linked  to  AMTOR Beacon/Mailbox while  you  were 
            away.  Automatic   NET/ROM  and  KA Node path set   up   from  
            LAN-LINK.DIR call/path directory file. 

            Selective answering machine and MAILBOX using  NC/L   command 
            dialogue. Screen indication  of  connect  by desired  station 
            (target call). 

            Automatic  Beacon Mode CQ caller. Will call CQ   repetitively  
            and  either work the connect and keep going after  disconnect 
            or  signal  you  when  a reply  is  received.  SAREX  special 
            features. :QRA: trigger to determine who else is on channel. 
            Automatic  AMTOR SELCAL determination. 

            Function key  change  from monitoring AMTOR FEC CQ's to QSO's 
            in  progress  (chirpcopy). NAVY MARS RTTY  file  transmitting 
            protocols  for the PK-232. Log files in dBASE 3  format.  AND 
            MORE !!!!!






        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP APPENDIX 3 SHAREWARE Page 133


        The  Association of Shareware Professionals (ASP) has established  
        standards for its members and for any organization which has "ASP 
        Approved"  status. The ASP wants to make sure that the  shareware 
        principle  works for you. If you are unable to resolve a  problem 
        with  an  ASP  member  or  organization  (other   than  technical 
        support),  the ASP may be able to help. Please write to  

        The  ASP Ombudsman, 545 Grover Rd, Muskegon, MI. 49442, U.S.A.

        You  are encouraged to copy the floppy disk and share  it  freely 
        with  others.  You have the luxury of trying out the  product  at 
        your own pace and in the comfort of your own home or workplace.  

        After  you  have used the material for  a  reasonable  evaluation 
        period  (90  days),  you should either  discontinue  use  of  the 
        material  or register your copy.  Your support is  important  and 
        greatly  appreciated.  With it, Shareware authors are  encouraged 
        to  design and distribute new products. Without it, a great  deal 
        of high quality, low cost software will cease to be available.

        Why pay at all?

           *  You receive support from the author.
           *  You receive a CURRENT copy of the program.
           *  Your input and ideas help shape future products.
           *  A sense of pride and ownership in having honestly
              participated in the Shareware revolution.
           *  You help to keep software prices down by supporting a
              distribution method which doesn't depend on expensive
              advertising campaigns.

        Be  aware of the following restrictions, designed to protect  the 
        community  of Shareware users and to prevent greedy  people  from 
        taking unfair advantage of the trust, hard work and good will  of 
        Shareware authors. 

        1.   No  price or consideration may be charged for the  material.           
             However, a distribution cost may be charged for the cost  of           
             the diskettes, shipping and handling, not to exceed $6.

        2.   The  files and programs on the disks may not be modified  or           
             deleted.

        3.   The  material  cannot  be sold as part of  some  other  more           
             inclusive package.

        4.   The material cannot be "rented" or "leased" to others.

        5.   The end user must be told clearly in writing on the  outside           
             of  the package and in all advertising that the  diskette(s)           


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP APPENDIX 3 SHAREWARE Page 134


             are "Shareware."

        6.   The package must contain a written explanation that the disk           
             is   for  evaluation  purposes,  and  that   an   additional           
             "registration  fee"  is  expected  by  the  author,  if  the           
             material is used beyond an initial evaluation period.

        7.   In the case of distribution via any telecommunications link,           
             the following must be done:

             An error checking protocol must be used.

             The individual files must be combined into, and  transferred           
             in a library or archive format.  

        8.   Shareware  distribution  is  permitted only  in  the  United           
             States, Canada, England, and Australia.



































        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP 1.20 Registration form


        WHATS-UP 1.20 Registration Fee $35.00
        LAN-LINK 1.59 Registration Fee $35.00 
        PC-HAM   3.52 Registration Fee $36.50
                 Register them all for $95.00.

        Evaluation Copies free, you pay only for the disk/postage. For an 
        evaluation  copy  (unregistered  full  blown  version)  of   each 
        software  send a formatted disk and SASE to Joe Kasser.  Overseas 
        users,  send  $5.00 ($10.00 covers all three)  instead.  Try  the 
        software  first, and only register your copy if you make  use  of 
        it. 

         To: Joe Kasser G3ZCZ,  P O BOX 3419,  SILVER SPRING,  MD 20918.

         CALL ________________ TODAY'S DATE _____________

         NAME ______________________________________________

         ADDRESS ___________________________________________

                 ___________________________________________

         CITY ___________________________________________

         STATE _________ POSTCODE ______________________

         TNC TYPE _____________________ Home BBS __________

        I enclose a check for ______. Please send me the latest version 
        of ______________, and register me as a user.

        I enclose a disk/sase or $5.00. Please send me the latest version 
        of ______________________ to evaluate. If I like it and use it, I 
        plan to become a registered user.

        Disk Size 5.25 _____(360k) 5.25 _____(1.2Mb) 3.5 ______(730k)

        I  AM  NOT/AM  currently using Shareware Version  _____  which  I 
        obtained from _________________________________________.

         Signature _______________________

        Classroom Registration    6 to 10 copies    $195.00.
        Radio Club Registrations 10 or more copies, 10% discount.
                                 50 or more copies, 25% discount.

        Clubs; designate one contact person to receive classroom or  club 
        registered  updates, and  supply  a list of names and call  signs 
        of club  members  who will be using the Registered Club Copy.



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 136


        Abort, 18
        Accessible, 99
        Accomplish, 99
        Achieve, 95
        ACK, 71
        Acquire, 21, 100, 105
        Acquisition, 6, 12, 21, 50, 98, 103, 105, 128
        Activate, 16, 30, 33
        Activities, 95
        Adapter, 15
        Addition, 98
        Additionally, 100
        Advised, 97
        AEA, 61
        Aerial, 98
        Aerials, 96, 97, 98, 99
        AFC, 90
        AFSK, 62, 89, 97
        Alarm, 7, 21, 104, 107
        Albeit, 55, 95
        Alert, 7, 104, 108, 132
        Alt-B, 3, 24, 25
        Alt-C, 3, 24, 25
        Alt-D, 3, 24, 25
        Alt-F, 3, 24, 25
        Alt-I, 3, 24, 25
        Alt-J, 3, 24, 25
        Alt-P, 3, 24, 25
        Alt-S, 3, 24, 25
        Alt-X, 3, 24, 25
        Aluminum, 99
        Amounting, 97
        Amplifier, 97
        Amplitude, 96, 97
        AMSAT-Belgium, 56
        AMSAT-DL, 88, 94
        AMSAT-NA, 113
        AMSAT-OSCAR, 1, 2, 6, 11, 13, 46, 48, 49, 50, 51, 52, 54, 56, 57, 
          63, 64, 65, 70, 72, 87, 88, 89, 91, 92, 93, 94, 110, 111, 113, 
          114, 117, 121, 128
        Amsat-U-Orbita, 88, 89
        Amsat-U-Sputnik, 88
        AMSAT-UK, 130
        AMTOR, 131, 132
        Analysis, 1, 11, 12, 13, 100, 105, 106
        Angle, 6, 22, 42, 43, 44, 45, 46, 50, 69, 105
        AOS, 12, 21, 22, 23, 39, 50, 108, 109, 111, 128
        Apogee, 34, 41, 44, 45, 49, 54, 79, 87
        Appropriate, 99
        Aries, 44


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 137


        Assembled, 99
        Astronomy, 55, 95
        Attitude, 48, 80, 89, 98
        Automatic, 12, 22, 31, 108, 109, 119, 129, 131, 132
        Autotrack, 3, 7, 14, 23, 24, 25, 111, 129
        Averages, 96
        Axis, 6, 34, 43, 44, 45, 57, 124
        Azimuth, 22, 50

        Backyard, 95
        Balance, 99
        Ballistic, 126
        Balloon, 95
        Band, 6, 51, 53, 54, 56, 59, 70, 73, 96, 128
        Banished, 97
        Battery, 10, 46, 47, 60, 62, 65, 66, 67, 78, 82, 83, 85, 86, 87, 
          98, 101, 102
        Beacon, 1, 5, 7, 10, 12, 14, 22, 24, 36, 37, 48, 49, 57, 63, 67, 
          80, 81, 82, 83, 84, 86, 87, 89, 90, 94, 97, 102, 103, 108, 109, 
          110, 111, 116, 117, 120, 124, 131, 132
        Beacons, 63, 69, 80, 81, 89, 90
        BELAMSAT, 56
        Belgium, 56
        Bell, 95
        Block, 29, 63, 64, 81, 118
        Blocks, 1, 13, 49, 63, 95, 113, 117
        Born, 95
        BPSK, 89, 90
        Branegan, 128, 129
        Breaks, 100
        Briefly, 14
        Brought, 95, 99
        Bureau, 56
        Burnt, 97
        Button, 98

        Cables, 99
        Calls, 95
        Calm, 96
        Capacitors, 97
        Capture-to-disk, 4, 12, 13, 16, 21, 24, 31, 32, 38, 104, 105, 110, 
          119, 129
        CEDEX, 55
        Channel, 4, 8, 9, 12, 13, 14, 19, 20, 23, 31, 58, 62, 63, 64, 65, 
          66, 68, 77, 80, 81, 91, 106, 112, 113, 114, 115, 116, 119, 121, 
          122, 123, 132
        Chemical, 97
        Chenee, 56
        Choosing, 99
        Closely, 96


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 138


        Coated, 99
        Coatings, 99
        Coding, 97
        Coefficients, 58, 72, 74, 76, 113, 114
        Combinational, 98
        Communicators, 95
        Comply, 55
        Computation, 96
        Concentrated, 96
        Condition, 100
        Configuration, 1, 3, 4, 5, 6, 7, 8, 13, 14, 16, 19, 20, 23, 25, 31, 
          35, 37, 38, 54, 88, 96, 103, 104, 105, 108, 109, 112, 124, 131
        Conservatively, 97
        Constitute, 99
        Consumer-made, 97
        Cooled, 97
        Correlate, 55
        Correlation, 96
        Craft, 98
        Critchions, 56
        Culmination, 95
        Cutter, 98
        CW, 5, 36, 39, 63, 77, 78, 80, 81, 82, 83, 84, 86, 89, 90, 91, 102, 
          103, 111, 119, 120, 129
        Cycle, 55, 97
        Cycles, 98

        D'Ingenieurs, 95
        Debugged, 97
        Decametric, 95, 96
        DECAMETRIQUE, 55
        Demodulate, 15
        Des, 56
        Descending, 44
        Diferent, 3
        Differences, 14
        Digitizes, 98
        Discovered, 95
        Discoveries, 55
        Discovery, 95
        Discrete, 95
        Dish, 95
        Dissipates, 99
        Distinguished, 96
        Doppler, 1, 3, 4, 5, 7, 9, 22, 24, 30, 31, 34, 104, 108, 110, 111, 
          123, 124, 125
        DOVE, 6, 8, 15, 17, 18, 19, 30, 35, 37, 51, 52, 53, 54, 56, 57, 58, 
          60, 70, 71, 103, 104, 108, 109, 110, 112, 117, 123, 125, 128
        DOVE-OSCAR, 1, 2, 6, 11, 13, 48, 49, 53, 57, 70, 110, 111, 128
        Downlink, 11, 48, 49, 54, 55, 56, 63, 70, 80, 81, 82, 89, 90, 93, 


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 139


          96, 97
        Downlinking, 97
        DPSK, 68
        Drag, 34, 40, 41, 45
        Dynamic, 97

        Earlier, 99
        Eccentricity, 6, 34, 43, 44, 126, 127
        Eclipsed, 98, 100
        Ecole, 95
        ECOUTE, 55
        Electromagnetic, 96
        Electronique, 95
        Electrotechnique, 95
        Element, 4, 7, 9, 28, 31, 33, 34, 46, 104, 105, 107, 108, 110, 114, 
          120, 125, 126, 127
        Elements, 4, 5, 12, 19, 33, 40, 43, 45, 50, 82, 107, 108, 119, 125, 
          127
        Elevation, 6, 22, 50, 103, 105
        Emission, 96
        Emissions, 95, 96
        Emitting, 95
        Empty, 18
        Environments, 39
        Epoch, 6, 34, 43, 45, 46, 126, 127
        Equation, 58, 64, 65, 72, 74, 76, 101, 113, 114, 115
        Equations, 10, 11, 56, 57, 58, 64, 65, 70, 72, 74, 76, 78, 82, 84, 
          85, 91, 92, 100, 101, 113
        ERA, 100
        Eruptions, 96
        ESIEE, 95
        ESIEESPACE, 95
        Et, 95
        Executed, 97
        Exterior, 99
        External, 99
        Extra, 96
        Extrapolated, 96

        F-O, 89
        Favorable, 97
        FLOW, 109
        Focused, 95
        Fold, 95
        Format, 2, 4, 9, 10, 13, 14, 19, 33, 34, 37, 55, 56, 58, 62, 70, 
          77, 82, 84, 91, 92, 93, 100, 101, 105, 112, 113, 114, 116, 119, 
          121, 123, 125, 126, 131, 132, 134
        FRANCE, 55, 95
        Freed, 96, 98
        FSK, 48, 51, 61, 68, 90, 128


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 140


        Ft, 95
        Fuji, 5, 8, 17, 18, 35, 36, 37, 79, 108, 109, 112, 113, 116, 120, 
          121
        Fuji's, 113
        Fuji-OSCAR, 1, 6, 11, 15, 48, 49, 51, 54, 56, 78, 79, 80, 81, 82, 
          83, 84, 85, 86, 87, 100, 101, 102, 110, 111, 119, 128
        Functions, 98
        FX, 55, 95

        Galactic, 96, 97
        Gap, 99
        Gave, 100
        GFZ, 95
        GRAND, 55
        Grote, 95

        Hamptaux, 56
        Hardened, 97
        Hardly, 95
        HEADERLINE, 13, 20
        Hex, 12, 58, 72, 74, 76, 85, 93, 101
        Hexadecimal, 56, 58, 62, 64, 84, 112, 121
        Hides, 96
        His, 95
        Hit, 98
        Holds, 95

        Icom, 112
        Ideally, 100
        IL, 95
        Included, 95
        Independent, 99
        Influence, 96
        Instance, 97
        Integration, 99
        Intensity, 96
        Interactive, 3, 4, 12, 18, 20, 23, 26
        Interference, 96, 98
        Interprets, 98
        Investigated, 95
        Io, 96, 99
        Ionizing, 98
        Ionosphere, 96
        Irregular, 96

        Jansky, 95
        Jersey, 95
        Jovian, 95, 96, 97, 100
        Junctions, 99
        JUPITER, 55, 95, 96, 97, 99, 100


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 141


        Jupiter's, 95, 96

        KAM, 2, 15, 16, 129
        Kenwood, 1, 12, 15, 28, 34, 111
        Kepler, 6, 9, 42, 103, 105, 125
        Keplerian, 7, 18, 21, 26, 31, 33, 108, 110, 125
        KHP, 56

        L'ACTIVITE, 55
        Laboratories, 95
        Lasting, 98
        Latitude, 6, 16, 79, 103, 104
        Launch, 10, 11, 40, 79, 88, 91, 93, 95, 96, 97, 98, 125, 126, 129
        Launcher, 95, 98, 99
        Launches, 95
        LE, 55
        Lighted, 99
        Locally, 98
        Longitude, 6, 16, 103, 104
        LUSAT, 2, 71, 76, 77, 78, 108, 125
        LUSAT-OSCAR, 1, 2, 6, 11, 48, 49, 51, 54, 56, 57, 70, 76, 77, 78, 
          110, 128

        Machines, 98
        Magnetic, 56, 57, 70, 80
        Magnetometer, 70
        Manages, 98
        Mapped, 95
        Meaningful, 96
        Mechanical, 99
        Menu, 4, 5, 15, 16, 19, 20, 24, 26, 27, 28, 30, 32, 33, 34, 35, 36, 
          37, 39, 129, 131, 132
        MFILTER, 109
        MFJ, 15, 16, 36, 37, 129
        Microcontroller, 98
        Microsat, 2, 5, 14, 17, 36, 37, 46, 71, 117, 121, 129
        Military, 97
        Milky, 95
        Mode-B, 65, 66, 128
        Mode-BS, 128
        Mode-J, 69
        Mode-JD, 81
        Mode-JL, 66, 128
        Mode-L, 66, 69
        Mode-LS, 128
        Mode-S, 66, 67, 68, 69, 128
        Moderate, 99
        Modify, 99
        Moons, 99
        Mostly, 96


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 142



        Natural, 96
        Needing, 97
        NOISY, 55
        Non-regulated, 98
        Noticed, 95
        Nto, 37
        Nxhw, 55

        Offset, 1, 6, 7, 67, 85, 87, 101, 103, 105, 109, 111
        Old, 55
        Opportunities, 99
        Opportunity, 55, 99
        Orbit, 3, 4, 7, 11, 21, 23, 28, 33, 34, 39, 40, 41, 42, 43, 44, 45, 
          46, 47, 48, 49, 50, 54, 57, 61, 63, 68, 69, 78, 79, 81, 87, 88, 
          89, 95, 96, 97, 98, 100, 104, 105, 107, 108, 124, 129
        Orientation, 99
        OSCAR, 1, 10, 46, 47, 48, 56, 57, 63, 64, 78, 80, 87, 94, 95, 108, 
          118, 128, 129, 130
        Outer, 97
        Overloading, 98
        Oversized, 97

        Packet, 1, 2, 3, 5, 8, 9, 13, 15, 16, 20, 21, 24, 25, 36, 37, 38, 
          51, 53, 56, 57, 60, 76, 80, 81, 90, 95, 110, 111, 118, 119, 120, 
          121, 122, 123, 126, 127, 131, 132
        PACSAT, 2, 71, 72, 108, 125
        Page, 3, 4, 7, 8, 9, 12, 13, 19, 24, 27, 29, 58, 60, 86, 87, 109, 
          112, 113, 114, 119, 120, 121, 122, 123
        Pair, 98
        Pairs, 96, 97
        Parameter, 7, 8, 12, 16, 61, 91, 92, 93, 104, 107, 109, 112
        Parameters, 4, 7, 8, 13, 14, 16, 17, 19, 26, 37, 43, 44, 49, 56, 
          91, 92, 103, 106, 109, 116, 120, 124, 129
        Parity, 7, 12, 103, 106, 107
        Partially, 96
        Passive, 99
        Patrick, 56
        Peaks, 96, 97
        Perhaps, 55
        Perigee, 6, 34, 41, 43, 44, 45, 46, 48, 49, 69, 79, 126, 127
        Period, 21, 34, 42, 46, 49, 79, 87, 88, 95, 96, 98, 133, 134
        Perpendicularly, 96
        PgDn, 29, 32, 33
        PgUp, 29
        Photovoltaic, 98
        Pieces, 99
        Pioneer, 95, 96
        Plate, 99
        Polarizations, 97


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 143


        Powerful, 96
        Prepares, 98
        Printed, 98
        Programming, 97
        PROMs, 97
        Proper, 98
        Properly, 15
        Protected, 98
        PSK, 6, 14, 15, 48, 51, 54, 55, 59, 63, 68, 69, 73, 75, 77, 80, 81, 
          83, 84, 86, 87, 89, 92, 93, 100, 102, 111, 120, 125, 128

        QRM, 97
        QSL, 56, 100
        QSL'd, 56
        Quadratic, 58, 113
        Qualified, 97
        Quasi-constant, 99
        Quasi-polar, 97

        RAAN, 6, 34, 43, 44
        Radio, 1, 2, 3, 4, 5, 7, 10, 11, 13, 14, 15, 16, 17, 23, 27, 28, 
          31, 34, 35, 36, 37, 39, 40, 49, 51, 52, 53, 55, 56, 60, 63, 70, 
          78, 87, 88, 95, 96, 99, 103, 106, 107, 109, 111, 124, 126, 127, 
          128, 129, 130, 131, 132, 135
        Radio-electric, 95
        Radio-electrical, 96
        RADIO-M, 88
        RADIOASTRONOMIE, 55
        Ranges, 96
        Rates, 98
        Rather, 97
        Reber, 95
        Receiver, 3, 7, 12, 13, 24, 25, 34, 51, 52, 53, 54, 55, 65, 66, 92, 
          97, 98, 111, 112
        Regardless, 96
        Relates, 55
        Reliability, 97
        Removed, 99
        Rename, 16
        Repairs, 97
        Report, 100
        Reports, 56
        Results, 96
        Retrograde, 42, 43
        Risky, 97
        Rolled, 96
        Roughly, 99
        RUDAK, 66, 67, 88, 89, 90, 91, 93, 94
        Run-Time, 18



        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 144


        SARA, 5, 15, 36, 37, 55, 56, 95, 96, 97, 99, 100, 129
        SARA's, 15, 55, 56, 95, 97
        SARA-OSCAR, 6, 37, 49, 55, 56, 95
        SAT, 55, 95
        Satellite's, 99
        Saturating, 97
        Screen, 3, 12, 18, 19, 25, 29, 38, 92, 104, 109, 113, 114, 115, 120, 
          123, 132
        Security, 98
        Segment, 8, 112, 114, 116, 117, 123
        Segments, 58, 117
        Semester, 100
        Sequencing, 98
        Serve, 97
        Serving, 56
        Sheets, 99
        Shells, 99
        Shines, 98
        Shortly, 55
        Sidereal, 99
        Silent, 97
        Simplified, 98, 99
        Single-handedly, 95
        Soldered, 99
        Sometimes, 96
        Spacecraft, 1, 4, 5, 6, 7, 9, 10, 11, 12, 13, 14, 15, 17, 18, 19, 
          21, 22, 23, 25, 27, 28, 31, 32, 33, 34, 35, 36, 37, 38, 42, 43, 
          44, 45, 46, 47, 48, 49, 50, 51, 52, 53, 54, 56, 57, 58, 60, 61, 
          63, 64, 70, 72, 74, 76, 79, 80, 81, 82, 87, 89, 90, 91, 95, 97, 
          99, 100, 103, 104, 105, 108, 109, 110, 111, 112, 115, 116, 120, 
          123, 127, 129, 130
        Specifies, 98
        Spite, 98
        Statistically, 97
        Status, 1, 7, 8, 10, 12, 13, 16, 18, 20, 23, 26, 35, 57, 60, 63, 
          65, 68, 71, 81, 82, 83, 84, 85, 86, 91, 93, 101, 102, 104, 107, 
          110, 119, 120, 121, 133
        Steel, 96
        Stores, 98
        Storm, 96
        Storms, 96, 97
        Strains, 99
        Stronger, 96
        Strongest, 96
        Sub, 95
        Succession, 97
        Sun's, 96
        Superieure, 95
        Supplying, 98
        Surfaces, 99


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 145


        Sweeping, 96
        Swing, 99
        Synchronized, 99

        Telemetry, 1, 2, 3, 6, 8, 9, 10, 11, 12, 13, 14, 18, 19, 20, 23, 
          24, 31, 36, 37, 38, 48, 49, 52, 53, 54, 55, 56, 57, 58, 60, 61, 
          62, 63, 64, 65, 70, 71, 72, 74, 76, 77, 78, 80, 81, 82, 84, 85, 
          86, 87, 88, 89, 90, 91, 92, 93, 96, 97, 98, 100, 101, 102, 103, 
          106, 110, 112, 113, 115, 116, 117, 118, 119, 120, 121, 122, 123, 
          129
        Telescope, 95
        Testing, 98
        Thermally, 99
        Thick, 99
        Thier, 56
        Time-tagged, 98
        TNCs, 3, 14, 15
        To-disk, 21

        Uninterrupted, 100
        Unrolled, 96
        UO, 11, 15, 18, 22, 47, 48, 55, 95, 108, 110, 128
        UoSAT, 5, 36, 37, 55, 60, 63, 95, 108
        UoSAT-F, 95
        UoSAT-OSCAR, 1, 6, 11, 36, 46, 47, 48, 49, 50, 51, 52, 53, 54, 56, 
          60, 61, 62, 63, 70, 89, 110, 111, 118, 121, 128, 129

        Vibrations, 97
        Vicinity, 96
        Viewing, 100
        Voyager, 96

        War, 95
        WASH, 13, 58, 60, 121
        Wavelengths, 95, 96
        WEBER-OSCAR, 1, 2, 6, 11, 48, 49, 51, 54, 56, 57, 70, 74, 110, 128
        WEBERSAT, 2, 125
        WHATS-UP, 1, 2, 3, 4, 5, 10, 11, 12, 14, 15, 16, 17, 18, 19, 20, 
          21, 22, 23, 24, 25, 27, 28, 30, 31, 33, 37, 38, 39, 61, 63, 70, 
          86, 100, 103, 104, 105, 106, 107, 108, 109, 110, 111, 112, 113, 
          114, 115, 117, 118, 119, 121, 122, 123, 126, 129, 130, 135
        Wheaton, 95
        Window, 7, 12, 16, 18, 19, 20, 21, 22, 23, 26, 28, 29, 32, 33, 35, 
          39, 104, 107, 108, 110
        Wipe, 96
        WKAM, 16
        WMFJ, 16
        World's, 95
        WPK, 16
        WTNC, 16


        COPYRIGHT Joe Kasser, G3ZCZ 1991.

        WHATS-UP Index Page 146



        XFLOW, 109

        Ypou, 32
















































        COPYRIGHT Joe Kasser, G3ZCZ 1991.