miniloop v1.0
(c)1992 J Scott Hedspeth

This program provides some general information on the design
of small circular loops <small being for a circumference of
less than 1/3 lambda>.  Construction is based on copper wire
with a conductivity <å> of 5.7E7 mhos/meter and air dielectric
with a permeability <æ> of 4ãE-7 henries/meter.

Output data includes far-field E and H values in table form.
Values for E and H are Volts/meter and Amps/meter, respectively.
Angles phi and theta are measured in degrees.

For hard copy of output data, use your  <prt scrn>  function.  
Output consists of two <2> full screens.

Limited error checking is provided  =>  garbage in = garbage out!

miniloop v1.0 is offered as FreeWare.  You may use, copy and
distribute as you wish provided:

        *  this document file is included in its unmodified form

        *  no fees are charged for miniloop v1.0

Current version is be available on the ECA Systems BBS listed below
in File Area #7  Engineering and CAD.

The author will not be held responsible for any claims resulting 
from the use of miniloop for any reason.

All comments are welcome via:

        ECA Systems BBS  704-284-4854 <8N1>

        CompuServe       71042,3277

        US Mail          Rt 4 Box 227
                         Mocksville, NC 27028