This is a "freeware" version of AutoWeather for the Ultimeter
        500 and Ultimeter 2000.  It does not have all the latest
        features and fixes but is fully functional and will allow you to
        see if the program fits your needs.  If you would like the
        latest version, see the order information at the end of this
        file.

        AutoWx is in use by over 100 hams in the U.S. and is also used
        for special projects by several government sites.

        A version for the Ultimeter II is on the ARRL BBS. It's named
        AUTWX63x.ZIP




        AW2Kx.EXE     (AutoWeather 2000)
        (C) 1994,95,96 N5KOA
        VER 2.x  04/96



        INTRODUCTION

        AutoWeather 2000 is a PC compatible packet program that accepts
        weather data from the Ultimeter 2000 or Ultimeter 500 home
        weather stations and makes the data available on packet by
        directly connected requests and/or via automatic beacons (in
        APRS beacon format).  To take full advantage of AutoWx you
        should read ALL the documentation. Read the version updates at
        the end of this documentation carefully - sometimes that is the
        only hint of new features until the documentation is updated.

        AutoWeather was written to run in DOS.  The idea was for
        AutoWeather to use a minimal personal computer, including only
        640K RAM and an XT-type processor.  This should allow more
        people to leave their AutoWeather node on full-time without
        tying up their "good" computer.  I use an A/B serial switch to
        switch my tnc to my other computer if I want to do packet
        keyboarding using a communication program with more features,
        like paKet 6.1 by Tony Lonsdale (VK2DHU).  AutoWeather will
        continue to monitor and log weather data while the tnc is
        switched out as long as the Ultimeter weather station is
        attached.

        If you don't want a fulltime, stand-alone packet weather
        station, there is an alternative.  paKet 6.1 by Tony Lonsdale
        (VK2DHU) is an excellent shareware packet program and I have
        written KWeather to support paKet.  KWeather, by way of paKet's
        script facility allows remote users to access weather
        information from the Ultimeter home weather station.  Please
        remember that shareware users are expected to support by
        registering.  KWeather can also be used with pk/kaGOLD.


 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page   1


        Features of AutoWeather 2000:

            Split-screen display shows weather data, including APRS
            weather beacons from other stations, for past 40 minutes on
            bottom - packet on top.

            Creates binary log files compatible with the Ultimeter Data
            Display software.

            Displays Hi/Lo Temperatures and Hi Wind with the time of
            day.

            Records and shows the highest wind speed for each 5 minute
            interval.

            Indicates pressure change; rising, falling or steady.

            Shows Hi/Lo Barometer for the day

            Allows packet stations to connect and request current
            weather conditions, including rain, and highs and lows for
            the date and longer terms.

            Indicates rainfall for hourly, daily, monthly and annual
            periods.

            Sends weather beacons in APRS format.

            Logs weather beacons from other AutoWx or APRS stations.

            Creates ASCII text file showing highs and lows for the date.

            Serves as a simple packet terminal program.

            Runs on a minimal computer system
        

        AutoWx assumes that your computer has COM1 and COM2
        serial ports available.  One must be used for the tnc and
        the other for the Ultimeter.


        Thanks to the many users of AutoWx around the country who have
        offered suggestions, comments and compliments!  A special thanks
        to Mr. Bill Peet at Peet Bros. for providing a "loaner"
        Ultimeter 2000 for software development because I gave the
        AutoWx program away and couldn't afford an upgrade.


 
 
 
 
 
                                          Page   2


        STARTUP / CONFIGURATION Parameters


        The following describes the setup necessary to begin using
        AutoWeather:


        The Ultimeter 2000 MUST be in COMPLETE RECORD LOGGING mode prior to
        starting the AutoWeather program.  Press and hold (CLEAR + RAIN)
        keys for three seconds.  Also, if you have a rain guage
        attached, make sure the Ultimeter display reflects the
        appropriate measurement:  10ths or 100ths
        
          ---------------------------------------------------------------
        = THE ULTIMTSR PROGRAM SHOULD NOT BE USED WHILE AW2K IS RUNNING  =
          ---------------------------------------------------------------

        The tnc must be in terminal mode - not KISS or HOST mode.
        ECHO should be ON, AUTOLF OFF, CSTAMP ON and MAXUSERS 1. If you
        are running a very slow 8088 machine, see the Tips section.

        Upon starting AutoWx the first time, you must enter some
        configuration parameters.  They are listed here along with
        information to help you identify the proper responses:

        The COM port of the TNC must be identified as (COM) "1" or "2".
        The other COM port will automatically be assigned to the
        Ultimeter 2000.  AutoWeather does not support COM3 or COM4 at
        this time.

        Supported baud rates for the TNC port are: 1200,2400,4800 & 9600
        If you need a different baud rate supported, contact me for a
        custom version.

        Your station's latitude and longitude are necessary to beacon in
        a format recognized by the Automatic Packet Reporting System (APRS
        by WB4APR). There is very little error validation in the entry
        of the coordinates so be very careful that they are entered in
        the format shown at the config prompt.  Null entries at the
        Latitude and Longitude prompts will result in "0000.00N" and
        "00000.00W".  The entry for 31d 52m 40s North would be 3152.66N

        A temperature adjustment value is included because the Ultimeter
        2000 temperature sensor can, in rare cases, be affected if
        additional lengths of cable are attached to it.  The default
        value for the temperature adjustment is 0 which will be correct
        if the display on the U-2000 is correct.

        If you prefer, you can have weather data displayed in METRIC
        values.  Kilometers-Per-Hour for wind, temperatures in Celsius
 
 
 
 
                                          Page   3


        and rain in millimeters.

        When prompted for the Log File Name, your entry should NOT
        include an extension.  The extension .LOG is automatically
        added.

        After the configuration information is entered, it is written to
        the ASCII file 2KWX.CFG.  The .CFG file is an ASCII text file
        and is pretty self-explanatory.  You can view or edit it to make
        changes as long as you adhere to proper syntax.

        If you want Month-To-Date and Year-To-Date rainfall amounts to
        be indicated, you must manually create a plain text data file
        named YTD.DAT.  You can quickly create this file from DOS using
        the command:    COPY CON YTD.DAT<enter>
                        1.2<enter>
                        3<enter>
                        <ctrl-z><enter>

        This example assumes MTD rain at 1.2 inches and YTD at 3 inches.
        (Note that the COPY CON command cannot be used to edit the file
        - only to create a new file.)  If you don't create YTD.DAT and
        place it in the AutoWx directory only current rainfall amounts
        will be transmitted.

        You should also include information in the tnc CTEXT to instruct
        users how to access the weather information.  For example, 
        include in your CTEXT something to the effect of,

        Type //WX for weather information.   //Bye to disconnect...

        Don't forget to turn CMSG ON so that users see this CTEXT when
        they connect.  

        One more thing... check and/or set your computer's time clock
        with the DOS Date and Time commands.  AutoWx will use both and
        the Ultimeter clock should be set at least 30 seconds slow or
        your computer clock should be set at lease 30 seconds fast.
        Otherwise, AutoWx may read the peak windspeed immediately after
        the Ultimeter resets it to zero each five minutes.

        At this point, AutoWx should be ready and running.  Other users
        can connect for weather information, the bottom half of the
        display will begin showing weather values every five minutes and
        values will be logged to the binary log file.  If that's not the
        case, see the Trouble Shooting section near the end of this
        documentation.  If you've made an error in the configuration
        entries, it may be easier to delete the file 2KWX.CFG and start
        over than to try and figure out how to make corrections.

 
 
 
 
                                          Page   4


        A list of available commands and functions are available on-line
        by typing ALT-H.




 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page   5


        WEATHER NODE (connected requests)

        A connected packet station can send any of the valid commands:

        //WX  for current weather values
              The response from AutoWeather will be:

                03-18-1996            15:53
                      TEMP  62.9 F
                        HI  64.3      15:19
                        LO  39.6      06:46
                  WIND  NW  12.9 MPH
                    HI NNE  27.7 MPH  10:20
                 BAROMETER  30.07s
                RAIN TODAY   0.00
                      YEAR   0.30
                AutoWx Ver 2K2.7


                If you have the optional outdoor humidity sensor
                attached, the response will also include humidity and
                dewpoint.

                If you are using the Ultimeter 500, which has no
                barometer, the BAROMETER line will be omitted.

                If you have not created the YTD.DAT file, the
                Year-to-date rainfall will be omitted.

                If you have toggled the WxNode OFF with ALT+X, the
                remote user will see the response:
                     "Wx information temporarily unavailable..."


        //yes   for yesterday's weather values.
                The AutoWeather response will be:


                Yesterday's weather...

                   HI Temp   73.9 F        13:55
                   LO Temp   45.7 F        07:29
                Hi Wind ENE  17.8 MPH  13:21
                   RAIN       0.0
                AutoWx Ver 2K2.3


        //bar   for the barometer values
                The AutoWeather response will be:

 
 
 
 
                                          Page   6


                3 hour Barometer change is -0.08 inHg.
                Hi is 30.18 inHg at 10:50
                Lo is 29.84 inHg at 00:00

                The Hi and Lo values are for today.  See the Ultimeter
                documentation for details on the 3-hour change.

        //long  for the long-term weather values
                The AutoWeather response will be:

                Long Term Hi's/Lo's...

                   HI Temp   91.8 F      14:10   02/21/1996
                   LO Temp   14.1 F      06:30   02/03/1996
                Hi Wind  W   43.7 MPH    16:23   02/18/1996
                   Hi Barom  30.70 inHg  01:07   03/08/1996
                   Lo Barom  29.49 inHg  17:49   03/17/1996
                Hi Rain       0.3                03/21/1996
                AutoWx Ver 2K2.7c

                (yes, these are actual values in West Texas)

                See the Ultimeter documentation for details on how to
                clear and/or set the long term values.

        //help  to send the contents of the optional HELP.AWX file
                If you have the optional HELP.AWX file present in the
                AutoWeather directory the connected user can send //HELP
                to see the contents of that file.  (If the file is not
                present, the user will see the message:  "No help
                available..."

                The HELP.AWX should be kept as short as possible,
                especially considering that a user may be connected via
                a network or several digis.  The sample HELP.AWX file on
                the distribution disk should be edited to reflect your
                own callsign and any other information specific to your
                station if you plan to use it.

        //BYE    to disconnect

        Commands can be entered in upper or lower case and anywhere on
        the packet line.  AutoWeather must see the *** CONNECTED TO
        message before considering the // commands valid.

        While a station is connected, the weather Beacon is suspended.
        Also, if UPDATES are OFF (ALT-U) a connected user will see the
        message, "Weather data temporarily not available...".
        
        The last ten stations that connected can be viewed by pressing
 
 
 
 
                                          Page   7


        the PgDn key.   (You MUST have CSTAMP turned on to see the
        Connect Log with PgDn.)
        
        If you enter a "greeting" with ALT-G, the message will be sent
        to connected users immediately after the CTEXT (if any) is
        transmitted.   You might use this to notify users to check the
        mailbox for bulletins, etc.  Remove the greeting message by
        entering a null response to the ALT-G prompt.


        DISPLAYS and FUNCTIONS

        The hi's and lo's for the current date are displayed in the
        status line at the bottom of the screen.

        ALT+B toggles the APRS beacons ON/OFF.  When toggled ON the
              user is prompted for the time interval and any message to
              be appended on the end of the beacon.  The status lines at
              the bottom of the screen will indicate whether the beacon
              is OFF or ON and, if ON, will show the interval.

              Beacons can also be turned off/on and interval selected
              remotely with the //BEACON and //BT commands documented
              elsewhere in this text.

        ALT+C will copy the WX.HST, xxxx.LOG, and WX.ERR files to floppy
              disk drive A: (or drive B: if you started AutoWx with the
              /B: switch).  There will be no WX.ERR file unless an error
              is generated from within AutoWx.

        ALT+D will "shell" to DOS.  This function allows you to perform
              some DOS commands.  Type EXIT at the DOS command prompt to
              return to AutoWeather. It will take a few seconds for the
              Ultimeter data stream to be read and parsed so be patient.
              Shelling to DOS may cause "bad things" to happen, Man.
              Don't make a habit of using it.  Just quit AutoWeather for
              your DOS tasks unless they are very brief and require very
              little memory.

        ALT+G allows you to enter a one-line Greeting message.  This
              message will be sent immediately after any CTEXT message.
             
        ALT+H will display a Help Window

        ALT+L will display long term values

        ALT+M does various things.  Among them are:
                Sends the TNC.AWX file to the tnc.  If you happen to be
                connected or in CONVERSE mode at the time ALT+M is
                pressed, you will have to manually return to the
 
 
 
 
                                          Page   8


                CONVERSE mode after the TNC.AWX file is sent to the tnc.
                This is because AutoWeather will send a CTRL+C before it
                reads the TNC.AWX file. IF YOUR TNC IS ONE THAT WILL
                REACT VIOLENTLY TO THE CONTROL-C CHARACTER, DO NOT USE
                ALT+M

                Edit the TNC.AWX file to be sure that it contains only
                commands that are valid for your tnc.

                This function also causes AutoWeather to forget that a
                station is connected.  This means the beacon will beacon
                at it's pre-determined time (if it's turned on).

                Generally you should not use ALT+M while a station is
                connected.

        ALT+R inhibits the logging of rainfall amounts to the binary log
              file and causes a -1 to be displayed with each update.
              This feature is pretty useless right now because the
              rainfall amounts are not logged anyway.  See the ERRORS
              section later in this document.

        ALT+S clears the scroll back buffer

        ALT+T causes an APRS beacon to be sent immediately.  If beacon
              is ON, the interval timer will be reset.

        ALT+U Toggles UPDATES ON/OFF.  I forgot why I put this in but it
              will stop logging to the screen and to the binary log
              file.  As a matter of fact it's probably useless except to
              cause problems somewhere.

        ALT+W turns on Weather beacon logging.  That means that any APRS
              or AutoWeather weather beacons seen will be logged in the
              bottom half of the display and to a plain text file named
              WX.LOG

        ALT+X will toggle the WxNode function OFF/ON as indicated at the
              bottom of the screen.

        ALT+Y will display yesterday's information in a pop-up window.

        ALT+Z will allow you to change the time on your computer.  It
              was originally a programmer tool I used to test with and
              it was (and still is) pretty primitive.  I did find it
              handy though so I decided to leave it in.

              You MUST enter the time in the format indicated (no
              commas, colons, etc.) and if you enter a time prior to the
              current time, it might cause the AutoWx update to wait for
 
 
 
 
                                          Page   9


              24 hours.  (If in doubt, quit and then restart
              AutoWeather.)

              A null response to the prompt leaves the time unchanged.

        PgDn will show the last ten stations that connected to you if
             you have CSTAMP turned on.

        PgUp will display the last few pages of screen.  Press the
             ESCape key to abort the display.
                            
        All screens called or popped up for functions will return to the
        main AutoWeather screen after a period of time or you can press
        any key to return to the main screen.  (Except when in the
        scroll back screen.)

        I just realized that some of these functions were present but
        never documented in earlier versions.  Oh well...
                               
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  10


        LOGGING

        AutoWeather also maintains a binary log of weather conditions
        for every five minutes.  This feature was necessary because the
        Terminate-Stay-Resident software that is available with the
        Ultimeter (ULTIMTSR) does not share the serial port.  In other
        words, if you are running the TSR and then try to read the
        serial port with another program, the TSR quits logging.
        Besides, if you want to keep the log up-to-date, you have to
        leave your computer on all the time.  Running a dedicated
        computer for the weather and sharing it with other packet users
        makes more sense.

        The log file will be named whatever you specified during the
        configuration of AutoWx.  It can be read, exported or
        graphically displayed with the Data Display software available
        from Peet Bros.  (You can also read U-II log files with the
        U-2000 display software.)

        At midnite on the last day of each month AutoWx will create a
        new log file.  The old log file will be named MMYY.LOG where MM
        = month and YY = year.  Log files can be appended by using the
        DOS Copy command as it applies to binary files.  For example, to
        combine the monthly files 0196.LOG and 0296.LOG into a new file
        named 2MOS.LOG, use the DOS command:

                        COPY /b 0196.LOG+0296.LOG 2MOS.LOG

        The original files are not altered.  After March, you could add
        the 0396.LOG file to create 3MOS.LOG using:

                        Copy /b 2MOS.LOG+0396.LOG 3MOS.LOG

        See your DOS manual for more details on combining binary files.

        The U-2000 Data Display program assumes that all log entries are
        at five minute intervals.  Therefore, if you suspend logging for
        more than a couple of minutes, the Data Display program will be
        reading data that was logged after the time displayed in the
        Data Display program.  For example:  If you suspended the logger
        with ALT-U at 10:28 and did not resume logging until 10:58, the
        Display program will show the data logged at 11:00 as if it were
        logged at 10:30 and there will be thirty minutes of no data at
        the end of the day.

        If you plan to NEVER use the log files you can delete it/them as
        often as you like.  Just remember... NEVER is a long time; you
        might change your mind someday.  Besides,  you will probably get
        a year's data on a 360K floppy so the log files don't take up
        much disk space.
 
 
 
 
                                          Page  11



        NOTE:  The logging of data to the log file is suspended if you
               toggle Updates OFF (ALT-U).




 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  12


        APRS Beacons

        When an AutoWx user beacons in APRS format all local APRS
        users will see the AutoWx station on their maps just as
        if the AutoWx user was running APRS.  You MUST include APRS in
        your tnc UNPROTO parameter. (i.e.  UNPROTO APRS VIA DIGI1)
        The beacon will be digi'd through any valid path specified in
        the UNPROTO tnc parameter. UNPROTO should be set to APRS or to
        APRS VIA xxxx in order to be identified by stations running
        APRS.

        The APRS beacon format is:

                /Txxx = current temperature
                /Rxxx = Rain since top of the hour
                /Pxxx = Current rainfall total (as indicated by the
                        Ultimeter 2000)
                /Bxxx = Barometer
                /Hxxx = Humidity ( ... if no sensor attached)

        Automatic beacons can be toggled ON/OFF with ALT-B. When Beacon
        is toggled ON, the user is prompted for the interval (in
        minutes;  default = 30 minutes) and for any text to be tagged on
        the end of the weather data.  The Beacon time will be in the
        nearest 5-minute increment regardless of the value entered;  for
        example, if you enter 9 minutes, the actual beacon time will be
        10 minutes.  Beacons are transmitted only when the log file is
        updated.

        The beacon will automatically include the Longitude and Latitude
        from the config file.   If you enter text to be appended to the
        beacon (Btext), it will be limited to 30 characters.

        The Beacon can be forced to xmit immediately by typing ALT-T.
        After using ALT-T, the beacon timer (if Beacon is ON), restarts.

        The Beacon can be turned off/on remotely with //BEACON.  Make
        sure that you have the correct path specified in UNPROTO prior
        to turning the beacon on.  The default time for beacons turned
        on REMOTELY is 20 minutes.  You can change this by starting
        AutoWeather 2000 with the /RB switch.  You will be prompted for
        the new interval.  The new time will remain in effect until the
        program is stopped.

        If you enable Weather Beacon Logging with ALT-W the program will
        capture any monitored APRS-type weather beacons and save them to
        an ASCII text file named WX.LOG.  While Weather Beacon Logging
        is enabled, an asterisk (*) will appear to the left of the UPDATE
        status at the bottom of the screen.  Weather Beacon Logging may
        not be compatible with slower 8088 class computers and/or you may
 
 
 
 
                                          Page  13


        have to use a slower baud rate to the tnc.  (See Tips)

        AutoWeather also looks for the APRS command string ?WX? when you
        are monitoring other packets.  If this weather query is detected
        AutoWeather will send an APRS beacon automatically.  This can be
        disabled by starting AutoWeather with the /NOWX switch if you do
        not want AutoWeather to respond to APRS weather queries.

        AUTOWEATHER USERS MUST INCLUDE "APRS" IN THEIR UNPROTO COMMAND
        FOR THEIR BEACONS TO BE LOGGED BY APRS AND/OR AUTOWEATHER.


        APRS is a map-based packet program by WB4APR, Bob Bruninga,
        Annapolis, MD


        
        UPDATE


        An "update" occurs when the program is started, every five
        minutes, and when a connected (//WX) request is received.  When
        a timed update occurs (every 5 minutes), the data is logged to
        disk.  The U-2000 data is read continuously and logged to disk
        every 5 minutes.  Whenever the data is updated, it is also
        printed on the lower portion of the screen.  Updates can be
        toggled off with ALT-U but this will also disable the logging of
        data to the log file.  If you are going to disconnect or
        otherwise disable the weather input, toggle the updates off with
        ALT-U to keep the program from hanging up during the update
        sequence.  While the UPDATEs are toggled OFF, connected requests
        for weather (//wx) will receive a message stating that "Weather
        data is temporarily unavailable...".

        When UPDATE is toggled off, the timer is not reset; when UPDATE
        is toggled back ON, if the programmed time (5 min.) has passed
        while UPDATE was OFF, the update will be performed immediately.

        

        
        RAIN

        There is no setting in AutoWeather 2000 for rain gauge
        increments.  If you have the gauge that measures in 100ths, set
        your Ultimeter 2000 for that measurement.  The Ultimeter 2000
        allows you to set rain measurement on the keyboard.  See your
        U-2000 instruction manual.

        Rain amounts, in tenths of an inch, are beaconed in the /R000
 
 
 
 
                                          Page  14


        (hourly) and /P000 (daily) format.  The hourly amount is
        calculated from the top of the hour.  (Beacons show rain in
        10ths inches even if you have the 100ths rain gauge.  100ths are
        rounded up to the nearest 1/10th.

        Updates on the screen show the amount of rain since the top of
        hour along with the amount of rain for the day in the format:
        (hour ->)  0.00 / 0.00  (<- day)

        Connected weather requests (//WX) show hourly, daily, and
        optionally, month-to-date and year-to-date rainfall.


        
        TERMINAL Mode

        If you use the program as a packet terminal to connect to other
        stations, temporarily turn the Beacon OFF (ALT-B).  If UPDATEs
        are left ON, the logger will continue to log data and the lower
        half of the screen screen will continue to receive updated data
        every five minutes without interferring with your keyboard QSO.
        The program will ignore the //wx request if you disable it with
        the ALT-X toggle.



        For the older Ultimeter II, use AutoWx.EXE as available on the
        ARRL BBS.  Look for AUTWXxxx.ZIP where xxx indicates the version
        number.  (Search for AUTOWX or ULTIM)  As of January 1996, the
        older program is probably AUTWX63.ZIP.

        The Ultimeter can be used with paKet 6.1 or the pk/kaGOLD
        programs with my KWeather.exe program.   If you received AutoWx
        from me, the KWeather program and documentation are included on
        your disk.




 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  15


        NOTES:

        AutoWeather 2000 is released for the use by other licensed
        amateur radio operators and no payment or registration fees are
        required although donations are accepted and appreciated. The
        program is copyright protected and I choose to retain all rights
        to the code.  AutoWeather 2000 may NOT be distributed with any
        commercial merchandise without written permission from the
        author.
        
        







        Ultimeter home weather stations are products of Peet Bros., Inc.
        Peet Bros. is not affiliated with the author of AutoWeather 2000
        and does not warranty or promote the use of the program.  (In
        other words, don't blame Peet Bros. if AutoWeather does not work
        like you think it should.  They have been very supportive of my
        project and of the ham population in general.  They have offered
        help and encouragement for amateur applications beyond that of
        any other home weather station manufacturer.)

 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  16


        Errors/Bugs and other annoyances...

        As of this release the logging of rain to the binary log file
        is disabled.  Apparently a bug in the Peet Bros. Data Display
        software inhibits the correct display of rain data and causes
        incorrect readings of other values when rain is logged.

        If you start AutoWeather 2000 WITH A FLOPPY DRIVE, make sure the
        startup floppy is in it's drive all the time.  If the diskette
        is not in it's drive when the write buffer is flushed the
        program will endlessly loop.   Also, do not attempt to use the
        ALT-C copy feature when running from a floppy; the log file is
        already on the diskette and a file cannot be copied onto itself!

        HF transmissions can interfere with the U-2000 and bad data can
        be passed to the AutoWeather program.  The use of an rf filter
        is highly recommended.  (A 30 db filter is available from PEET
        BROS.)  AutoWeather 2000 attempts to detect and discard invalid
        data before it is displayed or logged however, the long term
        values in your Ultimeter can be wiped out by rf.

        The National Weather Service calculates wind speed using a
        2-minute average of sustained wind.  AutoWeather 2000 records
        the highest wind speed during a 5-minute period.  The HI
        WindSpeed indicated by AutoWeather 2000 is closer to a "gust"
        windspeed if you want to be technical.

        I don't particularly like Windows myself but many users have
        indicated they use or plan to use AutoWx under windows.  I have
        included an icon, aw2000.ico and a .PIF file.  If you create an
        effective .PIF file, send it to me and I'll include it on the
        distribution disks.  I find it interesting that AutoWx runs well
        on an XT but really drags down a 386-40mHz running Windows 3.1
        What does that tell you?



 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  17


        TIPS

        
        If you use the TNC Command that inhibits the display of incoming
        characters while you type (FLOW), turn it off.  Better yet, make
        sure you hit the ENTER key the last thing after using your
        keyboard. After hitting ENTER the cmd: prompt should appear on
        the screen to let you know that there are no characters in the
        tnc buffer.

        Turn off your computer monitor and leave it off when not sitting
        at the keyboard.  (The screen will burn in the image of the
        weather data over time.)

        Import the WX.HST file to a database program and create custom
        statistical reports and graphs.  The WX.HST file is easy to
        import as a "comma-delimited ASCII file" into most popular
        database programs and many spreadsheet programs.

        If a BBS in your town supports modem connections, consider
        leaving your weather node on the BBS frequency (or a gateway
        port) so the node can be accessed by telephone, too.

        An ASCII error log file (WX.ERR) is created if an error is
        generated by AutoWeather 2000. If this file appears in your
        directory you can look at and/or delete it. Just make sure it
        doesn't get big enough to eat up disk space.

        Use BUDCALLS and BUDLIST to minimize traffic on the screen.
        This is highly recommended if you are running an 8088 computer
        and want to leave MONITOR ON.  Even callsigns that are not
        included in the BUDCALLS will can still connect to you (at least
        on the Kantronics tncs - I'm not sure about others).  For
        example, if you want to monitor only the local packet stations
        that are sending APRS weather beacons, include them in the
        BUDCALLS and set BUDCALLS to FROM or BOTH.  You'll see their
        beacons and anybody else can connect to AutoWx and get weather
        info. Using BUDLIST also maximizes the use of the
        "scrollback/review" buffer.  Connected users can leave msgs or
        notes for you while they are connected and you can scrollback
        through to read them.

        If you use a plain text file named HELP.AWX do not include the
        // commands in their unique syntax.  When the HELP.AWX file is
        sent, AutoWeather will see the command as a request to send
        information.  See the sample HELP.AWX for format.

        The plain text file TNC.AWX should contain only valid tnc
        commands.  See the sample TNC.AWX file.

 
 
 
 
                                          Page  18


        The UPDATE.DOC file has details on how to get the latest version
        of AutoWx by phone modem.

 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  19


        Log File Notes

        The binary log file is much like the one created by the
        Ultimeter Data Logger and is very efficient.  You can probably
        get a whole year's data on a 360K floppy.  The AutoWX program
        must run for at least ten minutes before any useable data is
        logged.  Also, starting and stopping the AutoWX program before
        any useable data is logged can cause errors in the display.  The
        Peet Data Display program reads a file header in the log file to
        determine the starting date and time but all data entries
        between headers are assumed to be in five minute intervals.  The
        AutoWX program writes a new date/time header each time it starts
        but if logging is suspended by the ALT-U toggle, the data may
        miss the 5 minute interval and therefore be incorrectly
        displayed by the U-II Data Display program. If the logger is
        suspended for more than 10 minutes, quit the AutoWX program and
        restart it to avoid the problem.  Although data may be missing
        for the suspended period, the data logged will be displayed with
        the correct time if you follow this procedure.

        If you want to build up same data fast but don't care if it's
        accurate, start AutoWx and then change the computer time after
        every update.  For example: start AutoWx at 13:03, then after an
        update, change the time to 13:09.  At 1310 another update will
        occur and be logged.  Then bump the time up 4 minutes again,
        etc.  Be sure to set the clock back to the correct time when you
        finish experimenting.  You can use ALT-Z to change the time.


 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  20


                          AutoWeather 2000 Quick Guide



    ESC   Clear Screen
   PgDn   Show last 10 connected stations
   PgUp   Scroll back buffer for packet screen (?)


ALT - B   BEACON on/off
ALT - C   Copy data files to Floppy
ALT - D   Shell to DOS
ALT - G   Enter GREETING message for additional "connect text"
ALT - H   Help Window
ALT - L   Long Term display
ALT - M   Initialize TNC with TNC.AWX
ALT - Q   Quit
ALT - R   Inhibit rain logging - (no effect in this release)
ALT - S   Clear scrollback buffer
ALT - T   Xmit Beacon
ALT - U   UPDATES off/on
ALT - W   Wx Beacon logging  (shows * near UPDATE when on)
ALT - X   Wx Node off/on
ALT - Y   Yesterday's display
ALT - Z   Check/Set TIME clock

Startup Options:

        /B:   Copy data files to DRIVE B: instead of DRIVE A: when
              using ALT-C

        /NOWX Inhibit the AutoWeather response to ?WX? from APRS users

        /RB   Change remote beacon time    (default = 30)

Files:

        2KWX.CFG  AutoWeather 2000 configuration data.

        WX.HST  Data file showing Hi's/Lo's for each date

        WX.ERR  Data file created only if program generates an error.
                (This file can be deleted at any time.)

        #5  - Illegal function call      #64 - Bad file name
        #11 - Division by zero           #68 - Device unavailable
        #24 - Device timeout             #69 - Communications-buffer overflow
        #55 - File already open          #71 - Disk not ready
        #57 - Device I/O error           #72 - Disk media error
        #61 - Disk full                  #75 - Path/File access error
        #62 - Input past end of file
 
 
 
                                          Page  21


       2KWX.LOG  Data file of any APRS beacons recorded from other
               stations.  (MONITOR must be on)
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  22


Help

PROBLEM:  When I start AutoWx, it says it can't see my Ultimeter on the
          COM port.

SOLUTION: Look at the 2KWX.CFG file and verify that TNC=COM1
          or TNC=COM2.  If the tnc is on COM1, the Ultimeter must be on
          COM2 (and vice-versa).


PROBLEM:  I see nothing but BAD DATA errors.

SOLUTION: The Ultimeter has to be in Complete Record mode.  Maybe you
          changed modes at the Ultimeter display.  Set it back to Data
          Logging Mode.  (CLEAR + RAIN)


PROBLEM:  My display shows "-1" every time the weather info updates in
          the bottom half of the screen.

SOLUTION: You have toggled the Rain Ignore switch.  Toggle it back with
          ALT-R.  While the Rain Ignore is toggled on, AutoWeather
          inhibits rain logging by the Ultimeter to the binary log
          file.


PROBLEM:  When I use PgDn to see the last ten connected stations, there
          is nothing there.

SOLUTION: Make sure the CSTAMP (or equivalent) parameter is
          ON.  AutoWx looks for the date and time in brackets ([]) to
          identify a connected station's callsign.  If there is no Date
          and Time in brackets with the ***CONNECTED msg, there will be
          nothing in the PgDn list.  (If you are using a tnc that does
          not use the square brackets around the date & time, let me
          know and we'll fix it in AutoWx.)


PROBLEM:  When I start AutoWx I see the weather data but I can't seem to
          control my tnc.

SOLUTION: The tnc MUST be in terminal mode - not KISS or HOST mode.  Run
          a terminal program such as ProComm or QModem to verify correct
          operation of the tnc.  You should see the cmd: prompt if the
          tnc is in terminal mode.  Make sure the baud rates of AutoWx
          and the tnc match.


PROBLEM:  When I try to type in my CTEXT to say: TYPE //WX for WEATHER
          The program keeps trying to send the weather information and
          messing up my screen.
 
 
 
                                          Page  23




SOLUTION: Hit ALT-X and try again.  Then turn the weather node back on
          with ALT-X when you finish entering your CTEXT.  (Weather node
          status is noted at the bottom of the screen.)  At version 2.7,
          the tnc must be CONNECTED to another station or // commands
          are ignored.

PROBLEM:  I am sending the weather beacon but APRS users are not seeing
          me on their map.

SOLUTION: Make sure your tnc UNPROTO parameter begins with "APRS". (No
          quotes, of course.)  Example: APRS V DIGI  This will cause the
          beacon to digipeat thru DIGI with the required syntax to be
          recognized by APRS stations.

PROBLEM:  I want to leave AutoWx running to keep my binary log file up-
          to-date while I run APRS but APRS uses Data Logging Mode and
          AutoWx uses Complete Record Mode on the Ultimeter 2000.

SOLUTION: AW2K1s.EXE is now included on the distribution disk.  This
          version of AutoWx uses the Ultimeter's Data Logging Mode.
          With two data cables (using a telephone duplex plug) you can
          run APRS and AutoWx at the same time, maintaining the binary
          log file.  (AW2k1s is an early version of AutoWx 2000 and does
          not include all the features of the 2k2_ versions but does do
          logging.)



                  

        Les Blalock, N5KOA    lcb911@apex2000.net
        1711 Pagewood
        Odessa, TX  79761
        (915) 332-7112 day
              332-1942 fax
              367-0408 eve  after 6 pm CST












 
 
 
 
                                          Page  24


Ver 2k2.x   Uses Complete Record Mode
      2.2   Fixed duplicate display of Barometer
            Added //BAR
      2.3   Added //YES
            Write WX.HST with other files upon ALT-C
            ALT-S clears scollbak buffer
            Minor tweaks
     2.4   Fixed the accumulated .04 rain amounts in /Rxxx
                  and displayed as hourly rain.  Added following:
                     //YES shows yesterday's data  (ALT+Y at keyboard)
                     //BAR shows 3-hour pressure change
     2.5    Fixed barometer values in binary log file
            Show f/s/r on barometer relative to last 5-minute value
            Minor tweaks
     2.6    Fixed APRS windspeed value (was 10x in first couple
            of copies sent out)
            Added today's Hi/Lo Barometer on //BAR
     2.7    Sends the contents of TNC.AWX to the tnc when you hit ALT+M
            Place a valid tnc command on each line with a plain text
            editor.  If you have problems, delete the TNC.AWX file from
            the AutoWx directory.
     2.7a   Fixed Barometer display in APRS beacon
            Fixed temperature rounding error in APRS beacon
     2.7b   Added HELP.AWX file for //HELP
     2.7c   Added //LONG and ALT+L
            Fixed Yesterday's Wind Direction
     2.7d   More accomodations for no barometer on Ultimeter 500 output
     2.7e   Fixed some rounding errors
     2.7f   Fixed APRS beacon - rounding of rainfall
            Fixed logging of U-II type beacons
            Fixed display of multiple ///'s in APRS beacons
     2.7g   Tweaked beacon logging routine
            Tweaker other parsing routines
     2.7i   A cleaned up (inside) version of 2.7g-gb

 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                          Page  25




The latest version of AutoWx is available for a $20 registration fee.
Registration ensures that you get the latest version of AutoWx and the
related Ultimeter programs and files.  Along with AutoWx, you will
receive:

KWeather - This program allows users to access the Ultimeter if you are
running paKet 6.1 or the ka/pkGOLD terminal programs.

WxRead - If you do not have the Peet Bros. Data Display software, this
program will read and export the binary log file created by AutoWx
and/or the Peet Bros. ULTIMTSR program


Some of the newest features of AutoWx include:

        Users can leave messages
        An integrated file viewer
        Remote status function
        Rain logging has been fixed
        APRS beacon logging has been cleaned up considerably





Les Blalock, N5KOA
1711 Pagewood
Odessa, TX  79761