MOSH.DOC
       ---------------------------------------------------------------------
			     MOSH vers. 3.2, May 1996 
			      In QBX Basic Compiler          
				       by
			       SM6KFY PETER HULTHE
				     Address
			     ***  Packet Mail  ***
			    SM6KFY @ SK6YW.O.SWE.EU
			      ***  Snail Mail ***
				    Box 5014
			 426 05 VŽSTRA FR™LUNDA, SWEDEN
       ---------------------------------------------------------------------
       With thanks for the timer routines to: 
		*** Esko Lehtinen, ELogik Company in Gothenburg, Sweden.
       With thanks for revising the English to: 
		*** G0OIK Peter King in Flamstead, Great Britain.
       ---------------------------------------------------------------------
 
       This programme was written to control the rig when sending CW to my
       friend Peter/G0OIK. With this program your concentration can be
       directed towards producing a good chat, while the machine takes over
       routine keying.
 
       It was made to be as short and simple as possible, and was intended to
       be run from DOS. It is possible to use a very simple PC, but a hard 
       disk makes life easier. 
       It is not recommended to be run from any integrated environment like 
       Windows, Windows 95 or OS2. Only with DOS it gives the very exact 
       timing of the Morse code that it was constructed for. It is possible 
       to run a very fast CW with this programme.
 
       With a PC and a tape recorder it is possible to make your own CW
       training tape. You can also practice the code with any text written in 
       standard DOS formate.
 
       When sending or receiving with your rig, you simply write on the
       keyboard. You can always (and as well as that) go over to the CW key
       whenever you like. What you write on the keyboard is stored in the
       log-file, which you can save or not at the end of your session as
       you like.
 
       There are many nice CW programmes written. This is an attempt to make
       a new one for all those who want a simple but efficiant programme,
       filling the gap between the most basic and the more complicated
       programs.
 
       ---------------------------------------------------------------------
 
       The head programme (MOSH.EXE) will automatically read the text file
       (MOSH.CFG) during start-up.
       By making changes in MOSH.CFG with a text editor (like the EDIT
       supplied by DOS 5.0 and higher) you are able to make your own MOSH.
       Points 1 - 12 will show what can be done.
 
       1.  Define your own characters (like national characters, KN etc.).
	   22 of the more seldom used keys (like {, (, ], [ etc.) can be
	   programmed to your own "Morse" code.
 
       2.  Set the CW-parameters to your own taste.
	   The length of Dits, Dahs and delays can be programmed, making
	   your Morse code personally coloured.
 
       3.  The default speed setting is done by MOSH.DEF.
	   Speed can then be adjusted up/down with the Left/Right arrows
	   or be set to "normal" by Home.
	   With some PC:s older than the 286, the speed will not always be
	   correctly reported on the screen. A calibration can then be done.
 
	   For a calibration of speed, adjust to a reading of 15 wpm (words
	   per minute). Then run the file PARIS. To do this, hold down the 
	   ALT key and type "F". You will then be presented with a list of 
	   files. Enter the file name "PARIS". The word "PARIS" will be sent 
	   in CW to your loudspeaker 10 times.
	   The 10 "PARIS" should take exactly 44 seconds. With some older
	   PC:s, the wpm reading may prove to be a little slower speed than 
	   15 real wpm. If this is the case you may chose a higher wpm figure 
	   and make a note of the difference.
       
       4.  The loudspeaker sound frequency is determined by the MOSH.CFG
	   file, but it can also be changed when running the programme. The
	   Up/Down arrows will increase/decrease the frequency in steps by 
	   200 Hz for each touch. If the frequency is too high to the 
	   loudspeaker, you will not be able to hear it, but the rig will 
	   still be controlled.
	   PgUp and PgDn give 20 kHz resp. 200 Hz.
	   With End on your keyboard, the frequency is brought back to the
	   normal (default) value again.
 
	   The loudspeaker is stopped/started with the Del key. In the
	   silent mode the rig is not affected by typing on the keyboard,
	   but the "silent text" will be stored in the log-file (if used).
	   This is a way to use the computer as a typewriter, during the
	   reception of CW or before a session, to make personal notes of
	   frequency, QRM level etc.
 
       5.  Define short standard texts to be sent using the shift/function
	   keys from within the MOSH.CFG file.
	   Up to 12 different messages ("quickies") can be programmed.
	   You may define the texts as you like. Max. length is 255
	   characters. Here some proposals:
 
	   Shift/F1  : Own call-sign key
	   Shift/F2  : A commonly used counter-station
	   Shift/F3  : A short call to the commonly used counter-station
	   Shift/F7  : CQ-call
	   Shift/F10 : Over-and-out
	   
	   There are three "computer signs" that can be used when writing 
	   these short standard texts. Their use will add a time of day 
	   indication in the log.

	   By holding down the right hand ALT on the keyboard and typing 157
	   on the numerical keypad you will produce a funny "Y" sign. When 
	   used at the end of the text, this will produce the K (Over-anyone 
	   to answer) code in CW, and also leave a time mark in the log.
	   Using ALT and 158 gives something like "Pt", producing a KN (Over- 
	   specified station to reply only) again with a time mark in the 
	   log.
	   ALT/159 gives a "Ÿ", and is used to produce a time mark only, 
	   and will not give any audible code.

       6.  Define the directory name for texts to be sent from, floppy or
	   hard disk. The directory for these texts should be defined in the
	   MOSH.CFG file.
	   Files of up to 10 Kb of text can be sent in any speed you choose.
 
	   ALT/F is used to send a text from floppy or hard disk, as was
	   explained in 3. above.
 
	   Texts you want to send can be written using the normal EDIT
	   function under DOS and be stored under any legal filename.
 
	   If you want to stop the text sending, press Esc to quiet it.
       
       7.  Define directory names for the log file and files to send. 
	   You may have a log-file generated after using MOSH. The file will 
	   be placed in a directory you may choose in MOSH.CFG.
       
       8.  The choice of COM-port is the last parameter in MOSH.CFG.
	   It is good to have a COM-port dedicated only to MOSH, but it is 
	   possible to combine the controlling of MOSH and other hardware 
	   using the same port.
 
       9.  Also some other details are controlled by MOSH.CFG (like the
	   colours of the written text on the screen, messages etc.).
 
	   If you try to run MOSH32.EXE without the MOSH.CFG it is possible,
	   but some useful functions will not be present. Please note that
	   the two files must be kept in the same directory.
 
       10. Other options in the programme are some special keys:
 
	   The BackSpace key produces a series of Dits (short signs). It
	   writes "Rub" on the screen and a text "RubOut" in the log-file.
 
	   The keyboard buffer can be deleted (made empty) by Ctrl/Pause if
	   you want to rub out what is yet not sent. The Ctrl/Pause is
	   sometimes very valuable to use for deleting mistakes. Please try
	   to remember it and use it!
 
	   The Ctrl/K key writes a "K" on the screen and in the log-file,
	   and makes the "K" Morse code. It also gives a time-mark in the
	   log-file for the next time a key is pressed.
 
	   The Ctrl/O (not the figure!) writes a "Kn" on the screen and in 
	   the log-file, makes the "KN" code plus a time-mark in the log-
	   file.
 
	   The Ctrl/T gives a time-mark in the log-file next time a key is
	   pressed.
 
	   The Ctrl/U writes "Ok!" on the screen and in the log-file and
	   makes the Understood code (...-.). Also the exclamation mark "!" 
	   can be used for that.
 
	   Ctrl/R clears the screen.
 
	   Alt/L locks the key ON (for aerial tuning purpose). Another Alt/L
	   (or any character key) will unlock it.
 
       11. To send small texts in Beacon mode.
	   The Alt/B key starts/stops the beacon function, where you define
	   own beacon text and beacon delay. Max. length is 80 characters.
	   The standard texts can be used as beacons.
	   One word of warning: This function may be illegally used if you
	   lack a beacon permission and use it for on air transmission.
 
       12. To stop the programme.
	   The programme can always be stopped using ALT/X (also Esc works).
 
 
       Help with the programme is always available with the F1 key (also
       Alt/H). The Help Menu can always be consulted during the running of
       the programme. There is no need to "escape" from help, just carry
       on typing.
 
       ---------------------------------------------------------------------
 
       Interfacing hardware.
 
       There are two ways of interfacing the computer to the rig.
 
       
       A. The loudspeaker method.
       
       To make a simple tap of the PC:s loudspeaker and to have the audio
       converted into a conducting path will probably work well. An 
       optocoupler (OC) is excellent for a job like that.
       An OC is a light emitting diode (LED) and a photo transistor, housed 
       in the same case, looking like an IC, often having 6 legs.
       
       The LED part (legs  1 - 2) is connected to the computer's loudspeaker 
       via a 150 Ohm resistor. A 33 nF capacitor is connected across the LED 
       terminals of the OC. The TL 111 and 4N25 OC:s were tried.
       The transistor part of the OC (legs 4-5 are used, the emitter and
       collector terminals) is connected to the rigs' key connections in such 
       a way that the key current will flow through the transistor of the OC 
       when the LED is lit by the loudspeaker current. A 1 nF capacitor 
       across the key terminals is used to reduce any leaking RF energy.
       This arrangement has worked well with an old XT and a 486 in my
       shack, together with a Yaesu FT101ZD and an ICOM IC735.
       However, with some PC:s and some rigs there can be problems. 
       The generating of sound is not standardized within the PC concept. If 
       the sound signal is too low, or if a polarizing voltage appears at the
       connectors to the loudspeaker, an extra transistor before the OC may 
       be needed. I have recently tried a Victor 286 which demanded for that 
       solution.
 
       It maybe found with some older rigs that a transistor may be required 
       between the rig and the OC. Connect the OC leg 4 to the base of the
       transistor and the OC leg 5 to the collector (Darlington connection). 
       The key connectors are then wired to the emitter and collector of the
       transistor (only one polarity works!).
 
       
       B. The COM port method.  
       
       An easy way to interface the PC to the rig is to use one of the 
       COM-ports (sometimes called RS-232, or serial ports). They are male 
       25 pin or 9 pin connectors at the rear of the PC, used for mice and 
       modems. As it is good advice to electrically separate the PC from the 
       rig I have been using an opto coupler to let the PC control the key
       line.
       TxD found in the COM-port is a connection used for data transfer.
       It is pin 2 in the 25-p or pin 3 in the 9-p D-sub. Ground (GND) is
       pin 7 in the 25-p or pin 5 in the 9-p D-sub. TxD is at about -12 V
       negative with no tone present. When a CW tone is produced by MOSH, the 
       TxD will go to a positive potential of +12 V on most PC:s. With some 
       PC:s (particularly lap-tops) the potentials are lower (mostly + and 
       - 5 V), but this should not change the function. 
       
       Connect TxD to the OC LED anode (pin 1) via a diode and a 2.2 kohm 
       resistor. Connect the OC LED cathode (pin 2) to GND of the COM port. 
       There will be a flow of about 5 mA from TxD to GND through the LED, 
       when a CW tone comes. This will make the OC transistor conduct. 
       For many rigs this conductance is enough to produce a sufficient key 
       current to switch the rig into transmit mode. 
       If not, a second transistor can be tried, making a Darlington stage 
       together with the OC transistor. If also this fails, the voltage 
       between the key terminals is not sufficient to supply the transistor. 
       Then a 3 V external voltage in series with a 1 kohm resistor can 
       help.
       A capacitor of 0.1 uF is likely to be placed over the LED legs of the 
       OC, and one of 1 nF over the transistor's legs to the rig's key line.
       
       The above methods have all been tried, and have solved all related
       problems I have been faced to up till now.

       It has been observed that the the interface used for HamComm (by
       DL5YEC) can use the same RS-232 port as MOSH. It will then be
       possible to use any of the two programmes to control the CW keying
       function, with the same opto-coupler CW interface.
 
       ---------------------------------------------------------------------
       SUMMARY OF CONTROL FUNCTIONS:
 
       Arrows Up/Down       -Raise/Lower audio freq' from the PCs loudspeaker
       PgUp                 -Highest setting, 20 KHz, gives quiet sending)
       PgDn                 -Lowest  setting, 200 Hz)
       End                  -Default setting of audio freq'
 
       Arrows Left/Right    -Increase/Decrease speed of CW
       Home                 -Default setting of CW speed
 
       Delete               -Toggles between TX/RX. (In TX what is typed is
			     sent, in RX what is typed is not sent, but is
			     recorded in the Log-file).
 
       Backspace            -Sends error character and writes "Rub" on
			     screen.
 
       Ctrl/K                Sends "K" (-.-) & makes time mark in log.
       Ctrl/O               -Sends "KN" (-.--.) & makes time mark in log.
       Ctrl/T               -Makes a time mark in the log.
       Ctrl/R               -Clears the screen.
       Ctrl/U  !            -Sends "Understood" (...-.) & writes "OK" in 
			     the log.
       Ctrl/Pause           -Clears the buffer and so stops sending.

       Shift/F1             -Sends pre-defined texts (like a CQ-call or what
       ---                   you may have chosen.
       Shift/F10
 
       Alt/B                -Starts/Stops beacon mode.
       Alt/F                -To send pre-written text files.
       Alt/H                -Shows help screen.
       Alt/X                -Exits the program.
 
       F1                   -Shows the help screen.
 
       Esc                  -Stops the sending of text files
			    -Also exits the program when no text file is
			     being sent.
 
       ---------------------------------------------------------------------
 
       This programme is FREEWARE. It allows you to use it as much as you
       like, as long as you want.
 
       If you find any errors, please tell me about them!
       And if you have got any bright idea about changes, don't
       forget to drop a few lines to me about that!


       73 de SM6KFY / Peter