This is version 1.30 of KAMterm.  Due to my lack of G-TOR capability
here, the G-TOR code is UN-TESTED.  According to the documentation from
Kantronics, I'm sending the right escape sequences, but I always like to
see it work for myself....  If anyone does find any problems with the
G-TOR code, please do let me know about it.

The following new features are added:

1) In the ``send immediately'' mode (i.e., each character is sent to the
   TNC as it is typed), a '@' at the beginning of a line will cause you
   to switch to the normal input mode for the remainder of that line,
   allowing you to use @amtor, @pactor, etc., commands in the
   immediate-input mode.

2) @amtor, @pactor, etc., commands supported in function key
   definitions.  Basically, anything that starts with an '@' is
   assumed to be a macro of some sort.  If it isn't a function key
   macro, as such, it is passed to the keyboard input routine based
   on the assumption that it's a shortcut command.

3) New function key macro:  @filemac --- allows multiple function key
   macros, lines of text, etc., to be put in a file.
   USAGE:  @filemac filename
   LIMITATIONS:  cannot have nested @filemac commands, still a limit
   of 79 chars / line.

4) Not a feature, as such, but a definite improvement:  now, when you
   record a conversation to a file, the stupid ``and thus spoke''
   nonsense is replaced with a simple >>callsign<< notation.

5) Added PACtor HF Specials to HFSPECIALS (Alt-S) menu that, for some
   reason, do not appear to have made it into versions 1.15--1.22.

6) Added G-TOR support with the following:
   *) New HFSPECIALS menu option for G-TOR 300 baud
   *) New HF specials function key definition:  GT300BAUD
      USAGE:  @hfspecials gt300baud
   *) Other PACtor HF specials stuff now for G-TOR, too

NOTE:  Binary-mode support for G-TOR didn't make this release---I
       need more documentation than I have right now, so that's on
       hold for another release....