Pacsat Protocol Upload Processor for the AEA DSP1232/DSP2232
     ____________________________________________________________


(C) Copyright by ABAX BVBA, Belgium, 1993. All Rights Reserved.

This software may be used and distributed free-of-charge by radio-amateurs or
SWLs in the course of amateur radio communications. It may not be sold nor
used for any non-amateur purpose without written permission from ABAX.

This software was written by Andre Marchandise, ON1AIG in cooperation with
AEA - Advanced Electronic Applications.


================================================================================
    __Version_Info__ * %n - V1 R02 M%v - Date %d *
* PG_AEA.DOC - V1 R02 M16 - Date 1-Nov-93 *
================================================================================



1. Introduction

        This software was especially written for the AEA DSP-1232/DSP-2232.
        It uses the features of this magnificent machine as much as
        possible. This results in a more reliable uplink then ever
        before possible.

        The program is developed using C and a commercially available
        communications package.


2. Copyright

        (C) Copyright by ABAX BVBA, Belgium, 1993. All Rights Reserved.

        This software may be used and distributed free-of-charge by
        radio-amateurs or SWLs in the course of amateur radio communications.
        It may not be sold nor used for any non-amateur purpose
        without written permission from ABAX.

        This software was written by Andre Marchandise, ON1AIG.


3. Packing List

        This package consists of the following :


        1. PG_AEA.EXE    : The Pacsat Upload Processor.

        2. PG_AEA.DOC    : This documentation

        3. PG_AEA16.TNC  : The file that get's uploaded to the DSP-UNIT
           PG_AEA22.TNC    at the beginning of the program.
           PG_AEA23.TNC
                           This file comes in three versions,
                           AO-16, UO-22 and KO-23.
                           Pls copy them to different directories.
                           Then rename PG_AEAxx.TNC to PG_AEA.TNC for
                           each of the three files.

        4. PG_AEA16.CFG  : Configuration file, whith COM-port, baud rate,
           PG_AEA22.CFG    etc.
           PG_AEA23.CFG
                           This file comes in three versions,
                           AO-16, UO-22 and KO-23.
                           Pls copy them to different directories, in
                           such a way that the PG_AEAxx.CFG is in the
                           same directory as the corresponding
                           PG_AEAxx.TNC file.
                           Then rename PG_AEAxx.CFG to PG_AEA.CFG for
                           each of the three files.


4. Installation


        First, PKUNZIP the PG_AEA.ZIP file.


        Install the program ( PG_AEA.EXE ) and the accompaning
        DOC-file ( PG_AEA.DOC ) in the directory where your other
        satellite programs reside.

        Now make sure the PG_AEA16.CFG and PG_AEA16.TNC end up in a
        separate directory for AO-16. The same applies for
        PG_AEA.22.CFG and PG_AEA22.TNC ( UOSAT5 ) and PG_AEA23.TNC and
        PG_AEA23.CFG ( KITSAT1 ).

        Make sure you rename the PG_AEAxx.CFG and PG_AEAxx.TNC to
        PG_AEA.CFG and PG_AEA.TNC respectively.

        Check your .BAT files and replace any reference to the
        original PG-program with PG_AEA.
        Users of SAS or Satsked will probably have to rename
        PG_AEA.EXE to PG.EXE, because the executable is called
        directly by another program.



5. Running the program


        Run the program by typing "PG_AEA" ( without the double quotes ! )
        at the DOS-prompt. ( or if you've renamed PG_AEA.EXE to
                                PG.EXE, you must type "PG" ).


        After being started, the program first looks in the current
        directory to see if there are files to upload. It will look
        for files with extension .OUT ( not uploaded yet )
        or with extension .PUL ( partially uploaded ).
        If there are no such files, the program will exit.

        Next the program initializes the TNC, by sending the file
        PG_AEA.TNC.  IT IS NOT RECOMMENDED TO ALTER THIS FILE IN ANY
        WAY, unless you know exactly what you're doing !!

        The program immediately tries to connect the satellite, as
        specified in the PACSAT PROTOCOL Suite Guidelines.

        There is a time-out function of 120 sec. during the procedure
        set-up, that will only start after receiving the first
        OPEN-packet from the satellite. During DATA-upload, the
        time-out is set to 360 sec.

        Upon receiving the ESC-key from a program like STUFFIT, the
        program will exit ( SatSked ).

        The program makes sure to reset the parameters that were
        altered, upon leaving the program.



6. Support of DSP PORT 2

        If you want PG_AEA to support DSP port 2, you should add the
        following statement to the PG_AEA.CFG file :

                DSPPORT 2


        Do not forget to alter the "MODEM"-statement in the
        PG_AEA.TNC-file to support a Port 2 modem ( modem 28 replacing
        modem 18 ).

        Also check the other statements in your PG_AEA.TNC-file to
        make sure they support port 2.
        Example :

                Using "FULLDUP ON" will only set DSP PORT 1 to fulldup.
                Instead use either :

                        FULLDUP /ON     ( only DSP PORT 2 in fulldup )

                or

                        FULLDUP ON/ON   ( recommended ).


7. Compatibility with other programs ( SAS, Satsked, .. )

        The best way to avoid any compatibility problems, is to rename
        your original PG.EXE in PG_UOS.EXE and then rename PG_AEA.EXE to
        PG.EXE. I guess it is best to leave the original PG.CFG, PG.TNC, ...
        in place, because some programs test for their existence.

        Remember that PG_AEA.EXE ( now renamed PG.EXE ) uses
        PG_AEA.CFG and PG_AEA.TNC. So DON'T RENAME them to PG.CFG/PG.TNC.



8. If you like the program, please leave a message on KO-23 ( preferred )
   or on AO-16 ( regularly checked ).




9. In case of problem

        If you're having a problem with the program, documentation,
        config files or whatever pls. feel free to contact the author :

        Andre Marchandise
        ON1AIG
        AX.25 : @ ON7RC.BT.BEL.EU
        SAT   : @ KO-23 & AO-16 (QRT UO-22)
        CIS   : 100272,1644