comTAP Serial Data Cable Specification


You must connect pins 3 and 7 (DB-25 version) or 2 and 5 (DE-9
version) to monitor data.  The cross connections from DTE: 22-20 and
DCE: 22-4 (DB-25 versions) or DTE: 9-4 and DCE: 9-7 (DE-9 versions)
are optional but recommended, as they support automatic device
detection.  Connect the shells labeled DTE and DCE to the MONITORING
computer.  The horizontal cable at the bottom of the diagram connects
the two devices under test and should be a normal RS-232 cable.
Remember, if you are connecting two DTE devices with the RS-232
cable, you must include a null modem converter or swap pins 2 and 3
at one end of the cable.


                         Monitoring Computer Shells


                        DTE                       DCE
                  Monitoring Port           Monitoring Port
                     Connector        |        Connector
                                      |
       DE-9     9     2     5     4   |    9     2     5     7
                                      |
       DB-25   22     3     7    20   |   22     3     7     4
                |     |     |     |   |    |     |     |     |
                +-----|-----|-----+   |    +-----|-----|-----+
                      |     |         |          |     |
                      |     |         |          |     |
                      |     |         |          |     |
                      |     |         |          |     |
                      |     |         |          |     |
                      |     |         |          |     |
                      |     |                    |     |
         2 -----------+-----|--------------------|-----|--------
         3 -----------------|--------------------+-----|--------
         4 -----------------|--------------------------|--------
         5 -----------------|--------------------------|--------
         6 -----------------|--------------------------|--------
         7 -----------------+--------------------------+--------
           Connect the two devices under test with this standard
           RS-232 cable. The monitoring tap connectors hook to
           a separate PC with two serial ports. Monitoring is
           passive - we do not use pass-through - so that timing
           of the transmissions is not affected in any way.




   
   Connections support data only; signal information is not included.


                              Pinout List
                             -------------

                         DE-9  |  RS-232  |  DB-25
                ---------------+----------+----------
                           9   |     x    |    22
                DTE        2   |     2    |     3
                           5   |     7    |     7
                           4   |     x    |    20
                ---------------+----------+----------
                           9   |     x    |    22
                DCE        2   |     3    |     3
                           5   |     7    |     7
                           7   |     x    |     4