This is the readme for ODINSUP.COM.

ODINSUP  COM    33867 02-23-93  8:58a version 1.22

Modification History:

 Changes from v1.01 to v1.10 beta

	1. Enhanced to run with Lan Manager 2.0 and 2.1.  These changes made
           to allow code to run with MicroSoft's NetBeui Protocol Stack.
           Use new NET.CFG parameter BUFFERED.

	2. Enhanced to allow detection of 386 MicroProcessor for better
           performance.

 Changes from v1.10 beta to v1.21

        1. Enhanced ODINSUP.COM driver from 1.0 NDIS spec to NDIS v2.0 spec.

	2. Fixed a bug in a code path where a variable lacked a CS override.
	   Symptom seen (under a heavy load to the AS/400 (ethernet) using 
           PC/SUPPORT the machine would either hang or drop the 
           AS/400 connection).

Changes from v1.21 to v2.22

	1. Changed the way ODINSUP registers as a default protocol stack.  
	   The previous method could cause a potential problem if another 
           default protocol stack registered with the Link Support Layer.


PURPOSE OF ODINSUP.COM:

As part of Novell's commitment to be interoperable, ODI supports NDIS. ODI's
modular architecture allows users to support support NDIS protocol stacks.
A module called ODINSUP.COM allows NDIS protocol stacks to run unmodified
over the ODI LSL and talk to an ODI LAN driver.  Now, multi-vendor network
transports like IBM's NetBEUI, DEC's LAT or 3COM's XNS can be run over a 
common Dat-Link (driver) specification.  For more information, read the 
ODIINFO.DOC file included in this .ZIP file.
 

DETAILED DESCRIPTION

This section gives a brief discussion on how to install and configure the   
ODINSUP modules.  
  
All NDIS MAC Drivers should be replaced on the node with their corresponding
ODI LAN Drivers.  For example, if you were currently using the ELNKII.DOS 
NDIS MAC Driver you would now use the 3C503.COM driver.
  
Installation of the ODINSUP module is simply a matter of installing it in
memory.  In DOS this is accomplished by loading ODINSUP.COM either at the
command line or in a batch file.  

Note that the NDIS PROTMAN device driver must be loaded before the ODINSUP
module is loaded.  
  
Configuration of ODINSUP is accomplished by adding statements to the system
NET.CFG file as outlined below.  ODINSUP only needs to be loaded once since
it can handle multiple ODI LAN Drivers from the same module memory image.
  
The NDIS PROTOCOL.INI file is still necessary to tell the NDIS Protocol(s)
which MAC it should bind to and use.  Normally all PROTOCOL.INI information
for NDIS MAC drivers can be removed.  No ODINSUP specific information is 
necessary in the PROTOCOL.INI file.  
  
At this time ODINSUP will only support Ethernet and Token-Ring compatible
ODI LAN Drivers.  ODINSUP requires that the underlying Ethernet or
Token-Ring ODI LAN Drivers have a number of frame types enabled.  For 
Ethernet ODI LAN Drivers the ETHERNET_802.2, ETHERNET_SNAP, and ETHERNET_II
frames types must be enabled.  For Token-Ring ODI LAN Drivers the TOKEN-RING,
and TOKEN-RING_SNAP frames types must be enabled.  Enabling frame types is 
accomplished by specifying the frame keyword under the appropriate ODI LAN
Drivers section header.  For example:  
  
Sample NET.CFG commands showing enabling of frame types:
  
      link driver ne1000  
             frame ethernet_802.3  
             frame ethernet_802.2  
             frame ethernet_snap  
             frame ethernet_ii  
  
If no binding information is present in the NET.CFG, ODINSUP will attempt to
locate an Ethernet or Token-Ring ODI LAN Driver.  If found, ODINSUP will
attempt to bind to it.  Support for more than one ODI LAN Driver or the need
to explicitly specify which ODI LAN Driver to bind to is accomplished by 
placing binding information in the NET.CFG.  ODINSUP can be bound to a 
maximum of four ODI LAN Drivers.  
  
If the default action of ODINSUP is not desired, binding information should
be placed in the NET.CFG to tell ODINSUP which ODI LAN Drivers it should
bind to.    

Bind entries specify the name of the ODI LAN Driver and optionally the   
instance number.  The name of the ODI LAN Driver is normally the name of 
the ODI LAN Driver's file (e.g. NE1000 for NE1000.COM).   The instance
number may be necessary in cases where more than one type of adapter is
installed in the node (e.g. Two 3C523 adapters).  If an instance value is
not specified, ODINSUP will default to the first ODI LAN Driver found
(e.g. If two 3C523 adapters were present, ODINSUP would bind to the first
loaded instance of the ODI LAN Driver). The lowest instance value is 1.
 
  
Sample NET.CFG commands under DOS showing assignment of the instance number:
  
  protocol ODINSUP  
     bind ne1000   ;Bind to the first instance of the NE1000 ODI LAN Driver
     bind 3c523 2  ;Bind to the second instance of the 3C523 ODI LAN Driver
     bind token 1  ;Bind to the first instance of the TOKEN ODI LAN Driver
 

OTHER SAMPLE FILES

AUTOEXEC.BAT:
  
      lsl  
      3c503  
      ODINSUP  
  
      ...Load NDIS Protocols if not loaded in CONFIG.SYS  
  
      netbind  
        
      ...Load ODI Protocols  
  

The PROTOCOL.INI must specify sections for each NDIS protocol used.  Part of
this information is the Bindings statement which specifies which NDIS MAC(s)
the protocol should bind to.  The name specified should be the name of the
ODI LAN Driver (e.g. NE1000, TOKEN, NE2, etc.).  If the ODI LAN Driver's
name starts with a number (e.g. 3C503) the MAC name to use for the Bindings
statement must be preceded with the letter 'X' (e.g. X3C503).   When an
adapter instance other than one is used (e.g. ODINSUP bound to second NE1000
ODI LAN Driver) the MAC name has the instance number appended to the end of
the ODI LAN Driver's name (e.g. NE10002 for second instance, X3C5234 for
fourth instance, etc.). The appropriate MAC names are displayed when ODINSUP
is loaded.  
  
  
PROTOCOL.INI file showing binding instructions:
  
       [PROTOCOL_MANAGER]  
             DriverName = PROTMAN$  
  
       [ETHERAND]  
             DriverName = DXME0$  
             Bindings = NE2  
  
             ; Bindings = x3C523  
             ; Bindings = ne22          ;for second instance NE2 Board  
  
  
Normally, DOS ODI modules are unloadable.  Since NDIS does not provide a 
dynamic interface for its protocols and MACs the ODINSUP.COM module is NOT 
unloadable. Since it must be loaded after the LSL.COM and ODI LAN Drivers
(e.g. NE1000.COM), these modules are not unloadable (i.e. LSL.COM and ODI
LAN Drivers are not unloadable).  The ODI protocols should be loaded after
NETBIND.EXE and the NDIS protocols have been loaded.  This will allow the
ODI protocol modules to be unloaded.  
  
ODINSUP.COM after installation consumes approximately 4900 bytes of DOS 
memory.  Each additional adapter ODINSUP is bound to will increase memory 
usage by approximately 2800 bytes.  The size of the installed LSL and ODI
LAN Driver usually take about the same amount of memory as the corresponding
NDIS PROTMAN and NDIS MAC Driver.  Using ODINSUP instead of a NDIS MAC
Driver incurs an additional 4900 bytes of memory usage, but this will vary
depending on the LAN Driver used.    
  
Limited performance comparisons were made using the 3Com EtherLink II 
adapter. A performance comparison using the native NDIS ELNKII.DOS MAC Driver
and the ODI 3C503.COM and ODINSUP.COM was performed.  It was found that both
setup's provided the same performance results, i.e. use of the ODINSUP module
incurred no performance penalty.  Use of other LAN Drivers may show different
results.   
  

COMMON QUESTIONS/ANSWERS ABOUT THE ODINSUP DRIVERS:


Q1.    The ODI driver I am using is from a third party company.  It doesn't
       appear to be working properly.  The ODI drivers from Novell run great. 
       What questions do I need to ask the developer?  The error message I am
       getting is "MLID does not support receive data size parameter. Call
       adapter manufacturer and request a newer MLID that supports it." or 
       something similar.

A1.    The developer must use version 1.2 or better of the MSM (Media Support
       Module) from Novell when creating the ODI driver.  The MSM used must
       support the "L Data Size in the Look ahead structure".  Version 1.2 of
       the MSM was shipped to third party developers in Sept of 1991.

Q2.    When I run NETBIND.EXE, I get the message, "PRO0025E: Failed to bind."
       What's wrong?

A2.    This message can be caused by a bad Bindings= statment in the
       PROTOCOL.INI file.  First, the PROTOCOL.INI file must reside in the 
       path given in the /I: parameter on the line referencing the PROTMAN 
       driver.  Then, the statements in the PROTOCOL.INI file must be correct.

Q3.    I only have an NDIS driver for my third party NIC card.  Will it work
       with ODINSUP?

A3.    No, the Novell ODINSUP solution requires that an ODI driver be written.

Q4.    What topologies are supported?

A4.    Ethernet and Token-ring.

Q5.    Can I route my NDIS application packets across a Novell Router.

A5.    No, Novell router only passes IPX packets.  The stacks below
       are obviously not IPX packets.

Q6.    I'm trying to communicate with LAN Manager (or other NDIS service) which
       is on the other side of a Novell router, but I can't get there.  Why 
       can't I get across a Novell router using ODINSUP?

A6.    A Novell router will only route packets for protocols which are loaded
       on the router.  Since ODINSUP interfaces to the NDIS protocol being
       used, the packets on the wire are not necessarily supported on the
       router.  Currently, only IPX and TCP/IP protocols are provided and
       supported by Novell.

Q7.    OK.. What are some examples of common configurations that have been
       seen to work?

A7.    The following examples of customer configurations are reported to  
       work successfully although most have not been tested by Novell.  You 
       may want to test the NDIS application you are using before putting the 
       configuration into production.  For many customers ODINSUP has 
       solved the NDIS business need.


SAMPLE DETAILED ENVIRONMENT-SPECIFIC CONFIGURATIONS

*****************************************************************************
****  Novell NetWare and AS/400 ethernet ************************************
*****************************************************************************

You can also use SAA 1.2 or better from NOVELL without having to use IBM lan 
support, odi drivers, or ODINSUP. 

The following is a working configuration of ODINSUP.COM ODINSP.ZIP
and AS/400 PC/SUPPORT 2.1 ethernet connectivity remote booting with
SMC cards (also known as Western Digital cards) with WD boot proms. 

 1. Use Lan Support version 1.25 from IBM for DXMA0MOD.SYS and
    DXME0MOD.SYS.
 2. Use SMCPLUS.COM 17385 2-13-92 or better.  Older versions of the ODI
    driver did not have the 1.2 MSM (Media Support Module linked in).


AUTOEXEC.BAT:

echo off        
prompt $p$g 
cls        
lsl    
smcplus  
ipxodi 
odinsup 
netbind          
netx  
f:       
Login
Startpcs


CONFIG.SYS:

files=30 
buffers=30 
device=protman.exe /I:A:\ 
device=dxma0mod.sys 001 
device=dxme0mod.sys 
device=EIMPCS.SYS P=0
device=ECYDDX.SYS FILES=8 DRIVES=2


NET.CFG:

protocol ODINSUP 
     Bind SMCPLUS 

Link Driver SMCPLUS 
     Frame Ethernet_802.3 
     Frame Ethernet_802.2 
     Frame Ethernet_II 
     Frame Ethernet_snap 
     Protocol IPX 0 Ethernet_802.3 


PROTOCOL.INI:

[PROTOCOL_MANAGER] 
    DriverName = PROTMAN$ 
  
[ETHERNET] 
    DriverName = DXME0$ 
    Bindings = SMCPLUS 


***************************************************************************
******* Novell NetWare and Banyan Vines ***********************************
***************************************************************************

AUTOEXEC.BAT:

ECHO OFF
PROMPT $P$G
lsl
ne2000
odinsup
ban /nc
ndisban
ipxodi
netx
f:login supervisor
c:
redirall
z:login admin@eng@testing


CONFIG.SYS:

files=20
buffers=20
DEVICE=c:\banyan\protman.dos /I:c:\lanman
lastdrive=E


NET.CFG:

LINK DRIVER NE2000
  INT 2
  PORT 320
  FRAME ETHERNET_802.3
  FRAME ETHERNET_SNAP
  FRAME ETHERNET_II
  FRAME ETHERNET_802.2

PROTOCOL ODINSUP
        BIND NE2000


PROTOCOL.INI:

[PROTOCOL_MANAGER]
    DRIVERNAME=PROTMAN$

[VINES_XIF]
   DRIVERNAME=NDISBAN$
   BINDINGS=NE2000

   
NOTES:  1. Run BANYAN PCCONFIG.EXE, Select NDIS ethernet card settings.

	2. SETHAND.EXE (available from BANYAN) must be run against
   	REDIRALL.EXE to decrease the amount of file handles used by BANYAN'S
   	REDIRALL.EXE. Decrease file handles from 255 to 200 (200 representing
   	the highest numbered file handle assigned by VINES.  You must have
   	the right version of SETHAND that works with the version of
   	REDIRALL.EXE that you have.

        3. The shell is loaded last (REDIRALL.EXE or NETX.COM) will be the 
   	shell that will have the drive mapping for any given letter.  For 
   	example: if you are using M: for a netware mapping and NETX.COM was
   	loaded after REDIRALL.EXE you can not use BANYAN SETDRIVE to map M:
   	to a BANYAN DRIVE.


***************************************************************************
******* Novell NetWare and IBM Lan Server *********************************
***************************************************************************

SAMPLE DOS ethernet IBM LAN SERVER and Netware 3.11 ODINSUP SOLUTION 
(using ODINSUP.COM dated 2-27-92 or better).

NOTE: It is REQUIRED TO load NETX AFTER NET START and CALL INITFSI.BAT.


AUTOEXEC.BAT:

prompt $P$G
lsl
ne2000
odinsup
NETBIND
NET START
CALL INITFSI.BAT
ipxodi
netx
n:


CONFIG.SYS:

device=c:\protman.exe
device=c:\dxma0mod.sys 001
device=c:\dxme0mod.sys
device=c:\dxmt0mod.sys S=12 C=14 ST=12 O=N
files=40
buffers=40
SHELL=C:\command.com /E:2000 /P
LASTDRIVE=M


NET.CFG:

Protocol ODINSUP
        Bind NE2000

Link Driver NE2000
        Int 5
        Port 360
        Frame Ethernet_802.3 
        Frame Ethernet_802.2 
        Frame Ethernet_II 
        Frame Ethernet_snap
	Protocol IPX 0 Ethernet_802.3


PROTOCOL.INI:

[PROTOCOL_MANAGER] 
    DriverName = PROTMAN$ 
  
[ETHERNET] 
    DriverName = DXME0$ 
    Bindings = NE2000

 
***************************************************************************
********* Novell NetWare and Microsoft Lan Manager ************************
***************************************************************************

NETWARE and MICROSOFT LAN MANAGER 2.0 and 2.1 requires ODINSUP.COM version
1.10 or better on the DOS client.  The BUFFERED parameter must be used in 
the NET.CFG.
 
In DOS the user must be using an LSL.COM that is version 1.10 or higher.  
MLIDs must be linked with v1.20 or higher of the Ethernet or Token-Ring MSM 
modules, i.e. Drivers which support the added LDataSize Field in the LookAhead 
structure, are capable of supporting ODINSUP.COM. 
 
Since the mapping between ODI and NDIS is not 1 to 1, a few functions in the 
ODINSUP module do not completely comply with the NDIS MAC specification.  It 
is not expected that any of these will create situations where certain NDIS 
Protocols will not work with ODINSUP since most protocols do not use these 
MAC capabilities. 
 
ODI Ethernet MLIDs provide a maximum of 128+14+3+5 bytes of receive look ahead 
data when doing a receive operation.  ODI Token-Ring drivers provide a maximum 
of 128+14+18+3+5 bytes of receive look ahead when doing a receive operation.  
NDIS specifies that MACs must support up to 256 bytes of receive look ahead.  
Therefore, NDIS protocols needing more than the stated maximums above will not 
work with ODINSUP unless the new switch BUFFERED is added to the NET.CFG file 
for ODINSUP.  The figures above are  derived as follows: 
 
     128   Bytes of Data. 
     14    Size of a 802.3 or 802.5 MAC Layer Header. 
     18    Maximum size of Source Routing field in Token-Ring. 
     3     Size of an 802.2 Type I Header. 
     5     Size of a SNAP Protocol ID Field. 

There is now a detection mechanism if a look ahead size larger than 128 bytes 
and the maximum media header (e.g. Ethernet is 22 bytes) is requested.  An 
error message is printed and the user asked to insert the new keyword 
"BUFFERED" into the NET.CFG file. 
 
    e.g.  NET.CFG 
 
          Protocol ODINSUP 
              bind ne2000 
              BUFFERED 
 
The ordering of the occurrence of the "BUFFERED" keyword does not matter.  
When ODINSUP.COM detects the "BUFFERED" keyword it enables double buffering 
of received packets for presentation to the NDIS Protocol Stacks.  This will 
incur a small degradation in performance due to a double copy of the packet, 
however in a DOS environment it should not significantly affect performance. 

Protocols that rely heavily on the MAC Interrupt Request function may not 
perform very well with ODINSUP.  This function requires the ability to generate 
asynchronous interrupts on demand of the protocol.  Since ODINSUP does not have 
direct access to a hardware device, this function must be emulated in software 
which limits the frequency of Interrupt Request acknowledges to a maximum of 
one every 55 milliseconds.  
      
The IBM DLC software requires interrupt requests but it was possible to hook 
their Int 5C interface to provide higher resolution interrupt request 
acknowledges. 

An optional MAC capability that allows on the fly node address overrides is 
not supported by ODINSUP since ODI MLIDs do not support this.  ODI MLIDs do 
support node address overrides from the NET.CFG.  

NDIS Protocols wishing to change the node address will not work with ODINSUP.  
This should not be a problem since the user desiring a different node address 
can simply specify it in the NET.CFG file.  

Note that ODINSUP will allow its NDIS Node Address function to be called, 
however it will return an error if the Node Address given does not match the 
Node Address already configured in the ODI MLID Driver it is using. 
 

***************************************************************************
**** Novell NetWare and Microsoft LAN MANAGER 2.0 *************************
***************************************************************************

NOTE: ODINSUP.COM 4-27-92 is required for Lan MANAGER 2.0 or better.


AUTOEXEC.BAT:

prompt $P$G
lsl
ne2000
odinsup
REM === LANMAN 2.0 === DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.0 ===
SET PATH=C:\LANMAN.DOS\NETPROG;%PATH%
C:\LANMAN.DOS\DRIVERS\PROTMAN\NETBIND
NET START WORKSTATION 
REM === LANMAN 2.0 === DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.0 ===
ipxodi
netx
n:


CONFIG.SYS:

LASTDRIVE=M
DEVICE=C:\LANMAN.DOS\DRIVERS\PROTMAN\PROTMAN.DOS /i:C:\LANMAN.DOS
DEVICE=C:\LANMAN.DOS\DRIVERS\PROTOCOL\NETBEUI\NETBEUI.DOS


NET.CFG:

Protocol ODINSUP
        Bind NE2000
        BUFFERED  <--------- REQUIRED

Link Driver NE2000
        Int 5
        Port 360
        Frame Ethernet_802.3 
        Frame Ethernet_802.2 
        Frame Ethernet_II 
        Frame Ethernet_snap
	Protocol IPX 0 Ethernet_802.3


PROTOCOL.INI:
 
[PROTMAN]
  DRIVERNAME = PROTMAN$
  DYNAMIC = YES
  PRIORITY = NETBEUI

[NETBEUI_XIF]
  Drivername = netbeui$
  SESSIONS = 6
  NCBS = 12
  BINDINGS = NE2000
  LANABASE = 0


****************************************************************************
**** Novell NetWare and Microsoft LAN MANAGER 2.1  *************************
****************************************************************************

NOTE: ODINSUP.COM 4-27-92 is required for Lan MANAGER 2.0 or better.


AUTOEXEC.BAT:

prompt $P$G
lsl
ne2000
odinsup
REM === LANMAN 2.1 === DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.1 ===
SET PATH=C:\LANMAN21.DOS\NETPROG;%PATH%
C:\LANMAN.DOS\DRIVERS\PROTMAN\NETBIND
NET START WORKSTATION 
LOAD NETBEUI
NET LOGON TESTER2 *
REM === LANMAN 2.1 === DO NOT MODIFY BETWEEN THESE LINES === LANMAN 2.1 ===
ipxodi
netx
n:


CONFIG.SYS:

FILES=20
BUFFERS=10
LASTDRIVE=M
DEVICE=C:\LANMAN.DOS\DRIVERS\PROTMAN\PROTMAN.DOS /i:C:\LANMAN.DOS


NET.CFG:

Link support
	buffers 10 1518

Protocol ODINSUP
        Bind NE2000
        BUFFERED  <--------- REQUIRED

Link Driver NE2000
        Int 5
        Port 360
        Frame Ethernet_802.3 
        Frame Ethernet_802.2 
        Frame Ethernet_II 
        Frame Ethernet_snap
	Protocol IPX 0 Ethernet_802.3


PROTOCOL.INI:
 
[PROTMAN]
  DRIVERNAME = PROTMAN$
  DYNAMIC = YES
  PRIORITY = NETBEUI

[NETBEUI_XIF]
  Drivername = netbeui$
  SESSIONS = 6
  NCBS = 12
  BINDINGS = NE2000
  LANABASE = 0


**************************************************************************
**** Novell NetWare and DEC Pathworks ************************************
**************************************************************************

* CONFIG.SYS changes

	All you need in CONFIG.SYS is PROTMAN.SYS, Rem out the NDIS.DOS 
        driver in CONFIG.SYS to use ODINSUP.


CONFIG.SYS:

	break on
	Files=40
	device=c:\qemm\qemm386.sys ram
	buffers=30
	device=c:\pwtcp.sys
	device=c:\protman.exe
	stacks=9,256
	lastdrive=m


* PROTOCOL.INI changes

	Edit PROTOCOL.INI and change the BINDINGS= section to
	bind to whatever driver you're really using. 


PROTOCOL.INI:

[PROTOCOL MANAGER]
  DRIVERNAME=PROTMAN$
	
[IPX4MAC]
  DRIVER=IPX$MAC
  BINDINGS=NE2000

[DATALINK]
  DRIVERNAME= DLL$MAC
  LG_BUFFERS=16
  SM_BUFFERS=6
  OUTSTANDING=32
  HEURISTICS=0
  BINDINGS=NE2000
  NI_IRQ=4	


* NET.CFG changes

You need to add the "address override" to your net.cfg file.
The address looks like:

	Link Driver NE1000
	  ..etc..	
	  Node Address AA000400xxxx

All DECnet addresses are in the form AA-00-04-00-XX-XX.  The final four digits 
are computed from the node address.

DECnet nodes are numbered in the form "area.number" -- For example, node 
9.440 is in area 9, number 440.

Basically, you calculate area*1024+node.  In this case, 9*1024+440 = 9656 
(decimal).  Convert this to hex, to get 0x25B8.  Swap the bytes and put them 
into the address.  You should get AA-00-04-00-B8-25.  So, for node 9.440, 
Node Address is AA000400B825


NET.CFG:

Link Support
	Buffers 20 1514
	MemPool 4096

Protocol ODINSUP
	bind ne2000
	Protocol IPX
	bind ne2000

Link Driver NE2000
	INT #1 4
	PORT #1 320
	MEM #1 D000
	Frame Ethernet_II
	Frame Ethernet_802.3
	Frame Ethernet_802.2
	Frame Ethernet_snap
	Protocol IPX 0 Ethernet_802.3
	Node Address AA000400B825

Setting up files

Make a directory \DECNET on your hard disk, a floppy, or
whatever the CURRENT disk is.  (if you're on E:, make E:\DECNET)
Copy the files from the floppy into this directory.

Copy or RENAME one of the .DAT files to DECPARM.DAT -If you
receive a message from DLLNDIS that says it couldn't find your 
DECPARM.DAT file, be sure it's on \DECNET on the current disk.
(this can be moved if you want).
	

AUTOEXEC.BAT:

LSL
NE2000			 
ODINSUP			
DLLNDIS			DLL->NDIS driver
NETBIND			
SCH			Load PATHWORKS network scheduler
DNNETH			Load DECnet network process
IPXODI			
NETX

ANOTHER SAMPLE AUTOEXEC.BAT (different configuration).

LSL
NE2000
ODINSUP
DLLNDIS
NDIS -d:2
PWBIND
SCH
DNNETH
REDIR5
setname joebob
use f: \\au1\pcsav41
use m: \\drie01\joebob%%joebob *
emsload lat
ipxodi
netx
	

****************************************************************************
**** Novell NetWare and HP ARPA Services in Windows ************************
****************************************************************************

Sample integration of WINDOWS MSDOS 5.0, QEMM 6.02, Netware 3.11, Hewlett
Packard HP ARPA services 2.1 using ODINSUP.  ARPA services is an NDIS
application that uses NDIS drivers instead of Novell ODI drivers.  However
ODINSUP will also work as an option.   In this case the customer didn't want
to use 802.3 for the servers. With ARPA services apparently 802.3 is the
only option.  For that reason ODINSUP was the solution.

SAMPLE Configuration ODINSUP.COM with Windows ARPA services - HP elite 16
nic card.
 

AUTOEXEC.BAT:
 
prompt $p$g
SET PATH=c:\QEMM;c:\windows;c:\dos;c:\;c:\hpnet;c:\HPNET\NETPROG;
LSL
HPDWSA16   <----- Newest HP ODI driver required dated June 1992 or better
ODINSUP
c:\HPNET\DRIVERS\PROTMAN\NETBIND
CALL C:\HPNET\NET_STRT 
IPXODI
netx
f:
login 
win
 

CONFIG.SYS:
 
DEVICE=C:\QEMM\QEMM386.SYS RAM ROM ON
DEVICE=C:\QEMM\LOADHI.SYS C:\DOS\SETVER.EXE
DEVICE=C:\QEMM\LOADHI.SYS C:\WINDOWS\MOUSE.SYS /Y
DEVICE=C:\QEMM\LOADHI.SYS C:\DOS\ANSI.SYS /X
INSTALL C:\DOS\SHARE.EXE
SHELL=c:\DOS\command.com C:\dos\ /e:384 /P
dos-high
BREAK-ON
STACKS=0,0
BUFFERS=40
FILES=60
DEVICE=c:\HPNET\DRIVERS\PROTMAN\PROTMAN.DOS /I:c:\HPNET
DEVICE=c:\HPNET\DRIVERS\PROTOCOL\TCPIP\NEMM.DOS
DEVICE=c:\HPNET\DRIVERS\PROTOCOL\TCPIP\TCPDRV.DOS /I:c:\HPNET
DEVICE=c:\HPNET\DRIVERS\PROTOCOL\TCPIP\IPXDRV.DOS


NET.CFG:
 
LINK Support
  Buffers 8 1500
  Mempool 4096

Protocol ODINSUP
  bind hpdwsa16
  BUFFERED

Link driver hpdwsa16
  Port #1 300
  Int #1 5
  frame ETHERNET_II
  frame ETHERNET_802.3
  Frame ETHERNET_802.2
  Frame ETHERNET_SNAP
  Protocol IPX 0 Ethernet_802.3

Protocol TCPIP
  IP_address xxx.xxx.xx.xxx
 

PROTOCOL.INI:

; Protocol Manager Initialization File

; HP IPX stub driver
[IPXDRV]
  DRIVERNAME = IPX$
  BINDINGS   = hpdwsa16  <---------- must be ODI driver name


; To add another NDIS driver uncomment (remove semicolon for [DEVICENAME] ) 
; the devicename and replace the new DeviceDriver description.  
; The new card may or may not require parameters following DRIVERNAME.
; If some parameter lines are not required then delete these lines.
; NOTE: semicolons represent commented out lines.
;
; [DEVICENAME]
; DRIVERNAME = DeviceDriver ??
; INTERRUPT = 5
; IOADDRESS = 0x300
; RAMAddress = 0x
; 

;************************
;**     PROTOCOLS      **
;************************

[TCPIP]
  DRIVERNAME      = TCPIP$
  BINDINGS = hpdwsa16  <--------------- Must be ODI driver Name
  TCPCONNECTIONS  = 11
  TCPWINDOWSIZE = 1450
  TCPSEGMENTSIZE = 1450
  TCPCONNTIMEOUT  = 30
  TCPKEEPALIVE    = 600
  LOADFACTOR      = 120
  LBUFSZ          = 1530
  MBUFSZ          = 600
  SBUFSZ = 256
  LBP             = 51
  MBP             = 31
  CLIENTOD        = 14
  CLIENTBD        = 40
  CLIENTMSG       = 18
  CLIENTAMSG      = 31
  IPSOCKETSIZE    = 3
  ARPTBLSIZE      = 28
  ERRLOGSIZE      = 1
  IPADDRESS0 = 15 13 161 69
  SUBNETMASK0 = 255 255 248 0
  DEFAULTGATEWAY0 = 15 13 160 254
  UDP_Q_PER_USER=10
  UDP_Q_TOTAL=20

[PROBE]
  DRIVERNAME = PROBE$
  BINDINGS = TCPIP
  NSDOMAIN = mayfield.hpcom

[TCPGLOBAL]
  HOSTNAME = hess486
  NETFILES = C:\HPNET\ETC

[TINYRFC]
  DRIVERNAME = TINYRFC$
  BINDINGS   = TCPIP
  NUMNAMES   = 9
  NUMSESSIONS = 0

[NMDRV]
  DRIVERNAME = NMDRV$
  BINDINGS   = TCPIP

[SOCKETS]
  DRIVERNAME = SOCKETS$
  BINDINGS = TCPIP
  NUMSOCKETS = 3
  POOLSIZE = 3200
  MAXSENDSIZE=1024

[DNR]
  DRIVERNAME = DNR$
  BINDINGS = TCPIP
  NAMESERVER0 = 15 3 32 17
  DOMAIN =mayfield.hp.com

[HP-VT]
  DRIVERNAME = VTCOM
  BINDINGS = TCPIP
  NSESSIONS = 3

[TELNET]
  DRIVERNAME = TELNET$
  BINDINGS = TCPIP
  NSESSIONS = 3
  MAX_OUT_SENDS = 3
  MAX_SEND_SIZE = 128
  DRIVER_EOL = 1
  APP_EOL = 1
  REDIRECT_COM = 1
  ECM_CHAR = "0x1E"
  BRK_ACTION = 3
  MUI_PROMPT = "MUI (? for help)> "

[TICL]
  DRIVERNAME = TICL$
  BINDINGS = TCPIP
  ACBS =
  CMDS = 
  VCS  = 2
  PORTS =


**************************************************************************
**** Novell NetWare, ODINSUP.COM, Synoptics NDIS LatisNet Network ********
**** Management Software (LNMS) version 4.0, and Microsoft Windows. ******
**************************************************************************

AUTOEXEC.BAT:

C:\WINDOWS\SMARTDRV.EXE
@ECHO OFF
PROMPT $p$g
PATH=C:\COMM;C:\WINDOWS;C:\DOS
SET TEMP=C:\DOS
CD \NET
LSL
NE2000
ODINSUP
C:\COMM\NETBIND
CD \
set TMP = C:\tmp 
SET PATH=C:\OV;%PATH% 
IPXODI
NETX
f:
login
win

(assuming LNMS 4.0 is already installed).


CONFIG.SYS:

DEVICE=C:\DOS\SETVER.EXE
DEVICE=C:\WINDOWS\HIMEM.SYS
DOS=HIGH
FILES=30
SHELL=C:\DOS\COMMAND.COM C:\DOS\  /p
STACKS=9,256
DEVICE=C:\COMM\PROTMAN.DOS /I:C:\NET
DEVICE=C:\COMM\NETMANAG.DOS


NET.CFG:

Link Support
       MEMPOOL 4096
       BUFFERS 8 1500

Protocol ODINSUP
       bind ne2000

Link Driver ne2000
       int 5
       port 360
       Frame Ethernet_802.3
       Frame Ethernet_II
       Frame Ethernet_SNAP
       Frame Ethernet_802.2
Protocol IPX 0 Ethernet_802.3

Protocol TCPIP
       ip_address      xxx.xxx.xx.x
       ip_netmask      xxx.xxx.x.x
       tcp_sockets     8
       udp_sockets     8
       raw_sockets     1
       nb_sessions     4
       nb_commands     8
       nb_adapter      0
       nb_domain


PROTOCOL.INI:

[PROTOCOL_MANAGER]
    DriverName = PROTMAN$

[NETMANAGE]
   DRIVERNAME=NETMNG$
   BINDINGS=ne2000


**************************************************************************
**** Novell NetWare and SUN PC/NFS PC NFS ********************************
**************************************************************************

The following were used:

PACKAGE/DRIVER          VERSION/COMMENTS
PC/NFS			3.5
NetWare			3.11
DOS			5.0
QEMM			6.03
ODINSUP.COM		1.01
LSL			current version
NETBIND			1.1
EXP16ODI		1.10 (Intel ODI Driver EtherExpress 16TP)
PCNFS.SYS		(for PC/NFS version 3.5)
SOCKDRV.SYS		(for PC/NFS version 3.5)
PROTMAN.SYS		1.1
NFS-NDIS.SYS		(for PC/NFS version 3.5)


AUTOEXEC.BAT:

prompt $P$G
ncc /fast
scrollbk /ems /m128
c:\qemm\loadhi /r:2 doskey
SET TZ=CST6CDT
SET NFSDRIVE=C
c:\qemm\loadhi /r:2 c:\lsl
c:\qemm\loadhi /r:2 c:\exp16odi
odinsup
netbind
c:\qemm\loadhi /r:2 prt *
nfsrun
c:\qemm\loadhi /r:1 ipxodi
emsnetx
f:


CONFIG.SYS:

DEVICE=c:\qemm\qemm386.sys ram nosh
DEVICE=c:\qemm\loadhi.sys /r:3 /res=4208 /sqt=f800-f8ff c:\dos\ansi.sys
dos=umb,high
SHELL =c:\dos\command.com c:\dos\ /P /E:1024
BUFFERS=40
FILES=40
DEVICE=c:\NFSPCNFS.SYS
DEVICE=c:\SOCKDRV.SYS
DEVICE=c:\lanman\protman.sys
DEVICE=C:\lanman\NFS-NDIS.SYS
LASTDRIVE=E


NET.CFG:

Protocol ODINSUP
        Bind EXP16ODI

Link Driver EXP16ODI
        Int 5
        Port 360
	Frame Ethernet_II
        Frame Ethernet_802.2 
        Frame Ethernet_802.3 
        Frame Ethernet_snap
	Protocol IPX O ethernet_802.3


PROTOCOL.INI:
 
[PROTOCOL MANAGER]
  DRIVERNAME = PROTMAN$

[NFS-NDIS]
  DRIVERNAME = NFSLINK1
  BINDINGS = EXP16ODI


***************************************************************************
**** Novell NetWare and 3+Share Server ************************************
***************************************************************************

CONFIG.SYS:

break     = on
buffers   = 4
files     = 20
lastdrive = h 
device = c:\himem.sys
device = c:\oditest\protman.dos /I:\oditest 	<--(NOTE that the /I:
device = c:\oditest\xnstp.dos			parameter points to the
	                                        location of PROTOCOL.INI.)

AUTOEXEC.BAT:

CD <path>
LSL 
3C503
ODINSUP
XNSTP
NETBIND
NETBIOS
MINSES12
MSREDIR
SETNAME $$3COM$$
3CLOGIN <username>
IPXODI A
NETX
<next available drive>

where path is to the directory ODINSUP.COM and NET.CFG files are found, and
next available drive is LASTDRIVE plus one.

For example, if LASTDRIVE=H:, the next available drive is I:. After the 
NetWare shell, NETX, is loaded, login to the NetWare server by accessing 
the drive indicated by LASTRDRIVE + 1.

Use XNSTP if you are using XNS. Use IPXODI to load IPX only, not SPX.


NET.CFG:

protocol ODINSUP
	bind 3c503

link driver 3c503
	frame ethernet_802.3
	frame ethernet_ii
	frame ethernet_802.2
	frame ethernet_snap
	Protocol IPX 0 Ethernet_802.3


PROTOCOL.INI:

[PROTOCOL_MANAGER]
	DriverName=PROTMAN$

[XNS]
	DriverName=XNSTP$
	Bindings=x3c503  <--(NOTE that an x must preceed the LAN DRIVER 
																					  if the LAN DRIVER name begins with a number)


***************************************************************************
**** Novell NetWare and Ungerman-Bass TCP NDIS Stack, UB ODI Driver *******
***************************************************************************

AUTOEXEC.BAT:

PROMPT $p$g
PATH c:\;c:\arch;c:\network;
set NETONE=c:\arch
lsl
ubodi
odinsup
c:\arch\netbind
ipxodi
netx


CONFIG.SYS:

BUFFERS=20
FILES=25
FCBs=16,8
device=c:\arch\protman.dos /i:c:\arch 
device=c:\arch\ubtpw.dos
device=c:\ubloop.dos
rem device=c:\arch\ubnei.dos
LASTDRIVE=m


NET.CFG:

Protocol ODINSUP
	Bind UBODI
	BUFFERED

Link Driver UBODI
	ADAPTERTYPE Personal NIU/ex
	INT 5
	MEM b0000
	PORT 368
	Frame Ethernet_802.3
	Frame Ethernet_802.2
	Frame Ethernet_II
	Frame Ethernet_snap
	Protocol IPX 0 Ethernet_802.3


PROTOCOL.INI:

; This is a sample PROTOCOL.INI file for the UBNEI Ungermann-Bass NDIS MAC
; driver. The [UBNEI] section shows examples of UBNEI configuration parameter
; settings. Comments at the end of the file explain these parameters and give
; their default, minimum and maximum values.  
;       Note that many of these parameters have default values (which are
; given below under "Comments about UBNEI parameters"). A parameter need not
; be specified in your PROTOCOL.INI if its default value is satisfactory.
    
[PROTOCOL MANAGER]
    Drivername=Protman$

[TCPBIOS]
    Drivername=UBDRV$0
    LCFile = c:\arch\91912a.lc
;    RCVWindow = 8
;    SendWindow = 8
    VCs = 10
    VCReceiveLarge = 40
    VCSends = 200
    Instance = 1
    Bindings = "UBLOOP"
  
[UBLOOP]
   DriverName = UBLOOP$
   Bindings = "UBODI"

[Adapter]
;    DriverName = UBNEI$
    AdapterType = PCNIUex
    MemoryWindow = 0xb0000
    IO_Port = 0x368
    IRQ_Level = 5
;   SlotNumber = 4
    MaxRequests = 6
    MaxTransmits = 6
    ReceiveBufSize = 600
    MaxMulticast = 16
    ReceiveMethod = ReceiveLookahead
    ReceiveBuffers = 64


****************************************************************************
**** Novell NetWare and Ungerman-BASS XNS NDIS STACK ***********************
****************************************************************************

AUTOEXEC.BAT:

PROMPT $p$g
PATH a:\;a:\arch;a:\network;
set NETONE=a:\arch
lsl
ubodi
odinsup
a:\arch\netbind
ipxodi
netx


CONFIG.SYS:

BUFFERS=20
FILES=25
FCBs=16,8
device=a:\arch\protman.dos /i:a:\arch 
device=a:\arch\ubxpw.dos
device=a:\ubloop.dos
rem device=a:\arch\ubnei.dos
LASTDRIVE=m


NET.CFG:

Protocol ODINSUP
	Bind UBODI
	BUFFERED

Link Driver UBODI
	ADAPTERTYPE Personal NIU/ex
	INT 5
	MEM b0000
	PORT 368
	Frame Ethernet_802.3
	Frame Ethernet_802.2
	Frame Ethernet_II
	Frame Ethernet_snap
	Protocol IPX 0 Ethernet_802.3


PROTOCOL.INI:

; This is a sample PROTOCOL.INI file for the UBNEI Ungermann-Bass NDIS MAC
; driver. The [UBNEI] section shows examples of UBNEI configuration parameter
; settings. Comments at the end of the file explain these parameters and give
; their default, minimum and maximum values.  
;       Note that many of these parameters have default values (which are
; given below under "Comments about UBNEI parameters"). A parameter need not
; be specified in your PROTOCOL.INI if its default value is satisfactory.
    
[PROTOCOL MANAGER]
    Drivername=Protman$

[XNSBIOS]
    Drivername=UBDRV$0
    LCFile = a:\arch\565505a.lc
    RCVWindow = 8
    SendWindow = 8
    VCs = 10
    VCReceiveLarge = 40
    VCSends = 200
    Instance = 1
    Bindings = "UBLOOP"
   
[UBLOOP]
   DriverName = UBLOOP$
   Bindings = "UBODI"

[Adapter]
;    DriverName = UBNEI$
    AdapterType = PCNIUex
    MemoryWindow = 0xb0000
    IO_Port = 0x368
    IRQ_Level = 5
;   SlotNumber = 4
    MaxRequests = 6
    MaxTransmits = 6
    ReceiveBufSize = 600
    MaxMulticast = 16
    ReceiveMethod = ReceiveLookahead
    ReceiveBuffers = 64


***************************************************************************
**** Novell NetWare and Ungermann-Bass NDIS stack with an NE2000 **********
***************************************************************************

AUTOEXEC.BAT:

REM  THIS IS AN EXAMPLE AUTOEXEC.BAT FOR USING A NE2000 COMPATIBLE 
REM  ADAPTER CARD IN A DOS WORKSTATION LOADING ONE UB NDIS TCP STACK 
REM  AND IPXODI USING ODINSUP. SUBSTITUTE THE PATH AND SET STATEMENTS 
REM  TO REFLECT YOUR DIRECTORY STRUCTURE.

PROMPT $p$g
PATH a:\;a:\arch;
set NETONE=a:\arch
lsl
NE2000
odinsup
a:\arch\netbind
ipxodi
netx


CONFIG.SYS:

REM  THIS IS AN EXAMPLE CONFIG.SYS FILE FOR USING A NE2000 COMPATIBLE 
REM  ADAPTER IN A DOS WORKSTATION LOADING ONE UB NDIS TCP STACK AND IPXODI 
REM  USING ODINSUP. SUBSTITUTE THE PATHS TO THE DEVICES AND CHANGE THE 
REM  LASTDRIVE STATEMENT TO MATCH YOUR ENVIRONMENT.
REM ***NOTE*** ON LINE 4 USE UBTPW.DOS IF YOU WILL BE USING NETCI OR 
REM  AN LC FILE
REM ***NOTE*** ON LINE 4 USE UBTPS.DOS IF YOU WILL NOT BE USING NETCI 
REM  OR AN LC FILE.

BUFFERS=20
FILES=25
device=a:\arch\protman.dos /i:a:\arch 
device=a:\arch\ubtpw.dos
device=a:\ubloop.dos
LASTDRIVE=m


NET.CFG:

REM  THIS IS AN EXAMPLE NET.CFG FOR USING A NE2000 COMPATIBLE 
REM  ADAPTER IN A DOS WORKSTATION LOADING ONE UB NDIS TCP STACK AND 
REM  IPXODI USING ODINSUP. SUBSTITUE THE INT, MEM, AND PORT SETTINGS TO 
REM  REFLECT THE JUMPER SETTINGS ON YOUR CARD.


Protocol ODINSUP
	Bind NE2000
	BUFFERED

Link Driver NE2000
	INT 5
	MEM D8000
	PORT 360
	Frame Ethernet_802.3
	Frame Ethernet_802.2
	Frame Ethernet_II
	Frame Ethernet_snap
	Protocol IPX 0 Ethernet_802.3


PROTOCOL.INI:

REM  THIS IS AN EXAMPLE PROTOCOL.INI FOR USING A NE2000 COMPATIBLE    
REM  ADAPTER IN A DOS WORKSTATION LOADING ONE UB TCP STACK AND IPXODI 
REM  WITH ODINSUP. SUBSTITUTE YOUR CORRECT IP ADDRESS AND SUB NET MASK.
REM  THE LC FILE IS ONLY REQUIRED IF NETCI WILL BE USED. SEE NOTE IN 
REM  CONFIG.SYS EXAMPLE.

[PROTOCOL MANAGER]
    Drivername=Protman$

[TCPBIOS]
    Drivername=UBDRV$0
    IPAddr    ="XXX.XXX.X.XXX"
    NetSubNetMask="XXX.XXX.XXX.X"
;   LCFile = a:\arch\XXXXXa.lc
    VCs = 10
    VCReceiveLarge = 40
    VCSends = 200
    Instance = 1
    Bindings = "UBLOOP"
   
[UBLOOP]
   DriverName = UBLOOP$
   Bindings = "NE2000"


***************************************************************************
*** Novell NetWare and Microsoft Windows for Workgroups with an NE2000 ****
***************************************************************************

Novell testing of the released WFW product found it to work generally as 
specified by Microsoft when communicating to a NetWare file server.  
Several compatibility and performance problems that were uncovered were 
solved by using the Novell ODINSUP.COM file that allows NDIS protocol 
stacks to run unmodified over the ODI LSL and talk to an ODI LAN driver.
For detailed information about specific issues relating to MS WFW and 
NetWare, see Novell Technical Bulletin TB.P.303, found in TBP300.ZIP in
NOVLIB section 11, or in the March 1993 Novell Research NetWare Application
Notes.

AUTOEXEC.BAT

PATH=C:\WINDOWS
C:\WINDOWS\SMARTDRV.EXE
LSL
NE2000
ODINSUP
C:\WINDOWS\NET START
IPXODI
REM C:\WINDOWS\MSIPX
SET TEMP=C:\WINDOWS\TEMP
NETX 
REM C:\WINDOWS\NETX
Q:
LOGIN SUPERVISOR

NET.CFG

PB BUFFERS 7
PROTOCOL ODINSUP
	BIND NE2000
	BUFFERED
LINK DRIVER NE2000
	FRAME ETHERNET_802.2
	FRAME ETHERNET_802.3
	FRAME ETHERNET_II
	FRAME ETHERNET_SNAP
		PROTOCOL IPX 0 ETHERNET_802.3

CONFIG.SYS

FILES=30
BUFFERS=30
DEVICE=C:\WINDOWS\PROTMAN.DOS /I:C:\WINDOWS
DEVICE=C:\WINDOWS\WORKGRP.SYS
LASTDRIVE=P
DEVICE=C:\WINDOWS\HIMEM.SYS
STACKS=9,256

PROTOCOL.INI

[NETWORK.SETUP]
VERSION=0X3100
NETCARD=NE2000,1,NE2000
TRANSPORT=MS$NETBEUI,MS$NETBEUI
TRANSPORT=IPX,IPX
LANA0=NE2000,1,IPX
LANA1=NE2000,1,MS$NETBEUI

[PROTMAN]
DRIVERNAME=PROTMAN$
PRIORITY=MS$NETBEUI

[NE2000]
DRIVERNAME=NE2000
IOBASE=0X300
INTERRUPT=3

[MS$NETBEUI]
DRIVERNAME=NETBEUI$
SESSIONS=10
NCBS=32
BINDINGS=NE2000
LANABASE=1

[IPX]
DRIVERNAME=IPX
MEDIATYPE=NOVELL/ETHERNET
BINDINGS=NE2000


*****************************************************************  
                    DISCLAIMER   
   
Novell, Inc. makes no representations or warranties with respect to 
any NetWare software, and specifically disclaims any express or 
implied warranties of merchantability, title, or fitness for a 
particular purpose.   
 
Distribution of any NetWare software is forbidden without the 
express written consent of Novell, Inc.  Further, Novell reserves 
the right to discontinue distribution of any NetWare software. 
 
Novell is not responsible for lost profits or revenue, loss of use 
of the software, loss of data, costs of re-creating lost data, the 
cost of any substitute equipment or program, or claims by any party 
other than you.  Novell strongly recommends a backup be made before 
any software is installed.   Technical support for this software 
may be provided at the discretion of Novell. 
*****************************************************************