This TOKODI.DOC accompanies DOSUP8.EXE which includes DOS ODI
drivers for IBM Token-Ring and Lan Support NetWare Clients.  The
following file(s) are included:

     TOKEN    COM    27381  4-12-93  6:27p
     LANSUP   COM    21943  2-02-93 11:54a
     TOKODI   DOC     (this file)

Token.com and lansup.com have been enhanced to include 'Least
Significant Bit' first (LSB) node addresses per the 'IEEE canonical
form' when sending frames above the Data-Link layer.   Previously,
token.com and lansup.com drivers provided 'Most Significant Bit'
first (MSB) only when sending MAC header node address information
above the Data-Link layer.  This LSB ability provides node ID
bit-reversal compatibility with IBM 8209 Bridges. Bit-reversals
take place on all source and destination node addresses 
when 8209 bridges transfer frames from ethernet segments to
token-ring segments unless "IPX Support" has been enabled on the
8209.  The 8209 will not bit-reverse IPX (E0E003/AAAA03/8137) node
addresses when "IPX Support" has been enabled.  The new LSB feature
of lansup.com and token.com allow compatibility with the 8209
without "IPX Support" enabled.  It is advised only to use the LSB
parameter on the Token- Ring segments with 8209 bit-reversal
enabled.  (see paragraphs below on Bit-Reversals)   

Additionally, these drivers provide full compatibility with the
latest IBM locally administered node address standard for
Token-Ring adapters.  In the past, IBM recommended that locally
administered addresses for Token-Ring adapters fall within a range
between and including the following addresses:

4000 0000 0000  to  4000 7FFF FFFF  (HEX)

IBM has expanded the range of recommended locally administered
addresses to the following:

4000 0000 0000  to  7FFF FFFF  (HEX)

There are some restrictions that apply to the above changes.  Some 
devices and/or programs may only be able to use decimal addresses. 

In this case, the following locally administered address range
would be appropriate:

4000 0000 0000  to  7999 9999 9999  (HEX)

It is recommended that 'NSSS FLASH N1005' be obtained from IBM for
all details pertaining to the above LAA changes and associated
restrictions.


********* USAGE **********
The following NET.CFG file demonstrates the enhanced abilities and
usage of lansup.com and token.com.    Please refer to the Novell
ODI shell for DOS manual (part #100-000871-001) for further
information on individual parameters.  Additional information
regarding implementation of token.com and lansup.com is available
in DOSODIWS.DOC found in DOSUP8.EXE also available on NetWire.

Sample NET.CFG  

IPX SOCKETS = 20
IPX RETRY COUNT = 20
CACHE BUFFERS = 5
LONG MACHINE TYPE = IBM_PC

PROTOCOL ipx
     BIND Token (or Lansup)
LINK DRIVER Token (or Lansup)
     Node Address 444400002D43
     Slot 2
     Frame TOKEN-RING_SNAP LSB 
     SAPS 2
     Link Stations 2
     ALTERNATE
     Max Frame Size = 2168



*********** BIT-REVERSALS ******** 
Bit-reversals are necessary because of the difference between
ethernet adapters and token-ring adapters:

Ethernet adapters transmit data onto the wire by transmitting one
byte of data at a time in the following manner:    Each byte of
data is bit-wise right-shifted one bit at a time onto the wire
until all 8 bits of the byte are transmitted onto the wire.  The
next byte of data is then loaded into the transmit register and the
process repeats itself.  The least significant bit, therefore, goes
onto the wire first with ethernet adapters.  

Token-Ring adapters do the opposite.  They take one byte of data
and do a bit-wise left-shift one bit at a time onto the wire until
all 8 bits of the byte are transmitted onto the wire.  Another byte
of data is then loaded into the transmit register for transmission.

The most significant bit, therefore, goes onto the wire first.  

Therefore, the byte 'AA (hex)' on an ethernet wire would appear as
the byte '55 (hex)' on a Token-Ring wire after being bit-reversed
by an IBM 8209 Ethernet to Token-Ring Bridge. 


************* TOKODI MODIFICATION HISTORY **************

3-12-91:   Initial release of TOKODIFT.ZIP beta drivers.

6-3-92:    Lansup.com has been updated to allow frame sizes above
           1K during RPL.  A new "OPEN" parameter for the NET.CFG 
           has been added.  This feature allows lansup.com to open 
           the token-ring adapter and set the frame size.  If     
           dxmt0mod.sys is also loading, one of two actions must be

           performed:  (1) set "o=n" on the dxmt0mod.sys command  
           argument line in the config.sys and use the "OPEN"     
           parameter for lansup.com in the net.cfg. -or-  (2) Set 
           "o=y" in dxmt0mod.sys command line allowing
           dxmt0mod.sys to open the adapter and set the frame     
           size, and exclude lansup.com's "OPEN" parameter from the

           net.cfg.

           Use the following net.cfg syntax when using "OPEN":

           LINK DRIVER LANSUP
                   OPEN
                   <add other parameters as needed>


9/14/92:  Lansup.com has been updated to be compatible with       
          DXME0MOD.sys from IBM Lan Support program v1.30.        
          Token.com has also been updated to work with Odinsup.com 
          where DXME0MOD.SYS V1.30 is involved.

          Files included in the previous revision: (Included in  
          TOKODI.ZIP)

               LANSUP   COM    21524  6-03-92  9:47a
               TOKODIFT DOC     (this file)
 
          Files also in a previous revision:

               TOKEN    COM    23564  8-05-92  2:55p
               LANSUP   COM    21588  8-05-92  2:56p
               TOKODI   DOC     (This File)

************* END OF MODIFICATION HISTORY *********************


*************************************************************** 
                    DISCLAIMER  
  
Novell, Inc. makes no representations or warranties with respect to
any NetWare software, and specifically disclaims any express or
implied warranties of merchantability, title, or fitness for a
particular purpose.  

Distribution of any NetWare software is forbidden without the
express written consent of Novell, Inc.  Further, Novell reserves
the right to discontinue distribution of any NetWare software.

Novell is not responsible for lost profits or revenue, loss of use
of the software, loss of data, costs of re-creating lost data, the
cost of any substitute equipment or program, or claims by any party
other than you.  Novell strongly recommends a backup be made before
any software is installed.   Technical support for this software
may be provided at the discretion of Novell.
***************************************************************