CDBENCH version 2.4 (C) 1992 Profit Press

CDBENCH reports CD-ROM interface performance information. It will only
operate on the Profit Press MegaDEMO CD-ROM. By operating on only this
CD-ROM (pressed by a single company) more reliable results can be
obtained. The run time of this program can be up to 5 minutes and is
neccessary to produce results that can be measured accurately by the
system timer.

Information on benchmarks

1/3 stroke seek:        The standard for determining the "average" seek
                        time of a drive. This test performs 60 seeks back
                        and forth across the disc.

Random seek:            Performs 60 seeks to a "random" areas of the CD-ROM
                        under the 350 megabyte mark. The seeks are always
                        the same every time CDBENCH is run. (allows for
                        relatively short seek comparisons between drives)

1/3 stroke seek & read: Performs 60 staggered seeks (to defeat caching)
                        over 1/3 of the CD-ROM. After each seek a single
                        2k sector is read. This test will defeat some
                        CD-ROM drives and caching programs that ignore
                        seek commands.

Sustained long read:    Reads 2 megabytes of consecutive sectors off
                        the CD-ROM in 32k blocks. This represents the
                        maximum data rate. Multimedia compatible drives
                        should read more than 150,000 bytes per second.

Sustained short read:   Reads 512k of consecutive sectors in single
                        sector (2k) blocks. This will show how well
                        the buffer or cache in the CD-ROM drive handles
                        small but frequent accesses.

MegaSearch benchmark:   A simulation of common file handling operations
                        used by MegaSearch Retrieval Software and MegaDOOR.
                        This should provide a good indication of relative
                        DOS random access speeds to the CD-ROM.


A database of CD-ROM results will be maintained on the Profit Press BBS.
The phone number is (602)299-0693 and we support 2400-14400 with v.32bis.
If you'd like an ASCII output of your results type CDBENCH <filename>
(preferably a filename that doesn't output to the CD-ROM!). Blanks will
be left in your output file to add information about your CD-ROM and
system configuration. Please upload your results to our BBS!


Results as of 10/16/92 include:

Drive                  1/3 seek  Rseek   Seek/read  Long read  Short read MS
-------------------------------------------------------------------------------
0 Toshiba 3201B (8/89)   N/A       N/A    407.5     153903.9   153903.9   32.6
1 Panasonic CR-501-C   630.95    473.44   501.83    154526.9    89177.9   31.65
2 Genstar 2000         475.3     310.4    761.0      69020.2     7466.4  N/A
3 NEC CDR-80             N/A       N/A    865.38     54139.24    5059.41  82.80
4 Amdek Laserdrive-1     N/A       N/A   1202.38     53909.84    4985.39 121.43
5 Texel DM3021           N/A       N/A    392.9     154527.0   156426.9   41.8
6 DAK/BSR $199 ext.    802.2     614.5   1046.7      68279.4    14199.5  115.3
7 Chinon ?             280.0     204.0    427.0     153903.0   144576.0  N/A
8 DAK/BSR $399 ext.    257.3     183.2    399.3      95420.4    14157.3   37.5
9 GenStar 3000i        901.1     627.3   1121.8     153903.9   134395.0  125.4

        N/A = NOT AVAILABLE

Information on drives:
  0 Toshiba 3201B (8/89)
        - 486/33 system with a WD-7000FAST 16 bit SCSI controller
  1 Panasonic CR-501-C
        - 486/50 system with a CSM 8 bit SCSI controller
  2 Genstar 2000
        - 386/20 system with proprietary 8 bit controller
  3 NEC CDR-80
        - 386/40 system with Trantor 8 bit SCSI
  4 Amdek Laserdrive-1
        - 386/40 system with proprietary 8 bit controller
  5 Texel DM3021
        - 386/25 system with Always IN-2000 16 bit SCSI
  6 DAK/BSR $199 ext.
        - 386/20 system with proprietary 8 bit controller
  7 Chinon
        - Unknown model number in CompuAd computer
  8 DAK/BSR $399 ext.
        - 386/40 system with proprietary 8 bit controller
          This is an older OEM Sony CD-ROM drive.
  9 GenStar 3000i internal (Mitsumi CRMC-LUOO2S)
        - 286/12 system with proprietary 8 bit controller