INTRODUCTION

    CDT is a small shell utility to cope with SCSI devices, but mainly with
    a CD-ROM. It has been written to be able to start audio playback with
    "stupid" drives that do support an advanced audio command as eg. used by
    SCSIutil. Its also possible to issue a load or eject command as well as 
    to lock or unlock a drive.

LEGAL

    CDT is Copyright © 1995 by Gunther Nikl, All Rights Reserved.
    Permission granted to distribute free of charge, in unchanged form,
    provided this documentation file is accompanied with the program.
    Permission granted to include on freely distributable software
    libraries such as Fred Fish's software library and the Aminet CD-ROM.

    CDT is provided as is, without any kind of warranty. By using CDT, the
    user accepts full responsibility for possible damage or data loss that
    might occur, directly or indirectly, from using CDT.

    CDT is GIFTWARE. If you use CDT, send me a gift (your own program, beer,
    chocolate, a new computer, a money donation, etc.), the address is in
    the end of this document.

FEATURES

    - supports any CD-ROM that has a SCSI-2 compliant device driver
      (thus also atapi drives)
    - can start/stop/pause/resume audio playback
    - written in C (and compiled with GCC 2.7.0 ;-)
    - 100% pure, can be made resident

INSTALLATION

    Installing CDT is fairly easy. Copy it to a location on you harddisk
    (preferable in the search path, eg. C:). Thats all :-).
    I would recommend to create aliases to avoid 

USAGE

    CDT can only be started from CLI! Do NOT try to start the program from
    Workbench since this will lead to a system crash!

    CDTs shell template:

    D=DEVICE,U=UNIT/K/N,STARTTRACK/N,STARTINDEX/N,LASTTRACK/N,LASTINDEX/N,
    LOAD/S,EJECT/S,LOCK/S,UNLOCK/S,PLAY/S,STOP/S,PAUSE/S,RESUME/S,INFO/S

    Detailed explanation:

    - D=DEVICE

      used to specify the lowlevel device driver to access the SCSI drive.
      Usual names are: scsi.device, atapi.device, etc.
      Alternative you can also specify a DOS-device. That means the name
      the drive is accessed from DOS, eg. "CD0:". CDT will try to get the
      name of the device driver and the device unit from DOS. If that fails
      it will use its internal defaults. An error message of the form:

        "couldn't open `scsi.device' unit `4'

      can be a hint that the information searched for wasn't available.

      Default device driver is `scsi.device'.

    - U=UNIT/K/N

      used to specify the driver number. If as device a DOS-device was
      specified this option will be ignored but only if all required
      information from the dos-device could be retrieved.

      Default unit is `4' (do not ask why ;-)

     - STARTTRACK/N

       first title to play (starts with 1)

       defaults to 1.

     - STARTINDEX/N

       which start index but can usually be omitted

       defaults to 0.

     - LASTTRACK/N

       last title to play (max. 99)

       defaults to 99.

     - LASTINDEX/N

       which end index but can usually be omitted

       defaults to 0.

     - PLAY/S

       starts the audio playback with the parameters above. First CDT will
       use an `intelligent' command to start the audio playback. If this
       fails CDT will try a more generic command to play an audio cd. This
       shall make CDT work with every CD-ROM drive, at least I hope so ...

       Some examples:

        - play
          will play the complete cd

        - play 5
          starts audio playback with title number 5

        - play 5 0 9
          will play from title number 5 to 9 (0 is the startindex, required)

     - PAUSE/S

       pauses audio playback (if its playing ignored otherwise)

     - RESUME/S

       resumes audio playback (if its paused ignored otherwise)

     - LOAD/S

       will close the drive's tray (if it was open)

     - EJECT/S

       will open the drive's tray (if it was closed)

     - LOCK/S

       prevents the opening of the tray

     - UNLOCK/S

       allows the opening of the tray

     - INFO/S

       prints information about the drive. This works also for harddisks.

BUGS

    This program has only be tested with IDE drives that device drivers
    emulate a SCSI-2 environment. The two tested drives had some problems:

      - playing only parts of an audio cd doesn't work (not quite true,
        if only the last title was requested it works :-)
        (Toshiba XM-5302B, Sony CDU-77E)
      - `pause' option does not work with Sony CDU-77E, the drive aborts
        the audio playback completely
      - closing the drive tray without inserted medium will give an error
        message

HISTORY

    1.0 - initial release

AUTHOR

    CDT is written by Gunther Nikl.  You can reach me by email at the address

    gnikl@informmatik.uni-rostock.de

    or by snailmail (for the time being, anyway) at the address

    Gunther Nikl
    Ziegendorfer Chaussee 96
    Parchim
    19370
    Germany