AN EXAMPLE OF CONVERTING A PROGRAM WRITTEN FOR MASM INTO ONE WRITTEN FOR A86
by Eric Isaacson


Recently a user sent me the file SETUP.ASM, a program written to assemble 
under Microsoft's MASM assembler.  He wanted to know why A86 wouldn't assemble 
it, and why he should choose A86 over MASM, in view of the fact that there are 
hundreds of programs out there written for MASM.  This paper is a response to 
that question.  In it, I show the minimum alterations necessary to produce an 
A86 source file that assembles to an equivalent functioning program.  I go on 
from there, to show how the language extension features of A86 can let you 
make the program simpler and clearer.  Finally, I do an extensive reworking of 
the program, rewriting portions of code, renaming variables and procedures, 
and adding more comments.  By carefully studying the source program at each 
stage of the transformation process, you'll learn not only about the 
differences between A86 and MASM, but about how to transform an ordinary 
assembly-language program into a well-written one. 


STEP 1.  CONVERTING THE PROGRAM

The program that the user sent me is in the file SETUP.ASM.  To make a COM 
program file from this source file using MASM, you must assemble it with MASM,
link the resulting OBJ file using LINK (ignoring the 1 error message that LINK 
always gives you when you use MASM to create a COM file), feed the resulting 
EXE file to EXE2BIN, and finally rename the resulting BIN file to SETUP.COM.
The resulting file is 3129 bytes long.

If you attempt to assemble SETUP.ASM using A86 version 3.04, you'll get four 
errors.  The first three are all of the same type-- an attempt to MOV a symbol 
into a general register, where the symbol is a segment name defined with a 
SEGMENT AT directive.  I corrected this by replacing the SEGMENT AT directives 
(all three are together at the top of the program) with EQU directives, 
EQUated to the AT-value.  Similarly, the single symbol defined within each of 
the SEGMENTS was converted to a definition via EQU. 

The fourth error is the END BEGIN at the end of the program.  Since A86 treats
this as equivalent to MAIN EQU BEGIN, and since the program already has a 
symbol MAIN defined elsewhere, this was a multiple definition.  I corrected 
this simply by deleting the END BEGIN line, since A86 doesn't need the END 
directive.

These modifications took me five minutes to find and make, and I had a program 
that A86 accepted.  But the program didn't work.  A glance at the code 
contents revealed that interrupt drivers were involved, in which the DS, ES,
and SS registers didn't have the same values as the CS register.  Some of the 
memory accesses needed explicit CS override bytes coded for them, since A86 
doesn't act on ASSUME directives.  I scanned through the code and found four 
places where CS overrides were needed.  Diagnosing and solving this problem 
took about twenty minutes; so I had a working A86 program within a half hour.
I would guess this to be worse than average, since most assembly-language COM 
programs don't use multiple-segments the way interrupt drivers do.

*** I have made enhancements so that starting with Version 3.05, my assembler
    will assemble SETUP.ASM without modification.  I added interpretation of
    SEGMENT AT to be an EQU of the segment name to the AT value, followed by
    entry into STRUC mode for assembly of declarations within the structure.
    V3.05 also completely ignores the END directive in non-OBJ mode.

The source for the minimal changes I have described is the file S1.8.  The 
command A86 S1.8 makes an S1.COM file directly, that is functionally 
equivalent to the SETUP.COM file produced by MASM, LINK, EXE2BIN, and REN.  
The S1.COM file is 3105 bytes long, which is 24 bytes shorter than SETUP.COM.  
The difference comes from 19 unnecessary segment-override bytes produced by 
MASM, plus 5 LEA instructions coded in situations where an equivalent MOV 
instruction would have been more efficient.  A86 automatically generates the 
more efficient MOV instruction, and MASM doesn't.



STEP 2.   INTRODUCING A86 LANGUAGE FEATURES THAT DON'T CHANGE THE PROGRAM

Of course, I could have stopped with step 1.  But I wanted to explore the 
possibilities for improving the program, so I continued.  The next step was to 
add A86 language features, to make the program clearer.  The first part of 
this transformation was to eliminate all unnecessary red-tape directives, and 
to replace all the place-marker symbols with A86 local labels (L0 through L9).  
The symbols were easy to find, since the author of the program followed the 
reasonable MASM practice of ending place-marker symbols with digits.  Because 
the local names are only two characters long, it becomes reasonable to indent 
instructions by only two spaces, leaving room for longer comments.  Next, I 
found places to incorporate A86 language features into individual instruction 
sequences: multiple operands to PUSH POP INC DEC, conditional returns, MOV 
segreg,segreg, and IF cond stmt.  The resulting program, S2.8, produces a 
virtually identical 3105-byte COM file to S1.8, but the source code appearance 
is considerably changed for the better. 


STEP 3.  MAKING MINOR CODE OPTIMIZATIONS

Next, I started making changes to improve the code itself.  Among the changes:

1. I renamed many variables and procedures, to make the program easier to 
   follow.  Same of the renaming was simple unabbreviation: for example, 
   VIDEO2MEM to VIDEO_TO_MEM, and PAGE_NO to PAGE_NUMBER.  Other renaming 
   involved making a completely different, clearer choice of name: for 
   example, SETUP_STATUS to WINDOW_ACTIVE?, and MAIN to OUR_HANDLER.

2. I combined that three original SEGMENT ATs and the variables they contained 
   into three DD constants, to be loaded into pointers with LDS or LES 
   instructions, followed by indirect memory instructions to access the 
   variables. 
   
3. I rearranged the main interactive loop to make the flow of control clearer.
   The exit-code executed when the ESC key is pressed is separated from the 
   main flow, and clearly labelled ESC_SEEN.  The rest of the main loop was 
   consolidated and arranged to clearly show its loop structure.

4. I performed code optimizations based on 86 instruction set features the 
   original author didn't take advantage of.  For example, the sequence

        L1:
          MOVSW
          LOOP L1

   was replaced by a simple REP MOVSW instruction.  The preceding CLD 
   instruction was moved to the start of interrupt processing, reducing the 
   procedure WRITELN to the single REP MOVSW line.  So I eliminated WRITELN 
   and replaced the instances of CALL WRITELN with REP MOVSW.  I could have 
   treated MEM2MEM similarly, except that MEM2MEM is never called so it can be 
   eliminated outright.  Finally, the sequence

         SUB BX,2
         MOV AL,DISPLAY_TABLE[BX]

   was replaced by MOV AL,DISPLAY_TABLE[BX-2] .

In addition to the coding changes, I converted all non-comment code to all-
caps, to complete the conversion of the program to my formatting conventions.  
The resulting program, S3.8, assembles to a 3065-byte COM file, 40 bytes less 
than the previous version due to the optimizations.


STEP 4.  MAKING MAJOR CODE OPTIMIZATIONS

For the final revision of the program I made major code optimizations:

1. I completely overhauled the usage of memory variables.  Some variables, 
   such as ATTRIBUTE1, were eliminated, their values kept in registers.  The 
   tables VIDEO and DISPLAY_TABLE were replaced by the more directly useful 
   ENABLE_VALUE and VIDEO_SEG.

2. I redesigned the parameterization of VIDEO_TO_MEM and MEM_TO_VIDEO, that 
   defines the size and location of the pop-up window.  It had previously been 
   a run-time parameterization, always called with the same values.  I 
   introduced a set of EQUs for the parameters, defining the window at 
   assembly time.  VIDEO_OFFSET was transformed from a run-time procedure to 
   an assembly-time expression EQUate.  All constant references depending on 
   window size were recast in terms of the parameter-symbols.  Assertion-
   checking was also introduced to insure that the declaration of the window 
   contents contains the proper number of bytes.

3. The program was rearranged to save space.  The buffer used for storing the 
   contents of the screen beneath the pop-up window was moved to the start of 
   the program, so that the 256-byte PSP buffer could be a part of the storage 
   buffer.  The initialization code and window source code was moved there 
   also, to save space.  The buffer containing the constructed window image 
   was moved to beyond the area of the COM file, reducing the size of the COM 
   file by 1064 bytes in one stroke.

4. The array CODE_TABLE was converted from fixed-length records to delimited 
   variable-length records, saving more program space.

5. The pushing of all registers except AX was deferred until after the hot-key 
   check, to reduce keystroke computational overhead time when the program is 
   not in effect.

6. More changes were made to improve program readability.  The installation 
   code was broken up into procedures, for clarity.  The keycode values FUNC 
   and SHIFT_F were declared and used, to make the key-scanning code easier to 
   follow.  The program itself was renamed to the more descriptive EPSONSET, 
   and an explanatory paragraph was added to the top of the source code.  The 
   instruction-level comments were improved.

The resulting final source program is S4.8, which assembles to a COM file of 
only 1237 bytes, less than 40% of the original program size.  I retained the 
original copyright notice, although it might be argued that I transformed the 
program enough to call it my own.