BINARY.DOC -- Description of BINARY.ASM
=======================================

  From `BLUEBOOK of ASSEMBLY ROUTINES for the IBM PC & XT'
        by Christopher L. Morgan
        Copyright (C) 1984 by The Waite Group, Inc.

  Purpose: BINARY.ASM contains routines to convert between number bases. 

     Contents:
     ---------
     BIN16IN	--  Convert from ASCII Binary to 16-bit Binary
     BIN16OUT	--  Convert from 16-bit Binary to ASCII Binary
     BIN8OUT	--  Convert from 8-bit Binary to ASCII Binary
     DEC16IN	--  Convert from ASCII Decimal to 16-bit Binary   	
     DEC16OUT	--  Convert from 16-bit Binary to ASCII Decimal
     DEC8OUT	--  Convert from 8-bit Binary to ASCII Decimal
     HEX16IN	--  Convert from ASCII Hexadecimal to 16-bit Binary
     HEX16OUT	--  Convert from 16-bit Binary to ASCII Hexadecimal
     HEX8OUT	--  Convert from 8-bit Binary to ASCII Hexadecimal
     OCT16IN	--  Convert from ASCII Octal to 16-bit Binary
     OCT16OUT	--  Convert from 16-bit Binary to ASCII Octal
     OCT8OUT	--  Convert from 8-bit Binary to ASCII Octal
		
  Overview: These routines perform conversion between the PC's 8- and 16-bit
    internal BINARY integer formats and all the popular external integer
    number bases: binary, octal, hexadecimal, and decimal.  For each number
    base, there are three routines:

		1) Input from external to 16-bit binary internal format
		2) Output from 8-bit binary internal format to external
		3) Output from 16-bit binary internal format to external

    Throughout the routines, the 8088 registers are used consistently:

 		AX is used for quick calculations and data movement
		CL & CX are used for counting, multiplying, or dividing
		DL & DX are used to pass numerical data in and out of routines

________________________________ BINARY ROUTINES ______________________________

BIN16IN -- Convert from ASCII Binary to 16-bit Binary

  Function: This routine accepts a binary number from the standard input
    device and converts it to internal 16-bit binary form.

  Input: The individual digits of the binary number are received in ASCII
    through a call to a standard I/O routine.  The valid digits are 0 and 1.
    An ASCII code other than for a valid digit will terminatete the routine.

  Output: A 16-bit binary number is returned in the DX register.

  Registers used: Only DX is modified.  It returns the result.

  Routines called: STDIN
______________________________________________________________________________

BIN8OUT

  Function: This routine accepts an 8-bit binary number in the DL register,
    converts it to ASCII binary form, and sends it to the standard output
    device.

  Input: Upon entry an 8-bit binary number is in the DL register.

  Output: A string of ASCII digits representing a binary number is sent out
    through the standard output device.

  Registers used: No registers are modified. DL is used for input.

  Routines called:  STDOUT
______________________________________________________________________________

BIN16OUT

  Function: This routine accepts a 16-bit binary number in the DX register,
    converts it to ASCII binary form, and sends it to the standard output
    device.

  Input: Upon entry a 16-bit binary number is in the DX register.

  Output: A string of ASCII digits representing a binary number is sent out
    through the standard output device.

  Registers used: No registers are modified. DX is used for input.

  Routines called: STDOUT
______________________________________________________________________________

OCT16IN

  Function: This routine accepts an octal number from the standard input
    device and converts it to internal 16-bit binary form.

  Input: The individual digits of the octal number are received in ASCII
    through a call to a standard I/O routine.  The valid digits are
    0 through 7. An ASCII code other than for a valid digit will terminate
    the routine.

  Output: A 16-bit binary number is returned in the DX register.

  Registers used: Only DX is modified. It returns the result.

  Routines called: STDIN
______________________________________________________________________________

OCT8OUT

  Function: This routine accepts an 8-bit binary number in the DL register,
    converts it to ASCII octal form and sends it to the standard output device.

  Input: Upon entry an 8-bit binary number is in the DL register.

  Output: A string of ASCII digits representing an Octal number is sent out
    through the standard output device.

  Registers used: No registers are modified. DL is used for input.

  Routines called: STDOUT
______________________________________________________________________________

OCT16OUT

  Function: This routine accepts 16-bit binary number in the DX register,
    converts it to ASCII octal form and sends it to the standard output device.

  Input: Upon entry a 16-bit binary number is in the DX register.

  Output: A string of ASCII digits representing an octal number is sent out
    through the standard output device.

  Registers used: No registers are modified. DX is used for input.

  Routines called: STDOUT
______________________________________________________________________________

HEX16IN

  Function: This routine accepts a hexadecimal number from the standard input
    device and converts it to internal 16-bit binary form.

  Input: The individual digits of the hexadecimal number are received in ASCII
    through a call to a standard I/O routine. The valid digits are 0 through 9
    and A through F. An ASCII code other than for a valid digit will terminate
    the routine.

  Output: A 16-bit binary number is returned in the DX register.

  Registers usnd: Only DX is modified. It returns the result.

  Routines called: STDIN
______________________________________________________________________________

HEX8OUT

  Function:  This routine accepts an 8-bit binary number in the DL register,
    converts it to ASCII hexadecimal form and sends it to the standard output
    device.

  Input: Upon entry an 8-bit binary number is in the DL register.

  Output: A string of ASCII digits representing a hexadecimal number is sent
    out through the standard output device.

  Registers used: No registers are modified. DL is used for input.

  Routines called: STDOUT
______________________________________________________________________________

HEX16OUT

  Function: This routine accepts a 16-bit binary number in the DX register,
    converts it to ASCII hexadecimal form and sends it to the standard output
    device.

  Input: Upon entry a 16-bit binary number is in the DX register.

  Output: A string of ASCII digits representing a hexadecimal number is sent
    out through the standard output device.

  Registers used: No registers are modified. DX is used for input.

  Routines called: STDOUT
______________________________________________________________________________
_
DEC16IN

  Function: This routine accepts a decimal number from the standard input
    device and converts it to internal 16-bit binary form.

  Input: The individual digits of the decimal number are received in ASCII
    through a call to a standard I/O routine.  The valid digits are
    0 through 0. An ASCII code other than for a valid digit will terminate
   the routine.

  Output: A 16-bit binary number is returned in the DX register.

  Registers used: Only DX is modified. It returns the result.

  Routines called: STDIN
______________________________________________________________________________

DEC8OUT

  Function: This routine accepts an 8-bit binary number in the DL register,
    converts it to ASCII decimal form and sends it to the standard output
    device.

  Input: Upon entry an 8-bit binary number is in the DL register.

  Output: A string of ASCII digits representing a decimal number is stored in
    a buffer called TBUFF and then sent out through the standard output device.

  Registers used: No registers are modified. DL is used for input.

  Segments referenced: DATAS is a data segment which contains TBUFF

  Routines called: STDOUT
______________________________________________________________________________

DEC16OUT

  Function: This routine accepts a 16-bit binary number in the DX register,
    converts it to ASCII decimal form and sends it to the standard output
    device.

  Input: Upon entry a 16-bit binary number is in the DX register

  Output: A string of ASCII digits representing a decimal number is stored in
    a buffer called TBUFF and then sent out through the standard output device.

  Registers used: No registers are modified. DX is used for input.

  Segments referenced: DATAS is data segment which contains TBUFF

  Routines called: STDOUT
______________________________________________________________________________
>>>>> Physical EOF BINARY.DOC <<<<<