STDIO.DOC -- Description of the I/O procedures in STDIO.ASM
===========================================================

  From `BLUEBOOK of ASSEMBLY ROUTINES for the IBM PC & XT'
        by Christopher L. Morgan
        Copyright (C) 1984 by The Waite Group, Inc.

  Purpose: These routines perform fundamental input/output functions for the
    keyboard, screen, and communication lines.  The standard I/O routines
    can be redirected.  The communications routines alleviate some of the
    problems encountered in DOS and BIOS serial communications handling.

   Contains:
   ---------
   COM_INCK	--  Communications line check
   COM_INIT	--  Initialize communications line
   COM_OFF	--  Communications line off
   COM_ON	--  Communications line on
   COM_OUT	--  Communications line output
   STD_CRLF	--  Standard output with carriage return & linefeed
   STD_IN	--  Standard input with echo
   STD_INCK	--  Standard input check
   STD_INNE	--  Standard input with no echo
   STD_MSGOUT	--  Standard output of a message
   STD_OUT	--  Standard output
   STD_OUTDR	--  Direct standard output
   STD_SPACE	--  Standard output of a space	
_______________________________________________________________________________

STD_IN -- Standard Input with Echo
---------------------------------
  Function: This routine accepts input from the standard I/O device. 

  Input: This routine waits for one character code from the std input device.

  Output: ASCII codes are returned in the AL register.  Each character is
    echoed out the standard output device as it is input through the standard
    input device.

  Registers used: AH is modified; AL is used for output.

  Routines called: DOS call #1 (Keyboard input) is used.
_______________________________________________________________________________

STD_INNE -- Standard Input with No Echo
--------------------------------------
  Function: This routine accepts input from the standard I/O device. No echo
    is generated.

  Input: This routine waits for one character code from the std input device.

  Output: ASCII codes are returned in the AL register.

  Registers used: AH is modified; AL is used for output

  Routines called: DOS call #8 (Console output without echo) is used.
_______________________________________________________________________________

STD_INCK -- Standard Input Check
-------------------------------
  Function: This routine checks, but does not wait for input from the standard
    input device.

  Input: Input is from the standard I/O device.  No check is made for ^-Break.

  Output: If a character is available, the routine returns with the flag
    condition NZ and a character in AL.  If no character is available, then
    the routine returns with the flag condition Z, and AL is garbage. No echo
    is generated for the input characters.	

  Registers used: AH is modified; AL is used for output.

  Routines called: DOS call #6 (Direct console I/O) is used.
_______________________________________________________________________________

STD_OUT -- Standard Output
-------------------------
  Function: This routine sends individual characters out the std output device.

  Input: Upon entry, an ASCII code is in AL.

  Output: A single character is output through the standard output device.

  Registers used: AH is modified; AL is used for input.

  Routines called: DOS call #2 (Display output) is used.
_______________________________________________________________________________

STD_OUTDR -- Direct Standard Output
----------------------------------
  Function: This routine sends individual characters out the standard output
    device, using direct output.

  Input: Upon entry, an ASCII code is in AL.

  Output: A single character is output through the direct standard output call.

  Registers used: AH is modified; AL is used for input.

  Routines called: DOS call #6 (Direct console I/O) is used.
_______________________________________________________________________________

STD_CRLF -- Standard Output of a Carriage Return/Linefeed Sequence
-----------------------------------------------------------------
  Function: This routine sends a <CR> and then a <LF> to the std output device.

  Input: None

  Output: ASCII code 13 for <CR> and ASCII code 10 for <LF> are sent to the
    standard output device.

  Registers used: AX is first saved and then restored.

  Routines called: STD_OUT
_______________________________________________________________________________

SDTSPACE -- Standard Output of a Space
--------------------------------------
  Function: This routine sends a space out through the standard output device.

  Input: None

  Output: ASCII code 32 for a space is sent to the standard output device.

  Registers used: AX is first saved and then restored.

  Routines called: STD_OUT
_______________________________________________________________________________

STD_MESSOUT -- Standard Output of a Message
------------------------------------------
  Function: This routine sends a message out through the std output device.

  Input: Upon input, DS:SI points to the message.  The message must terminate
         with an ASCII code 0.

  Output: The individual characters of the message are output through the 
    standard output device.

  Registers used: AX is first saved and then restored; SI is used to point to
    the input.

  Segments referenced: The data segment must contain the message.

  Routines called: STD_OUT
_______________________________________________________________________________

COM_INIT -- Initialize Communications Line
-----------------------------------------
  Function: This routine initializes one of the two communications lines.

  Input: Upon entry, AL contains the initialization byte as follows:

bit ---- 7  6  5 ---------- 4  3 ------------ 2 -------------- 1     0 ---- bit
        ---------          ------          --------          -----------   
	baud rate          parity          stop bit          word length 
        ==========        =========        ========          ===========    
      	000 =  110   	  00 = none   	    0 = 1            10 = 7 bits
        001 =  150        01 = odd          1 = 2            11 = 8 bits
        010 =  300        10 = none      
        011 =  600        11 = even
        100 = 1200        
        101 = 2400       
        110 = 4800
        111 = 9600
                          DX contains the unit number (0=COM_1:, 1=COM_2:). 

  Output: Output is sent to the hardware controlling the specified com line.

  Registers used: None

  Routines called: BIOS interrupt 14H (RS-232 I/O) is used.
_______________________________________________________________________________

COM_INCK -- Communications Line Input Check
------------------------------------------
  Function: This routine checks, but does not wait for input from one of the
    two serial communications lines.

  Input: Upon entry, DX contains the unit number (0=COM_1:, 1=COM_2:).  During
    the routine, input is from the specified communications line.

  Output: If a byte is available, the routine returns with the flag condition
    NZ and the byte in AL.  If no byte is available, the routine returns with
    the flag condition Z, and AL is garbage.

  Registers used: AH is modified; DX is used for input & AL is used for output.

  Segments referenced: The system data segment is referenced.
_______________________________________________________________________________

COM_OUT -- Communications Line Output
------------------------------------
  Function: This routine sends a byte out one of the two communications lines.

  Input: Upon entry, AL contains the byte to be sent out and DX contains the
    specified unit number (0=COM_1:, 1=COM_2:).

  Output: Output is sent to the specified communications line.

  Registers used: None.

  Routines called: BIOS interrupt 14H (RS-232 I/O) is used.
_______________________________________________________________________________

COM_ON -- Communications Line On
-------------------------------
  Function: This routine turns on the handshaking signal, DTR(line 20), and
    RTS (line 4) on the specified communications line

  Input: Upon entry, DX contains the unit number (0=COM_1:,1=COM_2:).

  Output: Just to the communications line

  Registers used: DX is used for input; no registers are modified.

  Segments referenced: The system data segment is referenced.
_______________________________________________________________________________

COM_OFF -- Communications Line Off
---------------------------------
  Function: This routine turns off the handshaking signal, DTR(line 20), on
    the specified communications line.  RTS(line 4) is kept on as it was.

  Input: Upon entry, DX contains the unit number (0=COM_1:,1=COM_2:).

  Output: Just to the communications line

  Registers used: DX is used for input; no registers are modified.

  Segments referenced: The system data segment is referenced.
_______________________________________________________________________________
>>>>> Physical EOF STDIO.DOC <<<<<