{ Cursor.doc - documentation for QWIK cursor routines       ver 4.1, 05-01-88 }

  GotoRC - Like Turbo's GotoXY, this procedure moves the cursor, but with a 
  couple of important differences.  The cursor is absolute to the entire 
  screen and ignores the limits set by the Turbo Window procedure.  In 
  addition, it will work on all the other video pages besides page 0.

  CursorChange - This procedure will let you change the mode (shape and 
  visibility) of the cursor.  At the same time, it saves the previous mode.  
  Using hex is the easiest way to set the integer.  The shape of the cursor 
  is defined by horizontal scan lines in the character cell where the top row 
  is of any cell is 0.  The starting (upper) row of the cursor mode is the 
  high (or left) byte of the integer and the ending (lower) row is the low 
  (or right) byte.  In addition, bits 5 and 6 of the starting row byte 
  control on/off and erratic blinking (remember a byte has bits 0 to 7).  See 
  QINIT.DOC for cell sizes.

     Shape:       Adapter   Default  Comments
                  --------  -------  -------------------------
                  MDA       $0B0C
                  CGA,MCGA  $0607
                  EGA       $0B0C    MD, ECD (640x350 25-line)
                  EGA       $0607    CD, ECD (640x200)
                  VGA       $0D0E    Emulation off
                  3270 PC   $0D0D    And converts MDA and CGA

     Cursor off:  Set start row bits 6-5 = 01.  All other bits don't matter.
     Blinking:    Set start row bits 6-5 = 11.  Creates erratic blinking on 
                  most machines.
|    Skew:        Set end bits 6-5 = 01, 10, or 11 on EGA or VGA to skew the 
|                 cursor to the right by 1, 2, or 3 spaces respectively.

     Suggestions: For block cursor,  set New:=$000E (Works on all machines.)
                  For hidden cursor, set New:=$2000

  CursorOff - Rather than using CursorChange to hide the cursor, use this 
  procedure.  You don't have to save the current cursor shape since all it 
  does is set the cursor-off bit on the current cursor mode.

  CursorOn - To restore the cursor after turning it off with CursorOff, use 
  this procedure.  The previous shape is maintained.

  WhereR/WhereC - Also like Turbo's WhereX/WhereY, these functions detect 
  cursor position, but with the same differences as GotoRC.

  Suggestions - Use discretion when changing the cursor mode.  Some users 
  prefer a block cursor for all their applications.  If your program forces 
  it to an underline, try to restore the original cursor.  Programs like 
  WordStar, never even touch the cursor.  There is only one case that I know 
  where you must set the cursor mode before using CursorOff/On.  The early 
  PCs had a bug in the BIOS that set the MDA default to be CGA instead.  You 
  can check for ActiveDispDev=MdaMono and a $0607 cursor.  If so, change it 
  to $0B0C for an underline.

  EGA Cursor Emulation - With 640x200, the emulation works fairly well.  With 
  640x350 and 25-line mode, the emulation works, too.  Outside of that, it is 
  suggested that any needed changes should be made with emulation off which 
  can be done be setting bit 0 of EgaInfo equal to 1.

  MCGA Cursor Emulation - Use the CGA cursor cell size even though the 
  character cell is 8x16.  The BIOS multiplies the start and end rows by 2 
  and then adds one to the end row before writing to the hardware video port 
  to emulate the CGA.

  VGA Cursor Emulation - Qinit sets the cursor emulation mode on so you don't 
  have to worry about special fonts and cells sizes.  The only cell sizes you 
  need to know is the MDA and CGA.  The video BIOS will adjust your cursor 
  shape to fit in the current cell size.  Here's the cursor shapes (types) 
  recognized by the VGA algorithm and how it responds:

     Cursor Type   Condition            Action
     ------------  -------------------  ---------------
     Hidden (off)  start bits 6-5 = 01  pass
     Split         start > end          invert to block
     Overbar       start < end <= 3     pass
     Underline     start+2 >= end       adjust
     Full-block    start <= 2           adjust
     Half-block    start > 2            adjust


  For adjustment, three more tests are required:

     Condition                          Action
     --------------------------------   ----------
     start or end >= cell height        adjust
     end = cell height - 1              pass
     start = cell height - 2            pass


  The final adjustment is made to the corresponding cursor type:

     Cursor Type  Adjustment
     -----------  -------------------------------------------------
     Overbar      pass
     Underline    move start/end to bottom of cell
     Half-block   start = cell height/2; move end to bottom of cell
     Full-block   move end to bottom of cell


  3270 PC Peculiarites - The 3270 PC cursor types are limited to only three.  
  In addition, the underline cursor is not visible on a white background on 
  the 5272 color display and it is advisable to use a block cursor together 
  with that attribute:
 
     Cursor Type   Comments
     ------------  ---------------------------------------------------
     Underline     $0D0D only.  CGA and MDA are emulated to this type.
     Hidden (off)  cursor start > cursor end.  $2000 is preferred.
     Block         anything other than the above