EMS0017 REDIRECTION OF LPT1.  PCJR INTERNAL MODEM REDIRECTED            
                                                                        
10/23/85                                                                
IBM PCjr  (4860067)                                                     
                                                                        
A base model PCjr with no internal  modem  and  no  parallel            
printer  adapter  automatically  sends  output  intended for            
LPT1:  to the serial port (for the Compact printer).  Hence,            
the  use  of  the  serial device is transparent to the user.            
This serial port is also COM1:  with no  options  installed.            
If  an  internal  modem  is  installed  the serial port then            
becomes COM2:.  Under these conditions the printer output is            
then  sent  to the COM2:  serial port (the Compact printer).            
This is handled automatically by ROM BIOS.                              
                                                                        
If a  parallel  printer  adapter  is  attached,  the  output            
intended  for the printer is automatically sent to the newly            
attached parallel printer.   To  use  the  Compact  printer,            
output must be redirected to the serial port.                           
                                                                        
     MODE COM1:1200,N,8,2,P                                             
     MODE LPT1:=COM1:                                                   
                                                                        
The  above  two  DOS  commands  work  on  a  PCjr without an            
internal modem.  COM2:  is used when the modem is installed.            
              *** END OF DOCUMENT  ***                                  
                                                                        
Note :  This modification or recommendation has not been subjected to   
        exhaustive testing and may not, in all circumstances, provide   
        a complete solution.                                            
sting and may not, in all circumstances, provide   
        a complete solution.