FRACTION.SHP and FRACTION.SHX
                               December 14, 1989
                         Copyright 1989, S.M. Westbrook
                                S.W. CAD Designs
                                 P.O. Box 1617
                            Sugarland, Texas  77487


=============================================================================
DESCRIPTION:

This AutoCad BIGFONT shape file enables you to enter vertical or slanted
fractions directly into you AutoCAD text strings.  The 200 series of vertical
fractions is the preferred type in mechanical drawings, as well as in other
drafting disciplines. They eliminate the confusion of interpreting 1 1/32 as
0.34375 instead of seeing it as 1.03125. The 300 series of fractions is
provided for pleasant looking fractions in drawing notes, title blocks, etc.
This series fits easier into the line spacing size AutoDesk selected for many
of it's text fonts.  Both series of fractions will be drawn to basic drafting
standards with the numerator and the denominator being 75% of the current text
height. The overall fraction will approximately be twice the text height. This
BIGFONT will accommodate any variation in x-scale factor, obliquing angle, etc.



=============================================================================
CONTENTS:

FRAC.ZIP contains the following files:

     1.  FRACTION.DOC  :  This documentation file
     2.  FRACTION.LIC  :  Registration form
     3.  FRACTION.SHP  :  The BIGFONT source code
     4.  FRACTION.SHX  :  Release 10 compiled file of FRACTION.SHP



=============================================================================
INSTALLATION:

1. Copy FRACTION.SHX to your AutoCad directory, the directory set by the ACAD
   system variable, or any other directory in your path. (Normally where you
   keep the other *.SHX files)

2. You can now add FRACTION.SHX to any new or existing "styles" in your
   drawings. An example of appending this BIGFONT to the standard SIMPLEX
   font would be to answer "simplex,fraction" when asked for the text font in
   the STYLE command. You may answer the other questions in any manner you
   wish, except for vertical text. FRACTION.SHX does not support vertical text
   at this time.

3. To enter a fraction into your drawing, you enter %%SXX where S is the series
   of fraction you desire, and XX is the actual fraction you want in terms of
   32nd of an inch. The S value will either be a "2" for vertical fractions or
   a "3" for slanted fractions. The XX will be in the range of 01 to 31, such
   as "03" for 3/32 or "16" for 1/2.




=============================================================================
 REGISTRATION/LICENSING:

    *  A $10 shareware contribution is requested for using the program.
    *  The author retains the sole right to sell the program.
    *  The author grants users the right to copy and distribute the program
       within the following constraints:
         - All program files remain unaltered and are distributed en masse.
         - No attempt is made to sell the program, or to make money from it
           or any modified version of it.
         - The program is not  bundled  with  any  other  hardware/software
           transactions without the author's permission.
         - Recognized users' groups may charge a maximum $5 duplication  or
           distribution fee.

    *  Please completely fill out the registration form found in FRACTION.LIC
       to properly register you. Registration will also add you to our mailing
       list for furthur releases of this product and for notifications of other
       CAD related programs.



=============================================================================
 DISCLAIMER:

   S.W. CAD Designs disclaims all warranties expressed or implied as to the
   quality or performance of these shapes. S.W. CAD Designs will not be held
   liable for any lost profits, lost savings or any other direct, indirect,
   incidental or consequential damages resulting from the use of this program.
   Your use of these shapes constitutes your agreement to this disclaimer and
   your release of S.W. CAD Designs from any form of liability or litigation.