MicroSpeed ADI Driver Device for AutoCAD
            ----------------------------------------


                           Overview
                            --------

This  document  describes the installation and use of a  FastTRAP 
pointing  device  driver  developed by MicroSpeed  for  use  with 
AutoCAD by Autodesk.   The driver is usable with all releases  of 
AutoCAD  which  support the Autodesk defined ADI (AutoCAD  Device 
Interface)  and  allows AutoCAD users to  significantly  simplify 
their use of AutoCAD.  

                          Installation
                          ------------

The basic installation process is as follows:


     1.   Make sure FastTRAP driver is properly installed

     2.   Install AutoCAD for an ADI digitizer

     3.   Install  the  FastTRAP  ADI  driver  prior  to  running 
          AutoCAD


The FastTRAP ADI driver file name is DGTRAP.COM.  As with all ADI 
device  drivers,  DGTRAP  is a terminate and stay resident  (TSR) 
program  which provides a standardized interface between  AutoCAD 
and a device specific software driver,  in this case MicroSpeed's 
MAP.SYS  or MAP.COM multi-axis pointer driver.   The  MAP  driver 
should  be installed for the system as described in Section 3  of 
the  FastTRAP  user's manual prior to installing  the  DGTRAP.COM 
driver.

Prior to using the FastTRAP ADI driver you must install AutoCAD's 
digitizer  to handle an ADI digitizing device.   This is done  as 
follows:  
     
          1.   Select   option   5  on  the  AutoCAD  main   menu 
               ("Configure AutoCAD")

          2.   Select   option  4  on  the   configuration   menu 
               ("Configure  digitizer").   A  list  of  available 
               digitizers will be displayed.

          3.   Select  "ADI digitizer" from the list of available 
               digitizers. (If your AutoCAD device driver library 
               is not in a hard disk sub-directory you will  need 
               to  have your a diskette containing AutoCAD device 
               drivers available during the installation).  Refer 
               to   your  AutoCAD  documentation   for   complete 
               information on installing device drivers.

After  AutoCAD  device  driver installation,  when you  list  the 
AutoCAD  hardware configuration the digitizer should be shown  as 
"ADI digitizer".

To  install the DGTRAP driver,  execute the following command  at 
the DOS command prompt:

     A>DGTRAP <options>

The options,  if specified,  define how DGTRAP will operate  with 
AutoCAD.  The options are:

          Z=MENU         Define trackwheel to select menu items

          Z=GAIN         Define trackwheel to set FastTRAP X-Y 
                         gain

          nnn            A number from 1 to 100 setting the 
                         FastTRAP X-Y-Z axis gain


The Z=MENU and Z=GAIN options are mutually exclusive - users must 
select  one  or the other.   In the event that both  options  are 
specified the last option on the line will be the one that  takes 
effect.


The  nnn option can be specified with either the Z=MENU or Z=GAIN 
options  by  following the selected option with a space  and  the 
desired  gain setting.   Valid gain settings are specified  on  a 
linear  scale  from 1 to 100,  with 1 being lowest gain  and  100 
being highest gain.   If the nnn option is not specified the gain 
is set to a default value of 25.

The default settings for the DGTRAP command is Z=MENU and gain=25 
if no options are specified.  This is equivalent to the command:

     A>DGTRAP Z=MENU 25

Examples:

     A>DGTRAP

     Set trackwheel for menu select and gain for X-Y-Z axes to 25

     A>DGTRAP Z=GAIN

     Set trackwheel for gain select with an initial gain setting 
     for X-Y-Z axes of 25

     A>DGTRAP 50

     Set trackwheel for menu select and gain for X-Y-Z axes to 50

     A>DGTRAP Z=GAIN 50

     Set trackwheel for gain select with an initial gain setting 
     for X-Y-Z axes of 50


NOTE:      The  DGTRAP driver must be installed prior to  running 
AutoCAD.   You  may want to set up a batch file to  automatically 
load the DGTRAP driver and then load AutoCAD.




                            OPERATION
                            ---------

The  ADI  driver utilizes all three of the FastTRAP's input  axes 
and  all three of it's input buttons to give AutoCAD  users  more 
efficient control over commonly used pointing functions,  thereby 
increasing   user  productivity.   The  ADI  driver  assigns  the 
FastTRAP's hardware resources as follows:

     
     Trackball:          Select pointer position 

     Trackwheel:         Select menu items or set X-Y gain
                         (see below)

     Left button:        Pick item

     Middle button:      Select modifiers menu

     Right button:       Enter command


The  trackwheel  function can be defined to  either  select  menu 
items or to set the gain of the FastTRAP trackball X-Y axis gain.  
For  most users the select menu option (the default) will be  the 
most useful.
     

The  ADI driver functional configuration is optimized to  improve 
user  productivity  compared  to  other  commonly  used  pointing 
devices.  For example, when using AutoCAD with a conventional two 
button  mouse all menu items must be selected by first moving the 
pointing  cursor  from  the  active  drawing  area  to  the  menu 
selection bar and then picking the menu item; selecting modifiers 
for  the  various menu options requires  additional  picking  and 
pointing.   In  many  drawing applications the  continual  cursor 
positioning  and  repositioning significantly  increases  drawing 
time.


Using the new FastTRAP ADI driver,  menu items and modifiers  can 
be  selected directly using the trackwheel and the middle button; 
there  is no longer any requirement that the pointing  cursor  be 
moved  from the active drawing area.   This reduces the number of 
required pointer positioning and repositioning operations with  a 
subsequent increase in user productivity.


For questions, contact MicroSpeed technical support: 415/490-1403


AutoDesk, AutoCAD, and ADI are registered trademarks of AutoDesk, 
Inc.

FastTRAP, MicroSpeed, and trackwheel are trademarks of 
MicroSpeed, Inc.
DI ar