The STAT program will allow you to display and change the status
  of any COM port.  The syntax of this utility is as follows:


                        Ú       ¿ Ú     ¿ Ú     ¿
                   STAT ³ COM1  ³ ³ INT ³ ³ ON  ³
                        ³ COM2  ³ ³ RTS ³ ³ OFF ³
                        ³ COM3  ³ ³ DTR ³ À     Ù
                        ³ COM4  ³ À     Ù
                        ³ PNNNN ³
                        À       Ù
            Where NNNN is a PORT address.

            EXAMPLE --> C>stat com1 int on

                          This will enable interrupts on port COM1


                        C>stat p3f8 rts off

                          This will turn off RTS on port 3F8


                        C>stat COM2

                          This will display the status of port COM2



  The INT operator will ENABLE or DISABLE interrupts for the selected
  COM port.  This could be useful if a piece of software left
  interrupts turned on for a port and another port was trying to use
  the same interrupt line.  You could then turn off interrupts for one
  of the ports allowing the other one to work.

  The RTS operator turns ON and OFF the Request To Send RS232 line.

  The DTR operator turns ON and OFF the Data Terminal Ready RS232 line.


  The following files are included:

       STAT.DOC   <---  This file.
       STAT.EXE   <---  Program compiled with Microsoft C 5.1
       STAT.C     <---  Source code

  This program is released into the Public Domain and may be used
  for whatever anyone wants to use it for.


                                  Dave DeDene
                                  (313) 497-1038
                                  Center Line  MI