MMMMMMMMM\     /MMMMMMMMM
      MMMMMMMMMM\   /MMMMMMMMMM
      MMMMMMMMMMM\ /MMMMMMMMMMM
      MMMMMMMMMM \M/ MMMMMMMMMM
      MMMMMMMMMM     MMMMMMMMMM
      MMMMMMMMMM     MMMMMMMMMM  EEEEEEE  .GGGGG   .AAAAA.
      MMMMMMMMMM     MMMMMMMMMM  EE       GG       AA   AA   -------
      MMMMMMMMMM     MMMMMMMMMM  EEEEE    GG  GGG  AAAAAAA      ------
      MMMMMMMMMM     MMMMMMMMMM  EE       GG   GG  AA   AA         ------
      MMMMMMMMMM     MMMMMMMMMM  EEEEEEE  'GGGGGG  AA   AA            ------


                         BBBBBBBBBB BBBBBB.
                         BBBBBBBBBB BBBBBBBBB
                         BBBBBBBBBB BBBBBBBBBB
           ______        BBBBBBBBBB BBBBBBBB'
        __|____  |       BBBBBBBBBB BBBB
      _|_____  | |       BBBBBBBBBB BBBBBBBB.    .AAAAA.   CCCC.  KK   KK
     |       | | |       BBBBBBBBBB BBBBBBBBBB   AA   AA  CC   C  KK  KK
     |   O   | |-|       BBBBBBBBBB BBBBBBBBBBB  AAAAAAA  CC      KKKK
     |   |   |-|         BBBBBBBBBB BBBBBBBBBBB  AA   AA  CC   C  KK  KK
     |___|___|           BBBBBBBBBB BBBBBBBB'    AA   AA   CCCC'  KK   KK

                                          ll
                                          ll
                                  .pppp   ll  uu  uu  +sss.
                                  p    p  ll  uu  uu  ss
                                  p    p  ll  uu  uu   ss+
                                  p    p  ll  uu  uu     ss
                                  ppppp   ll  uuuuuu  ssss+
                                  pp
                                  pp
                                  pp

                                   ___________________________________________
                                   |                                         |
                                   |  MegaBack Plus                          |
                                   |                                         |
                                   |  Comprehensive Backup for PC Systems    |
                                   |                                         |
-->                                |  April 1993                             |
                                   |                                         |
                                   |  User's Guide                           |
                                   |                                         |
                                   |                                         |
                                   |  Patri-Soft                             |
                                   |  5225 Canyon Crest Dr                   |
                                   |  Suite 71-358                           |
                                   |  Riverside, Ca  92507                   |
                                   |                                         |
                                   |  Patriquin's BBS                        |
-->                                |  (DATA)   909-352-2825                  |
-->                                |  (VOICE)  909-352-2820                  |
-->                                |  (FAX)    909-352-1527                  |
                                   |                                         |
                                   |  Copyright 1993 by Patri-Soft           |
                                   |  all rights reserved                    |
                                   |_________________________________________|



     MegaBack Plus              Table of Contents                    Page i

     About MegaBack  . . . . . . . . . . . . . . . . . . . . . . . . .    1

     MegaBack Features . . . . . . . . . . . . . . . . . . . . . . . .    1

     Backing up with MegaBack  . . . . . . . . . . . . . . . . . . . .    2

     Full/Incremental Backup . . . . . . . . . . . . . . . . . . . . .    3

     Multiple Hard Disks . . . . . . . . . . . . . . . . . . . . . . .    4

     Complements Tape Backup . . . . . . . . . . . . . . . . . . . . .    4

     Select/Exclude  . . . . . . . . . . . . . . . . . . . . . . . . .    5

     Reliability . . . . . . . . . . . . . . . . . . . . . . . . . . .    5

     System Setup/Installation . . . . . . . . . . . . . . . . . . . .    6
          Setting system options . . . . . . . . . . . . . . . . . . .    7
          Test to verify installation  . . . . . . . . . . . . . . . .   10

     Quick Start guide . . . . . . . . . . . . . . . . . . . . . . . .   12
          Starting MegaBack  . . . . . . . . . . . . . . . . . . . . .   12
          Backing up files . . . . . . . . . . . . . . . . . . . . . .   12
               Starting from the menu  . . . . . . . . . . . . . . . .   12
               Backup processing . . . . . . . . . . . . . . . . . . .   14
               Backup termination  . . . . . . . . . . . . . . . . . .   14
          Restoring files  . . . . . . . . . . . . . . . . . . . . . .   14
               Restoring files . . . . . . . . . . . . . . . . . . . .   14
               Initial restore file selection  . . . . . . . . . . . .   14
               Restore now or list specific files  . . . . . . . . . .   15
               Selecting files from the selection list . . . . . . . .   15
               Restore processing  . . . . . . . . . . . . . . . . . .   15
               Restore termination . . . . . . . . . . . . . . . . . .   15

     How MegaBack works  . . . . . . . . . . . . . . . . . . . . . . .   16
          Backup Volumes . . . . . . . . . . . . . . . . . . . . . . .   16
          Backup Sets  . . . . . . . . . . . . . . . . . . . . . . . .   16
          Backup File Index  . . . . . . . . . . . . . . . . . . . . .   17
          The Backup Volume Index  . . . . . . . . . . . . . . . . . .   17

     MegaBack reference  . . . . . . . . . . . . . . . . . . . . . . .   17
          Preparing backup volume sets . . . . . . . . . . . . . . . .   17

     MegaBack's Main Menus . . . . . . . . . . . . . . . . . . . . . .   18

     Backup Processing . . . . . . . . . . . . . . . . . . . . . . . .   18
          Backup Type Selection Display  . . . . . . . . . . . . . . .   19
          Full Backup <F>  . . . . . . . . . . . . . . . . . . . . . .   20
          Incremental Backup <I> . . . . . . . . . . . . . . . . . . .   20
          List Files <L> . . . . . . . . . . . . . . . . . . . . . . .   20
          Backup Status Display  . . . . . . . . . . . . . . . . . . .   21
          Status Bar . . . . . . . . . . . . . . . . . . . . . . . . .   21
          Totals . . . . . . . . . . . . . . . . . . . . . . . . . . .   21
          Current File . . . . . . . . . . . . . . . . . . . . . . . .   21





     MegaBack Plus              Table of Contents                   Page ii

          Disk Statistics  . . . . . . . . . . . . . . . . . . . . . .   21
          Request for backup volumes . . . . . . . . . . . . . . . . .   22
          Recovering from disk write errors  . . . . . . . . . . . . .   23
          Interrupting/Resuming backup . . . . . . . . . . . . . . . .   24
          Completing backup  . . . . . . . . . . . . . . . . . . . . .   24

     Restore . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   25
          Entering Restore Criteria  . . . . . . . . . . . . . . . . .   26
          Listing Files to Restore . . . . . . . . . . . . . . . . . .   28
          Restore File Select List Processing  . . . . . . . . . . . .   29
          Starting Restore . . . . . . . . . . . . . . . . . . . . . .   32
          Restore Processing . . . . . . . . . . . . . . . . . . . . .   32
          Overlaying Files with duplicate Names  . . . . . . . . . . .   33
          Completing Restore . . . . . . . . . . . . . . . . . . . . .   34

     Restoring to an Empty System  . . . . . . . . . . . . . . . . . .   35

     Making a system recovery boot diskette  . . . . . . . . . . . . .   35

     Utility Functions . . . . . . . . . . . . . . . . . . . . . . . .   37
          Synchronize hard disk. . . . . . . . . . . . . . . . . . . .   37
          Reset the backup indexes . . . . . . . . . . . . . . . . . .   38
          Recover backup indexes from last backup volume . . . . . . .   39
          Create reports . . . . . . . . . . . . . . . . . . . . . . .   40
          Verify backup volume data  . . . . . . . . . . . . . . . . .   40

     Options . . . . . . . . . . . . . . . . . . . . . . . . . . . . .   42
          Selection/Exclusion Procession . . . . . . . . . . . . . . .   42
          Backup File Selection Operation. . . . . . . . . . . . . . .   43
          Marking a full directory . . . . . . . . . . . . . . . . . .   44
          Completing file selection. . . . . . . . . . . . . . . . . .   45
          Set basic system options . . . . . . . . . . . . . . . . . .   45
          Advanced System Options. . . . . . . . . . . . . . . . . . .   45
          Define backup sets . . . . . . . . . . . . . . . . . . . . .   48
          Password Protection. . . . . . . . . . . . . . . . . . . . .   48
          Set alternate display type/colors. . . . . . . . . . . . . .   48

     Command Line operation  . . . . . . . . . . . . . . . . . . . . .   51
          command line format  . . . . . . . . . . . . . . . . . . . .   51
          Command parameter explanations . . . . . . . . . . . . . . .   51

     Specifying options through DOS environment variables  . . . . . .   53

     Backup Maintenance  . . . . . . . . . . . . . . . . . . . . . . .   54
          Multiple Backup sets . . . . . . . . . . . . . . . . . . . .   54
          Making copies of backup volumes  . . . . . . . . . . . . . .   54

     The Context Sensitive Help System . . . . . . . . . . . . . . . .   55

     Alarm/Reminder Utility. . . . . . . . . . . . . . . . . . . . . .   56

     System Requirements . . . . . . . . . . . . . . . . . . . . . . .   59
          Operating system compatibilities . . . . . . . . . . . . . .   59
          Backup device compatibilities  . . . . . . . . . . . . . . .   59





     MegaBack Plus              Table of Contents                  Page iii


     Troubleshooting . . . . . . . . . . . . . . . . . . . . . . . . .   59
          I/O errors on disks  . . . . . . . . . . . . . . . . . . . .   59
          Error Messages . . . . . . . . . . . . . . . . . . . . . . .   60
     Technical Support . . . . . . . . . . . . . . . . . . . . . . . .   60




     MegaBack Plus              Table of Contents                   Page iv


                         IMPORTANT WARRANTY INFORMATION


     TRIAL USE (SHAREWARE EVALUATION VERSION) WARRANTY:

     The Shareware evaluation (trial use) version is provided AS IS. Patri-
     Soft MAKES  NO WARRANTY OF  ANY KIND, EXPRESSED OR  IMPLIED, INCLUDING
     WITHOUT  LIMITATION, ANY WARRANTIES  OF MERCHANTABILITY AND/OR FITNESS
     FOR A PARTICULAR PURPOSE.



                        REGISTERED VERSION ONLY WARRANTY:

     Patri-Soft   warrants   the    physical   diskette(s)   and   physical
     documentation provided with registered versions to be free of  defects
     in materials and workmanship for a period of ninety days from the date
     of  registration.    If Patri-Soft  receives  notification  within the
     warranty  period  of defects  in  materials or  workmanship,  and such
     notification is  determined by  Patri-Soft to  be correct,  Patri-Soft
     will replace the defective diskette(s) or documentation.

     The  entire and  exclusive liability  and  remedy for  breach of  this
     Limited   Warranty  shall  be  limited  to  replacement  of  defective
     diskette(s) or  documentation and shall  not include or extend  to any
     claim for or  right to recover  any other damages,  including but  not
     limited to, loss of profit, data, or use of the software,  or special,
     incidental, or consequential damages or other  similar claims, even if
     Patri-Soft has  been specifically advised  of the possibility  of such
     damages.  In no  event will Patri-Soft's liability for any  damages to
     you or any other person ever exceed  the lower of suggested list price
     or actual price  paid for the license to  use the software, regardless
     of any form of the claim.

     Patri-Soft SPECIFICALLY DISCLAIMS ALL  OTHER WARRANTIES, EXPRESSED  OR
     IMPLIED,  INCLUDING  BUT  NOT  LIMITED TO,  ANY  IMPLIED  WARRANTY  OF
     MERCHANTABILITY AND/OR FITNESS FOR A PARTICULAR PURPOSE.















     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 1


     About MegaBack

     MegaBack  is a  personal backup  system for  your computer.   MegaBack
     software  automates and organizes  backup processing for  your system.
     It also provides comprehensive abilities  to restore backup files when
     needed.

     MegaBack is  designed to  be easy for  all PC  users.   Its menus  are
     simple   and  understandable.     MegaBack  makes  backup   simple  by
     surrounding  all complex  backup terms  and requirements  with a  menu
     driven system.



     MegaBack Features

     --   Lets you  control  backup  type  by  selecting  full  volume,  or
          incremental backup of updated files.

-->  --   Remember to backup regularly  by letting MegaBack's alarm feature
          remind you when backups are due.

     --   Saves your time by letting you optionally view files to be backed
          up before backup begins.

     --   Simplifies  restore by locating backup files quickly using backup
          indexes maintained by MegaBack.

     --   Simplifies multiple hard drive backup by automatically backing up
          all drives in a single backup process.

     --   Reduce backup time and diskettes required through a comprehensive
          exclusion facility that  lets you mark  directories and files  to
          exclude files from the backup process.

     --   Saves time and effort by Formatting new diskettes  automatically.

     --   Saves backup space by appending  daily backup of updated files to
          the last backup disk used.

     --   Saves backup space through very high compression and a smart disk
          storage techniques. Lets you store  the maximum amount of data on
          a minimum number of diskettes.

     --   Provides  flexibility  by  optionally  restoring  files   to  any
          specified location.

     --   Uses multiple storage media.  Backup  to diskette, removable hard
          disks, or optical disks.

     --   Provides transportability of  backup data to other  systems using
          portable backup volumes.






     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 2


     --   Provides  peace of mind through extensive capabilities to recover
          from backup errors and disk losses.

     --   Enhances backup  data integrity  by letting  you create  multiple
          backup disk sets to keep spare backup copies for your data.

     --   Adapts  to  your operation  preference  of menu  or  command line
          operation.

     --   Simplifies  learning  and  operation  through  instant  access to
          context sensitive help at any time (F1 key).

     --   Helps you use  available  time by  letting you  interrupt full or
          incremental backup at  any time and  resume processing when it is
          convenient for you.


     Backing up with MegaBack

     MegaBack  keeps compressed  and compacted copies  of files  on offline
     diskettes volumes  and maintains  records for every  file in  a backup
     index  on your  hard  disk.   The  backup index  lets you  immediately
     examine all information about your backup files without having to scan
     through backup diskettes.

     MegaBack compresses each file  as it is backed up to  make maximum use
     of diskette storage.  Compression  usually results in storing files in
     1/2 the space they would normally require on diskettes.

     MegaBack also compacts data on backup disks to improve performance and
     further reduce disk space required for backup.  All files backed up to
     a single diskette  are compacted into a  single backup file.   Writing
     this  single file  is  much  faster and  more  efficient than  writing
     multiple  files on  a backup  diskette.   In addition  to performance,
     compaction saves  disk space used  by unoccupied cluster space  at the
     end of each DOS file.

     Unlike some other backup systems,  MegaBack uses standard DOS disk I/O
     routines when  reading and writing  backup data.  This  makes MegaBack
     much more reliable as it  does not depend on unsupported, nonstandard,
     I/O techniques that may fail on some computers.

     MegaBack organizes your backup volumes (diskettes) in simple numerical
     order so it  is easy to file  and locate backup volumes.   All volumes
     are numbered sequentially starting  at 1.   Newly backed up files  are
     stored  in the  next available space  on the last  used backup volume.
     Volumes are completely used before  new volumes are started.  MegaBack
     tracks  volumes by  number  and records  information  about the  exact
     location of every stored file in its hard disk index.

     MegaBack's  backup  index  provides  a  backup  directory   containing
     valuable information  about every  file backed up.   The  backup index






     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 3


     lets  you  determine  if  you have  a  backup  of  any  file from  any
     directory, and tells you  the date and time the backup was  made.  The
     following information is maintained about every backup file:

          File name
          Drive where file was backed up from
          Directory where it was backed up from
          File Size
          Date the file was created or last changed
          Time the file was created or last changed
          File attributes
          Date the file was backed up
          Time the file was backed up
          The number of the backup disk(s) holding the file
          The compressed size of the backup file


     When you need  to restore files or  an entire volume, you  specify the
     drive, directory, and  file information for all files  to be restored.
     These specifications may be for an exact file or  may specify wildcard
     names for qualifying multiple files.  MegaBack can immediately restore
     all matching files, or it will provide a scrollable selection list for
     you  to select  one or  more  files to  be restored.    Once you  have
     selected files to  be restored, MegaBack  determines where the  backup
     files are stored, and requests volumes by number.

     This  organization  lets you keep many  volumes of  backup data  while
     still maintaining easy access to any file.


     Full/Incremental Backup

     It is  not reasonable to  expect you to  take the time to  backup your
     entire  hard disk  volume every  time you  want to  backup.   MegaBack
     provides two backup types.

     Full backup backs up all files on your hard disk.  Use Full backup the
     first time  you use  MegaBack, and then  periodically to  refresh your
     backups.   Full backup  is only  needed when  you have  used all  your
     backup disk volumes and want to condense multiple backup copies of the
     same file  down to a single  copy.  It  is also useful after  you have
     deleted many files from your hard disk and want to free up backup disk
     space used to hold the files.   Unbelievably, most users only need  to
     perform  a  full  backup  about once  every  three  months.   They use
     Incremental Backup is the term given to the process of backing up only
     files that have  been modified since  they were last  backed up.   DOS
     always  keeps  track  of  modified  files for  you  my  marking  their
     directory entries with an archive (changed) attribute.

     The DOS attribute command (ATTRIB in  DOS 5.0) can be used to  inspect
     or  change the archive attribute.   Whenever a file is created, copied
     to  a  new  location, or  changed  by an  application,  DOS  marks the
     directory  entry with  the archive attribute.   If you  have never run





     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 4


     backup,  the  archive attribute  will be  set  for each  file  on your
     system.  Backup programs remove the archive attribute from files after
     they  have been  backed up.   MegaBack's  Full and Incremental Backups
     reset the  archive  (changed)  indicator.    For  testing  or  special
     situations,  you can disable resetting this attribute through MegaBack
     options.

     Incremental Backup  can quickly  identify  all changed  files on  your
     system and  append them to  your backup set.   Since many  people only
     update a  few documents  or files each  day, incremental  backup often
     only takes a minute or two a day.  Since Incremental Backup only backs
     up a small  amount of information, you may use incremental backup each
     day for months before needing a full backup.

     Incremental Backup  has the effect  of storing multiple copies  of the
     same file in  the backup set if  the file is changed  between backups.
     This would occur when you were editing a word processing document over
     a period  of days.  Each day, the current  status of the document will
     be saved to the backup set.  Although you may at first think this is a
     waste  of backup disk  space, it is really  a very beneficial feature.
     Incremental backups of the same file provides a history of  changes to
     the file.  In the event you  need to restore an earlier version of the
     file, you can always find it in MegaBack's backup set.

     MegaBack's Incremental Backup lets you backup often.  In fact, you may
     want  to  backup  more  than  once  a  day  when working  on  critical
     information you cannot afford to  lose.  Since Incremental Backup only
     takes a minute, you won't hesitate to use it.


     Multiple Hard Disks

     MegaBack keeps track of all files by drive letter, and pathname so you
     may backup  multiple hard  disk volumes using  the same set  of backup
     disks and index.  When  restoring data, simply specify the originating
     drive to restore data from.


     Complements Tape Backup

     Those  of you with  tape backup systems  know how  time consuming tape
     backup can be.   Tape backup is  great for full volume  backup, or for
     regularly backing up very large systems, but it is often not efficient
     for regular daily  or even hourly backup.   Tape processing  takes too
     long!

     MegaBack does  not currently backup  to tape devices,  but is  still a
     great complement  to tape  backup systems.   Consider using  your tape
     system to do  full volume backups of  your hard disk drive.   Then use
     MegaBack for  Incremental Backup  of changed  data.   Your incremental
     backups will only take a  couple of minutes a day.   You will be  much
     more likely  to  take the time to do  daily  backup and your hard disk
     files will be better protected from loss.





     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 5


     To restore a system from  a combined tape/MegaBack backup, restore the
     entire backup from tape and then restore from MegaBack.  MegaBack will
     update the changed files with its copy.


     Select/Exclude

     Not all files need backing up!  This  may sound a little reckless, but
     there are often many files kept on hard disks that are easily replaced
     and do not justify  using backup time and space.   Software developers
     don't need  to backup intermediate  compiler .OBJ files and  test .EXE
     files.  Word  processing systems often create .BAK  or .BK! files that
     are redundant copies of their original files.  

     MegaBack  provides a Select/Exclude capability  to let you select only
     the files  to be backed  up, or to  exclude files or  directories from
     backup processing.   Use this facility to  reduce your backup time and
     the  amount of backup disk space needed.  MegaBack options indicate if
     you want to select files for backup, or back up an entire drive except
     specified files.  You select how its processing is to operate.


     Reliability

     The  most important  question  to  ask of  any  backup  system is  how
     reliable  it is?   MegaBack has  been designed  to safely  backup your
     files and double  check the backups to make sure they are accurate and
     correct.  In addition, file  and index recovery utilities are provided
     to make sure  files can be  restored even when  hard disk indexes  are
     lost,  or  when  sections  of  backup disks  are  lost  or  destroyed.
     MegaBack goes to  great lengths to  recover as  much data as  possible
     from your backup  set in the  event errors are  found.  Following  are
     MegaBack's data integrity features:

     --   MegaBack uses standard,  reliable, DOS I/O  routines to read  and
          write backup  data.   You do  not have  to worry  about it  being
          compatible with your system.

     --   You may activate optional DOS  VERIFY checking to confirm data is
          properly written to  disk.  This causes DOS to verify each record
          is correctly written to diskette before writing the next  record.

     --   A second MegaBack backup verification feature rereads all data on
          a backup  volume before  continuing to the  next volume.   Backup
          data is verified before backup is considered complete.

     --   MegaBack keeps a  CRC check value on each backup  file to confirm
          files are restored exactly as they were when they were originally
          backed up.

     --   A backup volume verify feature  lets you compare backup data with
          actual hard disk files  at any time.  You may use  it to verify a
          backup is accurate.





     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 6


     --   MegaBack  detects recovered,  and unrecoverable  disk I/O  errors
          during backup, and  asks you if it can take another backup of all
          files on the disk to a new volume.  MegaBack knows if one file on
          the diskette  has a problem,  the diskette cannot be  trusted and
          should be replaced.

     --   Restore processing recovers from disk I/O errors and restores all
          possible files from the bad disk volume.

     --   The backup indexes stored on the hard  disk are also backed up to
          the last backup volume, and  may be restored from the backup  set
          if they are lost.

     --   If the backup  indexes stored on the  last backup volume  are not
          recoverable, a MegaBack  utility is available to  scan individual
          backup disks and recreate the hard disk index.

     You  may think  all these  precautions are  excessive, but  users have
     different  and sometimes very stringent requirements for the integrity
     of their data.  MegaBack strives to provide the best data recovery and
     integrity found in a backup system.  You may optionally deactivate the
     verify features to improve your backup performance if you like.


     System Setup/Installation

     To install MegaBack take the following steps...

          1.   Place distribution diskette in any diskette drive.

          2.   Enter the following INSTALL command.   (If you are not using
               drive  A, substitute  the appropriate  drive  letter as  the
               first letter in the command.)

                         A:INSTALL

               Once  the  installation  is  complete,  you  will  find  the
               following  files installed in the selected directory on your
               hard disk:

               MB.EXE         The MegaBack program file.

-->            MBALARM.EXE    MegaBack's  alarm  utility  to   periodically
                              remind you of backup needs.

               MegaBack.HLP   Contains the context sensitive help.


               The first time MegaBack is  started it builds files it needs
               for its general operation.  They are:

               BAKOPT.DAT     The options file. These options are set using
                              the Setup option from the MegaBack menu.





     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 7


               BAKVOLIX.DAT   MegaBack's index containing information about
                              each backup volume it maintains.

               BAKFILIX.DAT   MegaBack's index containing information about
                              each file maintained in backup sets.

               Note:  Each  of  the  installed file  names  begin  with the
               letters "BAK".  MegaBack allows multiple backup disk sets to
               be  created.     Each  set   is  assigned  a   three  letter
               identification.  MegaBack's index and option file names will
               be  prefixed with the  three letter identifier  on secondary
               backup  sets so backup set data is maintained independently.
               Alternate  backup   sets  will   be  discussed  further   in
               subsequent sections of this manual.

-->       3.   Consider   implementing  the  backup  alarm  utility  to  be
               executed each time your system is started. The alarm utility
               is documented  later in this  manual.   Basic implementation
               requires   adding  the   following  lines  to  your   system
               AUTOEXEC.BAT file.  They should be added after at the end of
               the file,  but  before any menu  procedure or  DOS  shell is
               started.

                        \MEGABACK\MBALARM
                        IF ERRORLEVEL 1 \MEGABACK\MB

               These  lines will cause  MegaBack to determine if  backup is
               needed each  time you start your  computer.   When backup is
               needed,  you will  be asked  if backup is to  be  started or
               bypassed.  Other options for this utility provide additional
               capabilities  to  monitor  and  remind  you  of  your backup
               status.


     Setting system options

          MegaBack is installed with default  system options.  Verify these
          options before using MegaBack.  Enter the MB command from the DOS
          command line:

                    C> MB<Enter>

-->       From  MegaBack's  Main  Menu,  use  the  "Options"  menu item  by
          pressing 'O',  or by using the menu selection bar.   Once in this
          options menu, select "Basic system options."

          MegaBack's options  will be  displayed.   Examine and  modify the
          options  as  they  are  appropriate  for   you.    The  following
          descriptions will help  you decide what options to  choose.  Help
          is always available by pressing <F1> at any time.








     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 8


          Drive to backup to?
          ------------------------

          Enter the letter of  the DOS device you will use  to write backup
          data.  This  may be the drive  letter of any valid  DOS mountable
          disk device.   You may  use 5  1/4 or 3  1/2 diskette formats  or
          large capacity demountable hard disk type devices.

-->       Disk capacity?
          --------------

          Specify th size of disk you will be using for backup. Each backup
          disk should be the  same size.   This size is used  when MegaBack
          formats new diskettes for the backup set.

          If  you incorrectly  specify a size of  a high  density  disk and
          place a low density disk  in the drive,  MegaBack will format the
          disk  as  a  high  density  disk   and  format  errors   will  be
          encountered.

          Level of compression desired?
          -----------------------------

          Use  the Right  and Left  cursor positioning  keys to  select the
          level of compression desired for data written to backup  volumes.

               NONE      Do not  compress backup  data.   Will  provide the
                         fastest   possible   backup,   but  you  will  use
                         additional backup disks.

               MINIMUM   Provides  about 40% compression of data but is not
                         as slow as higher compression levels.  This is the
                         recommended level of compression.

               STANDARD  Provides  about 45% compression on data but is not
                         as slow as MAXIMUM compression.

               MAXIMUM   Provides  50-60% compression  but  is slower  than
                         other compression.

          Backup drives:
          --------------

-->       Optionally enter one or more backup device drive letters MegaBack
          is to backup data  from.  For most users,  drive letter C will be
          specified. You may specify up to eight different drive letters in
          any  sequence.  MegaBack  will  automatically  process all drives
          during backup.

          If you  leave this field  blank,  MegaBack  will use command line
          parameters to determine the backup source drive,  or will ask for
          the drive to process before backup starts.






     MegaBack Plus           Copyright 1993 by Patri-Soft            Page 9


-->       Synchronize backup index at backup time? (Y/N/Ask)
          --------------------------------------------------

          Index  synchronization  is the  process  of  scanning  MagaBack's
          backup index to mark any files  that may have  been deleted since
          the last backup.   Over the course of  several incremental backup
          processes,  files deleted  from you system  will still  be in the
          index as  existing files.  If you need to recover your hard disk,
          these files would  be incorrectly  restored.   Periodically it is
          good  to synchronize the  indexes with the contents  of your hard
          disk to avoid this problem.

          Index synchronization is usually done just  before backup starts.
          Specify  <N>  to ignore  synchronization,  <Y>  to  automatically
          synchronize the indexes before every backup, and  <A> to be asked
          if synchronization is desired before backup.  We recommended  <A>
          or  <N>  as automatic  synchronization  on  every  backup is  not
          usually needed.

          Use DOS Verify flag? (Y/N)
          --------------------------
          DOS  provides a  Verify feature  to check  that data  is properly
          written   during  disk  write  processing.    This  feature  adds
          additional  time to  verify  disk  data  during  processing,  but
          provides an additional  level of  assurance that  backup data  is
          properly  written  to disk  and  can  later  be accessed.    This
          verification  may  also  be  activated  through  the  DOS  VERIFY
          command. Documentation about VERIFY may be found in DOS reference
          manuals.

          Enter 'Y' to have MegaBack activate the DOS VERIFY feature during
          its operation.  We recommend you use this feature.

-->       Verify data after it is written? (Y/N)
          --------------------------------------
          For  data integrity, MegaBack  can verify backup  volume contents
          after writing all data to a backup volume.

          The  verify process  is performed  just before  you are  asked to
          remove a backup volume from the drive.  Verification rereads  the
          entire disk to make sure the data is accessible.

          Sound speaker tones when action needed? (Y/N)
          ---------------------------------------------
          If  you  dislike   the  speaker  sounds  MegaBack   makes  during
          processing,  specify  <N>  to have  MegaBack  disable  all sounds
          during its operation.

          When  <Y> is specified, you will hear a quiet tic as each file is
          backed up. This gives you audible signal that backup is currently
          working.   You will also  be beeped whenever MegaBack  is waiting
          for you to take an action, such  as placing another volume in the
          drive.





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 10


          Use exclude/select facility as exclude or select? (E/S)?
          --------------------------------------------------------
          You may setup MegaBack  to backup selected files and  directories
          on  your  hard  drive,  or  to process  all  files  except  those
          specifically  excluded.    Enter  <E>  to  make  MegaBack's  file
          selection facility an exclusion facility.   Enter <S> to have the
          file  selection facility  specify all  files  and directories  to
          backup.  The  file select/exclude facility is found in MegaBack's
          utilities  menu and may  be found by  pressing <U>  from the main
          menu.

          Reset archive attribute on files after backup? (Y/N)
          ----------------------------------------------------
          Backup  processing  normally   resets  DOS's  archive   attribute
          (indicating files  have changed  since backup)  after backing  up
          each  file.    This  lets Incremental  Backup  locate  only newly
          changed  files during its  processing.  Enter  <N> if  you do not
          want the DOS attribute reset.

          You may want  to specify <N> when  testing MegaBack, or to  run a
          special backup to a secondary backup diskette set.

          Reset archive attribute on files after restore?
          -----------------------------------------------
-->       This  option  indicates  how the  DOS  archive  attribute will be
          set after  MegaBack restores  files.  Specify <N> for MegaBack to
          set the DOS archive  attribute to  indicate the file has not been
          changed  since  the  last backup.  Specify  <Y>  to set  the flag
          indicating the file has been changed since backup.


     Test to verify installation

          After MegaBack is successfully installed  you will want to take a
          few minutes to learn how it  works and develop come confidence in
          it.   You  may test  MegaBack without  resetting the  DOS archive
          (file  changed) flag  by setting  the  "Reset archive  attribute"
          Setup option to <N>.

          Explore MegaBack's features by backing up and restoring files and
          directories.  When  restoring files, always specify  an alternate
          restore target pathname so you will not replace the files on your
          hard disk during your evaluation.

          Since MegaBack allows multiple backup sets to be created, you can
          create a special backup set to  test or demonstrate MegaBack.  If
          you  would  like to  use  this  feature  specify /ID:TMP  on  the
          MegaBack command line or set  a DOS environment variable with the
          backup set id desired.

                    SET MEGABACK=/ID:TMP

          You may  delete the  test  backup set  by using the  Reset Backup
          Indexes option from MegaBack's utility menu.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 11


          Backup volumes used for the test backup set may be reused for any
          other backup set.   You do not  need to delete  the files on  the
          disk before reusing them as MegaBack will do this for you.



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 12


     Quick Start guide

     If you dislike  reading manuals and want  to get right to  the action,
     this section will get  you started using MegaBack.  Remember  the <F1>
     key provides direct access to information about your current action in
     MegaBack.    The  context  sensitive  help  system  provides  complete
     information for using the system.

     Starting MegaBack

          Use the MB  command to start  MegaBack.  MegaBack may  be started
          from any  directory or disk.   MegaBack uses indexes  and options
-->       from the directory where MB.EXE is located.

          You may place  the MegaBack  directory in  your PATH  environment
          variable (see your DOS manual)  or may specify the pathname where
          the MB command exists as the command prefix.  Following are  some
          command examples:

               MB
               \MegaBack\MB
               C:\MegaBack\MB

          MegaBack can be  run from the DOS command line using command line
          parameters.  Command line parameters are documented later in this
          manual.   This  section assumes  you  are using  menus to  direct
          MegaBack's operation.

-->       We assume  you have already used the "Set system options"  of the
          Options Menu to specify system options. If you have not done this
          yet, do it now.


          Backing up files

          1.   Starting from the menu...

               Select  the  Backup  function  from  MegaBack's  main  menu.
               MegaBack will scan the selected hard drive to determine  how
               many files  exist on your volume  to be backed  up, and will
               also count  all files that  are marked with the  DOS archive
               attribute as changed since their last backup.

               You will  be presented  with a selection  screen that  shows
               totals  for full  and  incremental  backup.    These  totals
               indicate how many  files will be backed  up in each  type of
               backup, how  many backup  disk volumes are  to be  used, and
               approximately  how long  backup will  take.   The  estimated
               backup time may be off considerably during your first run of
               MegaBack   since  it  has  no  history  of  your  computer's
               performance.   After  the first  backup,  MegaBack uses  the
               previous   backup's  performance   statistics  to   estimate
               required time for backup.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 13


               Four possible  actions are possible  from this screen.   Use
               the cursor  arrow keys  to select an  option and  then press
               enter, or press the letter associated with the selection you
               desire.

               Full Backup

                    MegaBack will backup  all files on your hard  disk.  If
                    you  have selected or  excluded files for  backup, only
                    those files  designated for  processing will  be backed
                    up.

                    Full backup begins by asking if you want to start a new
                    backup set or to continue adding to an already existing
                    one.  Once this decision is made backup processing will
                    begin.

               Incremental Backup

                    Process  only files marked  with the DOS  archive (file
                    changed since backup)  attribute.  These will  be added
                    to an already  existing backup set.  If  no full backup
                    has  been  completed,  MegaBack  will  warn  you before
                    starting Backup.

               List Files

                    You may  obtain a  scrollable list of  all files  to be
                    backed  up  with  Full or  Incremental  backup.   After
                    selecting  this option, you will be  asked if ALL files
                    are to be listed, or if CHANGED files to be included in
-->                 Incremental backup are to be shown.   You may press "O"
                    from  the file  list display  to display  Other  fields
                    related to the files being listed.

                    The list files feature lets  you verify what data is to
                    be  processed before starting backup.  It is especially
                    useful to verify Incremental  Backup in processing only
                    those  files you desire to be backed  up.  You may want
-->                 to  review this  list  and then use  MegaBack's exclude
                    facility to exclude some files before backup begins.

                    ACTIVE KEYS:  Several keys are active in the listing.

                    X       Exclude  all  files  in  the  directory  of the
                            current files.
                    <SPACE>, <RIGHT ARROW>
                            Exclude  the specific file  under the highlight
                            bar. <SPACE> toggles
                    D       Delete the file under the highlight bar.
                    ALT-D   Delete file without confirmation
                    O       Show Other information about the listed files.
                    F10     Save the changes made to exclude file.




     MegaBack Plus        Copyright 1993 by Patri-Soft              Page 14


               Exit back to main menu

                    Press the  <Escape> key  to return  back to  MegaBack's
                    main menu.

          2.   Backup processing...

               MegaBack  will  present a backup  status display.   You will
               immediately be asked to place a backup volume in the  output
               drive.   Place  any  formatted or  unformatted  disk in  the
               drive.  IF THE DISK CONTAINS DATA IT WILL BE ERASED!   Press
               <Enter> to indicate the volume is ready.

               Backup processing  will progress while  continually updating
               the status on the display.  You will be asked for additional
               disk volumes as  they are needed.  Label  each backup volume
               with  the  number  indicated  by MegaBack.    It  is usually
               sufficient to  place a label  with a large  number on it  on
               each diskette.

          3.   Backup termination...

               When  backup processing ends, MegaBack saves its own indexes
               and options at  the end  of the backup  data on the  volume.
               This  may be  used if  you need  to recover  the indexes  on
               another machine.


          Restoring files


          1.   Restoring files...

               From  the  MegaBack  Main  Menu,  select  restore  to  begin
               processing.


          2.   Initial restore file selection...

               There are  two levels  of file selection  in restore.   Each
               level further qualifies files to be restored.

               At  the first level,  you indicate any  pathname or filename
               wildcard entries to be used  to select files to be restored.
               On  the same  display you  can specify beginning  and ending
               dates for files qualify for restore.

               Press <F10>  after entering the  information.   You are  not
               required to enter any  data at this  point.   Press <F10> to
               proceed to the next selection display.



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 15


          3.   Restore now or list specific files...

               MegaBack now asks  if you want to restore all files found in
               the  backup indexes matching  the selection criteria,  or if
               you want to review a list of these files and select specific
               ones to restore.

               If  you have already entered enough  information to have the
               proper  files  restored, you  are  ready  to  begin.   Start
               restore by pressing <R>.

          4.   Selecting files from the selection list...

               Selecting <L> for List will cause MegaBack to list all files
               that  qualify  your  selection  criteria.    Files  will  be
               displayed in a scrollable selection  list.  You may mark any
               number of  files to  be restored.   Use the  <Space Bar>  to
               toggle selection on or off.

               Press <F1> key for other features  of restore.  You may sort
               the list,  zoom it  larger to fill  the display  and display
               alternate  information about  the  backed  up  data.    When
               finished  with  the  selection list,  press  <F10>  to begin
               restoring the selected files.

          5.   Restore processing...

               The  restore  status  display  will be  shown  and  you will
               immediately be asked to place  a specific backup disk in the
               drive.  Press <Enter> to indicate the disk is ready. Restore
               will begin and  its status will be reported  until all files
               are processed.

          6.   Restore termination...

               When   restore  completes,   MegaBack  displays   a  message
               indicating it  is done.   Remove the backup volume  from the
               drive.

          That's  all there  is to  basic MegaBack  processing.   There are
          several features that have not been mentioned in this quick start
          section.  Use  the  help  system  or browse  this manual to learn
          more about the system.








     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 16


     How MegaBack works

          Backup Volumes

          Different disk device  types may be used to  contain backup data.
          These  devices  may include  3  1/2 diskettes,  5  1/4 diskettes,
          removable hard disk devices, optical disk devices, and more.  Due
          to this  variety of  backup storage devices,  any backup  storage
          media is referred to by MegaBack as a backup volume.

          MegaBack backup processing takes the files you  select and writes
          them on backup  volumes.   Each file  is written to  volume in  a
          compressed  format.   Each MegaBack  backup  volume contains  two
          files.  The first file is a backup volume label file  identifying
          the  backup  volume as  well as  information about  other volumes
          written before and after the volume.

          The  second  file on  a backup  volume  contains  all backup data
          written  to  the  volume.    This file  contains  any  number  of
          compressed backed  up files and  corresponding information needed
          to restore them.  Since all files  are written to a single output
          file,  backup  disk  space is  saved  and  backup  performance is
          improved.

          To  use volumes  efficiently, each  volume  is completely  filled
          before a new volume is started.  Whenever a new backup process is
          started, MegaBack  asks for the  last backup volume used  for the
          previous backup.  It then appends new data being backed up to the
          same volume.


          Backup Sets

          A set of backup volumes is a series of numbered diskettes or disk
          volumes containing  backup data.   MegaBack uses only one  set of
          backup data for any backup process.  To use an alternative backup
          set you must start MegaBack with 3 character set identifier.  Use
          the /ID:xxx parameter on the MegaBack command line.

          Separate  hard disk  backup indexes  are created for  each backup
          volume  set.   Basically,  backup  sets  let  you keep  track  of
          multiple backups on the same system.  A common reason for keeping
          multiple backup  sets  is to  manage a  backup set  for your  own
          system while still  being able to examine and  even restore files
          from secondary backup sets created on other systems.

          To restore files from another  user's backup set, start  MegaBack
          with the  /ID:xxx parameter  to  specify a  secondary backup  set
          name.   Use  MegaBack's  index recovery  utility  to recover  the
          user's backup index from their last backup diskette.  Now you may
          list and restore  the files as if  they were backed up  from your
          own system.






     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 17


          Backup File Index

          As files are  backed up, an entry  for each  file is  placed in a
          backup  index maintained in  the MegaBack directory  on your hard
          disk.  This  index is always  maintained on the  hard disk.   The
          backup  index  record  contains  all  information  necessary  for
          locating and restoring files.  The backup index makes it possible
          for MegaBack to  list backup files without having  to read backup
          volumes.

          When you restore a file, MegaBack uses its index to locate files.
          When files to be restored  are selected, information in the index
          identifies   the  exact  volumes  needed  to  restore  the  file.
          MegaBack starts restore processing and asks you to place specific
          volumes in the drive as they are needed.


          The Backup Volume Index

          In addition to the backup  file index, MegaBack also maintains an
          index about each backup volume.  The backup volume index contains
          information about each  volume and its status in  the backup set.
          The  index is  maintained  as  a separate  file  in the  MegaBack
          directory.


     MegaBack reference

          Preparing backup volume sets

          Before using MegaBack  you will need to  prepare a set of  backup
          volumes.   When using diskettes  as backup volumes, start  with a
          fresh box  of the  highest quality diskettes  you can  find.   Of
          course, MegaBack  can't tell  the quality of  your disks,  but if
          your backup  data is  important to you,  it is  worth a  few more
          cents per disk  to avoid the problems and wasted  time poor disks
          can cost you.

          Take  the labels provided with  the disks and  using a large felt
          marker, number the disks sequentially 1 through 10 (or whatever).
          If you plan on keeping multiple backup disk sets, you should mark
          all the disks in a set with a set identifier.

          MegaBack can keep  separate indexes for different  sets of backup
          volumes.   MegaBack only works with one backup  set at a time and
          places secondary  backup set names  in the upper right  corner of
          every display  so you may  be sure to  use the correct disks.   A
          good use for different backup  sets is to use a secondary  backup
          set  name to  restore files  from another  user's backup  on your
          system.








     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 18


     MegaBack's Main Menus

          Following are examples  of MegaBack's main  menu structure.   The
          (...) following a menu item indicates the  menu item takes you to
          another  sub-menu.   All other  selections  immediately take  the
          action specified.

          The  capitalized  character  on  each  menu  line  indicates  the
          specific   menu  selection  character  that  can  be  pressed  to
          immediately select  a menu  item.   You may  use a  mouse with  a
          single click to  select a menu option,  or use the cursor  up and
          down keys, followed by the <Enter> key, to select menu items.

                Main Menu
                   Begin backup
                   Restore backup data
                   Utilities...
                   Options...
                   Exit

                       Utilities
                          Synchronize hard disk
                          Reset backup indexes
                          recover backup Indexes
                          Create reports
                          Verify backup data
                          Quit to main

                                Options
                                   Exclude/select files from backup
                                   Basic system options
                                   Advanced system options
                                   Defin backup sets
                                   Password protection
                                   Set alternate display type
                                   Quit to main


     Backup Processing

     Backup begins by asking you to indicate the hard disk to be backed up.
     Following is an example:

-->        ______________________________________________
          |                                              |
          |      Select drive to be backed up:           |
          |                                              |
          |      ___           ___           _______     |
          |     | C:|         | D:|         | Other |    |
          |     |___|         |___|         |_______|    |
          |________ <Enter> accepts, Esc exits __________|




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 19


-->  Use  a  mouse, the  drive letter,  or  the left  and right  arrow keys
     followed  by  enter to  specify the drive  to be  acked up.   When you
     select  "Other",  MegaBack will ask you to specify the drive letter to
     be processed.

     MegaBack begins backup by scanning the selected drive to determine the
     number and size of files to be backed up in either Full or Incremental
     backup processing.  Status lines at the bottom of the display show the
     progress during this scan.

     The  following display  is  presented to  let you  select the  type of
     backup to be done:


     Backup Type Selection Display

      ___________________________________________________________________
     | MegaBack             Select Backup Type Desired           F1=HELP |
     |                                                                   |
     |                                         ____________________      |
     |   BACKUP ESTIMATES                     |                    |     |
     |   ________________                     |    FULL BACKUP     |     |
     |                                        |        <F>         |     |
     |   FULL BACKUP                          |____________________|     |
     |                                         ____________________      |
     |    Files:      1439                    |                    |     |
     |    Characters: 30,483,331              | INCREMENTAL BACKUP |     |
     |    Disks:      85                      |        <I>         |     |
     |    Minutes:    60                      |____________________|     |
     |                                         ____________________      |
     |   INCREMENTAL BACKUP                   |                    |     |
     |                                        |     LIST FILES     |     |
     |    Files:      32                      |        <L>         |     |
     |    Characters: 1,372,349               |____________________|     |
     |    Disks:      4                                                  |
     |    Minutes:    2                       Arrows Toggle Selection    |
     |                                           <Enter> Confirms        |
     |                                            <Escape> Exits         |
     |                                                                   |
     |                  Process ALL Files on the Drive                   |
     |___________________________________________________________________|


     The  Backup Type Selection Display shows  you what files both types of
     backup will process, how many backup disks will be required for  each,
     and the approximate amount of time that will be required.

     The estimated  backup time may  be off considerably during  your first
     run  of  MegaBack   since  it  has  no  history   of  your  computer's
     performance.   After  the first  backup,  MegaBack uses  the  previous
     backup's performance statistics to estimate required time for backup.

     Four possible actions  are possible from this screen.   Use the cursor
     arrow keys to  select an  option and  then press enter,  or press  the




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 20


     letter associated with the selection you desire.  The box representing
     the action selected will be highlighted and an explanatory line at the
     bottom of the display, will confirm your selection.


     Full Backup <F>

          MegaBack will backup  all files on your  hard disk.  If  you have
          selected  or  excluded   files  for  backup,  only   those  files
          designated for processing will be backed up.

          Full backup begins  by asking if you  want to start a  new backup
          set, or to continue adding to an already existing one.  Once this
          decision is made, backup processing will begin.

     Incremental Backup <I>

          Process  only  files marked  with the  DOS archive  (file changed
          since  backup) attribute.   These  will  be added  to an  already
          existing  backup set.   If  no  full backup  has been  completed,
          MegaBack will warn you before starting Backup.

     List Files <L>

          You may  obtain a scrollable  list of all  files to be  backed up
          with Full  or Incremental backup.   After selecting  this option,
          you  will be asked if  ALL files are to be  listed, or if CHANGED
          files to be included in Incremental backup are to be shown.

          The  list files  feature  lets you  verify  what  data is  to  be
          processed before  starting backup.   It  is especially  useful to
          verify  Incremental Backup  is processing  only  those files  you
          desire to be  backed up.  You  may want to  review this list  and
          then use MegaBack's exclude facility to exclude some files before
          backup begins.

-->       You may  delete files from the  List files  display  by  pressing
          ALT-D  at any time.   Press  <O>  at any  time to  view different
          information about files listed.

-->       If you see files  you want excluded from the backup  process, use
          the  left and  right  arrow keys to  unexclude,  or exclude files
          from the backup process.  Press  <X> over any file and the entire
          directory the file is located in will be excluded from the backup
          process.    These  exclude  criteria  will  also   be  stored  in
          MegaBack's  permanent exclude file so the  files will be excluded
          from all subsequent backup runs.  If you exclude files from these
          displays,  MegaBack  will again  rescan the  drives to  be backed
          to gather new backup statistics.

     Exit back to main menu <Escape>

          Press the <Escape> key to return back to MegaBack's main menu.



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 21



                    Backup Status Display

      ___________________________________________________________________
     |  ___________           M E G A B A C K                            |
     | |   .. 100% |    Copyright 1992 by Patri-Soft                     |
     | |   ..      |         Backup processing                           |
     | |   ..      |                                                     |
     | |   ..      |                                                     |
     | |   ..      |                                                     |
     | |   ..      |                  Total      Completed     Remaining |
     | |   ..      |   Files:         43         0             43        |
     | |   ..      |   Characters:    1,184,121  0             1,184,121 |
     | |   ..      |                                                     |
     | |   ..      |                                                     |
     | |   ..      |   Path:       D:\BUD\                               |
     | |   XX      |   Filename:   FY1991.WKS                            |
     | |   XX      |   Size:       4,397                                 |
     | |   XX      |   Date/Time:  31JUL91 / 5:31p                       |
     | |   XX      |                                                     |
     | |   XX      |                       Disk statistics for drive A:  |
     | |   XX      |                                Volume 1             |
     | |   XX      |                       >>>>>>>>>>>>>>>>>>>XXXXXXXXX  |
     | |   XX 0%   |                                                     |
     | |___________|                        Total bytes:                 |
     |                                      Bytes used:                  |
     | Percent Complete                     Bytes free:                  |
     |___________________________________________________________________|


     The backup  display keeps you informed  of the progress  of backup. It
     contains the following information:

          Status Bar

               The status  bar at  the left  side of  the  display gives  a
               graphic status of the completion of MegaBack.

          Totals

               The  totals  lines  show  the  number  of  files  and  total
               characters to be  processed, completed, and remaining  to be
               processed.

          Current File

               Shows information about  the file currently being  copied to
               diskette.

          Disk Statistics

-->            The  disk statistics, in  the  lower  right portion  of  the
               display, show the amount of  space used,  and the free space





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 22


               remaining  on the  backup  volume  being  written to.   This
               is  useful  to help  you  know how  long  it will  be before
               MegaBack will ask for the next backup volume.


          Request for backup volumes

          Immediately upon  starting backup you  will be asked to  insert a
          new volume  in the drive.  A message  like the one following will
          be shown:


           _____________________________________________________
          |        Insert backup disk 1 into drive A.           |
          |                                                     |
          |  Press Enter when ready, or ESC for other options   |
          |                                                     |
          |                      Waiting                        |
          |_____________________________________________________|


          MegaBack has searched its volume  indexes and found volume one to
          be the next  volume to  use.  Place  volume #1 in  the drive  and
          press <Enter> to continue processing.

          Press  <Escape> to be presented  with additional options you have
          when mounting a volume.


           ______________[  Waiting for disk #1 ]_______________
          |                                                     |
          | Select desired action:                              |
          | (You may safely quit at this point)                 |
          |                                                     |
          |      ____        ________        ______________     |
          |     |Quit|      |Continue|      |Start new disk|    |
          |     |____|      |________|      |______________|    |
          |_____________________________________________________|


          MegaBack  options indicate when  you may safely  quit processing.
          When a new volume is requested to hold the second part of a  file
          that  spans multiple volumes, you may not quit processing without
          having to restart backup for the file being processed.

          Select Continue by  pressing <C> and you will be  returned to the
          display requesting the volume to be placed in the drive.

          When MegaBack is requesting a  volume from a previous backup, you
          may press <S>  to start another new disk instead of appending new
          backup data to the last used  volume.  Use this feature when  you
          do not have access to the previous backup volume.  You might have
          stored the used disks of your backup set in  another location, or
          temporarily loaned them to someone.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 23


          Recovering from disk write errors

          If DOS  should encounter a  disk write  error when writing to the
          backup volume, you will be presented with messages and options to
          select to continue from the error.  This only applies if  the DOS
          VERIFY flag (see setup) is set on.


           ______________________________________________________________
          |    A disk I/O error has occurred during backup processing.   |
          |    The file currently being processed may not have been      |
          |    safely backed up.  Indicate how to continue:              |
          | ____  _________________  _________  ________________________ |
          ||Quit||Continue Normally||Try again||Force new disk/try again||
          ||____||_________________||_________||________________________||
          |_____________________ <Enter> accepts ________________________|


          This message is presented after  DOS issues its message to RETRY,
          FAIL, or ABORT after a disk I/O error.  If you selected RETRY and
          processing  continued  successfully,  the  file   was  backed  up
          successfully.  If  you selected FAIL or IGNORE, the  file was not
          backed up  correctly.  Select  one of the following  responses to
          indicate how to proceed after the I/O error:


               Quit
                    Stop backing up immediately.

               Continue Normally
                    The  retry  was  successful and  you  want  to continue
                    backing  up.   If  the  error was  caused  by a  faulty
                    volume, you may want to Try again,  or Try a new volume
                    to move  the data for  the file  from the  questionable
                    volume area.

               Try again
                    Backup the file again on a new area  of the same backup
                    volume.   This  will skip  over  the faulty  area of  a
                    volume.   We  recommend using  Force New  disk and  try
                    again over  this option since  it is better not  to try
                    and backup more data on a potentially faulty volume.

               Force new disk and try again

                    (Recommended)
                    Stop  writing to  the current  volume.   Ask for  a new
                    volume and  start backing up  for the same  file again.
                    The file will  be written to the new  volume and backup
                    processing will continue.








     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 24


               Interrupting/Resuming Backup

                    Both  incremental  and  full  backup  processes  may be
                    interrupted  before  they are complete.   MegaBack will
                    keep track  of its  current  status  and  can  continue
                    processing at a later time.

-->                 To   interrupt  backup,   press  ESC   during   backup
                    processing.   Processing  will  pause  after  the file
                    currently  being processed is  backed up to disk.  You
                    will   be  asked  to  verify  you  want  to  interrupt
                    processing or continue without stopping.

-->                 When  you  interrrupt  processing,  the backup indexes
                    will  be written to the  backup volumes and processing
                    will end.   You may terminate  MagaBack  and power off
                    your   system.  The  next  time  MegaBack   backup  is
                    started,  you  may  select the same backup process and
                    processing will resume where it left off.


          Completing backup

          Before backup completes the following message is presented on the
          display.  This  message is for your information only,  you do not
          need  to take  any action.   MegaBack is  letting you know  it is
          saving a  copy of its  backup indexes to  the last  output backup
          volume.

                _____________________________________________________
               |                                                     |
               | Saving Backup index backup to disk. Please wait...  |
               |                                                     |
               |_____________________________________________________|

          Once backup completes, the following message will be presented on
          the display.   This is  to give  you a chance  to examine  backup
          statistics before  leaving the status  display.   Press enter  to
          indicate you are ready to continue.

          The last message shown by backup reminds you to keep track of the
          last  backup volume  used as  it contains  a copy  of the  backup
          indexes for emergency recovery.  Remove the volume from the drive
          and  file it so you can identify it  as the last disk used.  Turn
          it sideways, upside-down, backwards, or just place it in front of
          all other volumes.












     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 25


           _______________________________________________________
          |                                                       |
          |                                                       |
          | Backup complete.  Remove volume from the drive and    |
          | store so you may relocate it if needed for recovery.  |
          |                                                       |
          |               Press <Enter> to continue...            |
          |                                                       |
          |___________________<Enter> to continue ________________|


          An  easy way to  keep track of the  last volume used is  to store
          disk volumes with the used backup volumes behind the unused ones.
          Rotate  the disks  as they  are used.   Always keep the last disk
          used in  the front of the set.  In the  following  figure, assume
          volume 3 was the last backup volume used.



                                            2________
                                           1_|______ |
                                          5_|______ ||
                                         4_|______ |||
                                        3_|______ |||-
                                         | Last  |||-
                                         |   O   ||-
                                         |   |   |-
                                         |_______|


          Once MegaBack  has returned  you back  to its  main menu you  may
          start another backup or exit back to DOS.


     Restore

     Restore is the  process  of copying  a backed up  file back to  normal
     disk storage.  Restore is a copy, not a move.  The backup copy remains
     intact exactly  as before the  restore.  You  may delete  the restored
     copy  and still have access to the data through the saved backup copy.

     MegaBack  makes locating and  restoring files easy.   Several features
     are included to help you organize backups and locate files they  hold.

     Backup  data is  stored in  a special  compressed form  on consecutive
     disks  of offline  storage.  The  special compressed  format obviously
     saves  disk  space  but  also  increases  backup  performance.    This
     compressed format  requires you  to use MegaBack  to restore  any file
     backed up by it.

     MegaBack indexes all  backed up files in  a set of hard  disk indexes.
     When you  search for  a  file to  be  restored, MegaBack's  hard  disk
     indexes are used to locate information about the file.





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 26


     MegaBack gets a  disk location and  a disk number  from the index  and
     asks you to place the disk  in the drive.  It then reads  the data and
     writes it to your hard disk.

     Restore begins by asking for  specifications for files to be restored.
     There are two levels of restore file selection:

          1.   First  you may optionally enter filename, pathname, and date
               ranges the file must fall within.

          2.   Files matching the first specification may be displayed in a
               scrollable   selection  list   for   your  examination   and
               processing selection.

     Once files are selected, restore processing begins.


     Entering Restore Criteria

     After selecting the Restore option  from MegaBack's main menu you will
     be presented with the following  display which asks for file selection
     criteria.  You  may skip  this selection  level by  pressing <F10>  to
     select all files for restore.

                             Restore File Selection
           ______________________________________________________________
          |  Select files BACKED UP from:                                |
          |             Drive   : *                                      |
          |                                                              |
          |             Path    : *_____________________________________ |
          |                                                              |
          | Pattern to restore  : *.*__________                          |
          |                                                              |
          | Restore TO directory: ______________________________________ |
          |                                                              |
          | Overlay files on restore? (Y/N/Ask/Update): _                |
          |                                                              |
          |  Select files backed up AFTER this date : __________         |
          |                                                              |
          |  Select files backed up BEFORE this date: __________         |
          |                                                              |
          |                       Enter text                             |
          |____________ Press F10 to begin or ESC to abort ______________|


     Selection criteria specification

          Drive  : *

                    Enter  a drive letter  indicating the drive  files were
                    originally backed  up from.   '*'  indicates to  select
                    files backed up from any drive.






     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 27


          Path   : *

                    Enter a pathname where files  were backed up from.  '*'
                    indicates  to select files backed up from any directory
                    name.  A  directory specification may  end with '*'  to
                    indicate   the  files  are  to  be  selected  from  any
                    directory  name beginning with the name specified up to
                    the *.  Valid specifications are:

                         \
                         \WP
                         \WP*
                         \WP\LETTERS
                         \WP\LETTERS\

          Pattern to restore  : *.*

                    Enter a complete  filename or wildcard pattern  name of
                    the backed  up files.   Extended  wildcard capabilities
                    allow  you to enter multiple * in a name specification.
                    The  * indicates any number  of characters may exist in
                    this portion of the name.  Valid specifications are:

                         AUTOEXEC.BAT
                         AUTO*.BAT
                         AUTO*.*
                         *.*
                         *TOEX*.BAT
                         *U*O*X*.BAT

          Restore TO directory:

                    Optionally enter a  target pathname where files  are to
                    be restored.   This is a full  pathname including drive
                    letter.  If no  directory is specified, the  files will
                    be  restored to their  original drive  and directories.
                    Valid specifications are:

                         C:\WP
                         \WP
                         C:\WP\LETTERS\

-->                 You  may  also specify  a  drive  designator  without a
                    directory name to indicate  files are to be restored to
                    the  original  directory  name  on  a  different drive.
                    Specify the drive letter followed by a colon:

                        D:

-->       Replace duplicate files? (Y/N/Ask/Update):

                    If  during  restore,  MegaBack  finds  a  file  already
                    defined on the hard disk with the same name as the file





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 28


                    being restored, it must decide if the  existing file is
                    to be replaced, or to bypass restoring the file.

                    The following options to indicate what action  MegaBack
                    is to take when files of duplicate names are found.

                    Yes       Replace the existing file with the new file.

                    No        Don't  overlay the existing  file.   Skip the
                              restore for  the file and  continue restoring
                              other files.

                    Ask       Prompt when  duplicate files are  encountered
                              and ask if the file is to be replaced, or the
                              restore bypassed.

                    Update
                              Replace files  that are  newer than  the ones
                              present on the  disk.   The DOS  date of  the
                              file on the hard disk will be compared to the
                              DOS date of the backup file recorded when the
                              file was originally backed up.

          Select files backed up AFTER this date :

                    Optionally enter a date to reject files last created or
                    updated on or prior to the date.

          Select files backed up BEFORE this date:

                    Optionally enter a date to reject files last created or
                    updated on or after the date.


     Listing Files to Restore

          Once  restore file selection has been  made, you will be asked if
          you would like to view and further select files to be restored or
          immediately begin the restore process.  The  following display is
          presented as the last step prior to starting the restore process.

           ___________________________________________________________
          |                                                           |
          | Do you want to List the files for manual selection, or    |
          | Restore them immediately?                                 |
          |                                                           |
          |              ____                    _______              |
          |             |List|                  |Restore|             |
          |             |____|                  |_______|             |
          |_______________ <Enter> accepts, Esc exits ________________|

          If you have already  specified sufficient criteria to  select all
          files to  be restored, press  <R> to restore all  selected files.





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 29


          If  you would  like  to  list all  files  matching the  selection
          criteria  entered, press  <L>.    You will  be  presented with  a
          scrollable selection list of files.


     Restore File Select List Processing

          Scrollable  selection lists  provide  complete information  about
          files maintained in MegaBack's backup indexes.  Due to the amount
          of data stored about  each file, MegaBack provides two  different
          views of  this list.   Each view  shows a  different category  of
          information about backed up files.

     Contents of backup list views


          View # 1
          ---------------------
          Filename
          DOS File Date
          DOS File Time
          Original file Size
          Original Pathname


          View # 2
          ---------------------
          Filename
          Backup Date
          Backup Time
          Backup Size
          Original Size(again)
          Compression Ratio
          Backup Volume Number


     When  the scrollable  selection list  is  first displayed  VIEW #1  is
     shown.  To change between the two different views, press the <F6> key.
     As <F6> is repeatedly pressed the opposite view is shown.

     The  following keys  are active  when  the restore  selection list  is
     displayed:


     <Space Bar>    Toggles selection - marks unmarked files to be selected
                    for restore.   Unmarks marked files to remove them from
                    being selected.

     <Right Arrow>
                    Marks file to  be  selected for restore.   Advances the
                    file selection bar to the next file.   Holding down the
                    key will mark a series of files.






     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 30


     <Left Arrow>   Unmarks file selected  for restore.  Advances  the file
                    selection bar to  the next file.  Holding  down the key
                    will unmark a series of files.

     <F1>           Help

     <F2>           Zoom.   When first  displayed, the  scrollable list  is
                    shown in reduced size to make room for help text at the
                    bottom of  the display. Press  <F2> to zoom  the screen
                    larger.  The help text at the bottom of the screen will
                    disappear.  Press <F2> again to reduce the  display and
                    view the help at the bottom.

     <F3>           Enter a DOS Command

     <F6>           Show next VIEW.  Toggles between the different views of
                    the backup file list.

     <F7>           Sort  the selection list.  You will be presented with a
                    sort selection menu as follows:

-->                           __Change Sort order__
                             | Name order          |
                             | Directory order     |
                             | daTe order          |
                             | Backup date order   |
-->                          | Size order          |
-->                          | Volume/offset order |
                             |_____________________|

                    Name order     Sorts by filename.

                    Directory order
                                   Sort by filename within directory name.

                    daTe order     Sort  by  the  date  the file  was  last
                                   updated or created (before it was backed
                                   up).

                    Backup date    Sort files  in sequence by the date they
                                   were backed up.

-->                 Size order     Sorts by file size.

-->                 Volume/offset  Sort files  in the order  they exist  on
                                   the backup volumes.

-->  <F8>           Print the list being  displayed.  You  will be asked to
                    be asked to indicate the printer identifier the list is
                    to be printed on.

     <F10>          Start restore.  After you have marked one or more files
                    to be  restored,  press  <F10>  to accept the  selected
                    items and start restore.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 31


     <Escape>       Exit file selection list and quit restore processing.


     Following are examples  of the different views of  the selection list.
     Select one or more files to be restored or press <Escape> to return to
     MegaBack's main menu.  After  selecting the desired files, press <F10>
     to start restoring the files.

                                     VIEW #1

           ____Name__________Date______Time______Size_______Path_______
          |   AUTO.BAT       15JUN91    2:26p    134        C:\BAT\    |
          |   B.BAT          15JUN91    2:39p    64         C:\BAT\    |
          |   BC.BAT          7SEP91    2:39p    83         C:\BAT\    |
          |   BCX.BAT        19MAY91    6:30p    144        C:\BAT\    |
          |   BITFAX.BAT     27MAR91    4:01p    29         C:\BAT\    |
          |   C.BAT          19AUG90    7:29p    99         C:\BAT\    |
          |   C2.BAT          9MAR91    7:54a    56         C:\BAT\    |
          |   DELA.BAT       20DEC90    7:48a    16         C:\BAT\    |
          |   DELB.BAT       19JUL91    6:22a    23         C:\BAT\    |
          |   DIRA.BAT       19NOV86    2:23p    11         C:\BAT\    |
          |   DIRB.BAT       25APR91    6:59a    8          C:\BAT\    |
          |__________________ F10 accepts, ESC exits __________________|


                                     VIEW #2

           __Name_______BakDate___BakTime___BakSize_____Ratio___Disk___
          | AUTO.BAT     8OCT91   10:17a    134         1.00%    1     |
          | B.BAT        8OCT91   10:17a    64          1.00%    1     |
          | BC.BAT       8OCT91   10:17a    83          1.00%    1     |
          | BCX.BAT      8OCT91   10:17a    144         1.00%    1     |
          | BITFAX.BAT   8OCT91   10:17a    29          1.00%    1     |
          | C.BAT        8OCT91   10:17a    99          1.00%    1     |
          | C2.BAT       8OCT91   10:17a    56          1.00%    1     |
          | DELA.BAT     8OCT91   10:17a    16          1.00%    1     |
          | DELB.BAT     8OCT91   10:17a    23          1.00%    1     |
          | DIRA.BAT     8OCT91   10:17a    11          1.00%    1     |
          | DIRB.BAT     8OCT91   10:17a    8           1.00%    1     |
          |___________________ F10 accepts, ESC exits__________________|





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 32


     Starting Restore

     After  starting  restore  MegaBack determines  the  volumes  needed to
     restore the files and immediately  requests you place the first volume
     needed in  the input  drive.  Following  is an  example of  the volume
     mount message.

           _______________________________________________________
          |             Insert backup 1 into drive A.             |
          |                                                       |
          |   Press Enter when ready, or ESC for other options    |
          |                                                       |
          |                        Waiting                        |
          |_______________________________________________________|

     Locate the requested  volume from your set of backup volumes and place
     it in the  drive.  You may  terminate restore at any time  by pressing
     <Escape>.  All files restored to this point of processing are restored
     correctly.  Other files selected will  need to be selected again in  a
     subsequent restore process to be restored.


     Restore Processing

     The restore display  is presented throughout the restore  process.  It
     provides status of the restore.


                             Restore Status Display

           _______________________________________________________________
          | _____________                 M E G A B A C K                 |
          | |  ..  100% |           Copyright 1992 by Patri-Soft          |
          | |  ..       |                Restore processing               |
          | |  ..       |                                                 |
          | |  ..       |              Total      Completed     Remaining |
          | |  ..       |  Files:        3                                |
          | |  ..       |  Characters:   219                              |
          | |  ..       |                                                 |
          | |  ..       |  Path:       C:\BAT\                            |
          | |  ..       |  Filename:   B.BAT                              |
          | |  XX       |  Size:       64                                 |
          | |  XX       |  Date/Time:  15JUN91 / 2:39p                    |
          | |  XX       |                                                 |
          | |  XX       |                  Disk statistics for drive C:   |
          | |  XX       |                  >>>>>>>>>>>>>XXXXXXXXXXXXXXX   |
          | |  XX       |                  0%       freespace      100%   |
          | |  XX  0%   |                                                 |
          | |___________|                   Total characters:             |
          |                                  Characters used:             |
          | Percent Complete                 Characters free:             |
          |_______________________________________________________________|






     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 33


     The  restore status  display keeps  you  informed of  the progress  of
     restoring files. It has the following basic contents:

          Status Bar

               The  status bar  at the  left side  of  the display  gives a
               graphic status of the completion of MegaBack.

          Totals

               The  totals  lines  show  the  number  of  files  and  total
               characters to be  processed, completed, and remaining  to be
               processed.

          Current File

               Shows information about the file currently being restored.

          Disk Statistics

               The  disk stats  shown in  the  lower right  portion of  the
               display show how much space is used  on the target hard disk
               and how much freespace remains.


     Overlaying Files with duplicate Names

          If MegaBack finds that a file with the same name as the one being
          restored already exists in the target directory, it may overwrite
          the file with  the backup version, bypass restoring  the file, or
          compare the dates and times of the two files and restore the file
          only if it is a more recent copy than the version on disk.

          MegaBack  Setup options let you specify any of these alternatives
          as an action to automatically be taken during restore.  A special
          restore option  of "Ask" indicates  restore processing is  to ask
          what action to  take each time  a duplicate file  name is  found.
          The following question is asked.


           ______________________________________________________
-->       |                                                      |
          | File B.BAT already exists.  Ok to replace?           |
          | ___  __  ______  __________  __________  __________  |
          ||   ||  ||      ||Continuous||continuous||continuous| |
          ||Yes||No||Update||update    ||Replace   ||No replace| |
          ||___||__||______||__________||__________||__________| |
          |                                                      |
          |_____________ <Enter> accepts, Esc exits _____________|









     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 34


          Press Y,  N, U, C, or R to indicate the action to take.  <Escape>
          immediately terminates  restore.   Following are  explanations of
          possible responses:

          <Yes>         Replace the file immediately.  The backup file will
                        overlay the already existing file.

          <No>           Do not  restore the file.   Leave the file  on the
                         hard disk.

          <Update>       Restore the file if it is a newer version than the
                         file on the  target drive. If  the backup file  is
                         older than  the disk  file, bypass  restoring this
                         file.

          <Continuous update>
                        This is  the same  response  as  <Update>  with the
                        additional feature of indicating MegaBack is not to
                        ask this  question again if another duplicate  file
                        name  is  found.   An  answer of  <Update>  will be
                        assumed for all future instances of this  situation
                        during this restore process.

          <continuous Replace>
                        This  is the same  response as  <Replace>  with the
                        additional feature that MegaBack is not to ask this
                        question  again if another  duplicate  file name is
                        found.  An answer of  <Replace> will be assumed for
                        all future instances of this situation during  this
                        restore process.

-->       <continuous No replace>

                        Takes the same action as <No>, and indicates to not
                        replace any additional diplicate files found.


     Completing Restore

          After all files have been restored, the following message will be
          presented  over   the  Restore   Status  Display.     It  is   an
          informational message  to let you  know the last action  taken by
          MegaBack.  Press <Enter> to acknowledge the message and return to
          MegaBack's main menu.


                               ____________________________
                              |                            |
                              |      Restore Complete      |
                              |                            |
                              |___ <Enter> to continue ____|







     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 35


     Restoring to an Empty System

     Both  DOS  and MegaBack  must  first be  present  on a  system  to use
     MegaBack.  If you lose your hard drive and want to restore your backup
     to it you should take the following steps:

     1.   Restore DOS to  the system.  Use  procedures outlined in the  DOS
          reference manual.

     2.   Install  MegaBack  on  the system  using  your  original MegaBack
          installation diskette or a copy of it.

     3.   Use MegaBack  index rebuild  utility to  regenerate the  MegaBack
          indexes from your last backup diskette.

     4.   Use MegaBack restore to restore all files back to your system.


     Making a system recovery boot diskette

     Some users choose  to make a MegaBack system recovery boot diskette to
     use in the  event their system is lost.  The  boot diskette contains a
     bootable versions of  DOS and  the MegaBack  system files.   Take  the
     following steps to make a recovery boot diskette:

     1.   Format a  diskette using  Format's DOS /S  parameter.   This will
          create a diskette  that will boot your machine  without DOS being
          on your system.

               FORMAT A:/S

     2.   Copy the following DOS files to the recovery diskette:

               FORMAT*.COM
               FDISK.EXE

     3.   Build a  CONFIG.SYS file on  the diskette that contains  at least
          the following lines.

               FILES=30
               BUFFERS=30

     4.   Build an AUTOEXEC.BAT on the diskette to start MegaBack.

               PROMPT $P$G
               MD C:\MegaBack
               CD C:\MegaBack
               COPY A:MB.EXE
               COPY A:MegaBack.HLP
               MB

     This recovery diskette will boot your system and start MegaBack if the
     system already  has  a  formatted  drive  C:.   If  drive  C:  is  not





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 36


     formatted,  use DOS  hard disk  setup procedures  to prepare  the hard
     disk,  and then  boot your  system  again with  the MegaBack  recovery
     diskette.



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 37



     Utility Functions

          The utility  menu of  MegaBack's  main  menu  provides access  to
          functions  supporting  MegaBack  backup  and  restore  functions.
          Select Utilities from the main  menu to access the following menu
          of options.


-->                     __________Utilities_____________
                       | Synchronize hard disk          |
                       | Reset backup indexes           |
                       | recover backup Indexes         |
                       | Create reports                 |
                       | Verify backup data             |
                       | Quit to main                   |
                       |________________________________|


-->  Utilities - Synchronize indexes with hard disk

          Since you may  use Incremental backup for  a long period  of time
          before again needing  to perform a Full backup,  your backup sets
          will eventually  contain copies of  files that have  been deleted
          from  your hard disk.   If you  should ever need  to recover your
          hard disk and restore  all backup files,  it is not desirable  to
          recreate these deleted files.

          MegaBack's synchronization feature  compares the files stored  in
          the  backup indexes with  the actual files on  your hard disk and
          records files no longer on your hard disk as deleted.

          MegaBack's  restore processing  provides  options to  include, or
          bypass these "deleted" files during restore.  Your data is always
          available and you  make sure not  to accidently restore  unwanted
          files.

          You  should perform the  backup synchronization  feature whenever
          you have deleted files from your hard drive.

          Upon  selecting  synchronization  from the  menu,  MegaBack  will
          immediately begin comparing the indexes with the hard disk files.
          A  status display will be  presented to show  you the progress of
          the activity.  You may safely  terminate the process at any  time
          by pressing any key during the  comparison.  MegaBack will ask if
          processing is to terminate or continue.

          Upon completing  synchronization processing you will  be returned
          to MegaBack's menus.

          The following display will be presented if you have  selected the
          <Ask>  option for index synchronization.   This  display explains





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 38


          that MegaBack synchronization processing may be performed at this
          point in backup processing.  Press  Y  to perform synchronization
          or  N to bypass synchronization for this backup.  Synchronization
          is only needed when you  have deleted files  from your hard disk,
          so is not necessary to run for every backup.

             _________ Synchronize hard disk with backup index ________
            |                                                          |
            | The synchronize feature allows you to make sure that all |
            | files that exist in the backup index are present on the  |
            | physical hard disk. If you have records for non-existent |
            | files, MegaBack will then delete the records.  Then, at  |
            | restore time, MegaBack will not attempt to restore files |
            | that had been deleted from your hard disk.               |
            |                                                          |
            |            Do you want to synchronize the index?         |
            |                                                          |
            |                _____                   ____              |
            |               | Yes |                 | No |             |
            |               |_____|                 |____|             |
            |                                                          |
            |_______ -> <- changes, <Enter> accepts, Esc exits ________|


-->  Utilities - Reset the backup indexes

          This  function  of MegaBack  deletes  the current  set  of backup
          indexes and creates new empty ones.  Use it before starting a new
          full backup for your system.

          After selecting the index delete function you will be prompted to
          verify you really do want to complete this process:

           __________________________________________________________
          |                                                          |
          |         Resetting the indexes will erase all             |
          |           information about backed up files.             |
          |                                                          |
          |        Are you sure you want to reset the indexes?       |
          |                                                          |
          |              ___                        __               |
          |             |Yes|                      |No|              |
          |             |___|                      |__|              |
          |_____________ <Enter> accepts, Esc exits _________________|

               Respond <Yes> to continue the process and delete the current
               backup index set.

               Respond <No> to cancel the index deletion process and return
               to MegaBack main menus.








     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 39


-->  Utilities - Recover backup indexes from last backup volume

          Since the  hard disk backup  indexes are critical to  the system,
          they are backed up to the last backup volume at the end  of every
          backup.   This takes  a little  time and  disk space  but ensures
          indexes are always backed up and are kept with backup data.

          Since the  indexes are  kept on backup  volumes, each  volume set
          becomes a portable  set of files you may take to another computer
          for use.

          To use any  backup set, the indexes must exist on your hard disk.
          If they are  somehow lost or not available  on the computer where
          you want  to restore files, you must first restore the index from
          the last backup volume.   It is your responsibility to keep track
          of the last backup volume used  since MegaBack does not know disk
          numbers without its indexes.  During index recovery MegaBack will
          ask you to place the last used backup volume in the drive.

          If you have  lost track of  the last backup  volume, use the  DOS
          directory  command to  display the  files  on each  volume.   The
          volume with the most recent file dates is the last disk used.

          Place  the last  volume  in  the drive  and  press <Enter>  after
          MegaBack asks  for it.   In  some cases  MegaBack may  ask for  a
          second volume if it  determines part of the indexes backed up are
          stored on a previous volume.

           _______________ Restoring Backup Indexes _______________
          |                                                        |
          |  Attempting to restore indexes from backup diskettes.  |
          |                                                        |
          |      Place the last backup disk used in drive A:       |
          |                                                        |
          |  Press <Enter> when volume is ready, <Escape> to exit. |
          |                                                        |
          |_________________ <Enter> to continue __________________|

          MegaBack  will read the  indexes and put them  on the hard drive.
          You will be notified when the indexes are properly restored.

          If the build  of the index from  the backup volume  fails, Patri-
          Soft provides an emergency index rebuild utility.   MEGARGEN will
          read individual backup  volumes and recreate their  index entries
          in an existing MegaBack index.  You will find  copies of MEGARGEN
          on  the  MegaBack distribution  diskette.   You  may  also always
          download  it  from  the  Patri-Soft BBS,  or  other  popular  BBS
          systems.

          MEGARGEN is not always included in the BBS version of MegaBack to
          reduce the size of data to download.  Contact us at Patri-Soft if
          you have any problems locating this utility.  There is no fee for
          the MEGARGEN utility, it is free to anyone.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 40


     Utilities - Create reports

          MegaBack  Plus  has  the  special   ability  to  generate  useful
          information about your backups.  Upon selecting this option,  you
          will be presented with three different report options.

          Print/View backup file list:
               After  selecting  this  option,  MegaBack  will  prompt  for
               information  similar  to the  restore  input  screen.  After
               filling in appropriate information (simply press F10 without
               changing any  of the defaults  for ALL files),  press F10 to
               view the files.  To print the list, press  F8 and select the
               appropriate printer.

          Log Analysis:

               MegaBack  keeps a log which details the actions performed by
               MegaBack.  This log may be viewed using this facility.  When
               selecting  this action,  you may view a log  summary of past
               actions, view the log itself,  or delete the log to start it
               over.

          Backup summary:

               This option  provides information  about how many  backed up
               files exist, number of characters,  number of diskettes, and
               the last backup date.


-->  Utilities - Verify backup volume data

          Use  verify  to  confirm backup  has  correctly  backed  up data.
          Sometimes you may be  unsure of the validity of your backup data.
          This might happen if you suspect faulty backup volumes were used,
          or a drive might not  be functioning properly.  MegaBack provides
          this function to  read backup data and  verify it can be  used to
          restore the files.

          Volume verification is quick and easy as it only requires a quick
          read of each backup  volume.  No data is actually  written to the
          hard disk.

          Two verification processes  actually occur.  First,  DOS verifies
          all the data  can be read from the backup volumes.  Second, a CRC
          check verifies data  is accurate by arithmetically  verifying the
          data on the volumes is the same as the data was on  the hard disk
          before it was backed up.

          Backup  verification  may  verify selected  backup  files,  or an
          entire backup volume set.  Upon selecting the verify function you
          will be presented with a specification display similar to restore
          processing.    Indicate the  qualifications  of all  files  to be
          verified.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 41


           __________________________________________________________
          |                                                          |
          |  Drive to verify    : *                                  |
          |                                                          |
          |  Path to verify     : *                                  |
          |                                                          |
          |  Pattern to verify  : *.*                                |
          |                                                          |
          |  Select files backed up AFTER this date :                |
          |                                                          |
          |  Select files Backed up BEFORE this date:                |
          |                                                          |
          |                             Enter text                   |
          |_____________ Press F10 to begin or ESC to abort _________|

          You are asked to fill in the following fields:

          Drive to verify:    Enter the drive  letter where  the files were
                              originally backed up from. (I.E. C, D)

          Path to verify:     Optionally enter the pathname where the files
                              were backed up from. If no path is specified,
                              files from all paths  will be selected.  I.E.
                              \LETTERS  \PICTURES

          Pattern to verify:  Enter a  filename pattern to verify. When not
                              specified,   all   file  patterns   will   be
                              selected.

          Backed up before/after:
                              Select files by the date they were backed up.
                              You  may   use  one   or  both  of  the  date
                              specifications.

          Press  <F10> to  accept  specifications  and start  verification.
          <Esc> to quit.

          Like restore, you will be asked to place each volume in the input
          drive  until all  data is  verified.  You  will be  notified with
          error message displays if any errors are found in the data.



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 42


-->  Options

          The Options menu is comprised of functions that alter the
          operation and control of MegaBack.

                       Options
                          Exclude/select files from backup
                          Basic system options
                          Advanced system options
                          Define backup sets
                          Password Protection
                          Set alternate display type/color
                          Quit to main

     Options - Selection/Exclusion Processing

          MegaBack can backup selected files, or all files on a disk except
          files  excluded from the process.   You may specify either select
          processing, or exclusion processing in MegaBack options.

          The selection/exclusion  facility displays  lists of  directories
          and files on your hard disk.  While viewing these lists, you mark
          files  to be  selected or excluded  from  processing depending on
          your option selected.

          While you are scrolling  through the lists of files, you may view
          the contents  of text and WordPerfect files using MegaBack's file
          viewers.   You may sort file lists by  file name, age, size, name
          or extension.

          Following is an example of a the file selection display area.


                __________________C:\WP____________________________
               |   <PARENT>          26APR91   10:32p   <DIR>      |
               |   <ROOT>            26APR91   10:32p   <DIR>      |
               |   AGENDAS            5MAY91    4:10p   <DIR>      |
               |   ARNOLD.LTR        10MAY91    8:15a   20430      |
               |   BACKDAY.NOT       21JUN91   12:15p    3021      |
               |   MONEY.GOT         19JUL91    7:32a   50583      |
               |__________________F10 accepts, ESC exits___________|


          The display shows files for one directory at a time.  Entries for
          the current  and root directory  are always sorted to  the top of
          the list along  with other subdirectories  defined in the  listed
          directory.

          The top border of the display indicates the drive and name of the
          directory being  displayed.  The  bottom border gives  brief help
          about keys  used to  terminate the  selection process.  The right
          hand border of  the display holds a scroll  bar for mouse control
          of the list (not shown above).   Also not shown is a  highlighted



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 43


          selection bar  that covers one entry at a time  in the list.  The
          selection bar's location is modified by using the UP, DOWN, LEFT,
          and RIGHT cursor control keys.


          Backup File Selection Operation

          The  following  keys  are  active  during  backup  select/exclude
          processing:

          <Space Bar>
                    When  positioned on  a file name,  it either  marks the
                    file to be  selected or  excluded,  or if the  file has
                    already  been  marked,  unmarks it.   Filenames  become
                    highlighted in the list after they  are marked. A small
                    checkmark symbol is also displayed next to the filename
                    to indicate it is selected.

          <Right Arrow>
                    Marks the file highlighted by the selection bar. If the
                    file is already marked, it will remain marked. The file
                    selection bar is also moved to the next filename in the
                    list.

          <Left Arrow>
                    Unmarks the file highlighted  by the selection bar.  If
                    the file  is not  marked it will  remain unmarked.  The
                    file selection  bar is also moved to the  next filename
                    in the list.

          <Enter>   When the file selection bar  is placed over a directory
                    name, changes the list to show the  selected directory.
                    Place the highlight bar on any directory name and press
                    the <Enter> key to change to the directory.

                    Special filenames of <PARENT> and <ROOT> are  shown for
                    any subdirectory listed.  You may press <Enter>  on the
                    <PARENT> entry to list the files in the directory above
                    the current directory listed. Pressing  <Enter>  on the
                    <ROOT>  entry lists the root directory of the currently
                    selected drive.

          <F1>      At any time press  the <F1> key for help on the current
                    activity.

          <F3>      Press <F3>  to bring up  a temporary window to  enter a
                    DOS command or to exit to DOS.

          <F10>     The  <F10>  key signals  the  end of  the  file marking
                    process.   You will be  returned back to  the utilities
                    menu.

          <Escape>  Use    the    <Escape>    key   to    terminate    file




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 44


                    selection/exclusion  processing   and  return   to  the
                    MegaBack main menu.  The  names of marked files are not
                    saved.

          <A>       Press  <A> when positioned on a  directory name to mark
                    the directory and all its subordinate directories.

          <D>       Press <D> to unmark any directory or file.

          <S>       Press <S> to activate a  selection window to specify an
                    alternate sort sequence for the file list.

                               ______________________
                              |   Change List Order  |
                              | Sort Date Descending |
                              | Sort Name Ascending  |
                              | Sort Size Descending |
                              |______________________|


          <T>       Tag  all  files in  the currently  displayed directory.
                    After tagging all files you can untag selected files to
                    be omitted from processing.

          <U>       Untag  all  tagged  files in  the  currently  displayed
                    directory.

          <V>       Press the  <V> key to  View text or  WordPerfect files.
                    The file viewer can examine up to 500 lines of a file.

                    Use the cursor control keys to control the viewing of a
                    file and press  <Escape>  from the  viewer to return to
                    the file list.


          Marking a full directory

               You  may   position  the   file  selection   bar  over   any
               subdirectory name and press the <Right Arrow> or <Space Bar>
               to mark it.  MegaBack will immediately present the following
               question:

                     ___________________________________________________
                    |  C:\DIR is marked.  Mark all files within it?     |
                    |                                                   |
                    |           ___                        ___          |
                    |          |Yes|                      |No |         |
                    |          |___|                      |___|         |
                    |___________________________________________________|

               This is a  reminder that you will mark  the entire directory
               as well as all directories below  it.  Press <Y> if this  is
               correct.  Press <N> to cancel the mark directory request.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 45


          Completing file selection

          Once you have marked all files,  press the <F10> key to exit  the
          file selection display and return back to MegaBack's menus.


     Options - Set basic system options

          Basic system options are discussed earlier  in this manual.   See
          the section on "System Setup/Installation".


-->  Options - Advanced System Options

-->       MegaBack's  advanced  options  are  intended  to  provide a finer
          granularity of control  for special backup  implemenations.  Most
          users  will not have a  need to alter  these options.  If you are
          unsure of the correct value of any option, leave the value as  it
          was distributed with MegaBack.

-->       Following is the  advanced  options  display  and explanations of
          each option:

        _______________ Specify advanced system options_________________
       |                                                                |
       | Target media type...................................: Diskette |
       | Directory to backup to:.............................: \        |
       |                                                                |
       | Scan disk before backup (Y/N/Ask)...................: Y        |
       |                                                                |
       | Default restore sort sequence.......................: Filename |
       |                                                                |
       | Maintain activity log (Y/N).........................: Y        |
       | Is activity log to be verbose (Y/N).................: N        |
       |                                                                |
       | Backup zero byte files (Y/N)........................: N        |
       | Skip Stowaway auto-restore files (Y/N)..............: N        |
       | Include records marked "Deleted" in restore.........: N        |
       | Exclude the MegaBack directory?.....................: Y        |
       |                                                                |
       | Select ID at startup?...............................: N        |
       |                                                                |
       |                     Press -> <- to change                      |
       |____________ Press F10 when finished or ESC to abort ___________|


-->       Target Media Type:
               Use the  right and  left arrow  keys to  select  the type of
               media MegaBack will use to hold backup data.   At this time,
               the  only  difference in  processing  between the  different
               types is  diskette backup  will ask for  volumes to be place
               in the  drive before processing.  Other  devices assume non-
               removable media and  will not ask for individual  volumes to
               be placed in drives.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 46


-->       Directory to backup to:
               For  other than diskette  based  backup,  you may  specify a
               subdirectory  to hold backup data.  For example, if you want
               to backup  to another hard disk,  specify a  subdirectory of
               D:\MB\MBDATA.   All  backup  files  will be written  to this
               directory.

-->       Scan disk before backup (Y/N/Ask):
               When backup is started, MegaBack normally scans the drive to
               be backed up to gather statistics  about the backup process.
               These statistics are displayed on a backup selection display
               where you can  decide if you  want to do incremental or full
               backup (a value of Y for this parameter).

-->            If you want to  avoid this first  disk scan  and immediately
               start backup, specify  <N>.   MegaBack will then immediately
               ask  you  if  you  want  Full  or  Incremental  backup.   No
               statistics will be presented. Specify <A> for this parameter
               if you want MegaBack to ask you, before backup,  if the scan
               is to be done.

-->            For MegaBack to give you  statistics  of the number and size
               of files to be processed for full and incremental backup, it
               will first need to scan all directories of the drives  to be
               backed up.   It will then  show the  statistics  and let you
               choose between Full or Incremental backup.


                     ___________________________________________________
                    |           Do you want to scan the disk?           |
                    |                                                   |
                    |           ___                        ___          |
                    |          |Yes|                      |No |         |
                    |          |___|                      |___|         |
                    |                                                   |
                    |_____ -><- changes, <Enter> accepts, Esc exits ____|

-->            Press <Y> to start the scan to gather the statistics.  Press
               <N>  to skip the directory  scan and immediately  ask you if
               Full or Incremental backup is desired.  This message box may
               be permanently modified  through MegaBack's  advanced system
               options.

-->            If <N> is specified, the following box will be shown for you
               to select the type of backup desired.

                    ______________________________________________________
                   | By your request, MegaBack will not scan the disk.    |
                   | Do you want to perform a Full or Incremental backup? |
                   |                                                      |
                   |           ____                 ___________           |
                   |          |Full|               |Incremental|          |
                   |          |____|               |___________|          |
                   |                                                      |
                   |_____ -><- changes, <Enter> accepts, Esc exits _______|



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 47


-->       Default restore sort
               When a  large  number of  files  are  selected  for restore,
               MegaBack may take awhile to sort it all.  In the interest of
               ffciency, MegaBack will sort it in the way that YOU  want it
               sorted in, so that you will not have to resort it.

-->       Maintain Activity Log:
               MegaBack may  optionally  keep an  activity  log of  all its
               actions.  This is a sequential text file named  MEGABACK.LOG
               that is  kept in MegaBack's  hard disk  directory.  You  may
               browse  this file at any  time to review  the backup actions
               you have taken  in the past.  Specify  <Y>  to maintain this
               log, <N> to not create a log.

-->            The backup log  will requre a small amount of disk space but
               may be  deleted at any time.   MegaBack  will  automatically
               create the log file if one is not found.

-->       Is activity log to be verbose:
               If you want a record of every file backed up  or restored to
               be placed in the activity log, specify  <Y> for  the verbose
               option.  This  will  require  significant  hard  disk space.
               Normally  the  activity  log  only  indicates  a  backup  or
               restore was done and the number of files processed.

-->       Backup zero byte files (Y/N)
               If  you do not  want files of  zero  size to be  backed  up,
               specify  <N>  for this parameter.  This  should only be used
               in special situations.  We recommend <Y> for this parameter.

-->       Skip Stowaway auto-restore files (Y/N)
               Patri-Soft's  Stowaway archival system  can be configured to
               leave  zero character empty  files on hard  disks.  If these
               files are  accessed,  Stowaway's auto restore  function will
               try to restore them so they can be backed up.   Specify Y if
               you  use  Stowaway  to  archive  data  on your system.  This
               option is ignored if you do not use Stowaway.

          Include records marked "Deleted" in restore
               During synchronization,  MegaBack scans  the disk for  files
               that are  in the backup  index yet  have been  removed  from
               the hard disk.  It marks  the corresponding  records in  the
               file index as  "Deleted"  and  makes  them  unavailable  for
               restore.  This option  overrides  the delete  flag and makes
               them available for restore.

          Exclude the MegaBack directory?
               If  you do not want to  process the files  located  in  your
               MegaBack directory set this option to <Y>.

          Select ID at start-up?
               MegaBack  Plus  allows the user to select  an ID at start-up
               time by  setting  this  option to  Y.  If  Y,  MegaBack will




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 48


               allow the user  to scroll through available  IDs  and select
               the ID to use by pressing <ENTER>.


     Options - Define backup sets

          MegaBack has a  facility to  handle  your  multiple backup  index
          sets.  This option  may be configured  so that each time MegaBack
          starts, it will prompt  the user  to select  a backup set.   This
          screen presents the user with the available backup IDs along with
          the date and  time the indexes were  created,  last accessed, and
          the last  backup date/time.  A  description is also  available by
          pressing 'O' to rotate the view.  Available keys are:

               A    Add a new ID.  This will prompt the user to enter a new
                    ID name and description.

               D    Delete the ID which is located under the highlight bar.
                    If the  deletion  is  accidental,  press  'D'  again to
                    undelete BEFORE exiting this screen.

               E    Edit the  current ID.  The only  thing you will be able
                    to change is the description of the highlighted ID.


     Options - Password Protection

          You may optionally set a  password to protect  MegaBack's restore
          from unauthorized access.  To enter a password,  select this menu
          option.  If this is the  first time that  you select this option,
          MegaBack will prompt you to enter the  new password to be used to
          protect restore.  After entering the password, pres <ENTER>.  You
          will be returned to the main menu.

          After setting the password, you will not be allowed to change it.
          If you have  to change the password,  the only way to do so is to
          reset the backup index, select a new password,  and do a new full
          backup.


-->  Options - Set alternate display type/colors

-->       MegaBack  has  three  predefined available  color schemes.  After
          selecting  this option,  you will be prompted  with the following
          screen:

          ________________________________________________________________
         | Select color type                                              |
         |                                                                |
         |  __________   ___________   ______________   ________________  |
         | |LCD colors| |Mono colors| |Default colors| |Customize colors| |
         | |__________| |___________| |______________| |________________| |
         |_________ -> changes, <Enter> accepts, Esc exits _______________|




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 49


-->       Select  LCD colors,  Mono Colors,  or Default  colors  to  change
          MegaBack's colors to suit your monitor.  If you select Customized
          Colors, read the following:

          MegaBack lets you change the colors of all its display windows to
          any  colors of  your choice.   Setting  alternate display  colors
          involves setting  NORMAL, REVERSE,  HIGHLIGHT, and  BORDER colors
          for each different type of window.

          When  changing colors,  you are  presented  with a  menu of  each
          window type used  by MegaBack.  You  may change colors on  any or
          all window types.

          Window colors are stored permanently  on disk in the options file
          so they will  be used each time  you use MegaBack.  When  you are
          finished setting  colors, press  <Exit> to  return to  MegaBack's
          menus.


           _____________________ Select Colors_____________________
          |                                                        |
          |                    Menus                               |
          |                    Pop-Ups                             |
          |                    User input                          |
          |                    Backup/Restore/Main                 |
          |                    Copyright Message                   |
          |                    Registration Message                |
          |                    Disk statistics                     |
          |                    disK mounts                         |
          |                    Thermometers                        |
          |                    default colors                      |
          |                    Help Colors                         |
          |                    textured Background                 |
          |                    Exit to main                        |
          |                                                        |
          |  ____________________________________________________  |
          | |               Change all Menu colors               | |
          | |____________________________________________________| |
          |_______________ Press <Enter> to select ________________|


          You are presented with  a screen with  four major color types  to
          pick across  the top and with a screen full of color combinations
          below.

          Use  the <Space Bar>  to move between each  color type.  Pressing
          the  space  bar indicates  the  current color  selection  for the
          active type is to be accepted.



     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 50


          Use the <Arrow  Keys> to position the selection box  on the color
          combination to be  used for the current color type.  When you are
          positioned on the desired color, press the <Space Bar>.

          Press <Enter>  to accept all colors and return to the window type
          menu.  You can then change colors on another window type.

          Press <Escape> to  return to the window selection  menu and leave
          the colors as they were originally defined.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 51


     Command Line operation

          MegaBack is normally  operated through its menu structure.   This
          provides  a simple technique for  backing up files that reassures
          you at every  step with displays  and questions to  let you  make
          decisions.

          More experienced  users may want  to use MegaBack's  command line
          interface  to  backup  their  system.    When  the  command  line
          operation is used, MegaBack will take  all its basic instructions
          from the  command line  and start the  backup process.   It  will
          still require  the proper disks be  placed in the  drives and may
          ask  for  other decisions  to  be  made  based on  your  options.
          Although  not totally  automated, it  provides a  quick start  to
          backing up specific data.

          The MegaBack command line format

               MB        path  /C   /EV:vol  /F   /I  /ID:xxx  /S   /SV:vol
                         /R /AF /NL /NS /V

          Command parameter explanations

               path      Specify  pathname  to  be restored.  You must also
                         specify the /R parameter.

-->            /AF       Assume  Formatted.   MegaBack will assume that all
                         input backup disks are formatted and thus will not
                         take the time to check them.

               /C        Used by  MegaBack's installation program  to start
                         MegaBack and  proceed directly  to setting  system
                         options.

               /EV:vol   During restore, it is sometimes desirable  to only
                         restore files in certain volumes.  You may specify
                         a range of  disk volumes by using the  /EV and /SV
                         parameters.   For  example, to  restore the  files
                         after volume 6  and before  volume 9, the  command
                         line would be:

                              MB /SV:6 /EV:9

               /F        Start MegaBack  and immediately start  Full volume
                         backup.

               /I        Start MegaBack  and immediately  start Incremental
                         backup processing.

               /ID:xxx   Use  alternative backup index set id.  Specify any
                         three characters  to use  an alternate  index set.
                         For more information  about alternate index  sets,
                         see the  heading about  Backup Index  Sets in  the




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 52


                         manual.   When  not specified  it  is assumed  the
                         value will be "BAK".

                              /ID:TOM

-->            /NL       No Log.  MegaBack normally  creates  and maintains
                         MEGABACK.LOG.  To suppress this feature,  use  /NL
                         parameter.

-->            /NS       No Scan.  MegaBack  normally  scans  the  disk  to
                         determine  which files  need  backup  in order  to
                         supply  the user  with the  processing statistics.

                         To  skip  this   operation,  use  this  parameter.
                         MegaBack   will   not   provide   ongoing   backup
                         statistics,  but this  may save  time on  machines
                         with large hard disks.

               /R        You may  also accomplish restore from  the command
                         line.  Specify a path and append /R to the command
                         line.

               /S        If  you already  know the  backup volume  MegaBack
                         will use, you  may place it in the  drive prior to
                         starting MegaBack  and specify  this parameter  to
                         have  MegaBack  assume  the  volume  is   present.
                         MegaBack will not ask you to place it in the drive
                         during backup.

                         This parameter is designed for those users backing
                         up  to huge  capacity  disk devices  where  volume
                         mounting is not normally necessary.

               /SV:vol   To  start  the  restore  process  with  a  certain
                         diskette,  use  this  command.    For example,  to
                         restore only files  on disk 6  and above, use  the
                         command:

                                   MB /SV:6

               /V        Verbose log.  MegaBack's log  keeps track  of only
                         the major functions performed.  For a more verbose
                         log,  specify this  parameter.   MegaBack will log
                         files backed up, restored, and more.


     Specifying options through DOS environment variables

          Any  MegaBack  command  line  parameters may  be  placed  in  DOS
          environment  variables  to  be effective  each  time  MegaBack is
          started.   Use the DOS  SET command to  add the parameter  to the
          environment  string.   The  environment  variable  name  used  by
          MegaBack is  MegaBack.   The following  example demonstrates  the




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 53


          most common use of the environment variable for MegaBack. In this
          example, the  SET command  is used  to cause  MegaBack to  use an
          alternate index set identifier of TOM each time it is started.

               SET MegaBack=/ID:TOM

          See your DOS  manual for more information about  the SET command.
          The SET  command is often  placed in  the AUTOEXEC.BAT file  on a
          user's hard disk so it may automatically be issued each time your
          system is started.








     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 54


     Backup Maintenance

     Multiple Backup sets

          MegaBack  lets you keep and use  multiple backup sets on the same
          computer system.  Although  not often necessary, this  feature is
          useful in many situations.  Some examples are:

               --   To  create a special backup  set apart from your normal
                    set to move files from one system to another.

               --   To create separate backup sets for multiple users of  a
                    system.

               --   To  test your  current  backup  set  by  restoring  its
                    indexes to a different backup set identifier.

          A backup set consists of hard disk indexes and all backup volumes
          holding files referenced by those indexes.  Backup sets are given
          three character  set identifiers.   This  identifier is  normally
          "BAK"  but may  be altered  when starting  MegaBack by  using the
          /ID:xxx command  parameter.  An alternate set identifier may also
          be established by placing the /ID:xxx parameter in MegaBack's DOS
          environment variable.

          Backup  set indexes consist  of a set  of two index  files and an
          options  file.  These files exist  on the hard disk in MegaBack's
          directory.  The normal files are named as follows:

               BAKOPT.DAT
               BAKVOLIX.DAT
               BAKFILIX.DAT

          Alternate backup sets are identical  in function and usage to the
          normal  index  MegaBack   uses.    When  using   alternate  index
          identifiers,  be careful  to use  the correct  index set  for the
          files you are processing.


     Making copies of backup volumes

          Each backup volume is in a normal DOS format.  Backup volumes may
          be copied using DOS DISKCOPY, COPY, or XCOPY commands.

          For  safety  reasons you  may  want  to  take a  copy  of  backup
          information and store it at an offsite location.  To do this, use
          the DISKCOPY  command  to copy  the  original volume  to  another
          volume.  Store the original volume  back with the backup set, and
          take the copied volumes to your offsite location.

          When you only  have a single drive  to read and write  a specific
          disk format use the DOS DISKCOPY command as follows.  It will use
          memory to copy a volume to  a new volume.  The drive letters  for





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 55


          the source and new volumes are the same.  DOS will issue messages
          indicating what volumes to place in the drives and when.

               DISKCOPY A: A:

          If  you have  multiple drives  able to  read and  write the  same
          volume  format, use  the DISKCOPY  command  with different  drive
          letters.   The first drive  identifier is for the  source volume,
          the second letter is for the drive to hold the new volume.

               DISKCOPY A: B:

          Backup  disks may be copied to  different disk formats as long as
          the new disk  has enough capacity to hold  all information on the
          source volume.  Once backed up, backup data cannot again be split
          across multiple volumes.


     The Context Sensitive Help System

          MegaBack provides  immediate help  about its  operation at  every
          point  of its  processing.   A comprehensive  help system  may be
          interrogated at any  time by pressing the <F1> key.  When <F1> is
          pressed,  MegaBack  automatically  determines  what  function  is
          active and  action is  being requested.   It will  search a  help
          index and retrieve information about your current activity.  Help
          systems  that  bring up  help  about  your current  activity  are
          referred to as "context sensitive"  meaning they are aware of the
          context in which they are requested.

          In  addition to being context  sensitive, MegaBack help system is
          layered  to let  you not  only  examine help  about your  current
          activity, but also  lets you browse through the  help displays to
          learn about related  topics or other aspects of  MegaBack.  Press
          the <Home> key any time you are in the help system to display the
          help menu.

          The  intelligent  help  system  may  be  examined  by  using  the
          following navigation keys...

          <Enter>   Takes you to the next related screen
          <Esc>     Takes you back to the processing screen
          <Alt>     Allows you to  peek back  at the  processing  screen to
                    review what you are reading help about.
          <PgUp>    Will  take you up to  a more general  topic in the help
                    system
          <Home>    Displays the main help menu

          The LEFT,  RIGHT, UP,  and DOWN keys  are available  when viewing
          screens smaller than  the full page.   Use them to move  the help
          window around on  the display  to view areas  hidden by the  help
          window.






     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 56


-->  Alarm/Reminder Utility

-->       Included   with  MegaBack   is  its   MBALARM  utility  that  may
          optionally be  implemented to remind  you when  backup is needed.
          MBALARM has many options to let you specify how often,  and when,
          you are to be reminded backup is needed.

-->       MBALARM  is a stand alone  utility that may be  run at any  time,
          but it is usually implemented in your system's AUTOEXEC.BAT  file
          so it  is automatically  run every time  your system  is started.
          Its normal mode is to  check for backup once each  day, and  scan
          your system to determine if backup is needed.  When it determines
          backup is needed,  you will be prompted to  indicate if backup is
          to be started,  or skipped.   Placing the following  two lines in
          you  AUTOEXEC.BAT  file will implement  MBALARM with its standard
          options.

               \MEGABACK\MBALARM
               IF ERRORLEVEL 1 \MEGABACK\MB

-->       The first  line runs the alarm utility.   The second line  starts
          MegaBack if MBALARM has set  ERRORLEVEL to 1 indicating backup is
          to be started.

-->       The following  command  line  parameters  may  be  placed on  the
          MBALARM  statement.   They modify its operation to best suit your
          needs.

-->            /A   Include All files,  updated or not in backup scan.  Use
                    to dtermine the amount of data to be backed up for full
                    volume backup.

-->            /CD:nn
                    Check for backup  nn days since last backup.  Normally,
                    MBALARM  checks once  a day to  determine if  backup is
                    needed.  Use to delay  checking for backup  to every nn
                    days.  /CD:4  causes  MBALARM  to remain inactive until
                    4 days since the last backup.

-->            /D:xx
                    Disk  volumes  to  be  checked.   You  may  provide  an
                    optional  list of volumes  to be  scanned to  determine
                    when backup  is needed.  If this list  is not provided,
                    the  list  provided in  MegaBack  options is  used.  If
                    both are absent, the current drive is scanned.

-->            /F   Force backup when it is needed.  Do not let user select
                    if backup is to be started.

-->            /FD:nn
                    Force backup after nn days since last backup.  Like the
                    force  (/F),  except force is not  implemented until nn
                    days after  the last backup.  Use  to give the user the
                    option to backup for a few days, then force a backup.




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 57


-->            /M   Cause MBALARM to check backup every time it is started,
                    instead of only one time each day.

-->            /NC  Prevent   clearing  of  the   display  during   MBALARM
                    processing.

-->            /ND  Don't  display  statistics  of  backup  status  on  the
                    display  MBALARM  processing.  Take appropriate  backup
                    action based  on parameters supplied.  Do not  let user
                    decide if backup is to be started.  This parameter also
                    sets the /F (force) option.

-->            /NL  Do not let the user select the option to display a list
                    of directories  to be backed  up when  asked if  backup
                    should be done.

-->            /NS  Don't scan directories to determine if backup is needed
                    and  display  totals   of  files  needing  backup.  The
                    decision to backup will be made solely on the number of
                    days since the last backup, or on the users decision.

-->            /NX  Ignore  eXclusion criteria and count  all updated files
                    found on  the scanned drives.   Normally  MBALARM  uses
                    MegaBack  exclusion criteria to  ignore files regularly
                    excluded from the backup process.

-->            /XM  Print exit  messages on the  display showing the  value
                    MBALARM set ERRORLEVEL to before it ended.


-->       MBALARM Examples:

-->       Following are examples of different MBALARM implementations:

-->            To check for  backup once a day,  and ask user  if backup is
               to be started:

                    \MEGABACK\MBALARM

-->            To  check for  backup  once a day,  and  force  backup  when
               needed:

                    \MEGABACK\MBALARM /F

-->            To check backup every time your computer is started, and ask
               user to incicate if backup is to be started:

                    \MEGABACK\MBALARM /M

-->            To check  for buackup once  a day,  and force  backup once a
               week:

                    \MEGABACK\MBALARM /FD:7





     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 58


-->            To check for  backup every other day,  and force backup once
               a week:

                    \MEGABACK\MBALARM /CD:2/FD:7

-->            Don't scan to find any  updated files.  Ask user each day if
               backup is to be started:

                    \MEGABACK\MBALARM /NS


-->       Adding MBALARM to AUTOEXEC.BAT file

-->            Use  the DOS, EDIT command, EDLIN command,  or your favorite
               text  editor, to  modify your  AUTOEXEC.BAT  file to include
               MBALARM  statements.   If   you  are  unfamiliar   with  the
               AUTOEXEC.BAT  file,  or  its  function,  consult  your   DOS
               reference manual.

-->            The  MBALARM  statements may be added at any location in the
               file,  but are usually added at the end,  before  control is
               given to DOS or another application.

-->            Following  is  a  sample  AUTOEXEC.BAT  file before  MBALARM
               statements are added.

                    SET COMSPEC=COMMAND.COM
                    PATH C:\DOS50;C:\BAT
                    PROMPT $P$G
                    DOSKEY
                    SHARE
                    MODE CON: RATE=25 DELAY=2
                    DOSSHELL

-->            Following  is the same example with the  MBALARM  statements
               added:

                    SET COMSPEC=COMMAND.COM
                    PATH C:\DOS50;C:\BAT
                    PROMPT $P$G
                    DOSKEY
                    SHARE
                    MODE CON: RATE=25 DELAY=2
                    REM ************************
                    \MEGABACK\MBALARM /CD:2/FD:7
                    IF ERRORLEVEL 1 \MEGABACK\MB
                    REM ************************
                    DOSSHELL




     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 59


     System Requirements


          Operating system compatibilities

               MegaBack must run on a 100% compatible PC, XT,  or AT system
               and requires DOS  3.2 or above for its  operation.  MegaBack
               may operate on some other nonstandard systems but  we cannot
               guarantee its  correct operation  nor make  any promises  to
               make it compatible with those systems.


          Backup device compatibilities

               MegaBack uses  only standard  DOS disk  devices for  holding
               backup data.  The obvious devices are various forms of 3 1/2
               and 5 1/4 diskette systems.

               MegaBack is also designed to use large format removable disk
               devices as backup media.  These devices must have a standard
               DOS format and must appear to DOS as a normal disk device.


     Troubleshooting


          I/O errors on disks

               If you should  have a problem restoring data  from a damaged
               or faulty  volume  take the  following steps  to attempt  to
               circumvent the problem.

                    --   Try  turning  the  disk in  the  sleeve  with your
                         fingers to make  sure it is  loose and will  spin.
                         If  5  1/4  diskettes appear  too  tight,  you can
                         relieve some pressure placed on the magnetic media
                         by  drawing each edge  of the diskette  across the
                         edge  of a table  applying a reasonable  amount of
                         pressure.   This will  expand the area  inside the
                         jacket for the media to move.

                    --   Attempt to copy the diskette to another  diskette.
                         If the copy is successful, attempt  to use the new
                         disk to restore the data.

                    --   Take  the  volume  in error  to  another  drive on
                         another machine to attempt to restore the data.

                    --   When  all else fails, use the "FAIL" option during
                         backup  volume read  error  detection to  indicate
                         backup  is  to attempt  to  read as  much  data as
                         possible.






     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 60


          Error Messages

               MegaBack  has  comprehensive  error  and exception  checking
               designed into  every component  of the  system.   MegaBack's
               help  systems  contains   help  about  messages   issued  by
               MegaBack.  Whenever an error message is displayed, press the
               <F1>  key  for  a  complete explanation  of  the  error  and
               suggested actions to take as a result of the error.


     Technical Support

          Patri-Soft may be reached for technical support through a variety
          of  sources.  Normal  technical support hours  are 8:30AM through
          5:00 PM Monday through Friday (PST).

          You may contact us through the following methods...

                 CompuServe     76347,2477
                 Phone          909-352-2820
                 BBS            909-352-2825
                 FAX            909-352-1527
                 Mail:
                    Patri-Soft
                    5225 Canyon Crest Drive  Suite 71-358
                    Riverside, CA  92507

          A special order  line is available if you would  like to purchase
          using VISA or MasterCard or discuss other purchase options.

          When  calling for  technical support  please  have the  following
          information ready so we may serve you efficiently:

               a.   The exact version of MegaBack  you are using.  MegaBack
                    main menu contains this data.

               b.   An exact problem description

               c.   Screen print of the MegaBack directory and all files it
                    contains.

               d.   The software configuration of your system including DOS
                    version, AUTOEXEC.BAT  contents as  well as  CONFIG.SYS
                    contents.

               e.   The hardware configuration of your system.

          A good problem description indicates  exactly what you were doing
          when  you  encountered  the  error,  and  exactly  what  symptoms
          occurred as  a result of the  error.  Please avoid  the following
          problem  descriptions. They  are  much  too  brief  to  begin  to
          analyze. 






     MegaBack Plus           Copyright 1993 by Patri-Soft           Page 61


          Poor problem descriptions:
               a.   Backup is not working.
               b.   The machine will not read my disk.
               c.   I can't restore my indexes
               d.   The system fails during backup or restore.

          Following are examples of better problem descriptions:
               a.   Backup is  failing.  MegaBack  asks for a backup volume
                    and  after I  place it  in the  drive, the  drive light
                    comes  on, goes off, and MegaBack  indicates no disk is
                    in the drive.

               b.   I am attempting to restore indexes from a backup volume
                    and MegaBack indicates the indexes are not  present.  I
                    have displayed the  contents of the last  used diskette
                    and it appears to be ok. Its contents are...



     MegaBack Plus                    Index                         Page 62


                                      Index

     Advanced options
          MegaBack's . . . . . . . . . . . . . . . . . . . . . . . . . . 45
     Alarm Utility . . . . . . . . . . . . . . . . . . . . . . . . . . . 56
     Archive Attribute
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  3
          setting option . . . . . . . . . . . . . . . . . . . . . . . . 10
     Backup
          Drive  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  8
          Processing . . . . . . . . . . . . . . . . . . . . . . . . . . 18
          Selecting Backup Type  . . . . . . . . . . . . . . . . . . . . 20
     Backup data
          Verify . . . . . . . . . . . . . . . . . . . . . . . . . . . .  9
     Backup Maintenance. . . . . . . . . . . . . . . . . . . . . . . . . 54
     Backup Sets
          Multiple . . . . . . . . . . . . . . . . . . . . . . . . . . . 54
     Backup type
          Full Backup  . . . . . . . . . . . . . . . . . . . . . . . . .  3
          Incremental Backup . . . . . . . . . . . . . . . . . . . . . .  3
     Build Index from backup
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 39
     Colors
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 48
     Command line format . . . . . . . . . . . . . . . . . . . . . . . . 51
     Command Line operation
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 51
     Compacted . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  2
     Compressed  . . . . . . . . . . . . . . . . . . . . . . . . . . . .  2
     Compression Option
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  8
     CompuServe
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 60
     CRC Check Value
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  5
     Date
          Restore Selection  . . . . . . . . . . . . . . . . . . . . . . 28
     Disk
          Backup Disk Size . . . . . . . . . . . . . . . . . . . . . . .  8
     Diskette
          Recovering from write errors . . . . . . . . . . . . . . . . . 23
     Diskettes
          Backup Volumes . . . . . . . . . . . . . . . . . . . . . . . . 16
     Display Colors
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 48
     End volume for backup
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 51
     Environment Variables
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 52
     Error Messages
             . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 60
     Exclude
          Select/Exclude options . . . . . . . . . . . . . . . . . . . . 10





     MegaBack Plus                       Index                      Page 63


     FAX . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 60
     Features  . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  1
     Full backup . . . . . . . . . . . . . . . . . . . . . . . . . .  3, 13
     Help. . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 55
     I/O Errors. . . . . . . . . . . . . . . . . . . . . . . . . . . . . 59
     Incremental Backup. . . . . . . . . . . . . . . . . . . . . . .  3, 13
     Indexes
          Backup File Index  . . . . . . . . . . . . . . . . . . . . . . 17
          Backup Volume Index  . . . . . . . . . . . . . . . . . . . . . 17
          Emergency Recovery . . . . . . . . . . . . . . . . . . . . . . 39
          MEGARGEN Index recovery. . . . . . . . . . . . . . . . . . . . 39
          Recovering Indexes . . . . . . . . . . . . . . . . . . . . . . 39
          Saving Backup Indexes  . . . . . . . . . . . . . . . . . . . . 24
     Initialize Indexes. . . . . . . . . . . . . . . . . . . . . . . . . 38
     Listing Files . . . . . . . . . . . . . . . . . . . . . . . . . . . 28
          Restore  . . . . . . . . . . . . . . . . . . . . . . . . . . . 28
     Main Menus. . . . . . . . . . . . . . . . . . . . . . . . . . . . . 18
     MBALARM . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 56
     Options
          Advanced system options. . . . . . . . . . . . . . . . . . . . 45
          Basic system options . . . . . . . . . . . . . . . . . . . . . 45
          Exclude/Select files from backup . . . . . . . . . . . . . . . 42
          Set display type/colors. . . . . . . . . . . . . . . . . . . . 48
          Setting Options  . . . . . . . . . . . . . . . . . . . . . . .  7
     Ordering MegaBack . . . . . . . . . . . . . . . . . . . . . . . . . 60
     Overlay
          Files with duplicate name  . . . . . . . . . . . . . . . . . . 33
     Overlay Files . . . . . . . . . . . . . . . . . . . . . . . . . . . 33
     Patri-Soft. . . . . . . . . . . . . . . . . . . . . . . . . . . . . 60
     Phone   . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 60
     Quick Start . . . . . . . . . . . . . . . . . . . . . . . . . . . . 12
     Recover Index . . . . . . . . . . . . . . . . . . . . . . . . . . . 39
     Reinitialize Indexes. . . . . . . . . . . . . . . . . . . . . . . . 38
     Reliability . . . . . . . . . . . . . . . . . . . . . . . . . . . .  5
     Restore . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 32
          Boot Diskette  . . . . . . . . . . . . . . . . . . . . . . . . 35
          Combined Tape/MegaBack . . . . . . . . . . . . . . . . . . . .  4
          Processing . . . . . . . . . . . . . . . . . . . . . . . . . . 32
          system recovery diskette . . . . . . . . . . . . . . . . . . . 35
          to empty system  . . . . . . . . . . . . . . . . . . . . . . . 35
     Restore Index . . . . . . . . . . . . . . . . . . . . . . . . . . . 39
     RETRY
          disk I/O error . . . . . . . . . . . . . . . . . . . . . . . . 23
     Select/Exclude  . . . . . . . . . . . . . . . . . . . . . . . . . .  5
          Select/Exclude options . . . . . . . . . . . . . . . . . . . . 10
     Select/Exclude Processing . . . . . . . . . . . . . . . . . . . . . 42
     SET MEGABACK= . . . . . . . . . . . . . . . . . . . . . . . . . . . 53
     Set system options. . . . . . . . . . . . . . . . . . . . . . . . .  7
     Setup/Installation  . . . . . . . . . . . . . . . . . . . . . . . .  6
     Speaker
          Setting sounds options . . . . . . . . . . . . . . . . . . . .  9
     Start volume for backup . . . . . . . . . . . . . . . . . . . . . . 52






     MegaBack Plus                       Index                      Page 64


     Starting
          Restore  . . . . . . . . . . . . . . . . . . . . . . . . . . . 32
     Starting MegaBack . . . . . . . . . . . . . . . . . . . . . . . . . 12
     status bar. . . . . . . . . . . . . . . . . . . . . . . . . . . . . 21
     Synchronize hard disk with indexes. . . . . . . . . . . . . . . . . 37
     System
          Requirements . . . . . . . . . . . . . . . . . . . . . . . . . 59
     Tape
          Complementing Tape Backup  . . . . . . . . . . . . . . . . . .  4
     Technical Support . . . . . . . . . . . . . . . . . . . . . . . . . 60
     Troubleshooting . . . . . . . . . . . . . . . . . . . . . . . . . . 59
     Utilities . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 37
          Synchronize hard disk. . . . . . . . . . . . . . . . . . . . . 37
          Recover backup indexes . . . . . . . . . . . . . . . . . . . . 39
          Reset backup indexes . . . . . . . . . . . . . . . . . . . . . 38
          Verify backup data . . . . . . . . . . . . . . . . . . . . . . 40
     Verify
          DOS VERIFY option  . . . . . . . . . . . . . . . . . . . . . .  9
          Verify data after writing  . . . . . . . . . . . . . . . . . .  9
     Verify backup data. . . . . . . . . . . . . . . . . . . . . . . . . 40
     Volumes
          Backup Volume Sets . . . . . . . . . . . . . . . . . . . . . . 16
          Backup Volumes . . . . . . . . . . . . . . . . . . . . . . . . 16
          copying  . . . . . . . . . . . . . . . . . . . . . . . . . . . 54
          Preparing backup volumes . . . . . . . . . . . . . . . . . . . 17
          specification of start volume  . . . . . . . . . . . . . . . . 52