Introducing I-Queue! Server


   (c) Copyright 1992 by


                      ÜÜÛÛÛÛÜÜ
            ÜÛßÛÜ   ÜÛßß  ßßÛÛÛÜ
           Ûß   ßÛÜÛß        ÛÛÛ
           ßÛÜ ÜÛß ßÛÜÜ    ÜÛÛß
             ßßß      ßßßßßß
           ÛÛÛ           ÜÛÛÛ ÛÛÛ          ÛÛÛ  ÜÛÛ
           ÛÛÛ ÜÜÜ ÜÜÜ  ÜÛÛÛÜ ÜÜÜ ÜÜÜ ÜÜÜ  ÜÜÜ ÜÛÛÛÜ  ÜÜÜÜ
           ÛÛÛ ÛÛÛß ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛß ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛÜÛÛ
           ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛÜ ßÛÛÜÜÜ

            T   E   C   H   N   O   L   O   G   I   E   S

                   11433 Cronridge Drive, Suite H
                       Owings Mills, MD 21117
                          +1-410-363-1097
                       FAX: +1-410-363-3779

                      MHS: Support @ Infinite
          CompuServe: >MHS:Support @ Infinite (or 73270,405)
            Internet: Support@Infinite.MHS.CompuServe.com


  Technical Support provided on the CompuServe Information Service in
                          NOVVEN Section 4



OVERVIEW

   I-Queue! Server is a software utility that allows you to turn a
   printer connected to any workstation on your network into a
   shared printer.  I-Queue! Server runs as a small TSR on the
   workstation providing shared access to the printer (or multiple
   printers) via the standard NetWare print queue mechanism.

   Since NetWare already includes RPRINTER to provide a similar
   service, you may be wondering why you need I-Queue! Server.
   We shared that opinion until we actually tried to run RPRINTER
   in our offices, and judging from the volume of problems reported
   in the printing sections of the NOVB, NETW2X and NETW3X forums on
   CompuServe, we are not alone.

   I-Queue! Server was designed primarily to address the following
   requirements:

     1.) Compatibility with workstations running Microsoft Windows.

     2.) Compatibility with more printer ports without the requirement
         for "hardware interrupt support".

     3.) Faster printing speed.  (I-Queue! Server is 2 to 4 times
         faster than RPRINTER depending on the speed of the PC it
         is running on.)

     4.) The availability of an RPRINTER replacement in a 30-day
         trial version format so that users can "try before they buy".

   While you are testing I-Queue! Server, you may wish to try it in
   conjunction with the companion I-Queue! product.  A brief overview
   of the I-Queue! product follows below.


I-QUEUE!:  THE NETWARE PRINTING TOOLBOX  (available in the IQUEUE.ZIP file)

   I-Queue! simplifies printing in the Novell NetWare environment.

   From a small memory-resident pop-up (0 to 2-1/2KB), I-Queue! allows
   users to easily change NetWare print queues and modify "capture"
   parameters.

   I-Queue! for Windows is a convenient Windows application that
   adds similar conveniences for Windows users, combining NetWare
   print queue selection and Windows print driver selection into
   a single menu.

   Key features include:

     * Select a file server/print queue for caputuring
     * Capture your output to a file
     * Select the number of copies
     * Enter or choose printer setup strings from existing PRINTDEF
       information
     * Select forms
     * Ability to select from pre-defined PRINTCON job configurations
     * Select timeout interval
     * Enable or disable form feed
     * Expand or disable tabs (text or binary mode)
     * Enable or disable banner
     * Notify when job is printed (available with Novell's PSERVER,
       I-Queue! Server and several other third-party print servers)

   Users can also easily display a list of jobs in any queue to
   determine the status of a job, as well as deleting or changing
   the parameters of any job that they submit before it prints.

   Queue operators have the added capability of deleting print jobs,
   moving and copying jobs between print queues, and re-ordering the
   position of jobs in the queue.

   I-Queue! also includes the following additional utilities:

   OnHold is a TSR which allows users to submit print jobs that can
   automatically be placed "on hold", or delayed for printing at a
   later time.

   DefCap allows you to modify CAPTURE parameters from the
   command-line, but only modifies the specified parameters, leaving
   all others intact.

   Com2Lpt allows you to redirect serial (COM) port output to a
   parallel (LPT) port, provided that your application prints
   through the BIOS or DOS, and not directly to the serial port
   hardware.

   CreateQ allows you to create NetWare print queues where the
   temporary files are stored on a volume other than SYS:.



INSTALLING I-QUEUE! SERVER


   1.) LOGIN TO YOUR FILE SERVER AS SUPERVISOR OR A SUPERVISOR-EQUIVALENT.


   2.) COPY I-QUEUE! SERVER TO YOUR SERVER

       Copy I-Queue! Server's program files into the SYS:LOGIN
       directory on your file server.  This will allow workstations
       to load I-Queue! Server before they are logged into the
       network.

         IQS.EXE
         IQSE.EXE
         IQSN.COM      (optional)
         LOADIQS.BAT   (optional)
         GETNODE.EXE   (optional)
         QSETUP.EXE    (setup utility...requires SUPERVISOR rights)
         SHOWPS.EXE    (optional...administrative utility)
         DEDICATE.COM  (optional)

   3.) RUN IQS30DAY OR IQSINST TO INITIALIZE I-QUEUE!

       Run IQS30DAY.EXE to initialize the I-Queue! Server 30 day trial period.

       If this is a purchased copy, run IQSINST to initialize I-Queue!
       Server for your network.

   4.) RUN QSETUP

       The QSETUP utility is used to define the I-Queue! Print Server
       ID (QSERVER).

       Additionally, for each queue that will be serviced by I-Queue!
       Server, it must be defined with this simple utility.

       After you type QSETUP, if multiple file servers exist in your
       network, you will be presented with a list of file servers
       from which to choose, with the current server highlighted.
       Press Enter to select a file server.

       The next menu (or the first menu if you only have one file
       server) displays the print queues on your network that are
       being serviced by I-Queue! Server.  Press Insert to select
       from a list of other print queues on your file server that
       can be setup for I-Queue! Server, then highlight an additional
       print queue and press Enter.

   5.) CONFIGURE WORKSTATIONS TO RUN I-QUEUE! SERVER

       I-Queue! Server must be loaded as a TSR on any workstations
       which will operate as "print servers".

       For best results, it is recommended that you load I-Queue!
       Server into memory on the workstations acting as print servers
       before they log into the network.

   *** The easiest way to accomplish this is to load I-Queue! Server
       in the AUTOEXEC.BAT file of any workstations that will be
       operating as print servers. ***

       Alternatively, you may wish to create a common batch file on the
       network which loads I-Queue! Server for print server
       workstations.  LOADIQS.BAT is a sample batch file included with
       I-Queue!  Server, which illustrates a simple technique.

       There are two separate versions of the I-Queue! Server program.
       IQS.EXE uses unencrypted passwords, and can be used under NetWare
       2.x or NetWare 3.x when you have issued the statement SET ALLOW
       UNENCRYPTED PASSWORDS = ON at the file server console.  IQSE.EXE
       uses encrypted passwords, and can be used in either the NetWare
       2.x or 3.x environment without restriction.  However, IQSE.EXE
       requires approximately 3-1/2KB of additional memory to provide
       the encrypted password support, so NetWare 3.x users may wish to
       enable unencrypted passwords and use IQS.EXE instead.

       Command line options for IQS.EXE and IQSE.EXE.

         /U              to un-install.

         /Q<queuename>   primary queue to service.
         /Q2<queuename>  2nd queue name.
                         (NOTE:  To specify a queue on another file server
                         use the syntax /Qserver\queue)

         /x              x is Printer (1-3 for LPT1-LPT3 / 1-4 for COM1-COM4).
                           LPT1 is DEFAULT

         /S              Serial version (use COMx instead of LPTx)
                         (NOTE:  When using the serial option, you must
                         initialize the port's baud rate and parameters
                         using the DOS MODE command before loading IQS.)

         /Cx             x is 1-9 for copy to load.
                         (NOTE:  You can load up to 9 copies of IQS per
                         workstation, simply specify a different copy #
                         each time.)

         /P              Use Direct Port I/O to print. (DEFAULT)
         /B              Use BIOS to print.
                         (NOTE:  The BIOS option is slower, but will be
                         compatible with more "unusual" devices.)

         /Dxxx           Delay between jobs for xxx seconds.
                         (NOTE:  This option is useful for printers that
                         auto-switch between PCL and PostScript.)

         /Rxxxx          Printer Reset String...
                         (NOTE:  This is an ASCII string that will be
                         sent to the printer after each print job.
                         Use {xx} to include non-printable ASCII characters.
                         For example, <Escape>-E, which is the reset code
                         on HP LaserJets would be denoted /R{27}E)

         /Oxxx           Optimization. X is 16-1024 (128 Default).
                         (NOTE:  Higher values give higher priority to
                         printing activity and will slow down other
                         applications running on the same PC.  Lower
                         values will increase the response time for
                         other applications.)

         /Fx             Form Servicing Mode, where:
                           0 - Ignore forms changes. (DEFAULT)
                           1 - Minimize form changes.
                           2 - Change forms as needed.
                           3 - Plotter mode (pause for form to be
                               mounted before each print job)
                         (NOTE:  The default mode 0 means that I-Queue!
                         Server will ignore form specifications in print jobs.
                         Modes 1 & 2 will cause IQS to request form
                         changes.)

         /L              Local notification of printer errors/form changes
                         (DEFAULT)
         /N              No local notification of printer errors/form changes
                         (NOTE:  By default or with the /L parameter, IQS will
                         send NetWare broadcast messages to the workstation
                         it is running on with printer error or form change
                         notifications.

         /Ex             User who submitted a print job will be notified of
                         any printer status errors while their job is printing.
                           0 - User notification DISABLED.
                           1 - User notification ENABLED.  (DEFAULT)

         /I              Show status Information.

         /Wx             Specifies a "polling delay" of how many seconds
                         IQS will wait between checking for new print
                         jobs when it is idle.  The default is 3 seconds.

         /Kxxxx          This parameter allows you to change the number
                         of bytes that IQS reads at a time from the
                         print queue.  The default (and minimum) buffer
                         size is 512 bytes.  To increase the buffer size
                         to 1KB, use IQS /K1024.



LOADIQS.BAT

       LOADIQS.BAT is a sample batch file included with I-Queue!
       Server, which illustrates a simple technique for maintaining
       centralized management of IQS configuations.  It is NOT
       necessary to use this approach, this is merely one alternative.

       This batch file executes the GETNODE.EXE program (included with
       I-Queue!  Server) to set two environmental variables with the
       network address of the current workstation.  Conditional
       statements are then issued to load I-Queue! Server on selected
       workstations with the appropriate parameters.

       An easy way to accomplish this is to place this batch file and
       the GETNODE.EXE program in your SYS:LOGIN directory.  Rename
       LOGIN.EXE to LOGON.EXE, and rename this batch file to LOGIN.BAT,
       so that workstations will execute it first instead of LOGIN.EXE.
       Include LOGON as the last statement of this batch file to execute
       the standard Novell LOGIN procedure.

       The GETNODE program sets two environmental variables.  NET will
       be set to the current workstation's network address.  NODE will
       be set to the curren workstation's node address.  Combined, these
       will uniquely identify each of your workstations.

       Here are some sample commands from LOADIQS.BAT showing how IQS
       can be loaded in different configurations:

REM Bill's PC...Print Queue LASER1 to LPT2 with no local notification of errors.
IF %NET%$==00000001$ IF %NODE%$==000000000046$ IQS /QLASER1 /2 /N

REM Joe's PC...Print Queue LASER7 to COM1 with a reset code of <Escape>E
IF %NET%$==D0DAD0DA$ IF %NODE%$==02608CBADBAD$ MODE COM1:9600,n,8,1
IF %NET%$==D0DAD0DA$ IF %NODE%$==02608CBADBAD$ IQS /QLASER7 /S /1 /R{27}E

REM Print Server Workstation with multiple printers
REM First example is servicing 2 print queues.
REM Second example shows 1 print queue being serviced by 2 printers.
IF %NET%$==00000001$ IF %NODE%$==00000000006F$ IQS /C1 /QEPSON /Q2FS2\EPSON /1
IF %NET%$==00000001$ IF %NODE%$==00000000006F$ IQS /C2 /QLASER2 /2
IF %NET%$==00000001$ IF %NODE%$==00000000006F$ MODE COM1:9600,n,8,1
IF %NET%$==00000001$ IF %NODE%$==00000000006F$ IQS /C3 /QLASER2 /1 /S



FORMS MANAGEMENT

   I-Queue! Server supports form changes if loaded with the /F1 or /F2
   command line parameter.

   When form changes are requested, a broadcast message will be sent to
   the workstation operating as a print server.

   Execute IQS /M to notify I-Queue! Server that the requested form
   has been mounted.


USING I-QUEUE! SERVER AS A DEDICATED PRINT SERVER

   In many instances, it may be desirable to dedicate a workstation
   with multiple printers attached for print services.

   Using the /C parameter, I-Queue! Server allows you to load multiple
   copies of IQS or IQSE to service up to 7 printers (LPT1, LPT2, LPT3,
   COM1, COM2, COM3 and COM4) from a single PC.

   To gain additional printing speed from a non-dedicated workstation,
   run the DEDICATE.COM program on this workstation, which will cause
   I-Queue! Server to allocate additional time slices for printing
   activities.  Alternatively, you may wish to run I-Queue!'s print
   queue management display on the print server workstation.  I-Queue!
   will also signal I-Queue! Server to allocate additional time slices
   for printing activities.


ADMINISTRATIVE UTILITIES

   QSETUP.EXE is used to define which print queues are serviced by IQS.

   IQSN.COM is an optional TSR module that can be loaded after IQS/IQSE
   to notify system operators that a printer requires servicing
   because of a general error or out of paper condition.

   IQSN supports the following command-line parameters:

      /Nname     - "name" specifies a brief descriptive name for the printer
                   location to appear in the error broadcast message.

      /1username - "username" specifies a user to be notified of error
      /2username   conditions.  Up to 4 users may be specified.
      /3username
      /4username

   SHOWPS.EXE is a command-line utility that reports the status of
   IQS/IQSE print servers connected to your network.



ORDERING I-QUEUE! SERVER
------------------------

I-Queue! Server is currently available for $149, for unlimited use on a
single file server.

I-Queue!, the NetWare Printing Toolbox, is currently available for $199,
for unlimited use on a single file server.

Or, both can be purchased together as the I-Queue! Bundle for $249, for
unlimited use on a single file server.

Dealer inquiries are invited!


                                                                    COST

Please rush me ___ copies of the I-Queue! Bundle for $249 each  ____________
Please rush me ___ copies of I-Queue! Server for $149 each      ____________
Please rush me ___ copies of I-Queue! Toolbox for $199 each     ____________

   Disk Size:  ___ 3-1/2  ___ 5-1/4

Maryland residents add 5% sales tax                             ____________

Shipping and Handling (UPS Ground Service) *                    _______$8___
============================================================================
TOTAL                                                           ____________


   Name:  __________________________________________________________________
Company:  __________________________________________________________________
Address:  __________________________________________________________________
   City:  _____________________  State:  ________  Zip:  ___________________
Country:  _____________________

Telephone Number:  _________________________________________________________
      FAX Number:  _________________________________________________________
   CompuServe ID:  ___________________
     MHS Address:  ___________________ (via _________)

Method of Payment:            ___ Visa  ___ Master Card  ___ Check Enclosed
                                  Card #:  _________________________________
                      Name of Cardholder:  _________________________________
                               Signature:  _________________________________
                         Expiration Date:  _________________________________


* Overseas payments by Visa or Master Charge only.  There will be
  an additional charge applied for shipping costs to reflect the
  actual cost of shipment.




INFINITE TECHNOLOGIES
11433 CRONRIDGE DRIVE, SUITE H
OWINGS MILLS, MD  21117
(410)-363-1097

FAX your credit card orders -- (410)-363-3779



PRODUCTS FROM INFINITE TECHNOLOGIES
===================================

Infinite Technologies offers innovative and easy-to-use software
solutions, designed primarily for the networked environment.

We back our products with dependable service and special attention
to individual requirements.  All of our programs are easy to learn
and use, and are designed to increase your efficiency.

We also want to help keep you up-to-date with product information,
updates and technical support.

These services are provided via the following mechanisms:

On the CompuServe Information Service, Infinite Technologies offers
support and product updates in Section and Library 4 of the NOVVEN
forum.

Via MHS (through CSERVE or NHUB), you can address technical support
and/or product information inquiries to SUPPORT @ INFINITE.

You can also subscribe to our MHS Librarian! mailing list, which
will include notices of product updates.  To join this mailing
list, send a message via MHS (CSERVE or NHUB) to LIBRARY @ INFINITE
with SUBSCRIBE on your subject line.  (CompuServe users can send a
message to >MHS:Library@Infinite via CompuServe Mail.)

For an index of files available via LIBRARY @ INFINITE, send a message
with INDEX on your subject line.


NETWORK UTILITIES
-----------------

*  I-Queue! - Simplifies network printing and print queue management
   in the Novell NetWare environment.  From within a small memory
   resident pop-up (0 to 2-1/2KB), I-Queue! allows users to easily
   change NetWare print queues and modify "capture" parameters.
   I-Queue! is compatible with Novell's PRINTCON/PRINTDEF and adds
   global PRINTCON support for Novell's own utilities.
   Queue management capabilities include:  delete/reorder print jobs,
   move/copy jobs between queues, and hold/delayed printing.
   NOW INCLUDES A WINDOWS VERSION!

*  I-Queue! Server - Turn printers attached to any network workstation
   into shared network printers.  Two to four times faster than RPRINTER,
   compatible with workstations running Windows, and compatible with
   printer ports that do not provide "hardware interrupt support".

*  LockIT! - Intelligent Security for DOS & Windows workstations
   on Novell NetWare networks.  LockIT! addresses the problem of
   users leaving workstations unattended, and the security issues
   that this presents.  Unlike other solutions that will reboot or
   logout a workstation after a period of "inactivity", potentially
   leading to data loss, LockIT! locks out keyboard input until you
   enter your NetWare password...even allowing unattended processes
   to continue executing.

*  CastAway! - A better NetWare broadcast message trap.  Get NetWare
   message notification (e.g., SEND) without your PC locking up until
   you press CTRL-ENTER!  Get notified of new messages while in graphics
   based applications!  All in 0 to 1-1/2KB of conventional memory!

*  PopIT! - Gain pop-up access to almost ANY program with less than
   2-1/2 KB overhead.  Network administrators -- access SYSCON,
   RCONSOLE, FCONSOLE and all of your favorite network utilities
   without leaving your current application.

*  OnCall! - A memory resident "Chat" utility for Novell NetWare,
   that runs in between 0 and 2-1/2 KB of workstation memory.
   Simple, straightforward, and easy to use.  NOW INCLUDES A
   WINDOWS VERSION!

EXPRESSIT! ELECTRONIC MAIL
--------------------------

*  ExpressIT! Electronic Mail - The ExpressIT! Electronic Mail product
   family includes the following products:

   *  ExpressIT! - The network version of ExpressIT!, including
      the MHS-compatible DOS version, which runs in less than 2KB of
      resident memory.

   *  ExpressIT! Remote - A remote version of ExpressIT! (DOS) customized
      for use on stand-alone/remote PCs.  Includes Personal MHS and
      allows users to send and receive mail with any MHS based
      electronic mail system.  Includes the ability to run the MHS
      Connectivity Manager from within the 2KB TSR without exiting
      your current application.

   *  ExpressIT! Windows Client - An upgrade for the network version
      of ExpressIT! offering native support for the Microsoft Windows
      environment, and a wealth of additional features.

   *  ExpressIT! Remote Windows - A remote version of the Windows
      version of ExpressIT! customized for use on stand-alone/remote
      PCs.  Includes Personal MHS and allows users to send and receive
      mail with any MHS based electronic mail system.

      A special Windows based MHS configuration utility eliminates the
      need to use the MHS Directory Manager.

   All versions of ExpressIT! include ExpressIT! Directory Assistance,
   facilitating automatic exchange of user directories between ExpressIT!
   hosts.

MHS GATEWAYS AND UTILITIES
--------------------------

*  MHS Scheduler - An MHS mail agent that provides greater flexibility
   in configuring when MHS will connect to a host.  On a host-by-host
   basis, the MHS administrator can configure different frequencies of
   forced connections based on different times of the day, with
   separate weekday, weekend, and holiday scheduling possible.
   MHS gateways and internetwork connections can also be scheduled.
   The companion RunIT! utility simplifies the creation of batch file
   gateways...now you can run your tape backup system on your MHS
   server.

*  MHS Librarian! - An MHS Gateway that allows users to request
   information to be forwarded to them via MHS.  Requests are
   made by placing a keyword in the "SUBJECT" field of the message
   that you address to the library.  A list of files may be
   requested by sending a message with the keyword of INDEX.  The
   system Admin can also configure MHS Librarian so that selected
   users can request files or directories other than those that
   appear in the index.  Security is provided by a password program
   that generates unique daily passwords, a fixed password, or you
   can create your own password utility.

   MHS Librarian! also supports "discussion lists", similar to
   the "list server" concept on the internet.

*  PageIT! - An MHS gateway connecting MHS-based electronic mail
   systems to full text alphanumeric pagers.  Once configured,
   sending messages to an alphanumeric pager is as simple as
   sending a message from your favorite MHS application.

*  ForwardIT! - An MHS mail agent for automatically forwarding
   MHS based electronic mail messages.  ForwardIT! can forward
   (or copy) messages addressed to an MHS address to an alternate
   address.

   ForwardIT! is most useful in the MHS remote e-mail environment.
   By remote, we refer to field workers or business travelers who
   operate ExpressIT! Remote, or other MHS compatible remote
   software, on a PC or laptop to access their electronic mail
   from a distant location.  Examples could include a salesperson
   between sales calls, a business traveler in a hotel room,
   or work-at-home scenarios.

   Without ForwardIT!, when mail is sent to a recipient's office
   address, MHS does not allow for a remote user to dial into the
   network and retrieve mail waiting for their office address.  Mail
   addressed to this office address can only be picked up at the
   office.

   In order to send a message to the user's MHS remote, the sender
   must assume responsibility for sending a copy of the message to
   the remote MHS address.

   With ForwardIT!, the user leaves a forwarding address at the
   office, and while they're out, all messages will be forwarded,
   or copied, to their forwarding address, giving users transparent
   access to their electronic mail while away from the office.

   This forwarding address can be any valid MHS address, including
   addresses via MHS gateways.

*  MhsQ! - An MHS gateway interface to NetWare print queues.
   Messages can be sent via MHS to a NetWare print queue.
   This capability can be useful for MHS remote sites and/or
   MHS enabled applications for generating printed output
   and/or reports.

   MhsQ! can also redirect print queues on one file server
   to a remote print queue on another file server via MHS.

*  ExpressIT! MHS Directory Assistant - A directory services
   gateway that automatically creates and updates user routes
   in a multi-host workgroup environment.  Add a user at one
   host within the workgroup, and the user route will automatically
   be created at all other hosts within the workgroup.  Add a
   new host to your workgroup, and the host and user lists will
   automatically be added to other hosts within the workgroup.
   (Directory Assistant is bundled with ExpressIT! but is also
   available separately.)

*  MHSNotify! - A TSR which runs on the MHS mail server only, and
   automatically notifies recipients of new electronic mail
   received from remote MHS sites, or across internetwork
   connections.  An excellent alternative to MHSALERT for
   DaVinci e-mail users!  (MHSNotify! is bundled with ExpressIT!)

REQUESTING TRIAL VERSIONS VIA MHS
---------------------------------

   30-Day Trial Versions of many Infinite Technologies Products can
   be requested via MHS.

   For more information, send an MHS message to LIBRARY @ INFINITE
   via CSERVE or NHUB, with a subject line of INDEX.

DOWNLOADING TRIAL VERSIONS FROM COMPUSERVE
------------------------------------------

   30-Day Trial Versions of many Infinite Technologies Products are
   available on CompuServe!  Look for the following files in the
   NOVVEN Forum, Library 4:

      EXPDOS.ZIP - ExpressIT! E-Mail (NetWare) (DOS Version)
      EXPWIN.ZIP - ExpressIT! E-Mail (NetWare) (Windows Version)
      REMDOS.ZIP - ExpressIT! E-Mail (Remote & non-NetWare) (DOS Version)
      REMWIN.ZIP - ExpressIT! E-Mail (Remote & non-NetWare) (Windows Version)
      EXSPEL.ZIP - Supplemental file for ExpressIT! (Spelling Dictionary)

      POPIT.ZIP  - PopIT!
      ONCALL.ZIP - OnCall!
      CASTAW.ZIP - CastAway!
      IQUEUE.ZIP - I-Queue!
      IQS.ZIP    - I-Queue! Server
      LOCKIT.ZIP - LockIT!
      MHSCED.ZIP - MHS Scheduler
      PAGEIT.ZIP - PageIT!
      4WARD.ZIP  - ForwardIT!
      MHSNFY.ZIP - MHSNotify!
      MHSLIB.ZIP - MHS Librarian!
      EXDA.ZIP   - ExpressIT! MHS Directory Assistant
      MHSQ.ZIP   - MhsQ!

   And don't miss our *FREE* utilities (also in NOVVEN Library 4):

      NETERR.ZIP - Network error handlers (CRITTER, SHATTACH)
                   to reboot unattended workstations and clear
                   network errors.
      CREATQ.ZIP - Create NetWare print queues on a volume other
                   than SYS:
      LOGIN.ZIP  - Load TSRs from the NetWare Login Script without
                   losing available memory!
      MHSACT.ZIP - Automatically re-activate deactivated MHS
                   internetwork hosts without operator intervention.
      MHSSWP.ZIP - Redirect MHS swap files to a local drive or
                   VDISK.
      MHSBPL.ZIP - Configure MHS 1.5C host to host communications
                   to use the B+ protocol.
      SENDIT.ZIP - Send MHS messages from the DOS command line
                   or batch files.

   Plus, other helpful text files and reports:

      MHSGAT.TXT - NetWare MHS and Gateways overview
      DOSMEM.TXT - PC Memory management/architecture overview
      WINTIP.TXT - Windows vs. NetWare Troubleshooting Tips



   ...and stay tuned for MORE!!!





FOR MORE INFORMATION, CONTACT:


                      ÜÜÛÛÛÛÜÜ
            ÜÛßÛÜ   ÜÛßß  ßßÛÛÛÜ
           Ûß   ßÛÜÛß        ÛÛÛ
           ßÛÜ ÜÛß ßÛÜÜ    ÜÛÛß
             ßßß      ßßßßßß
           ÛÛÛ           ÜÛÛÛ ÛÛÛ          ÛÛÛ  ÜÛÛ
           ÛÛÛ ÜÜÜ ÜÜÜ  ÜÛÛÛÜ ÜÜÜ ÜÜÜ ÜÜÜ  ÜÜÜ ÜÛÛÛÜ  ÜÜÜÜ
           ÛÛÛ ÛÛÛß ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛß ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛÜÛÛ
           ÛÛÛ ÛÛÛ  ÛÛÛ  ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛ ÛÛÛ  ÛÛÛÜ ßÛÛÜÜÜ

            T   E   C   H   N   O   L   O   G   I   E   S

                   11433 Cronridge Drive, Suite H
                       Owings Mills, MD 21117
                          +1-410-363-1097
                       FAX: +1-410-363-3779

                      MHS: Support @ Infinite
          CompuServe: >MHS:Support @ Infinite (or 73270,405)
            Internet: Support@Infinite.MHS.CompuServe.com

  Technical Support provided on the CompuServe Information Service in
                   NOVVEN Section 4 (GO INFINITE)


 In Germany:
    Ing. B�ro, K.H. Lendroth, Auf dem Kleinen Feld 8, D-2820 Bremen 77
    Telephone: +49 421 6361391, FAX: +49 421 6362344, MHS: KLendrot@Lend-Ing

 In U.K.:
    NetConnect Limited, St. John's Innovation Centre, Cowley Road, Cambridge
    Telephone: +44 223 423523, FAX: +44 223 420655, MHS: SBacon@NetCon

 In Norway:
    Infonor Kompetanse A-S, 1816 Skiptvet, Langli
    Telephone: +47 809 766,  FAX: +47 9 809 814, MHS: Olaf@InfoKomp

 In Australia:
    Future Technologies, Level 2 - 60 York Street, Sydney NSW
    Telephone: +61 02 299-1400, FAX: +61 02 299-1401
    Contacts: Cynthia Kuiper, Richard Denyer or Steve Ross