Gport

                    C Language Game Port Library

                    Version 1.01

                    1 September 91

                    Copyright (c) 1991  Bri Productions










































                                        1




        Table of Contents


            Introduction

                    General Description.....................3

                    Disclaimer..............................3

                    Registration............................3

                    Contacting the Author...................3

                    A typedef...............................3


            General Functions

                    Description.............................4

                    GamOpen.................................5

                    GamClose................................6

                    GamAxis.................................6

                    GamAxes.................................7

                    GamButton...............................8


            Calibration Functions

                    Description............................10

                    GamRawAxis.............................11

                    GamCalAxis.............................12

                    GamCenter..............................13



            Appendix A - Things to Look Out For............15

            Appendix B - Joystick Calibration/Centering....16

            Appendix C - Registration Form.................18










                                        2




        General Description.

        Gport is a C language, high speed, high resolution game port
        library for IBM and compatible computers. Gport is compatible
        with most if not all DOS based C compilers.


        Some of Gport's features are:

        ù Timer driven button monitor.
        ù Optional joystick calibration.
        ù Choice of REAL or MEAN centering modes.
        ù Yields higher resolution on faster computers.
        ù Constant axis scaling to approximately ñ1000.
        ù Written in assembly language for optimum speed and efficiency.


        DISCLAIMER.

        Gport is provided AS IS. Bri Productions specifically disclaims
        any and all warranties, expressed or implied, including fitness
        for a particular purpose. Use this product at your own risk.


        Registration.

        Gport is a user supported software product. Distribution of
        this product, unaltered and without charge, is encouraged. If
        you find this product useful, you are encouraged to register
        your copy. This allows Bri Productions to continue to provide
        and support low cost, high quality shareware.

        The registration fee is $25.00 US dollars and includes libraries
        for small, medium, compact and large memory models and complete
        source code. A registration form is provided in Appendix C.


        Contacting the author.

        Bri Productions may be contacted by any of the following means:

        U.S. mail       -       Bri Productions
                                P.O.Box 7121
                                Fremont, CA 94537-7121
        Phone           -       (510) 794-0616
        CompuServe      -       76635,2246

        CompuServe is a trademark of CompuServe Inc.


        A typedef.

        You will see the data type 'byte' throughout the Gport library.
        This is a typedef defined in gport.h. Byte is an unsigned
        character used for byte size values.




                                        3




        General functions

        There are two functions that are required before other game
        port functions can be called. They are GamOpen() and GamClose().
        GamOpen() initializes the game port and installs an interrupt
        handler for monitoring the buttons. GamClose() releases the
        interrupt handler. Failing to call GamClose() prior to the
        program's termination will most certainly cause an operating
        system crash.

        GamAxis() and GamAxes() fetches the position(s) of one or
        more joystick axes. A full up or right joystick returns a value
        of approximately +1000 and full down or left returns a value of
        approximately -1000. GamButton() fetches the status of the game
        port's buttons. Information on a button pressed since the last
        call to GamButton() as well as a presently pressed is available.










































                                        4




        ----------------------------------------------------------------
        GamOpen
        ----------------------------------------------------------------

        Function

                Initializes the game port and installs the interrupt
                handler.


        Syntax

                #include "gport.h"
                int GamOpen(void);


        Remarks

                GamOpen initializes the game port. If an axis is found to
                be valid, it's corresponding bit is set in the returned
                status word. After a call to GamOpen, a subsequent call
                to GamClose is required. Failure to do so will most
                definitely cause the operating system to crash.


        Return Value

                GamOpen returns a valid axis status word. The bits/values
                are defined as follows:

                        JAX_VAL  (0x1) - Joystick A, x axis valid
                        JAY_VAL  (0x2) - Joystick A, y axis valid
                        JA_VAL   (0x3) - Joystick A, both axes valid
                        JBX_VAL  (0x4) - Joystick B, x axis valid
                        JBY_VAL  (0x8) - Joystick B, y axis valid
                        JB_VAL   (0xC) - Joystick B, both axes valid


        See also

                GamClose


        Example

                Attempt to open the game port and check Joystick A.

                {
                int valid_axes;

                   valid_axes = GamOpen();
                   if((valid_axis & JA_VAL) == JA_VAL)
                   {
                      ...Joystick A OK

                   }
                }

                                        5




        ----------------------------------------------------------------
        GamClose
        ----------------------------------------------------------------

        Function

                Releases the interrupt handler.


        Syntax

                #include "gport.h"
                void GamClose(void);


        Remarks

                After a call to GamOpen, a subsequent call to GamClose
                is required. Failure to do so will most definitely cause
                the operating system to crash.


        See also

                GamOpen


        Example

                Close the game port prior to terminating.

                {

                  ...closing code

                  GamClose();
                  exit(0)

                }




        ----------------------------------------------------------------
        GamAxis
        ----------------------------------------------------------------

        Function

                Gets the coordinate of a joystick axis.


        Syntax

                #include "gport.h"
                signed GamAxis(byte axis);


                                        6




        Parameters

                axis  - Constant that defines which axis to get the
                        coordinate of. Possibilities are:

                           JAX  (0) - Joystick A, X axis
                           JAY  (1) - Joystick A, Y axis
                           JBX  (2) - Joystick B, X axis
                           JBY  (3) - Joystick B, Y axis


        Remarks

                GamAxis fetches the coordinate of a single joystick
                axis. The coordinate is returned as a signed integer.


        Return value

                GamCoord returns the coordinate of the specified axis.
                The values will range from -1000 to +1000.


        See also

                GamAxes GamButton




        Example

                Update the current positions of the X & Y axes for
                joystick A.


                {

                   YourXaxisFunction( GamAxis(JAX) );
                   YourYaxisFunction( GamAxis(JAY) );
                }



        ----------------------------------------------------------------
        GamAxes
        ----------------------------------------------------------------

        Function

                Gets the both axes coordinates of a joystick.


        Syntax

                #include "gport.h"
                void GamAxes(byte stick, signed *x, signed *y);

                                        7






        Parameters

                stick - Constant that defines which joystick to get
                        the coordinates of. Possibilities are:

                           JA  (0) - Joystick A
                           JB  (1) - Joystick B

                    x - pointer to the signed integer where the x axis
                        coordinate will be stored.

                    y - pointer to the signed integer where the y axis
                        coordinate will be stored.


        Remarks

                GamAxes fetches the coordinates of both axes for
                the specified joystick. The coordinates are stored
                at the pointers passed to GamAxes. The values will
                range from -1000 to +1000.



        See also

                GamAxis GamButton


        Example

                Update the current positions of the X & Y axes for
                joystick A.


                {
                signed x,y;

                   GamAxes(JA, &x, &y);

                   YourXaxisFunction( x );
                   YourYaxisFunction( y );
                }



        ----------------------------------------------------------------
        GamButton
        ----------------------------------------------------------------

        Function

                Gets the status of the joystick buttons.



                                        8




        Syntax

                #include "gport.h"
                byte GamButton(void);


        Remarks

                GamButton returns the current status of the joystick
                buttons as well as any button status since the last
                call to GamButton.


        Return value

                GamButton returns the status of the joystick buttons.
                If the button is currently pressed, it's current bit
                will be set. If a button has been pressed since the
                last call to GamButton, it's pending bit is set.
                The bit constants are as follows:

                  BA1_CURR (0x01) - Joystick A, button 1 current.
                  BA2_CURR (0x02) - Joystick A, button 2 current.
                  BB1_CURR (0x04) - Joystick B, button 1 current.
                  BB2_CURR (0x08) - Joystick B, button 2 current.
                  BA1_PEND (0x10) - Joystick A, button 1 pending.
                  BA2_PEND (0x20) - Joystick A, button 2 pending.
                  BB1_PEND (0x40) - Joystick B, button 1 pending.
                  BB2_PEND (0x80) - Joystick B, button 2 pending.


        See also

                GamAxis GamAxes


        Example

                Check if the player has fired (button 1). If so
                call the fire update function.

                #define FIRE  (BA1_PEND) | (BA1_CURR)

                {

                   if(GamButton() & FIRE)
                   {
                      YourFireFunction();

                      ...more code
                   }

                }





                                        9





        Calibration Functions


        The performance of the joystick can be significantly improved
        by calibrating it, especially if the joystick is misaligned.
        This is achieved by collecting the raw value of the position of
        the joystick extremes; full up, down, left, and right; and
        recalculating scaling math. GamRawAxis() fetches the raw
        value of the position of the joystick, which is passed to the
        function GamCalAxis(). GamCalAxis() then recalculates the
        scaling math.

        The calibration is done in two steps in order to leave open
        the option of saving the raw values to disk for future
        reference. This saves the step of having to recalibrate
        every time a program is run.

        GamCenter() sets the centering mode. There are two ways to
        determine where the center of a joystick is. The REAL center
        is defined as where the joystick comes to rest. The MEAN
        center is defined as the mean between the joystick extremes.

        For a more detailed description on calibration, see Appendix B.


































                                        10




        ----------------------------------------------------------------
        GamRawAxis
        ----------------------------------------------------------------

        Function

                Gets the raw value of a joystick axis.


        Syntax

                #include "gport.h"
                unsigned GamRawAxis(byte axis);


        Parameters

                axis  - Constant that defines which axis to get the
                        coordinate of. Possibilities are:

                           JAX  (0) - Joystick A, X axis
                           JAY  (1) - Joystick A, Y axis
                           JBX  (2) - Joystick B, X axis
                           JBY  (3) - Joystick B, Y axis


        Remarks

                GamRawAxis returns the raw value of a joystick position
                to be used for calibrating the joystick . Smaller values
                are to the left and up while larger values are to the
                right and down. The actual value will vary from machine
                to machine.


        Return value

                GamRawAxis returns the raw value for the position of
                the selected joystick axis.


        See also

                GamCal GamCenter


        Example

                Calibrate the X axis on joystick A.

                {
                int raw_ax_right;
                int raw_ax_left;


                   puts("Hold joystick full right and press any key");
                   getch();

                                        11




                   raw_ax_right = GamRawAxis(JAX);
                   GamCalAxis(JAX, raw_ax_left);

                   puts("Hold joystick full left and press any key");
                   getch();
                   raw_ax_left  = GamRawAxis(JAX);
                   GamCalAxis(JAX, raw_ax_right);
                }




        ----------------------------------------------------------------
        GamCalAxis
        ----------------------------------------------------------------

        Function

                Calibrates a joystick axis extreme from a raw value.


        Syntax

                #include "gport.h"
                void GamCalAxis(byte axis, unsigned raw_value);


        Parameters

                axis  - Constant that defines which axis to get the
                        coordinate of. Possibilities are:

                           JAX  (0) - Joystick A, X axis
                           JAY  (1) - Joystick A, Y axis
                           JBX  (2) - Joystick B, X axis
                           JBY  (3) - Joystick B, Y axis

                raw_value - Raw value returned from a call to GamRaw
                        on which to calibrate.


        Remarks

                GamCalAxis calibrates a joystick extreme from a raw
                value from a previous call to GamRawAxis. Notice that
                it is not necessary to specify the extreme (left/right
                or up/down) in question.


        See also

                GamRawAxis GamCenter






                                        12




        Example

                Calibrate the X axis on joystick A.

                {

                   puts("Hold joystick full right and press any key");
                   getch();
                   GamCalAxis(JAX, GamRawAxis(JAX));

                   puts("Hold joystick full left and press any key");
                   getch();
                   GamCalAxis(JAX, GamRawAxis(JAX));
                }



        ----------------------------------------------------------------
        GamCenter
        ----------------------------------------------------------------

        Function

                Sets the centering mode.


        Syntax

                #include "gport.h"
                void GamCenter(byte mode);


        Parameters

                mode - Constant defining the centering mode to be used.
                       Possibilities are:

                       *  REAL (0) - real centering mode.
                          MEAN (1) - mean value centering.

                          * default

        Remarks

                GamCenter sets the centering mode to be used. In real
                mode, the center of an axis will be where the joystick
                is at rest. In mean mode, the center is calculated as
                the mean between the two previously calibrated extremes.
                For a more detailed description of the centering
                modes see Appendix B.


        See also

                GamRawAxis GamCalAxis



                                        13




        Example

                Set the centering to mean mode.

                {

                        GamCenter(MEAN);

                }

















































                                        14




        Appendix A


        Things to look out for.

        ù Gport installs a timer interrupt at interrupt 0x1C (user
          timer link). Gport does not take over this interrupt but
          chains into it.

        ù Some faster machines will exhibit a "fold back" on the down
          and right strokes of the joystick. Special AT game ports
          are available which usually resolve this problem.














































                                        15




          Appendix B


        Calibration

        When the function GamOpen() is called, some assumptions are made
        about the raw values of the positions of the joystick extremes;
        left, right, up and down. The assumptions are based on the raw
        value of the joystick axes at the time of the call to  GamOpen()
        (at rest at the center). In most cases the joystick will perform
        reasonably well providing the alignment of the joystick is at
        least fair.

        The performance of the joystick can be greatly improved if it
        is calibrated. Even a poorly aligned joystick can be made to
        appear to perform quite well. In order to accomplish this the
        assumptions about the joystick extremes must be replaced by
        their actual raw values. This requires the cooperation of the
        user as well as the functions GamRawAxis() and GamCalAxis().

        Typically the user will be prompted to hold the joystick to
        each of the four extremes and hit a key on the keyboard. For
        each extreme, the raw value of the joystick position is read
        by a call to GamRawAxis() and the returned value is passes to
        GamCalAxis(). GamCalAxis will then make some recalculations
        and replace the previous assumptions (or calibration).

        Notice that the calibration is done in two steps. First the
        raw value is fetched and then it is passed. This allows the
        program to store the raw values for future reference. Next
        time the program is run, the values can be retrieved and
        passes directly to GamCalAxis(). This saves the step of
        having to interface with the user and calling GamRawAxis()
        every time the program runs.




        Centering

        There are two ways to interpret where the center of the
        joystick is . One way is to define the center as being where
        the joystick comes to rest. Gport port refers to this as REAL
        mode. The second way is to define the center as being
        equidistant, or at the mean, from all of the joystick extremes.
        Gport refers to this centering mode as MEAN mode.

        REAL mode has the obvious advantage that the joystick will
        always return approximately to the center. This will preclude
        any drifting. The disadvantage of REAL mode is that there is
        no evidence of how well the joystick is actually aligned.

        The advantage and disadvantage of MEAN mode is the complement
        of those of REAL mode. Drift will occur if the joystick is
        not aligned well. But since there will be the evidence of
        the joystick's misalignment, MEAN mode could be used to
        actually align a joystick.

                                        16





        Recall that MEAN mode refers to the joystick extremes. Also
        recall that the joystick extremes are assumed until the
        joystick is calibrated. For this reason there is little
        difference between the two centering modes until the joystick
        is calibrated. Calculating the mean center using the assumed
        extremes will result in the same center since the reverse
        process is used to calculate the assumed extremes.


















































                                        17




      Appendix C


        Gport Registration Form

        Name: ______________________________________________________

        Company: ___________________________________________________

        Address: ___________________________________________________

        City: ____________________________  State: _________________

        Zip code: _________________  Phone # : _____________________

        CompuServe # : _____________________________________________

        How did you acquire Gport ? _________________________________

        ____________________________________________________________

        What functions do you find most useful ?____________________

        ____________________________________________________________

        What functions do you find least useful ?___________________

        ____________________________________________________________

        What functions, not in Gport, would you like to see ?_______

        ____________________________________________________________

        What other types of libraries would you find useful ?_______

        __ Serial Communications  __ Expanded Memory  __ IEEE/GPIB

        Others: ____________________________________________________

        registration                                      $ 25.00

        California residents add sales tax (  8.25% )     $________

        shipping inside continental U.S.   ( $ 2.00 )
        shipping outside continental U.S.  ( $ 5.00 )     $________


                                                 Total:   $________

        All Payments Must be in U.S. Dollars

        Make check or money order payable to:    Bri Productions
                                                 P.O. Box 7121
                                                 Fremont, CA 94537-7121




                                        18