TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


                               Table of Contents


    1. INTRODUCTION...................................... 2
        1.1. Purpose of TbUtil........................... 2

    2. USAGE OF THE PROGRAM.............................. 4
        2.1. System requirements......................... 4
        2.2. Program invocation.......................... 4
        2.3. Command line options........................ 4
            2.3.1. immunize ............................. 4
            2.3.2. patch ................................ 5
            2.3.3. store ................................ 5
            2.3.4. compare .............................. 6
            2.3.5. restore .............................. 6
            2.3.6. norepeat ............................. 6
            2.3.7. description .......................... 6
            2.3.8. part ................................. 6
            2.3.9. boot ................................. 7
            2.3.10. cmos ................................ 7
        2.4. Examples:................................... 7
        2.5. Using the anti-virus partition.............. 7

    3. THE THUNDERBYTE PARTITION CODE.................... 9
        3.1. What is a partition?........................ 9
        3.2. What is a partition table?.................. 9
        3.3. The partition code.......................... 9

    4. MISCELLANOUS INFORMATION......................... 12
        4.1. Exit codes................................. 12
        4.2. Recommendations............................ 12
























                                     Page i




























































                                     Page 1


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


1.  INTRODUCTION


  1.1.  Purpose of TbUtil

    TbUtil has been developed as a tool to provide a defense against
    partition table and bootsector viruses.

    -   It can save the partition table, bootsector and CMOS data area
        to a file.

    -   It can compare and restore the partition table, bootsector and
        CMOS data area after an (virus) accident.

    -   It can remove a partition table virus without having to
        low-level format the hard disk, even if there is no backup of
        the partition table.

    -   It can remove bootsector viruses.

    -   It can create a partition table that has some first-line virus
        defense built-in.

    -   It can replace the infected or clean bootsector by a bootsector
        which has advantages over the standard ones.

    Unlike most file viruses, partition table viruses are hard to
    remove. The only solution is to low-level format the hard disk and
    to make a new partition table, or to make use of undocumented DOS
    commands.

    TbUtil makes a backup of the partition table and bootsector, and
    this backup can be used to compare and restore the original
    partition table and bootsector once they are infected. You don't
    have to format your disk anymore to get rid of a partition table or
    bootsector virus.  The program can also restore the CMOS
    configuration.

    If your partition table is damaged and you don't have a backup of
    it, TbUtil will try to create a new partition table, avoiding the
    need of a low-level format.

    Another important feature is that you can use TbUtil to replace the
    partition table code with it's own code which is more resistant
    against viruses. The TbUtil partition code will be executed before
    the bootsector gains control, so it is able to check the bootsector
    in a clean environment. Once the bootsector is executed it is
    difficult to check it, because the virus is already resident in
    memory and can fool every protection. Instead of booting from a
    clean DOS diskette just to inspect the bootsector, the TbUtil
    partition code performs a CRC calculation on the bootsector just
    before control is passed to it. If the bootsector has been modified



                                     Page 2


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


    the TbUtil partition code will warn you about this. The TbUtil
    partition code also checks the RAM layout and informs you when it
    is changed. It does this every time you boot from your hard disk.

    TbUtil can replace infected and clean bootsectors by a new
    bootsector, which has advantages over the standard bootsector.  It
    has bootsector virus detection capabilities, it performs a sanity
    check, and it offers you the possibility to redirect the boot
    process to the hard disk without opening the diskette drive door.














































                                     Page 3


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


2.  USAGE OF THE PROGRAM


  2.1.  System requirements

    TbUtil should work on any machine with a working hard disk, and
    with any DOS version.  The program requires only about 64Kb of free
    RAM to execute.


  2.2.  Program invocation

    The use of the program is very easy: just run TbUtil without
    parameters to get a help screen.

    The syntax:
                TBUTIL <options>


  2.3.  Command line options

    It is possible to specify options on the command line. TbUtil
    recognizes option-characters and option-words. The words are
    easier to remember, and they will be used in this manual for
    convenience.

    optionword  parameter short  explanation
    ----------  --------- ---- -------------------------------------
    immunize <drive>       im  = Immunize/Clean boot/MBR of <drive>
    patch    <filename>    pa  = Patch format utility <filename>
    store    [<filename>]  st  = Store system information
    restore  [<filename>]  re  = Restore system information
    compare  [<filename>]  co  = Compare system information
        Sub-options of option 'Immunize':
    norepeat               nr  = Do not ask for next diskette
        Sub-options of option 'Store':
    description =<descr.>  de  = Add description to data file
        Sub-options of option 'Restore':
    part                   pt  = Restore partition table
    boot                   bo  = Restore bootsector of HD
    cmos                   cm  = Restore CMOS

   2.3.1.  immunize (im)

    This option requires an additional parameter specifying the drive 
    to process. You can specify the hard disk as well as diskette 
    drives.

    Effect of option 'immunize' on the hard disk (immunize C:)

    This is a very powerful option, it can be used to clean an
    infected partition table if there is no TbUtil data file, and it



                                     Page 4


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


    replaces the existing partition table code by a new partition
    routine that has some virus detection capabilities. The original
    partition code will be saved in a file. You have to run TbUtil
    from a floppy drive or you have to specify the name of the file
    (the specified drive should be a diskette drive) to store the
    original partition code. For more information about the
    new partition code see the next chapter.

    If the original partition table is completely damaged and can not
    be used to built a new one, TbUtil will search the entire disk for
    information about the original disk layout. TbUtil will also search
    for TbUtil data files on the hard disk. It is however recommended
    to store the data file on a diskette, but it is a good idea to keep
    a copy of it on the hard disk.  Just in case!

    Effect of option 'immunize' on diskette drives.

    Option 'immunize' can be used to clean diskettes infected by a 
    bootsector virus. Option 'immunize' can also be used to replace the 
    standard bootsector by a bootsector which has advantages over the 
    original one:

    -   It has virus detection capabilities. The bootsector will check 
        that it is still located on the correct place on the diskette, 
        and that Int 13h and/or Int 40h are still located in system 
        ROM. This makes it possible to detect even 'stealth' viruses.

    -   The TBAV bootsector is able to load the system files if they 
        are available on the disk, but if the DOS system files are not
        on the disk the TBAV bootsector will present a small menu and 
        offers you two possibilities: retry the boot operation with 
        another diskette, or to boot from the harddisk. If the user 
        selects the latter, it is not required to open the 
        diskette drive door.

   2.3.2.  patch (pa)

    The TBAV bootsector is quite convenient, but it has to be installed 
    by TbUtil every time you format a diskette. Option 'patch' allows 
    you to patch your format utility so that it automatically writes 
    the TBAV bootsector to the diskette being formatted, instead of
    the 'standard' bootsector. You should specify the name of the 
    format utility you wish to modify. TBAV will automatically locate 
    the bootsector within the format utility and replace it by the 
    enhanced TBAV bootsector. The format utility will now write the
    TBAV bootsector to the diskette rather than the standard one.

   2.3.3.  store (st)

    This option stores the partition table, bootsector and CMOS data
    area into the TbUtil data file. 




                                     Page 5


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


   2.3.4.  compare (co)

    This option enables you to check that everything is still Ok.  If
    you specify this option TbUtil will compare the information in
    the TbUtil data file against the partition table, bootsector and
    CMOS data area.  It will also show the comment stored in the data
    file. And of course, if you use this option you will also be sure
    that the TbUtil data file is still readable.

   2.3.5.  restore (re)

    This option enables you to restore the partition table, bootsector,
    and CMOS data area. It will ask you to confirm that the data file
    belongs to the current machine. Finally it will restore the
    partition table, bootsector of the partition to be used to boot,
    and the CMOS data area.

   2.3.6.  norepeat (nr)

    TbUtil will prompt you for next diskette after you immunized a 
    diskette. With option 'norepeat' you can disable this.

   2.3.7.  description (de)

    You can add a description to a TbUtil data file, which makes it 
    easier to determine which data file belongs to which machine.

    Enter a meaningful description of the machine. Enter something like 
    "AT 12MHz, 4Mb, room 12, Mr. Smith".  You do NOT have to remember 
    it, TbUtil will display it on the screen when comparing or 
    restoring, but it helps you to verify that the data file belongs to 
    the machine.

    It is also possible to check the comment from the DOS command
    prompt. Enter:
                Type TbUtil.Dat
    This will show the comment of the TbUtil.Dat file (without any
    other garbage being displayed).

    Note: if you want to include spaces within the comment, you should 
    surround the text by quotes (").

    Example:
        TbUtil Store Descripion="AT 12 MHz, 4Mb, room 12"

   2.3.8.  part (pt)

    TbUtil will by default restore the partition code, bootsector and 
    CMOS if option 'restore' is specified. If you use one of the 
    options 'part', 'boot' or 'cmos' in combination with option 
    'restore' TbUtil will restore just the items specified.




                                     Page 6


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


   2.3.9.  boot (bo)

    TbUtil will by default restore the partition code, bootsector and 
    CMOS if option 'restore' is specified. If you use one of the 
    options 'part', 'boot' or 'cmos' in combination with option 
    'restore' TbUtil will restore just the items specified.

   2.3.10.  cmos (cm)

    TbUtil will by default restore the partition code, bootsector and 
    CMOS if option 'restore' is specified. If you use one of the 
    options 'part', 'boot' or 'cmos' in combination with option 
    'restore' TbUtil will restore just the items specified.


  2.4.  Examples:

        TbUtil store

        TbUtil st

        TbUtil store A:TbUtil.Dat

        TbUtil store A:TbUtil.Dat description = "Test machine"

        TbUtil compare A:TbUtil.Dat

        TbUtil restore A:TbUtil.Dat part cmos

        TbUtil immunize A:

        TbUtil patch c:\dos\format.com

        Type A:TbUtil.Dat


  2.5.  Using the anti-virus partition.

    If you install the Thunderbyte partition code (TbUtil immunize),
    you will see the following while booting a clean system:

        Thunderbyte anti-virus partition v5.00 (C) 1992 Thunderbyte BV.

        Checking bootsector CRC -> OK!
        Checking available RAM -> OK!
        Checking INT 13h -> OK!

    If there is a virus in the bootsector or partition table you will
    see this:

        Thunderbyte anti-virus partition v5.00 (C) 1992 Thunderbyte BV.




                                     Page 7


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


        Checking bootsector CRC -> OK!
        Checking available RAM -> Failed!

        System might be infected. Continue? (N/Y)

    If your system configuration changes, i.e. you update your DOS
    version, or change the amount of memory, you need to update the
    information stored in the immune partition too. You can do this
    with the command "TbUtil immunize c:".

    Some other messages that can be displayed are "No system.", which 
    means that there is no active partition on the disk, and "Disk 
    error" which meaning is obvious.










































                                     Page 8


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


3.  THE THUNDERBYTE PARTITION CODE.


  3.1.  What is a partition?

    A partition is a logical drive on a hard disk. One physical hard
    disk can contain mulitple DOS partitions. Every DOS partition has
    its own drive ID (C: D: E:).


  3.2.  What is a partition table?

    How does the system know about the disk lay-out? How does the
    system know where a partition starts and ends?
    This is defined by the partition table. The partition table contains
    the start and end cylinder of every partition. The partition table
    also carries information about the operating system of a partition
    and which partition should be used to boot. The partition table is
    always located at the first sector of the hard disk. It is called 
    the "Master Boot Record".


  3.3.  The partition code

    The first sector of the hard disk contains the partition table, but
    it also contains a piece of code. This code will be called by the
    BIOS boot-routine of the machine. It is the first piece of non-BIOS
    code that will be executed. The partition code normally interprets
    the partition table, and determines which partition should be used
    to boot. It reads the bootsector of the bootable partition and
    transfers control to it. The bootsector invokes the DOS hidden
    files and the system fires up.

    Since the partition code does not do very much and is a very small
    routine (about 80 bytes) you will never notice that it is there and
    is executed every time you boot.

    However, there are some viruses which overwrite the existing
    partition table or bootsector, and while performing the normal boot
    procedure, the code remains resident in memory and infects every
    diskette. When there is a virus in a file, you can easily get rid
    of the virus by deleting the infected file. However, the partition
    table can not be deleted, and the only thing a user can do is to
    low-level format the hard disk and to re-partition it, take their
    chances with undocumented DOS commands, or to use TbUtil (or a
    similar product) to restore the original partition table.

    Anyway, it is often difficult to detect a partition or
    bootsector virus, since the virus is already resident in memory
    when DOS and eventually an anti-virus product fires up. Like any
    other memory resident program, a virus can do anything. The virus
    intercepts the BIOS calls, and if an anti-virus product (a scanner



                                     Page 9


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


    or checksummer) wants to read the bootsector in order to inspect
    it, the virus intercepts the BIOS request, and supplies the program
    with an unaltered copy of the original bootsector stored somewhere
    on the disk, instead of the infected bootsector. This means that a
    well-designed bootsector virus can hide itself completely from
    anti-virus products. To detect the virus, you have to be sure the
    virus is not resident in memory. There are only two possibilities
    to achieve this:

    -   By booting from a clean DOS diskette (the virus is not executed
        and not resident in memory and can not prevent the anti-virus
        program to read it)

    -   By executing a piece of software that is executed before the
        bootsector gains control. The only software that is executed
        before the bootsector gains control is the machine BIOS and
        additional hardware (like Thunderbyte) and the partition code...

    Except for hardware immunizers (like Thunderbyte) only the
    partition code will be executed before the bootsector gains
    control, so only a routine in the partition code can safely check
    the bootsector while booting from the harddisk.

    This consideration has lead to the development of the Thunderbyte
    anti-virus partition code. The Thunderbyte anti-virus code performs
    the normal tasks of the partition code, but it also has some
    additional routines, which check the CRC (a sophisticated sort of
    checksum) of the bootsector, the amount of free RAM, and the
    location of the INT 13h handler.

    Smart users will have noticed that we changed our subject from
    partition viruses to bootsector viruses. The bootsector can be
    checked completely by the partition code, but how about the
    partition code itself? The answer is that it is not possible to
    check the partition code accurately. This can only be done by
    hardware like the Thunderbyte add-on card. However, we have
    built-in some additional tools to detect partition table viruses.
    To know how they work additional information about partition
    viruses is required.

    A partition virus that wants to hide itself has to remain resident
    in memory and has to intercept all attempts to read the partition
    code. Since the partition code is normally removed from memory as
    soon as DOS fires up, the partition virus has to 1) allocate some
    memory to remain resident. The virus also has to intercept all
    requests to read the partition code in order to hide itself, so it
    has to 2) hook the BIOS INT 13h call. After the virus is memory
    resident, the virus reads the original partition code and transfers
    control to it. For the user nothing has changed...

    When installing the Thunderbyte partition code, TbUtil determines
    the amount of RAM at system startup and it calculates the CRC of



                                    Page 10


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


    the bootsector of the bootable harddisk partition. Both values are
    stored in the partition code.

    If there is a virus in the bootsector the CRC does not match
    anymore, and the partition code will notify the user of this. If
    the partition code has been overwritten by a virus, and the virus
    has installed itself in memory before invoking the Thunderbyte
    partition code, the amount of available RAM has been decreased.
    The Thunderbyte partition code will notify the user about the
    unexepected RAM decrease. Finally, the partition code will check
    whether INT 13h points to ROM or RAM. Usually, the partition code
    is the first piece of software being executed, so INT 13h should
    point to ROM. If it points to RAM it means that another piece of
    software has been executed before the Thunderbyte partition gained
    control, and it is likely that it is a virus. If the virus did not
    hook INT 13h, it would be possible to detect the virus with a
    normal virus scanner or checksummer. Anyway, if INT 13h points to
    RAM, the Thunderbyte partition code will notify the user of this.





































                                    Page 11


 TbUtil anti virus tool. (C) Copyright 1988-1993 Thunderbyte B.V.


4.  MISCELLANOUS INFORMATION


  4.1.  Exit codes

    TbUtil terminates with one of the following exit codes:
        Errorlevel 1 when option 'compare' fails or an error occurs.
        Errorlevel 0 when everything was okay.


  4.2.  Recommendations

    Since the PC is completely inaccessable to DOS if the partition
    table gets damaged, it is HIGHLY RECOMMENDED to store both the
    TbUtil data file and the program TbUtil.Exe itself on a diskette!
    It is not nice if the partition table is destroyed, and the only
    solution to the problem resides on the same inaccessable disk...

    If you own more than one PC, create one TbUtil diskette with all
    TbUtil data files of all your PC's on it.  Just execute "TbUtil
    store = a:TbUtil.<number>" on every PC's.  The number specifies
    the number (or even name) of the PC.

    Do NOT automatically invoke TbUtil from within the autoexec.bat
    file with the 'store' option set. If you do this, the data file will
    be overwritten by the virus immediately after the disk gets
    infected.




























                                    Page 12