VIDTYPE 1.1
                             by Yousuf Khan

Introduction
============

You may use this program's executable, VIDTYPE.COM, with no obligations
or fees and include it in any software package, shareware or commercial
as you please. You may use all or parts of this program's source code,
VIDTYPE.ASM, with no fees, and with the sole condition that you
mention me within your own programming ventures.

This document divides itself between two sections. The first section
describes how to use this program and how to interpret its information.
The second section describes how it was programmed.

(1) How to use this program
===========================

IBM PCs were designed from the beginning to be able to use many
different types of video hardware. Not only that, but PCs can use upto
two different video subsystems at once. This program will identify many
of these adapters, and it will return configurable DOS errorlevels for
testing inside of batchfiles.

The following are the command-line parameters you can feed to the
program before running:

Param   Function
-----   --------
none    errorlevel based on prim subsystem standard video code
"e"     errorlevel based on prim subsystem extended video code
"2"     errorlevel based on sec subsystem standard video code
both    errorlevel based on sec subsystem extended video code

Examples would be:

vidtype
vidtype e
vidtype 2
vidtype e2
vidtype 2E

You'll note that upper or lower case do not matter.

The Standard or Extended video Code:
-----------------------------------
The standard video code returns standard IBM-recognized video adapters,
such as CGA, MDA, MCGA, EGA, or VGA. Just about all video adapters will
return at least one of these codes for compatibility.

The extended video code is returned only by extended adapter types like
the various Hercules or Super VGA adapters. The Hercules adapters, for
example, all appear to be standard MDA monochrome adapters to the
standard video code, but they are recognized separately in the extended
video code. Same for the Super VGA adapters, which all appear to be
standard VGA, but separate extended.

        Extended MDA errorlevel codes:
        0       no Hercules, regular MDA only
        1       regular Hercules card
        2       Hercules Plus card
        3       Hercules InColor card

        Extended VGA errorlevel codes:
        0       regular VGA
        1       ATI
        2       Ahead
        3       Paradise
        4       Oak
        5       Genoa
        6       Cirrus
        7       Chips&Tech
        8       Tseng
        9       ZyMos
        If a VESA BIOS is present, then add 128 to errorlevels returned.

The Primary or Secondary Subsystem:
----------------------------------
The primary video subsystem is the system where DOS and BIOS will send
all their output to at present. The secondary is system is considered to
be dormant, but it to can be used independently by software that
recognizes the existence of two separate subsystems. At any time you can
swap which subsystem is primary or secondary with the DOS MODE command.

VIDTYPE will return a screen similar to the one below:

VIDTYPE v1.0 (c) 1992, Yousuf J. Khan
    Primary video subsystem:
        Standard video information:
            VGA w/ color analog display
        Extended video information:
            Super VGA: ATI
            VESA BIOS present
    Secondary video subsystem:
        Standard video information:
            no display
        Extended video information:
            no extended info available

In the above example, we have a system with a single primary subsystem,
no secondary subsystem. It was determined to be a VGA standard, an ATI
Super VGA extended, and had a VESA BIOS installed.

(2) Programming highlights
==========================

You will find the complete assembler source code, VIDTYPE.ASM, included
in this archive. It was written in Masm-style code with Borland's Turbo
Assembler 2.0. Although I've attempted to maintain Masm compatibility as
best as I can, there's no guarantees that it will assemble under Masm.

There are four important instance variables in the system. They are
[Std0type], [Ext0type], [Std1type], and [Ext1type]. Each are a byte
long. [Std?type] variables all indicate an IBM standard video adapter
type, such as CGA, MDA, EGA, or VGA. [Ext?type] variables all indicate
extended information (if available) about those adapters, eg. whether an
MDA is also a Hercules-style monographics adapter, or whether a VGA is a
form of Super VGA. [*0type] variables indicate that the information has
been gathered for the primary video subsystem, while [*1type] indicates
info about the secondary subsystem.

There is a fifth instance variable, also a byte long, [egatype], which
is used only after the EGA adaptor detection test. Since the EGA can be
either a monochrome or color adaptor, after the test, this instance
variable indicates which one it was. If a monochrome EGA were found, for
example, then the MDA test could be be skipped later. Similarly if a
color EGA were found the CGA tests could be skipped.

The first test carried out is the procedure FindVGA. It uses video BIOS
function AX=1A00h, Get Display Combination Code, which is only available
on PS/2, MCGA, and/or VGA systems. If it is detected that this function
is supported by the current machine, then no more work needs to be done
to detect standard video display types, because all the relevant
information is returned in BX by this function. BH contains the display
combination code (DCC) for the secondary subsystem, and BL contains the
DCC for the primary. A list of DCCs is included inside the FindVGA
procedure.

However, even though the DCC is returned, it only represents information
relevant to standard video adapter types, tests still need to be done to
determine extended video types. If an MDA is found then the FindHGC
procedure performed afterwards, to determine if it's Hercules. If a VGA
is found then the FindSVGA procedure is performed.

The FindSVGA procedure will determine if a VGA has a Super VGA
extension. There are currently 9 distinct SVGA types that it will
identify. Some of the SVGAs can be identified easily by looking for
certain strings at prespecified locations on their BIOS. Other SVGAs
can only be identified by testing for the existence of extended,
brand-specific registers. Whatever the case, it will return a value
between 0 and 9 which will be placed in one of the [ext?type] instance
variables. Later on, FindSVGA will also determine if the BIOS conforms
to the VESA BIOS specfications. If a VESA compliant BIOS is found then
the 7th bit of [ext?type] will be set, in other words increasing the
value of [ext?type] by 128.

The FindEGA procedure uses a video BIOS function available only on EGA
and later adapters, Int 10h, AH=12h, BL=10h, GET EGA INFO. If this
function is supported then BX will have been changed upon return. BH
will return the fact that the EGA is either in monochrome or color mode,
which is then be used to set the [egatype] instance variable. No
[ext?type] instance variables are set during this function.

The FindEGA procedure is performed next. If the [egatype] instance varb
indicates that a color EGA was found, then this procedure is bypassed.
Otherwise it determines if a CGA is installed by testing for the
presence of 6845 or compatible CRTC at the assumed i/o port location of
color adapters, 3D4h.

The FindMono procedure is performed last. If the [egatype] indicates a
mono EGA was found, then this procedure is skipped. Otherwise the same
6845 detection procedure is performed as with the CGA, but this time at
port location 3B4h. And if it is determined that an MDA adapter is
present, then an extended test for Hercules, FindHGC, is called.

The FindHGC procedure is called only after it has been determined that
an MDA exists. It returns a value from 0 to 3 depending whether and what
type of Hercules or compatible card is installed.

The Find6845 procedure is used by both FindCGA and FindMono to test for
the presence of a 6845 at their respective assumed locations.

The Determine_subsystem procedure is used only by FindEGA, FindCGA, and
FindMono. It will make a determination whether the currently tested
subsystem is the primary or secondary subsystem. It makes this
determination by looking at offset 63h in the BIOS Data Segment (ie.
segment 40h), which contains the value of video base port address. That
is if the color subsystem is active then it will contain 3D4h. If the
mono is active then it will contain 3B4h.

The Write_msg procedure displays all this information to the user.

The Return_errorlevel procedure parses the command-line and returns a
DOS errorlevel. The only possible command-line parameters are "2" and
"e". If "e" (case-insensitive) is present then the errorlevel returned
will be based on the [ext0type] value. If "2" is on the command-line,
then the errorlevel is based on the [std1type]. If both parameters are
present, then the errorlevel returned is from [ext1type]. If no
parameters are on the command-line, or garbage parameters are on the
command-line then the errorlevel is based on the [std0type] value.*

* Note: there is a bug in the command-line parsing here and simply
sending no parameters will not work, you must send garbage parameters.

Version History
===============

Vers #  Date    Description
------  ----    -----------
1.0     Nov 92  -first release to public

1.1     Nov 92  -fixed a silly bug that made a Tseng mistakenly send the
                return code for a C&T, and made a ZyMos send the return
                code for a Tseng. Pointed out by John Olson in Fidonet's
                80XXX echo.
                -added Trident chipset detector sent over by the same
                John Olson, above.
                -added an installation check for the 8514/A's
                HDILOAD.EXE driver. Treated like any other Super VGA
                installation check.
                -received reports that the C&T chipset test was causing
                lockups on other people's machines. Have moved test
                location to the very last position, so hopefully other
                chipsets have a chance to be detected before this test
                is performed. May consider commenting over this test
                entirely, if any more reports come in about lockups.
                -command-line bug is still present.

Conclusion
==========

Well, that's that. I hope you find this program useful. Better yet, I
hope you find this program educational, that's why I included its source
code. If you have any questions, or if you got any hot new Super VGA
detectors that you would want me to implement, write to me at:

Postal address: Yousuf J. Khan
                1007 Alenmede Cres.
                Ottawa, Ont., Canada
                K2B 8H2
Fidonet address: 1:163/215.6
Internet address: 1:163/215.6@fidonet.org