xxvii


                      APPENDIX III - INSTRUCTION SPEED AND FLAGS


             This appendix contains a list of all the 8086 instructions along
             with their relatives speed and the flags they affect. These speed
             numbers are from INTEL and are in clock ticks.{1} If you have a
             25 mhz clock, then it is doing 25 million ticks per second. If
             you have a 4.77 mhz clock, then it is doing 4.77 million ticks
             per second. Instead of calling them ticks, I'll be calling them
             clocks.

             In order to understand these numbers, you need a little extra
             information. In order to do an instruction, ANY microprocessor
             must:

                 (1) calculate any memory addresses.
                 (2) fetch the two operands (or the single operand if it is   
                     an instruction like NOT).
                 (3) process the instruction and 
                 (4) put the result in the destination. 

             While (3) will require the same amount of time whether the
             operands are in memory or in registers, (1), (2) and (4) are all
             different depending on where the operands are. Some machines
             allow both operands to be in memory, but the 8086 does not.
             Therefore, (1) is either NO memory addresses (if everything is in
             registers) or ONE memory address. 

             Calculating a memory address involves (a) calculating the offset
             from the beginning of the segment and (b) adding it to the
             segment starting address. Part (a) is different depending on the
             addressing mode. In terms of the speed of calculating (a) and
             (b), the order is:

                 (i)     one pointer
                 (ii)    named variable (+ constant) 
                 (iii)   two pointers
                 (iv)    one pointer + constant
                 (v)     two pointers + constant

             The reason that (ii) contains both "variable" and "variable +
             constant" is that the addition (variable + constant) is done by
             the assembler, not the 8086. By the time the 8086 sees it, it is
             a single number. The constants in both (iv) and (v) need to be
             added by the 8086, and this takes extra time. According to INTEL,
             here is the time required for calculating all possible memory
             addresses. Note that some pointers are marginally faster than
             other pointers (this is trivial - don't worry about it).

             ____________________

                1 All the speed numbers are from "Programmer's Pocket
             Reference Guide", (c)1980, 1982 Intel Corporation.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1990 Chuck Nelson





             The PC Assembler Tutor                                     xxviii
             ______________________


                        ADDRESSING MODE                          CLOCKS (EA)
                 (i)   [bx], [si], [di], [bp]                           5
                 (ii)  variable (+ constant)                            6
                 (iii) [bp+di] or [bx+si]                               7
                       [bp+si] or [bx+di]                               8
                 (iv)  ([bx] or [si] or [di] or [bp]) + constant        9
                 (v)   ([bp+di] or [bx+si]) + constant                  11
                       ([bp+si] or [bx+di]) + constant                  12
                        
             The most complicated memory address takes 2.4 times longer to
             calculate than the simplest address. These calculation times will
             be noted by EA (calculate Effective Address). Remember, if both
             operands are in registers, this calculation does not have to be
             done. 

             In order for you to see how all of this works, we'll use ADD as
             an example. Don't start using the table till you understand this
             example.

             On the 8086, we normaly have the following possibilities for
             source and destination:

                 register, register
                 register, memory
                 memory, register
                 register, constant
                 memory, constant

             In Appendix II, we simply combined them as:

                 reg/mem, reg/mem
                 reg/mem, constant

             We can't do this here because they all have different times. For
             ADD they are:

                 ADD                      CLOCKS
                 register, register       3
                 register, memory         9  + EA
                 memory, register         16 + EA
                 register, constant       4
                 memory, constant         17 + EA

             Notice how much faster using a register is. The EA stands for
             "calculate Effective Address" and is the number from the list
             above. If you have:

                 add  ax, bx

             that is "register, register", and it will take 3 clocks to
             execute. If you have:

                 add [bx+di+9], 17

             that is "memory, constant" and will take 17 + EA. What is EA
             here? According to the above list, [BX+DI+CONSTANT] takes 12





             Appendix III - Speeds and Flag Settings                      xxix
             _______________________________________

             cycles, so 17 + EA is 17 + 12 is 29, so this will take 29 clocks.
             That's right. The one instruction is almost 10 times slower than
             the other. If you can move things into some registers, do a
             number of calculations, and then move them back to memory, you
             can save a lot of time. Let's do a few examples to make sure that
             you see all of them:


                 INSTRUCTION              TYPE                TIME

                 add  variable1, bl       memory, register    16 + EA = 22
                 add  bl, variable1       register, memory    9  + EA = 15
                 add  [si], di            memory, register    16 + EA = 21
                 add  di, [si]            register, memory    9  + EA = 14

             Examples 1 and 2 are the same except that source and destination
             have been switched. The same applies to examples 3 and 4. Notice
             that when the 8086 has to fetch the variable and then put the
             result back in memory, it is significantly slower than when it
             just gets the variable from memory and puts the result in a
             register.


                 INSTRUCTION              TYPE                TIME

                 add  ax, cx              register, register  3
                 add  di, 1876            register, constant  4
                 add  variable1, 199      memory, constant    17 + EA = 23

             To show you how the different types of EA effect the time, let's
             do all 3 types of "source, destination" that involve memory.
             First, "memory, register":


                 INSTRUCTION              TIME

                 add  [bx], ax            16 + EA = 21
                 add  variable1, ax       16 + EA = 22
                 add  [bp+di], ax         16 + EA = 23
                 add  [bp+si], ax         16 + EA = 24
                 add  [bx+9], ax          16 + EA = 25
                 add  [bp+di+294], ax     16 + EA = 27
                 add  [bx+di+294], ax     16 + EA = 28

             Now let's do the same things but go "register, memory":

                 INSTRUCTION              TIME

                 add  ax, [bx]            9 + EA = 14
                 add  ax, variable1       9 + EA = 15
                 add  ax, [bp+di]         9 + EA = 16
                 add  ax, [bp+si]         9 + EA = 17
                 add  ax, [bx+9]          9 + EA = 18
                 add  ax, [bp+di+294]     9 + EA = 20
                 add  ax, [bx+di+294]     9 + EA = 21







             The PC Assembler Tutor                                        xxx
             ______________________

             And finally we have "memory, constant":

                 INSTRUCTION              TIME

                 add  [bx], 177           17 + EA = 22
                 add  variable1, 177      17 + EA = 23
                 add  [bp+di], 177        17 + EA = 24
                 add  [bp+si], 177        17 + EA = 25
                 add  [bx+9], 177         17 + EA = 26
                 add  [bp+di+294], 177    17 + EA = 28
                 add  [bx+di+294], 177    17 + EA = 29


             Is this everything you need to know before looking at the list?
             Not quite. Most of the 8086 family has a 16 bit data bus. That
             means that there are 16 wires connecting the processor to memory,
             and the processor reads 1 word (2 bytes) at a time. These memory
             reads ALWAYS start at an even location 1472d, 88026d, 198752d,
             etc. If you are reading one byte, it makes no difference whether
             it is at an even or odd location. If you are reading a word at an
             even location, then everything is normal. If you are reading a
             word at an ODD location, however, the processor must:

                 1) start reading at the first even location that contains
                 the variable.
                 2) read the next even location (which contains the last part
                 of the variable).
                 3) join the parts together.

             As an example, let's take a word at address 21957 (i.e. 21957-
             21958). The processor will:

                 1) read the high byte from the word at 21956
                 2) read the low byte from the word at 21958
                 3) join them together. It now has 21957-21958.

             The processor can do this, but it takes extra time (4 extra clock
             ticks), so our speed listing will also contain the following
             notice:

                 WORDS WHICH ARE AT ODD ADDRESSES NEED 4 EXTRA CLOCKS

             Thus for:

                 add  ax, variable1        (9 + EA = 15)

             if the address is an even location, the instruction will require
             15 clocks. If it is an odd location, the instruction will require
             19 clocks (4 extra ticks). It is worth your while to keep words
             at even locations if at all possible.












             Appendix III - Speeds and Flag Settings                      xxxi
             _______________________________________


                                INSTRUCTION SPEEDS AND FLAGS


             REGISTER:
                 One of the arithmetic registers - either word (AX, BX, CX,
                 DX, SI, DI, BP, SP for word operations) or byte (AH, AL, BH,
                 BL, CH, CL, DH or DL for byte operations).

             AX or AL:
                 AX and AL are considered special on the 8086. Sometimes
                 there is a special AX/AL form of the instruction, (such as
                 for ADD). This form will be shorter. It will only be noted
                 if it is FASTER (such as for MOV) or if it is the only form
                 allowed. It will either say (AX/AL) or (AX only) depending
                 on whether both words and bytes are allowed or only words
                 are allowed. Though both multiplication and division require
                 the use of the (AX/AL) register, the AX/AL is understood,
                 and is not mentioned in the instruction.

             SEGREG:
                 One of the 4 segment registers - CS, DS, ES or SS.

             MEMORY:
                 Either a byte or word in memory. It may be addressed with
                 any possible addressing mode, and the extra time needed to
                 calculate the address in memory (EA - calculate Effective
                 Address) is the following:


                        ADDRESSING MODE                          CLOCKS (EA)

                 (i)   [bx], [si], [di], [bp]                           5
                 (ii)  variable (+ constant)                            6
                 (iii) [bp+di] or [bx+si]                               7
                       [bp+si] or [bx+di]                               8
                 (iv)  ([bx] or [si] or [di] or [bp]) + constant        9
                 (v)   ([bp+di] or [bx+si]) + constant                  11
                       ([bp+si] or [bx+di]) + constant                  12
                        
             EXTRA TIME:
                 1) WORDS WHICH ARE AT ODD ADDRESSES NEED 4 EXTRA CLOCKS.
                 2) A segment override adds 2 clocks to the instruction.



             FLAGS

             Following the instruction mnemonic is information in square
             brackets that indicates how the instruction effects the flags
             register. There are three possibilities

                 1) The instruction may alter the value of a flag in a
                 particular way depending on the result. For AND, the sign,
                 zero and parity flags [SZP] will be set according to the
                 result.






             The PC Assembler Tutor                                      xxxii
             ______________________

                 2) The instruction may set a flag to a specific number
                 (either 1 or 0). For AND, the overflow flag and the carry
                 flag are cleared [(OC=0)].

                 3) The instruction may unreliably alter a flag. That means
                 that the instruction might change the flag, but that it
                 gives you no information. This kind of flag cannot be
                 trusted after this operation. For AND, the auxillary flag is
                 unreliable [?A?].

             The information will always be displayed in this order. The flags
             which are reliably set according to the result will be listed
             first [SZP]. Next, any flags which are either set or cleared will
             be put inside parentheses followed by an equal sign followed by
             the value of the flag (all inside of the parentheses)
             [SZP,(OC=0)]. Finally, any unrelaible flags will be put between
             question marks [SZP,(OC=0),?A?]. Each part will be separated by
             commas. If no flags are changed by the instruction, the brackets
             will have [none] written between them.

             Each flags will be indicated by a single letter. The letters are:

                 O    overflow flag       0 = no overflow, 1 = overflow

                 D    direction flag      direction of movement
                                          for string instructions
                                          0 = upwards, 1 = downwards

                 I    interrupt enable    0 = no ints, 1 = ints o.k.

                 T    trap flag           trap next instruction?
                                          0 = no trap, 1 = trap

                 S    sign flag           0 = positive, 1 = negative

                 Z    zero flag           0 = non-zero, 1 = zero

                 A    auxillary flag      carry out of bottom half
                                          register?  0 = no, 1 = yes

                 P    parity flag         0 = odd, 1 = even

                 C    carry flag          0 = no carry, 1 = carry



             ***************** THE INSTRUCTIONS *********************

             INSTRUCTION                TIMING

             AAA [AC,?OSZP?]         4 clocks

             AAD [SZP,?OAC?]         60 clocks

             AAM [SZP,?OAC?]         83 clocks

             AAS [AC,?OSZP?]         4 clocks





             Appendix III - Speeds and Flag Settings                    xxxiii
             _______________________________________


             ADC [OSZAPC]            see ADD

             ADD [OSZAPC]            register, register    3
                                     register, memory      9  + EA
                                     memory, register      16 + EA
                                     register, constant    4
                                     memory, constant      17 + EA

             AND [SZP,(OC=0),?A?]    see ADD

             CALL [none]             near call                19
                                     far call                 28
                                     near call (reg-ind)      16  {2}
                                     near call (mem-ind)      21 + EA
                                     far call (mem-ind)       37 + EA

             CBW [none]              2 clocks

             CLC [(C=0)]             2 clocks

             CLD [(D=0)]             2 clocks

             CLI [(I=0)]             2 clocks

             CMC [C]                 2 clocks

             CMP [OSZAPC]            register, register    3
                                     register, memory      9  + EA
                                     memory, register      9  + EA
                                     register, constant    4
                                     memory, constant      10 + EA

             CMPS [OSZAPC]           22 clocks

             CWD [none]              5 clocks

             DAA [SZAPC,?O?]         4 clocks

             DAS [SZAPC,?O?]         4 clocks

             DEC [OSZAP]             word register       2
                                     byte register       3
                                     word/byte memory    15 + EA

             DIV [?OSZAPC?]          byte register       80 - 90  {3}
                                     word register       144 - 162
             ____________________

                2 These three last ones are indirect calls. They get the
             address of the subroutine from a register (reg-ind) or from
             memory (mem-ind).

                3 The smaller the numbers, the faster this operation can be
             accomplished. This applies for signed and unsigned multiplication
             and division. They all show a range of values rather than a
             specific value.





             The PC Assembler Tutor                                      xxxiv
             ______________________

                                     byte memory         (86 - 96) + EA
                                     word memory         (150 - 168) + EA

             ESC [none]              memory              8 + EA
                                     coproc. register    2
                                     This only makes sense if you know
                                     about coprocessors.

             HLT [none]              2 clocks

             IDIV [none]             byte register       101 - 112
                                     word register       165 - 184
                                     byte memory         (107 - 118) + EA
                                     word memory         (171 - 190) + EA

             IMUL [OC,?SZAP?]        byte register       80 - 98
                                     word register       128 - 154
                                     byte memory         (86 - 104) + EA
                                     word memory         (134 - 160) + EA

             IN [none]               (AX/AL), port#      10
                                     (AX/AL), dx         8

             INC [OSCAP]             word register       2
                                     byte register       3
                                     word/byte memory    15 + EA

             INT [(IT=0) {4} ]       51 clocks  {5}

             INTO [ {6} ]            overflow            54
                                     no overflow         4

             IRET [ {7} ]            24 clocks


             J(condition) [none]     This includes all conditional jumps
                                     (JAE, JZ, JNO, JLE, JP, etc.) with the
                                     exception of JCXZ.
                                     jump                16
                                     no jump             4
             ____________________

                4 Although this sets the trap flag and interrupt flag to 0, it
             doesn't do it to YOUR flags, it does it to the flags that the
             interrupt will see. Your flags are safely stored on the stack and
             will return unaltered at the end of the interrupt.

                5 There is one exception. INT 3, when coded as the single byte
             trap interrupt, is 52 clocks.

                6 If there is overflow, it pushes your flags and sets (IT=0)
             for the interrupt. If there was no overflow, it does nothing. In
             either case your own flags will remain unaffected.

                7 This puts the copy of your old flags back in the flags
             register. The flags will be the same as they were when you called
             the interrupt.





             Appendix III - Speeds and Flag Settings                      xxxv
             _______________________________________


             JCXZ [none]             jump                18
                                     no jump             6

             JMP [none]              same segment        15
                                     different segment   15
                                     near (reg-ind)      11  {8}
                                     near (mem-ind)      18 + EA
                                     far  (mem-ind)      24 + EA

             LAHF [none]             4 clocks

             LDS [none]              16 + EA

             LES [none]              16 + EA

             LEA [none]              2 + EA

             LOCK [none]             2 clocks

             LODS [none]             12 clocks

             LOOP [none]             jump                17
                                     no jump             5

             LOOPE/LOOPZ [none]      jump                18
                                     no jump             6

             LOOPNE/LOOPNZ [none]    jump                19
                                     no jump             5

             MOV [none]              register, register    2
                                     register, memory      8  + EA
                                     memory, register      9  + EA
                                     register, constant    4
                                     memory, constant      10 + EA
                                     (AX/AL) <-> memory    10 {9}



             ____________________

                8 These last three are indirect jumps. The information about
             where to jump to is coming from a register (reg-ind) or from
             memory (mem-ind).

                9 This is a special instruction which moves a directly
             addressed variable to or from AX (or AL for bytes). Pointers are
             not allowed, only the forms:

                 mov  ax, variable1
                 mov  variable1, ax

             This takes 10 clocks instead of 14 or 15 for the other form.
             Whether this form gets used is up to the assembler, not you.
             Fortunately, MASM, TurboAssembler and A86 all use this form when
             appropriate.





             The PC Assembler Tutor                                      xxxvi
             ______________________

                                     segreg <-> register   2  {10}
                                     segreg, memory        8 + EA
                                     memory, segreg        9 + EA

             MOVS [none]             11 clocks

             MUL [OC,?SZAP?]         byte register       70 - 77
                                     word register       118 - 133
                                     byte memory         (76 - 83) + EA
                                     word memory         (124 - 139) + EA

             NEG [OSZAPC] {11}       register            3
                                     memory              16 + EA

             NOP [none]              3 clocks

             NOT [none]              register            3
                                     memory              16 + EA

             OR [SZP,(OC=0),?A?]     see ADD

             OUT [none]              (AX/AL), port#      10
                                     (AX/AL), dx         8

             POP [none]              register            8
                                     segreg              8
                                     memory              17 + EA

             POPF [ {12} ]           8 clocks

             PUSH [none]             register            11
                                     segreg              10
                                     memory              16 + EA

             PUSHF [none]            10 clocks

             RCL [OC]                register by 1 bit     2
                                     memory by 1 bit       15 + EA
                                     register by # in CL   8 + (4 * #) {13}
                                     memory by # in CL     20 + EA + (4 * #)

             RCR [OC]                see RCL

             ____________________

                10 MOV, PUSH and POP are the only instructions that can alter
             the segment registers (other than CALLs and JMPs).

                11 (NEG number) sets the flags the same as (SUB 0, number).

                12 POPF resets the flags register by POPping a word of the
             stack and using the values stored in that word.

                13 Thus, if you rotate right by 3 bits add (4 * 3), if you
             rotate by 7 bits add (4 * 7), if you rotate by 2 bits add 
             (4 * 2).  As you can see, this can cost a lot of time if you are
             rotating more than 3 or 4 bits.





             Appendix III - Speeds and Flag Settings                    xxxvii
             _______________________________________

             REP [none]              2 clocks

             RET [none]              near ret            8 {14}
                                     near ret (#)        12
                                     far ret             18
                                     far ret (#)         17

             ROL [OC]                see RCL

             ROR [OC]                see RCL

             SAHF [ {15} ]           4 clocks

             SAL/SHL [OSZPC,?A?]     see RCL

             SAR [OSZPC,?A?]         see RCL

             SBB [OSZAPC]            see ADD

             SCAS [OSZAPC]           15 clocks

             SEGMENT OVERRIDE [none] 2 clocks

             SHR [OSZPC,?A?]         see RCL

             STC [(C=1)]             2 clocks

             STD [(D=1)]             2 clocks

             STI [(I=1)]             2 clocks

             STOS [none]             11 clocks

             SUB [OSZAPC]            see ADD

             TEST [SZP,(OC=0),?A?]   register, register    3
                                     register, memory      9  + EA
                                     memory, register      9  + EA
                                     (AX/AL), constant     4
                                     register, constant    5
                                     memory, constant      11 + EA

             WAIT [none]             3 clocks minimum, then check every 5
                                     clocks 

             XCHG [none]             register, register    4
                                     (AX only), register   3
             ____________________

                14 The # here indicates that you pop things off the stack as
             you would in a Pascal program:

                 ret (18)
                 ret (6)

                15 Alters the values of the SZAPC flags according to the
             values in the AH register.





             The PC Assembler Tutor                                    xxxviii
             ______________________

                                     register, memory      17 + EA

             XLAT [none]             11 clocks

             XOR [SZP,(OC=0),?A?]    see ADD