240

             The first thing to talk about is the 8086 mnemonics. The four
             instructions for unpacked BCD numbers are:

                 AAA       ASCII adjust for addition
                 AAD       ASCII adjust for division
                 AAM       ASCII adjust for multiplication
                 AAS       ASCII adjust for subtraction.


             Even though all four instructions have ASCII as part of their
             mnemonic, they have NOTHING to do with ASCII numbers. These
             instructions operate on unpacked BCD numbers. They always give
             results which are unpacked BCD numbers. Because of side effects
             of the 8086 microcode, the add and subtract instructions do
             something unusual, but this will be covered a little later.

             Just like the packed BCD instructions, these four unpacked
             instructions use the normal arithmetic operations and adjust the
             results to compensate for their being unpacked BCD numbers. Let's
             start with addition. The following program is like the BCD
             program except that we use AAA (ascii adjust for addition)
             instead of DAA (decimal adjust for addition).

             ; - - - - - - - - - - START CODE BELOW THIS LINE 
                    mov   ax_byte, 0C4h       ; half registers, hex, hex 
                    mov   bx_byte, 94h        ; half regs, signed, hex
                    mov   dx_byte, 91h        ; half regs, signed, signed
                    lea   ax, ax_byte 
                    call  set_reg_style 
              
                    mov   cx, 0                    ; clear cx for clarity
             outer_loop:                            
                    mov   ax, 0                    ; clear the registers 
                    mov   bx, 0 
                    mov   dx, 0 
                    call  set_count 
                    call  show_regs        
              
                    call  get_hex_byte             ; byte for al 
                    mov   dx, ax                   ; copy for dx 
                    push  ax                       ; save al 
                    call  get_hex_byte             ; byte for bl 
                    mov   bl, al 
                    mov   bh, bl                   ; copy to bh
                    pop   ax                       ; restore al 
                    call  show_regs_and_wait 
                    add   al, bl                   ; normal add  
                    mov   dx, ax                   ; copy to dx 
                    call  show_regs_and_wait 
                    aaa                            ; make adjustment 
                    mov   dx, ax                   ; copy to dx 
                    call  show_regs_and_wait 
                    jmp   outer_loop 
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             ______________________

             The PC Assembler Tutor - Copyright (C) 1989 Chuck Nelson





             Chapter 22 - BCD Numbers                                      241
             ________________________


             Since this is a mixture of unpacked BCD instructions and normal
             integer instructions, a copy of AX (which is showing hex) is
             moved to DX (which is showing signed) each time AX is changed.
             Also, a copy of BL is put in BH.

             For the rest of this chapter, I will refer to the one's digit,
             the ten's digit and the hundred's digit. In the number 346, 3 is
             the hundred's digit, 4 is the ten's digit, and 6 is the one's
             digit. In the number 928, 9 is the hundred's digit, 2 is the
             ten's digit, and 8 is the one's digit.

             If two valid unpacked BCD numbers are added, the result will be
             between 0 and 18. This result MUST be in AL. AAA sets CF if this
             result is greater than 9 ( i.e. there was a carry). AAA leaves
             the one's digit in AL and adds the ten's digit to AH. (The ten's
             digit can only be 0 for 0 - 9 or 1 for 10 - 18).

             Run this. The standard input should be hex numbers between 00h
             and 09h. When you feel comfortable with this, stop for a minute
             and read on.

             We now come to the peculiarity of this instruction. It isn't
             operating on the whole byte, only the lower half byte.
             Technically, if the LOWER HALF BYTE of each of the two numbers
             which are added is a legitimate BCD digit, then at the end of AAA
             the above results will be true and the UPPER HALF BYTE of AL will
             be set to 0. If you put anything in the upper half byte, it will
             be added by ADD, but will be blanked out (zeroed) by AAA.{1}


             As a side effect of blanking out (zeroing) the upper half byte,
             it is possible to use the ASCII numbers '0' (30h) to '9' (39h) as
             addends. The result (after AAA) will still be a number between
             00h and 09h with the carry flag either set or cleared, and AH
             incremented if appropriate. Don't use it this way. The
             multiplication and division instructions REQUIRE that the numbers
             be between 00h and 09h, so all numbers should be changed into
             unpacked BCD on data entry. Here is a partial list of things you
             can add to get the result 07h:

                 03h + 04h           'c' + 'd'           '+' + 't'
                 '3' + '4'           's' + 't'           'c' + '4'
                 'C' + 'D'           '#' + '$'           'S' + '$'

             As you can see, the addition instruction is pretty indiscriminate
             about what kind of data you can put in and still get a legitimate
             unpacked number out. It is your job to make sure that you have
             ____________________

                1. They used the same microcode as for the beginning of DAA.
             If the low half byte of AL is greater than 9, or if there was a
             carry out of the low half byte (if AF, the auxillary flag was
             set), then the 8086 adds 6 to AL, which shifts the excess out of
             the low half byte. It then zeros the high half byte, sets the
             carry flag, and increments AH. If you don't understand this, go
             back and give the footnote on DAA a try. 





             The PC Assembler Tutor                                        242
             ______________________

             legitimate unpacked data upon data entry.

             If this is just a side effect of blanking the upper half byte,
             why did they name the instruction "ascii adjust for addition"?
             It's just that impish sense of humor of those Intel engineers. If
             you think of these instructions as having anything to do with
             ASCII numbers, you will only confuse yourself. These are
             instructions on unpacked BCD numbers, period. 

             The other thing to notice is that this instruction increments the
             AH register if there is a carry, so whenever you use AAA, it is
             going to trash the AH register. Count on it. If AH contains
             important data, store it somewhere else.


             SUBTRACTION

             When you have gotten used to how this works, look at subtraction.
             The subtraction routine is the same as the addition routine
             except that (1) ADD is replaced by SUB and (2) AAA is replaced by
             AAS (ascii adjust for subtraction). If you generate a borrow, the
             carry flag will be set and AH will be decremented by 1. 

             If you have two legitimate unpacked BCD numbers, then after
             subtraction the result will be from +9 to -9. This result must be
             in AL. After AAS (ascii adjust for subtraction), (1) if AL was
             from 0 to +9, it will stay the same and CF will be cleared (CF=0)
             or (2) if AL was -1 to -9, AAF will borrow 1 from AH (considering
             it a ten's digit), and add 10 to AL. This will give a number from
             +1 to +9. It will also set the carry flag (CF=1) to signal a
             borrow. This is what you do with pencil and paper except that you
             always do the borrow BEFORE the subtraction and AAS always does
             the borrow AFTER the subtraction. Once again, this operates on
             the LOW HALF BYTE, so what is in the upper half byte of the
             numbers is irrelevant. It will be zeroed by AAS.

             There is all sorts of data which will generate a legitimate
             unpacked result; some of it is actually legitimate input. It too
             trashes the AH register, so beware. Run this program till you see
             what is going on with individual numbers.


             MULTIPLICATION

             There is also an instruction for multiplication. It assumes that
             AL contains the result of the multiplication of two unpacked BCD
             numbers. That is, 0 <= AL <= 81. After AAM (ascii adjust for
             multiplication), AH will contain the 10's digit and AL will
             contain the 1's digit. If AL is 75, then after AAM, AH will be 7
             and AL will be 5. If AL is 48, then after AAM, AH will be 4 and
             AL will be 8. (If AL is 183, an illegal result, then after AAM, 
             AH will be 18 and AL will be 3).

             We are going to use a similar program for multiplication, but AX
             and BL will be half byte unsigned; BH and DX will be half byte
             hex. Every time we change AX, we will copy it to DX. Here is the
             program:





             Chapter 22 - BCD Numbers                                      243
             ________________________


             ; - - - - - - - - - - START CODE BELOW THIS LINE 
                    mov   ax_byte, 0A2h       ; half registers, unsigned 
                    mov   bx_byte, 0C2h       ; half regs, hex, unsigned 
                    mov   dx_byte, 0C4h       ; half regs, hex 
                    lea   ax, ax_byte 
                    call  set_reg_style 

                    mov   cx, 0               ; clear cx for clarity 
             outer_loop: 
                    mov   ax, 0               ; clear the registers 
                    mov   bx, 0 
                    mov   dx, 0 
                    call  set_count 
                    call  show_regs       
              
                    call  get_hex_byte        ; byte for al 
                    mov   dx, ax              ; copy to dx 
                    push  ax                  ; save al 
                    call  get_hex_byte        ; byte for bl 
                    mov   bl, al 
                    mov   bh, bl              ; copy to bh 
                    pop   ax                  ; restore al 
                    call  show_regs_and_wait 
                    mul   bl                  ; unsigned multiplication 
                    mov   dx, ax              ; copy to dx
                    call  show_regs_and_wait 
                    aam                       ; make adjustment 
                    mov   dx, ax              ; copy to dx 
                    call  show_regs_and_wait 
                    jmp   outer_loop 
              ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             All you need to change from the addition program is the register
             style, ADD -> MUL and AAA -> AAM.

             Try this out. Notice that after MUL, what we get in DX is
             garbage. This number is a pure unsigned number, not a BCD number.
             Just to underline how important it is to have legitimate unpacked
             BCD data, try a few multiplications where the upper half byte is
             non-zero and see what happens.


             DIVISION

             AAD (ascii adjust for division) is slightly different. What we
             want to do is divide a number from 0 - 99 by a number from 1 to 9
             (0 gives a zero divide interrupt). Therefore, AAD multiplies what
             is in AH by 10 and adds it to what is in AL. It clears AH for the
             coming unsigned division.{2}  If AH contains 7 and AL contains 2,
             then after AAD, AL will be 72 and AH will be 0. If AH is 4 and AL
             is 6, then after AAD, AL will be 46 and AH will be 0. (If AH is
             14 and AL is 7 - an illegal situation - then after AAD, AL will
             ____________________

                2. Remember that for unsigned byte division, we set AH to 0.
             This was back in the first chapter on division.





             The PC Assembler Tutor                                        244
             ______________________

             be 147 and AH will be 0)

             After you have done AAD, you are ready for regular unsigned
             division. After division, the quotient will be in AL and the
             remainder will be in AH. Here's the program:

             ; - - - - - - - - - - START CODE BELOW THIS LINE 
                    mov   ax_byte, 0A2h      ; half registers, unsigned 
                    mov   bx_byte, 0C2h      ; half regs, hex, unsigned 
                    mov   dx_byte, 0C4h      ; half regs, hex 
                    lea   ax, ax_byte 
                    call  set_reg_style 
              
                    mov   cx, 0              ; clear cx for clarity 
             outer_loop: 
                    mov   ax, 0               ; clear the registers 
                    mov   bx, 0 
                    mov   dx, 0 
                    call  set_count 
                    call  show_regs       
              
                    call  get_hex             ; word 
                    mov   dx, ax              ; copy to dx 
                    push  ax                  ; save al for later 
                    call  get_hex_byte        ; byte for bl 
                    mov   bl, al 
                    mov   bh, bl              ; copy to bh 
                    pop   ax                  ; get back al 
                    call  show_regs_and_wait 
                    aad                       ; adjust for division 
                    mov   dx, ax              ; copy to dx
                    call  show_regs_and_wait 
                    div   bl                  ; unsigned division 
                    mov   dx, ax              ; copy to dx 
                    call  show_regs_and_wait 
                    jmp   outer_loop 
              
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             The differences from the multiplication routine are (1) we get a
             TWO byte hex number for the dividend and (2) AAD comes first,
             then DIV. That's all.

             We need to enter a TWO byte unpacked BCD number in order to get
             grist for the mill. 87 is 0807h, 93 is 0903h, 42 is 0402h. This
             will give us two unpacked digits so we have something to put in
             AH. 

             Run this program and enter legitimate (and if you want,
             illegitimate) data. Notice that even with legitimate data, it is
             possible to get a quotient that is larger than 9. (47 / 3 is 15,
             remainder 2). Don't worry about this. We will avoid this problem
             in the real program.


             PACKING AND UNPACKING






             Chapter 22 - BCD Numbers                                      245
             ________________________

             Making an i/o routine is such a bother that we will enter data
             with 'get_bcd' and output data with 'print_bcd'. To do this, we
             need to pack and unpack the data. The calls in C would be:

                 unpack_bcd (&packed_number, &unpacked_number) ;
                 pack_bcd (&unpacked_number, &packed_number) ;{3}

             The thing to be operated on is the first variable and the result
             is the second variable. First, here's the unpacking routine:

             ; - - - - - - - - - -  
             unpack_bcd proc near 
              
                    UNPACK_UNPACKED_ADDRESS  EQU    [bp + 6] 
                    UNPACK_BCD_ADDRESS       EQU    [bp + 4] 
              
              
                    push  bp 
                    mov   bp, sp 
                    PUSHREGS  ax, bx, cx, si, di 
              
                    mov   si, UNPACK_BCD_ADDRESS 
                    mov   di, UNPACK_UNPACKED_ADDRESS 
              
                    ; start at top to unpack 
                    add   si, 9               ; bcd sign 
                    add   di, 18              ; unpacked sign 
                    mov   al, [si]            ; move sign to unpacked 
                    mov   [di], al 
                    dec   si                  ; move down to next byte 
                    dec   di 
                     
                    mov   cx, 9               ; 9 bcd data bytes 
                    ; unpack high byte first, then low byte 
             unpack_loop: 
                    push  cx                  ; save counter
                    mov   al, [si]            ; bcd byte to al 
                    mov   bl, al              ; copy to bl 
                    mov   cl, 4 
                    ror   al, cl              ; high half byte to low half 
                    and   al, 0Fh             ; blank upper half byte 
                    mov   [di], al            ; al is high half of bcd byte 
                    dec   di                  ; result pointer
                    and   bl, 0Fh             ; blank upper half byte 
                    mov   [di], bl            ; bl is low half bcd byte 
                    dec   di                  ; result pointer
                    dec   si                  ; source pointer
                    pop   cx                  ; restore counter
                    loop  unpack_loop 
              
                    POPREGS  ax, bx, cx, si, di 
                    pop   bp 
                    ret 
             ____________________

                3. That '&' means that we are passing the addresses, not the
             values.





             The PC Assembler Tutor                                        246
             ______________________

              
             unpack_bcd  endp 
             ; - - - - - - - - - - - - - - - - 

             This is pretty straightforward. First it moves the sign. Then,
             taking a BCD byte, the routine divides it in two parts, rotating
             the high half byte to the proper position, storing it,
             DECREMENTING the pointer and storing the low half byte. The upper
             half byte of each unpacked byte is zeroed. Notice that by
             starting at the top, it is possible to unpack a number in place.
             Diagram what is happening to make sure you believe that.

             Here's the packing routine:

             ; - - - - - - - - - - - - - - - - 
             pack_bcd     proc near 
              
                    PACK_BCD_ADDRESS       EQU     [bp + 6] 
                    PACK_UNPACKED_ADDRESS  EQU     [bp + 4] 
              
                    push  bp 
                    mov   bp, sp 
                    PUSHREGS  ax, bx, cx, si, di 
              
                    mov   si, PACK_UNPACKED_ADDRESS 
                    mov   di, PACK_BCD_ADDRESS 
              
                    ; start at bottom to pack 
                    mov   cx, 9               ; 9 bytes of bcd data 
             pack_loop: 
                    push  cx                  ; save counter
                    mov   al, [si + 1]        ; high unpacked byte 
                    mov   cl, 4 
                    ror   al, cl              ; move to high half byte 
                    or    al, [si]            ; OR low half with high half 
                    mov   [di], al            ; move to BCD 
                    inc   di                  ; adjust pointers 
                    add   si, 2  
                    pop   cx                  ; restore counter
                    loop  pack_loop 
              
                    ; si and di are now in the right place for the sign 
                    mov   al, [si] 
                    mov   [di], al 
              
                    POPREGS  ax, bx, cx, si, di 
                    pop   bp 
                    ret 
              
             pack_bcd endp 
             ; - - - - - - - - 

             This does the reverse process, rotating the high byte to the
             proper place, then ORing the two together to form a packed BCD
             byte. Notice that by starting at the BOTTOM it is possible to
             pack a number in place. Diagram the action to make sure you
             believe this. 





             Chapter 22 - BCD Numbers                                      247
             ________________________


             These two routines allow us to use 19 byte unpacked BCD numbers.
             Here's the multiplication routine for a 19 byte (18 data bytes
             and 1 sign byte) unpacked number by a 1 byte unpacked number:

             ; - - - - -
             unpacked_multiply  proc near 
              
                    PUSHREGS  ax, bx, cx, dx, si, di 
                    mov   si, offset multiplicand 
                    mov   di, offset result 
                    mov   dh, 0                    ; clear dh for carry 
                    mov   bl, multiplier_copy 
                    mov   cx, 18                   ; 18 data bytes 
              
             mult_loop: 
                    mov   al, [si]                 ; multiplicand to al 
                    mul   bl                       ; multiply 
                    add   al, dh                   ; add old carry 
                    aam                            ; adjust al 
                    mov   [di], al                 ; partial result 
                    mov   dh, ah                   ; save carry 
                    inc   si                       ; adjust pointers
                    inc   di 
                    loop  mult_loop 
              
                    mov   extra_byte, ah           ; extra byte 
                    POPREGS  ax, bx, cx, dx, si, di 
                    ret 
              
             unpacked_multiply  endp 
             ; - - - - -  

             This is a clone of what we had in the chapter on multiple word
             multiplication but is byte multiplication instead of word
             multiplication. Refer back to that chapter to understand the
             mechanics of the process. We store the partial result and save
             the high byte for addition with the next multiplication. At the
             end we save the 19th byte for printout.

             We are cheating a little. we have:

                    mul   bl                       ; multiply 
                    add   al, dh                   ; add old carry 
                    aam                            ; adjust al 

             when we should have:

                    mul   bl                       ; multiply 
                    aam                            ; adjust al 
                    add   al, dh                   ; add old carry 
                    aaa                            ; adjust al

             The reason this works is that the maximum multiplication is
             9X9=81. The maximum addition is 81+9 = 90. AAM will work
             correctly with any number 99 or less, so we save a step; we do
             one adjustment instead of two. 





             The PC Assembler Tutor                                        248
             ______________________


             Now, let's look at the driver for the program:

             ; + + + + + START DATA BELOW THIS LINE 
             multiplier_message  db    "Enter a number from -9 to +9", 0 
             bcd_in              dt    ? 
             bcd_out             dt    ? 
             multiplicand        db    19 dup (?) 
             multiplier          db    ? 
             multiplier_copy     db    ? 
             result              db    19 dup (?) 
             extra_byte          db    ? 
             result_sign         db    ? 
             ; + + + + + END DATA ABOVE THIS LINE 


             ; + + + + + START CODE BELOW THIS LINE 
             outer_loop: 
                    mov   ax, offset bcd_in 
                    call  get_bcd 
                    call  print_bcd           ; reprint for clarity 
                    lea   cx, multiplicand 
                    push  cx                  ; unpacked address 
                    push  ax                  ; bcd_in address 
                    call  unpack_bcd 
                    add   sp, 4               ; adjust the stack 
                    mov   al, multiplicand + 18      ; sign byte 
                    mov   result_sign, al     ; either 00h or 80h 
              
             enter_multiplier: 
                    lea   ax, multiplier_message 
                    call  print_string 
                    call  get_signed_byte 
                    ; check for valid multiplier 
                    cmp   al, 9               ; > +9 ? 
                    jg    enter_multiplier 
                    cmp   al, -9              ; < -9? 
                    jl    enter_multiplier 
              
                    ; adjust multiplier sign 
                    mov   multiplier, al  
                    mov   multiplier_copy, al 
                    and   al, 80h             ; sign bit set? 
                    jz    do_the_multiplication 
                    ; negative multiplier, so adjust 
                    neg   multiplier_copy     ; make positive 
                    xor   result_sign, 80h    ; reverse sign of result 
              
             do_the_multiplication: 
                    call  unpacked_multiply 
              
                    mov   al, result_sign   ; transfer sign to result 
                    mov   result + 18, al 
              
                    ; pack the result 
                    mov   ax, offset bcd_out  ; bcd number 
                    push  ax 





             Chapter 22 - BCD Numbers                                      249
             ________________________

                    mov   ax, offset result   ; unpacked number 
                    push  ax 
                    call  pack_bcd 
                    add   sp, 4               ; adjust the stack 
              
                    ; print multiplicand, multiplier, extra byte and result 
                    mov   ax, offset bcd_in 
                    call  print_bcd 
                    mov   al, multiplier 
                    call  print_signed_byte 
                    mov   al, extra_byte 
                    call  print_hex_byte 
                    mov   ax, offset bcd_out 
                    call  print_bcd 

                    jmp   outer_loop 
             ; - - - - - END CODE ABOVE THIS LINE

             We enter a multiplicand, unpack it, enter a number from -9 to +9
             and save a copy of its absolute value as well as the sign the
             result will be. We adjust the sign of the result after the
             multiplication. No matter what you enter, the sign will be
             correct, and if you put the 19th byte in front of the BCD number
             which you have printed, the absolute value will be correct. We
             are multiplying with a COPY of the multiplier, so we can reprint
             the actual multiplier; it hasn't changed. At the end we pack the
             result and print everything. The order of printout is
             multiplicand, multiplier, extra byte and result.

             Notice that we are not passing the parameters for
             unpacked_multiply on the stack. This is pure whim. A rule for
             when to pass on the stack is (1) If the subroutine doesn't know
             where the parameters will be located in memory, you MUST pass
             them on the stack but (2) if the subroutine knows for certain
             where the parameters will be, it can fetch them itself.

             DIVISION

             Here is the division routine for 19 byte unpacked numbers:

             ; - - - - - - - - 
             unpacked_divide  proc near 
              
                    PUSHREGS  ax, bx, cx, si, di 
              
                    mov   bl, divisor_copy 
                    mov   si, offset dividend + 17  ; start at the top 
                    mov   di, offset quotient + 17 
                    mov   cx, 18              ; 18 numeric bytes 
                    mov   ah, 0               ; clear ah for division
              
             div_loop: 
                    mov   al, [si]            ; dividend byte to al 
                    aad                       ; adjust for unpacked number 
                    div   bl                  ; bl is divisor 
                    mov   [di], al            ; move partial quotient 
                    dec   si                  ; decrement pointers 





             The PC Assembler Tutor                                        250
             ______________________

                    dec   di 
                    loop  div_loop 
              
                    mov   remainder, ah       ; final remainder 
              
                    POPREGS  ax, bx, cx, si, di 
                    ret 
              
             unpacked_divide  endp 
             ; - - - - - 

             It is pretty simple; it too is a clone of the multiple word
             division process. Go back to multiple word division if you don't
             understand it. We keep the previous remainder for the next
             division. Here is the driver:

             ; + + + + + + + + + + + + + + + START DATA BELOW THIS LINE 
             divisor_message db "Enter a number from -9 to +9 (but not 0).",0
             bcd_in          dt     ? 
             bcd_out         dt     ? 
             quotient_sign   db     ? 
             remainder_sign  db     ? 
             divisor         db     ? 
             divisor_copy    db     ? 
             dividend        db     19 dup (?) 
             quotient        db     19 dup (?) 
             remainder       db     ? 
             ; + + + + + + + + + + + + + + + END DATA ABOVE THIS LINE 

             ; + + + + + + + + + + + + + + + START CODE BELOW THIS LINE 
             outer_loop: 
                    mov   ax, offset bcd_in 
                    call  get_bcd 
                    call  print_bcd           ; reprint for clarity 
                    lea   cx, dividend 
                    push  cx                  ; unpacked address 
                    push  ax                  ; bcd_in address 
                    call  unpack_bcd 
                    add   sp, 4               ; adjust the stack 
                    mov   al, dividend + 18   ; sign byte 
                    mov   quotient_sign, al   ; either 00h or 80h 
                    mov   remainder_sign, al  ; ditto 
              
             enter_divisor: 
                    lea   ax, divisor_message 
                    call  print_string 
                    call  get_signed_byte 
                    ; check for valid divisor 
                    cmp   al, 0               ; 0? 
                    je    enter_divisor 
                    cmp   al, 9               ; > +9 ? 
                    jg    enter_divisor 
                    cmp   al, -9              ; < -9? 
                    jl    enter_divisor 
              
                    ; adjust divisor, quotient sign 
                    mov   divisor, al  





             Chapter 22 - BCD Numbers                                      251
             ________________________

                    mov   divisor_copy, al 
                    and   al, 80h             ; sign bit set? 
                    jz    do_the_division 
                    ; negative divisor, so adjust 
                    neg   divisor_copy        ; make positive 
                    xor   quotient_sign, 80h  ; reverse sign of quotient 
              
             do_the_division: 
                    call  unpacked_divide 
              
                    mov   al, quotient_sign   ; transfer sign to quotient 
                    mov   quotient + 18, al 
                    test  remainder_sign, 0FFh  ; positive or negative?
                    jz    pack_the_quotient
                    neg   remainder             ; make the remainder negative
              
             pack_the_quotient:
                    mov   ax, offset bcd_out  ; bcd number 
                    push  ax 
                    mov   ax, offset quotient ; unpacked number 
                    push  ax 
                    call  pack_bcd 
                    add   sp, 4               ; adjust the stack 
              
                    ; print dividend, divisor, quotient and remainder 
                    mov   ax, offset bcd_in 
                    call  print_bcd 
                    mov   al, divisor 
                    call  print_signed_byte 
                    mov   ax, offset bcd_out 
                    call  print_bcd 
                    mov   al, remainder 
                    call  print_signed_byte 
              
                    jmp   outer_loop 
             ; + + + + + + + + + + + + + + + END CODE ABOVE THIS LINE 

             Enter a BCD number, unpack it. Enter a signed number, do range
             checking, and if it is ok, store it (along with a copy, which we
             make sure is positive). Calculate the sign of the quotient and
             remainder. Do the division, then print the dividend, divisor,
             quotient and remainder. (which have been sign adjusted). The
             remainder is a signed byte.

             Like unpacked_multiply, unpacked_divide fetches the parameters
             directly from memory rather than from the stack.
















             The PC Assembler Tutor                                        252
             ______________________

                                    SUMMARY



             PACKED BCD INSTRUCTIONS

             DAA (decimal adjust for addition) adjusts AL, assuming that it
             contains the result of a legitimate packed BCD addition. It
             treats AL as two independent half-bytes. If the result of the
             lower half-byte is 10 or over, it subtracts 10 from the lower
             half-byte and adds the carry to the upper half byte. It then
             looks at the upper half byte. If its result is 10 or over, DAA
             subtracts 10 from the upper half byte and sets the carry flag.
             Otherwise the carry flag is cleared.

             DAS (decimal adjust for subtraction) adjusts AL, assuming that it
             contains the result of a legitimate packed BCD subtraction.It
             treats AL as two independent half-bytes. If the result of the
             lower half-byte is -1 or less, it adds 10 to the lower half-byte
             and borrows 1 from the upper half byte. It then looks at the
             upper half byte. If its result is -1 or less, DAS adds 10 to the
             upper half byte and sets the carry flag to indicate a borrow.
             Otherwise the carry flag is cleared.


             UNPACKED BCD INSTRUCTIONS

             AAA  (ascii adjust for addition) adjusts AL, assuming that it
             contains the result of a legitimate unpacked BCD addition. If the
             lower half-byte has generated a result 10 or over, it subtracts
             10, carries 1 to AH, and sets the carry flag. If the result is 9
             or less, it clears CF. In either case it zeroes the upper
             half-byte of AL.

             AAD (ascii adjust for division) PREPARES AL and AH for division.
             It assumes that AH contains the 10's digit and AL contains the
             1's digit of a two byte unpacked BCD number. It multiplies AH by
             10 and adds it to AL, thus making a single integer between 0 and
             99. It zeroes AH in preparation for division.

             AAM (ascii adjust for multiplication) adjusts AL, assuming that
             it contains the result of a legitimate BCD multiplication. It
             divides the result by 10, putting the quotient in AH and the
             remainder in AL.

             AAS  (ascii adjust for subtraction) adjusts AL, assuming that it
             contains the result of a legitimate unpacked BCD subtraction. If
             the lower half-byte has generated a result -1 or less, it borrows
             1 from AH, adds 10 to AL, and sets the carry flag. If the result
             is 0 or more, it clears CF. In either case it zeroes the upper
             half-byte of AL