268

                            CHAPTER 25 - WHAT DOES IT ALL MEAN?


             What does it all mean? Not a whole lot, actually. We can now save
             memory space and we can save a lot of time. But with the
             incessant march of technology these things mean less and less. A
             few years ago, when 64k or 128k was a lot of memory and memory
             was expensive, having a 20k program instead of a 40k program was
             a significant advantage. Now it means almost nothing unless it is
             a memory resident program. What about disk space? Just a while
             back we were operating with two 360k floppy disks and a hard disk
             was too expensive. Nowdays everyone has a 20meg hard disk.{1} And
             speed? Those programs that were slow on an 8088 now seem o.k. on
             an 80386. Those programs that were unbearably slow on the 8088
             died a quick death and are no longer around.

             Compilers are better and they have more subroutines available.
             They are also easier to program than going to the assembler
             level. What this chapter is about is when NOT to use the standard
             compiler functions and subroutines.

             First, you should understand that all compiler subroutines are
             general purpose subroutines. They need to be all things to all
             people. Imagine what a vehicle would be like if we gave the
             designer the following specification:

                 We want to be able to drive to the store for groceries. It
                 should be fuel efficient. In case we want to go into the
                 mountains it should be an all terrain vehicle. We also want
                 to be able to haul a roomful of furniture from coast to
                 coast. Oh yes, and we want to be able to race it at Le Mans.

             Being universal requires a lot of code and it slows things down.
             Whether this extra code and time is too much is a question you
             need to decide for yourself. First, here are some examples of
             size. This is a C program that does almost nothing:

                 #include <stdio.h> 
                 main() 
                 { 
                         int     x ; 
                         x = 27 ;                        /* line 1 */ 
                         scanf  ( "%d", &x ) ;           /* line 2 */ 
                         printf ( "%d\n", x ) ;          /* line 3 */ 
                 } 
             ____________________

                1. Which has led to one of my pet peeves. All installation
             programs for compilers and word processors dump EVERYTHING on the
             hard disk. This gives us subdirectories that have 50 files in
             them, and we don't have the foggiest notion of what any of the
             files are for. If these installation programs would only prompt
             us by type of file to find out what we want to install and want
             to leave off the hard disk, we would all be better off.

             ______________________

             The PC Assembler Tutor - Copyright (C) 1990 Chuck Nelson





             Chapter 25 - What Does It All Mean?                           269
             ___________________________________


             I have made 3 programs from this. LINE1.C has line1 only. LINE2.C
             has lines 1 and 2. LINE3.C has lines 1, 2 and 3. For those non C
             people, scanf is an input function, printf is an output function.
             Guess how big each program is. Here's the directory listing.

                 LINE1    EXE     3176   6-22-90   8:48a 
                 LINE2    EXE     7170   6-22-90   8:49a 
                 LINE3    EXE     9134   6-22-90   8:49a 

             It takes 3000 bytes to start a C program (this is the startup
             module) 4000 bytes more to enter something and 2000 bytes extra
             to print something. That first 3000 bytes is unavoidable if you
             are writing in a high level language. If you are doing a lot of
             general purpose i/o, these extra amounts aren't too bad. There
             are two cases where you might want to use your own i/o routines.
             First, if you have something simple or secondly, if you have
             something special, you want to do your own i/o.

             If you don't need all that flexibility, you are better off doing
             your own i/o. Here are two files that write a text screen to a
             disk file.

                 COPYSCRN EXE    10454   6-10-90   9:30a 
                 INTSCRN  COM      445   6-12-90   7:40p 

             They both do the same thing except that the .COM file is a little
             more sophisticated. Notice the difference in size. Speed really
             doesn't play a part here because what they do is so simple that
             it takes just a second in any case. The program was so simple
             that it only took an hour or two to write, so I didn't lose any
             time by writing it in assembler.

             The other case is when you have a specific idea of what the
             screen should look like. You want control of the whole screen all
             the time. This includes all word processors, databases,
             programming environments, etc. They all take charge of the screen
             because some DOS functions are too slow. If you remember from the
             ZOOM chapter, there is a radical difference between what you can
             do and what DOS can do. Even though these large programs are
             written in C, they all bypass the C i/o functions. That does not
             mean that they go down to the assembler level, however.


             INTERRUPTS

             You have done a few interrupts. They call the standard DOS or
             BIOS functions. Remember, they do this by going into low memory
             (the first 1k of memory) and getting the address of the
             subprogram that handles that particular interrupt. However, you
             do not need to call these interrupts from the assembler level.
             All modern compilers support interrupt calls in the language. If
             yours doesn't, you need a more recent compiler. Before going on
             with this chapter you need to read your compiler documentation
             about interrupts. TURBO Pascal has INTR, QuickBASIC and QuickC
             have INT86.  Read the documentation now. 






             The PC Assembler Tutor                                        270
             ______________________

             Have you read it? No cheating is allowed, because you won't
             understand the rest of this if you haven't read it. 

             Though technically C is a structure and Pascal is a record, they
             are actually arrays where each array element has a specific name.
             The interrupt routine reads all these values into the
             corresponding register, calls the interrupt, then reads the
             register values back into the array. Some languages have one
             array for the input and another for the output. Int 21h is
             special so QuickC has a special function called INTDOS. It is the
             same as using Int 21h.

             The order of registers in the array is arbitrary and language
             dependent. For TurboPascal it is (AX, BX, CX, DX, BP, SI, DI, DS,
             ES, FLAGS). You enter values in the registers specified by the
             interrupt, and then call the interrupt. The routine does the
             rest. 

                 INTR ( int_no: byte, var the_regs: Registers)

             This will push the interrupt number, then the array address. On
             entry to the interrupt call and after initializing BP, we will
             have:
                      int_no              bp + 6
                      array_address       bp + 4
                      old IP              bp + 2
                bp -> old BP              bp

             What follows is not the exact code, but is similar to what the
             Pascal routine does:

                 ; - - - - - - - - - - 
                 intr proc near

                      push bp
                      mov  bp, sp
                      push ax   ; save all registers except SP, DS, SS, CS
                      push bx
                      push cx
                      push dx
                      push si
                      push di
                      push bp   ; this is OUR bp
                      push es

                      ; insert the interrupt number in the interrupt
                      mov  al, [bp+6]  ; AL now contains the interrupt number
                      lea  si, interrupt_spot  ; where the interrupt is
                      mov  cs:[si+1], al       ; insert it in the interrupt

                      ; change all the registers
                      mov  si, [bp+4]     ; array address is DS:SI
                      mov  ax, [si]
                      mov  bx, [si+2]
                      mov  cx, [si+4]
                      mov  dx, [si+6]
                      mov  bp, [si+8]





             Chapter 25 - What Does It All Mean?                           271
             ___________________________________

                      mov  di, [si+12]
                      mov  es, [si+16]

                      ; special manipulation for DS and SI
                      push ds             ; save ds
                      push si             ; save si
                      push ax             ; temp save of ax from array
                      mov  ax, [si+14]         ; ds from array to ax
                      mov  si, [si+10]         ; si from array to si
                      mov  ds, ax              ; now move ax to ds
                      pop  ax                  ; restore ax

                      ; call the interrupt
             interupt_spot:
                      int  0         ; dummy number for the interrupt

                      ; special needs for SI and DS
                      ; our SI and DS are at the top of the stack
                      ; save values of flags, si and ds from interrupt
                      pushf          ; value from interrupt
                      push si        ; value from interrupt
                      push ds        ; value from interrupt
                      add  sp, 6     ; get to our si and ds
                      pop  si        ; our si
                      pop  ds        ; our ds
                      sub  sp, 10    ; sp is where it was a moment ago.
                      mov  [si], ax  ; DS:SI points to array
                      mov  [si+2], bx
                      mov  [si+4], cx
                      mov  [si+6], dx
                      mov  [si+8], bp
                      mov  [si+12], di
                      mov  [si+16], es
                      pop  [si+14]   ; ds from the interrupt
                      pop  [si+10]   ; si from the interrupt
                      pop  [si+18]   ; flags from the interrupt
                      add  sp, 4     ; skip our DS and SI (already in regs)

                      pop  es
                      pop  bp        ; this is OUR bp
                      pop  di
                      pop  si
                      pop  dx
                      pop  cx
                      pop  bx
                      pop  ax

                      mov  sp, bp
                      pop  bp

                      ret (4)        ; clear arguments off the stack
                      ; - - - - - - - - - - - - - - - - - - - - 

             This should test your insight into using code. DS and SI are
             needed for moving data, so we use some kludges to get it to work.

             There are two things here that you shouldn't normally do. First,





             The PC Assembler Tutor                                        272
             ______________________

             we are inserting the interrupt number directly in the machine
             code. Secondly, we are playing around with the value of SP. These
             are rare exceptions and shouldn't occur in your own code unless
             absolutely necessary. 

             The first thing you are going to say is, "Gosh, that's a lot of
             code for one interrupt." True, especially when the interrupt is
             interrupt 12h. Here's int 12h inside of our template file:

                 ; - - - - - START CODE HERE
                      int  12h       ; machine memory  (return in ax)
                      call print unsigned
                 ; - - - - - END CODE HERE

             It finds out how much memory your computer has and returns the
             number of kbytes in AX. But how much extra time does using this
             Pascal interrupt routine take? About 700 clocks or about .0002
             seconds (that's right, 2 ten thousandths) on the slowest machine.
             How many times will you call it during a program? Only one time.
             There is no point in going down to the assembler level to write a
             program that saves you .0002 seconds. In Pascal, you would write:

                 INTR ( $12 , the_regs) ;

             and be done with it. No big loss of time and no trouble at all. 


             In fact, as far as I can see, there is no reason for doing any
             interrupts from the assembler level. You may want to do a whole
             subprogram that contains interrupts, but if you just need one or
             two interrupts, it is easier to work from inside the high-level
             language. 

             This includes the i/o we were talking about a minute ago. Yoy can
             write a screen program inside a high level language using arrays.
             Just think of a screen as a 80X25 array. If a two dimensional
             array is too slow you need to go to a one dimensional array. All
             interrupts that tell what kind of video card is in the computer,
             what mode the screen is in, etc. can be done from the high-level
             language. The most you need assembler for (depending on the
             language) is moving the text array into video memory. You want a
             bunch of help screens? Put all the help screens in a single file
             and use the interrupt for random access file read to read a
             screen when you need it.{2}

             Anything else?  Yes, we still have the need for speed. There are
             certain types of operations like block moves of data, word
             searches and sorting of arrays that are characterized by large
             amounts of data and/or large amounts of computation. If you think
             you see a way to use registers effectively for one of these
             ____________________

                2. What you actually want to do is have the first block of
             data in the file tell you where each screen is and how long its
             data is. Then the first 2 bytes or words of the screen data
             should say the dimensions of the screen data ( 12 X 25, 17 X 3,
             etc.). This will allow you to store and use screens of any size.





             Chapter 25 - What Does It All Mean?                           273
             ___________________________________

             things, you probably can beat a compiled version of the
             subprogram. Then the only question is whether or not it is worth
             the trouble.

             We have used the words "fast" and "slow" ambiguously so far, but
             now it is time to quantify them. Before you get the numbers, you
             need to know one thing about memory. People always talk about the
             "data bus". What is it? It is a group of wires connecting the
             80x86 chip to memory. The 8088 has 8 wires, the 8086, 80286 and
             80386/SX have 16 wires, and the 80386 has 32 wires. That means
             that the 8088 can transfer 8 bits of information at one time, the
             8086 et. al. can transfer 16 bits at a time and the 80386 can
             transfer 32 bits at a time. This means one byte, two byte and
             four byte transfers respectively. This also means that the memory
             bytes are ordered a little differently. You will never notice it
             externally, but here is the different internal ordering.

             The 8088 has all bytes one after the other. All memory
             read/writes are done with the same 8 wires:

                           8088
                     MEMORY ADDRESSES

                           00005
                           00004
                           00003
                           00002
                           00001
                           00000
             data lines   ||||||||   (8 bits)

             (All our examples will use absolute memory locations starting at
             00000). The chips with a 16 bit data bus have all the even
             locations on the first 8 wires and the odd locations on the other
             8 wires. They come in pairs - first even then odd:

                                8086
                          MEMORY ADDRESSES

                           00006     00007
                           00004     00005
                           00002     00003
                           00000     00001
             data lines   ||||||||  ||||||||   (16 bits)

             When one of these chips reads or writes, it can read/write either
             the left or the right byte or the whole word. What it cannot do
             is read the right byte from one pair along with the left byte
             from another pair. If you want to read the word at 00005:00006,
             the 8086 must:

                 1) read the 00005 byte.
                 2) read the 00006 byte.
                 3) join them together.

             This takes longer than just a single word read.






             The PC Assembler Tutor                                        274
             ______________________

             The true 80386 has a 32 bit data bus. This allows it to read 4
             bytes at a time, and its physical memory structure looks like
             this:

                                          80386
                                     MEMORY ADDRESSES

                           00010     00011     00012     00013
                           0000C     0000D     0000E     0000F
                           00008     00009     0000A     0000B
                           00004     00005     00006     00007
                           00000     00001     00002     00003
             data lines   ||||||||  ||||||||  ||||||||  ||||||||  (32 bits)

             Instead of memory pairs, we now have memory quadruplets. As long
             as a word is totally inside of one quadruplet, the read/write
             time will be unaffected. If the read/write crosses the boundary
             (as we did above), the read/write time will be affected in the
             same way. The 80386 can also read 4 byte data quickly as long as
             the total data is inside of one memory quadruplet. 

             In the 8086 family, data can always be read across these
             boundaries but it takes more time. (On the IBM 370, on the other
             hand, there are instructions that REQUIRE that data be aligned
             along 32 bit boundaries).

             This means you should order your data in the following way in the
             data segment:

                 QWORD DATA
                 DWORD DATA
                 TBYTE DATA     ; this is for the 8087
                 WORD DATA
                 BYTE DATA      ; all strings, etc.

             This insures that any read/write for that type of data will
             always be as fast as possible. If the segment  definition has no
             alignment type, it will start on a paragraph boundary - i.e.
             every 16 bytes, and will work with anything. {3}

             In addition, if you ever subtract a number from SP to provide for
             a temporary data area, it should always be an even number. If SP
             is at an odd address instead of an even address, it takes longer
             for PUSHes and POPs. Also, when you define the size of the stack
             segment, it should be an even number of bytes.

             Having said that, it is now time for you to see the speeds of
             ____________________

                3. The alignment type is a word after the word SEGMENT which
             says how the segment should be aligned. The following:

                      DATASTUFF SEGMENT BYTE PUBLIC 'DATA'

             says the segment can be aligned at any byte. The allowable forms
             are BYTE, WORD, DWORD, PARA, PAGE (256 bytes). If there is no
             explicit type, the default is PARA.





             Chapter 25 - What Does It All Mean?                           275
             ___________________________________

             instructions. Read the introduction to APPENDIX III, then glance
             at the times to get the general idea of how fast times are. Come
             back to this chapter when you are comfortable with what the times
             look like. 

             Have you read APPENDIX III? If not, do it before going on.

             The compiled languages all have one thing in common. They tell
             you that if you are writing a subroutine, you need to return from
             the subroutine with DS, BP, SS, and SP unchanged. They don't say
             a thing about any of the other registers. One thing this tells us
             is that they are doing everything from memory locations, not
             register locations. If you have taken a good look at the
             execution times, you will have noticed the phenomenal difference
             in time between a "memory, register" addition and a "register,
             register" addition. 

             Now, if all you are going to do is move a number to a register,
             add it, and move it out again, a compiler can do it as fast as
             you can. But, if you run into a situation where you can use three
             or four registers at the same time, you can cut the execution
             time drastically. Compilers really can't use registers as
             efficiently as we can (yet). This is an ideal spot for using
             assembly language.

             The old adage that 10% of the code uses 90% of the computer time
             is appropriate here. You now know about assembler language, and
             you know what you want to do with it, so go out and enjoy. But
             before you do, try to slog your way through the next chapter on
             "simplified" segment definitions and linking to high level
             languages.